## Slide 1
Shi Miaomiao/swx791350
New

## Slide 2: Introduction to Network Devices

## Slide 3
As the current network develops rapidly, people can easily learn the latest information in the world and communicate with friends and colleagues at any time. This greatly enriches people's communication and life. The future will hold a fully connected and intelligent world.
Network construction requires the support of network devices, physical connections, and multiple protocols between devices. Routers and switches are the most commonly used network devices for network interconnection.
There are various types of low-end, mid-range, and high-end routers and switches on networks of different levels. How do these devices work and process data packets?
This course uses routers and switches as examples to describe the working mechanism and packet forwarding process of network devices.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the logical structure of network devices.
  Describe each functional module of network devices.
  Describe the forwarding process of network devices.

## Slide 5
Overview of Network Device Framework
Packet Processing by Network Devices

## Slide 6: Network Devices
The network infrastructure consists of switches, routers, and firewalls. These devices receive and send data. How does a device forward data received from an interface to another interface?
What are components of a network device? How do these components work collaboratively?
...
...
Layer 2 forwarding
Layer 3 forwarding
How does a switch forward packets from one interface to another interface?

## Slide 7: Hardware Modules of Modular Devices
The following uses the S12700E-8 as an example to describe the architecture of a typical network device.
  Main Processing Unit (MPU): is responsible for control plane and management plane of the entire system.
  Switch Fabric Unit (SFU): is responsible for the data plane of the entire system. The data plane provides high-speed non-blocking data channels for data switching between service modules.
  Line Processing Unit (LPU): provides data forwarding and optical and electrical interfaces with different rates.
  SFUs and LPUs have their own management chips, which work with MPUs to form the control and management plane of the entire device.
Typical panel of a network device
MPU
LPU
SFU
LPU

## Slide 8: MPU
The MPU provides the control plane and management plane for the entire system.
  The control plane provides functions such as protocol processing, service processing, route calculation, forwarding control, service scheduling, traffic statistics collection, and system security.
  The management plane is responsible for system status monitoring, environment monitoring, log and alarm processing, system software loading, and system upgrade.
MPU

## Slide 9: SFU
The SFU provides the data plane for the entire system. LPUs and MPUs communicate with each other through SFUs.
SFU

## Slide 10: LPU
The LPU provides access interfaces of different types (optical and electrical interfaces) and different rates, and forwards data through the distributed data plane.
LPU

## Slide 11: Fixed Device
Different from a modular device, service modules of fixed devices are not independent hardware modules. Instead, they are integrated in one chassis.
Access interface
Main control module
Switching module

## Slide 12: Logical Diagram of Module Connections
Modules of a modular device are categorized as different boards. The cards communicate with each other through internal connections of the modular device.
The fixed integrates the modules, and the modules communicate with each other through internal connections.
LPUs are connected to each other through SFUs, and communication data between LPUs is forwarded through SFUs.
LPU
SFU
MPU
Standby MPU
LPU
SFU
SFU
LPU1
LPU2
LPU4
LPU3
LPU
LPU5
LPU6
LPU8
LPU7
LPU

## Slide 13: Logical Architecture of Network Devices
Network devices can be logically divided into three planes: data plane, control and management plane, and monitoring plane.

## Slide 14: Control Plane
The control plane of a device consists of the MPU and the management unit of the LPU.
The control and management plane provides control and management functions for the system and is the core of the entire system. The control plane provides functions such as protocol processing, service processing, route calculation, forwarding control, service scheduling, traffic statistics collection, and system security. The control plane of a switch is used to control and manage the running of all network protocols. The control plane provides various network information and forwarding entries required by the data plane for data processing and forwarding.
LPU
MPU
Main control unit
Management unit
Control plane
Route calculation
Forwarding control
Service scheduling
System security
...

## Slide 15: Forwarding Plane
The forwarding plane consists of SFUs and LPUs.
An LPU has a forwarding plane engine (FPE), which is essentially a switching chip that implements switching between interfaces on the LPU.
The data plane is responsible for high-speed processing and non-blocking switching of data packets. It encapsulates or decapsulates packets, forwards IPv4/IPv6/MPLS packets, performs QoS and scheduling, completes inner high-speed switching, and collects statistics.
SFU
LPU
LPU
LPU
LPU
Forwarding plane
Encapsulation
Decapsulation
Service scheduling
...
Packet forwarding
QoS
Internal switching

## Slide 16: Monitoring Plane
The monitoring plane consists of the monitoring units of MPUs and LPUs. Some modular switches have independent centralized monitoring units (CMUs).
The monitoring plane monitors the ambient environment to ensure the secure and stable operation of the system. It detects voltage levels, controls system power-on and power-off, monitors the temperature, and controls fan modules. If a unit fails, the monitoring plane isolates the faulty unit promptly so that the other units remain unaffected.
LPU
MPU
Monitoring unit
Monitoring unit
Monitoring plane
Voltage detection
Temperature detection
Fan control
Power supply control
...
CMU

## Slide 17
Overview of Network Device Framework
Packet Processing by Network Devices

## Slide 18: Uplink and Downlink Packet Forwarding
With the SFU as the center, packet forwarding involves uplink and downlink processing.
Uplink
SFU
LPU
LPU
Uplink
Downlink
Downlink
Notes: Packets processed by a network device are classified into service packets and protocol packets.
The device only forwards service packets from one interface to another interface based on forwarding entries.
After receiving protocol packets (such as ARP, OSPF, and BGP packets), the device sends the packets to the control plane for processing. For example, the ARP packets are sent to the control plane for processing. After determining whether to respond to the ARP packets, the device determines whether to learn the source MAC address and source IP address in the ARP packets.

## Slide 19: Processing of Service Packets
After service packets enter the uplink LPU from an interface, they are sent to the SFU through the internal bus of the modular switch. The SFU sends the service packets to the downlink LPU for processing and then sends them out from the interface.
Receive optical/electrical signals
Parse packets
Query entries and forward packets
Fragment packets
Reassemble packets
Obtain encapsulation information
Perform egress processing
Send optical/electrical signals
LPU
PFE
LPU
PFE
SFU
Uplink LPU
Downlink LPU
Service packet
Notes: PFE: Packet Forwarding Engine
Service packets: packets during interaction between services and applications
Fragmentation: Before packets are sent to the SFU, they are sliced with a fixed length based on a certain granularity.
Reassembly: Fragmented packets sent from the SFU are reassembled.

## Slide 20: Determining the Egress of Packets (1)
When a packet enters an LPU, the device determines the outbound interface of the packet based on the forwarding entry (such as the IP routing table and MAC address table). For a modular switch, the downlink LPU needs to be determined.
When the packet reaches the SFU, the outbound interface and downlink LPU are specified. Therefore, the forwarding entry is queried on the uplink LPU.
SFU
LPU
Service packet
MPU
MPU's CPU
LPU
LPU
LPU
1
LPU's CPU
LPU's CPU
LPU's CPU
LPU's CPU
Both the MPU and LPU have CPUs and provide the control plane function. Are forwarding entries stored and queried on the MPU or LPU?
Forwarding entry
Notes: For Layer 2 forwarding, the MAC address table is queried. For Layer 3 forwarding, the Layer 3 routing table is queried.

## Slide 21: Determining the Egress of Packets (2)
Forwarding entries are stored on the MPU. After packets enter the LPU, the LPU queries entries from the MPU.
The LPU needs to communicate with the MPU when packets are forwarded each time. The forwarding efficiency is low and the packet delay increases. For a high-rate LPU, the forwarding rate decreases greatly.
SFU
LPU
Service packet
MPU
MPU's CPU
LPU
LPU
LPU
1
LPU's CPU
LPU's CPU
LPU's CPU
LPU's CPU
Forwarding entry
Query the forwarding entry
2
3
4
5
Store forwarding entries
Notes: For Layer 2 forwarding, the MAC address table is queried. For Layer 3 forwarding, the Layer 3 routing table is queried.

## Slide 22: Determining the Egress of Packets (3)
Forwarding entries are stored on the LPU. After packets enter the LPU, the LPU directly queries the packets, improving the packet forwarding efficiency.
Forwarding entries are stored on all LPUs, causing high resource usage on the control plane.
SFU
LPU
Service packet
MPU
MPU's CPU
LPU
LPU
LPU
1
LPU's CPU
LPU's CPU
LPU's CPU
LPU's CPU
Forwarding entry
2
3
4
Store
forwarding entries
Deliver forwarding entries
Notes: For Layer 2 forwarding, the MAC address table is queried. For Layer 3 forwarding, the Layer 3 routing table is queried.

## Slide 23: Forwarding Information
Service packets of high-end devices are not processed by the CPU of the MPU, and forwarding information is queried by the LPU.
The forwarding information on the LPU does not exist in forwarding entries (such as the IP routing table and MAC address table) of the MPU. After generating forwarding entries, the MPU generates corresponding forwarding information and delivers the information to the LPU.
MPU
MPU's CPU
LPU
LPU
LPU
FIB table
Generation
IP routing table
FIB table
FIB table
FIB table
The IP routing table is used as an example. After the routing table is generated, the MPU generates the FIB table based on the routing table and delivers the FIB table to the LPU. The LPU then forwards packets based on the FIB table.

## Slide 24: Hardware-based Forwarding
The PFE, usually an NP or ASIC chip, is responsible for packet forwarding on an LPU. The LPU directly forwards packets without the involvement of the MPU.
The forwarding plane and control plane of a high-end modular switch are distributed to different components. The MPU on the control plane runs forwarding-related protocols and maintains forwarding entries. The LPU on the forwarding plane can independently complete forwarding based on forwarding information delivered by the control plane. When the MPU on the control plane is heavily loaded, the forwarding plane is not affected. This working mechanism is called forwarding-control decoupling.
SFU
Downlink LPU
Uplink LPU
FIB table
PFE
…
…
Service packet
Service packets are forwarded by the LPU and SFU independently, without the participation of the MPU.

## Slide 25: Processing of Protocol Packets
Protocol packets received by a device, such as OSPF packets, IS-IS packets, BGP packets, ARP packets, STP BPDUs, and ICMP Request packets, need to be processed by the control plane of the device. That is, these packets are sent to the CPU of the MPU for processing.
Receive optical/electrical signals
Perform ingress processing
Search entries and forward packets
Fragment packets
Reassemble packets
Obtain encapsulation information
Perform egress processing
Send optical/electrical signals
LPU
PFE
LPU
PFE
SFU
Uplink LPU
Downlink LPU
Protocol packet
MPU
LPU's CPU
MPU's CPU
Notes: After receiving protocol packets, the CPU of the MPU processes the packets. If the CPU needs to respond to the packets, the control board constructs the protocol packets. For example, after receiving ARP Request and ICMP Echo Request packets sent to the CPU, the MPU constructs the ARP Reply and ICMP Echo Reply packets.
The CPU processing capability of the MPU is limited. If too many protocol packets are sent to the CPU of the MPU, the CPU is busy and cannot respond to the protocol packets in a timely manner. Therefore, the rate at which various protocol packets are sent to the CPU of the MPU is limited by default.

## Slide 26: Processing of Protocol Packets Sent by the Device
Protocol packets sent by the device, such as OSPF packets, IS-IS packets, BGP packets, ARP packets, STP BPDUs, and ICMP packets, are constructed by the CPU of the MPU and then sent by the LPU.
Receive optical/electrical signals
Perform ingress processing
Forward packets
Fragment packets
Reassemble packets
Obtain encapsulation information
Perform egress processing
Send optical/electrical signals
LPU
PFE
LPU
PFE
SFU
Uplink LPU
Downlink LPU
MPU
MPU's CPU
LPU's CPU
Protocol packet

## Slide 27
(Single) Which of the following modules on a modular switch is responsible for running routing protocols and generating and maintaining routing tables?
  LPU
  SFU
  MPU
  SPU
(Essay) When forwarding service packets, does a high-end modular switch query forwarding entries from the MPU?
Notes: C
No. The high-end modular switch delivers forwarding information to the LPU, and the LPU directly forwards packets without querying forwarding entries from the MPU.

## Slide 28
Each network device has an independent control plane, forwarding plane, and monitoring plane. The control plane is responsible for protocol processing, route calculation, and service scheduling, and the forwarding plane is responsible for data forwarding to implement packet exchange between service modules. The monitoring plane monitors the ambient environment to ensure the secure and stable operation of the system.
On a high-end modular switch, each plane has different boards installed. LPUs and SFUs implement functions of the forwarding plane, MPUs implement functions of the control plane, and CMUs implement functions of the monitoring plane.
High-end modular switches use hardware-based forwarding. Packets are directly forwarded by LPUs, without participation of the control plane. Therefore, the packet forwarding efficiency is high.