## Slide 1
Lu Yueyue/lwx445705
2020.4
New

## Slide 2: IP Routing Basics

## Slide 3
When a router receives an IP packet, the router searches the Forwarding Information Base (FIB) table according to the destination IP address of the packet. After finding the most matching routing entry, the router forwards the packet according to the outbound interface or next hop in the routing entry.
A router can obtain three types of routes: dynamic routes such as the Open Shortest Path First (OSPF), static routes, and direct routes. A network may have the three types of routes. How are routers that use different types of routes are reachable?
This course describes the basics of IP routing, including the routing forwarding, routing table, and route import.

## Slide 4
Upon completion of this course, you will be able to:
  Identify the IP routing table and FIB table.
  Analyze the route-based forwarding process.
  Describe the principles of route import.
  Understand application scenarios of route import.

## Slide 5
IP Routing Basics
Advanced Applications of IP Routing

## Slide 6: Overview of IP Routing
When receiving an IP packet, a router matches the destination address of the IP packet with a routing entry.
  If the IP packet matches a routing entry, the router forwards the packet according to the outbound interface or next hop in the routing entry.
  If the IP packet does not match any routing entry, the router does not have routing information to guide packet forwarding. In this case, the router discards the packet.
GE0/0/0
GE0/0/1
GE0/0/2
IP Packet
PC1
192.168.11.1/24
PC2
192.168.21.1/24

## Slide 7: RIB and FIB
A network device that provides the routing function maintains two important data tables: Routing Information Base (RIB) and Forwarding Information Base (FIB).
OSPF process 1
IS-IS process 1
OSPF process 1
RIB table
IS-IS process 1
RIB table
Route selection
RIB
FIB
Control plane
Data plane
Download
IP packet
A router maintains a local core RIB table and RIB tables of routing protocols.
The router downloads the optimal route from the local core routing table to the FIB table. The forwarding chip of the router forwards packets according to the FIB table.
…
…
Static route
Static routing table
Direct route
Direct routing table
Notes: RIB table:
  A RIB table can be considered to be located on the control plane of a router. Actually, a RIB table does not directly guide data forwarding. When a router queries routes, it does not query the destination address of a packet in the RIB table. Instead, it queries the FIB table to guide data forwarding. The router downloads the optimal route from the RIB table to the FIB table. If related entries in the RIB table change, the FIB table is synchronized immediately.
  Because the two tables are consistent and the RIB table is easy to read, the RIB table (routing table) is used in most cases to describe the data forwarding process of a router. Actually, the router queries the FIB table, and the RIB table at the control layer provides only routing information.
FIB table:
  The FIB table is located on the data plane of a router and is also called the forwarding table. Each forwarding entry specifies the outbound interface and next-hop IP address for reaching a destination.
Note:
  Huawei routers and Layer 3 switches provide the routing function. This course uses routers as an example.
  Both OSPF and Intermediate System to Intermediate System (IS-IS) use the Shortest Path First (SPF) algorithm to calculate routes based on link state information. For details about OSPF and IS-IS, see the following courses.
  Routing process: A router supports multiple OSPF and IS-IS processes. Different processes can be assigned based on service types, and they are independent of each other. An OSPF process ID takes effect on the local device, and does not affect packet exchange between the local route and other routers. Packets can be exchanged between routers with different process IDs.

## Slide 8: RIB Table
Each router has a RIB table. RIB tables fall into the local core routing table and protocol routing tables.
Local Core Routing Table
Each router stores a local core routing table. A router preferentially selects the same entries in the routing table of each protocol to obtain the local core routing table, and then delivers the local core routes to the FIB table to guide packet forwarding.
Routing Tables: Public
Destinations : 10 Routes : 10
Destination/Mask Proto Pre Cost NextHop Interface
  0.0.0.0/0 Static 60 0 10.0.2.2 GigabitEthernet0/0/1
10.3.3.3/32 OSPF 10 1 10.0.1.1 GigabitEthernet0/0/0
10.4.4.4/32 EBGP 255 0 10.0.2.2 GigabitEthernet0/0/1
10.0.1.0/24 Direct 0 0 10.0.1.2 GigabitEthernet0/0/0
10.0.1.2/32 Direct 0 0 127.0.0.1 GigabitEthernet0/0/0
10.0.3.0/24 EBGP 255 0 10.0.2.2 GigabitEthernet0/0/1
127.0.0.0/8 Direct 0 0 127.0.0.1 InLoopBack0
127.0.0.1/32 Direct 0 0 127.0.0.1 InLoopBack0
Protocol Routing Table
A protocol routing table stores routing information discovered by the protocol.
OSPF is used as an example.
Public routing table : OSPF
Destinations : 1 Routes : 1
OSPF routing table status : <Active>
Destinations : 1 Routes : 1
Destination/Mask Proto Pre Cost NextHop Interface
10.3.3.3/32 OSPF 10 1 10.0.1.1 GigabitEthernet0/0/0
OSPF routing table status : <Inactive>
Destinations : 0 Routes : 0
The optimal route in the local core routing table is selected based on the preference and metric of each routing protocol.
Notes: Key fields in a routing table:
  Destination: indicates the destination address of a route. It identifies the destination IP address or destination network segment of IP packets.
  Mask: indicates the subnet mask of the destination IP address. It is used with the destination address to identify the address of the network segment where the destination host or router is located.
  Proto (protocol): indicates the protocol through which routes are learned.
  Pre (Preference): indicates the routing protocol preference of the route.
    Routers define external and internal preferences. The external preference can be manually configured for each routing protocol, while the internal preference cannot be manually modified.
    During route selection, a router first compares the external preferences of routes. When the same external preference is set for different routing protocols, the router selects the optimal route based on the internal preference.
  Cost: indicates the cost of a route.
  NextHop: indicates the next hop to the destination network. It specifies the next-hop device to which packets are forwarded.
  Interface: indicates the outbound interface that forwards packets to the destination network. It specifies the local router interface from which packets are forwarded.
The Preference value is used to compare the preferences of different routing protocols, while the Cost value is used to compare the preferences of different routes of the same routing protocol.
Note: The routing table in the body is truncated.

## Slide 9: Longest Match Principle for IP Route Query
When searching the FIB table, a router performs the "AND" operation on the destination address in a packet and the network mask of each entry in the FIB table. The router then compares the result of the "AND" operation with entries in the FIB table.
According to the comparison, the router selects the optimal route to forward packets according to the longest match.
[Huawei] display fib 0
Route Flags: G - Gateway Route, H - Host Route, U - Up Route
S - Static Route, D - Dynamic Route, B - Black Hole Route
---------------------------------------------------------------------------------------------
FIB Table:
Total number of Routes : 8
Destination/Mask Nexthop Flag TimeStamp Interface TunnelID
10.3.3.3/32 10.0.1.1 DGHU t[15123] GE0/0/0 0x0
10.4.4.4/32 10.0.2.2 DGHU t[11177] GE0/0/1 0x0
10.0.1.2/32 127.0.0.1 HU t[9058] InLoop0 0x0
127.0.0.1/32 127.0.0.1 HU t[19] InLoop0 0x0
127.0.0.0/8 127.0.0.1 U t[19] InLoop0 0x0
0.0.0.0/0 10.0.2.2 GSU t[122] GE0/0/1 0x0
10.0.1.0/24 10.0.1.2 U t[9058] GE0/0/0 0x0
10.0.3.0/24 10.0.2.2 DGU t[11177] GE0/0/1 0x0
If the destination IP address of a data packet is 10.3.3.3, which interface does the router forward the data packet?
Notes: Each entry in the FIB table contains the physical or logical interface through which a packet is sent to a network segment or host to reach the next-hop router. An entry also indicates whether the packet can be sent to a destination host on a directly connected network.
The display fib [ slot-id ] command is used to check information about the FIB table.
  slot-id: displays information about the FIB table with a specified slot ID. The value is an integer, and the value range depends on the device configuration.
Fields in the FIB table:
  Total number of Routes: indicates the total number of routes in the routing table.
  Destination/Mask: indicates the destination address or mask length.
  Nexthop: indicates the next hop.
  Flag: indicates the current flag, which is the combination of G, H, U, S, D, and B.
    G (Gateway): indicates that the next hop is a gateway.
    H (Host): indicates that the next hop is a host.
    U (Up): indicates that the route status is Up.
    S (Static): indicates the static route.
    D (Dynamic): indicates the dynamic route.
    B (Blackhole): indicates the blackhole route, with the next hop as a null interface.

## Slide 10
Notes:   Timestamp: indicates the lifetime of an entry, in seconds.
  Interface: indicates the outbound interface used to reach the destination.
  TunnelID: indicates the index of a forwarding entry. If the value is not 0, packets matching the entry are forwarded through a tunnel, for example, MPLS tunnel. If the value is 0, packets are not forwarded through a tunnel.

## Slide 11: Route Types
GE0/0/0
192.168.11.0/24
10.0.12.0/24
GE0/0/1
GE0/0/1
192.168.21.0/24
192.168.31.0/24
GE0/0/1
Direct Route
Route Type | Destination/Mask | Outbound Interface
Direct route | 192.168.11.0/24 | GE0/0/0
Direct route | 10.0.12.0/24 | GE0/0/1
Static Route
Dynamic Route
Route Type | Destination/Mask | Outbound Interface
Static route | 192.168.21.0/24 | GE0/0/1
Dynamic routing protocol
Example: OSPF
Route Type | Destination/Mask | Outbound Interface
OSPF | 192.168.31.0/24 | GE0/0/1
Direct routes are automatically generated by devices and point to local directly connected networks.
Static routes are manually configured by network administrators.
Dynamic routes are learned by dynamic routing protocols running on routers.
Notes: Direct routes are destined for the subnets to which directly connected interfaces belong. They are automatically generated by devices.
Static routes are manually configured by network administrators.
Dynamic routes are learned by dynamic routing protocols, such as OSPF, IS-IS, and Border Gateway Protocol (BGP).
  The Border Gateway Protocol (BGP) is a distance vector routing protocol that allows devices in different ASs to communicate and select optimal routes.
  An AS is a group of IP networks that are controlled by one entity, typically an Internet service provider (ISP), and have the same routing policy.

## Slide 12: Dynamic Routing Protocols
Dynamic routing protocols are classified into the following types based on application scopes:
  Interior Gateway Protocols (IGPs): run inside an autonomous system (AS), including the OSPF and IS-IS.
  Exterior Gateway Protocols (EGPs): run between ASs, including the Border Gateway Protocol (BGP).
Company A's network
OSPF
192.168.11.0/24
192.168.12.0/24
192.168.13.0/24
...
ASBR1
ASBR2
192.168.21.0/24
192.168.22.0/24
192.168.23.0/24
...
Company B's network
IS-IS
ASBR3
ASBR4
BGP

## Slide 13: Route Recursion
Routes can be used to forward traffic only when they have directly connected next hops. However, a static or BGP route may contain an indirect next hop. Therefore, in a process referred to as route recursion, a device needs to search for a directly connected next hop for the route.
GE0/0/1
10.0.23.2/24
GE0/0/0
10.0.12.2/24
GE0/0/1
10.0.23.3/24
GE0/0/0
10.0.12.1/24
R1
R3
R2
192.168.21.0/24
Destination Network | Next Hop | Outbound Interface
192.168.21.0/24 | 10.0.23.3 | GE0/0/0
10.0.23.0/24 | 10.0.12.2 | GE0/0/0
ip route-static 192.168.21.0 24 10.0.23.3
ip route-static 10.0.23.0 24 10.0.12.2
Obtain the directly connected next hop through recursion
In this example, a route to 10.0.23.3 is added to R1 so that the route to 192.168.21.0/24 can be recursive.
Recursion

## Slide 14: Data Forwarding Process
Destination IP address:
192.168.21.1
Gateway
Gateway
R1
R2
R3
GE0/0/1
GE0/0/1
10.0.12.2
10.0.12.1
10.0.23.2
10.0.23.3
GE0/0/0
GE0/0/0
GE0/0/0
GE0/0/1
192.168.11.1/24
192.168.21.1/24
10.0.23.0/24
10.0.12.0/24
192.168.11.2
192.168.21.2
PC1
PC2
Destination/Mask | Next Hop | Outbound Interface
10.0.12.0/24 | 10.0.12.1 | GE0/0/0
10.0.23.0/24 | 10.0.12.2 | GE0/0/0
192.168.11.0/24 | 192.168.11.2 | GE0/0/1
192.168.21.0/24 | 10.0.12.2 | GE0/0/0
R1's routing table
R2's routing table
Destination/Mask | Next Hop | Outbound Interface
10.0.12.0/24 | 10.0.23.2 | GE0/0/0
10.0.23.0/24 | 10.0.23.3 | GE0/0/0
192.168.11.0/24 | 10.0.23.2 | GE0/0/0
192.168.21.0/24 | 192.168.21.2 | GE0/0/1
R3's routing table
Destination/Mask | Next Hop | Outbound Interface
10.0.12.0/24 | 10.0.12.2 | GE0/0/0
10.0.23.0/24 | 10.0.23.2 | GE0/0/1
192.168.11.0/24 | 10.0.12.1 | GE0/0/0
192.168.21.0/24 | 10.0.23.3 | GE0/0/1
1
2
3
4
Notes: The process for PC1 to send a data packet to PC2 is as follows:
  PC1 sends the packet to the gateway R1.
  R1 searches the routing table for the next hop and outbound interface, and forwards the packet to R2.
  R2 forwards the packet to R3 based on the routing table.
  After receiving the packet, R3 looks up the routing table and finds that the destination IP address of the packet belongs to the network segment where the local interface resides. R3 then forwards the packet locally and finally sends the packet to the destination PC2.

## Slide 15
IP Routing Basics
Advanced Applications of IP Routing

## Slide 16: Scenario Analysis of Advanced Applications of IP Routing (1)
Scenario:
  Assume that company A and company B have their own networks, which are managed and maintained independently. The networks of company A and company B run OSPF and IS-IS, respectively.
  After the two companies are merged into one company, the original two networks must be integrated. To ensure that service traffic of the new company can be normally exchanged on the integrated network, the company requires interworking based on routing.
OSPF
192.168.11.0/24
192.168.12.0/24
192.168.13.0/24
……
R1
R2
192.168.21.0/24
192.168.22.0/24
192.168.23.0/24
……
IS-IS
R3
R4
Company A
Company B
OSPF/IS-IS
Notes: OSPF and IS-IS are two different dynamic routing protocols, so they cannot directly exchange routing information.
In the figure, OSPF is deployed on the network of company A, and R1 and R2 are edge devices. IS-IS is deployed on the network of company B, and R3 and R4 are edge devices. OSPF or IS-IS can be deployed on the connected network segments of borders. For example, OSPF can be deployed on network segments between R1 and R3 and between R2 and R4. In this case, only R3 and R4 are border devices.

## Slide 17: Scenario Analysis of Advanced Applications of IP Routing (2)
Scenario:
  On a large-scale enterprise network, a single routing protocol cannot meet network requirements. In most cases, multiple routing protocols coexist.
  In addition, different routing protocols are designed and deployed in different network topologies considering the service logic or administrative management, making the routing hierarchy clear and controllable.
  In such a network environment, interworking based on routing also needs to be implemented.
Municipal company
LAN
Branch
Region core
HQ
Backbone network
...
BGP
IS-IS
OSPF/
Static routing

## Slide 18: Basic Concept of Route Import
Route import refers to the process of advertising routing information from one routing protocol to another.
  Route import allows routing information to be transmitted between different routing protocols.
  When importing routes, you can deploy route control to flexibly control service traffic.
OSPF
192.168.11.0/24
192.168.12.0/24
192.168.13.0/24
...
192.168.21.0/24
192.168.22.0/24
192.168.23.0/24
...
IS-IS
R1
R2
To implement interworking based on routing, perform the following operations:
Re-plan and modify network-wide routing protocols, which is complex.
Perform operations on the edge devices in OSPF and IS-IS routing domains so that routing information can be transmitted between OSPF and IS-IS. This solution does not change the original topology and is easy to deploy. However, loops may occur.
Routing information of two routing protocols is isolated from each other.
Notes: In the figure, OSPF and IS-IS networks have different network segments. Only R1 and R2 know all routing entries.
Question: How do all devices obtain all routes?

## Slide 19: Direction of Route Import
Route import is directional. If routing information is imported from routing protocol A to routing protocol B, routing protocol B can learn routing information about routing protocol A. However, routing protocol A does not know routing information about routing protocol B, unless route import from routing protocol B to routing protocol A is configured.
When importing routes, pay attention to the following points:
  Route preference
  Route injection
  Route metric
OSPF
192.168.11.0/24
192.168.12.0/24
192.168.13.0/24
...
192.168.21.0/24
192.168.22.0/24
192.168.23.0/24
...
IS-IS
R1
Import OSPF routes
into IS-IS
Import IS-IS route
into OSPF
Question: Can two networks communicate with each other if only OSPF routes are imported to IS-IS?
Notes: During route import, focus on the route convergence time. This course does not describe the route convergence time.
The implementation and configuration of route import will be described in other HCIP-Datacom certification courses.

## Slide 20: Route Import: Route Preference
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
Import direct route
Import OSPF routes into IS-IS
2
2
3
1
4
5
4
OSPF route
IS-IS route
Destination/Mask Proto Pre
10.1.1.0/24 ISIS 15
Access traffic
Scenario:
  R1 imports the direct route 10.1.1.0/24 into OSPF.
  R3 learns the route (OSPF external route with the preference of 150) to the network segment 10.1.1.0/24 through OSPF.
  R2 imports OSPF routes to the IS-IS process.
  R3 also learns the route (the preference is 15) to the network segment 10.1.1.0/24 through IS-IS.
  For R3, the IS-IS route has a higher priority than the OSPF external route, so the IS-IS route from R4 is preferred.
  R3 accesses the network segment 10.1.1.0/24 through the path R3->R4->R2->R1, which is the second optimal path.
Notes: Route preferences defined by Huawei:
  Direct: 0
  OSPF: 10
  IS-IS: 5
  Static: 60
  OSPF ASE: 150
  OSPF NSSA: 150
  IBGP: 255
  EBGP: 255
Note: The route preferences may vary with vendors.

## Slide 21: Route Import: Route Injection
10.1.1.0/24
OSPF
R1
R2
R3
R4
Scenario:
  R1 imports the direct route 10.1.1.0/24 to OSPF.
  The direct route 10.1.1.0/24 is advertised in the entire OSPF domain.
  R2 imports OSPF routes to the IS-IS process.
  The direct route 10.1.1.0/24 is advertised in the entire IS-IS domain.
  R3 imports IS-IS routes to the OSPF process.
  The direct route 10.1.1.0/24 is advertised in the entire OSPF domain again, resulting in route injection.
IS-IS
Import direct route
Import OSPF route into IS-IS
2
2
3
1
4
4
OSPF route
IS-IS route
6
6
Import IS-IS route into OSPF
5

## Slide 22: Route Import: Route Metric
Scenario:
  OSPF routes are imported into IS-IS.
  IS-IS routes are imported into OSPF.
Different routing protocols define different route metrics. How are metrics of imported routes defined when routes are imported between routing protocols? What are the metrics?
Import OSPF route into IS-IS
Import IS-IS route into OSPF
R1
192.168.11.0/24 cost=100
192.168.12.0/24 cost=200
192.168.21.0/24 cost=10
192.168.22.0/24 cost=10
OSPF
IS-IS
1
2

## Slide 23: Route Import Scenario
Route import involves the following scenarios:
  Route import between dynamic routing protocols
  Importing direct routes to a dynamic routing protocol
  Importing static routes to a dynamic routing protocol
OSPF
192.168.11.0/24
IS-IS
192.168.21.0/24
2. Import direct route
1. Import OSPF routes into IS-IS
Static route
3. Import static route
Directly connected

## Slide 24: Basic Configuration Commands for Route Import
[Huawei-ospf-100] import-route { bgp | direct | static | isis [ process-id-isis ] | ospf [ process-id-ospf ]}
Configure OSPF to import external routes.
In the OSPF view, import BGP routes, direct routes, static routes, IS-IS routes, and routes of other OSPF processes.
Notes: If a device on an OSPF network needs to access a device on the network running a non-OSPF protocol, the OSPF device needs to import routes from the non-OSPF protocol into the OSPF network.

## Slide 25: Case 1: Importing Direct Routes to OSPF
You can run the import-route direct command to import all direct routes in the routing table to a dynamic routing protocol.
The imported routes are advertised as OSPF external routes on the entire OSPF network.
OSPF
192.168.11.0/24
Directly connected
R1
R2
R3
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | Direct | 192.168.11.1
10.0.12.0/24 | Direct | 10.0.12.1
10.0.23.0/24 | OSPF | 10.0.12.2
R1's routing table
10.0.12.1
10.0.12.2
10.0.23.2
10.0.23.3
Import direct route
import-route direct
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | O_ASE | 10.0.23.2
10.0.12.0/24 | OSPF | 10.0.23.2
10.0.23.0/24 | Direct | 10.0.23.3
R3's routing table
Notes: To enable a device configured with a dynamic routing protocol to advertise the routes of its directly connected interface to a dynamic routing protocol, enable the dynamic routing protocol on the interface. In addition, direct routes can be imported to dynamic routing protocols.
In the figure:
  OSPF is deployed on R1, R2, and R3. R1 has a direct network segment 192.168.11.0/24. To enable R2 and R3 to generate a route to 192.168.11.0/24, import the direct route to OSPF on R1.
Note: On an OSPF network, if the protocol field in the routing table is displayed as O_ASE, the route is an OSPF external route.

## Slide 26: Case 2: Importing Static Routes to OSPF
You can run the import-route static command to import all static routes in the routing table to a dynamic routing protocol.
The imported routes are advertised as OSPF external routes on the entire OSPF network.
OSPF
192.168.11.0/24
R1
R2
R3
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | Static | 10.0.12.1
10.0.12.0/24 | Direct | 10.0.12.2
10.0.23.0/24 | Direct | 10.0.23.2
R2's routing table
Import static route
import-route static
ip route-static 192.168.11.0 24 10.0.12.1
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | O_ASE | 10.0.23.2
10.0.23.0/24 | Direct | 10.0.23.3
R3's routing table
10.0.12.1
10.0.12.2
10.0.23.2
10.0.23.3
OSPF not supported
Notes: For dynamic routing protocols, static routes are considered as external routes and are not detected by dynamic routing protocols. To enable all devices in a dynamic routing protocol domain to learn a static route, import the static route to the dynamic routing protocol.
In the figure:
  R2 and R3 run OSPF, but R1 does not support OSPF. Add a static route pointing to network segment 192.168.11.0/24 and import the static route to OSPF on R2 so that both R2 and R3 can generate a route to 192.168.11.0/24.

## Slide 27: Case 3: Importing IS-IS Routes to OSPF
You can run the import-route isis 1 command to import all IS-IS routes in the routing table to a dynamic routing protocol.
The imported routes are advertised as OSPF external routes on the entire OSPF network.
OSPF
192.168.11.0/24
R1
R2
R3
IS-IS
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | IS-IS | 10.0.12.1
10.0.12.0/24 | Direct | 10.0.12.2
10.0.23.0/24 | Direct | 10.0.23.2
R2's routing table
Destination/Mask | Protocol | Next Hop
192.168.11.0/24 | O_ASE | 10.0.23.2
10.0.12.0/24 | O_ASE | 10.0.23.2
10.0.23.0/24 | Direct | 10.0.23.3
R3's routing table
Import IS-IS routes
import-route isis 1
10.0.12.1
10.0.12.2
10.0.23.2
10.0.23.3
Notes: The typical scenario is to import routes from one dynamic routing protocol to another.
In the figure:
  IS-IS runs on R1 and R2, and OSPF runs on R2 and R3. The routes maintained by the two protocols are isolated. Therefore, R1 has all routes on the IS-IS network but cannot access the OSPF network. R3 has all routes on the OSPF network but cannot access the IS-IS network. You can configure R2 to import IS-IS routes to OSPF.

## Slide 28
(Single) If a router has the following four FIB entries, which route is used by the router to forward the IP packet with the destination IP address 10.0.1.1? ( )
  0.0.0.0/0
  10.0.0.0.0/16
  10.0.1.0/24
  10.0.2.0/24
Notes: C

## Slide 29
(Multiple) Which of the following statements about route import are false? ( )
  In the OSPF process of a router, you can run the import-route command to import routes from other OSPF processes.
  In the OSPF process of a router, you can run the import-route command to import static routes of the routing table.
  On a router, to import routes from routing protocol X to routing protocol Y, you need to run the import-route command in the view of routing protocol X.
  After the import-route command is run on a router and the direct route of GE0/0/1 is imported to OSPF, OSPF is activated on the interface and the interface periodically sends Hello packets.
Notes: CD

## Slide 30
Different routing protocols have different working mechanisms, so multiple routes may be generated to the same destination network segment. A router selects the optimal route based on the priority of the routing protocol and the route cost, and adds the optimal route to the FIB table. The router forwards data according to the FIB table.
On a large-scale network running multiple routing protocols, routes are advertised between routing protocols by importing routes. A large number of routes may be imported, and some low-performance devices cannot support the imported routes. Therefore, route control is required to implement on-demand route distribution.
OSPF, IS-IS, and route control listed in this course will be illustrated in subsequent courses.