## Slide 1
V5R2
V1R1
He Junjian/HWX580230
2019-11-11
New

## Slide 2: OSPF Basics

## Slide 3
Routers forward data packets based on routing tables. Routing entries can be manually configured or generated using dynamic routing protocols.
Compared with dynamic routes, static routes use less bandwidth and do not utilize CPU resources for route calculation and update analysis. Static routes alone can implement interworking for simple networks. If a network fault occurs or the topology changes, static routes cannot be automatically updated and must be manually reconfigured to adapt to the network change.
Compared with static routes, dynamic routing protocols have higher scalability and better adaptability.
The Open Shortest Path First (OSPF), as an Interior Gateway Protocol (IGP), is widely used because it features high scalability and fast convergence.
This course describes basic OSPF concepts, OSPF adjacency establishment, and basic OSPF configurations.

## Slide 4
On completion of this course, you will be able to:
  Describe the overall process of OSPF route calculation.
  Clarify functions of the DR and BDR.
  Describe OSPF packets and their functions.
  Configure basic OSPF functions.
  Distinguish the OSPF neighbor relationship and adjacency.

## Slide 5
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
Basic OSPF Configurations

## Slide 6: Classification of Dynamic Routing Protocols
Interior Gateway Protocols (IGPs)
RIP
OSPF
IS-IS
By ASs
Exterior Gateway Protocols (EGPs)
BGP
By working mechanisms and algorithms
Distance Vector Routing Protocols
Link-State Routing Protocols
OSPF
IS-IS
RIP
Notes: BGP uses the path-vector algorithm, which is a modified version of the distance-vector algorithm.

## Slide 7: Distance-Vector Routing Protocol
A router running a distance-vector routing protocol periodically floods its routing table. Through route exchange, each router learns routes from neighboring routers, loads the routes to its routing table, and then advertises the routes to other neighboring routers.
All routers on a network do not know the network topology. They only know the direction to a destination network segment and the cost.
R1
R2
R3
Routing
Table
Routing
Table
Routing
Table
To reach the device at 10.0.3.3, pass through R2.
10.0.3.3

## Slide 8: Link State Routing Protocol: LSA Flooding
A link-state routing protocol advertises the link state but not routing information.
Routers running link-state routing protocols establish neighbor relationships and then exchange Link State Advertisements (LSAs).
Advertise LSAs to describe link status information.
An LSA describes the status of a router interface, such as the cost of the interface and the connected object.
R2
R4
R1
R3
LSA
LSA
LSA
LSA
100M
1000M
1.544M
100M
OSPF
Notes: Each router generates a link state advertisement (LSA) that describes the status of its directly connected interface, including the interface cost and the relationship between the router and its neighboring router.

## Slide 9: Link State Routing Protocol: LSDB Maintenance
Each router generates LSAs and adds the received LSAs to its own link state database (LSDB). Routers parse the LSAs stored in their LSDBs to obtain the network topology.
R2
R4
R1
R3
LSA
LSA
LSA
LSA
100M
1000M
1.544M
100M
Routers use LSDBs to store LSAs.
An LSDB usually stores various types of LSAs, and each type of LSA describes different information.
LSDB
LSDB
LSDB
LSDB
OSPF

## Slide 10: Link State Routing Protocol: SPF Calculation
Each router uses the Shortest Path First (SPF) algorithm to calculate routes based on the LSDB. Each router calculates a loop-free tree with itself as the root and the shortest path. With the tree, the router knows the optimal paths to all network segments.
R2
R4
R1
R3
100M
1000M
1.544M
100M
Each router calculates a loop-free tree with itself as the root and the shortest path.
LSDB
LSDB
LSDB
LSDB
2
4
3
1
OSPF
Notes: SPF is a core algorithm of OSPF. It is used to select optimal routes on a complex network.

## Slide 11: Link State Routing Protocol: Routing Table Generation
A router installs the calculated optimal path to its routing table.
R2
R4
R1
R3
100M
1000M
1.544M
100M
Based on the SPF calculation result, each router installs routes to the routing table.
LSDB
LSDB
LSDB
LSDB
Routing Table
Routing table
Routing table
Routing table
Routing table
OSPF

## Slide 12: Summary of Link State Routing Protocols
R1
R2
R3
Exchange link state information
Exchange link state information
Exchange link state information
R1
R2
R3
Establish a neighbor relationship
Establish a neighbor relationship
Establish a neighbor relationship
R1
R2
R3
R1
R2
R3
Calculate the path
Calculate the path
Calculate the path
1
2
3
LSDB
LSDB
LSDB
Routing table
Routing table
Routing table
Generate routing entries
1
2
3
4
Notes: A link state routing protocol involves four steps:
  Step 1: Establish a neighbor relationship between neighboring routers.
  Step 2: Exchange link state information and synchronize LSDBs between neighbors.
  Step 3: Calculate the optimal path.
  Step 4: Generate routing entries according to the shortest path tree and load the routing entries to the routing table.

## Slide 13
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
Basic OSPF Configurations

## Slide 14: Overview of OSPF
OSPF, defined by the Internet Engineering Task Force (IETF), is an IGP based on the link state. OSPF version 2 (OSPFv2), defined in RFC 2328, is intended for IPv4, and OSPF version 3 (OSPFv3)), defined in RFC 2740, is intended for IPv6.
OSPF has the following advantages:
  Uses the accumulated link cost as the reference value for route selection based on the SPF algorithm.
  Transmits and receives some protocol packets in multicast mode.
  Supports area partition
  Supports load balancing among equal-cost routes.
  Supports packet authentication.

## Slide 15: OSPF Application Scenarios
OSPF is usually deployed on large-scale enterprise networks to ensure reachable routes between buildings.
  The core and aggregation layers are deployed in the OSPF backbone area.
  The access and aggregation layers are deployed in the OSPF non-backbone area.
Access layer
Core layer
Area 1
Area 0
Area N
…
Aggregation layer
Notes: Access layer: uses transmission media such as optical fibers, twisted pairs, coaxial cables, and wireless access technologies to connect to users and allocate services and bandwidth. The access layer allows terminal users to connect to the network. Therefore, access switches have low costs and high port density.
Aggregation layer: provides policy-based connections for the access layer, such as address combination, protocol filtering, routing service, and authentication management. Network segments are divided to implement isolation, preventing network faults from spreading and affecting the core layer. The aggregation layer also provides interconnection between virtual networks at the access layer, controls and restricts access from the access layer to the core layer, and ensures security and stability of the core layer.
Core layer: implements optimized transmission between backbone networks. The core layer focuses on redundancy, reliability, and high-speed transmission.

## Slide 16: Basic OSPF Concepts: Router ID
A router ID is a 32-bit integer that uniquely identifies an OSPF router in an AS.
The rules for selecting a router ID are as follows:
  The router ID of an OSPF router is manually configured (recommended).
  If the router ID is not manually configured, a router uses the largest IP address of a loopback interface as the router ID.
  If no loopback interface is configured, the router uses the largest IP address of a physical interface as the router ID.
Router ID 10.0.1.1
R1
R3
R2
Router ID 10.0.2.2
Router ID 10.0.3.3
Area
Router ID
Metric
I'm 10.0.1.1
Area 0
Notes: To change a specified router ID, you must restart the OSPF process.
In practice, it is recommended that router IDs of OSPF routers be specified manually. First, plan a private network segment such as 192.168.1.0/24 for OSPF router ID selection. Before starting the OSPF process, create a loopback interface on each OSPF router, and use a private IP address with a 32-bit mask as the IP address of the loopback interface. This private IP address is then used as the router's router ID. If there is no special requirement, this loopback interface address does not need to be advertised to the OSPF network.

## Slide 17: Basic OSPF Concepts: Area
Each OSPF area is regarded as a logical group and identified by an area ID.
An OSPF area ID is a 32-bit non-negative integer in dotted decimal notation (the format is the same as that of an IPv4 address), for example, area 0.0.0.1. For simplicity, an OSPF area ID is also expressed in decimal notation.
Area 0
R1
R3
R2
Area
Router ID
Metric
Notes: For example, area 0.0.0.1 is equivalent to area 1, area 0.0.0.255 is equivalent to area 255, and area 0.0.1.0 is equivalent to area 256. Devices of many network vendors support the two area ID configuration and representation modes.

## Slide 18: Basic OSPF Concepts: Metric
OSPF uses the cost as the route metric. Each OSPF-enabled interface maintains an interface cost. The default interface cost is 100 Mbit/s divided by interface bandwidth. The value 100 Mbit/s is the default reference value specified by OSPF and is configurable.
OSPF uses the accumulated cost, that is, the total cost of the outbound interfaces of all routers that the traffic passes from the source network to the destination network.
FE interface
Default cost = 1
GE interface
Default cost = 1
Serial interface (1.544 Mbit/s) Default cost = 64
Cost = 1
Cost = 64
10.0.1.1/32
R1
R2
R3
In the routing table of R3, the cost of the OSPF route to network segment 10.0.1.1/32 is 1 plus 64, that is, 65.
Cost of the OSPF Interface
Different OSPF interfaces have different costs because of their different bandwidths.
Accumulated Cost of the OSPF Path
Area
Router ID
Metric
Notes: In practice, you are advised to manually set the cost based on the interface bandwidth instead of changing the OSPF reference bandwidth.

## Slide 19: Basic OSPF Concepts: Example for Changing the Metric
[R4]display ip routing-table 10.0.1.1
Summary Count : 1
[R4]display ip routing-table 10.0.1.1
Summary Count : 2
Area
Router ID
Metric
Access layer
Area 0
Aggregation layer
R1
R2
R3
R4
Area 1
10.0.1.1/32
Default cost of GE 0/0/0
Default cost of GE 0/0/0
Default cost of GE 0/0/1
Default cost of GE 0/0/1
Destination/Mask | Proto | Cost | NextHop | Interface
10.0.1.1/32 | OSPF | 2 | 10.0.34.3 | GigabitEthernet0/0/1
 | OSPF | 2 | 10.0.24.2 | GigabitEthernet0/0/0
Destination/Mask | Proto | Cost | NextHop | Interface
10.0.1.1/32 | OSPF | 20 | 10.0.34.3 | GigabitEthernet0/0/0
Area 0
R1
R2
R3
R4
Area 1
GE 0/0/0 Cost 10
GE 0/0/0 Cost 100
GE 0/0/1 Cost 10
GE 0/0/1 Cost 10
Aggregation layer
By default, there are two paths from R4 to network segment 10.0.1.1/32, and the data forwarding path is uncontrollable.
10.0.1.1/32
In the figure, the cost of the device interface is changed to ensure that traffic does not need to pass through R2 when the access router accesses R1.
Notes: During traffic path planning, it is recommended that the cost of the direct link at the aggregation layer be greater than the sum of costs of all links on the access ring. In this way, traffic can be directly transmitted to R1 or R2 through the access router.
The preceding figure is used as an example. R1 and R2 are located at the aggregation layer of the enterprise network. The direct link between R1 and R2 belongs to area 0. R1 has a directly connected network segment 10.0.1.1/32 in area 0.
  By default, the route from R4 to 10.0.1.1/32 has two next hops.
  After the cost is changed, the route from R4 to 10.0.1.1 has only one next hop.

## Slide 20: Three OSPF Tables: OSPF Neighbor Table
OSPF has three important tables: OSPF neighbor table, LSDB, and OSPF routing table. Pay attention to the following information about the OSPF neighbor table:
  Before OSPF transmits link state information, OSPF neighbor relationships must be established.
  OSPF neighbor relationships are established by exchanging Hello packets.
  The OSPF neighbor table displays the status of the neighbor relationship between OSPF routers. You can run the display ospf peer command to view the status.
[R1]display ospf peer
<R1> display ospf peer
OSPF Process 1 with Router ID 10.0.1.1
Neighbors
Area 0.0.0.0 interface 10.0.12.1(GigabitEthernet1/0/0)'s neighbors
Router ID: 10.0.2.2 Address: 10.0.12.2 GR State: Normal
State: Full Mode:Nbr is Master Priority: 1
DR: 10.0.12.1 BDR: 10.0.12.2 MTU: 0
Dead timer due in 35 sec
Retrans timer interval: 5
Neighbor is up for 00:00:05
Authentication Sequence: [ 0 ]
R1
R2
Router ID:10.0.1.1
Router ID:10.0.2.2
OSPF Neighbor Table
LSDB
OSPF Routing Table
10.0.12.2/30
10.0.12.1/30
GE1/0/0
GE1/0/0

## Slide 21: Three OSPF Tables: LSDB
Pay attention to the following information about the LSDB:
  The LSDB stores the LSAs generated by R1 and received from its neighbors. In this example, the LSDB of R1 contains three LSAs.
  Type indicates the LSA type, and AdvRouter indicates the router that sends the LSA.
  You can run the display ospf lsdb command to check the LSDB.
<R1> display ospf lsdb
OSPF Process 1 with Router ID 10.0.1.1
Link State Database
Area: 0.0.0.0
[R1]display ospf lsdb
R1
R2
Router ID:10.0.1.1
Router ID:10.0.2.2
10.0.12.2/30
10.0.12.1/30
GE1/0/0
GE1/0/0
Type | LinkStateID | AdvRouter | Age | Len | Sequence | Metric
Router | 10.0.2.2 | 10.0.2.2 | 98 | 36 | 8000000B | 1
Router | 10.0.1.1 | 10.0.1.1 | 92 | 36 | 80000005 | 1
Network | 10.0.12.2 | 10.0.2.2 | 98 | 32 | 80000004 | 0
OSPF Neighbor Table
LSDB
OSPF Routing Table

## Slide 22: Three OSPF Tables: OSPF Routing Table
Pay attention to the following information about the OSPF routing table:
  The OSPF routing table and the router routing table are different. In this example, the OSPF routing table contains three routes.
  An OSPF routing table contains information that guides packet forwarding, for example, destination, cost, and next hop.
  You can run the display ip routing-table command to check the OSPF routing table.
<R1> display ospf routing
OSPF Process 1 with Router ID 10.0.1.1
Routing Tables
Routing for Network
Destination Cost Type NextHop AdvRouter Area
10.0.1.1/32 0 stub 10.0.1.1 10.0.1.1 0.0.0.0
10.1.12.0/20 1 Transit 10.0.12.1 10.0.1.1 0.0.0.0
10.0.2.2/32 1 stub 10.0.12.2 10.0.2.2 0.0.0.0
Total Nets: 3
Intra Area: 3 Inter Area: 0 ASE: 0 NSSA: 0
[R1]display ospf routing
R1
R2
Router ID:10.0.1.1
Router ID:10.0.2.2
10.0.12.2/30
10.0.12.1/30
GE1/0/0
GE1/0/0
OSPF Neighbor Table
LSDB
OSPF Routing Table
Notes: The routing table of a router is called a global routing table. Not all OSPF routes can be added to the routing table of a router.

## Slide 23: OSPF Packet Format and Type
OSPF defines five types of packets. Different types of OSPF packets have the same header format.
OSPF packets are encapsulated in IP packets. The protocol number in the IP header of OSPF packets is 89.
Type | Packet Name | Function
1 | Hello | Discovers and maintains neighbor relationships.
2 | Database Description | Exchanges brief LSDB information.
3 | Link State Request | Requests specific link state information.
4 | Link State Update | Sends detailed link state information.
5 | Link State Ack | Acknowledges LSAs.
Version | Type | Packet Length
Router ID |  | 
Area ID |  | 
Checksum |  | Auth Type
Authentication |  | 
IP Packet header | OSPF Packet header | OSPF Packet data
Protocol number 89
Notes: Key fields:
  Version: indicates the OSPF version. The value of this field is 2 for OSPFv2.
  Router ID: indicates the router ID of the router that generates the packet.
  Area ID: indicates the ID of the area to which the packet is advertised.
  Type: indicates the packet type.
  Packet length: indicates the length of an OSPF packet, in bytes.
  Checksum: indicates the LSA checksum. It is used to check the entire OSPF packet, including the OSPF packet header.
  Auth Type:
    0: no authentication
    1: plain-text password authentication
    2: cipher-text (MD5) authentication
  Authentication: indicates information required for authentication. The value of this field varies according to the value of AuType.

## Slide 24
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
  Neighbor Relationship Establishment
  Adjacency Establishment
  Functions of the DR and BDR
Basic OSPF Configurations

## Slide 25: Summary of OSPF Working Mechanism
R1
R2
Discover neighbors on a direct link through Hello packets
Negotiate master/slave roles
Describe LSDBs (summary information)
Update LSAs and synchronize LSDBs of both ends
1
2
4
3
5
Calculate route
Steps 1 to 4 are performed through interaction between the two parties, and step 5 is performed independently.
Calculate route
Neighbor relationship
Adjacency

## Slide 26: Neighbor Relationship Establishment
OSPF uses Hello packets to discover and establish neighbor relationships.
On an Ethernet link, by default, OSPF sends Hello packets in multicast mode (destination address: 224.0.0.5).
An OSPF Hello packet contains information such as the router ID and neighbor list of a router.
Down: Initial state of a neighbor, which indicates that no packets are received from the neighbor.
Init: The router has received a Hello packet from its neighbor, but its router ID is not in the neighbor list of the received Hello packet.
2-way: The router finds that its router ID exists in the neighbor list of the received Hello packet.
R2
10.0.2.2
Hello (Router ID: 10.0.2.2 neighbor: null)
Hello (Router ID: 10.0.2.2 neighbor: 10.0.1.1)
R1
10.0.1.1
Hello (Router ID: 10.0.1.1 neighbor: null)
Neighbor status of R1
Down
Init
2-way
1
1
2
Notes: R1 and R2 send Hello packets to each other. The first Hello packet contains an empty neighbor list.
After R2 receives the Hello packet from R1, R2 finds that parameters in the Hello packet match those configured on R2. Then R2 adds R1 to its neighbor list when sending a Hello packet again.
On an Ethernet link, Hello packets are transmitted in multicast mode.
  The value 224.0.0.5 is the reserved IP multicast address of the OSPF device.
  The value 224.0.0.6 is the IP multicast address reserved for Designated Routers (DRs) or Backup Designated Routers (BDRs).
For links that do not support multicast, OSPF can send Hello packets in unicast mode.

## Slide 27: Hello Packet
Hello packets are used in the following scenarios:
  Neighbor discovery: Hello packets are used to automatically discover neighboring routers.
  Neighbor relationship establishment: The two ends negotiate parameters in Hello packets and establish a neighbor relationship.
  Neighbor relationship holding: A router periodically sends and receives Hello packets to detect the operating status of neighbors.
Network Mask |  | 
Hello Interval | Options | Router Priority
RouterDeadInterval |  | 
Designated Router |  | 
Backup Designated Router |  | 
Neighbor |  | 
… |  | 
Key fields
Network Mask: indicates the network mask of the interface that sends Hello packets.
HelloInterval: indicates the interval at which Hello packets are sent. The value is 10s typically.
RouterDeadInterval: indicates the expiration time of a neighbor relationship. If a device does not receive any Hello packets from its neighbors within a specified Dead interval, the neighbors are considered to be Down. The value is 40s typically.
Neighbor: indicates the router ID of a neighbor.
Description of other fields
Options:
  E: indicates whether external routes are supported.
  MC: indicates whether to support forwarding of multicast data packets.
  N/P: indicates whether the area is an NSSA.
  Router Priority: indicates the DR priority. The default value is 1. If it is set to 0, the router cannot participate in DR or BDR election.
Designated Router: indicates the interface address of a DR.
Backup Designated Router: indicates the interface address of a BDR.

## Slide 28
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
  Neighbor Relationship Establishment
  Adjacency Establishment
  Functions of the DR and BDR
Basic OSPF Configurations

## Slide 29: Adjacency Establishment (1)
Exchange
DD(Seq=X, I=1, M=1, MS=1)
DD(Seq=Y, I=1, M=1, MS=1)
DD (Seq=Y, LSDB summary)
DD (Seq = Y + 1, LSDB summary, MS = 1)
DD(Seq=Y+1)
R1
10.0.1.1
R2
10.0.2.2
ExStart
Loading
2-way
Fields in DD packets
I: If the DD packet is the first among multiple consecutive DD packets sent by a device, this field is set to 1. Otherwise, this field is set to 0.
M (More): If the DD packet is the last among multiple consecutive DD packets sent by a device, this field is set to 0. Otherwise, this field is set to 1.
MS (Master/Slave): When two OSPF routers exchange DD packets, they need to determine the master/slave relationship. The router with a larger router ID becomes the master router. The value 1 indicates that the sender is the master.
DD sequence number: indicates the sequence number of a DD packet. The master and slave devices use sequence numbers to ensure the reliability and integrity of DD packet transmission.
Neighbor status of R1
ExStart: The router starts to send DD packets to its neighbor. The DD packets sent in this state do not contain the link state description.
Exchange: A router and its neighbor exchange DD packets that contain link state summaries.
Loading: A router and its neighbor send LSR packets, LSU packets, and LSAck packets to each other.
Notes: The router IDs of R1 and R2 are 10.0.1.1 and 10.0.2.2 respectively, and the neighbor relationship has been established between R1 and R2. When the neighbor status of R1 changes to ExStart, R1 sends the first DD packet. In the DD packet, if the M-bit is set to 1, subsequent DD packets need to be sent. If the MS-bit is set to 1, R1 declares itself as the master router. The DD sequence number is randomly set to X, and the I-bit is set to 1, indicating that this is the first DD packet.
Similarly, when the neighbor status of R2 changes to ExStart, R2 also sends the first DD packet. In this packet, the DD sequence number is randomly set to Y (I-bit=1, M-bit=1, MS-bit=1, and the meaning is the same as above). Because R2 has a larger router ID, R2 becomes the master router. After R1 receives this packet, R1 generates a Negotiation-Done event and changes the neighbor status from ExStart to Exchange.
When the neighbor status of R1 changes to Exchange, R1 sends a new DD packet carrying the LSDB summary. The sequence number is set to the sequence number Y used by R2 in step 2. The I-bit is 0, indicating that R1 is not the first DD packet. The M-bit is 0, indicating that the packet is the last DD packet carrying the LSDB summary. The MS-bit is 0, indicating that R1 declares itself as the slave device. After R2 receives the packet, R2 changes the neighbor status from ExStart to Exchange.
When the neighbor status of R2 changes to Exchange, R2 sends a new DD packet that contains the summary of the LSDB. The DD sequence number is set to (Y+1) and the MS-bit is set to 1, indicating that R2 declares itself as the master router.
Although R1 does not need to send a new DD packet that contains the LSDB summary, R1 needs to acknowledge each DD packet sent by the master router. Therefore, R1 sends a new DD packet with the sequence number (Y+1) to R2. The packet is empty. After the packet is sent, RTA generates an Exchange-Done event and changes the neighbor status to Loading. After receiving the packet, R2 changes the neighbor status to Full. (Assume that the LSDB of R2 is the latest and does not need to request R1 to update the LSDB.)

## Slide 30: DD Packet
A DD packet contains the LSA header information, including the LS type, LS ID, Advertising Router, LS Sequence Number, and LS Checksum.
Interface MTU | Options | 0 0 0 0 0 I M MS
DD sequence number |  | 
LSA Header |  | 
Description of other fields
  Interface MTU: indicates the maximum size of an IP packet that an interface can send without fragmenting the packet. The DD packets sent by two neighbors contain the MTU. If the MTU in the received DD packet is different from the local MTU, the DD packet is discarded. By default, MTU check is disabled on a Huawei device.
  Options: The field is the same as that in a Hello packet.

## Slide 31: Adjacency Establishment (2)
Neighbor status of R1
LSR
LSU
LSAck
R1
R2
Full
Loading
R1 starts to send LSR packets to R2 to request the link state information that is discovered through DD packets in Exchange state and does not exist in the local LSDB.
R2 sends an LSU packet to R1. The LSU packet contains detailed information about the requested link state. After R1 receives the LSU packet and does not have other LSAs to be requested, R1 changes the neighbor status from Loading to Full.
R1 sends an LSAck packet to R2 to acknowledge the LSU packet.
Question: If multiple routers are located on the same broadcast network, what are the problems in establishing adjacencies using the preceding method?
Full: The router has synchronized the LSDB with the neighbor.

## Slide 32
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
  Neighbor Relationship Establishment
  Adjacency Establishment
  Functions of the DR and BDR
Basic OSPF Configurations

## Slide 33: Functions of the DR and BDR
Solution
Problems on the MA Network
  n x (n-1)/2 adjacencies complicate management.
  Repeated LSA flooding wastes resources.
DR election on an MA network:
  A DR establishes and maintains adjacencies on an MA network and synchronizes LSAs.
  The DR establishes adjacencies with all other routers and exchanges link state information with them. Other routers do not directly exchange link state information.
  To prevent single points of failures (SPOFs), a BDR is elected to quickly take over services of the DR when the DR fails.
Adjacency
R1
R3
R5
R2
R4
R1
R3
R5
R2
R4
DR
BDR
DR
BDR
Notes: Multiple access (MA) is classified into broadcast multi-access (BMA) and non-broadcast multiple access (NBMA). The network formed by Ethernet links is a typical BMA network. FR links are logically divided to form a typical NBMA network. (Note: FR-related information is not described here.)
DRother: A router that is not a DR or a BDR is a DRother.

## Slide 34: DR and BDR Election Rules
DR or BDR election is in non-preemption mode.
DR or BDR election is based on interfaces.
  The greater the DR priority of an interface, the higher the priority.
  If the DR priorities of interfaces are the same, the interface with a larger router ID is preferred.
100
0
95
200
10.0.1.1
R1 (DR)
10.0.1.1
R2 (DRother)
10.0.2.2
R3 (BDR)
10.0.3.3
New router - R4 (DRother)
10.0.4.4
Not participating in the election
Question:
  If the priorities of the four routers in the preceding figure are all set to 0, can OSPF work normally?
  Which types of links form an MA network by default?
R4 is a new device and cannot become a DR or BDR.
Notes: The DR and BDR election process on a broadcast or NBMA link is as follows:
  When going Up, an interface sends Hello packets and enters the waiting state. In Waiting state, there is a WaitingTimer that has the same value as the DeadTimer. By default, the waiting timer duration is 40 seconds, which cannot be changed.
  Before the waiting timer is triggered, sent Hello packets carry no DR or BDR field. During the waiting period, if the received Hello packets contain the DR or BDR field, the election is not triggered and routers directly leave the waiting state to start neighbor synchronization.
  Assume that a DR and a BDR exist on the network. Any router newly connected to the network will accept the DR and BDR that exist on the network regardless of its router ID or DR priority.
  If the DR fails and goes Down, the BDR takes over the role of the DR and the remaining devices whose priority is greater than 0 compete to become the new BDR.
  The DR is elected based on the rules only when routers with different router IDs or DR priorities become Up and perform DR election simultaneously.

## Slide 35: DR and BDR Election on Different Types of Networks
OSPF Network Type | Common Data Link Layer Protocol | Whether to Elect a DR | Whether to Establish an Adjacency with the Neighbor
Point-to-point | PPP and HDLC | No | Yes
Broadcast | Ethernet | Yes | The DR establishes adjacencies with the BDR and DRothers. The BDR establishes adjacencies with the DR and DRothers. The DRothers establish a neighbor relationship.
NBMA | FR |  | 
P2MP | Manually specified protocol | No | Yes
Notes: P2MP: point-to-multipoint

## Slide 36: Adjusting the OSPF Network Type of Device Interfaces as Needed
CO-R1
CO-R2
AS-R1
AS-R2
OSPF
Ethernet link
The OSPF network type is automatically set based on the data link layer encapsulation of the interface.
Routers in the figure are interconnected through Ethernet interfaces, so the network type of these interfaces is broadcast by default.
Each link is a point-to-point (P2P) link, so it is unnecessary to elect the DR and BDR on a link.
To improve OSPF efficiency and speed up the establishment of neighbor relationships, you can change the network type of these interconnected interfaces to P2P.
In the interface view, run the ospf network { p2p | p2mp | broadcast | nbma } command to change the network type of the interface.
Notes: The OSPF network type is automatically set according to the data link layer encapsulation of an interface. As shown in the figure, two routers AS-R1 and AS-R2 at the network access layer are connected to the routers CO-R1 and CO-R2 at the core layer through two links. OSPF is enabled on the interfaces of the four routers. These routers are interconnected through Ethernet interfaces, so the network type of these interfaces is broadcast by default. During the establishment of neighbor relationships, OSPF elects the DR and BDR on each Ethernet link.
However, this is unnecessary and time-consuming (the DR and BDR election process involves a waiting timer, which increases the time for directly connected routers to establish adjacencies). These links are P2P connections logically, so DR or BDR election is unnecessary. To improve OSPF efficiency and speed up the establishment of neighbor relationships, you can change the network type of these interconnected interfaces to P2P.

## Slide 37
Introduction to Dynamic Routing Protocols
Overview of OSPF
OSPF Working Mechanism
Basic OSPF Configurations

## Slide 38: Configuration Commands (1)
[Huawei] ospf [ process-id | Router ID Router ID ]
Create an OSPF process and enter the OSPF view.
The router supports OSPF multi-process, and the process ID is configured locally. Two devices that use different OSPF process IDs can also establish an adjacency.
[Huawei-ospf-1] area area-id
Create an OSPF area and enter the OSPF area view.
[Huawei-ospf-1-area-0.0.0.0] network network-address wildcard-mask
Enable OSPF in the OSPF area.
[Huawei-GigabitEthernet1/0/0] ospf enable process-id area area-id
Enable OSPF in the interface view.
Run the following command to configure the network segment included in the area. The mask length of the interface IP address is larger than or equal to the mask length specified by the network command, and the primary IP address of the interface must be on the network segment specified by the network command. In this case, OSPF can be activated in the corresponding area on the interface.
The ospf enable command takes precedence over the network command.
Notes: By default, OSPF advertises the IP address of a loopback interface as a 32-bit host route, which is independent of the mask length configured on the loopback interface. Therefore, to configure OSPF to advertise the actual network segment of a loopback interface, set the network type of the interface to NBMA or broadcast on the loopback interface.

## Slide 39: Configuration Commands (2)
[Huawei-GigabitEthernet1/0/0] ospf dr-priority priority
Set a priority for an interface that participates in the DR election in the interface view.
[Huawei-GigabitEthernet1/0/0] ospf timer Hello interval
Set the interval for sending Hello packets on an interface.
[Huawei-GigabitEthernet1/0/0] ospf network-type { broadcast | nbma | p2mp | p2p }
Set a network type for an OSPF interface.
By default, the priority is 1.
By default, the network type of an interface is determined by the physical interface. The network type of an Ethernet interface is broadcast, and the network type of a serial interface or a POS interface (PPP or HDLC is used) is P2P.
By default, for a P2P or broadcast interface, the interval for sending Hello packets is 10 seconds; the dead interval after which an interface considers its OSPF neighbor invalid is four times the interval for sending Hello packets.

## Slide 40: OSPF Configuration Examples
The configuration on R2 is used as an example.
[R2]ospf 1 router-id 10.0.2.2
[R2-ospf-1]area 0.0.0.0
[R2-ospf-1-area-0.0.0.0] network 10.0.12.0 0.0.0.255
[R2-ospf-1-area-0.0.0.0] network 10.0.24.2 0.0.0.0
[R2-ospf-1-area-0.0.0.0] network 10.0.235.2 0.0.0.0
R2
R3
R5
R1
R4
SW1
Ethernet link
Serial link
GE0/0/0
GE0/0/0
Se1/0/1
Se1/0/1
Basic information: The router ID of each device is 10.0.x.x, where x is the router number. For example, the router ID of R5 is 10.0.5.5. The IP address for interconnection between devices is 10.0.xyz.x(y)/24, where xyz indicate the router numbers. The router numbers are in ascending order. For example, the IP address of GE0/0/1 on R2 is 10.0.235.2/24.
Topology: Five routers work in area 0.
Se1/0/0
Se1/0/0
GE0/0/0
GE0/0/1
GE0/0/0
Se1/0/1
Se1/0/0
GE0/0/1
GE0/0/2
GE0/0/3

## Slide 41: OSPF Configuration Verification (1)
Run the display ospf interface all command to check information about all OSPF interfaces on the device.
  Time parameters, such as the interval for sending Hello packets and dead interval
  Link type and MTU of the interface
  Interface IP address of the DR and the priority of the DR for an Ethernet link
[R2]display ospf interface all
OSPF Process 1 with Router ID 10.0.2.2
Area: 0.0.0.0
Interface: 10.0.12.2 (GigabitEthernet0/0/0)
Cost: 1 State: DR Type: Broadcast MTU: 1500 Priority: 1
Designated Router: 10.0.12.2
Backup Designated Router: 10.0.12.1
Timers: HELLO 10 , Dead 40 , Poll 120 , Retransmit 5 , Transmit Delay 1
Interface: 10.0.235.2 (GigabitEthernet0/0/1)
Cost: 1 State: DROther Type: Broadcast MTU: 1500 Priority: 1
Designated Router: 10.0.235.5
Backup Designated Router: 10.0.235.3
Timers: HELLO 10 , Dead 40 , Poll 120 , Retransmit 5 , Transmit Delay 1
Interface: 10.0.24.2 (Serial1/0/1) --> 10.0.24.4
Cost: 48 State: P-2-P Type: P2P MTU: 1500
Timers: HELLO 10 , Dead 40 , Poll 120 , Retransmit 5 , Transmit Delay 1
R2
R3
R5
R1
R4
SW1
OSPF interface
GE0/0/0
Se1/0/1
GE0/0/1

## Slide 42: OSPF Configuration Verification (2)
<R2>display ospf peer
OSPF Process 1 with Router ID 10.0.2.2
Area 0.0.0.0 interface 10.0.12.2(GigabitEthernet0/0/0)'s neighbors
Router ID: 10.0.1.1 Address: 10.0.12.1
State: Full Mode:Nbr is Slave Priority: 1
DR: 10.0.12.2 BDR: 10.0.12.1 MTU: 0
Dead timer due in 28 sec
Retrans timer interval: 5
Neighbor is up for 00:01:31
Authentication Sequence: [ 0 ]
Area 0.0.0.0 interface 10.0.235.2(GigabitEthernet0/0/1)'s neighbors
Router ID: 10.0.3.3 Address: 10.0.235.3
State: Full Mode:Nbr is Master Priority: 1
DR: 10.0.235.5 BDR: 10.0.235.3 MTU: 0
Dead timer due in 30 sec
Retrans timer interval: 5
Neighbor is up for 00:01:31
Authentication Sequence: [ 0 ]
R2
R3
R5
R1
R4
SW1
Run the display ospf peer command to check the neighbor status of the device.
  Router ID of the neighboring router
  Neighbor status, such as FULL, TWO-WAY, and DOWN

## Slide 43: OSPF Configuration Verification (3)
<R2>display ospf peer
OSPF Process 1 with Router ID 10.0.2.2
Area 0.0.0.0 interface 10.0.235.2(GigabitEthernet0/0/1)'s neighbors
Router ID: 10.0.5.5 Address: 10.0.235.5
State: Full Mode:Nbr is Master Priority: 1
DR: 10.0.235.5 BDR: 10.0.235.3 MTU: 0
Dead timer due in 40 sec
Retrans timer interval: 0
Neighbor is up for 00:01:27
Authentication Sequence: [ 0 ]
Area 0.0.0.0 interface 10.0.24.2(Serial1/0/1)'s neighbors
Router ID: 10.0.4.4 Address: 10.0.24.4
State: Full Mode:Nbr is Master Priority: 1
DR: None BDR: None MTU: 0
Dead timer due in 35 sec
Retrans timer interval: 5
Neighbor is up for 00:01:56
Authentication Sequence: [ 0 ]
R2
R3
R5
R1
R4
SW1
  On a P2P network, DR or BDR election is not required. Therefore, when checking the OSPF neighbor table of R2, you can find that the DR/BDR field of Serial1/0/1 in the command output is None.

## Slide 44: OSPF Configuration Verification (4)
Are LSDBs on other devices the same?
<R2>display ospf lsdb
OSPF Process 1 with Router ID 10.0.2.2
Link State Database
Area: 0.0.0.0
R2
R3
R5
R1
R4
SW1
Type | LinkState ID | AdvRouter | Age | Len | Sequence | Metric
Router | 10.0.4.4 | 10.0.4.4 | 662 | 72 | 80000006 | 48
Router | 10.0.2.2 | 10.0.2.2 | 625 | 72 | 8000000C | 1
Router | 10.0.1.1 | 10.0.1.1 | 638 | 60 | 80000007 | 1
Router | 10.0.5.5 | 10.0.5.5 | 634 | 60 | 8000000B | 1
Router | 10.0.3.3 | 10.0.3.3 | 639 | 60 | 80000009 | 1
Network | 10.0.235.5 | 10.0.5.5 | 634 | 36 | 80000005 | 0
Network | 10.0.12.2 | 10.0.2.2 | 629 | 32 | 80000003 | 0
Run the display ospf lsdb command to check the LSDB of the device.
  An LSDB consists of multiple types of LSAs. All LSAs have the same packet header format, in which key fields such as Type, LinkState ID, and AdvRouter are included. The next course will focus on LSA details.

## Slide 45: OSPF Configuration Verification (5)
Run the display ospf routing command to check the OSPF routing table of the device.
  The OSPF routing table of R2 shows that R2 has learned the routes to the entire network through OSPF.
<R2>display ospf routing
OSPF Process 1 with Router ID 10.0.2.2
Routing Tables
R2
R3
R5
R1
R4
SW1
Destination | Cost | Type | NextHop | AdvRouter | Area
10.0.12.0/24 | 1 | Transit | 10.0.12.2 | 10.0.2.2 | 0.0.0.0
10.0.24.0/24 | 48 | Stub | 10.0.24.2 | 10.0.2.2 | 0.0.0.0
10.0.235.0/24 | 1 | Transit | 10.0.235.2 | 10.0.2.2 | 0.0.0.0
10.0.13.0/24 | 49 | Stub | 10.0.12.1 | 10.0.1.1 | 0.0.0.0
10.0.13.0/24 | 49 | Stub | 10.0.235.3 | 10.0.3.3 | 0.0.0.0
10.0.45.0/24 | 49 | Stub | 10.0.235.5 | 10.0.5.5 | 0.0.0.0

## Slide 46
(Single) Which of the following packets is used by OSPF to maintain neighbor relationships? ( )
  Hello
  Database Description
  LSR
  LSU
(Multiple) Which of the following network types are supported by OSPF? ( )
  P2P network
  P2MP network
  Broadcast network
  NBMA network
Notes: A
ABCD

## Slide 47
This course describes basic OSPF concepts, including the router ID, area, and cost. Routers running OSPF send link state information to each other to calculate the topology and routes.
This course describes the process of establishing OSPF neighbor relationships and adjacencies. On an MA network, the DR and BDR need to be elected. There are five types of OSPF packets. All packets have the same packet header format. An OSPF router periodically sends Hello packets to discover and maintain neighbor relationships, and uses DD, LSR, LSU, and LSAck packets to synchronize LSDBs. Finally, this course introduces the simple configuration of a single OSPF area.