## Slide 1
He Junjian/hwx580230
2019-11-11
New

## Slide 2: OSPF Route Calculation

## Slide 3
Open Shortest Path First (OSPF) routers in the same area have the same link state database (LSDB). In an area, OSPF uses the shortest path first (SPF) algorithm to calculate routes.
As the network scale expands, routers consume more memory and CPU resources to calculate routes. Area partitioning can relieve the pressure on routers to some extent.
On a large-scale network, there may be other routing protocols besides OSPF. OSPF can import external routes so that OSPF routers can know the routes to other areas.
This course describes the principles of OSPF route calculation, including the calculation of intra-area routes, inter-area routes, and external routes.

## Slide 4
Upon completion of this course, you will be able to:
  Explain functions of key fields in link-state advertisements (LSAs).
  Describe common LSA types and functions.
  Illustrate the SPF algorithm.
  Describe the principles for calculating intra-area and inter-area OSPF routes.
  Describe the loop prevention mechanism of OSPF inter-area routes.
  Describe the principles for calculating OSPF external routes.

## Slide 5
Intra-Area Route Calculation
  Introduction to LSAs
  Router-LSA
  Network-LSA
  SPF Calculation Process
Inter-Area Route Calculation
External Route Calculation

## Slide 6: OSPF Review
All routers in the same area have the same LSDB. According to the command output of R2, multiple LSAs exist on the network.
R2
R3
R5
R1
R4
SW1
<R2>display ospf lsdb
OSPF Process 1 with Router ID 10.0.2.2
Link State Database
Area: 0.0.0.0
Type | LinkState ID | AdvRouter | Age | Len | Sequence | Metric
Router | 10.0.4.4 | 10.0.4.4 | 662 | 72 | 80000006 | 48
Router | 10.0.2.2 | 10.0.2.2 | 625 | 72 | 8000000C | 1
Router | 10.0.1.1 | 10.0.1.1 | 638 | 60 | 80000007 | 1
Router | 10.0.5.5 | 10.0.5.5 | 634 | 60 | 8000000B | 1
Router | 10.0.3.3 | 10.0.3.3 | 639 | 60 | 80000009 | 1
Network | 10.0.235.5 | 10.0.5.5 | 634 | 36 | 80000005 | 0
Network | 10.0.12.2 | 10.0.2.2 | 629 | 32 | 80000003 | 0
What information does each LSA contain? Based on the preceding information, how does a router calculate routes?
Ethernet link
Serial link

## Slide 7: Basic Concepts of LSAs
LSAs are the basis for OSPF to calculate routes.
An OSPF Link State Update (LSU) packet can carry multiple types of LSAs.
LSAs of different types have the same packet header.
LS Age | Options | LS Type
Link State ID |  | 
Advertising Router |  | 
LS Sequence Number |  | 
LS Checksum | Length | 
IP Header | OSPF Header | LSU Payload
Key Fields
  LS Age: indicates the lifetime of an LSA, in seconds.
  Options: Each bit corresponds to a feature supported by OSPF.
  LS Type: indicates the type of the local LSA.
  Link State ID: indicates the link state ID in the LSA header. This field varies with LSAs.
  Advertising Router: indicates the router ID of the device that generates the LSA.
  LS Sequence Number: indicates the sequence number in the LSA header. The value increases each time a new instance is generated.
  LS Checksum: is used to ensure data integrity and accuracy.
  Length: indicates the length of an LSA, including the length of the LSA header.
LS Type, Link State ID, and Advertising Router uniquely identify an LSA.
LS Age, LS Sequence Number, and LS Checksum are used to determine whether an LSA is old or new.
LSA Header | Payload
… | …
Notes: LS Age: When an LSA is originated, the value of this field is 0. The value of this field increases as the LSA is flooded on the network. When the value of this field reaches the value of MaxAge (3600s by default), the LSA is not used for route calculation.
LS Sequence Number: This field is used to determine whether an LSA is old or new or whether there are duplicate instances. The sequence number ranges from 0x80000001 to 0x7FFFFFFF. A router originates an LSA with the sequence number 0x80000001. The sequence number increases by 1 each time the LSA is updated. When the sequence number of the LSA reaches the maximum value, the LSA is regenerated and the sequence number is set to 0x80000001.

## Slide 8: Common LSA Types
Type | Name | Description
1 | Router-LSA | Every router on an OSPF network generates Router-LSAs. A Router-LSA describes a router's link state and cost and can be flooded only in the area to which the interface belongs.
2 | Network-LSA | A designated router (DR) generates Network-LSAs. A Network-LSA describes all the routers that establish adjacencies with the DR on the MA network to which the DR is connected and the DR itself. The LSA can be flooded only in the area to which the interface belongs.
3 | Network-summary-LSA | An area border router (ABR) generates Network-summary-LSAs. A Network-summary-LSA describes the route to the destination network segment of an area. It is used to transmit inter-area routes.
4 | ASBR-summary-LSA | An ABR generates ASBR-summary-LSAs. An ASBR-summary-LSA describes routes to an ASBR, and is equivalent to a host route to an autonomous system border router (ASBR).
5 | AS-external-LSA | An ASBR generates AS-external-LSAs. An AS-external-LSA describes routes to destinations outside an AS.
7 | NSSA LSA | An ASBR generates NSSA LSAs. An NSSA LSA describes routes to destinations outside an AS. NSSA LSAs have similar functions as AS-external-LSAs, but are flooded in different areas. NSSA LSAs can be flooded only in the NSSA and cannot enter area 0. The ABR in the NSSA converts Type 7 LSAs into Type 5 LSAs and injects them into area 0.
Notes: In many cases, the type value is used to refer to the corresponding LSA. For example, Type 1 LSAs indicate Router-LSAs and Type 2 LSAs indicate Network-LSAs, and so on.

## Slide 9
Intra-Area Route Calculation
  Introduction to LSAs
  Router-LSA
  Network-LSA
  SPF Calculation Process
Inter-Area Route Calculation
External Route Calculation

## Slide 10: Description of a Router-LSA (1)
Router-LSA (Type 1 LSA): Every router on an OSPF network generates Router-LSAs. A Router-LSA describes a router's link state and cost.
Router-LSAs can be flooded only in the area that the interface belongs to.
LS Age |  |  |  |  | Options | LS Type
Link State ID |  |  |  |  |  | 
Advertising Router |  |  |  |  |  | 
LS Sequence Number |  |  |  |  |  | 
LS Checksum |  |  |  |  | Length | 
0 | V | E | B | 0 | #Links | 
Link ID |  |  |  |  |  | 
Link Data |  |  |  |  |  | 
Link Type | #TOS |  |  |  | Metric | 
… |  |  |  |  |  | 
V (virtual link): If the router that generates the LSA is the endpoint of a virtual link, this field is set to 1.
E (external): If the router that generates the LSA is an ASBR, this field is set to 1.
B (border): If the router that generates the LSA is an ABR, this field is set to 1.
Links: indicates the number of links in the LSA. Router-LSAs use links to carry information about directly connected interfaces on routers.

## Slide 11: Description of a Router-LSA (2)
Router-LSAs use links to carry information about directly connected interfaces on routers.
Each link contains the link type, link ID, link data, and metric.
A router may use one or more links to describe an interface.
LS Age |  |  |  |  | Options | LS Type
Link State ID |  |  |  |  |  | 
Advertising Router |  |  |  |  |  | 
LS sequence number |  |  |  |  |  | 
LS checksum |  |  |  |  | length | 
0 | V | E | B | 0 | #links | 
Link ID |  |  |  |  |  | 
Link Data |  |  |  |  |  | 
link type | #TOS |  |  |  | metric | 
… |  |  |  |  |  | 
Link Type | Link ID | Link Data
Point-to-point (P2P): describes a P2P link between the local router and a neighboring router, which is included in the topology information. | ID of the neighboring router. | IP address of the router interface that advertises the Router-LSA.
TransNet: describes a connection from the local router to a transit network segment such as an MA or NBMA network segment, which is included in the topology information. | Interface IP address of the DR | IP address of the router interface that advertises the Router-LSA.
StubNet: describes a connection from the local router to a stub network segment, for example, a loopback interface, which is included in the network segment information. | Network IP address of the router interface that advertises the Router-LSA | Subnet mask of the stub network.
Notes: Metric: indicates the cost.

## Slide 12: Router-LSAs: P2P Networks
<R1>display ospf lsdb router self-originate
Type : Router
Ls id : 10.0.1.1
Adv rtr : 10.0.1.1
* Link ID: 10.0.3.3
Data : 10.0.13.1
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.13.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
R1
R3
Router ID 10.0.1.1
Router ID 10.0.3.3
R1 sends a Router-LSA to R3. The Router-LSA carries topology and network segment information.
Router-LSA
LSA header
First link in the Router-LSA:
Describe the topology information.
Second link in the Router-LSA:
Describe the network segment information.
Serial
10.0.13.1/24
10.0.13.3/24

## Slide 13: Router-LSAs: TransNet Networks
R3
R2
R5
<R2>display ospf lsdb router self-originate
Type : Router
Ls id : 10.0.2.2
Adv rtr : 10.0.2.2
* Link ID: 10.0.235.2
Data : 10.0.235.2
Link Type: TransNet
Metric : 1
Router ID 10.0.2.2
Router ID 10.0.3.3
Router ID 10.0.5.5
R2 sends Router-LSAs carrying topology information to R3 and R5.
Router-LSA
LSA header
Link contained in a Router-LSA:
Describe topology information.
How is complete network segment information described on the TransNet network if there is no network mask information?
DR
10.0.235.2

## Slide 14
Intra-Area Route Calculation
  Introduction to LSAs
  Router-LSA
  Network-LSA
  SPF Calculation Process
Inter-Area Route Calculation
External Route Calculation

## Slide 15: Description of a Network-LSA
Network-LSA (Type 2 LSA): is originated by a DR, describes the link state of the local network segment, and is advertised in an area to which the DR belongs.
A Network-LSA records all OSPF routers that have established adjacencies with the DR on the network segment and carries the network mask of the network segment.
LS Age | Options | LS Type
Link State ID |  | 
Advertising Router |  | 
LS Sequence Number |  | 
LS Checksum | Length | 
Network Mask |  | 
Attached Router |  | 
... |  | 
Link State ID: indicates the IP address of an interface on the DR.
Network Mask: indicates the subnet mask of the MA network.
Attached Router: indicates the router ID of the device connected to the MA network.

## Slide 16: Network-LSAs Describe the MA Network
<R2>display ospf lsdb network self-originate
OSPF Process 1 with Router ID 10.0.2.2
Area: 0.0.0.0
Link State Database
Type : Network
Ls id : 10.0.235.2
Adv rtr : 10.0.2.2
Net mask : 255.255.255.0
Priority : Low
Attached Router 10.0.2.2
Attached Router 10.0.3.3
Attached Router 10.0.5.5
R3
R2
R5
Router ID 10.0.2.2
Router ID 10.0.3.3
Router ID 10.0.5.5
R2 sends Network-LSAs to R3 and R5, carrying topology and network segment information.
10.0.235.0/24
LSA header
Topology information
DR
10.0.235.2
Network-LSA

## Slide 17
Intra-Area Route Calculation
  Introduction to LSAs
  Router-LSA
  Network-LSA
  SPF Calculation Process
Inter-Area Route Calculation
External Route Calculation

## Slide 18: SPF Algorithm (1)
Phase 1: Construct an SPF tree.
  A router takes itself as the root of the SPF tree. Each time a new node is added, the router with the smallest cost is added to the SPF tree based on the topology information in the Router-LSA and Network-LSA. A router is identified by a router ID or DR ID.
  On a broadcast network, the cost between the DR and the router connected to it is 0.
  The SPF tree has only the unidirectional shortest path, which prevents routing loops in the OSPF area.
10.0.3.3
Cost 1
DR
10.0.12.2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
10.0.5.5
Cost 0
Cost 0
10.0.4.4
Cost 48
Root
10.0.1.1

## Slide 19: SPF Algorithm (2)
Phase 2: Calculate the optimal route.
  The routing information in the Router-LSA and Network-LSA is attached to the corresponding OSPF router to calculate the optimal route.
  The existing routing information is not added to the SPF tree.
10.0.3.3
Cost 1
DR
10.0.12.2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
10.0.5.5
Cost 0
Cost 0
10.0.4.4
Cost 48
Root
10.0.1.1
10.0.13.0/24
10.0.12.0/24
10.0.24.0/24
10.0.235.0/24
10.145.0/24
Cost 48
Cost 0
Cost 48
Cost
48
Cost 0

## Slide 20: SPF Algorithm Example
The following uses R1 as an example to describe the OSPF topology and route calculation process.
R2
R3
R5
R1
R4
SW1
Neighbor to be ignored
Neighbor to be added
Route prefix

## Slide 21: Setting Up an SPF Tree (1)
<R1>display ospf lsdb router self-originate
Type : Router
Ls id : 10.0.1.1
Adv rtr : 10.0.1.1
* Link ID : 10.0.12.2
Data : 10.0.12.1
Link Type : TransNet
Metric : 1
* Link ID : 10.0.3.3
Data : 10.0.13.1
Link Type : P-2-P
Metric : 48
* Link ID : 10.0.13.0
Data : 255.255.255.0
Link Type : StubNet
Metric : 48
Priority : Low
R1
10.0.1.1
Cost 1
DR
10.0.12.2
R1 takes itself as the root and checks the Router-LSA. For a non-StubNet link, R1 adds the link ID to the candidate list and records the path cost.
R1 moves the candidate with the lowest total path cost from the candidate list to the SPF tree, and deletes the candidate from the candidate list.
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.12.2 | 1 | 10.0.1.1
10.0.3.3 | 48 | 10.0.1.1
Phase 1
Phase 2
First route prefix
10.0.13.0/24
1
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.12.2 | 1 | 10.0.1.1
10.0.3.3 | 48 | 10.0.1.1
Notes: Note:
  The total candidate cost is the sum of the metric described in the LSA and the cost of the route from the parent node to the root node.
  The candidate list records the neighbor list.

## Slide 22: Setting Up an SPF Tree (2)
R1
10.0.1.1
Cost 1
DR
10.0.12.2
R2
10.0.2.2
Cost 0
R1 moves the candidate with the lowest total path cost from the candidate list to the SPF tree, and deletes the candidate from the candidate list.
R1 continues to query the Network-LSAs generated by the DR and adds the topology information described in the Network-LSAs to the candidate list. If the node described in the LSAs already exists in the SPF tree, the node does not need to be added to the topology.
<R1>display ospf lsdb network 10.0.12.2
Type : Network
Ls id : 10.0.12.2
Adv rtr : 10.0.2.2
Net mask : 255.255.255.0
Priority : Low
Attached Router 10.0.2.2
Attached Router 10.0.1.1
Phase 1
Phase 2
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.2.2 | 1+0 | 10.0.12.2
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.2.2 | 1+0 | 10.0.12.2
Second route prefix
10.0.12.0/24
2
The node does not need to be added to the topology because the node already exists in the SPF tree.

## Slide 23: Setting Up an SPF Tree (3)
<R1>display ospf lsdb router 10.0.2.2
Type : Router
Ls id : 10.0.2.2
Adv rtr : 10.0.2.2
* Link ID: 10.0.235.2
Data : 10.0.235.2
Link Type: TransNet
Metric : 1
* Link ID: 10.0.4.4
Data : 10.0.24.2
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.12.2
Data : 10.0.12.2
Link Type: TransNet
Metric : 1
* Link ID: 10.0.24.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.235.2 | 1+0+1 | 10.0.2.2
10.0.4.4 | 1+0+48 | 10.0.2.2
R1
10.0.1.1
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
Third route prefix
10.0.24.0/24
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.235.2 | 1+0+1 | 10.0.2.2
10.0.4.4 | 1+0+48 | 10.0.2.2
3
Phase 1
Phase 2
Based on Router-LSAs generated by R2, R1 records neighbor information in the candidate list.
R1 moves the candidate with the lowest total path cost from the candidate list to the SPF tree, and deletes the candidate from the candidate list.

## Slide 24: Setting Up an SPF Tree (4)
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.4.4 | 1+0+48 | 10.0.2.2
10.0.3.3 | 1+0+1+0 | 10.0.235.2
10.0.5.5 | 1+0+1+0 | 10.0.235.2
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.3.3 | 48 | 10.0.1.1
10.0.4.4 | 1+0+48 | 10.0.2.2
10.0.3.3 | 1+0+1+0 | 10.0.235.2
10.0.5.5 | 1+0+1+0 | 10.0.235.2
R3
10.0.3.3
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
R5
10.0.5.5
Cost 0
Cost 0
R1
10.0.1.1
<R1>display ospf lsdb network 10.0.235.2
Type : Network
Ls id : 10.0.235.2
Adv rtr : 10.0.2.2
Net mask : 255.255.255.0
Priority : Low
Attached Router 10.0.2.2
Attached Router 10.0.3.3
Attached Router 10.0.5.5
Fourth route prefix
10.0.235.0/24
4
Phase 1
Phase 2
R1 continues to query Type 2 LSAs generated by the DR and adds the topology information described in Type 2 LSAs to the candidate list.
R1 moves the candidate with the lowest total path cost from the candidate list to the SPF tree, and deletes the candidate from the candidate list.
Notes: R3 has two different cost values in the candidate list: 48 and 2. Therefore, R3 adds the route with the smallest cost to the SPF tree and deletes the route from the candidate list.

## Slide 25: Setting Up an SPF Tree (5)
<R1>display ospf lsdb router 10.0.3.3
Type : Router
Ls id : 10.0.3.3
Adv rtr : 10.0.3.3
* Link ID: 10.0.235.2
Data : 10.0.235.3
Link Type: TransNet
Metric : 1
* Link ID: 10.0.1.1
Data : 10.0.13.3
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.13.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
Phase 1
Phase 2
R1 queries Type 1 LSAs of R3. All neighbors of R3 are in the SPF tree, and the topology does not change.
Same as the first route prefix 10.0.13.0/24
1
The two nodes do not need to be added to the topology because the two nodes already exist in the SPF tree.
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.4.4 | 1+0+48 | 10.0.2.2
R3
10.0.3.3
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
R5
10.0.5.5
Cost 0
Cost 0
R1
10.0.1.1

## Slide 26: Setting Up an SPF Tree (6)
<R1>display ospf lsdb router 10.0.5.5
Type : Router
Ls id : 10.0.5.5
Adv rtr : 10.0.5.5
* Link ID: 10.0.235.2
Data : 10.0.235.5
Link Type: TransNet
Metric : 1
* Link ID: 10.0.4.4
Data : 10.0.45.5
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.45.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
Fifth route prefix
10.0.45.0/24
5
Phase 1
Phase 2
R1 queries Type 1 LSAs of R5, adds R4 to the SPF tree, and deletes R4 from the candidate list.
Candidate List | Total Candidate Cost | Root/Parent Node
10.0.4.4 | 1+0+48 | 10.0.2.2
10.0.4.4 | 1+0+1+0+48 | 10.0.5.5
R3
10.0.3.3
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
R5
10.0.5.5
Cost 0
Cost 0
R4
10.0.4.4
R1
10.0.1.1
Cost 48

## Slide 27: Setting Up an SPF Tree (7)
<R1>display ospf lsdb router 10.0.4.4
Type : Router
Ls id : 10.0.4.4
Adv rtr : 10.0.4.4
* Link ID: 10.0.2.2
Data : 10.0.24.4
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.5.5
Data : 10.0.45.4
Link Type: P-2-P
Metric : 48
* Link ID: 10.0.24.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
* Link ID: 10.0.45.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
R3
10.0.3.3
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
R5
10.0.5.5
Cost 0
Cost 0
R4
10.0.4.4
R1
10.0.1.1
Cost 48
Same as the second route prefix
10.0.24.0/24
Same as the second route prefix
10.0.45.0/24
5
2
Phase 1
Phase 2
R1 queries Type 1 LSAs of R4. All neighbors are in the SPF tree. In addition, all LSAs have been calculated, and the SPF tree has been established.

## Slide 28: Calculating the Optimal Route
Starting from the root node, routing information in the LSA of each node is added according to the sequence in which nodes are added to the SPF tree. The routes that have been added to the SPF tree are not added.
R3
10.0.3.3
Cost 1
DR
10.0.12.2
R2
10.0.2.2
DR
10.0.235.2
Cost 0
Cost 1
R5
10.0.5.5
Cost 0
Cost 0
R4
10.0.4.4
Cost 48
R1
10.0.1.1
* Link ID: 10.0.13.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
Type : Network
Ls id : 10.0.12.2
Adv rtr : 10.0.2.2
Net mask : 255.255.255.0
* Link ID: 10.0.24.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
* Link ID: 10.0.45.0
Data : 255.255.255.0
Link Type: StubNet
Metric : 48
Priority : Low
Type : Network
Ls id : 10.0.235.2
Adv rtr : 10.0.2.2
Net mask : 255.255.255.0
1
2
5
4
3
Phase 1
Phase 2
Notes: In the second phase, the router calculates the optimal route based on routing information in the Router-LSA and Network-LSA.
Starting from the root node, routing information in the LSA of each node is added according to the sequence in which nodes are added to the SPF tree:
  In the Router-LSA of R1 at 10.0.1.1, there is one network. The network ID/subnet mask is 10.0.13.0/24, and the metric is 48.
  In the Network-LSA of DR at 10.0.12.2, the network ID/subnet mask is 10.0.12.0/24, and the metric is 1 (1+0).
  In the Router-LSA of R2 at 10.0.2.2, there is one network. The network ID/subnet mask is 10.0.24.0/24, and the metric is 49 (1+0+48).
  In the Network-LSA of DR at 10.0.235.2, the network ID/subnet mask is 10.0.235.0/24, and the metric is 2 (1+0+1).
  In the Router-LSA of R3 at 10.0.3.3, there is one network. The network ID/subnet mask is 10.0.13.0/24, which already exists on R1 and can be ignored.
  In the Router-LSA of R5 at 10.0.5.5, there is one network. The network ID/subnet mask is 10.0.45.0/24, and the metric is 50 (1+0+0+1+48).
  In the Router-LSA of R4 at 10.0.4.4, there are two networks. One network ID/subnet mask is 10.0.24.0/24, which already exists on R2 and is not added. The other network ID/subnet mask is 10.0.45.0/24, which already exists on R5 and is not added.

## Slide 29: Verifying the Configuration
Question: Why are not all routes in the OSPF routing table of R1 displayed in the global routing table?
<R1>display ospf routing
OSPF Process 1 with Router ID 10.0.1.1
Routing Tables
Routing for Network
Destination Cost Type NextHop AdvRouter Area
10.0.12.0/24 1 Transit 10.0.12.1 10.0.1.1 0.0.0.0
10.0.13.0/24 48 Stub 10.0.13.1 10.0.1.1 0.0.0.0
10.0.24.0/24 49 Stub 10.0.12.2 10.0.2.2 0.0.0.0
10.0.45.0/24 50 Stub 10.0.12.2 10.0.5.5 0.0.0.0
10.0.235.0/24 2 Transit 10.0.12.2 10.0.5.5 0.0.0.0
<R1>display ip routing-table
Destination/Mask Proto Pre Cost NextHop
10.0.12.0/24 Direct 0 0 10.0.12.1
10.0.13.0/24 Direct 0 0 10.0.13.1
10.0.24.0/24 OSPF 10 49 10.0.12.2
10.0.45.0/24 OSPF 10 50 10.0.12.2
10.0.235.0/24 OSPF 10 2 10.0.12.2
OSPF routing table of R1
Global routing table of R1

## Slide 30
(Multiple) Which of the following link types are included in a Router-LSA?( )
  P2P
  TransNet
  StubNet
  Vlink
(TorF) After the SPF algorithm is used to calculate routes, the OSPF routes that are considered as the optimal routes are added to the routing table of the router.
Notes: ABCD
False

## Slide 31
OSPF calculates the routing table based on the LSDB. The LSDB may contain multiple types of LSAs, and all LSAs have the same packet header format.
OSPF routers in the same area have the same LSDB. When there is only one area, there are two types of LSAs in the area: Router-LSA and Network-LSA.
Each router generates a Router-LSA that describes the information about the directly connected interface of the router.
On an MA network, a DR generates a Network-LSA to describe the router IDs (including the DR itself) of all the routers that access the MA network and the mask of the network.

## Slide 32
Intra-Area Route Calculation
Inter-Area Route Calculation
  Inter-Area Route Calculation Process
  Inter-Area Routing Loop Prevention Mechanism
  Functions and Configurations of Virtual Links
External Route Calculation

## Slide 33: Problems in a Single OSPF Area on a Large-Scale Network
A network consisting of a series of consecutive OSPF routers is called an OSPF domain.
OSPF requires that routers on the network synchronize their LSDBs to keep consistent network information.
When the network scale increases continuously, the LSDB becomes oversized. A device calculates routes based on the LSDB, which increases the burden. In addition, the size of the routing table of the router increases, deteriorating the performance of the router.
When the network topology changes, the changes need to be spread to the entire network and may trigger route recalculation on the entire network.
The single-area design makes it impossible to deploy route summarization.
…
…
Area 0

## Slide 34: Area Partitioning
Router-LSAs and Network-LSAs are flooded only within an area, so area partitioning reduces the memory and CPU usage of network devices.
…
…
Area N
Area 1
Area 0
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
Internal router
ABR
R1
R2
R4
R3
R5
After areas are partitioned, routers can be classified into the following types:
  Internal router: An internal router has all its interfaces belonging to the same OSPF area, for example, R1, R4, and R5.
  Area border router (ABR): An ABR connects to two or more areas, for example, R2 and R3.

## Slide 35: Inter-Area Routing Information Transmission
OSPF inter-area routing information is transmitted through Type 3 Network-Summary-LSAs generated by ABRs.
Transmission of the route to 192.168.1.0/24 is used as an example.
  R2 calculates a route (intra-area route) to 192.168.1.0/24 based on the Router-LSA and Network-LSA flooded in area 1, and advertises the route to area 0 through a Network-Summary-LSA. R3 can calculate the inter-area route to 192.168.1.0/24 based on the Network-Summary-LSA.
  R3 generates a Network-Summary-LSA and advertises it to area 2. Then, routers in all OSPF areas can learn the route to 192.168.1.0/24.
Type 1 LSA
Type 3 LSA
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
192.168.1.0/24
192.168.2.0/24
192.168.1.0/24
R2 generates a Type 3 LSA.
192.168.1.0/24
R3 regenerates a Type 3 LSA.

## Slide 36: Description of a Network-Summary-LSA
An ABR generates Network-summary-LSAs (Type 3 LSAs) and advertises them within its area to notify destination addresses of routes from this area to other areas.
LS Age |  | Options | LS Type
Link State ID |  |  | 
Advertising Router |  |  | 
LS Sequence Number |  |  | 
LS Checksum |  | Length | 
Network Mask |  |  | 
0 | Metric |  | 
... |  |  | 
Main Fields
  LS Type: The value 3 indicates a Network-summary-LSA.
  Link State ID: indicates the destination network address of a route.
  Advertising Router: indicates the router ID of the device that generates the LSA.
  Network Mask: indicates the network mask of a route.
  Metric: indicates the cost of the route to the destination address.

## Slide 37: Example of a Network-Summary-LSA
<R2>display ospf lsdb summary 192.168.1.0
OSPF Process 1 with Router ID 10.0.2.2
Area: 0.0.0.0
Link State Database
Type : Sum-Net
Ls id : 192.168.1.0
Adv rtr : 10.0.2.2
Ls age : 86
Len : 28
Options : E
seq# : 80000001
chksum : 0x7c6d
Net mask : 255.255.255.0
Tos0 metric: 1
Priority : Low
Routing information
192.168.1.0/24
This LSA is generated by R2 and is used to advertise inter-area routes destined for 192.168.1.0/24 to area 0.
Area 0
R4
R2
10.0.2.2
R3
R5
R1
Area 1
Area 2
192.168.1.0/24
Network-Summary-LSA
192.168.1.0/24
Cost = 1

## Slide 38: Route Calculation on R1 and R3
Through SPF calculation, the cost of the route from R1 to R2 is 1, and that of the route from R3 to R2 is 2.
R1 and R3 calculate routes based on the received Network-Summary-LSAs.
  R1 adds the cost of the route to R2 and the cost carried in the Network-summary-LSA. Therefore, the cost of the route from R1 to 192.168.1.0/24 is 2.
  R3 adds the cost of the route to R2 and the cost carried in the Network-summary-LSA. Therefore, the cost of the route from R3 to 192.168.1.0/24 is 3.
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
Cost 1
192.168.1.0/24
The cost of the route from R2 to 192.168.1.0/24 is 1, so the cost of the route to 192.168.1.0/24 advertised by R2 to area 0 is 1.
192.168.1.0/24
Cost = 1+1
192.168.1.0/24
Cost = 1+1+1
Cost = 1
Cost = 1
Cost = 1

## Slide 39: Route Calculation on R5
The cost of the route from R3 to 192.168.1.0/24 is 3, so the cost of the route to 192.168.1.0/24 advertised by R3 to area 2 is 3.
Area 0
R2
R3
R5
R1
R4
Area 2
192.168.1.0/24
Cost =1+3
R3 functions as an ABR. It calculates the route to 192.168.1.0/24 based on the Network-Summary-LSA flooded in area 0, and reinjects the Network-Summary-LSA to area 2. The Network-Summary-LSA contains the cost (value 3) of the route to the network segment.
Through SPF calculation, the cost of the route from R5 to R3 is 1, so the cost of the route from R5 to 192.168.1.0/24 is 4.
Area 1
Cost = 1
Network-Summary-LSA
192.168.1.0/24 Cost = 3

## Slide 40: Inter-Area Route Calculation Result Verification
Check the routing tables on R1, R3, and R5.
Area 0
R2
R3
R5
R1
R4
Area 2
Area 1
<R1>display ip routing-table
Destination/Mask Proto Pre Cost
192.168.1.0/24 OSPF 10 2
<R3>display ip routing-table
Destination/Mask Proto Pre Cost
192.168.1.0/24 OSPF 10 3
<R5>display ip routing-table
Destination/Mask Proto Pre Cost
192.168.1.0/24 OSPF 10 4

## Slide 41
Intra-Area Route Calculation
Inter-Area Route Calculation
  Inter-Area Route Calculation Process
  Inter-Area Routing Loop Prevention Mechanism
  Functions and Configurations of Virtual Links
External Route Calculation

## Slide 42: Inter-Area Routing Loops
The process of advertising OSPF inter-area routes is similar to that of advertising routes of distance-vector routing protocols.
OSPF also requires a loop prevention mechanism for inter-area route advertisement.
Area 0
Area 2
R2
R3
R5
R1
R4
Area 3
Area 1
192.168.1.0/24
R2 advertises the inter-area route to 192.168.1.0/24 to area 0.
1
R3 advertises the inter-area route to 192.168.1.0/24 to area 2.
2
R5 advertises the inter-area route to 192.168.1.0/24 to area 3.
3
4
Potential routing loop

## Slide 43: Inter-Area Routing Loop Prevention Mechanism (1)
OSPF requires that all non-backbone areas be directly connected to area 0 and inter-area routes be advertised through area 0.
Inter-area routes cannot be advertised between two non-backbone areas. As such, a star topology is logically formed in the OSPF area architecture.
Area 0
Area 1
Area 2
Area 3
Inter-area route
Notes: OSPF requires that at least one interface of the ABR should belong to the backbone area.

## Slide 44: Inter-Area Routing Loop Prevention Mechanism (2)
An ABR does not reinject Type 3 LSAs that describe routes to a network segment in an area to the area.
R1
R2
R3
Area 1
Area 0
Type 1 and Type 2 LSAs
Type 3 LSA

## Slide 45: Inter-Area Routing Loop Prevention Mechanism (3)
The link between R1 and R2 and the link between R3 and R4 are disconnected, forming the non-contiguous backbone area.
R4 advertises the route to 10.0.2.2/32 to area 1 in the form of Type 3 LSA.
R5 and R6 can calculate the route to 10.0.2.2/32 based on the Type 3 LSA.
After receiving Type 3 LSAs from a non-backbone area, R3 does not calculate routes or advertise them to other areas.
In this case, R1 and R3 cannot communicate with the device at 10.0.2.2/32.
Type 3 LSAs received by an ABR from a non-backbone area cannot be used to calculate inter-area routes.
Area 0
Area 1
R3
R6
R5
R1
R2
R4
How to solve the problem of the non-contiguous backbone area?
Loopback 0
10.0.2.2/32

## Slide 46
Intra-Area Route Calculation
Inter-Area Route Calculation
  Intra-Area Route Calculation Process
  Inter-Area Routing Loop Prevention Mechanism
  Functions and Configurations of Virtual Links
External Route Calculation

## Slide 47: Functions and Configurations of Virtual Links
OSPF requires that the backbone area should be contiguous physically or logically using virtual links.
A virtual link can be established between any two ABRs, but the two ABRs must have interfaces connected to the same non-backbone area.
Area 1
R4
R2
R3
R5
R1
Area 0
Area 2
Virtual link
[R2-ospf-1]ospf 1
[R2-ospf-1]area 1
[R2-ospf-1-area-0.0.0.1]vlink-peer 10.0.3.3
[R3-ospf-1]ospf 1
[R3-ospf-1]area 1
[R3-ospf-1-area-0.0.0.1]vlink-peer 10.0.2.2
Router ID 10.0.2.2
Router ID 10.0.3.3
Notes: Note: The virtual link enables OSPF routers to communicate through a non-backbone area, which may cause routing loops in some scenarios. Therefore, you are not advised to deploy an OSPF virtual link.

## Slide 48
(TorF) A Network-summary-LSA can describe only one route.
(Essay) How does OSPF prevent inter-area routing loops?
Notes: True
An OSPF network is partitioned into the backbone area and non-backbone areas. All non-backbone areas are directly connected to the backbone area, and there is only one backbone area. Non-backbone areas communicate with each other through the backbone area. In addition, the Type 3 LSAs from the backbone area do not return to the backbone area.

## Slide 49
OSPF introduces the concept of multi-area to support larger-scale networking.
OSPF uses Type 3 LSAs to describe inter-area routing information.
To prevent inter-area routing loops, OSPF defines multiple rules.
An OSPF virtual link is a virtual and logical link deployed between two OSPF routers. It traverses a non-backbone area to connect another non-backbone area to the backbone area (area 0). The virtual link is only used in the scenario where a non-backbone area is not directly connected to area 0.

## Slide 50
Intra-Area Route Calculation
Inter-Area Route Calculation
External Route Calculation

## Slide 51: Importing External Routes
The OSPF protocol is not enabled for some links on the network.
  Routers connect to external networks using static routes or BGP routes.
  The OSPF protocol is not enabled for the link directly connected to the server.
…
…
Area N
Area 1
Area 0
Common server
1
2

## Slide 52: Basic Concepts for External Route Import
Autonomous system boundary router (ASBR): An OSPF device that imports external routes will become an ASBR, for example, R1 in the figure.
An ASBR floods external routes in AS-external-LSAs (Type 5 LSAs) on an OSPF network.
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
External route
192.168.1.0/24
ASBR
[R1]ospf 1
[R1-ospf-1]import-route …
Type 5 LSA
Notes: Run the following commands in the OSPF process view to import external routes: BGP routes, IS-IS routes, OSPF routes, direct routes, and static routes can be imported.
  import-route { limit limit-number | { bgp [ permit-ibgp ] | direct | unr | rip [ process-id-rip ] | static | isis [ process-id-isis ] | ospf [ process-id-ospf ] } [ cost cost | type type | tag tag | route-policy route-policy-name ] * }

## Slide 53: Description of AS-external LSAs
AS-external-LSA (Type 5 LSA): Originated by an ASBR, an AS-External-LSA describes routes to destinations outside an AS, and is flooded to all areas except stub areas and NSSAs.
LS Age |  |  | Options | LS Type
Link State ID |  |  |  | 
Advertising Router |  |  |  | 
LS Sequence Number |  |  |  | 
LS Checksum |  |  | length | 
Network Mask |  |  |  | 
E | 0 | Metric |  | 
Forwarding Address |  |  |  | 
External Route Tag |  |  |  | 
... |  |  |  | 
Main fields
  LS Type: The value 5 indicates an AS-external-LSA.
  Link State ID: indicates the destination network address of an external route.
  Advertising Router: indicates the router ID of the device that originates the LSA.
  Network Mask: indicates the network mask of a route.
  E: indicates the metric type used by the external route.
    0: The metric type is Metric-Type-1.
    1: The metric type is Metric-Type-2.
  Metric: indicates the cost of the route to the destination network.
  Forwarding Address (FA): Packets destined for the advertised destination address are forwarded to the address specified by this field.
Notes: Forwarding Address: When the value of this field is 0.0.0.0, traffic destined for the external network segment is sent to the ASBR that imports the external route. If the value of this field is not 0.0.0.0, traffic is sent to this forwarding address. This field is used to avoid the sub-optimal path problem in some special scenarios.
External Route Tag: indicates the external route tag and is often used to deploy routing policies.

## Slide 54: Example of an AS-external-LSA
<R1>display ospf lsdb ase self-originate
OSPF Process 1 with Router ID 10.0.1.1
Link State Database
Type : External
Ls id : 192.168.1.0
Adv rtr : 10.0.1.1
Ls age : 1340
Len : 36
Options : E
seq# : 80000004
chksum : 0xb5cc
Net mask : 255.255.255.0
TOS 0 Metric: 1
E type : 2
Forwarding Address : 0.0.0.0
Tag : 1
Priority : Low
Routing information
192.168.1.0/24
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
Server
192.168.1.0/24
[R1]ospf 1
[R1-ospf-1] import-route direct
R1 is directly connected to the server on the network segment 192.168.1.0/24. After the direct route is imported to OSPF on R1, R1 injects an AS-external-LSA that describes the route to 192.168.1.0/24 to OSPF. The AS-external-LSA is flooded in the entire OSPF area.
Router ID 10.0.1.1

## Slide 55: Route Calculation on R3
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
192.168.1.0/24
Cost 1
External routes are attached to R1.
According to the Advertising Router field in the Type 5 LSA, R3 determines that the packet needs to pass through R1 before reaching the external network.
R3 performs intra-area SPF calculation and adds R1 to the SPF tree. R3 sets the next-hop router of the route to the external network to R1.
The calculation method of R2 is similar to that of R3.
[R3]display ospf routing
Destination Cost Type NextHop AdvRouter
192.168.1.0/24 1 Type2 10.0.12.1 10.0.1.1
R3 and R1 (ASBR) are in the same area, so R3 can calculate the route to the ASBR based on the flooded Router-LSAs and Network-LSAs.
If R5 and R1 are not in the same area, how does R5 calculate external routes?
10.0.12.1

## Slide 56: Description of an ASBR-Summary-LSA
ASBR-Summary-LSA (Type 4 LSA): Originated by an ABR, an ASBR-summary-LSA describes the routes to an ASBR, and is flooded to related areas.
LS Age |  | Options | LS Type
Link State ID |  |  | 
Advertising Router |  |  | 
LS Sequence Number |  |  | 
LS Checksum |  | Length | 
Network Mask |  |  | 
0 | Metric |  | 
... |  |  | 
Main fields
  LS Type: The value 4 indicates an ASBR-summary LSA.
  Link State ID: indicates the router ID of an ASBR.
  Advertising Router: indicates the router ID of the device that originates the LSA.
  Network Mask: This parameter is reserved.
  Metric: indicates the cost of the route to the destination address.
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
R2 and R3 generate Type 4 LSAs and advertise them to area 1 and area 2 respectively.
[R1]ospf 1
[R1-ospf-1] import-route direct
Type 4 LSA
Type 5 LSA

## Slide 57: Example of an ASBR-Summary LSA
<R3>display ospf lsdb asbr self-originate
Area: 0.0.0.2
Link State Database
Type : Sum-Asbr
Ls id : 10.0.1.1
Adv rtr : 10.0.3.3
Ls age : 15
Len : 28
Options : E
seq# : 80000005
chksum : 0xf456
Tos 0 metric: 1
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
[R1]ospf 1
[R1-ospf-1] import-route direct
Router ID of the ASBR
Cost of the route from R3 to the ASBR
Router ID 10.0.1.1
The following uses the ASBR-summary LSA advertised by R3 to area 2 as an example.
Cost = 1

## Slide 58: Route Calculation on R5
[R5]display ospf routing
Destination Cost Type NextHop AdvRouter
192.168.1.0/24 1 Type2 10.0.34.3 10.0.1.1
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
External routes are attached to R1.
R5 determines that the Type 5 LSA is generated by R1 according to the Advertising Router field in the Type 5 LSA. However, R1 does not exist in the SPF tree of R5.
Based on the Type 4 LSAs generated by R3, R5 sets the next hop of the route to the external network to R3.
Route calculation on R4 is similar to that on R5.
On the physical network, the costs of the routes from R3 and R5 to the external network are different, but cannot be represented in the routing table.
[R3]display ospf routing
Destination Cost Type NextHop AdvRouter
192.168.1.0/24 1 Type2 10.0.12.1 10.0.1.1
192.168.1.0/24
Note: The cost of all device interfaces is 1.

## Slide 59: Distinguishing Two Types of OSPF External Routes (1)
Metric-Type-1
  When the cost of an external route equals that of an AS internal route and can be compared with the cost of an OSPF route, the external route has high reliability and can be configured as a Metric-Type-1 external route.
  The cost of a Metric-Type-1 external route equals that of a link between a router and its ASBR plus the cost of the link between the ASBR and the destination.
Metric-Type-2
  When the cost of the route from an ASBR to the destination outside an AS is much greater than the cost of the internal route to the ASBR, the external route has low reliability and can be configured as a Metric-Type-2 external route.
  Metric-Type-2 external routes have the same cost as AS external routes.
OSPF
Outside the OSPF area
192.168.1.0/24
Type 5 LSA
Route to 192.168.1.0/24
Cost of the link between the ASBR and the destination
ASBR
Cost of a link between a router and its ASBR

## Slide 60: Distinguishing Two Types of OSPF External Routes (2)
[R3]display ospf routing
Destination Cost Type Tag NextHop AdvRouter
192.168.1.0/24 2 Type1 1 10.0.12.1 10.0.1.1
[R5]display ospf routing
Destination Cost Type Tag NextHop AdvRouter
192.168.1.0/24 3 Type1 1 10.0.34.3 10.0.1.1
Area 0
R4
R2
R3
R5
R1
Area 1
Area 2
Server
192.168.1.0/24
[R1]ospf 1
[R1-ospf-1]import-route direct type 1 cost 1
Imported Metric-Type-1 external route
Type | Description | Cost
Metric-Type-1 | High reliability. | Cost of the AS internal route + Cost of the AS external route
Metric-Type-2 (default) | Low reliability. The cost of the AS external route is much greater than the cost of the AS internal route. | Cost of the AS external route
The cost of the external route is 1.
Cost = 1
Cost = 1
The external route type is Metric-Type-1. In the routing table of R3, the cost of the route to 192.168.1.0/24 is the cost of the external route plus the cost of the internal route from R3 to R1 (ASBR).
The cost of the route to 192.168.1.0/24 in the routing table of R5 is equal to the cost of the external route plus the cost of the internal route from R5 to R1 (ASBR).

## Slide 61
(Multiple) Which of the following types of LSAs may be originated by an ABR?( )
  ASBR-summary-LSA
  AS-external-LSA
  Router-LSA
  Network-summary-LSA
(Single) Which of the following routes has the highest priority for the same route prefix?( )
  Intra-area route
  Inter-area route
  Type 1 external route
  Type 2 external route
Notes: ABCD
A

## Slide 62
On a large-scale network, there may be multiple routing protocols. OSPF can import AS external routes to the local AS so that routers in the AS can learn the routes to other ASs.
After an ASBR imports external routes into OSPF, the ASBR uses Type 5 LSAs to describe these routes. Routers in the same area as the ASBR can calculate external routes based on Type 5 LSAs as well as Type 1 and Type 2 LSAs in the area. Routers that are not in the same area as the ASBR need to use Type 4 LSAs to calculate external routes.
After OSPF imports external routes, you can set the metric type of the routes to Metric-Type-1 or Metric-Type-2. The cost calculation methods and priorities of external routes with different metric types are different, Metric-Type-1 routes have a higher priority than Metric-Type-2 routes.

## Slide 63
This course describes calculation of OSPF intra-area routes, inter-area routes, and external routes.
Intra-area routes, inter-area routes, Metric-Type-1 external routes, and Metric-Type-2 external routes are in descending order of priority.
LSAs carry OSPF link state information. As the network scale expands, network services become complex. As OSPF areas are partitioned and a large number of external routes are imported, the LSDB of a router may contain a large number of Type 1, Type 2, Type 3, Type 4, and Type 5 LSAs, which may cause the device performance to deteriorate.
What technical means does OSPF use to prevent the device performance from deteriorating while ensuring network reachability?