## Slide 1
V5R2
V1R1
He Junjian HWX580230
2019-11-11
New

## Slide 2: OSPF Special Areas and Other Features

## Slide 3
On a large-scale network, an Open Shortest Path First (OSPF) router needs to maintain the database composed of intra-area, inter-area, and external routes. As the network scale expands, the link state database (LSDB) size also increases. If an area does not need to provide traffic forwarding services for other areas, routers in this area do not need to maintain link status information outside the area.
By partitioning areas, OSPF can reduce the LSDB size of routers in an area. Low-end routers in non-backbone areas at the border of an Autonomous System (AS) cannot accommodate the LSDB. OSPF special areas can further reduce the number of Link State Advertisements (LSAs) and the size of the routing table.
This course describes OSPF special areas and OSPF-related features.

## Slide 4
Upon completion of this course, you will be able to:
  Describe types and characteristics of OSPF special areas.
  Describe application scenarios and advantages of OSPF route summarization.
  Configure OSPF packet authentication.

## Slide 5
Stub Area and Totally Stub Area
NSSA and Totally NSSA
Summarization of Inter-Area and External Routes
OSPF Features

## Slide 6: Problems Caused by the Increase of the Network Scale
OSPF routers calculate intra-area, inter-area, and external routes based on LSAs on a network. When the network scale increases, the LSDB size of the device also increases, which makes route calculation more difficult and lowers device performance.
LSDB of R5
Type 1 and Type 2 LSAs
Type 3 LSA
Type 4 LSA
Type 5 LSA
How to reduce the number of LSAs without affecting IP reachability?
…
…
Area N
Area 1
Area 0
Common server
1
2
Area 0
R4
R2
R3
R5
R1
R4
R2
R1
R3
R5
Area 1
Area 2
External route

## Slide 7: Transit Area and Stub Area
OSPF areas are classified into the following types:
  Transit area: carries traffic originated from and destined for the local area as well as traffic whose source and destination IP addresses do not belong to the local area, for example, traffic in area 0.
  Stub area: carries only the traffic initiated by and destined for the local area, for example, traffic in areas 1 and 2.
External route
Area 0
Area 1
Area 2
R4
R2
R3
R5
R1
Stub area
Transit area
Stub area

## Slide 8: Stub Area
The Area Border Router (ABR) in a stub area does not advertise the received AS external routes to the stub area, which significantly decreases the LSDB and routing table sizes of routers in the stub area.
To ensure the reachability of AS external routes, the ABR generates a default route (carried by Type 3 LSAs) and advertises the route to non-ABRs in the stub area.
Note the following when configuring a stub area:
  A backbone area cannot be configured as a stub area.
  Stub area attributes need to be configured on all the routers in the area that needs to be configured as a stub area.
  AS external routes cannot be imported or received within a stub area.
  A virtual link cannot pass through a stub area.
LSDB of R5
Type 1 and Type 2 LSAs
Type 3 LSA
Type 4 LSA
Type 5 LSA
Common Area
Stub Area
LSDB of R5
Type 1 and Type 2 LSAs
Type 3 LSA
*Type 3 LSA
Area 0
Area 1
Area 2
Stub
R4
R2
R3
R5
R1
External route
*Default route advertised by the ABR

## Slide 9: Routing Table of the Stub Area and Type 3 LSAs
R1 functions as an ASBR to import multiple external network segments. If area 2 is a common area, R3 imports Type 5 and Type 4 LSAs to this area.
After area 2 is configured as a stub area:
  R3 does not inject Type 5 and Type 4 LSAs into area 2.
  R3 sends a Type 3 LSA carrying the default route to area 2. Although routers in area 2 do not know the specific route to the AS external network, they can still reach the AS external network through the default route.
Area 0
Area 1
Area 2
Stub
R4
R2
R3
R5
R1
192.168.1.0/24
...
<R5>display ospf routing
OSPF Process 1 with Router ID 10.0.5.5
Routing Tables
Routing for Network
Destination Cost Type NextHop AdvRouter Area
10.0.35.0/24 1 Transit 10.0.35.5 10.0.5.5 0.0.0.2
0.0.0.0/0 2 Inter-area 10.0.35.3 10.0.3.3 0.0.0.2
10.0.12.0/24 3 Inter-area 10.0.35.3 10.0.3.3 0.0.0.2
10.0.13.0/24 2 Inter-area 10.0.35.3 10.0.3.3 0.0.0.2
10.0.24.0/24 4 Inter-area 10.0.35.3 10.0.3.3 0.0.0.2
ospf 1
area 0.0.0.2
stub
#
<R5>display ospf lsdb
OSPF Process 1 with Router ID 10.0.5.5
Link State Database
Area: 0.0.0.2
Type LinkState ID AdvRouter Metric
Sum-Net 0.0.0.0 10.0.3.3 1
Sum-Net 10.0.13.0 10.0.3.3 1
Sum-Net 10.0.24.0 10.0.3.3 3
Sum-Net 10.0.12.0 10.0.3.3 2
Type 4 and Type 5 LSAs do not exist, but Type 3 LSAs that carrying inter-area routes still exist.
10.0.13.0/24
10.0.24.0/24
10.0.12.0/24

## Slide 10: Totally Stub Area (1)
A totally stub area does not allow AS external routes or inter-area routes to be advertised within the area.
Other routers except the ABR in a totally stub area use default routes (carried by Type 3 LSAs) delivered by the ABR to each other areas and AS external network.
When configuring a totally stub area, pay attention to the following points:
  The difference between the stub area and the totally stub area is that no-summary is specified on the ABR for the totally stub area.
Area 0
Area 1
Area 2
Totally stub
R4
R2
R3
R5
R1
External route
ospf 1
area 0.0.0.2
stub no-summary
LSDB of R5
Type 1 and Type 2 LSAs
Type 3 LSA
Type 4 LSA
Type 5 LSA
Common Area
Totally Stub Area
LSDB of R5
Type 1 and Type 2 LSAs
*Type 3 LSA
* Default route advertised by the ABR
Notes: Question: Why is the no-summary parameter not required for non-ABR devices?

## Slide 11: Totally Stub Area (2)
The totally stub area accesses other areas and AS external networks through default routes.
The topology and route changes outside an AS or in other OSPF areas do not cause routers in the totally stub area to recalculate routes. This prevents device performance from deteriorating.
<R5>display ospf lsdb
OSPF Process 1 with Router ID 10.0.5.5
Link State Database
Area: 0.0.0.2
Type LinkState ID AdvRouter Metric
Sum-Net 0.0.0.0 10.0.3.3 1
The stub area and totally stub area solve the problem of maintaining a large LSDB in the end area. In certain scenarios, they are not the best solutions.
Area 0
Area 1
R4
R2
R3
R5
R1
192.168.1.0/24
...
ospf 1
area 0.0.0.2
stub no-summary
10.0.13.0/24
10.0.24.0/24
10.0.12.0/24
Area 2
Totally stub
After area 2 is configured as a totally stub area:
R3 does not inject Type 5 and Type 4 LSAs into area 2.
R3 does not inject Type 3 LSAs into area 2, but injects a default route carried by Type 3 LSAs into area 2.
R5 uses the default route to reach the AS external network and other OSPF areas.

## Slide 12
Stub Area and Totally Stub Area
NSSA and Totally NSSA
Summarization of Inter-Area and External Routes
OSPF Features

## Slide 13: Problems in the Stub Area and Totally Stub Area
As defined in OSPF, the stub area cannot import external routes. This mechanism prevents a large number of external routes from consuming resources of devices in the stub area.
Stub and totally stub areas cannot apply to the scenario where external routes need to be imported and resource consumption caused by external routes also needs to be avoided.
R5 needs to import external routes.
Area 0
Area 1
Area 2
Stub
R4
R2
R3
R5
R1
External route
Common server
192.168.3.0/24
New server
1
2

## Slide 14: NSSA and Totally NSSA
An NSSA can import external routes but cannot learn external routes imported from other areas on the OSPF network.
The difference between the totally NSSA and NSSA is that no-summary is specified on the ABR for the totally NSSA.
Area 0
Area 1
Area 2
NSSA
R4
R2
R3
R5
R1
Common server
192.168.3.0/24
Type 7 LSA (default route)
Type 5 LSA
Type 4 LSA
Type 5 LSA
Type 4 LSA
Type 7 LSA
Type 7 LSA converted into Type 5 LSA
Type 7 LSA
R5 imports the external route 192.168.3.0/24 to OSPF.
Notes: An NSSA can import external routes but cannot learn external routes from other areas on the OSPF network.
  Type 7 LSAs are generated by an Autonomous System Boundary Router (ASBR) in an NSSA and advertised only within the NSSA. After an ASBR in an NSSA imports external routes to the NSSA, the ASBR generate Type 7 LSAs to carry information about the external routes.
  The Type 7 LSAs are advertised only within the NSSA.
  When Type 7 LSAs reach an ABR in the NSSA, the ABR translates the Type 7 LSAs into Type 5 LSAs, imports them to the backbone area, and floods them to the entire AS.
  The ABR in an NSSA prevents external routes imported from other areas from being imported into the NSSA. That is, Type 4 and Type 5 LSAs do not exist in the NSSA. To enable routers in the NSSA to reach the AS external network through the backbone area, the ABR in the NSSA automatically injects a default route carried by a Type 7 LAS into the NSSA.

## Slide 15: LSDBs of the NSSA and Totally NSSA
<R5>display ospf lsdb
OSPF Process 1 with Router ID 10.0.5.5 Area: 0.0.0.2
<R5>display ospf lsdb
OSPF Process 1 with Router ID 10.0.5.5 Area: 0.0.0.2
Area 0
Area 1
Area 2
NSSA
R4
R2
R3
R5
R1
192.168.3.0/24
ospf 1
area 0.0.0.2
nssa
Area 0
Area 1
Area 2
Totally NSSA
R4
R2
R3
R5
R1
ospf 1
area 0.0.0.2
nssa no-summary
192.168.3.0/24
Type | LinkStateID | AdvRouter | Metric
NSSA | 192.168.3.0 | 10.0.5.5 | 1
NSSA | 0.0.0.0 | 10.0.3.3 | 1
Sum-Net | 10.0.13.0 | 10.0.3.3 | 1
Sum-Net | 10.0.24.0 | 10.0.3.3 | 3
Type | LinkStateID | AdvRouter | Metric
Sum-Net | 0.0.0.0 | 10.0.3.3 | 1
NSSA | 192.168.3.0 | 10.0.5.5 | 1
NSSA | 0.0.0.0 | 10.0.3.3 | 1
Notes: Scenario 1 (area 2 is configured as an NSSA): When R5 imports external route 192.168.3.0/24 to the NSSA, R5 functions as an ASBR to generate Type 7 LSAs and flood them in area 2. R3 generates a default route that is carried by a Type 7 LSA and imports the route to area 2. The routers in area 2 still receive the Type 3 LSAs imported by R3 and calculate the inter-area routes to other areas.
Scenario 2 (area 2 is configured as a totally NSSA): A totally NSSA is similar to an NSSA. The difference is that the ABR in a totally NSSA prevents Type 3 LSAs from entering the totally NSSA. In this scenario, R3 does not inject inter-area routes into area 2. Therefore, in the LSDB of R5, there is only one Type 3 LSA that carries the default route.

## Slide 16: OSPF LSA Review
Type | Name | Description
1 | Router-LSA | Every router on an OSPF network generates Router-LSAs. A Router-LSA describes a router's link state and cost and can be flooded only in the area that the interface belongs to.
2 | Network-LSA | A DR generates Network-LSAs. A Network-LSA describes all the routers that establish adjacencies with the DR on the MA network to which the DR is connected and the DR itself. The LSA can be flooded only in the area to which the interface belongs.
3 | Network-summary-LSA | An ABR generates Network-summary-LSAs. A Network-summary-LSA describes the route to the destination network segment of an area. It is used to transmit inter-area routes.
4 | ASBR-summary-LSA | An ABR generates ASBR-summary-LSAs. An ASBR-Summary-LSA describes routes to an ASBR, and is equivalent to a host route to an ASBR.
5 | AS-external-LSA | An ASBR generates AS-external-LSAs. An AS-external-LSA describes routes to destinations outside an AS.
7 | NSSA LSA | An ASBR generates NSSA LSAs. An NSSA LSA describes routes to destinations outside an AS. NSSA LSAs have similar functions as AS-external-LSAs, but are flooded in different areas. NSSA LSAs can be flooded only in the NSSA and cannot enter area 0. The ABR in the NSSA converts Type 7 LSAs into Type 5 LSAs and injects them into area 0.
  The use of special areas reduces the LSDB size on the device, thus preventing device performance from deteriorating and minimizing the impact of network faults.
  How to reduce LSA flooding and LSDB size in a common area to optimize the OSPF network while ensuring IP reachability?

## Slide 17: LSA Processing on a Router
OSPF synchronizes LSDBs by exchanging LSAs. After receiving LSAs, a router processes the LSAs according to the following principles:
  If the received LSA does not exist in the local LSDB, the router updates the LSDB and floods the LSA.
  If the LSA already exists in the local LSDB but an update is received, the router updates the LSDB and floods the LSA.
  If the received LSA is the same as that in the LSDB, the router ignores the LSA and does not flood it.
  If the received LSA is damaged, for example, the checksum is incorrect, the router does not accept it.
Receive multiple instances of an LSA
Is the sequence number the same?
Is the checksum the same?
Max Age=3600s
The received LAS is better
Yes
Yes
No
A larger sequence number is preferred.
No
A larger checksum is preferred.
No
A smaller Max Age value is preferred
The received LSAs are considered the same and the LSA that is received first is reserved
No
No
Yes
Yes
Does the
difference between Max Age values exceed 15
minutes?

## Slide 18
Stub Area and Totally Stub Area
NSSA and Totally NSSA
Summarization of Inter-Area and External Routes
OSPF Features

## Slide 19: Route Summarization on an ABR
Route summarization indicates that a group of routes with the same prefix is summarized into one route to reduce the size of the routing table and optimize the usage of device resources. The routes before summarization are called refined or specific routes, the route summarized by the group of routes is called summarized route.
OSPF route summarization:
  Route summarization on an ABR: Inter-area routes are summarized.
  Route summarization on an ASBR: Imported external routes are summarized.
Area 0
Area 1
R4
R2
R3
R1
172.16.0.0/24
172.16.1.0/24
172.16.2.0/24
…
172.16.7.0/24
[R2]ospf
[R2-ospf-1]area 1
[R2-ospf-1-area-0.0.0.1]abr-summary 172.16.0.0 255.255.248.0
<R2>display ospf lsdb
area 0
Type LinkState ID AdvRouter
Sum-Net 172.16.0.0 10.0.2.2
<R2>display ospf lsdb
area 0
Type LinkState ID AdvRouter
Sum-Net 172.16.0.0 10.0.2.2
Sum-Net 172.16.1.0 10.0.2.2
Sum-Net 172.16.2.0 10.0.2.2
Sum-Net 172.16.3.0 10.0.2.2
Sum-Net 172.16.4.0 10.0.2.2
Sum-Net 172.16.5.0 10.0.2.2
Sum-Net 172.16.6.0 10.0.2.2
Sum-Net 172.16.7.0 10.0.2.2
After route summarization, R2 (ABR) advertises only the summarized route 172.16.0.0/21 to area 0.
If the network segment corresponding to a specific route flaps (Up/Down), the impact of the topology change is limited to area 1.
Before route summarization
After route summarization

## Slide 20: Route Summarization on an ASBR
After route summarization is configured on an ASBR, the ASBR summarizes the external routes imported by itself.
An ASBR in an NSSA can also summarize the external routes imported into the NSSA.
In an NSSA, the ABR translates Type 7 LSAs to Type 5 LSAs. In this case, the ABR is also an ASBR. If route summarization is configured, the ABR summarizes Type 5 LSAs converted from Type 7 LSAs.
<R3>display ospf lsdb
OSPF Process 1 with Router ID 10.0.3.3
Area: 0.0.0.2
Area: 0.0.0.0
Type | LinkStateID | AdvRouter
NSSA | 0.0.0.0 | 10.0.3.3
NSSA | 172.19.0.0 | 10.0.3.3
NSSA | 172.18.0.0 | 10.0.5.5
Type | LinkState ID | AdvRouter
External | 172.19.0.0 | 10.0.3.3
External | 172.18.0.0 | 10.0.3.3
External | 172.17.0.0 | 10.0.1.1
Area 0
Area 1
R4
R2
R3
R1
172.17.0.0/24
172.17.1.0/24
172.17.2.0/24
172.17.7.0/24
R5
172.18.0.0/24
172.18.1.0/24
172.18.7.0/24
Area 2
NSSA
ospf 1
asbr-summary 172.18.0.0 255.255.248.0
ospf 1
asbr-summary 172.19.0.0 255.255.248.0
172.19.0.0/24
172.19.1.0/24
172.19.7.0/24
ospf 1
asbr-summary 172.17.0.0 255.255.248.0
Notes: R1, R3, and R5 summarize the imported external routes.

## Slide 21
Stub Area and Totally Stub Area
NSSA and Totally NSSA
Summarization of Inter-Area and External Routes
OSPF Features

## Slide 22: Silent Interface
This can enhance the networking adaptability of OSPF and reduce system resource consumption.
A silent interface has the following features:
  A silent interface does not receive or send OSPF packets.
  Direct routes of a silent interface can still be advertised.
<R1>display ospf interface GigabitEthernet 0/0/1
OSPF Process 1 with Router ID 10.0.1.1
Interface: 10.0.13.1 (GigabitEthernet0/0/1)
Cost: 1 State: Waiting Type: Broadcast MTU: 1500
Priority: 1
Designated Router: 0.0.0.0
Backup Designated Router: 0.0.0.0
Timers: Hello 10 , Dead 40 , Poll 120 , Retransmit 5 , Transmit Delay 1
Silent interface, No hellos
Area 0
R2
R1
Server
GE 0/0/1
192.168.4.0/24
[R1]ospf
[R1-ospf-1]area 0
[R1-ospf-1-area-0.0.0.0]network 192.168.4.0 0.0.0.255
[R1-ospf-1]silent-interface GigabitEthernet 0/0/1
GE0/0/1 of R1 is on the network segment configured using the network command.
The route to the interface is advertised to OSPF so that other devices can access the server.
The interface is not connected to any other OSPF router, so the administrator configures the interface as a silent interface. The interface does not send or receive Hello packets, which prevents the performance of the server from deteriorating.

## Slide 23: OSPF Packet Authentication
OSPF supports packet authentication. Only the OSPF packets that pass the authentication can be received.
The router supports two OSPF packet authentication modes. When both modes are available, the interface authentication mode is preferred.
  Area authentication: The authentication mode and password on all routers in the same area must be the same.
  Interface authentication: The authentication mode and password of the interfaces directly connected to neighboring routers must be the same.
[R2]ospf
[R2-ospf-1]area 0
[R2-ospf-1-area-0.0.0.0]authentication-mode simple cipher Huawei
Area 1
R3
R2
R1
Area 0
[R2]interface GigabitEthernet 0/0/1
[R2-GigabitEthernet0/0/1]ospf authentication-mode md5 1 cipher Huawei
Configure an authentication mode on GE0/0/1 of R2.
Enable area authentication in area 0 on R2.
In this example, interface authentication and area authentication are configured on R2. To establish an OSPF neighbor relationship, you also need to configure interface authentication and area authentication on R3 and R1.
Notes: In the OSPF area view, configure an authentication mode for the OSPF area.
  Run authentication-mode simple [ plain plain-text | [ cipher ] cipher-text ] to configure an authentication mode for the OSPF area.
    plain: plain-text password
    cipher: cipher-text password For MD5 or HMAC-MD5 authentication, the cipher-text mode is used by default.
Configure an authentication mode on an interface.
  Run ospf authentication-mode simple [ plain plain-text | [ cipher ] cipher-text ] to configure an authentication mode on an OSPF interface.

## Slide 24
(Multiple) Which of the following special areas are defined by OSPF?
  Stub Area
  Totally Stub Area
  Not-So-Stubby Area (NSSA)
  Totally NSSA
(Essay) What is the difference between a stub area and a totally stub area?
(Essay) Which router is configured with the inter-area route summarization function?
Notes: ABCD
A stub area does not allow Type 4 and Type 5 LSAs, but allows Type 3 LSAs. A totally stub area does not allow Type 4 and Type 5 LSAs or Type 3 LSAs. It allows only Type 3 LSAs that carry default routes.
It is configured on the ABR.

## Slide 25
This chapter describes OSPF special areas. Routers in the stub area reach the external network through the default route. Routers in the totally stub area reach the external network and the OSPF inter-area network through the default route. The routers in the NSSA and totally NSSA can import external routes.
This chapter also describes OSPF features, including the silent interface, authentication, and processing mode when an OSPF router receives LSAs.