## Slide 1
He Junjian/hwx580230
2019-11-11
New

## Slide 2: IS-IS Implementation and Configuration

## Slide 3
Intermediate System-to-Intermediate System (IS-IS) is a dynamic routing protocol initially designed by the International Organization for Standardization (ISO) for its Connectionless Network Protocol (CLNP).
To support IP routing, the Internet Engineering Task Force (IETF) extended and modified IS-IS in RFC 1195. This modification enables IS-IS to apply to TCP/IP and OSI environments. This type of IS-IS is called Integrated IS-IS. IS-IS stated in this course refers to Integrated IS-IS, unless otherwise stated.
This course describes the basic concepts, working mechanism, and configuration methods of IS-IS.

## Slide 4
Upon completion of this course, you will be able to:
  Describe basic concepts of IS-IS.
  Understand how IS-IS is implemented.
  Describe the differences between IS-IS and OSPF.
  Perform basic IS-IS configurations

## Slide 5
Basic Concepts of IS-IS
Working Mechanism of IS-IS
Basic IS-IS Configurations

## Slide 6: Overview of IS-IS
IS-IS is a part of the connectionless network service (CLNS) in the OSI protocol stack defined by the ISO.
OSPF has the following characteristics:
  OSPF applies to only the IP network.
  OSPF packets are encapsulated in IP packets.
Application layer
Presentation layer
Session layer
Transport layer
Network layer
Data link layer
Physical layer
OSI
Application layer
Transport layer
Network layer
Data link layer
Physical layer
TCP/IP
CLNP
IP
Does CLNP
also use an IP address?
ES-IS
IS-IS
OSPF
IS-IS has the following characteristics:
  IS-IS applies to CLNP and IP networks.
  IS-IS packets are encapsulated in frames at the data link layer.
Notes: IS-IS is a link-state routing protocol. IS-IS is similar to OSPF in many aspects. For example, directly connected devices running IS-IS discover each other by sending Hello packets, establish adjacencies, and exchange link-state information.
A NET includes the following elements:
  CLNP: is similar to the IP protocol in TCP/IP.
  IS-IS: is similar to OSPF in TCP/IP.
  ES-IS: is similar to ARP or ICMP in TCP/IP.
End system (ES): is similar to a host on the IP network.
ES-IS: End System to Intermediate System
CLNP and ES-IS are not involved on the IP network, so they are not described in this course.

## Slide 7: NSAP
The network service access point (NSAP) is an address defined by the OSI to locate resources. It provides interfaces between the network layer and upper-layer applications. The NSAP is composed of the initial domain part (IDP) and the domain specific part (DSP).
High Order DSP
System ID
SEL
IDI
AFI
1-13 bytes
6 bytes
1 byte
NSAP
IDP
DSP
The IDP is similar to the network ID in an IP address. It is defined by the ISO and consists of the authority and format identifier (AFI) and the initial domain identifier (IDI). The AFI indicates the address allocation authority and address format, and the IDI identifies a domain.
The DSP is similar to the subnet ID and host address in an IP address. The DSP consists of the High Order DSP (HODSP), system ID, and NSAP Selector (SEL). The HODSP is used to divide areas, the system ID identifies a host, and the SEL indicates the service type.
Address Structure
Topology
Packet Type

## Slide 8: NET
A network entity title (NET) indicates the network layer information of an IS and consists of an area ID and a system ID. It is used for route calculation. A NET can be considered as a special NSAP (the NSAP whose SEL is 00).
The length of the NET field is the same as that of an NSAP. Its maximum length is 20 bytes and its minimum length is 8 bytes.
When IS-IS runs on an IP network, you only need to configure NETs. Devices can obtain area IDs and system IDs based on NETs.
Example of a NET: 49.0001.0000.0000.0001.00
Area ID System ID SEL
High Order DSP
System ID
SEL
IDI
AFI
1-13 bytes
6 bytes
1 byte
49.0001
0000.0000.0001
00
Is the topology different because the area ID is different from that of OSPF?
Address Structure
Topology
Packet Type
Notes: An area ID consists of the IDP and HODSP in the DSP. It can identify a routing domain and an area in the routing domain. Therefore, they are called an area address, which is equivalent to the area number in OSPF.
  In most cases, a router can be configured with only one area address. The area address of all nodes in an area must be the same. To support seamless combination, division, and transformation of areas, a device can be configured with a maximum of three area addresses in an IS-IS process by default.
A system ID uniquely identifies a host or a router in an area. The fixed length of the system ID on the device is 6 bytes.

## Slide 9: Example of a NET
Each network device running IS-IS must have at least one NET. A device can be configured with multiple NETs, but the system IDs of these NETs must be the same.
On Huawei network devices, the length of the system ID is always 6 bytes. In an IS-IS routing domain, the system ID of a device must be unique. To facilitate management, configure the system ID based on the router ID.
10.0.1.1
010.000.001.001
0100.0000.1001
For example, if the area ID of a device is 49.0001 and the router ID is 10.0.1.1, the NET of the device is 49.0001.0100.0000.1001.00.
Each part is extended to 3 digits
Re-divide three parts
49.0001.0100.0000.1001.00
System ID
Router ID
Add area ID + SEL
NET
Address Structure
Topology
Packet Type

## Slide 10: Differences Between Area Division of IS-IS and OSPF
L1: Level-1
L1/2: Level-1-2
L2: Level-2
L1/2
L1/2
L1
L1
L2
L2
L1/2
L1/2
Area 49.0002
Area 49.0003
L2
L2
Area 49.0001
Area 0
Area 2
Area 1
OSPF
IS-IS
Backbone
area
IS-IS uses a two-level hierarchy in an AS: backbone area and non-backbone area.
  Level-1 routers are deployed in non-backbone areas.
  Level-2 and Level-1-2 routers are deployed in the backbone area.
Each non-backbone area connects to the backbone area through a Level-1-2 router.
In the figure, the backbone area contains all the routers in area 49.002 and Level-1-2 routers in other areas.
Area 0 is the backbone area.
Address Structure
Topology
Packet Type
Notes: During the learning of OSPF, we have learned the advantages of multi-area and hierarchical network design. For a link-state routing protocol, a device running the protocol advertises link state information to the network, collects and stores the flooded link-state information, and performs calculation based on the information to obtain routing information. If the multi-area deployment mode is not used, more and more link state information will be flooded on the network as the network scale increases. All devices on the network will bear heavier burdens, and route convergence will become slower. This also results in low network scalability.
The two types of topologies show the differences between IS-IS and OSPF:
  In IS-IS, each router belongs to only one area. In OSPF, different interfaces of a router may belong to different areas.
  In IS-IS, no area is defined as the backbone area. In OSPF, area 0 is defined as the backbone area.
  In IS-IS, Level-1 and Level-2 routes are calculated using the SPF algorithm to generate the shortest path tree (SPT). In OSPF, the SPF algorithm is used only in the same area, and inter-area routes are forwarded by the backbone area.

## Slide 11: IS-IS Router Types (1)
Level-1 router
  A Level-1 router (for example, R1 in the figure) is an internal router in an IS-IS area. It establishes Level-1 neighbor relationships with only Level-1 and Level-1-2 routers in the same area. A Level-1 router cannot establish the neighbor relationship with a Level-2 router.
  A Level-1 router maintains only the Level-1 LSDB, which contains only the routing information of the local area. The Level-1 router must access the IS-IS backbone area through a Level-1-2 router to access other areas.
Level-1 neighbor relationship
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
R6 (L2)
R7 (L2)
Address Structure
Topology
Packet Type

## Slide 12: IS-IS Router Types (2)
Level-2 router
  Level-2 routers (such as R4, R5, R6, and R7 in the figure) are IS-IS backbone routers. They can establish neighbor relationships with Level-2 routers or Level-1-2 routers in the same area or different areas. A Level-2 router maintains a Level-2 LSDB that contains all routing information of the IS-IS domain.
  All Level-2 routers form the backbone network of the routing domain. They establish Level-2 neighbor relationships and are responsible for inter-area communication. Level-2 routers in the routing domain must be physically contiguous to ensure the continuity of the backbone network.
Level-2 neighbor relationship
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
R6 (L2)
R7 (L2)
Address Structure
Topology
Packet Type

## Slide 13: IS-IS Router Types (3)
Level-1-2 router
  Similar to an ABR in OSPF, a Level-1-2 router is also a part of the IS-IS backbone network.
  A Level-1-2 router maintains two LSDBs: a Level-1 LSDB and a Level-2 LSDB. The Level-1 LSDB saves for intra-area routing and the Level-2 LSDB saves for inter-area routing.
  A router that belongs to both a Level-1 area and a Level-2 area is called a Level-1-2 router (for example, R2 and R3). It can establish Level-1 neighbor relationships with Level-1 and Level-1-2 routers in the same area. It can also establish Level-2 neighbor relationships with Level-2 and Level-1-2 routers in different areas.
Level-2 neighbor relationship
Level-1 neighbor relationship
R1 (L1)
R3(L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
R6 (L2)
R7 (L2)
Address Structure
Topology
Packet Type
Notes: When IS-IS is configured on a Huawei router, the router type is Level-1-2 by default. You can run commands to change the router type.

## Slide 14: Network Types Supported by IS-IS
IS-IS automatically determines the default network type of an interface based on the data link layer encapsulation type of the interface. IS-IS supports the following network types:
  Broadcast: such as Ethernet.
  Point-to-point (P2P): such as PPP and HDLC
Broadcast
GE 0/0/0
P2P
Serial 1/0/0
Address Structure
Topology
Packet Type
Notes: For a Non-Broadcast Multi-Access (NBMA) network, you should configure its sub-interfaces as P2P interfaces.

## Slide 15: IS-IS Cost
IS-IS uses the cost as the route metric. A smaller cost indicates a better path. The cost of an IS-IS link is related to an interface of the device. Similar to OSPF, each IS-IS-enabled interface maintains the interface cost. Unlike OSPF, the cost of an IS-IS-enabled interface is not related to the interface bandwidth by default. In actual deployment, IS-IS can adjust the cost based on the interface bandwidth. The default cost is 10 regardless of the interface bandwidth.
The cost of an IS-IS path is the sum of the costs of all links from the local router to the destination network segment.
The costs of IS-IS interfaces can be determined in the following modes (in descending order of priority):
  Interface cost: configured for a specified interface.
  Global cost: configured for all interfaces.
  Automatically calculated cost: automatically calculated based on the interface bandwidth.
Cost = 10
Cost = 10
10.0.1.1/32
Cost = 0
R1
R2
R3
GE0/0/0
GE0/0/0
49.0001
As shown in the figure, IS-IS runs on the entire network. The cost of the route from R3 to 10.0.1.1/32 is 20 (10 + 10 + 0).
Address Structure
Topology
Packet Type
Notes: In ISO 10589, the maximum metric value of an IS-IS interface can only be 63 and the IS-IS cost type is narrow. A small range of metrics cannot meet the requirements on large-scale networks. As defined in RFC 3784, the cost of an IS-IS interface can be extended to 16777215. In this case, the IS-IS cost type is wide.
By default, the cost type of Huawei routers is narrow.
The following lists the TLVs used in narrow mode:
  TLV 128 (IP Internal Reachability TLV): carries IS-IS routes in a routing domain.
  TLV 130 (IP External Reachability TLV): carries IS-IS routes outside a routing domain.
  TLV 2 (IS Neighbors TLV): carries neighbor information.
The following lists the TLVs used in wide mode:
  TLV 135 (Extended IP Reachability TLV): replaces the earlier IP reachability TLV and carries IS-IS routing information. This TLV expands the route metric and carries sub-TLVs.
  TLV 22 (IS Extended Neighbors TLV): carries neighbor information.

## Slide 16: IS-IS Packet Format
IS-IS packets are encapsulated in frames at the data link layer.
A protocol data unit (PDU) consists of an IS-IS header and variable length fields.
The IS-IS header can be further classified into the common header and specific header. For all PDUs, the common headers are the same, but the dedicated headers vary according to the PDU type.
Payload
Variable Length Fields (TLV)
IS-IS Header
Data Link Header
PDU Specific Header
PDU Common Header
Type |  |  | 
Length |  |  | 
Value |  |  | 
Intradomain Routing Protocol Discriminator |  |  | 
PDU Header Length |  |  | 
Version/Protocol ID Extension |  |  | 
System ID Length |  |  | 
R | R | R | PDU type (5 bits)
Version |  |  | 
Reserved |  |  | 
Max.Areas |  |  | 
Address Structure
Topology
Packet Type

## Slide 17: Description of the PDU Common Header
Common header
Main fields:
  Intradomain Routing Protocol Discriminator: The fixed value is 0x83.
  Length Indicator: indicates the length of the IS-IS header (including the common header and dedicated header), in bytes.
  Version/Protocol ID Extension: The fixed value is 0x01.
  System ID Length: indicates the length of the system ID in the NSAP or NET. If it is set to 0, the system ID has 6 bytes.
  R (Reserved): The fixed value is 0.
  Version: The fixed value is 0x01.
  Maximum Area Address: indicates the maximum number of the addresses of supported areas. An integer value ranging from 1 to 254 indicates the maximum number of area addresses allowed by an IS-IS process. The default value 0 indicates that the IS-IS process supports a maximum of three area addresses.
Intradomain Routing Protocol Discriminator |  |  | 
PDU Header Length |  |  | 
Version/Protocol ID Extension |  |  | 
System ID Length |  |  | 
R | R | R | PDU type (5 bits)
Version |  |  | 
Reserved |  |  | 
Max.Areas |  |  | 
1 byte
Address Structure
Topology
Packet Type

## Slide 18: IS-IS Packet Types
IS-IS PDUs are classified into four types: IS-IS Hello PDUs (IIH), link state PDUs (LSPs), Complete Sequence Number PDUs (CSNPs), and Partial Sequence Number PDU (PSNPs).
IIHs: are used to set up and maintain neighbor relationships. Among them, Level-1 LAN IIHs apply to the Level-1 routers on broadcast LANs; Level-2 LAN IIHs apply to the Level-2 routers on broadcast LANs; and P2P IIHs apply to non-broadcast networks.
LSPs: are used to exchange link-state information. There are two types of LSPs: Level-1 and Level-2 LSPs.
SNPs: describe the LSPs in all or some databases to help synchronize and maintain all LSDBs. SNPs are classified into CSNPs and PSNPs, which can be further classified into Level-1 CSNPs, Level-2 CSNPs, Level-1 PSNPs, and Level-2 PSNPs.
… |  |  | 
System ID Length |  |  | 
R | R | R | PDU type
Type Value | Description
15 | L1 LAN IIH
16 | L2 LAN IIH
17 | P2P IIH
18 | L1 LSP
20 | L2 LSP
24 | L1 CSNP
25 | L2 CSNP
26 | L1 PSNP
27 | L2 PSNP
Address Structure
Topology
Packet Type

## Slide 19: Common IS-IS TLVs
A TLV is a data structure that consists of the Type, Length, and Value fields.
The TLV structure features high flexibility and scalability in packet construction. The TLV is used to fix the overall structure of a packet. To add a new feature, you only need to add a new TLV without changing the overall structure of the packet.
TLV Type | Name | PDU Type
1 | Area Addresses | IIH, LSP
2 | IS Neighbors (LSP) | LSP
4 | Partition Designated Level2 IS | L2 LSP
6 | IS Neighbors (MAC Address) | LAN IIH
7 | IS Neighbors (SNPA Address) | LAN IIH
8 | Padding | IIH
9 | LSP Entries | SNP
10 | Authentication Information | IIH, LSP, SNP
128 | IP Internal Reachability Information | LSP
129 | Protocols Supported | IIH, LSP
130 | IP External Reachability Information | LSP
131 | Inter-Domain Routing Protocol Information | L2 LSP
132 | IP Interface Address | IIH, LSP
Address Structure
Topology
Packet Type
Notes: A TLV is also called a code-length-value (CLV).

## Slide 20
Basic Concepts of IS-IS
Working Mechanism of IS-IS
  Neighbor Relationship Setup
  LSDB Synchronization
  Route Calculation
Basic IS-IS Configurations

## Slide 21: Basic Rules for Establishing IS-IS Neighbor Relationships
Basic rules for establishing an IS-IS neighbor relationship are as follows:
  Only neighboring routers of the same level can set up the neighbor relationship with each other.
  Level-1 routers must have the same area IDs.
  Network types of IS-IS interfaces on both ends of a link must be consistent.
  IP addresses of IS-IS interfaces on both ends of a link must be on the same network segment by default.
IS-IS runs on the data link layer and was initially designed for CLNP. Therefore, the establishment of IS-IS neighbor relationships is not related to IP addresses. When IS-IS runs over IP, IS-IS needs to check the IP address of its neighbor. If secondary IP addresses are assigned to the interfaces, the routers can set up the IS-IS neighbor relationship as long as either the primary or secondary IP address is on the same network segment as the local and remote interfaces.
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation
Notes: By simulating an Ethernet interface as a P2P interface, a router can establish a P2P neighbor relationship.
When IP addresses of IS-IS interfaces on both ends of a link are on different network segments, a neighbor relationship can still be established on the two interfaces if the interfaces are configured not to check the IP addresses in received Hello packets.
  For P2P interfaces, you can configure the interfaces not to check the IP addresses.
  For Ethernet interfaces, you must simulate Ethernet interfaces as P2P interfaces and then configure the interfaces not to check the IP addresses.
Generally, one interface only needs one primary IP address. In some special cases, one interface needs additional secondary IP addresses. For example, a router connects to a physical network through an interface, and hosts on this network belong to two network segments. To enable the router to communicate with all hosts on the physical network, configure a primary IP address and a secondary IP address for this interface. You can configure multiple IP addresses for a Layer 3 interface on a router, one as the primary IP address, and the others as secondary IP addresses. Each Layer 3 interface can have a maximum of 31 secondary IP addresses.

## Slide 22: IIH
IIHs are used to set up and maintain neighbor relationships. Among them, Level-1 LAN IIHs apply to the Level-1 routers on broadcast LANs; Level-2 LAN IIHs apply to the Level-2 routers on broadcast LANs; and P2P IIHs apply to non-broadcast networks.
PDU Common Header | 
Reserved/Circuit Type | 
Source ID | 
Holding Time | 
PDU Length | 
R | Priority (7 bits)
LAN ID | 
Local Circuit ID | 
Variable Length Fields | 
Reserved/Circuit Type: indicates the type of the router (01 indicates L1, 10 indicates L2, and 11 indicates L1/L2).
Source ID: indicates the system ID of the router that sends Hello packets.
Holding Time: If no Hello packet is received from the neighbor within the holding time, the neighbor relationship is terminated.
Priority: specifies the priority of the Designated Intermediate System (DIS). The value ranges from 0 to 127. A larger value indicates a higher priority. This field is carried only in LAN IIHs on a broadcast network. P2P IIHs on a P2P network do not have this field or the R bit preceding this field.
LAN ID: includes the system ID and pseudonode ID of the DIS. This field is carried only in LAN IIHs on a broadcast network. P2P IIHs on a P2P network do not contain this field.
Local Circuit ID: This field is carried only in P2P IIHs of the P2P network. LAN IIHs on a broadcast network do not have this field.
1 byte
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 23: Process of Establishing an IS-IS Neighbor Relationship on a Broadcast Network
In Down state, R1 multicasts a Level-1 LAN IIH. The neighbor list in the packet is empty.
After receiving the packet, R2 sets the neighbor relationship status to Initial. R2 then responds to R1 with a Level-1 LAN IIH, indicating that R1 is a neighbor of R2.
R1 receives this packet and sets the status of the neighbor relationship with R2 to Up. R1 then sends R2 a Level-1 LAN IIH that identifies R2 used as a neighbor of R1.
R2 receives this packet and sets the status of the neighbor relationship with R1 to Up. R1 and R2 establish a neighbor relationship successfully.
The network is a broadcast network, so a DIS needs to be elected. After the neighbor relationship is established, routers wait for two intervals before sending IIHs to elect the DIS.
R1(Level-1)
NET 49.0001. 0100.0000.1001.00
Level-1 LAN IIH
System ID: 0100.0000.1001
Area: 49.0001
Neighbour: null
Initial
Up
Two IS-IS routers must establish a neighbor relationship before exchanging packets to implement routing. The modes for establishing IS-IS neighbors vary depending on the network type. On a broadcast network, three-way handshake is used to establish a neighbor relationship.
R1 and R2 are connected through GE interfaces. The process of establishing a neighbor relationship between the two directly connected Level-1 routers is as follows:
R2(Level-1)
NET 49.0001.0100.0000.2002.00
Level-1 LAN IIH
System ID: 0100.0000.2002
Area: 49.0001
Neighbour: 0100.0000.1001
Level-1 LAN IIH
System ID: 0100.0000.1001
Area: 49.0001
Neighbour: 0100.0000.2002
Down
Up
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation
Notes: Multicast addresses of Level-1 and Level-2 IIHs are 01-80-C2-00-00-14 and 01-80-C2-00-00-15 respectively.
Down: It is the initial status of the neighbor relationship.
Initial: The IIH is received, but the neighbor list in the packet does not contain the system ID of the router.
UP: The IIS is received and the neighbor list contains the system ID of the router.

## Slide 24: DIS and Pseudonode
In a broadcast network, IS-IS needs to elect a DIS from all the routers.
DISs are used to create and update pseudonodes and generate LSPs of pseudonodes to describe available network devices. The pseudonode is used to simulate a virtual node on the broadcast network and is not an actual router. In IS-IS, a pseudonode is identified by the system ID of the DIS and Circuit ID (its value is not 0).
L1
L1
DIS
L1
L1
DIS
L1
L1
L1
L1
Pseudonode
Physical link
Logical link
Physical topology
Logical topology
Record all IS-IS routers on the broadcast network.
Ensure that LSDBs are synchronized on a broadcast network.
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 25: DIS in IS-IS and DR in OSPF
Level-1 and Level-2 DISs are elected separately. You can configure different priorities for DISs of different levels.
DIS election rules are as follows:
  The router with the highest priority is elected as the DIS.
  If there are multiple routers with the same highest priority on a broadcast network, the one with the highest MAC address is chosen.
The interval for the DIS to send IIHs is one third of the interval for a common router. This ensures that the faulty DIS can be quickly discovered.
DIS election in IS-IS differs from designated router (DR) election in OSPF:
  On an IS-IS broadcast network, the router with priority 0 also takes part in DIS election. In OSPF, the router with priority 0 does not take part in DR election.
  In IS-IS, when a new router that is qualified for being a DIS connects to a broadcast network, the router is elected as the new DIS and the previous pseudonode is deleted. This causes a new flooding of LSPs. In OSPF, when a new router connects to a network, it is not immediately elected as the DR even if it has the highest DR priority.
  On an IS-IS broadcast network, routers (including non-DIS routers) of the same level on a network segment set up neighbor relationships. In OSPF, routers set up neighbor relationships with only the DR and backup designated router (BDR).
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 26: Process of Establishing a Neighbor Relationship on a P2P Network
On a P2P network, the two-way handshake mechanism is used to establish a neighbor relationship. When a router receives an IIH from the peer, the router declares the neighbor relationship status to be Up and establishes a neighbor relationship.
The two-way handshake mechanism has defects. When IS-IS is used on a P2P network, Huawei devices use three-way handshake to establish neighbor relationships by default. In this mode, three P2P IIHs are sent to establish a neighbor relationship.
R1(Level-1)
NET 49.0001. 0100.0000.1001.00
Level-1 P2P IIH
System ID: 0100.0000.1001
Area: 49.0001
Neighbor: null
Initial
Up
R2(Level-1)
NET 49.0001.0100.0000.2002.00
Level-1 P2P IIH
System ID: 0100.0000.2002
Area: 49.0001
Neighbor: 0100.0000.1001
Level-1 P2P IIH
System ID: 0100.0000.1001
Area: 49.0001
Neighbor: 0100.0000.2002
Down
Up
Serial link
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 27
Basic Concepts of IS-IS
Working Mechanism of IS-IS
  Neighbor Relationship Setup
  LSDB Synchronization
  Route Calculation
Basic IS-IS Configurations

## Slide 28: LSP
LSPs are used to exchange link state information. There are two types of LSPs: Level-1 and Level-2 LSPs. A Level-1 router transmits Level-1 LSPs; a Level-2 router transmits Level-2 LSPs; and a Level-1-2 router can transmit both Level-1 and Level-2 LSPs.
Level-1 and Level-2 LSPs have the same format.
PDU Common Header |  |  | 
PDU Length |  |  | 
Remaining Lifetime |  |  | 
Holding Time |  |  | 
LSP ID |  |  | 
Sequence Number |  |  | 
Checksum |  |  | 
P | ATT(4bit) | OL | IS Type
Variable Length Fields |  |  | 
Remaining Lifetime: indicates the lifetime of an LSP, in seconds.
LSP ID: consists of the system ID, pseudonode ID, and LSP fragment number.
Sequence Number: indicates the LSP sequence number. When a router is started, the sequence number of the first LSP sent by the router is 1. When a new LSP is generated, the sequence number of the LSP is equal to the sequence number of the previous LSP plus 1. Therefore, newer LSPs have larger sequence numbers.
Checksum: indicates the checksum of an LSP.
ATT (Attachment): is generated by a Level-1-2 router to identify whether the originating router is connected to other areas. Though this field is also included in Level-1 or Level-2 LSPs sent by Level-1 or Level2 routers, it is associated only with Level-1 LSPs sent by Level-1-2 routers.
OL (1 bit): indicates the LSDB overload. LSPs with the overload bit are still flooded on the network, but these LSPs are ignored during the calculation of the routes that pass through a router in overload state. After the overload bit is set on a router, other routers ignore the router when performing SPF calculation. If a router is experiencing a memory shortage, it automatically configures the overload bit in LSPs to be sent.
IS Type (2 bits): indicates the type of the router generating the LSP. It is used to specify whether the router is a Level-1 router or a Level-2 router (01 indicates Level-1; 11 indicates Level-2).
1 byte
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 29: IS-IS LSDB
R1(L1)
R3(L1/2)
R2(L1/2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
1.1.1.0/24
Area 49.0001
R1's system ID: 0100.0000.1001
R2's system ID: 0100.0000.2002
R3's system ID: 0100.0000.3003
<R1> display isis lsdb
Database information for ISIS(1)
Level-1 Link State Database
LSPID Seq Num Checksum Holdtime Length ATT/P/OL
---------------------------------------------------------------------------------------------
0100.0000.1001.00-00* 0x00000005 0x13a8 1187 97 0/0/0
0100.0000.1001.01-00* 0x00000001 0xda2e 1185 55 0/0/0
0100.0000.2002.00-00 0x00000004 0x94e9 1188 86 1/0/0
Total LSP(s): 5
*(In TLV)-Leaking Route, *(By LSPID)-Self LSP, +-Self LSP(Extended),
ATT-Attached, P-Partition, OL-Overload
0100.0000.1001 | 00 | 00 | *
System-ID | Pseudonode ID | Fragment ID | Self-originated LSP
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation
Notes: Pseudonode ID: If the value of this parameter is not 0, the LSP is generated by a pseudonode.
Fragment ID: When an IS-IS router needs to advertise the LSPs that contain much information, the IS-IS router generates multiple LSP fragments to carry more IS-IS information. The fragment ID is used to distinguish different LSP fragments.

## Slide 30: Checking the LSP of the Non-pseudonode
R1(L1)
R3(L1/2)
R2(L1/2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
1.1.1.0/24
Area 49.0001
<R1> display isis lsdb 0100.0000.1001.00-00 verbose
Database information for ISIS(1)
Level-1 Link State Database
LSPID Seq Num Checksum Holdtime Length ATT/P/OL
--------------------------------------------------------------------------------------------------
0100.0000.1001.00-00* 0x0000000e 0x9a75 1072 113 0/0/0
SOURCE 0100.0000.1001.00
NLPID IPV4
AREA ADDR 49.0123
INTF ADDR 10.1.12.1 //Describe interface information.
INTF ADDR 10.1.13.1
NBR ID 0100.0000.1001.01 COST: 10 //Describe the neighbor relationship.
NBR ID 0100.0000.3003.01 COST: 10
IP-Internal 10.1.12.0 255.255.255.0 COST: 10
IP-Internal 10.1.13.0 255.255.255.0 COST: 10 //Describe the route information.
IP-Internal 1.1.1.0 255.255.255.0 COST: 10
Total LSP(s): 1
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation
Notes: AREA ADDR: indicates the area ID of the device that generates the LSP.
INTF ADDR: indicates the interface address described in the LSP.
NBR ID: indicates the neighbor information described in the LSP.
IP-Internal: indicates the network segment information described in the LSP.

## Slide 31: Checking the LSP of a Pseudonode
The LSP of the pseudonode contains only neighbor information but not routing information.
R1(L1)
R3(L1/2)
R2(L1/2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
1.1.1.0/24
Area 49.0001
<R1> display isis lsdb 0100.0000.1001.01-00 verbose
Database information for ISIS(1)
Level-1 Link State Database
LSPID Seq Num Checksum Holdtime Length ATT/P/OL
----------------------------------------------------------------------------------------------------
0100.0000.1001.01-00* 0x00000009 0xca36 431 55 0/0/0
SOURCE 0100.0000.1001.01
NLPID IPV4
NBR ID 0100.0000.1001.00 COST: 0 //Describe all IS-IS routers on the broadcast network.
NBR ID 0100.0000.2002.00 COST: 0 //The cost of the route from the pseudonode to other routers is 0.
Total LSP(s): 1
*(In TLV)-Leaking Route, *(By LSPID)-Self LSP, +-Self LSP(Extended),
ATT-Attached, P-Partition, OL-Overload
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 32: CSNP
A CSNP contains the summary of all LSPs in the LSDB of a router. The router determines whether to synchronize its LSDB by exchanging CSNPs.
  On a broadcast network, CSNPs are sent by a DIS periodically (at a default interval of 10 seconds).
  On a P2P link, CSNPs are sent only during initial establishment of a neighbor relationship.
Source ID: indicates the system ID of the router that sends the CSNP.
Start LSP: indicates the ID of the first LSP in a CSNP.
End LSP: indicates the ID of the last LSP in a CSNP.
PDU Common Header
PDU Length
Source ID
Start LSP ID
End LSP ID
Variable Length Fields
1 byte
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 33: PSNP
Unlike a CSNP, a PSNP contains only the summary of some LSPs.
  When the LSDB is not synchronized, the PSNP is used to request the neighbor to send a new LSP.
  On a P2P network, when an LSP is received, a PSNP is used to acknowledge the received LSP.
PDU Common Header
PDU Length
Source ID
Variable Length Fields
Source ID: indicates the system ID of the router that sends the PSNP.
1 byte
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 34: LSP Synchronization on a Broadcast Network
Process of synchronizing LSDBs between a new router and the DIS on a broadcast network:
  The new router R3 sends IIHs to establish neighbor relationships with the other routers in the broadcast domain. R3 establishes neighbor relationships with R1 and R2, waits for the timeout of the LSP refresh timer, and then sends its LSP to a multicast address (01-80-C2-00-00-14 for a Level-1 router and 01-80-C2-00-00-15 for a Level-2 router). All neighbors on the network can receive the LSP.
  The DIS on the network segment adds the received LSP to its LSDB. After the CSNP timer expires, the DIS sends CSNPs to synchronize the LSDBs on the network.
  R3 receives the CSNPs from the DIS, checks its LSDB, and sends a PSNP to request the LSPs it does not have.
  The DIS receives the PSNP and sends R3 the required LSPs for LSDB synchronization.
  On a broadcast network, CSNPs are sent only by the DIS in multicast mode.
PSNP
R1.00-00
R2.00-00
R2.01-00
LSP
R3.00-00
R3.00-01
CSNP
R1.00-00
R2.00-00
R2.01-00
R3.00-00
R3.00-01
LSP
R1.00-00
R2.00-00
R2.01-00
LSP of a pseudonode
Fragmented LSP
R1
R3
R2
DIS
1
3
2
4
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 35: LSP Synchronization on a P2P Network
IS-IS LSDB synchronization on a P2P network:
  R1 establishes a neighbor relationship with R2.
  R1 and R2 send a CSNP to each other. If the LSDB of the neighbor and the received CSNP are not synchronized, the neighbor sends a PSNP to request the required LSP.
  Assume that R2 requests a corresponding LSP from R1.
    R1 sends the required LSP to R2, starts the LSP retransmission timer, and waits for a PSNP from R2 as an acknowledgement for the received LSP.
    If R1 does not receive the PSNP from the neighbor after the LSP retransmission timer expires, it resends the LSP.
    R1 resends the LSP.
    After receiving the LSP, R2 sends a PSNP for acknowledgment.
LSP
R1.00-00
PSNP
R1.00-00
Retransmission timeout
LSP
R1.00-00
PSNP
R1.00-00
Retransmit PSNP
R1
R2
1
3
2
4
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation


## Slide 36: LSP Processing Mechanism
IS-IS synchronizes LSDBs by exchanging LSPs. After receiving LSPs, a router processes the LSPs according to the following rules:
If the received LSP is better than the local LSP or the local device does not have the LSP:
  On a broadcast network, the router adds the LSP to its LSDB and multicasts the LSP.
  On a P2P network, the router adds the LSP to its LSDB and sends a PSNP to acknowledge the receipt of the LSP. Then the router sends the new LSP to all its neighbors except the neighbor that sends the LSP.
If the received LSP cannot be compared with the local LSP, the router does not process the LSP.
Receive multiple instances of an LSP
Are sequence numbers the same?
The LSP is not processed.
Yes
No
No
A larger sequence number is preferred.
Yes
The LSP where the keepalive time is 0 is preferred.
No
Yes
Is the holding time 0s?
A large checksum is preferred.
Is the checksum the same?
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation
Notes: All routers in the IS-IS routing domain can generate LSPs. The following events trigger the generation of a new LSP:
  The neighbor is Up or Down.
  The related interface goes Up or Down.
  The imported IP routes change.
  Inter-area IP routes change.
  The interface is assigned a new metric value.
  LSPs are updated periodically (update interval: 15 minutes).

## Slide 37
Basic Concepts of IS-IS
Working Mechanism of IS-IS
  Neighbor Relationship Setup
  LSDB Synchronization
  Route Calculation
Basic IS-IS Configurations

## Slide 38: Route Calculation on a Level-1 Router
R1 is a Level-1 router and maintains only the Level-1 LSDB. The LSDB contains Level-1 LSPs generated by R1 and level-1 LSPs of R2 and R3.
R1 calculates the topology of Area 49.0001 and the routes to each network segment in the area based on the Level-1 LSPs in the LSDB.
R2 and R3 are Level-1-2 routers in Area 49.0001. They set the ATT field in the Level-1 LSPs they send to the area to announce that they can reach other areas through themselves. As a Level-1 router, R1 calculates the default route to R2 or R3 based on the ATT field.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5(L2)
R4(L2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
192.168.10.0/24
192.168.20.0/24
10.1.45.0/24
Area 49.0001
Area 49.0002
ATT=1
ATT=1
L1 LSP
L1: Level-1 router
L2: Level-2 router
L1/2: Level-1-2 router
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 39: Sub-optimal Path of a Level-1 Router
By default, R1 can reach the destination outside an area only through the default route pointing to R2 or R3. However, the costs of the routes from R1 to R2 and R3 are the same. Therefore, when R1 sends a data packet to 192.168.20.0/24, path 2 may be selected. As a result, the sub-optimal path problem occurs.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
10
10
10
10
10
Cost of path 1:
Cost = 10+10+10 = 30
Cost of path 2:
Cost = 10+10+10+10 = 40
10
10
192.168.10.0/24
192.168.20.0/24
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 40: Route Leaking
By default, a Level-1-2 router does not advertise the routes to other areas to the local Level-1 area.
Through route leaking, inter-area routes can be transmitted to the Level-1 area through the Level-1-2 router. In this case, the Level-1 router can learn the specific routes of other areas and calculate the optimal path.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
192.168.10.0/24
192.168.20.0/24
192.168.10.0/24
192.168.20.0/24
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 41: Route Calculation on a Level-1-2 Router
R2 and R3 maintain Level-1 LSDBs and can calculate routes in Area 49.0001 based on LSPs in the LSDBs.
R2 and R3 maintain Level-2 LSDBs and can calculate routes in Area 49.0002 based on LSPs in the LSDBs.
R2 and R3 send the routes to Area 49.0001 to Area 49.0002 through Level-2 LSPs.
L1 LSP
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
10.1.45.0/24
L2 LSP
Level-2 LSP
that describes
the route to Area 49.0001
Area 49.0001
Area 49.0002
192.168.10.0/24
192.168.20.0/24
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 42: Route Calculation on a Level-2 Router
R4 and R5 used as Level-2 routers maintain only Level-2 LSDBs and can calculate routes to network segments on the entire network based on the LSDBs.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
10.1.45.0/24
Area 49.0001
Area 49.0002
192.168.10.0/24
192.168.20.0/24
L1 LSP
L2 LSP
Level-2 LSP that describes the route to Area 49.0001
Neighbor Relationship Setup
LSDB Synchronization
Route Calculation

## Slide 43
Basic Concepts of IS-IS
Working Mechanism of IS-IS
Basic IS-IS Configurations

## Slide 44: Basic IS-IS Configurations (1)
[Huawei] isis [process-id ]
Create an IS-IS process and enter the IS-IS process view.
process-id specifies the ID of an IS-IS process. If process-id is not specified, the default IS-IS process ID is 1.
[Huawei-isis-1] network-entity net
Configure a NET.
Generally, you only need to configure one NET for an IS-IS process. When an area needs to be redefined, for example, the area needs to be merged with other areas or divided into sub-areas, configure multiple NETs to ensure route correctness. A maximum of three area addresses can be configured in an IS-IS process, and therefore, you can configure only a maximum of three NETs. When you configure multiple NETs, ensure that their system IDs are the same.
[Huawei-isis-1] is-level { level-1 | level-1-2 | level-2 }
Configure a device level.
By default, the level of the device is Level-1-2.
If the levels of IS-IS devices are changed during network operation, the IS-IS process will be restarted, and IS-IS neighbor relationships will be disconnected. Setting the levels of devices when configuring IS-IS is recommended.

## Slide 45: Basic IS-IS Configurations (2)
[Huawei]interface interface-type interface-number
Enter the interface view.
interface-type specifies the interface type and interface-number specifies the interface number.
[Huawei-GigabitEthernet0/0/1] isis enable [ process-id ]
Enable IS-IS on the interface.
After this command is run, IS-IS establishes neighbor relationships and floods LSPs through this interface.
[Huawei-GigabitEthernet0/0/1] isis circuit-level [ level-1 | level-1-2 | level-2 ]
Configure the level of the interface.
By default, the level of an interface is Level-1-2.
By default, Level-1 and Level-2 neighbor relationships will be established between two Level-1-2 devices. To allow the two Level-1-2 devices to establish only the Level-1 or Level-2 neighbor relationship, change the level of interfaces.

## Slide 46: Basic IS-IS Configurations (3)
[Huawei-GigabitEthernet0/0/1]isis circuit-type p2p
Set the network type of the interface to P2P.
By default, the network type of an interface is determined by the physical type of the interface.
After a broadcast interface is simulated as a P2P interface, the interval for sending IIHs, the number of IIHs that IS-IS does not receive from a neighbor before the neighbor is declared Down, interval for resending LSPs on a P2P link, and various IS-IS authentication modes are restored to the default settings; other configurations such as the DIS priority, DIS name, and interval for sending CSNPs on a broadcast network become invalid.
[Huawei-GigabitEthernet0/0/1] undo isis circuit-type
Restore the default network type of the IS-IS interface.
After the undo isis circuit-type command is run to restore the default network type of an IS-IS interface, the interval for sending IIHs, number of IIHs that IS-IS does not receive from a neighbor before the neighbor is declared Down, interval for retransmitting LSPs on a P2P link, various IS-IS authentication modes, DIS priority, and interval for sending CSNPs on a broadcast network are restored to the default settings.
[Huawei-GigabitEthernet0/0/1] isis dis-priority priority [ level-1 | level-2 ]
Change the DIS priority of an IS-IS interface.
By default, the DIS priority of an IS-IS interface is 64.
The isis dis-priority command sets a priority for an interface to run for the DIS on a specified level.

## Slide 47: Case: IS-IS Configuration
Networking Requirements
As shown in the figure, five routers are deployed on the network. The five routers need to communicate with each other. R1 can only process a small amount of data because it has lower performance than the other routers. R1 is required to select the optimal path to access network segments 192.168.10.0/24 and 192.168.20.0/24.
Configuration Roadmap
Enable IS-IS on each router so that the routers can be interconnected. Configure R1 as a Level-1 router to enable it to maintain less data. In addition, configure R2 and R3 as Level-1-2 routers to interconnect with Level-2 routers of R4 and R5.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
GE0/0/0
10.1.12.1/24
GE0/0/2
192.168.10.0/24
GE0/0/2
192.168.20.0/24
GE0/0/1
10.1.13.1/24
GE0/0/0
10.1.12.2/24
GE0/0/0
10.1.13.3/24
GE0/0/1
10.1.24.2/24
GE0/0/1
10.1.35.3/24
GE0/0/0
10.1.24.4/24
GE0/0/0
10.1.35.5/24
GE0/0/1
10.1.45.4/24
GE0/0/1
10.1.45.5/24
Area 49.0001
Area 49.0002
LoopBack1
1.1.1.1/32
LoopBack1
2.2.2.2/32
LoopBack1
3.3.3.3/32
LoopBack1
4.4.4.4/32
LoopBack1
5.5.5.5/32

## Slide 48: Case: Configurations of R1, R2, and R3
R1 (L1)
R3 (L1/2)
R2 (L1/2)
GE0/0/0
10.1.12.1/24
GE0/0/1
10.1.13.1/24
GE0/0/0
10.1.12.2/24
GE0/0/0
10.1.13.3/24
GE0/0/1
10.1.24.2/24
GE0/0/1
10.1.35.3/24
Area 49.0001
LoopBack1
1.1.1.1/32
LoopBack1
2.2.2.2/32
LoopBack1
3.3.3.3/32
[R1] isis 1
[R1-isis-1] is-level level-1
[R1-isis-1] network-entity 49.0010.0100.1001.00
[R1-isis-1] quit
[R1] interface gigabitethernet 0/0/0
[R1-GigabitEthernet0/0/0] isis enable 1
[R1-GigabitEthernet0/0/0] interface gigabitethernet 0/0/1
[R1-GigabitEthernet0/0/1] isis enable 1
R1 configuration:
[R2] isis 1
[R2-isis-1] is-level level-1-2
[R2-isis-1] network-entity 49.0020.0200.2002.00
[R2-isis-1] quit
[R2] interface gigabitethernet 0/0/0
[R2-GigabitEthernet0/0/0] isis enable 1
[R2-GigabitEthernet0/0/0] interface gigabitethernet 0/0/1
[R2-GigabitEthernet0/0/1] isis enable 1
R2 configuration:
The level of R1 needs to be set to Level-1 and the levels of R2 and R3 to Level-1-2.
The configuration of R3 is similar to that of R2 and is not provided here.

## Slide 49: Case: Configurations of R4 and R5
R5 (L2)
R4 (L2)
GE0/0/2
192.168.10.0/24
GE0/0/2
192.168.20.0/24
GE0/0/0
10.1.24.4/24
GE0/0/0
10.1.35.5/24
GE0/0/1
10.1.45.4/24
GE0/0/1
10.1.45.5/24
Area 49.0002
LoopBack1
4.4.4.4/32
LoopBack1
5.5.5.5/32
[R4] isis 1
[R4-isis-1] is-level level-2
[R4-isis-1] network-entity 49.0040.0400.4004.00
[R4-isis-1] quit
[R4] interface gigabitethernet 0/0/0
[R4-GigabitEthernet0/0/0] isis enable 1
[R4-GigabitEthernet0/0/0] interface gigabitethernet 0/0/1
[R4-GigabitEthernet0/0/1] isis enable 1
[R4-GigabitEthernet0/0/1] interface gigabitethernet 0/0/2
[R4-GigabitEthernet0/0/2] isis enable 1
R4 configuration:
The level of R4 and R5 needs to be set to Level-2.
The configuration of R5 is similar to that of R4 and is not provided here.

## Slide 50: Case: Configuration Verification (Checking the IS-IS Neighbor Relationship Table)
<R1> display isis peer
Peer information for ISIS(1)
Total Peer(s): 2
<R4> display isis peer
Peer information for ISIS(1)
Total Peer(s): 2
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
GE0/0/0
GE0/0/1
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
Area 49.0001
Area 49.0002
System Id | Interface | Circuit Id | State | HoldTime | Type | PRI
0020.0200.2002 | GE0/0/0 | 0040.0400.4004.01 | Up | 25s | L2 | 64
0050.0500.5005 | GE0/0/1 | 0050.0500.5005.01 | Up | 13s | L2 | 64
System Id | Interface | Circuit Id | State | HoldTime | Type | PRI
0020.0200.2002 | GE0/0/0 | 0010.0100.1001.01 | Up | 29s | L1 | 64
0030.0300.3003 | GE0/0/1 | 0030.0300.3003.01 | Up | 9s | L1 | 64
R4 sets up a Level-2 neighbor relationship.
R1 sets up a Level-1 adjacency.
Notes: System Id: indicates the system ID of the neighbor.
Interface: describes the router interface through which the neighbor relationship is established.
Type: indicates the type of the neighbor relationship.
PRI: indicates the DIS priority of the interface.

## Slide 51: Case: Configuration Verification (Checking the IS-IS Routing Table)
<R1> display isis route
Route information for ISIS(1)
ISIS(1) Level-1 Forwarding Table
IPV4 Destination | IntCost | ExtCost | ExitInterface | NextHop
0.0.0.0/0 | 10 | NULL | GE0/0/0 | 10.1.12.2
 |  |  | GE0/0/1 | 10.1.13.3
10.1.24.0/24 | 20 | NULL | GE0/0/0 | 10.1.12.2
10.1.13.0/24 | 10 | NULL | GE0/0/1 | Direct
10.1.12.0/24 | 10 | NULL | GE0/0/0 | Direct
10.1.35.0/24 | 20 | NULL | GE0/0/1 | 10.1.13.3
The routing table of R1 contains specific routes in the area and two equal-cost default routes.
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
GE0/0/0
GE0/0/1
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
Area 49.0001
Area 49.0002

## Slide 52: Case: Configuration Verification (Checking the IS-IS Routing Table)
<R3>display isis route
Route information for ISIS(1)
-----------------------------
ISIS(1) Level-1 Forwarding Table
--------------------------------
IPV4 Destination IntCost ExtCost ExitInterface NextHop Flags
-------------------------------------------------------------------------------
0.0.0.0/0 20 NULL
10.1.24.0/24 30 NULL GE0/0/0 10.1.13.1 A/-/L/-
10.1.13.0/24 10 NULL GE0/0/0 Direct D/-/L/-
10.1.12.0/24 20 NULL GE0/0/0 10.1.13.1 A/-/L/-
10.1.35.0/24 10 NULL GE0/0/1 Direct D/-/L/-
Flags: D-Direct, A-Added to URT, L-Advertised in LSPs, S-IGP Shortcut,
U-Up/Down Bit Set
……
……
ISIS(1) Level-2 Forwarding Table
--------------------------------
IPV4 Destination IntCost ExtCost ExitInterface NextHop Flags
-------------------------------------------------------------------------------
10.1.24.0/24 30 NULL
10.1.13.0/24 10 NULL GE0/0/0 Direct D/-/L/-
10.1.12.0/24 40 NULL
192.168.20.0/24 20 NULL GE0/0/1 10.1.35.5 A/-/-/-
10.1.45.0/24 20 NULL GE0/0/1 10.1.35.5 A/-/-/-
192.168.10.0/24 30 NULL GE0/0/1 10.1.35.5 A/-/-/-
10.1.35.0/24 10 NULL GE0/0/1 Direct D/-/L/-
Flags: D-Direct, A-Added to URT, L-Advertised in LSPs, S-IGP Shortcut,
U-Up/Down Bit Set
R3 functions as a Level-1-2 router and has Level-1 and Level-2 routes in the routing table.

## Slide 53: Route Leaking Configuration
[R2] ip ip-prefix 1 permit 192.168.10.0 24
[R2] isis 1
[R2-isis-1] import-route isis level-2 into level-1 filter-policy ip-prefix 1
R2 configuration:
[R3] ip ip-prefix 1 permit 192.168.20.0 24
[R3] isis 1
[R3-isis-1] import-route isis level-2 into level-1 filter-policy ip-prefix 1
R3 configuration:
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
Area 49.0001
Area 49.0002
192.168.10.0/24
192.168.20.0/24
192.168.10.0/24
192.168.20.0/24
Notes: The filtering policy will be described in subsequent courses.

## Slide 54: Route Leaking Verification
Check the routing table of R1. You can see that two specific routes to 192.168.10.0/24 and 192.168.20.0/24 are added. The costs of the two routes are 30. When a data packet reaches the two network segments through R1, no sub-optimal path is generated.
<R1> display ip routing-table protocol isis
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Public routing table : ISIS
Destinations : 5 Routes : 6
ISIS routing table status : <Active>
Destinations : 5 Routes : 6
Destination/Mask Proto Pre Cost Flags NextHop Interface
0.0.0.0/0 ISIS-L1 15 10 D 10.1.12.2 GigabitEthernet0/0/0
ISIS-L1 15 10 D 10.1.13.3 GigabitEthernet0/0/1
192.168.10.0/2 ISIS-L1 15 30 D 10.1.12.2 GigabitEthernet0/0/0
192.168.20.0/2 ISIS-L1 15 30 D 10.1.13.3 GigabitEthernet0/0/1
10.1.24.0/24 ISIS-L1 15 20 D 10.1.12.2 GigabitEthernet0/0/0
10.1.35.0/24 ISIS-L1 15 20 D 10.1.13.3 GigabitEthernet0/0/1
R1 (L1)
R3 (L1/2)
R2 (L1/2)
R5 (L2)
R4 (L2)
GE0/0/2
192.168.10.0/24
GE0/0/2
192.168.20.0/24
Area 49.0001
Area 49.0002

## Slide 55: IS-IS Authentication Types
To ensure network security, IS-IS authentication encrypts IS-IS packets by adding an authentication field to packets. When a local router receives IS-IS packets from a remote router, the local router discards the packets if the authentication passwords do not match. This protects the local router.
Based on the types of packets, authentication is classified as follows:
  Interface authentication: is configured in the interface view to authenticate Level-1 and Level-2 IS-to-IS Hello PDUs (IIHs).
  Area authentication: is configured in the IS-IS process view to authenticate Level-1 CSNPs, PSNPs, and LSPs.
  Routing domain authentication: is configured in the IS-IS process view to authenticate Level-2 CSNPS, PSNPs, and LSPs.
Based on the authentication modes of packets, authentication is classified into the following types:
  Cleartext authentication: is a simple authentication mode in which passwords are directly added to packets. This mode provides the lowest password security among all the authentication modes listed here.
  MD5 authentication: uses the MD5 algorithm to encrypt a password before adding the password to the packet, which improves password security.
  Keychain authentication: further improves network security with configurable key chain that changes with time.
  HMAC-SHA256 authentication: uses the HMAC-SHA256 algorithm to encrypt a password before adding the password to the packet, which improves password security.

## Slide 56: IS-IS Authentication
Interface authentication
  Authentication passwords for IIHs are saved on interfaces. The interfaces send authentication packets with the authentication TLV. Interconnected router interfaces must be configured with the same password.
Area authentication
  Every router in an IS-IS area must use the same authentication mode and have the same key chain.
Routing domain authentication
  Every Level-2 or Level-1-2 router in an IS-IS area must use the same authentication mode and have the same key chain.
  In area authentication and routing domain authentication, you can configure a router to authenticate LSPs and SNPs separately in the following ways:
    A router sends LSPs and SNPs carrying the authentication TLV and verifies the authentication information about the received LSPs and SNPs.
    A router sends LSPs that carry the authentication TLV and verifies the authentication information of the LSPs it receives. The router sends SNPs that carry the authentication TLV and does not verify the authentication information of the SNPs it receives.
    A router sends LSPs that carry the authentication TLV and verifies the authentication information of the LSPs it receives. The router sends SNPs without the authentication TLV and does not verify the authentication information of the SNPs it receives.
    A router sends LSPs and SNPs that carry the authentication TLV but does not verify the authentication information of the LSPs and SNPs it receives.

## Slide 57: IS-IS Authentication Configuration (1)
[Huawei-isis-1] area-authentication-mode { { simple | md5 } { plain plain-text | [ cipher ] plain-cipher-text } keychain keychain-name | hmac-sha256 key-id key-id } [ snp-packet { authentication-avoid | send-only } | all-send-only ]
Configure IS-IS area authentication.
simple indicates that the password is authenticated in plain-text mode. keychain specifies the key chain that changes with time. md5 indicates that the password is encrypted using the HMAC-MD5 algorithm and then used for authentication.
snp-packet indicates SNP authentication. authentication-avoid indicates that the router encapsulates generated LSPs but not SNPs with authentication information and authenticates received LSPs but not SNPs. send-only indicates that the router encapsulates generated LSPs and SNPs with authentication information, and authenticates received LSPs but not SNPs. all-send-only indicates that the router encapsulates generated LSPs and SNPs with authentication information, but does not authenticate received LSPs and SNPs.
[Huawei-isis-1] domain-authentication-mode { { simple | md5 } { plain plain-text | [ cipher ] plain-cipher-text } keychain keychain-name | hmac-sha256 key-id key-id } [ snp-packet { authentication-avoid | send-only } | all-send-only ]
Configure IS-IS routing domain authentication.
The parameter description is the same as that of area authentication.

## Slide 58: IS-IS Authentication Configuration (2)
[Huawei-GigabitEthernet0/0/0] isis authentication-mode [keychain | md5 | simple ] [ level-1 | level-2 ] [ ip | osi ] [ send-only ]
Configure IS-IS interface authentication.
level-1 indicates level-1 authentication. level-2 indicates level-2 authentication. send-only indicates that the router only encapsulates authentication information to the sent IIHs, but does not authenticate the received IIHs.
Interface authentication is used as an example.
R1(L1)
R2(L1)
GE0/0/0
10.1.12.2/24
GE0/0/0
10.1.12.1/24
[R1] interface GigabitEthernet0/0/0
[R1-GigabitEthernet0/0/0] isis authentication-mode simple cipher huawei
Configure interface authentication on GE0/0/0 of R1.
[R1] display isis error
Hello packet errors:
Mismatched Max Area Addr : 0 Bad Authentication : 6
Interface authentication is not configured on R2, so an authentication error is displayed when IS-IS error information is displayed.

## Slide 59
(Multiple) Which of the following statements about OSPF and IS-IS are true?( )
  Both OSPF and IS-IS are link-state routing protocols.
  OSPF supports only IP networks, whereas Integrated IS-IS supports CLNP and IP networks.
  OSPF uses area 0 to identify the backbone area.
  The IS-IS backbone area consists of Level-2 and Level-1-2 routers.
(Multiple) Which of the following statements about Level-1 routers are true?( )
  A Level-1 router can establish neighbor relationships only with IS-IS routers in the same area.
  A Level-1 router can establish a neighbor relationship with a Level-2 router in the same area.
  By default, a Level-1 router can reach the destination outside an area only through the default route.
  The LSDB of a Level-1 router contains only Level-1 LSPs.
Notes: ABCD
ACD

## Slide 60
This course describes basic concepts of IS-IS. Each IS-IS router has at least one NET. IS-IS uses a hierarchical architecture. All Level-2 and Level-1-2 routers form a backbone area, and Level-1 routers in the same area form a common area. IS-IS packets are classified into four types: IIH, CSNP, PSNP, and LSP.
A Level-1 router maintains only the LSDB of the area. A Level-1 route reaches the destination outside the area through the closest Level-1-2 router. To prevent sub-optimal paths, you can configure route leaking on the Level-1-2 router.
IS-IS supports interface authentication, area authentication, and routing domain authentication.
Both IS-IS and OSPF are link-state routing protocols and need to maintain LSDBs. As the network scale expands, a large LSDB degrades the overall performance of routers. Therefore, for the two routing protocols, multi-area network design is required for larger-scale networking.