## Slide 1
Shi Miaomiao/swx791350
2019-12-17
New

## Slide 2: BGP Basics

## Slide 3
A network is divided into different autonomous systems (ASs) to facilitate network management. An Exterior Gateway Protocol (EGP) was used to dynamically exchange routing information between ASs. However, the EGP advertises only reachable routes and does not select optimal routes or prevent routing loops. Therefore, the EGP cannot meet network management requirements.
BGP was designed to replace the EGP and has the following capabilities: BGP selects optimal routes, prevents routing loops, transmits routing information efficiently, and maintains a lot of routes.
This course describes BGP basics.

## Slide 4
Upon completion of this course, you will be able to:
  Describe basic concepts of BGP.
  Describes BGP peer types.
  Learn how to set up a BGP peer relationship.
  Learn BGP state machine.
  Perform basic BGP configurations.

## Slide 5
Introduction to BGP
Basic Concepts of BGP
Basic BGP Configurations

## Slide 6: AS
IGPs, such as OSPF and IS-IS, are widely used on organizational networks. As the network scale expands and the number of routes on the network increases, IGPs cannot manage large-scale networks. As a result, the concept of Autonomous Systems (ASs) emerges.
An AS is a collection of devices that are managed by the same organization and use the same route selection policy.
ASs are distinguished by AS numbers. An AS number can be expressed in 16-bit or 32-bit format. The Internet Assigned Numbers Authority (IANA) assigns AS numbers.
When different ASs need to communicate with each other, which routing protocol should be used to transmit routes between the ASs?
AS 100
AS 200
?
…
…
OSPF
IS-IS
…
…
…
OSPF
…
Notes: IANA: an organization under the Internet Architecture Board (IAB). The IANA authorizes the Network Information Center (NIC) and other organizations to assign IP addresses and domain names. In addition, the IANA maintains the protocol identifier database used by the TCP/IP protocol suite, including AS numbers.
In 16-bit format, AS numbers 64512-65534 are private ones. In 32-bit format, AS numbers 4200000000-4294967294 are private ones.

## Slide 7: Using an IGP to Transmit Routes
  A direct or logical link (for example, a GRE tunnel) must be established between ASs for peer relationship setup.
  ASs may belong to different organizations or companies and cannot be trusted mutually. Using an IGP may expose network information inside an AS.
  As the network scale expands, the number of routes increases, the routing table size increases, route convergence becomes slow, and device performance consumption increases.
OSPF
OSPF LSA
IS-IS
…
…
…
OSPF
…
…
…
OSPF
AS 100
AS 200
Notes: Virtual private network (VPN): is used to build a logically and directly connected network.

## Slide 8: Using BGP to Transmit Routes
The Border Gateway Protocol (BGP) is specially used between ASs for route transmission. Compared with a conventional IGP, BGP has the following characteristics:
  BGP is based on TCP. A BGP connection can be established as long as a TCP connection can be established.
  BGP transmits only routing information, but does not expose topology information in an AS.
  BGP routes are updated only upon network changes. They are not updated periodically.
BGP route update
BGP
IS-IS
…
…
…
OSPF
…
…
…
OSPF
AS 100
AS 200

## Slide 9: BGP Development History
AS 100
AS 200
EGP
...
...
AS 100
AS 200
BGP-1
...
...
AS 100
AS 200
BGP4+
...
...
After years of development, many RFCs about BGP have been released. Starting from BGP-4 (RFC 1771), BGP has become a classless routing protocol, and BGP4+ supports multiple address families.
Currently, BGP4+ is proposed.
About 1980, the concept of AS was proposed.
An EGP advertises only routes and does not control route selection or prevent routing loops. In 1989, BGP RFC 1105 (BGP-1) was released. RFC 1163 released in 1990 proposed the concept of path attributes. BGP can select routes and control paths based on path attributes.
In 1989, the first RFC of BGP was released.
In about 1980, the network scale expands and the number of routes increases. To solve this problem, the concept of AS is introduced. An External Gateway Protocol (EGP) is used between ASs.
Notes: The latest RFC for BGP-4 is RFC 4271. Compared with RFC 1771, RFC 4271 further describes some details, such as events, state machine, and BGP route decision-making process.

## Slide 10: BGP Application in Enterprises
Communication within an Enterprise
Communication Between Enterprises and a Carrier
Branches of a large enterprise use BGP to exchange routes. Different branches belong to different BGP ASs.
The enterprise and carrier can use BGP to exchange routes so that the enterprise network can obtain specific routes to the carrier network and the carrier can obtain routes to the enterprise network.
AS 100
AS 200
AS 800
BGP
HQ
Branch 1
Branch 8
AS 200
AS 800
Carrier X
Enterprise B
Enterprise N
BGP
BGP
BGP
Enterprise A
AS 1000

## Slide 11
Introduction to BGP
Basic Concepts of BGP
Basic BGP Configurations

## Slide 12: Overview of BGP
BGP is a path vector protocol that allows devices between ASs to communicate and selects optimal routes. BGP-1 (defined in RFC 1105), BGP-2 (defined in RFC 1163), and BGP-3 (defined in RFC 1267) are three earlier versions of BGP. BGP-4 (defined in RFC 1771) has been used since 1994. Since 2006, unicast IPv4 networks have been using BGP-4 defined in RFC 4271, and other networks (such as IPv6 networks) have been using Multiprotocol BGP (MP-BGP) defined in RFC 4760.
BGP has the following characteristics:
  BGP uses TCP (port 179) as the transport layer protocol and triggers route updates instead of periodic route updates.
  BGP can carry a large amount of routing information and support large-scale networks.
  BGP provides various routing policies to flexibly select routes and instruct peers to advertise routes based on routing policies.
  BGP supports MPLS/VPN applications and transmits VPN routes.
  BGP offers route summarization and route dampening functions to prevent route flapping, enhancing network stability.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 13: BGP Characteristics (1)
BGP uses TCP as the transport layer protocol and TCP port number is 179. BGP sessions between routers are established based on TCP connections.
A router that runs BGP is called a BGP speaker or a BGP router.
Two routers that establish a BGP session are peers of each other, and BGP peers exchange BGP routing tables.
A BGP router sends only incremental BGP route updates.
BGP can carry a large number of route prefixes and can be applied to large-scale networks.
AS 200
AS 300
IP routing Table
Route number: 70W+
BGP speaker
BGP speaker
BGP
TCP
IP
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 14: BGP Characteristics (2)
BGP is also called a path vector routing protocol.
Each BGP route carries multiple path attributes. Different from IS-IS and OSPF that use costs to select paths, BGP selects paths based on path attributes. Therefore, BGP is easy to operate and allows you to select the most appropriate path control mode in different scenarios.
AS 100
AS 200
BGP
…
…
AS 300
…
AS 400
…
BGP
BGP
BGP
BGP route update
10.1.2.0/8
Path Attribute – Origin: IGP
Path Attribute - AS_PATH: 200
Path Attribute – Nexthop: 10.0.12.1
…
BGP route update
10.1.2.0/8
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 15: BGP Peer Relationship
Different from OSPF and IS-IS, BGP sessions are established based on TCP. The two routers that establish a BGP peer relationship do not need to be directly connected.
BGP has two types of peer relationships:
  External BGP (EBGP): BGP peer relationship between BGP routers in different ASs To establish an EBGP peer relationship between two routers, ensure that the following conditions are met:
    The two routers belong to different ASs (AS numbers).
    When configuring EBGP, ensure that the IP address of the peer specified in the peer command is reachable and the TCP connection can be set up.
  Internal BGP (IBGP): BGP peer relationship between BGP routers in the same AS.
AS 100
AS 300
EBGP Peer
AS 200
EBGP Peer
IBGP Peer
OSPF
WAN
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 16: Establishing a BGP Peer Relationship (1)
The router that first starts BGP initiates a TCP connection. As shown in the figure on the left, R1 first starts BGP and uses a random port number to initiate a TCP connection to port 179 of R2.
After the three-way handshake is complete, R1 and R2 send Open messages carrying parameters to each other to establish a peer relationship. After the parameters are negotiated, R1 and R2 send Keepalive messages to each other. After receiving the Keepalive messages from each other, the two routers establish a peer relationship. In addition, R1 and R2 periodically send Keepalive messages to maintain the connection.
The Open message carries the following information:
  My Autonomous System: indicates the AS number.
  Hold Time: is used to negotiate the time for sending Keepalive messages.
  BGP Identifier: indicates the router ID of the local router.
WAN
TCP SYN
AS 300
AS 200
TCP SYN+ACK
TCP ACK
Open
Open
Keepalive
Keepalive
1
2
3
R1
R2
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: Each BGP peer initiates a TCP three-way handshake, so two TCP connections are established. Actually, BGP retains only one TCP connection. After obtaining the BGP identifier of the peer from an Open message, the BGP peer compares the local router ID with the peer router ID. If the local router ID is smaller than the remote router ID, the local router terminates the TCP connection and uses the TCP connection initiated by the remote router to exchange BGP messages.

## Slide 17: Establishing a BGP Peer Relationship (2)
After a BGP peer relationship is established, a BGP router sends a BGP Update message to advertise routes to the peer.
WAN
AS 300
AS 200
Update
Update
R1
R2
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 18: Source Address of a TCP Connection
By default, BGP uses the interface that sends BGP messages as the local interface of a TCP connection.
When deploying IBGP peer relationships, you are advised to use loopback addresses as source addresses of TCP connections. The loopback interface is stable. The reliability can be ensured by using the IGP and redundancy topology in the AS.
During EBGP peer relationship setup, the IP address of the directly connected interface is often used as the source address. If you use a loopback interface to establish an EBGP peer relationship, pay attention to the EBGP multi-hop problem.
AS 200
R2
R3
R4
R1
GE0/0/0
10.0.12.1
GE0/0/0
10.0.13.3
IBGP peer
Typically, a network in an AS provides certain redundancy. If R1 and R3 use directly connected interfaces to establish an IBGP peer relationship, the BGP session will be interrupted once the directly connected interface or link fails. However, due to redundant links, the IP connectivity between R1 and R3 is not Down. (R1 and R3 can still communicate with each other through R4.)
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 19: BGP Message Types (1)
There are five types of BGP messages. Different types of messages have the same header.
L2 Header | IP Header | TCP Header | BGP Packet | CRC
BGP Header | BGP Packet
Open
Update
Notification
Keepalive
Route-refresh
Marker (16 bytes) |  | 
Length (2 bytes) | Type (1 byte) | 
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: Different from common IGP protocols, BGP uses TCP as the transport layer protocol and port 179. This enables BGP to establish peer relationships between indirectly connected routers.

## Slide 20: BGP Message Types (2)
Name | Function | Usage Scenario
Open | Negotiate BGP peer parameters and establish peer relationships. | After a BGP TCP connection is established, Open messages are sent.
Update | Send BGP route update. | After a BGP peer relationship is established and routes need to be sent or routes change, Update messages are sent.
Notification | Report error information and terminate the peer relationship. | When detecting an error during BGP running, the local BGP router sends a Notification message to notify the peer of the error.
Keepalive | Indicate that the peer relationship is established and the BGP peer relationship is maintained. | After receiving a Keepalive message from the peer, the BGP router sets the peer relationship status to Established and periodically sends Keepalive messages to maintain the connection.
Route-refresh | Request the peer to retransmit routes if routing policies are changed. Only the BGP devices supporting route-refresh can send and respond to Route-refresh messages. | When the routing policy changes, Route-refresh messages are sent to trigger the peer to re-advertise routes.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 21: BGP Message Format: Header Format
The five types of BGP messages have the same header, as shown in the left part of. The main fields are described as follows:
  Marker: is used to check whether synchronization information of BGP peers is complete and for BGP authentication. It has 16 bytes. If authentication is not used, all bits are set to 1 (all FFs in hexadecimal notation).
  Length: indicates the total length of a BGP message (including the packet header), in bytes. It has 2 bytes.
  Type: indicates the type of BGP messages. It has 1 byte. The value ranges from 1 to 5, indicating Open, Update, Notification, Keepalive, and Route-refresh messages.
Marker (16 bytes) |  |  |  | 
Length (2 bytes) | Type (1 byte) |  |  | 
1: Open
2: Update
3: Notification
4: Keepalive
5: Route-refresh
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 22: BGP Message Format: Open
The Open message is the first message sent after a TCP connection is established. It is used to establish a connection between BGP peers. The figure on the left shows the Open message format. The main fields in the Open message are described as follows:
  Version: indicates the BGP version number. For BGPv4, the value is 4.
  My AS: indicates the local AS number. By comparing AS numbers of the two ends, you can determine whether the peer end and the local end are in the same AS.
  Hold Time: indicates the holding time. BGP peers need to negotiate the holding time and keep it consistent when establishing a peer relationship. If a router does not receive any Keepalive or Update message from its peer within the holding time, the BGP connection is considered as disconnected.
  BGP Identifier: indicates the router ID of a BGP router. The field is in IP address format and identifies a BGP router.
Version (8 bits) |  |  | 
My AS (16 bits) |  |  | 
Hold Time (16 bits) |  |  | 
BGP Identifier (32 bits) |  |  | 
Opt Parm Len (8 bits) |  |  | 
Optional parameters (variable length) |  |  | 
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: Opt Parm Len: indicates the length of Optional parameters.
Optional parameters: declares optional capabilities of a BGP router, such as authentication and multi-protocol support.
In addition to IPv4 unicast routing information, BGP4+ supports multiple network layer protocols, such as IPv6 and multicast. During negotiation, BGP peers negotiate the support for network layer protocols through the Optional parameters field.

## Slide 23: BGP Message Format: Update
Update messages are used to transmit routing information between peers. Update messages can be used to advertise and withdraw routes.
An Update message can advertise a type of routes with the same path attributes, which are placed in Network Layer Reachability Information (NLRI) fields. In addition, the Update message can carry multiple unreachable routes, which are stored in the Withdrawn Routes field.
The figure on the left shows the message format. The main fields in the message are described as follows:
  Withdrawn routes: indicates the list of unreachable routes.
  Path attributes: indicates the list of all path attributes related to NLRI. Each path attribute consists of a Type-Length-Value (TLV).
  NLRI: indicates the prefix and prefix length of a reachable route.
1 byte
Unfeasible Routes length (2 bytes)
Withdrawn Routes (N bytes)
Total path attribute length (2 bytes)
Path Attributes (N bytes)
NLRI (N bytes)
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: Unfeasible routes length: indicates the length of the Unfeasible Routes field, in bytes. If the value is 0, the Withdrawn Routes field does not exist.
Withdrawn Routes Length: indicates the length of the Withdrawn Routes field. If the value is 0, the Withdrawn Routes field is omitted.
Total path attribute length: indicates the length of the Path Attributes field, in bytes. If the value is 0, the Path Attributes field does not exist.

## Slide 24: BGP Message Format: Notification
When BGP detects an error (may occur during or after the establishment of a peer relationship), BGP sends a Notification message to the peer to notify the peer of the error cause. Then the BGP connection is interrupted immediately.
  Error Code and Error Subcode: are used to notify the peer of the specific error type.
  Data: is used to describe the detailed error content. The length is variable.
Error Code (8 bits) | Error Subcode (8 bits) | 
Data (variable length) |  | 
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 25: BGP Message Format: Keepalive
After receiving a Keepalive message from the peer, the BGP router sets the peer relationship status to Established and periodically sends Keepalive messages to maintain the connection.
The Keepalive message only contains the packet header without any other fields.
Marker (16 bytes) |  |  |  | 
Length (2 bytes) | Type (1 byte) |  |  | 
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 26: BGP Message Format: Route-refresh
Route-refresh messages are used to request the peer to resend routing information of a specified address family. In most cases, after the local end modifies a routing policy, the peer sends Update messages again. Then the local end recalculates BGP routes according to the new routing policy.
The main fields are described as follows:
  Address Family Identifier (AFI): identifies an address family, for example, IPv4.
  Res.: is reserved. The 8 bits must be set to 0.
  Subsequent Address Family Identifier (SAFI): indicates the sub-address family identifier.
AFI (16 bits) | Res (8 bits) | SAFI (8 bits)
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: During Open message negotiation, the two BGP routers negotiate whether they support route-refresh. If they support route-refresh, you can run the refresh bgp command to softly reset the BGP connection to refresh a BGP routing table without tearing down any BGP connection
If a device's peer does not support route-refresh, you can run the peer keep-all-routes command to configure the device to retain all routing updates received from the peer so that the device can refresh its routing table without tearing down the BGP connection with the peer.
By default, the device is not configured to retain all routing updates received from the peer.

## Slide 27: BGP State Machine (1)
Peer Status | Usage
Idle | Prepare TCP connections and monitor remote peers. When enabling BGP, prepare sufficient resources.
Connect | A TCP connection is being set up. Authentication is completed during the TCP connection setup. If the TCP connection fails to be established, the local end enters the Active state and attempts to establish a TCP connection repeatedly.
Active | The TCP connection fails to be set up and the local end attempts to establish a TCP connection repeatedly.
OpenSent | After the TCP connection is established, the local end sends an Open packet carrying parameters to negotiate the establishment of the peer.
OpenConfirm | After the parameter and capability negotiation succeeds, the local end sends a Keepalive message and waits for the Keepalive message from the peer end.
Established | The local end has received the Keepalive message from the peer. The capabilities of the two ends are the same after negotiation. The local end starts to use the Update message to advertise routing information.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 28: BGP State Machine (2)
Start
TCP
Established
Receive
Correct Open
Receive
Correct Keepalive
Error
Error
Error
Error
TCP
Failed
TCP
Established
Connect Retry
Timeout
Idle
Active
OpenSent
OpenConfirm
Established
Connect
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: Initially, BGP is in Idle state. In Idle state, a BGP device refuses BGP connection requests from the peer. The BGP device initiates a TCP connection with its BGP peer and changes its state to Connect only after receiving a Start event from the system.
  The Start event occurs when an operator configures a BGP process or resets an existing BGP process or when the router software resets a BGP process.
  If an error occurs in any state, for example, BGP receives a Notification message or a TCP disconnection notification, BGP returns to the Idle state.
In the Connect state, BGP starts the Connect Retry timer and waits for a TCP connection to be established:
  If the TCP connection is established, BGP sends an Open message to the peer and transitions to the OpenSent state.
  If the TCP connection fails to be established, BGP transitions to the Active state.
  If the BGP device does not receive a response from the peer before the Connect Retry timer expires, the BGP device attempts to establish a TCP connection with another peer and stays in Connect state.
In Active state, the BGP device keeps trying to establish a TCP connection with the peer.
  If the TCP connection is established, BGP sends an Open message to the peer, terminates the Connect Retry timer, and transitions to the OpenSent state.
  If the TCP connection fails to be established, BGP stays in Active state.
  If the BGP device does not receive a response from the peer before the Connect Retry timer expires, the BGP device returns to the Connect state.

## Slide 29
Notes: In OpenSent state, the BGP device waits for an Open message from the peer and then checks the validity of the received Open message, including the AS number, version, and authentication password.
  If the received Open message is valid, BGP sends a Keepalive message and transitions to the OpenConfirm state.
  If the received Open message is invalid, the BGP device sends a Notification message to the peer and returns to the Idle state.
In OpenConfirm state, the BGP device waits for a Keepalive or Notification message from the peer. If the BGP device receives a Keepalive message, it changes to the Established state. If it receives a Notification message, it returns to the Idle state.
In Established state, the BGP device exchanges Update, Keepalive, Route-refresh, and Notification messages with the peer.
  If the BGP device receives a valid Update or Keepalive message, it considers that the peer is working properly and maintains the BGP connection with the peer.
  If the BGP device receives an invalid Update or Keepalive message, it sends a Notification message to the peer and returns to the Idle state.
  If the BGP device receives a Route-refresh message, it does not change its status.
  If the BGP device receives a Notification message, it returns to the Idle state.
  If BGP receives a TCP disconnect notification, it terminates the TCP connection with the peer and returns to the Idle state.

## Slide 30: Illustration of BGP State Machine (1)
WAN
AS 300
AS 200
R1
R2
Idle state
Connect, Active
WAN
AS 300
AS 200
R1
R2
TCP SYN
Retransmit TCP SYN
…
Retransmit TCP SYN
Connect
Active
After a BGP peer is configured and the route to the peer address is found, a TCP three-way handshake is initiated. During the three-way handshake, the BGP device is in Connect state. If the TCP connection cannot be established for a long time, the BGP device enters the Active state.
There is no route to the BGP peer (common cause), so the local end remains in Idle state.
After a BGP peer is configured, the device attempts to establish a TCP connection. If the TCP connection cannot be established, the device remains in Idle state.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 31: Illustration of BGP State Machine (2)
OpenSent, OpenConfirm
Established
WAN
AS 300
AS 200
R1
R2
OpenSent
TCP Connection Established
Open
Open
After the TCP three-way handshake is complete, the local end sends an Open message to establish a peer relationship and enters the OpenSent state. After receiving an Open message from the peer end and verifying that the parameters are correct, the local end sends a Keepalive message. Then the local end enters the OpenConfirm state.
After entering the OpenConfirm state and receiving a Keepalive message from its peer, the BGP router enters the Established state. The peer relationship is then established.
OpenConfirm
WAN
AS 300
AS 200
R1
R2
Open
OpenConfirm
Keepalive
Established
Keepalive
Keepalive
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 32: BGP Peer Table
<R1>display bgp peer
BGP local router ID : 10.0.1.1
Local AS number : 100
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
10.0.12.2 4 100 25719 25714 0 0428h32m Established 1
You can run the display bgp peer command to check the BGP peer table. The parameters in the command output are described as follows:
  Peer: indicates the IP address of the peer.
  V: indicates the BGP version used on the peer.
  AS: indicates the AS number.
  Up/Down: indicates the period of time during which a BGP session keeps the current state.
  State: indicates the status of the peer.
  PrefRcv: indicates the number of route prefixes sent from the peer.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: The BGP peer table lists the BGP peer of the local device and the status of the peer.
MsgRcvd: indicates the number of received messages.
MsgSent: indicates the number of sent messages.
OutQ: indicates the message to be sent to the specified peer. The value is always 0.

## Slide 33: BGP Routing Table (1)
Run the display bgp routing-table command on the device to check the BGP routing table.
  Network: indicates the destination network address and subnet mask of the route.
  NextHop: indicates the IP address of the next hop.
To check detailed information about a route, run the display bgp routing-table ipv4-address { mask | mask-length} command. This command displays detailed information about matched BGP routes.
<R1>display bgp routing-table |  |  |  |  |  | 
BGP Local router ID is 10.0.1.1 |  |  |  |  |  | 
Status codes: * - valid, > - best, d - damped, |  |  |  |  |  | 
h - history, i - internal, s - suppressed, S - Stale |  |  |  |  |  | 
Origin : i - IGP, e - EGP, ? - incomplete |  |  |  |  |  | 
Total Number of Routes: 2 |  |  |  |  |  | 
 | Network | NextHop | MED | LocPrf | PrefVal | Path/Ogn
*>i | 10.0.45.0/24 | 10.0.4.4 | 0 | 100 | 0 | ?
* i |  | 10.0.4.4 | 0 | 100 | 0 | ?
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: The BGP routing table lists all the BGP routes discovered by the local device. If multiple routes to the same destination exist, all the routes are listed, but only one route is preferred for each destination.

## Slide 34: BGP Routing Table (2)
<R1>display bgp routing-table 10.0.45.0 24
BGP local router ID : 10.0.1.1
Local AS number : 100
Paths: 2 available, 1 best, 1 select
BGP routing table entry information of 10.0.45.0/24:
From: 10.0.2.2 (10.0.2.2) #Specify the route source.
Route Duration: 06h19m44s
Relay IP Nexthop: 10.0.12.2
Relay IP Out-Interface: GigabitEthernet0/0/0
Original nexthop: 10.0.4.4 #Specify the next-hop IP address of the route.
Qos information : 0x0
AS-path Nil, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, active, pre 255, IGP cost 2 # Indicate the path attribute and whether the path is preferred.
Originator: 10.0.4.4
Cluster list: 10.0.2.2
Not advertised to any peer yet
BGP routing table entry information of 10.0.45.0/24:
From: 10.0.3.3 (10.0.3.3)
Route Duration: 05h17m56s
Relay IP Nexthop: 10.0.12.2
Relay IP Out-Interface: GigabitEthernet0/0/0
Original nexthop: 10.0.4.4
Qos information : 0x0
AS-path Nil, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, pre 255, IGP cost 2, not preferred for peer address
Originator: 10.0.4.4
Cluster list: 10.0.3.3
Not advertised to any peer yet
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: The display bgp routing-table ipv4-address { mask | mask-length } command displays information about a BGP route with a specified IP address/mask length. The information includes the route originator, next-hop address, and route path attributes.

## Slide 35: BGP Route Generation
AS 300
R3
EBGP
IGP routing table
BGP routing table
Route
Route
Import
BGP route update
BGP Update message
1
2
Different from an IGP, BGP does not discover or calculate routes. Instead, BGP injects routes from the IGP routing table to the BGP routing table and sends Update messages carrying the routes to BGP peers.
BGP can import routes in either of the following modes:
  network
  import-route
Similar to an IGP, BGP can summarize routes based on existing routes to generate a summarized route.
AS 200
OSPF
R1
R2
R1's routing table
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 36: Importing Routes Using the network Command (1)
AS 300
R3
IGP routing table
10.1.0.0/24 OSPF
10.2.0.0/24 OSPF
BGP routing table
*>i 10.1.0.0/24
*>i 10.2.0.0/24
Import routes using the network command
1
bgp 200
network 10.1.0.0 24
network 10.2.0.0 24
Routes are imported by using the network command:
The BGP router in AS 200 has learned two routes to 10.1.0.0/24 and 10.2.0.0/24 through OSPF. The two routes are imported to the BGP process through the network command and added to the local BGP routing table.
The BGP router in AS 200 sends Update messages to advertise routes to the BGP router in AS 300.
After receiving the routes, the BGP router in AS 300 adds the two routes to the local BGP routing table.
R1's routing table
AS 200
OSPF
R1
R2
EBGP
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: The routes imported using the network command must exist in the IP routing table. Otherwise, the routes cannot be imported to the BGP routing table.

## Slide 37: Importing Routes Using the network Command (2)
AS 300
R3
EBGP
BGP route update
BGP Update
10.1.0.0/24
10.2.0.0/24
BGP routing table
*>i 10.1.0.0/24
*>i 10.2.0.0/24
R3's BGP routing table
BGP Update message
2
3
AS 200
OSPF
R1
R2
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Routes are imported by using the network command:
The BGP router in AS 200 has learned two routes to 10.1.0.0/24 and 10.2.0.0/24 through OSPF. The two routes are imported to the BGP process through the network command and added to the local BGP routing table.
The BGP router in AS 200 sends Update messages to advertise routes to the BGP router in AS 300.
After receiving the routes, the BGP router in AS 300 adds the two routes to the local BGP routing table.

## Slide 38: Importing Routes Using the import-route Command
Although the routes imported by using the network command are accurate, only one route can be imported into the IP routing table one by one. If a large number of routes are imported, the configuration commands are complex. In this case, you can use the import-route command to import the following routes to the BGP routing table:
Direct routes
Static routes
OSPF routes
IS-IS routes
AS 300
R3
IGP routing table
10.1.0.0/24 OSPF
10.3.0.0/24 Static
BGP routing table
*>i 10.1.0.0/24
*>i 10.3.0.0/24
EBGP
Import routes using the import-route command
bgp 200
import-route ospf
Import-route static
BGP route update
1
2
AS 200
OSPF
R2
R1
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 39: BGP Route Summarization
Similar to an IGP, BGP also supports manual route summarization. You can run the aggregate command in the BGP view to manually summarize BGP routes. After BGP has learned specific routes, the device will import the specified summarized routes to BGP.
AS 300
R3
EBGP
bgp 200
aggregate 10.1.0.0 22 detail-suppressed
1
Run the aggregate command on R1 to summarize routes.
AS 200
OSPF
R2
R1
BGP route update
BGP Update
10.1.0.0/22
2
R3's BGP routing table
3
BGP routing table
10.1.0.0/22
BGP routing table
10.1.1.0/24
10.1.2.0/24
10.1.3.0/24
BGP routing table
10.1.1.0/24
10.1.2.0/24
10.1.3.0/24
10.1.0.0/22
Routes before summarization on R1
Route after summarization on R1
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: After route summarization is performed, the local BGP routing table contains an additional summarized route in addition to the original specific routes.
If detail-suppressed is specified during route summarization, BGP advertises only the summarized route to the peer, but not the specific routes before route summarization.
If detail-suppressed is configured during route summarization, only BGP route to 10.1.0.0/22 is displayed in R3's routing table, and the specific routes before summarization are not displayed.

## Slide 40: Advertisement Rule
After BGP generates BGP routes using the network, import-route, or aggregate command, BGP sends Update messages carrying the BGP routes to the peer.
BGP routes are advertised according to the following rules:
  Only the optimal and valid routes are advertised.
  The routes obtained from EBGP peers are advertised to all BGP peers.
  IBGP split horizon: The routes obtained from IBGP peers are not advertised to IBGP peers.
  When a router learns a BGP route (IBGP route) from its IBGP peer, the router cannot use this route or advertise this route to its EBGP peer unless the router learns this route from an IGP. In this situation, IBGP routes and IGP routes need to be synchronized. Route synchronization is used to prevent BGP routing blackholes.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 41: BGP Route Advertisement Rule 1
Total Number of Routes: 2
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 10.1.0.0/24 11.1.0.1 0 100 0 ?
*i 11.1.0.2 0 100 0 ?
Rule 1: Only the optimal and valid routes (that is, the next-hop address is reachable) are advertised.
Run the display bgp routing-table command to check the BGP routing table.
The BGP routing table contains the optimal and valid routes with the following flags:
  *: indicates the valid route.
  >: indicates the optimal route.
AS 300
R3
R1's BGP routing table
Network Nexthop
*>i 10.1.0.0/24 11.1.0.1
*i 11.10.2
EBGP
BGP route update
BGP Update
10.1.0.0/24
BGP Update message
1
AS 200
OSPF
R2
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
R1

## Slide 42: BGP Route Advertisement Rule 2
AS 300
R4
AS 200
R2
R3
BGP routing table
*>i 10.1.0.0/24
EBGP
BGP routing table
*>i 10.1.0.0/24
BGP router in AS 300
Check the BGP routing table
BGP Update message
AS 300
EBGP
R1
IBGP
BGP routing table
*>i 10.1.0.0/24
BGP router in AS 300
Check the BGP routing table
Rule 2: The routes obtained from EBGP peers are advertised to all peers.
The routes that R2 obtains from EBGP peers are advertised to all EBGP and IBGP peers.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 43: BGP Route Advertisement Rule 3 (1)
AS 200
R1
R3
BGP Update message
IBGP
R2
IBGP
IBGP
Rule 3: The BGP routes obtained from an IBGP peer are not advertised to other IBGP peers.
This is also called IBGP split horizon.
As shown in the figure, if the routes learned by an IBGP peer are advertised to other IBGP peers, a routing loop occurs:
  R2 advertises a route to its IBGP peer R3.
  R3 advertises the received route to its IBGP peer R1.
  R1 continues to advertise the route to its IBGP peer R2.
1
2
3
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 44: BGP Route Advertisement Rule 3 (2)
AS 200
R1
R3
BGP Update message
IBGP
R2
IBGP
IBGP
Full-mesh IBGP connections
Rule 3 may bring new problems. As shown in the figure on the left, when R2 sends a route to R1, R1 cannot send the route to R3 because of the limitation of rule 3. As a result, R3 cannot learn the route.
To solve this problem, you can establish full-mesh IBGP peer relationships in an AS. Here, R2 and R3 establish an IBGP peer relationship so that R2 can advertise routes to R3.
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 45: BGP Route Advertisement Rule 4 (1)
AS 300
R5
OSPF
BGP Update message
AS 200
R1
R3
R2
IBGP
AS 100
R4
BGP routing table
*>i 10.0.4.0/24
Rule 4: When a router learns a BGP route (IBGP route) from its IBGP peer, the router cannot use this route or advertise this route to its EBGP peer unless the router learns this route from an IGP. In this situation, IBGP routes and IGP routes need to be synchronized. This rule is also called BGP synchronization rule.
In the figure:
  R4 has a route to 10.0.4.0/24, which is advertised to R2.
  R2 advertises the route to its indirectly connected IBGP peer R3.
  R3 advertises the route to R5.
  R5 initiates an access request to 10.0.4.4.
EBGP
EBGP
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship

## Slide 46: BGP Route Advertisement Rule 4 (2)
AS 300
R5
OSPF
AS 200
R1
R3
R2
IBGP
AS 100
R4
BGP routing table
R5 accesses a data packet at 10.0.4.4.
R1 does not have a route to 10.0.4.4, so it discards the packet.
R5 accesses 10.0.4.4.
  R5 searches the routing table and sends the packet to R3.
  After receiving the packet, R3 searches the routing table and finds a BGP route with the next hop being R2. R2 is an indirect next hop and needs to recurse routes. The route learned through IGP is recursed to R1. R3 sends the packet to R1.
  After receiving the packet, R1 searches the routing table. Because R1 is not a BGP router and does not establish an IBGP peer relationship with R2, R1 does not have the BGP route to 10.0.4.0/24. As a result, R1 does not find the matching route and discards the packet.
1
2
3
*>i 10.0.4.0/24
Overview
Route Generation
Protocol Entry
Advertisement Rule
Message and State Machine
Peer Relationship
Notes: The root cause of this problem is that the BGP-incapable router in AS 200 does not have the route learned from BGP. As a result, R1 fails to find the route and discards the packet. BGP synchronization is defined as follows: BGP routes are advertised only when they exist in the IGP routing table. For example, in the figure, when R3 finds that the OSPF routing table does not contain the route to 10.0.4.0/24, R3 does not advertise the route to R5. This prevents subsequent access failures.
The solutions are as follows:
  BGP routes are redistributed to an IGP. This mode is seldom used.
  Fully-mesh IBGP peer relationships are established so that all routers on the network have BGP routes.

## Slide 47
Introduction to BGP
Basic Concepts of BGP
Basic BGP Configurations

## Slide 48: BGP Configuration
[Huawei] bgp { as-number-plain | as-number-dot }
[Huawei-bgp] router-id ipv4-address
Start a BGP process, specify the local AS number, and enter the BGP view.
When running the router-id command to configure the BGP router ID, you are advised to set the BGP router ID to the IP address of the loopback interface on the device.
[Huawei-bgp] peer { ipv4-address | ipv6-address } as-number { as-number-plain | as-number-dot }
Create a BGP peer and specify the peer address and AS number.
[Huawei-bgp] peer ipv4-address connect-interface interface-type interface-number [ ipv4-source-address ]
[Huawei-bgp] peer ipv4-address ebgp-max-hop [ hop-count ]
Configure the source address used to establish the peer relationship and the maximum number of hops of an EBGP peer.
In this case, you can also specify the source address used for establishing a connection. By default, the maximum number of hops allowed for an EBGP connection is 1. That is, an EBGP connection must be established on a directly connected physical link.
Notes: If the router ID is not set, BGP selects the router ID in the system view as the router ID. For router ID selection rules in the system view, see the description about the router-id command.

## Slide 49: Configuration Example (1)
The figure shows BGP peer relationships, AS numbers, and device interconnection addresses.
The IP address of Loopback1 on each device is 10.0.x.x/32, where x is the device ID. All devices use the IP address of Loopback1 as the router ID.
R1 and R3 establish an IBGP peer relationship using the IP address of Loopback1 as the source address of a TCP connection; R3 and R4 establish an EBGP peer relationship using the IP address of the interconnected interface as the source address.
AS 100
EBGP peer
AS 200
IBGP peer
R1
R2
R3
R4
[R1] bgp 100
[R1-bgp] router-id 10.0.1.1
[R1-bgp] peer 10.0.3.3 as-number 100
[R1-bgp] peer 10.0.3.3 connect-interface LoopBack1
R1 configuration:
[R3] bgp 100
[R3-bgp] router-id 10.0.3.3
[R3-bgp] peer 10.0.1.1 as-number 100
[R3-bgp] peer 10.0.1.1 connect-interface LoopBack1
[R3-bgp] peer 10.0.34.4 as-number 200
R3 configuration:
10.0.34.3/24
OSPF
10.0.34.4/24

## Slide 50: Configuration Example (2)
The figure shows BGP peer relationships, AS numbers, and device interconnection addresses.
The IP address of Loopback1 on each device is 10.0.x.x/32, where x is the device ID. All devices use the IP address of Loopback1 as the router ID.
R1 and R3 establish an IBGP peer relationship using the IP address of Loopback1 as the source address of a TCP connection; R3 and R4 establish an EBGP peer relationship using the IP address of the interconnected interface as the source address.
R4 configuration:
AS 100
EBGP peer
AS 200
IBGP peer
R1
R2
R3
R4
10.0.34.3/24
OSPF
10.0.34.4/24
[R4] bgp 200
[R4-bgp] router-id 10.0.4.4
[R4-bgp] peer 10.0.34.3 as-number 100

## Slide 51: Configuration Example (3)
Check the BGP peer relationship on R3.
<R3> display bgp peer
BGP Local router ID : 10.0.3.3
local AS number : 100
Total number of peers : 2
Peers in established state : 2
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
10.0.1.1 4 100 0 0 0 00:00:07 Established 0
10.0.34.4 4 200 32 35 0 00:17:49 Established 0

## Slide 52
(Essay) What is the TCP destination port number used by BGP?
(Essay) What types of BGP peer relationships? What is the basis for classification?
(Multiple) Which of the following messages are used to establish a BGP peer relationship and update routes?( )
  Route-refresh
  Open
  Notification
  Update
Notes: 179
BGP peer relationships fall into IBGP and EBGP peer relationships, which are classified based on whether the two devices belong to the same AS.
B, D

## Slide 53
This course describes BGP basics, including the background of BGP, AS concept, and BGP characteristics.
This course describes the process of establishing a BGP peer relationship and the BGP state machine, which helps you understand and memorize the process.
Different from an IGP, BGP cannot discover or calculate routes by itself. Instead, routes are obtained from advertised routes in the IGP routing table.
BGP advertises routes based on the four rules, which restrict the transmission of BGP routes.