## Slide 1
Shi Miaomiao/swx791350
2020.4
New

## Slide 2: Routing Policy and Routing Control

## Slide 3
On a complex data communication network, the routing policy can be configured to filter routes and set route attributes as needed. Route control affects data traffic forwarding.
A routing policy is not a single technique or protocol, but a special technical topic or methodology that involves multiple tools and methods.
This course describes route selection tools and principles, as well as how to configure route-policies.

## Slide 4
Upon completion of this course, you will be able to:
  Use an ACL to filter routes.
  Use an IP prefix to filter routes.
  Use a filter-policy to filter routes.
  Use a route-policy to filter routes and modify route attributes.

## Slide 5
Routing Control Overview
Route Control Tool
  Route Matching Tool
  Route-Policy
Route Control Cases

## Slide 6: Technical Background
R1 imports the network segment routes of services A and B to R1, but does not import the route destined for the service C network segment. When R3 imports OSPF routes to the IS-IS routing table, R3 needs to import only the route destined for the service B network segment.
In this case, a tool is required to control routes to be imported.
R1
R2
R3
R4
GE0/0/2
10.0.34.3/24
GE0/0/3
10.0.34.4/24
GE0/0/2
10.0.12.1/24
GE0/0/3
10.0.12.2/24
GE0/0/2
10.0.23.2/24
GE0/0/3
10.0.23.3/24
Service A 172.16.1.0/24
OSPF area 0
IS-IS area 49.0001
Level-1
Service B 172.16.2.0/24
Service C 172.16.3.0/24
The route destined for the service B network segment is not imported.
The route destined for the service C network segment
is not imported.

## Slide 7: Routing Control Overview
Route control can be implemented using a route-policy. The route-policy is flexibly used in the following scenarios:
  Controlling route advertisement: A route-policy is used to filter the routes to be advertised so that a device advertises only the routes that match matching conditions.
  Controlling route receipt: A route-policy is used to filter the routes to be accepted so that a device accepts only the routes that match matching conditions.
  Controlling route import: A route-policy is used to filter the routes to be imported so that a device imports only the routes that match matching conditions.
Defining route characteristics
To match the routes against a route-policy, define a group of matching rules. The rules can base on various attributes, such as the destination address and tag value, in routing information.
Route advertisement
Route receipt
Route import
Apply

## Slide 8
Routing Control Overview
Route Control Tool
  Route Matching Tool
  Route-Policy
Route Control Cases

## Slide 9: Matching Tool 1: ACL
An access control list (ACL) is a matching tool that can match and distinguish packets and routes.
An ACL consists of multiple permit, deny, or both clauses. Each statement is a rule of the ACL. The permit or deny action in each statement is an action bound to the rule.
rule 5 permit source 1.1.1.0 0.0.0.255
acl number 2000
rule 10 deny source 2.2.2.0 0.0.0.255
rule 15 permit source 3.3.3.0 0.0.0.255
...
rule 4294967294 deny
ACL Number
User-defined rules
Implicit rule at the end of an ACL
Rule number
Action
Matching condition
(source IP address)
ACL
IP Prefix List
Notes: An ACL consists of the following elements:
  ACL number: Each ACL configured on a device is assigned a number, which is called an ACL number and is used to identify the ACL. The ACL number range varies according to the ACL type.
  Rule: As mentioned above, an ACL is usually consists of multiple permit, deny, or both clauses, and each clause is a rule of the ACL.
  Rule number: Each rule has a rule number, which identifies an ACL rule. The value can be user-defined or automatically allocated by the system. The number of an ACL rule is an integer ranging from 0 to 4294967294. All ACL rules are numbered in ascending order.
  Action: "Permit" or "deny" in each rule is an action bound to a rule. ACLs are usually used together with other technologies. The meanings of actions vary according to the scenario.
    For example, if an ACL is used together with a traffic filtering technology (the ACL is applied to the traffic filtering function), "permit" indicates that traffic is allowed to pass, and "deny" indicates that traffic is rejected.
  Item to be matched against: The ACL defines abundant items to be matched against. In this example, the source IP address is used. The ACL also supports many other items. For instance, the items can be Layer 2 Ethernet frame header information (such as a source MAC address, destination MAC address, and Ethernet frame protocol type), Layer 3 packet information (such as a destination address and protocol type), or Layer 4 packet information (such as a TCP/UDP port number).
Question: What does the rule 5 permit source 1.1.1.0 0.0.0.255 command meanh This will be introduced later.

## Slide 10: Wildcard
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 15 permit source 10.1.1.0 0.0.0.255
Wildcard
Matching rule:
  0: match; 1: no match
How do I match IP addresses within network segment 192.168.1.0/24 ?
192.168.1.1
0.0.0.255
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Exact match
No match
Network segment 192.168.1.0/24
Wildcard
A wildcard is a 32-bit string. It is used to indicate which bits must be exactly matched and which bits may not be matched in an IP address.
The wildcard is usually expressed in dotted decimal notation similar to a network mask, and its meaning is opposite to that of the network mask.
ACL
IP Prefix List
Notes: For an IP address to be matched against a matching rule, the address is followed by a 32-bit mask. The 32-bit mask is called a wildcard.
The wildcard is in dotted decimal notation. After it is converted into the binary format, value 0 indicates a "match" and value 1 indicates "no match". 1s or 0s in the wildcard may be discontinuous.
There are two examples:
  rule 5: rejects packets with source IP address 10.1.1.1. The all-0 wildcard indicates that each bit must be exactly matched. Therefore, the host IP address 10.1.1.1 matches the rule.
  rule 15: permits packets whose source IP addresses belong to network segment 10.1.1.0/24. The wildcard is 0.0.0.111111111, and the right-most 8 bits are 1, which indicates that these bits in packets can be ignored. As such, the right-most 8 bits in 10.1.1.xxxxxxxx can be any value, and the network segment 10.1.1.0/24 matches this rule.
Example: To exactly match the network segment address of 192.168.1.1/24, which wildcard can be used?
  It can be concluded that network bits must be exactly matched and host bits can be ignored. Therefore, the wildcard is 0.0.0.255.
Two special wildcards:
  The all-0 wildcard is used to exactly match a specific IP address.
  When the all-1 wildcard is used to match 0.0.0.0, it indicates that all IP addresses are matched.

## Slide 11: ACL Classification and Basic ACLs
Classification based on the ACL rule definition mode
Category | Number Range | Rule Definition
Basic ACL | 2000–2999 | Defines rules based on source IP addresses, fragment information, and validity time ranges.
Advanced ACL | 3000–3999 | Defines rules based on source IP addresses, destination IP addresses, IP protocol types, ICMP types, TCP source/destination port numbers, UDP source/destination port numbers, and time ranges.
Layer 2 ACL | 4000–4999 | Defines rules based on the Ethernet frame header information, such as the source MAC address, destination MAC address, and Layer 2 protocol type.
User-defined ACL | 5000–5999 | Defines rules based on the packet header, offsets, string masks, and user-defined strings.
User ACL | 6000–6999 | Defines rules based on the source IP address or source user control list (UCL) group of IPv4 packets, destination IP address or destination UCL group, IP protocol types, ICMP types, TCP source/destination port numbers, and UDP source/destination port numbers.
Basic ACL
IP Header | TCP/UDP Header | Data
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 15 permit source 10.1.1.0 0.0.0.255
Source IP address
ACL
IP Prefix List
Notes: Only basic ACLs can be used to match routes.

## Slide 12: ACL Fundamentals
Does an ACL to be applied exist?
Does the ACL contain rules?
Analyze the first rule.
Does the target hit the rule?
Do other rules exist?
Analyze the next rule.
Is the ACL action "permit"
or "deny"?
Result is deny.
Result is permit.
Packets do not match the rule.
Yes
Yes
No
Yes
No
No
No
Yes
permit
deny
Matching rule: The matching stops once the target is hit.
Start
End
ACL
IP Prefix List
Notes: The ACL matching mechanism is as follows:
  After a device configured with an ACL receives a packet, the device matches the packet against ACL rules one by one. If the packet does not match an ACL rule, the device attempts to match the packet against a next rule.
  Once the packet matches a rule, the device performs the action defined in the rule on the packet and no longer matches the packet against other rules.
Matching process:
The device checks whether an ACL is configured.
If no ACL is configured, the device returns the result "negative match."
If an ACL is configured, the device checks whether the ACL contains rules.
  If the ACL does not contain rules, the device returns the result "negative match."
  If the ACL contains rules, the device matches the packets against the rules in ascending order of rule IDs.
    When the packets match a permit rule, the device stops matching and returns the result "positive match (permit)."
    When the packets match a deny rule, the device stops matching and returns the result "positive match (deny)."
    If the packets do not match any rule in the ACL, the device returns the result "negative match."

## Slide 13
Notes: The ACL matching results include "positive match" and "negative match."
  Positive match: Packets match a rule in an ACL. The result is "positive match" regardless of whether packets match a permit or deny rule in an ACL.
  Negative match: No ACL exists, the ACL does not contain rules, or packets do not match any rule in an ACL.
Matching rule: The matching stops once a rule is matched.

## Slide 14: Matching Order and Result of ACL Rules
Configuration sequence (config mode)
  The system matches packets against ACL rules in ascending order by rule ID. A rule with a smaller ID is earlier to be matched.
1.1.1.1/32
1.1.1.0/24
1.1.0.0/16
1.0.0.0/8
1.1.1.1/32
1.1.1.0/24
1.1.0.0/16
acl 2000
rule 5 permit source 1.1.0.0 0.0.255.255
Object to be matched
Route entries to be matched
What does "permit" mean?
rule 5: matches route prefixes whose destination network addresses start at 1.1.
ACL
IP Prefix List
IP routing table
Matching route entries
Notes: An ACL consists of multiple deny | permit clauses, each of which describes a rule. These rules may repeat or conflict. In this situation, the matching order decides the matching result.
Huawei devices support two matching orders: automatic order (auto mode) and configured order (config mode). The configured mode is used by default.
  Automatic order: The system arranges rules according to the precision degree of the rules (depth first principle), and matches packets against the rules in descending order of precision. A rule with the highest precision defines strictest conditions, and has the highest priority. This process is complex, so we will not go into details here. Anyone interested in this can read materials after class.
  Configured order: The system matches packets against ACL rules in ascending order of rule IDs. That is, the rule with the smallest ID is processed first. This is the matching order we mentioned earlier.
    If another rule is added, the rule is added to a corresponding position, and packets are still matched against the rules in ascending order by rule ID.
Note: ACLs are always used together with other technologies. The actual functions of "permit" and "deny" vary with technologies. For example, when an ACL is used together with route filtering, "permit" means that a route is a match, and "deny" means that a route is not a match.

## Slide 15: Common Matching Examples
1.1.1.0/24
1.1.2.0/24
1.1.3.0/24
acl 2000
rule 5 permit source 1.1.2.0 0.0.0.255
1.1.2.0/24
1.1.1.0/24
1.1.2.0/24
0.0.0.0/0
acl 2000
rule 5 permit source 0.0.0.0 255.255.255.255
1.1.1.0/24
1.1.2.0/24
0.0.0.0/0
1.1.1.1/32
1.1.1.2/32
1.1.1.3/32
acl 2000
rule 5 permit source 1.1.1.1 0.0.0.254
1.1.1.1/32
1.1.1.3/32
Matches routes carrying prefix 1.1.1 and ending with an odd number.
ACL
IP Prefix List
Matches routes with prefixes starting at 1.1.2.
Matches any route.
An ACL can match only route prefixes, but not network masks.

## Slide 16: Basic Configuration Commands of Basic ACLs
[Huawei] acl [ number ] acl-number [ match-order config ]
Create a basic ACL.
Create a numbered basic ACL (2000–2999) and enter the basic ACL view.
[Huawei] acl name acl-name { basic | acl-number } [ match-order config ]
Create a named basic ACL and enter the basic ACL view.
[Huawei-acl-basic-2000] rule [ rule-id ] { deny | permit } [ source { source-address source-wildcard | any } | time-range time-name ]
Configure an ACL rule.
You can run this command in the basic ACL view to configure rules for the basic ACL.
ACL
IP Prefix List
Notes: Create a basic ACL.
[Huawei] acl [ number ] acl-number [ match-order config ]
  acl-number: specifies the number of an ACL.
  match-order config: indicates the matching order of ACL rules. config indicates the configuration order.
[Huawei] acl name acl-name { basic | acl-number } [ match-order config ]
  acl-name: specifies the name of an ACL.
  basic: indicates a basic ACL.
Configure a basic ACL rule.
[Huawei-acl-basic-2000] rule [ rule-id ] { deny | permit } [ source { source-address source-wildcard | any } | time-range time-name ]
  rule-id: specifies the ID of an ACL rule.
  deny: rejects packets that meet the matching conditions.
  permit: permits the packets that meet the matching conditions.

## Slide 17
Notes:   source {source-address source-wildcard | any}: specifies the source IP address of the packets that match the ACL rule. If no source IP address is specified, packets with any source IP address are matched. In the preceding information:
    source-address: specifies the source address of packets.
    source-wildcard: specifies the wildcard of the source IP address.
    any: indicates any source IP address of packets. That is, source-address is 0.0.0.0 or source-wildcard is 255.255.255.255.
  time-range time-name: specifies the time range during which an ACL rule takes effect. time-name specifies the name of a time range during which the ACL rule takes effect. If no time range is specified, the rule takes effect at any time.

## Slide 18: Matching Tool 2: IP Prefix List
An IP prefix list is a filter that uses the network address and mask length of routes as matching rules. An IP prefix list can be used when a routing protocol advertises or receives routes.
Different from an ACL, an IP prefix list can match both the IP address prefix length and mask length, which enhances matching accuracy.
ACL
IP Prefix List
[Huawei] ip ip-prefix test index 10 permit 192.168.1.0 22 greater-equal 24 less-equal 26
ip-prefix-name
No.
Action
Mask range
IP network segment and mask
1. ip-prefix-name: specifies the name of an IP prefix list.
2. Sequence number: indicates the sequence number of a matching entry in the IP prefix list. The IP prefixes are matched in ascending order by sequence number.
3. Action: permit or deny, indicating match or mismatch.
4. IP network segment and mask: match the network address of a route and exactly match the leftmost N bits of the network address.
5. Mask length range: mask-length <= greater-equal-value <= less-equal-value <= 32

## Slide 19: IP-Prefix Fundamentals
Start
Analyze the first Index entry.
Is the route to be matched within the defined range?
Do other index entries exist?
Analyze the next index entry.
Is the action "permit"
or "deny"?
The matching result is deny.
The matching result is permit.
End
Yes
No
permit
deny
Sequence matching
Yes
No
Unique match
Denied by default
ACL
IP Prefix List

## Slide 20: Example of IP-Prefix Matching
1.1.1.1/32
1.1.1.0/27
1.1.1.0/26
1.1.1.0/25
1.1.1.0/24
1.1.1.0/27
1.1.1.0/26
1.1.1.0/25
1.1.1.0/24
ip ip-prefix List1 index 10 permit
1.1.1.0 24 greater-equal 24 less-equal 27
Object to be matched
Matched route entries
The preceding IP prefix list matches the routes whose left-most 24 bits in the network address are the same as those in 1.1.1.0 and whose network mask length is greater than or equal to 24 and less than or equal to 27. As such, 1.1.1.1/32 does not match the IP prefix list.
IP routing table
Matching route entries
ACL
IP Prefix List

## Slide 21: Basic Configuration Commands of an IP Prefix List
[Huawei] ip ip-prefix ip-prefix-name [ index index-number ] { permit | deny } ipv4-address mask-length [ match-network ] [ greater-equal greater-equal-value ] [ less-equal less-equal-value ]
Create an IPv4 prefix list.
Create an IPv4 prefix list or add an entry to the IPv4 prefix list.
ACL
IP Prefix List
ip-prefix-name: specifies the name of an IP prefix list.
index index-number: specifies the index of a matching entry in the IP prefix list.
permit: indicates that the matching mode of the IP prefix list is permit.
deny: indicates that the matching mode of the IP prefix list is deny.
ipv4-address mask-length: specifies the IP address and mask length.
greater-equal greater-equal-value: specifies the lower limit of the matching range of the mask length.
less-equal less-equal-value: specifies the upper limit of the matching range of the mask length.
Notes: ip-prefix-name: specifies the name of an IP prefix list. The value is a string of 1 to 169 case-sensitive characters, spaces not supported.
index index-number: specifies the index of a matching entry in the IP prefix list. The value is an integer ranging from 0 to 4294967295. By default, the sequence number increases by 10 each time an entry is added and is automatically indexed. If the system automatically assigns an index, the index starts at 10.
permit: indicates that the matching mode of the IP prefix list is permit. In this mode, if the IP address to be filtered is within the defined range, the IP address passes the filtering. If no match is found, the system moves to a next node.
deny: indicates that the matching mode of the IP prefix list is deny. In this mode, if the IP address to be filtered is within the defined range, the IP address fails to pass the filtering and cannot be matched against a next node. If the IP address is out of the range, the system moves to a next node.
ipv4-address mask-length: specifies the IP address and mask length. The mask-length value is an integer ranging from 0 to 32.

## Slide 22
Notes: greater-equal greater-equal-value: specifies the lower limit of the matching range of the mask length. If neither greater-equal greater-equal-value nor less-equal less-equal-value is specified, mask-length is used as the mask length.
  The greater-equal-value setting must meet the following formula: mask-length <= greater-equal-value <= less-equal-value <= 32.
  If only greater-equal is set, the mask length ranges from greater-equal-value to 32.
less-equal less-equal-value: specifies the upper limit of the matching range of the mask length. If neither greater-equal greater-equal-value nor less-equal less-equal-value is specified, mask-length is used as the mask length.
  The less-equal-value setting must meet the following formula: mask-length <= greater-equal-value <= less-equal-value <= 32.
  If only less-equal is configured, the mask length ranges from mask-length to less-equal-value.

## Slide 23: IP Prefix Configuration Example (1)
Single-Statement Matching
  Case 1: The route 10.1.1.0/24 is permitted, and other routes are rejected.
  Case 2: All routes are rejected.
ip ip-prefix aa index 10 permit 10.1.1.0 24
ACL
IP Prefix List
10.1.0.0/16
10.1.1.0/24
10.1.1.0/26
10.1.1.1/32
10.2.2.0/24
OSPF
R1
R2
R3
Routes
ip ip-prefix bb index 10 deny 10.1.1.0 24
Use an IP prefix list to filter routes.
Notes: Case1: This is the single-node exact matching. Only the route of the specified destination address and mask can match the IP prefix. In addition, the matching mode of the node is permit. As such, the route 10.1.1.0/24 matches the node and is permitted, and the other routes are rejected because they fail to match the IP prefix.
Case 2: This is the single-node exact matching, and the matching mode of the node is deny. As such, the route 10.1.1.0/24 matches the node and is rejected, and other routes are rejected by default because they do not match the IP prefix.

## Slide 24: IP Prefix Configuration Example (2)
Multi-Statement Matching
  Case 1: The route 10.1.1.0/24 is rejected, the route 10.1.1.1/32 is permitted, and other routes are rejected.
  Case 2: Routes 10.1.1.0/26 and 10.1.1.1/32 are permitted, and the other routes are rejected.
ip ip-prefix aa index 10 deny 10.1.1.0 24
ip ip-prefix aa index 20 permit 10.1.1.1 32
ACL
IP Prefix List
ip ip-prefix bb index 10 permit 10.1.1.0 24 greater-equal 26 less-equal 32
10.1.0.0/16
10.1.1.0/24
10.1.1.0/26
10.1.1.1/32
10.2.2.0/24
OSPF
R1
R2
R3
Routes
Use an IP prefix list to filter routes.
Notes: Case 1: This is the multi-node exact matching.
  When the route 10.1.1.0/24 is matched against index 10, the route meets the matching condition but is rejected because the matching mode is deny.
  The route 10.1.1.1/32 does not match index 10 and continues to be matched against index 20. The matching is successful, and the matching mode of index 20 is permit, indicating that the route is permitted.
  Other routes are rejected by default because they do not meet the conditions of indexes 10 and 20.
Case 2: In this case, greater-equal-value is 26, and less-equal-value is 32. The setting must meet the following formula: mask-length <= greater-equal-value <= less-equal-value. Otherwise, the configuration fails.

## Slide 25: IP Prefix Configuration Example (3)
Wildcard address matching
  Case 1: All routes with the mask length ranging from 8 to 32 bits are permitted.
  Case 2: The route 10.1.0.0/16 is permitted, and other routes are rejected.
ip ip-prefix aa index 10 permit 10.0.0.0 8 less-equal 32
ACL
IP Prefix List
ip ip-prefix bb index 10 deny 10.1.1.0 24 less-equal 32
ip ip-prefix bb index 20 permit 10.1.0.0 16 less-equal 32
10.1.0.0/16
10.1.1.0/24
10.1.1.0/26
10.1.1.1/32
10.2.2.0/24
OSPF
R1
R2
R3
Routes
Use an IP prefix list to filter routes.
Notes: Case 1: In this case, greater-equal-value is 8, less-equal-value is 32, routes whose left-most 8 bits match those in 10.0.0.0 and with the mask length ranging from 8 to 32 bits match the IP prefix.
Case 2:
  For index 10, greater-equal-value is 24, and less-equal-value is 32. Routes whose the left-most 24 bits match those in 10.1.1.0 and with the mask length ranging from 24 to 32 bits are rejected.
  For index 20, greater-equal-value is 0, and less-equal-value is 32. Routes whose left-most 16 bits match those in 10.1.0.0, and with the mask length ranging from 16 to 32 bits match the prefix. In this case, only the route 10.1.0.0/16 is a match, and the other routes are rejected by default.

## Slide 26
Routing Control Overview
Route Control Tool
  Route Matching Tool
  Route-Policy
Route Control Cases

## Slide 27: Policy Tool 1: Filter-Policy
The filter-policy is a common tool for filtering routing information. It can filter routes to be accepted, advertised, and imported. The filter-policy applies to IS-IS, OSPF, and BGP.
As shown in the preceding figure, BGP runs between R1, R2, and R3. Routes are transmitted between devices. To filter certain routing information as needed, you can use the filter-policy.
Filter-Policy
Route-Policy
BGP
R1
R2
R3
10.1.1.0
10.1.2.0
10.1.3.0
10.1.1.0
10.1.2.0
10.1.3.0
Filter-Policy

## Slide 28: Filter-Policy Application in Distance-Vector Routing Protocols
In distance-vector routing protocols, routing information is transmitted between devices. To filter such information, you can use filter-policies. The following figure shows the locations where the filter-policies take effect in the inbound and outbound directions.
Database
IP routing table
Database
IP routing table
filter-policy export
Routing information
Routing information
Routing information
filter-policy import
R1
R2
Filter-Policy
Route-Policy
Notes: A distance-vector protocol generates routes based on the routing table. Consequently, the filter affects the routes to be accepted from neighbors and the routes to be advertised to neighbors.
To filter out the routes from an upstream device to a downstream device, run the filter-policy export command on the upstream device or the filter-policy import command on the downstream device.

## Slide 29: Filter-Policy Application in Link-State Routing Protocols
In a link-state routing protocol, routing devices exchange LSAs, and then calculate entries in the routing table based on LSDB information summarized from the LSAs. A filter-policy, however, can filter routes but not LSAs.
LSDB
IP routing table
LSDB
IP routing table
filter-policy export
LSA
LSA
LSA
filter-policy import
Locally originated Type 5 LSA
Import filtering:
Do not add routes to the routing table.
Export filtering:
Filtering routes
Filtering routes to be imported from other protocols
R1
R2
Filter-Policy
Route-Policy
Notes: OSPF stores the flooded LSAs in its LSDB and runs the SPF algorithm to calculate a loop-free SPT with the local device as the root. The filter-policy module filters the routes calculated by OSPF (before the routes are installed into the routing table) but does not filter LSAs.
The preceding example uses OSPF to show how a filter-policy is applied in a link-state routing protocol.

## Slide 30: Basic Configuration Commands of a Filter-Policy (1)
[Huawei-ospf-100] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name [ secondary ] } import
Application in OSPF
Configure a filter-policy to filter routes to be accepted by OSPF.
Filter-Policy
Route-Policy
[Huawei-ospf-100] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export [ protocol [ process-id ] ]
Filter the imported routes to be advertised based on the filter-policy.
Notes: Command: [Huawei-ospf-100] filter-policy {acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name [secondary]} import
  acl-number: specifies the number of a basic ACL. The value is an integer ranging from 2000 to 2999.
  acl-name acl-name: specifies the name of an ACL. The value is a string of 1 to 32 case-sensitive characters, spaces not supported. The value must start with a letter (a to z or A to Z).
  ip-prefix ip-prefix-name: specifies the name of an IP prefix list. The value is a string of 1 to 169 case-sensitive characters, spaces not supported. If spaces are used, the string must start and end with double quotation marks (").
  route-policy route-policy-name: specifies the name of a route-policy. The value is a string of 1 to 40 case-sensitive characters, spaces not supported. If spaces are used, the string must start and end with double quotation marks (").
  secondary: indicates that the sub-optimal route is selected.
Command: [Huawei-ospf-100] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export [ protocol [ process-id ] ]
  protocol process-id: specifies the protocol whose routes are to be filtered. Currently, the value can be direct, isis, bgp, ospf, unr, or static. When RIP, IS-IS, or OSPF is specified as a routing protocol, you can also specify a process ID. The value is an integer ranging from 1 to 65535. The default value is 1.

## Slide 31: Basic Configuration Commands of a Filter-Policy (2)
[Huawei-isis-1] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } import
Application in IS-IS
Configure a filter-policy to filter IS-IS routes to be added to the IP routing table.
Filter-Policy
Route-Policy
[Huawei-isis-1] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export [ protocol [ process-id ] ]
Configure a filter-policy for IS-IS to filter imported routes to be advertised.

## Slide 32: Basic Configuration Commands of a Filter-Policy (3)
[Huawei-bgp-af-ipv4] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name } import
Application in BGP
Configure a filter-policy to filter routes to be accepted by BGP.
Filter-Policy
Route-Policy
[Huawei-bgp-af-ipv4] filter-policy { acl-number | acl-name acl-name | ip-prefix ip-prefix-name } export [ protocol [ process-id ] ]
Configure a filter-policy to filter routes to be advertised. Only the routes that pass the filtering can be advertised by BGP.
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address } filter-policy { acl-number | acl-name acl-name } { import | export }
Configure a filter-policy to filter routes to be advertised to or accepted from a specified peer or peer group.

## Slide 33: Applying a Filter-Policy to OSPF
R1
R2
ospf 1
filter-policy 2000 import
R1
R2
ospf 1
import-route static
filter-policy 2000 export
The filter-policy import command configures a filter-policy to filter routes to be accepted. Only the routes that pass the filter-policy are added to the routing table. The routes that do not pass the filter-policy are not added to the routing table, but they can be advertised.
After OSPF imports external routes using the import-route command, to prevent routing loops, you can run the filter-policy export command to filter the imported routes to be advertised. Only the external routes that meet the filtering conditions are translated into Type 5 LSAs (AS-external-LSAs) and then advertised.
Filter-Policy
Route-Policy
filter-policy import
filter-policy export
LSA 1
LSA 2
LSA 3
LSA 4
LSA 1
LSA 2
LSA 3
LSA 4
172.16.1.0/24
172.16.2.0/24
172.16.3.0/24
172.16.1.0/24
172.16.2.0/24
172.16.3.0/24
R1's routing table
10.1.1.0 24
10.1.2.0 24
10.1.3.0 24
10.1.4.0 24
R2's routing table
10.1.1.0 24
10.1.2.0 24
10.1.3.0 24
Link state information
Notes: OSPF routing information is recorded in the LSDB. The filter-policy import command is used to filter the routes calculated by OSPF, but not to filter LSAs to be accepted or advertised.
The filter-policy export command allows you to specify a protocol or process ID to filter the routes of a specified protocol or a specified process. If neither protocol nor process-id is specified, OSPF filters all imported routes.

## Slide 34: Applying a Filter-Policy to IS-IS
filter-policy import
R1
R2
isis
filter-policy 2000 import
Similar to usage in OSPF, the filter-policy import command affects only the local routing table. That is, the matching routes are not added to the routing table, and the LSP flooding and LSDB synchronization of the local device are not affected.
filter-policy export
LSP 1
LSP 2
LSP 3
LSP 4
LSP 1
LSP 2
LSP 3
LSP 4
R1
R2
Isis 1
import-route bgp
filter-policy 2000 export
BGP
IS-IS
BGP routing table
IS-IS routing table
If IS-IS and other routing protocols are deployed on a network and a boundary device has imported routes from other routing protocols, the boundary device advertises all imported external routes to its IS-IS neighbors by default. To advertise only the imported external routes to neighbors, run the filter-policy export command.
Link state information
Filter-Policy
Route-Policy
R1's routing table
10.1.1.0 24
10.1.2.0 24
10.1.3.0 24
10.1.4.0 24
R2's routing table
10.1.1.0 24
10.1.2.0 24
10.1.3.0 24
Notes: IS-IS routing entries can be used to guide IP packet forwarding only after they are successfully delivered to the IP routing table. If an IS-IS routing table has routes destined for a specific network segment but these routes do not need to be added to the IP routing table, run the filter-policy import command and use a basic ACL, an IP prefix list, or a route-policy to filter the IS-IS routes to be added to the IP routing table.

## Slide 35: Applying a Filter-Policy to BGP
filter-policy import
R1
R2
bgp 100
ipv4-family unicast
filter-policy 2000 import
The filter-policy import command can be used to filter the routes to be accepted by BGP globally and determine whether to add the routes to the BGP routing table.
filter-policy export
The filter-policy export command is used to filter the routes to be advertised. Only the routes that pass the filtering can be added to the local BGP routing table and advertised by BGP.
AS 100
BGP Update
NLRI: Route-entry 1
NLRI: Route-entry 2
BGP Update
NLRI: Route-entry 1
R1
R2
bgp 100
ipv4-family unicast
filter-policy 2000 export
AS 100
BGP Update
NLRI: Route-entry 1
NLRI: Route-entry 2
BGP Update
Filter-Policy
Route-Policy
R1's routing table
10.1.1.0 24
10.1.2.0 24
R2's routing table
10.1.1.0 24
R1's routing table
10.1.1.0 24
10.1.2.0 24
10.1.3.0 24

## Slide 36: Policy Tool 2: Route-Policy
A route-policy is a policy tool used to filter routes and set route attributes for the filtered routes.
A route-policy consists of one or more nodes. Each node can be a set of conditional statements (matching conditions) and executive statements (actions). These statements are arranged in ascending order by sequence number.
Filter-Policy
Route-Policy
Node 1 (matching mode: permit)
Conditional statement
Executive statement
Node 2 (matching mode: permit)
Conditional statement
Executive statement
Node N (matching mode: permit)
Conditional statement
Executive statement
...
Top-Down
route-policy test
Each node contains multiple conditional statements. The relationship between multiple conditional statements on a node is AND. The action on the node is executed only when all conditional statements are met.
The relationship between nodes is OR. The route-policy is executed in ascending order by node ID. A node in a route-policy will not be further matched.
Notes: When a route-policy is used, the node with a smaller ID is matched first. After a route matches a node, the route is not matched against other nodes. If a route fails to match all nodes, the route is filtered out.

## Slide 37: Components of a Route-Policy
A route-policy consists of one or more nodes. Each node contains multiple if-match and apply clauses.
route-policy test permit node 10
if-match x1
if-match x2
apply y1
route-policy test permit node 20
if-match x3 x4
apply y2
route-policy test permit node N
if-match xn
apply yn
...
permit or deny: The matching mode of a route-policy node is "permit" or "deny".
node: specifies the node ID of a route-policy. The value is an integer ranging from 0 to 65535.
if-match clause: defines the matching condition of a node.
apply clause: defines an action to be performed on a matching route.
Route-policy name
Matching mode of a node
Node ID
Conditional statement
Executive statement
Filter-Policy
Route-Policy

## Slide 38: Matching Order for a Route-Policy
Route-policies use different matching conditions and modes to select routes and change route attributes.
route-policy
node 10
If-match
If-match
...
Matching mode
apply
apply
...
Match the route-policy.
...
node N
If-match
If-match
...
Matching mode
apply
apply
...
Match the route-policy.
Deny
Deny
Deny
Meet all conditions.
Match
all conditions.
permit
permit
deny
deny
Meet only some conditions.
Meet only some conditions.
Sequence matching
Unique match
Filter-Policy
Route-Policy
Notes: A route-policy contains N (N >= 1) nodes. After routes match the route-policy, the system checks whether the routes match the nodes in ascending order by node ID. The matching condition is defined in the if-match clause.
  After a route matches all if-match clauses of a node, the system proceeds to select a matching mode and no longer matches the route against other nodes. The matching mode can be "permit" or "deny."
    permit: The route is permitted, and the apply clause of the node is used to set some attributes of the route.
    deny: The route is rejected.
  If a route fails to match any if-match clause of the node, the route is further matched against the next node. If a route does not match any node, the route is rejected.

## Slide 39: Basic Configuration Commands of a Route-Policy (1)
[Huawei] route-policy route-policy-name { permit | deny } node node
Create a route-policy.
Create a route-policy and enter the route-policy view.
Filter-Policy
Route-Policy
[Huawei-route-policy] if-match ?
acl: matches a basic ACL.
cost: matches the cost of a route.
interface: matches the outbound interface in a route.
ip-prefix: matches a prefix list.
...
(Optional) Configure if-match clauses.
Notes: Command: route-policy route-policy-name { permit | deny } node node
  permit: sets the matching mode of a route-policy node to permit. If a route matches all if-match clauses of a node, the apply clause of the node is executed. Otherwise, the system goes to the next node.
  deny: indicates that the matching mode of the route-policy node is deny. If a route matches all if-match clauses of a node, the route is rejected. Otherwise, the system goes to the next node.
  node node: specifies the node ID of a route-policy. When a route-policy is used, the node with the smallest node ID is matched first. After a route matches a node, the route is not matched against other nodes. If a route fails to match any nodes, the route is filtered out. The value is an integer ranging from 0 to 65535.

## Slide 40: Basic Configuration Commands of a Route-Policy (2)
[Huawei-route-policy] apply ?
cost: sets the cost of a route.
cost-type {type-1 | type-2}: sets the OSPF cost type.
ip-address next-hop: sets the next-hop address for an IPv4 route.
preference: sets the preference of a routing protocol.
tag: sets the tag field in routing information.
...
(Optional) Configure an apply clause.
Filter-Policy
Route-Policy
Notes: The apply clause is used to specify an action for the route-policy and set the attributes of the routes that match the route-policy. If no apply clause is configured for a node, the node only filters routes. If one or more apply clauses are configured, all apply clauses are applied to the routes that match the node.

## Slide 41
Routing Control Overview
Implementation of Route Control
  Route Matching Tool
  Route-Policy
Route Control Cases

## Slide 42: Filtering Received Routes
OSPF area 0
R1
R2
R3
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
192.168.4.0/24
OSPF runs on R1, R2, and R3. R1 advertises the routes 192.168.1.0/24, 192.168.2.0/24, 192.168.3.0/24, and 192.168.4.0/24 to OSPF.
It is required that R2 cannot access network segment 192.168.1.0/24 on R1, but R3 can.
To meet this requirement, you can use a filter-policy to filter the received routes on R2.
[R2] ip ip-prefix in index 10 permit 192.168.2.0 24
[R2] ip ip-prefix in index 20 permit 192.168.3.0 24
[R2] ip ip-prefix in index 30 permit 192.168.4.0 24
[R2] ospf
[R2-ospf-1] filter-policy ip-prefix in import
The configuration of R2 is as follows:
Note: Basic network configurations are not provided.
Notes: When a filter-policy is used to filter routes, only the local routing table is affected. Therefore, R3 can learn the routes to network segment 192.168.1.0/24.

## Slide 43: Filtering Routes to Be Advertised
R1
R2
R3
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
192.168.4.0/24
Introduce direct routes.
OSPF runs on R1, R2, and R3. R1 imports the direct routes 192.168.1.0/24, 192.168.2.0/24, 192.168.3.0/24, and 192.168.4.0/24 to OSPF.
It is required that R2 and R3 learn only the routes to 192.168.1.0/24 and not the routes to the other three network segments.
To meet this requirement, configure a filter-policy on R1 to filter the imported routes to be advertised.
[R1] ip ip-prefix out index 10 permit 192.168.1.0 24
[R1] ospf
[R1-ospf-1] import-route direct
[R1-ospf-1] filter-policy ip-prefix out export
The configuration of R1 is as follows:
OSPF area 0
Note: Basic network configurations are not provided.

## Slide 44: Modifying Route Attributes
192.168.1.0/24
R1
R2
R3
Import direct connections.
OSPF runs on R1, R2, and R3. R1 imports the direct route 192.168.1.0/24 to OSPF.
It is required that the OSPF route 192.168.1.0/24 learned by R2 and R3 be an external Type 1 route. By default, the route is an external Type 2 route.
To meet this requirement, you can use a route-policy on R1 to change the type of external routes to external Type 1 when routes are imported.
[R1] ip ip-prefix external index 10 permit 192.168.1.0 24
[R1] route-policy RP permit node 10
[R1-route-policy] if-match ip-prefix external
[R1-route-policy] apply cost-type type-1
[R1-route-policy] quit
[R1] ospf
[R1-ospf-1] import-route direct route-policy RP
The configuration of R1 is as follows:
Note: Basic network configurations are not provided.
OSPF area 0

## Slide 45: Dual-Node Bidirectional Route Import
Bidirectional route import refers to the process in which boundary routers in two routing domains imports routes into each other.
If two border routers are on the borders of two routing domains and bidirectional route import is performed on both border routers, this is called dual-node bidirectional route import.
Dual-node bidirectional route import is a typical routing model. Single-node bidirectional route import lacks redundancy. Once a single-node border router is faulty, communication between two routing domains may fail. Therefore, dual-node bidirectional route import is generally used in large-scale network deployment.
Although this function enhances network reliability, it may cause problems, such as sub-optimal paths and routing loops.
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
10.4.4.0/24
Import OSPF routes to IS-IS.
Import IS-IS routes to OSPF.

## Slide 46: Suboptimal Path Problem
10.1.1.0/24
The following uses the direct route 10.1.1.0/24 as an example:
  R1 imports the direct route 10.1.1.0/24 to OSPF.
  R2 and R3 re-advertise bidirectional routes. R2 re-advertises the route 10.1.1.0/24 to IS-IS, and R3 learns the IS-IS route from R4.
  For R3, the IS-IS route with preference 15 is preferred over the OSPF external route with preference 150. Therefore, the IS-IS route from R4 is preferred. The path through which R3 accesses the network segment 10.1.1.0/24 is R3 -> R4 -> R2 -> R1, which is the second optimal path.
OSPF
R1
R2
R3
R4
IS-IS
Import direct routes.
2
2
1
3
3
OSPF LSA
IS-IS LSP
Suboptimal Path
Routing Loop
Destination/Mask Proto Pre
10.1.1.0/24 ISIS 15
Access traffic

## Slide 47: Solving the Suboptimal Path Problem (1)
Destination/Mask Proto Pre
10.1.1.0/24 OSPF 150
Solution 1: In the IS-IS process of R3, configure a filter-policy to prevent the route 10.1.1.0/24 sent by R4 from being added to the local routing table.
Perform the following operations on R3:
[R3] acl 2001
[R3-acl-basic-2001] rule 5 deny source 10.1.1.0 0
[R3-acl-basic-2001] rule 10 permit
[R3] isis
[R3-isis-1] filter-policy 2001 import
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
Access traffic
Suboptimal Path
Routing Loop
Import direct routes.
1

## Slide 48: Solving the Suboptimal Path Problem (2)
Solution 2: Configure an ACL on R3 to match the route 10.1.1.0/24, apply the ACL to the route-policy, and set the preference of the route that matches the ACL to 14 (higher than IS-IS). Run the preference ase command in the OSPF view to invoke the route-policy to change the preference of external routes.
Perform the following operations on R3:
[R3]acl 2000
[R3-acl-basic-2000] rule permit source 10.1.1.0 0
[R3-acl-basic-2000] quit
[R3]route-policy hcip permit node 10
[R3-route-policy] if-match acl 2000
[R3-route-policy] apply preference 14
[R3-route-policy] quit
[R3]ospf 1
[R3-ospf-1] preference ase route-policy hcip
Destination/Mask Proto Pre
10.1.1.0/24 OSPF 14
10.1.1.0/24
OSPF
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
Access traffic
Suboptimal Path
Routing Loop
Import direct routes.
1
R1

## Slide 49: Routing Loops
Suboptimal Path
Routing Loop
10.1.1.0/24
OSPF
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
4
4
Scenario description:
  Import the direct route 10.1.1.0/24 to OSPF on R1.
  Configure OSPF on R1, R2, and R3. The route to the network segment 10.1.1.0/24 is advertised in the entire OSPF area.
  R2 re-advertises bidirectional routes.
  Configure IS-IS on R2, R3, and R4. The route to the network segment 10.1.1.0/24 is advertised in the entire IS-IS domain.
  R3 re-advertises bidirectional routes.
  The route destined for the network segment 10.1.1.0/24 is advertised to the OSPF area again, forming a routing loop.
Destination/Mask Proto Pre
10.1.1.0/24 ISIS 15
Import direct routes.
1
R1

## Slide 50: Preventing Routing Loops (1)
Solution 1: Configure a route-policy on R3 to filter out the route destined for 10.1.1.0/24 when OSPF imports IS-IS routes.
Perform the following operations on R3:
[R3] acl 2001
[R3-acl-basic-2001] rule 5 deny source 10.1.1.0 0
[R3-acl-basic-2001] rule 10 permit
[R3] route-policy RP permit node 10
[R3-route-policy] if-match 2001
[R3-route-policy] quit
[R3] ospf
[R3-ospf-1] import-route isis 1 route-policy RP
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
Suboptimal Path
Routing Loop
Destination/Mask Proto Pre
10.1.1.0/24 OSPF 150
Import direct routes.
1

## Slide 51: Preventing Routing Loops (2)
Solution 2: Use tags to implement selective route import. Add tag 200 to the route 10.1.1.0/24 imported from OSPF to IS-IS on R2, and filter the route with tag 200 when importing the route from IS-IS to OSPF on R3.
Perform the following operations on R2:
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
Using a route-policy to filter routes with tag 200
Configure a route-policy.
Add tag 200 to the route 10.1.1.0/24.
Suboptimal Path
Routing Loop
[R2]acl 2000
[R2-acl-basic-2000]rule permit source 10.1.1.0 0
[R2-acl-basic-2000]quit
[R2]route-policy hcip permit node 10
[R2-route-policy]if-match acl 2000
[R2-route-policy]apply tag 200
[R2-route-policy]quit
[R2]isis 1
[R2-isis-1]import-route ospf route-policy hcip
Import direct routes.
1

## Slide 52: Preventing Routing Loops (3)
Perform the following operations on R3:
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
2
2
3
3
OSPF LSA
IS-IS LSP
Using a route-policy to filter routes with tag 200
Configure a route-policy.
Add tag 200 to the route 10.1.1.0/24.
Suboptimal Path
Routing Loop
[R3]route-policy hcip deny node 10
[R3-route-policy]if-match tag 200
[R3-route-policy]quit
[R3]route-policy hcip permit node 20
[R3]ospf 1
[R3-ospf-1]import-route isis route-policy hcip
Although IP prefix-based route filtering can be used for route re-advertisement, the involved configuration workload is heavy on a large network. Instead of using IP prefixes, setting tags greatly reduces the configuration workload.
Import direct routes.
1

## Slide 53: Thinking About the Following Scenario
10.1.1.0/24
OSPF
R1
R2
R3
R4
IS-IS
10.4.4.0/24
Suboptimal Path
Routing Loop
On R1, import the network segment route 10.1.1.0/24 to OSPF; on R4, import the network segment route 10.4.4.0/24 to IS-IS; on R2 and R3, import routes bidirectionally. In this scenario, how can we prevent routing loops by setting tags?

## Slide 54
(Essay) What are the functions of export filter-policies in OSPF and BGP?
(Essay) What is the logical relationship between nodes in a route-policy? What is the logical relationship between multiple conditional statements on a node?
Notes: In OSPF, the export filter-policy is used to filter the routes to be imported from other routing protocols to OSPF. In BGP, the export filter-policy is used to filter routes to be advertised.
The logical relationship between nodes is OR, and the logical relationship between conditional statements is AND.

## Slide 55
To control the advertisement and receipt of routes, use a tool to obtain routes. The most common tools are ACL and IP prefix list.
Both filter-policies and route-policies can be used to filter routes to be accepted or advertised. Note that the use of filter-policies in link-state routing protocols cannot filter link state information, but affects only the local routing table.
Before a device accepts or advertises routes, the device can use a route-policy to flexibly modify route attributes to meet route control requirements.