## Slide 1
He Junjian/hwx580230
2020.3.24
Zhu Shigeng/00261992
New

## Slide 2: Introduction to Typical Campus Network Technologies

## Slide 3
The networks that are constructed in scenarios such as factories, government agencies, shopping malls, office buildings, school campuses, and parks to implement network interconnection are all called campus networks. Campus networks vary depending on industry attributes. However, a campus network is typically divided into the egress layer, core layer, aggregation layer, and access layer.
This course describes the overall architecture of a campus network, common technologies and protocols used at each layer of the network, and typical networking scenarios.
Notes: Other courses have illustrated various routing protocols, which are not provided here.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the typical architecture of a large-scale campus network.
  Describe common Ethernet switching technologies.
  Describe common WLAN application scenarios.
  Describe common technologies used to ensure campus network reliability.
  Describe common technologies used for campus network service and management.
  Describe common technologies used to ensure campus network security.
  Describe common VPN technologies used on campus networks.

## Slide 5
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 6: Many Campuses Exist in a City
5h&22h
90%+
80%+
90%+
City residents work and live in campuses.
GDP is created in campuses.
Innovations are made in campuses.
Daily smart terminal usage time & time in the campus every day

## Slide 7: Introduction to a Campus Network
A campus network is an internal network of an enterprise or organization.
A campus network is built to ensure that enterprise or organization services are running efficiently.
Campus networks can be classified into the following types based on the scale:
  Large-sized campus network: number of terminal users > 2000, number of NEs > 100
  Medium-sized campus network: 2000 > number of terminal users > 200, 100 > number of NEs > 25
  Small-sized campus network: number of terminal users < 200, number of NEs < 25
Some enterprises have branches dispersed in different areas. Each branch network can be considered as a single campus network.

## Slide 8: Common Industry Campus Networks
Enterprise campus network
School campus network
Government campus network
Entrepreneur campus network
It focuses on network reliability and advancement, and aims to continuously improve employees' office experience and ensure the efficiency and quality of operation and production.
School campus networks are classified into primary and secondary education and higher education campus networks.
Higher education campus networks are complex and include teaching and research networks, student networks, and operational dormitory networks.
There are high requirements on network manageability, security, and advancement.
It usually refers to the internal network of a government agency.
High security is required. In most cases, the internal network and external network are isolated to ensure high security of confidential information.
Such campus networks include networks of shopping malls, supermarkets, hotels, and parks.
The campus network is mainly used to serve consumers and includes the internal office network.
It provides Internet access services and deploys an intelligent service system to improve user experience, reduce O&M costs, improve business efficiency, and achieve value transfer.
Notes: To meet requirements of different industry campuses, the campus network architecture is designed based on the characteristics of the industry that the campus network serves. The campus network solution is based on industry attributes.

## Slide 9: Typical Architecture of a Campus Network
Core layer: is the backbone area of a campus network and is the data switching core. It connects various parts of the campus network, such as the data center, aggregation layer, and egress area.
Aggregation layer: is located at the middle layer of a campus network to implement data aggregation or switching and provide key network functions, such as routing and security.
Access layer: connects end users to a campus network and is the edge of a campus network.
Egress area: is the edge between the campus internal network and the external network. Through this egress area, internal users can access the public network and external users (including customers, partners, branch users, and remote users) can access the internal network.
Data center area: has servers and application systems deployed to provide data and application services for internal and external users of the enterprise.
iStack/CSS link
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
O&M area
Data center

## Slide 10: Main Protocols and Technologies on Campus Networks
Common Protocols and Technologies
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
O&M area
Data center
DHCP, iStack/CSS, link aggregation, LLDP, VRRP, MSTP, VLAN, 802.11, etc.
Cluster, 802.11, OSPF, IS-IS, LLDP, NETCONF/YANG, SNMP, VPN, etc.
NAT, BGP, static routing, firewall, VPN, etc.
iStack/CSS, link aggregation, LLDP, OSPF, IS-IS, etc.
Notes: NAT: Network Address Translation
The Link Layer Discovery Protocol (LLDP) is a Layer 2 discovery protocol defined in the IEEE 802.1ab standard. Using LLDP, the NMS can rapidly obtain the Layer 2 network topology and topology changes when the network scale expands.
Network Configuration Protocol (NETCONF) is a communication management protocol for NEs. It uses Extensible Markup Language (XML) for configuration data and protocol messages, allowing you to install, operate, and delete NEs.
Yet Another Next Generation (YANG) is a data modeling language for data sent using NETCONF. It can be used to model configuration and status data of NEs.
SNMP: Simple Network Management Protocol
VRRP: Virtual Router Redundancy Protocol
MSTP: Multiple Spanning Tree Protocol

## Slide 11
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 12: TCP/IP Model
Dividing network communication into small components facilitates development, design, and troubleshooting of each component.
Network components are standardized so that they can be developed by multiple vendors.
The functions of each layer can be defined to impel industry standardization.
Communication between network hardware and software of different types is allowed.
Application layer
Transport layer
Network layer
Data link layer
Physical layer
Payload
Payload
Payload
Payload
TCP/UDP header
TCP/UDP header
TCP/UDP header
IP header
IP header
Ethernet header
Ethernet trailer
11010010 10010000 01011010 ……
Segment
Packet
Frame
Bit

## Slide 13: Campus Network and Ethernet Layer 2 Switching
The access layer provides various access modes for users and is the first network layer to which terminals connect.
The access layer is usually composed of access switches. There are a large number of access switches that are sparsely distributed in different places on the network. In most cases, an access switch is a simple Layer 2 switch.
If wireless terminals are present at the terminal layer, wireless access points (APs) need to be deployed at the access layer and access the network through access switches.
iStack/CSS link
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
O&M area
Data center

## Slide 14: Overview of Layer 2 Switching
Core-SW
Access-SW1
Access-SW1
Terminal 1
192.168.1.1/24
5469-98AB-0001
Terminal 2
192.168.1.2/24
5469-98AB-0002
Terminal 3
192.168.1.3/24
5469-98AB-0003
Terminal 4
192.168.2.1/24
5469-98AB-0004
Layer 2 communication
Payload
TCP/UDP header
IP header
Ethernet header
Ethernet trailer
Layer 4 header
Layer 3 header
Layer 2 header
Destination MAC address
Source MAC address
Layer 2 switching is a basic function of Ethernet switches.
In Layer 2 switching, a switch forwards a frame according to the destination MAC address in the Layer 2 header of the frame.
Each switch maintains a MAC address table to guide data frame forwarding.
When receiving a data frame, the switch queries the destination MAC address of the frame in the MAC address table and performs the corresponding operation according to the matched entry. When a switch receives a data frame, it also learns the source MAC address of the frame.
Notes: A Layer 2 device works at the second layer of the OSI model and forwards data packets based on MAC addresses.
A Layer 2 device parses and learns source MAC addresses of Ethernet frames and maintains a mapping table of MAC addresses and interfaces. This table is called a MAC address table. When receiving an Ethernet frame, the device searches for the destination MAC address of the frame in the MAC table to determine the interface to which the frame is forwarded.
Interfaces on a Layer 2 device send and receive data independently and belong to different collision domains. Collision domains are isolated at the physical layer so that collisions will not occur between hosts (or networks) connected through this Layer 2 device due to uneven traffic rates on these hosts (or networks).

## Slide 15: VLAN
Virtual Local Area Network (VLAN) technology logically divides a physical LAN into multiple broadcast domains, each of which is called a VLAN.
All devices in a VLAN belong to the same broadcast domain. Different VLANs belong to different broadcast domains.
Devices in a VLAN can directly communicate with each other, whereas devices in different VLANs cannot communicate directly.
Services in different VLANs are isolated from each other. Devices in different VLANs communicate with each other through Layer 3 devices.
Generally, a VLAN is a logical subnet.
Members of a VLAN are allocated based on interfaces of a switch. Generally, an interface of a switch is added to a specified VLAN. In this case, the device connected to the interface is added to the VLAN.
Core-SW
Access-SW1
Access-SW2
Terminal 1
192.168.1.1/24
Terminal 2
192.168.1.2/24
Terminal 3
192.168.1.3/24
Terminal 4
192.168.2.1/24
VLAN 10 (office)
VLAN 20 (monitoring)

## Slide 16: Layer 2 Ethernet Interface Types
Ethernet Layer 2 interfaces on switches are classified into the following types:
  An access interface is used to connect a switch to a terminal, such as a PC or server. Typically, the NICs on such a terminal receive and send only untagged frames. An access interface can be added to only one VLAN.
  A trunk interface allows frames that belong to multiple VLANs to pass through and differentiates the frames using the 802.1Q tag. This type of interface is used to connect a switch to another switch or a sub-interface on a device, such as a router or firewall.
  Similar to a trunk interface, a hybrid interface also allows frames that belong to multiple VLANs to pass through and differentiates the frames using the 802.1Q tag. You can determine whether to allow a hybrid interface to carry VLAN tags when sending the frames of one or more VLANs.
Access
Trunk
Core-SW
Access-SW1
Access-SW2
Terminal 1
192.168.1.1/24
Terminal 2
192.168.1.2/24
Terminal 3
192.168.1.3/24
Terminal 4
192.168.2.1/24
VLAN 10 (office)
VLAN 20 (monitoring)

## Slide 17: Access Interface
GE0/0/1
Access (VLAN 10)
GE0/0/1
Access (VLAN 10)
GE0/0/1
Access (VLAN 10)
GE0/0/1
Access (VLAN 10)
Inside a switch
Untagged frame
Tagged frame
10
Frame receiving
Frame sending
10
Untagged frame
After receiving an untagged frame:
The interface permits the frame and adds a VLAN tag carrying the PVID of the interface.
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is the same as the PVID of the interface, the interface permits the frame.
If the VLAN ID of the frame is different from the PVID of the interface, the interface discards the frame.
Inside a switch
Untagged frame
If the VLAN ID of the frame is the same as the PVID of the interface:
The interface removes the VLAN tag from the frame and then sends the frame.
Inside a switch
20
If the VLAN ID of the frame is different from the PVID of the interface:
The interface is not allowed to send the frame.
10
10
Notes: All Layer 2 interfaces have a default VLAN ID, which is called Port Default VLAN ID (PVID). On Huawei switches, the default PVID is 1. In addition, all data frames carry tags inside the switch to improve the processing efficiency of data frames.

## Slide 18: Trunk Interface
GE0/0/1
Trunk (PVID=10)
Inside a switch
Frame receiving
Frame sending
10
Untagged frame
After receiving an untagged frame:
The interface adds a VLAN tag with the VID being the PVID of the interface to the frame and permits the frame only when the PVID is in the list of VLAN IDs permitted by the interface. If the PVID is not in the list, the interface discards the frame.
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface permits the frame. Otherwise, the interface discards the frame.
Inside a switch
Untagged frame
If the VLAN ID of the frame is the same as the PVID of the interface:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface removes the tag from the frame and sends the frame out. Otherwise, the interface is not allowed to send the frame.
Inside a switch
20
If the VLAN ID of the frame is different from the PVID of the interface:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface sends the frame out without removing the tag of the frame. Otherwise, the interface is not allowed to send the frame.
10
10
Permitted VLAN ID: 10
GE0/0/1
Trunk (PVID=1)
Permitted VLAN ID: 10
GE0/0/1
Trunk (PVID=10)
Permitted VLAN ID: 10
GE0/0/1
Trunk (PVID=10)
Permitted VLAN ID: 10
20

## Slide 19: Hybrid Interface
GE0/0/1
Hybrid (PVID=10)
GE0/0/1
Hybrid (PVID=1)
GE0/0/1
Hybrid (PVID=1)
GE0/0/1
Hybrid (PVID=1)
Inside a switch
Frame receiving
Frame sending
10
Untagged frame
After receiving an untagged frame:
The interface adds a VLAN tag with the VID being the PVID of the interface to the frame and permits the frame only when the PVID is in the list of VLAN IDs permitted by the interface. If the PVID is not in the list, the interface discards the frame.
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface permits the frame. Otherwise, the interface discards the frame.
Inside a switch
Untagged frame
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface:
If the interface has been configured not to carry VLAN tags when sending frames, it removes the tag from the frame and then sends the frame out.
Inside a switch
20
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface:
If the interface has been configured to carry VLAN tags when sending frames, it sends the frame out without removing the tag of the frame.
10
10
Permitted VLAN ID: 10
Permitted VLAN ID: 10
Permitted VLAN ID: 10
Permitted VLAN ID: 20
20
Notes: A hybrid interface can transmit data of multiple VLANs. The behavior of a hybrid interface is similar to that of a trunk interface in receiving data frames. When a trunk interface sends a data frame, the switch removes the tag of the data frame only when the VLAN ID of the data frame is the same as the PVID of the interface. In addition, data frames of other VLANs sent by the interface carry tags. A hybrid interface sends data frames in a different way from a trunk interface. You can run commands to configure a hybrid interface to send untagged data frames of a certain VLAN or some VLANs.

## Slide 20: VLAN Assignment Methods
VLAN Assignment Method | Description
Interface-based assignment | VLANs are assigned based on switch interfaces.
MAC address-based assignment | VLANs are assigned based on the source MAC addresses of frames.
IP subnet-based assignment | VLANs are assigned based on the source IP addresses of frames.
Protocol-based assignment | VLANs are assigned based on protocol types and encapsulation formats of frames.
Policy-based assignment | VLANs are assigned based on policies such as combinations of interfaces, MAC addresses, and IP addresses.

## Slide 21: Inter-VLAN Communication
Through physical interfaces of a router
Through sub-interfaces of a router
Through a Layer 3 switch
Terminal 1
Terminal 4
VLAN 10 (office)
VLAN 20 (monitoring)
GE0/0/1
192.168.10.254
GE0/0/2
192.168.20.254
192.168.10.0/24
Default gateway: 192.168.10.254
VLAN 10
VLAN 20
192.168.20.0/24
Default gateway: 192.168.20.254
Terminal 1
Terminal 4
VLAN 10 (office)
VLAN 20 (monitoring)
GE0/0/1.10
192.168.10.254
GE0/0/1.20
192.168.20.254
192.168.10.0/24
Default gateway: 192.168.10.254
192.168.20.0/24
Default gateway: 192.168.20.254
Trunk
Terminal 1
Terminal 4
VLAN 10 (office)
VLAN 20 (monitoring)
192.168.10.0/24
Default gateway: 192.168.10.254
192.168.20.0/24
Default gateway: 192.168.20.254
Trunk
VLANIF 10 192.168.10.254
VLANIF 20 192.168.20.254

## Slide 22: Ethernet Link Aggregation
Core-SW
Access-SW1
Access-SW1
Terminal 1
Terminal 2
Terminal 3
Terminal 4
Internet
Link Aggregation (LAG) technology bundles multiple physical links into a logical link to increase link bandwidth.
The aggregated link is called an Ethernet aggregation link.
FW1
FW2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
Eth-Trunk 1
Eth-Trunk 1
Increased bandwidth
Improved reliability
Load balancing
Notes: As networks grow in scale, users require Ethernet backbone networks to provide higher bandwidth and availability. In the past, the only way to increase bandwidth was to upgrade the network with high-speed LPUs, which is costly and inflexible.
In contrast, link aggregation increases bandwidth by bundling a group of physical port into a single logical port, without the need to upgrade hardware. In addition, link aggregation provides link backup mechanisms, greatly improving link availability.
An LAG is the logical link bundled by many Ethernet links, and is short for Eth-Trunk. Each LAG corresponds to a unique logical interface, which is called an aggregation interface or Eth-Trunk interface.
Link aggregation has the following advantages:
  Improved bandwidth: The maximum bandwidth of a link aggregation group (LAG) is the combined bandwidth of all member links.
  Improved reliability: If an active link fails, traffic can be switched to other available member links.
  Load balancing: The traffic load can be balanced among the active member links in a LAG.

## Slide 23: STP: Loop Prevention + Layer 2 Network Reliability
Eliminates loops on a switching network.
Dynamically adapts to network topology changes.
Ensures Layer 2 network reliability together with redundant links.
Layer 3 network
Layer 2 network
STP running environment
iStack/CSS link
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
O&M area
DC

## Slide 24
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 25: WLAN and Main NEs
Wireless
terminals
Wireless
access
Wireless
control
IP network
Laptop
Mobile phone
Tablet
AirEngine series wireless AP
Access switch
Aggregation switch
Core switch
AirEngine series AC
Barcode scanners, AGV cars, wristbands, etc.
Remote unit (RU)
Overview of WLAN
WLAN is a network that uses high-frequency (2.4 GHz or 5 GHz) signals such as radio waves, lasers, and infrared rays to replace the traditional media used for transmission on a wired LAN.
The WLAN technologies described in this document are based on 802.11 standards.
802.11 was originally a wireless LAN communications standard defined by the Institute of Electrical and Electronics Engineers (IEEE) in 1997.
The IEEE then made amendments to the standard, forming the 802.11 family, including 802.11, 802.11a, 802.11b, 802.11e, 802.11g, 802.11i, 802.11n, and 802.11ac.

## Slide 26: Network Architecture Overview
Fat AP
Internet
Networking characteristics: A Fat AP works independently and needs to be configured separately. It provides only simple functions and is cost-effective.
Applicable scope: Families or mini-stores
AC + Fit AP
Networking characteristics: A Fit AP provides multiple functions and is used with the AC. It is managed and configured by the AC in a unified manner. There are high requirements on skills of maintenance personnel.
Applicable scope: Medium- and large-sized enterprises
Fat AP
Fit AP
AC
Notes: AP
  The AP can switch flexibly among the Fat, Fit, and cloud modes based on the network plan.
  Fat AP: applies to home WLANs. A Fat AP works independently and requires separate configurations. It provides only simple functions and is cost-effective. The Fat AP independently implements functions such as user access, authentication, data security, service forwarding, and QoS.
  Fit AP: applies to medium- and large-sized enterprises. Fit APs are managed and configured by the AC in a unified manner, provide various functions, and have high requirements on network maintenance personnel's skills. Fit APs must work with a AC for user access, AP going-online, authentication, routing, AP management, security, and QoS.
  Cloud AP: applies to small- and medium-sized enterprises. Cloud APs are managed and configured by a cloud management platform in a unified manner, provide various functions, support plug-and-play, and have low requirements on network maintenance personnel's skills.
AC
  An AC is usually deployed at the aggregation layer of a network to provide high-speed, secure, and reliable WLAN services.
  Huawei ACs provide a large capacity and high performance. They are highly reliable, easy to install and maintain, and feature such advantages as flexible networking and energy conservation.

## Slide 27: AC + Fit AP Architecture (1)
CAPWAP tunnel
AC
Fit AP
Basic Concepts
AC: controls and manages all Fit APs on a AC + Fit AP network.
The AC is responsible for WLAN access control, forwarding and statistics, AP configuration monitoring, roaming management, AP network management agent, and security control.
A Fit AP encrypts and decrypts 802.11 packets, provides 802.11 physical layer functions, collects air interface statistics, and is managed by an AC.
The AC and Fit APs communicate through CAPWAP.
Compared with the Fat AP architecture, the AC + Fit AP architecture has the following advantages:
  Easier configuration and deployment
  Higher security
  Easier update and expansion
Fit AP
Notes: The AC and Fit APs communicate through CAPWAP. With CAPWAP, APs automatically discover the AC, the AC authenticates the APs, and the APs obtain the software package and the initial and dynamic configurations from the AC. CAPWAP tunnels are established between the AC and APs. CAPWAP tunnels include control and data tunnels. The control tunnel is used to transmit control packets (also called management packets, which are used by the AC to manage and control APs). The data tunnel is used to transmit data packets. The CAPWAP tunnels allow for Datagram Transport Layer Security (DTLS) encryption, so that transmitted packets are more secure.
Compared with the Fat AP architecture, the AC + Fit AP architecture has the following advantages:
  Configuration and deployment: The AC centrally configures and manages the wireless network so that you do not need to configure each AP separately. In addition, the channels and power of APs on the entire network are automatically adjusted, eliminating the need for manual adjustment.

## Slide 28
Notes:   Security: Fat APs cannot be upgraded in a unified manner, which cannot ensure the latest security patches are installed for all AP versions. In the AC + Fit AP architecture, security capabilities are mainly implemented on the AC, and we only need to perform the software upgrade and security configuration on the AC. This can quickly perform global security configurations. Additionally, to prevent malicious code from being loaded, the AC performs digital signature authentication on the software, enhancing the security of the update process. The AC also implements some security functions that are not supported by the Fat AP architecture, including advanced security features such as virus detection, uniform resource locator (URL) filtering, and stateful inspection firewall.
  Upgrade and extension: The centralized management mode of this architecture enables APs on the same AC to run the same software version. When an upgrade is required, the AC obtains the new software package or patch and then upgrades the AP version. The separation of AP and AC functions prevents frequent AP version upgrades. We only need to update the user authentication, network management, and security functions on the AC.

## Slide 29: AC + Fit AP Architecture (2)
Overview of CAPWAP
Control And Provisioning of Wireless Access Points (CAPWAP): defines how to manage and configure APs. That is, a AC manages and controls APs in a centralized manner through CAPWAP tunnels.
With CAPWAP, APs automatically discover the AC, the AC authenticates the APs, and the APs obtain the software package and the initial and dynamic configurations from the AC. CAPWAP tunnels are established between the AC and APs.
CAPWAP Tunnel Functions
CAPWAP tunnels include control and data tunnels.
The control tunnel is used to transmit control packets (also called management packets, which are used by the AC to manage and control APs). The data tunnel is used to transmit data packets. The CAPWAP tunnels allow for Datagram Transport Layer Security (DTLS) encryption, so that transmitted packets are more secure. Allows APs to exchange data sent by STAs with the AC through CAPWAP tunnels when the tunnel forwarding mode is used.
AC
Fit AP
Fit AP
AC
Control tunnel
Data tunnel
Control packet
Data packet
CAPWAP tunnel

## Slide 30
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 31: Using VRRP to Implement Gateway Redundancy
Basic VRRP Applications
Typical Applications of MSTP+VRRP
Aggregation switch 1
Aggregation switch 2
Access switch
Aggregation switch 1
Aggregation switch 2
Access switch
VRRP
Virtual router
192.168.1.254
IP address: 192.168.1.1/24
Default gateway: 192.168.1.254
Redundancy
Load balancing
Association
VLANs 11, 12 , ..., 20
VLANIF interfaces 11-20 VRRP Master
VLANIF interfaces 21-30 VRRP Backup
MSTI 10 Primary root bridge
MSTI 20 Secondary root bridge
MSTP
VLANIF interfaces 11-20 VRRP Backup
VLANIF interfaces 21-30 VRRP Master
MSTI 10 Secondary root bridge
MSTI 20 Primary root bridge
MSTP
VRRP
VRRP
VLANs 21, 12 , ..., 30
VRRP and MSTP are used to implement gateway redundancy, load balancing, Layer 2 loop prevention, and reliability.
Notes: The Virtual Router Redundancy Protocol (VRRP) specifies an election protocol that dynamically assigns responsibility for a virtual router to VRRP routers on a LAN. It allows several routers on a subnet to use the same virtual IP address, with the physical routers representing a virtual logical router. If a gateway fails, VRRP selects a different gateway to forward traffic, thereby ensuring reliable communication.
Generally, all hosts on the same network segment are configured with the same default route with the gateway address as the next hop address. The hosts use the default route to send packets to the gateway and the gateway forwards the packets to other network segments. When the gateway fails, hosts with the same default route cannot communicate with external networks. To improve network reliability, multiple egress gateways can be configured. However, route selection between the gateways becomes an issue.
VRRP resolves this issue. The virtual router IP address is configured as the default gateway address. If a gateway fails, VRRP selects a different gateway to forward traffic, thereby ensuring reliable communication.
  Redundancy: Multiple routing devices enabled with VRRP constitute a VRRP group and the VRRP group is used as the default gateway. When a single point of failure occurs, services are transmitted through the backup link. This reduces the possibility of network faults and ensures uninterrupted transmission of various services.

## Slide 32
Notes:   Load balancing: VRRP enables multiple available routers to share the load more uniformly, reducing the traffic burden on the master.
  Association: VRRP can monitor faults on uplinks. When the upstream interface or uplink is faulty, the priority of the original master decreases, and an optimal backup becomes the master, ensuring proper traffic forwarding. Association between VRRP and BFD speeds up the active/standby switchover. To speed up the active/standby switchover in the VRRP group, configure a BFD session between the master and backup and associate the BFD session with the VRRP group. This is because BFD can fast detect faults. When the link between the master and backup becomes Down, the backup immediately switches to the master and takes over traffic.

## Slide 33: Overview of CSS/iStack
Intelligent stack (iStack) enables multiple stacking-capable switches to function as a single logical switch. iStack is applicable to Huawei fixed switches.
A cluster switch system (CSS) combines two clustering-capable switches into a single logical switch. A CSS is also called a cluster. CSS is applicable to Huawei modular switches.
CSS
iStack
iStack

## Slide 34: Traditional STP Networking and iStack Networking
Traditional STP networking
Switch iStack networking (tree networking)
iStack
Two aggregation switch and access switches form a triangle-shaped Layer 2 loop. STP has to be deployed on the network to block network interfaces. As a result, the link bandwidth cannot be fully used.
Aggregation switch 1
Aggregation switch 2
Access switch
Access switch
Access switch
Access switch
Aggregation switches enabled with iStack constitute a logical device.
Aggregation switches enabled with iStack constitute a logical device, simplifying the network topology. In addition, link aggregation can be deployed between aggregation switch and access switches to form a tree topology, eliminating Layer 2 loops and improving link bandwidth utilization.
Notes: iStack enables multiple stacking-capable switches to function as a logical device.
Before a stack is set up, each switch is independent and has its own IP address and MAC address. You need to manage the switches separately. After a stack is set up, switches in the stack form a logical entity and can be managed and maintained using a single IP address. iStack technology improves forwarding performance and network reliability, and simplifies network management.

## Slide 35
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 36: DHCP
Using the Dynamic Host Configuration Protocol (DHCP) to automatically configure IP addresses
Typical application of DHCP on a large-scale campus network
DHCP client
Layer 2 switch
DHCP server
The DHCP client broadcasts a DHCP Discover message
1
2
The DHCP server responds with a DHCP Offer message.
The DHCP client broadcasts a DHCP Request message.
3
2
The DHCP server responds with a DHCP ACK message.
Search for the DHCP server on the network
Provide information such as the IP address
Specify the IP address provided by a DHCP server
Check the IP address allocation
DHCP server
DHCP client
DHCP client
Layer 3 gateway
Deploy a DHCP relay agent
DHCP is widely used on various campus networks to implement automatic IP address configuration for wired or wireless terminals.
A DHCP relay agent forwards DHCP messages between a DHCP server and DHCP clients to help the DHCP server to dynamically allocate network parameters to the DHCP clients.
Layer 3 gateway
Deploy a DHCP relay agent
Notes: DHCP dynamically configures and uniformly manages IP addresses of hosts. It simplifies network deployment and scale-out, even for small networks.
DHCP enables a host to obtain an IP address dynamically, but does not specify an IP address for each host.
DHCP can allocate other configuration parameters, such as the boot file of a client, so that the client can obtain all the required configuration information by using only one message.
DHCP is defined in RFC 2131 and uses the client/server communication mode. A DHCP client requests configuration information from a DHCP server, and the DHCP server returns the configuration information allocated to the DHCP client.
DHCP supports dynamic and static IP address allocation.
  Dynamic allocation: DHCP allocates an IP address with a limited validity period (known as a lease) to a client. This mechanism applies to scenarios where hosts temporarily access the network and the number of idle IP addresses is less than the total number of hosts.
  Static allocation: DHCP allocates fixed IP addresses to clients as configured. Compared with manual IP address configuration, DHCP static allocation prevents manual configuration errors and enables unified maintenance and management.
DHCPv4 offers the following benefits:
  Reduced client configuration and maintenance costs
  Centralized management

## Slide 37: NTP
Network management: Analysis on logs or debugging information collected from different routers must be performed based on time.
Charging system: The clocks of all devices must be consistent.
Several systems interworking on the same complex event: The systems must use the same clock for reference to ensure proper sequencing of operations.
Incremental backup between the backup server and clients: Clocks on the backup server and clients should be synchronized.
System time: Some applications need to know the time when user logs in to the system and the file revision time.
The Network Time Protocol (NTP) is mainly used in the following scenarios where the clocks of all network devices must be consistent:
Clock synchronization
08:54:44.160 UTC Nov 22 2013
08:54:44.160 UTC Nov 22 2013
Notes: NTP is an application layer protocol belonging to the Transmission Control Protocol/Internet Protocol (TCP/IP) suite. NTP synchronizes time between time servers and clients. NTP implementation is based on IP and User Datagram Protocol (UDP). NTP packets are transmitted by UDP over port 123.
As network topologies become increasingly complex, clock synchronization becomes more important for all devices within a network. Manual configuration of system clocks by network administrators is both labor-intensive and error-prone, potentially affecting clock precision. To address this problem, NTP is introduced to synchronize the clocks of devices within a network.
NTP is used when clocks of all devices on a network need to be consistent. For example, in network management, the logs and debugging information collected from different routers need to be analyzed based on time.
  Charging system: The clocks of all devices must be consistent.
  Several systems interworking on the same complex event: The systems must use the same clock for reference to ensure proper sequencing of operations.
  Incremental backup between the backup server and clients: Clocks on the backup server and clients should be synchronized.
  System time: Some applications need to know the time when user logs in to the system and the file revision time.
A switch can function as both an NTP server and an NTP client.

## Slide 38: LLDP
Network management requirements and overview of the Link Layer Discovery Protocol (LLDP)
Application of LLDP in Huawei CloudCampus solution
Most NMSs can detect Layer 3 network topologies, but they cannot detect detailed Layer 2 topologies or configuration conflicts.
LLDP provides a standard link-layer discovery method:
  Obtains the topology status of the connected devices.
  Displays paths between devices.
  Detects configuration conflicts between devices and queries network failure causes.
You can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.
SW1
SW2
SW3
GE1/0/1
GE1/0/1
[SW3] display lldp neighbor brief
Local Intf Neighbor Dev Neighbor Intf Exptime(s)
GE1/0/1 SwitchB GE1/0/1 101
The device reports LLDP information to the controller.
1
2
3
The controller restores and displays the network topology based on the LLDP information reported by devices.
Notes: LLDP is a standard Layer 2 topology discovery protocol defined in IEEE 802.1ab. LLDP collects local device information including the management IP address, device ID, and port ID and advertises the information to neighbors. Neighbors save the received information in their management information bases (MIBs). The NMS can use data in MIBs to query the link status.
An NMS must be capable of managing multiple network devices with diverse functions and complex configurations. Most NMSs can detect Layer 3 network topologies, but they cannot detect detailed Layer 2 topologies or configuration conflicts. A standard protocol is required to exchange Layer 2 information between network devices.
LLDP provides a standard link-layer discovery method. Layer 2 information obtained from LLDP allows the NMS to detect the topology of neighboring devices, and display paths between clients, switches, routers, application servers, and network servers. The NMS can also detect configuration conflicts between network devices and identify causes of network failures. Enterprise users can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.

## Slide 39: SNMP
The Simple Network Management Protocol (SNMP) is a network management standard widely used on TCP/IP networks.
SNMP uses a central computer (a network management station) that runs network management software to manage devices.
By employing the "network management over networks" mode, SNMP is used for efficient and batch network device management. In addition, SNMP enables unified management of network devices of different types and from different vendors.
Overview of SNMP
SNMP
NMS (SNMP server)
Example: iMaster NCE
Managed device (SNMP client)
Example: Routers and switches
Agent
MIB
SNMP

## Slide 40: NETCONF/YANG
SNMP is not a configuration-oriented protocol. On a large-sized network with a complex topology, SNMP cannot meet network management requirements, especially configuration management requirements.
SNMP Weaknesses
NETCONF
NMS (NETCONF server)
Example: iMaster NCE
Managed device (NETCONF client)
Example: Routers and switches
NETCONF provides a mechanism for communication between the NMS and network devices.
A network administrator can use NETCONF to add, modify, or delete configurations of network devices, and obtain configurations and status of network devices.
NETCONF is based on Extensible Markup Language (XML).
NETCONF

## Slide 41
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 42: Overview of Network Security
Internet
WAN
WLAN AC
WLAN AC
DataCenter
Access layer
Core and aggregation layer
Campus border
O&M area
Deploy service isolation and mutual access traffic control.
Deploy network admission control on demand.
Deploy local attack defense to improve anti-attack capabilities of devices.
It is recommended that security functions such as broadcast storm control, DHCP snooping, IPSG, and DAI be enabled and port isolation be deployed to enhance user communication security.
Deploy network access control to authenticate identities or terminals of users who access the campus network and grant network access permissions based on the authentication results.
Deploy wireless air interface security and wireless service security.
Deploy firewalls to divide security zones, isolate services, and implement security management and control.
Deploy anti-DDoS devices to defend against DDoS attacks.
Deploy IPS devices to provide intrusion detection and security posture awareness.
Intelligent security collaboration

## Slide 43: Firewall-based Security Zone Division and Security Policies
A security zone is introduced on a device. Most security policies are implemented based on security zones.
A security zone is a set of the networks connected by interfaces. Users on these networks have the same security attributes.
Employees, servers, and external networks can be assigned to different security zones for inter-zone traffic inspection and protection.
Core-SW
Access-SW1
Access-SW1
Terminal 1
Terminal 2
Terminal 3
Terminal 4
Trusted zone
DMZ
Untrusted zone
Deploy security policies to control inter-zone traffic
Internet
Notes: Two security zones with the same security level cannot be created on a firewall.
Interfaces on a firewall must be added to a security zone. Otherwise, traffic cannot be forwarded properly.
An interface on a firewall can belong to a security zone.
A security zone of a firewall can have multiple interfaces.
The default security zones of the system cannot be deleted. You can create a user-defined security zone as required.

## Slide 44: Overview of Firewall HSB
Core-SW
Access-SW1
Access-SW2
Terminal 1
Terminal 2
Terminal 3
Terminal 4
Internet
When one firewall is deployed at the egress of the network and a fault occurs on it, services on the entire network will be adversely affected. Network reliability needs to be improved.
Multiple firewalls can be deployed to improve reliability. Service continuity must be ensured during device switchover.
Requirement
Two firewalls are deployed and work in hot standby (HSB) mode.
HSB requires two firewalls with the same hardware and software configurations.
The two firewalls are connected through an independent link, which is usually called a heartbeat link. The two firewalls learn the health status of each other and back up configurations and entries (such as session table entries and IPsec SAs) to each other through the heartbeat link.
If one firewall fails, services can be smoothly switched over to the other firewall to ensure service continuity.
Solution
Heartbeat

## Slide 45: NAT
Terminal 1
192.168.1.1/24
Terminal 2
192.168.1.2/24
When an intranet user (using a private IP address) needs to access the Internet, the source IP address needs to be translated into a public IP address.
Extranet users need to access the server (such as the web server) that uses a private IP address.
Requirement
Web server
10.1.1.1/24
NAT translates between private and public IP addresses carried in the headers of IP data packets.
Common NAT:
  Source IP address-based NAT:
    No-PAT
    Network address and port translation (NAPT)
  Destination IP address-based NAT:
    NAT server
NAT
1.2.3.4
5.6.7.8
Source IP | 192.168.1.2
Destination IP | 1.2.3.4
Payload | Data
Source IP | 200.1.2.3
Destination IP | 1.2.3.4
Payload | Data
Source IP | 5.6.7.8
Destination IP | 200.4.5.6
Payload | Data
Source IP | 5.6.7.8
Destination IP | 10.1.1.1
Payload | Data
1
2
1
2

## Slide 46
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 47: VPN Technology Application Scenario
For a large-scale enterprise, network access requirements are not limited to the headquarters network. Branches, traveling employees, and partners also need to access network resources of the headquarters. Generally, Virtual Private Network (VPN) technology is used to meet this requirement.
VPN technology builds a virtual private network without any change in the network topology. Compared with leased lines, VPN is a more cost-effective solution to build a private network.
Different VPN technologies have different features and implementation modes. Common VPN technologies include IPsec VPN, GRE VPN, L2TP VPN, and MPLS VPN.
O&M area
DC
Branch network
Traveling employee
VPN traffic
Notes: Internet Protocol Security (IPsec)
Generic Routing Encapsulation (GRE)
Layer 2 Tunneling Protocol (L2TP)
Multiprotocol Label Switching (MPLS)

## Slide 48
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 49: Multicast Application Scenarios
An enterprise has some bulletins, such as the weather, duty schedule, precautions in the equipment room, and promotion videos. To facilitate employees and visitors to obtain the information in a timely manner, display screens are usually deployed in densely populated areas.
The content displayed on each screen is the same. This is a typical point-to-multipoint communication scenario. If information is transmitted in unicast mode, device performance and link bandwidth on the network are wasted to a certain extent.
Multicast technology efficiently implements point-to-multipoint data transmission over an IP network, while conserving network bandwidth and reducing network loads.
Media server
Exhibition hall display
Exhibition hall display
Exhibition hall display
...
Notes: Unicast transmission is implemented between a source IP host and a destination IP host. Most of data is transmitted in unicast mode on a network. For example, email and online banking applications are implemented in unicast mode.
  In unicast mode, each data packet has a specific destination IP address. For the same data, if there are multiple receivers, the server needs to send unicast data packets with the same number as the number of receivers. When there are hundreds or thousands of receivers, the server consumes a lot of resources to create the same data and send multiple copies of the same data. As a result, the device performance and link bandwidth on the network are wasted to a certain extent. The unicast mode is applicable to networks with a small number of users. When there are a large number of users, the unicast mode cannot ensure the network transmission quality.
Broadcast transmission is implemented between a source IP host and all the other IP hosts on the local network. All hosts can receive data from the source host, regardless of whether they require the data.
  Broadcast data packets are restricted in a broadcast domain. Once a device sends broadcast data, all devices in the broadcast domain receive the data packet and have to consume resources to process the data packet. A large number of broadcast data packets consume network bandwidth and device resources. The broadcast mode applies only to shared network segments, and cannot ensure information security and paid services.
Multicast transmission is implemented between one source IP host and a group of IP hosts. Intermediate routers and switches selectively replicate and forward data based on demands of receivers.

## Slide 50: Basic Multicast Network Architecture
A multicast network can be divided into three parts:
  Source network: sends multicast data generated by the multicast source to the multicast network.
  Multicast forwarding network: A loop-free multicast forwarding path is formed. This forwarding path is also called a multicast distribution tree (MDT).
  Member network: enables the multicast network to detect the locations of multicast group members and the multicast groups that the members join.
Multicast source
Multicast group member
Multicast group member
Multicast router
(first hop)
Multicast router
(last hop)
Source network
Multicast forwarding network
Member network
Join multicast group 1
Join multicast group 2
Multicast routing protocol
Multicast forwarding path formed based on a multicast routing protocol
Detect multicast group members' locations and multicast groups based on the Internet Group Management Protocol (IGMP)
Send multicast data to the multicast network
Notes: Multicast source: indicates a multicast traffic sender, for example, a multimedia server. A multicast source does not need to run any multicast protocol. It only needs to send multicast data.
Multicast receiver: is also called a multicast group member and a device that expects to receive traffic of a specific multicast group, for example, a PC running the multimedia live broadcast client software.
Multicast group: indicates a group of receivers identified by a multicast IP address. User hosts (or other receiver devices) that have joined a multicast group become members of the group and can identify and receive the IP packets destined for the multicast group address.
Multicast router: indicates a network device that supports multicast and runs multicast protocols. In addition to routers, switches and firewalls support multicast (depending on device models). A router is only a representative.
First-hop router: indicates a router that directly connects to the multicast source on the multicast forwarding path and is responsible for forwarding multicast data from the multicast source.
Last-hop router: indicates a router that directly connects to multicast group members (receivers) on the multicast forwarding path and is responsible for forwarding multicast data to these members.
In the TCP/IP protocol suite, IGMP manages IP multicast members, and sets up and maintains multicast member relationships between receivers and their directly connected multicast routers.

## Slide 51
Campus Network Architecture and Common Technologies
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN
Multicast
IPv6

## Slide 52: Overview of IPv6
IPv4 is a widely used Internet protocol. In the early stage of the Internet, IPv4 developed rapidly due to its simple design, easy implementation, and good interoperability. However, with the rapid development of the Internet, the shortage of IPv4 address spaces becomes increasingly serious, and it is imperative that IPv6 replace IPv4.
Internet Protocol version 6 (IPv6), also called IP Next Generation (IPng), is a second-generation network layer protocol designed by the Internet Engineering Task Force (IETF), IPv6 is an upgraded version of IPv4.
The 128-bit address length provides numerous addresses, meeting requirements of emerging services such as the IoT and facilitating service evolution and expansion.
IPv6

## Slide 53: ICMPv6
The Internet Control Message Protocol version 6 (ICMPv6) is one of the basic IPv6 protocols.
ICMPv6 messages are widely used in other protocols, such as NDP and path MTU discovery.
ICMPv6 controls key IPv6 processes, such as address autoconfiguration, address resolution, address conflict detection, route selection, and error control.
R1
R2
GE0/0/1
PC1
R3
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
PC1
ICMPv6 is indispensable in each network communication phase.
Notes: NDP: Neighbor Discovery Protocol

## Slide 54: IPv6 Routing
IPv6 networks support static and dynamic routing protocols.
  Static route:
    The method of configuring an IPv6 static route is the same as that of configuring an IPv4 static route.
  Dynamic routing protocols:
    OSPFv3
    IS-IS
    BGP4+
OSPFv3
IS-IS (IPv6)
BGP4+
Static routing
BGP4+

## Slide 55
(Multiple) Which of the following statements about Layer 2 interfaces of switches are true?( )
  Layer 2 interfaces on switches include access, trunk, and hybrid interfaces.
  An access interface can be added to only one VLAN.
  By default, a trunk interface allows traffic from VLAN 1 to pass through and sends untagged packets.
  On a hybrid interface, you can run a command to specify whether the packets sent from a specified VLAN carry VLAN tags.
(Multiple) What are advantages of Ethernet link aggregation?( )
  Improved bandwidth: The maximum bandwidth of a link aggregation group (LAG) is the combined bandwidth of all member links.
  Improved reliability: If an active link is faulty, traffic can be switched to other available member links.
  Load balancing: The traffic load can be balanced among the active member links in a LAG.
  Intelligent optimization: The number of active interfaces can be automatically adjusted based on the traffic volume.
Notes: ABCD
ABC

## Slide 56
This course describes typical application scenarios of campus network technologies, including Ethernet switching basics, wireless access, network reliability, network service and management, routing and network reachability, network security, and VPN.
This document cannot list all technologies used on campus networks. After completing this course, you will be able to understand the typical architecture of campus networks and the application of typical technologies on campus networks. This will help you continue to learn the following courses.
In subsequent courses, we will discuss key technologies of campus networks to lay a solid foundation for learning campus network solutions in the future.