## Slide 1
Lu Yueyue/lwx445705
2020-02
New

## Slide 2: RSTP Implementation and Configuration

## Slide 3
On an Ethernet switching network, redundant links are used to implement link backup and enhance network reliability. The downside of this is that it may produce loops, leading to broadcast storms and an unstable MAC address table. As a result, communication on the network may deteriorate or even be interrupted. To prevent loops, IEEE introduced the Spanning Tree Protocol (STP), which is standardized as IEEE 802.1d.
The convergence speed of an STP topology slows as the number of LANs increases. Therefore, IEEE introduced the Rapid Spanning Tree Protocol (RSTP), standardized as 802.1w, in 2001 to improve the network convergence speed.
This document describes the improvements of RSTP compared with STP, working mechanism of RSTP, and RSTP configurations.

## Slide 4
Upon completion of this course, you will be able to:
  Describe defects of STP technology.
  Describe RSTP improvements compared with STP.
  Describe the working mechanism of RSTP.
  Perform basic RSTP configurations.

## Slide 5
Introduction to RSTP
  STP Review and Defects
  RSTP Overview
Improvements Made in RSTP
Working Mechanism of RSTP
RSTP Configurations

## Slide 6: Review: STP Implementation
SW2
SW3
SW1 (root bridge)
STP Configuration BPDUs
STP transmits configuration BPDUs between switches to elect the root switch (or root bridge) and determine the role and status of each switch port.
Each switch actively sends configuration BPDUs during initialization.
After the network topology becomes stable, only the root bridge proactively sends configuration BPDUs. Other bridges send configuration BPDUs only after receiving configuration BPDUs from uplink devices.
A configuration BPDU contains parameters such as the bridge ID, path cost, and port ID.
Configuration BPDU
Hello Time: 2s
PID | PVI | BPDU Type | Flag | Root ID | RPC | Bridge ID | Port ID | Message Age | Max Age | Hello Time | Forward Delay
Format of configuration BPDUs
Notes: Flooding of configuration BPDUs:
  During generation of the STP tree, all STP switches generate and send configuration BPDUs periodically (Hello Time, 2s by default). All STP switches consider themselves as the root bridge.
  When BPDUs are flooded and collected, switches compare information in BPDUs and elect the root bridge.
  After the STP tree is formed, only the root bridge generates and sends configuration BPDUs periodically (2s by default). A non-root bridge periodically receives configuration BPDUs from its root port, immediately generates configuration BPDUs, and sends the configuration BPDUs through its designated port. During the process, configuration BPDUs from the root bridge pass through the other switches hop by hop. As shown in the figure, the link between SW1 and SW2 is the uplink of SW2, and the link between SW2 and SW3 is the downlink of SW2.
Packet format:
  Parameters in BPDUs are classified into the following types:
  Type 1: BPDU identifiers, including Protocol ID, Protocol version ID, BPDU Type, and Flag.
    Protocol ID (PID): The value has 2 bytes and is always 0x000.
    Protocol version ID (PVI): The value has 1 byte and is always 0x00.
    BPDU Type: The value has 1 byte and is always 0x00.
    Flag: It refers to the network topology change flag. The value has 1 byte. Only the least significant bit and most significant bit are used.

## Slide 7
Notes:   Type 2: parameters used for STP calculation, including the BID of the current root bridge, root path cost, BID of the switch that sends BPDUs, and PID of the port that sends BPDUs.
    Root ID: indicates the BID of the current root bridge. It has 8 bytes.
    Root path cost (RPC): indicates the accumulated cost of the port that sends BPDUs to the root bridge. It has 4 bytes.
    Bridge ID (BID): indicates the BID of the switch that sends BPDUs. It has 8 bytes.
    Port ID (PID): indicates the ID of the port that sends BPDUs. It has 2 bytes.
  Type 3: time parameters, including the Message Age, Max Age, Hello time, and Forward Delay.
    Message Age: indicates the number of seconds after a BPDU is sent from the root bridge. It has 2 bytes. The value of the Message Age field in configuration BPDUs sent from the root bridge is 0. The Message Age value of a configuration BPDU is incremented by 1 each time the configuration BPDU passes through a bridge.
    Max Age: indicates the maximum lifecycle of BPDUs. It has 2 bytes. The default value is 20s.
    Hello time: indicates the interval for the root bridge to send configuration BPDUs. It has 2 bytes. The default value is 2s.
    Forward Delay: indicates the interval for the port to stay in Listening and Learning states. It has 2 bytes. The default value is 15s.

## Slide 8: Review: STP Tree Generation Process
Four Steps of STP Calculation
Roles are elected by comparing the following four parameters:
Root bridge ID, root path cost, bridge ID, and port ID
Elect the root bridge.
Elect a root bridge on a switching network.
Elect the root port.
Elect a root port on each non-root-bridge.
Elect a designated port.
Elect a designated port for each network segment.
Block non-designated ports.
Block all the remaining non-root and non-designated ports on switches.
R
Root port
D
Designated port
Non-designated port
SW2
SW3
SW1 (root bridge)
D
D
R
D
R
Notes: STP working mechanism:
  On a switching network with loops, switches run STP to automatically generate a loop-free working topology, which is also called an STP tree. A tree node is a specific switch, and a tree branch is a specific link.
STP uses the following four steps to prevent Layer 2 loops (a spanning tree is generated):
  Elect a root bridge on a switching network; elect a root port on each non-root bridge; elect a designated port for each network segment; block all the remaining non-root and non-designated ports (alternate ports) on switches.
How is an STP tree generated?
  Compare the root bridge ID, root path cost, bridge ID, and port ID. A smaller value indicates a higher priority. These parameters are all fields in BPDUs.
    Root bridge election: The device with the smallest root bridge ID is the root bridge.
    Root port election: The system compares the RPC, peer BID, peer PID, and local PID in sequence and selects the port with the smallest value.
    Designated port election: The system compares the RPC, local BID, and local PID in sequence and selects the port with the smallest value.
    After the root port and designated port are determined, all the remaining non-root ports and non-designated ports on the switch are blocked.
On Huawei switches, a blocked non-designated port is an alternate port.

## Slide 9: Review: STP Port State Transition
STP Port State Transition
The port is initialized or enabled and enters the Blocking state.
If the port is selected as the root port or designated port, it enters the Listening state.
The port enters the Learning state after the Forward Delay timer expires. After another Forward Delay timer, the port enters the Forwarding state.
If a port is no longer the root port or designated port, it enters the Blocking state.
The port is disabled or the link is terminated.
Disabled
Blocking
Listening
1
Learning
Forwarding
2
3
3
4
4
4
5
5
5
5
Forward Delay: 15s
Forward Delay: 15s
Notes: STP defines five port states: Disabled, Blocking, Listening, Learning, and Forwarding, depending on whether the port can receive and send STP BPDUs and whether the port can forward user data frames.
  Disabled: The port cannot receive or send any frame. That is, the port does not process BPDUs or forward user data frames. The port is in Down state.
  Blocking: The port can only receive and process BPDUs but cannot send BPDUs or forward user data frames.
  Listening: The port can receive and send BPDUs but cannot learn MAC addresses or forward user data frames. This is a transitional state. It is used to determine the port role, elect the root bridge, root port, and designated port, and prevent temporary loops.
  Learning: The port can receive and send BPDUs, learn MAC addresses, and create a MAC address table based on received user data frames. However, the port cannot forward user data frames. This is a transitional state, which is used to prevent the flooding of a large number of user data frames on the network when the MAC address table is not created.
  Forwarding: Ports can receive and send BPDUs, or they can learn MAC addresses, while forwarding user data frames. Only the root port and designated port can enter the Forwarding state.

## Slide 10
Notes: Port state transition:
  When an STP switch port is initially started, it changes from the Disabled state to the Blocking state. In the Blocking state, the port only receives and analyzes BPDUs, but does not send BPDUs.
  During the entire process, a port enters the Disabled state once it is shut down or a link fault occurs.
  If the port is selected as the root port or designated port, the port enters the Listening state. In this state, the port receives and sends BPDUs. This state lasts for an interval of the Forward Delay timer (15s by default), which prevents temporary loops. Temporary loops may occur on the network because the calculation processes of the STP trees are not synchronized.
  If a port is determined as a non-root port or a non-designated port during port state transition, the port immediately returns to the Blocking state.
  If the port does not return to the Disabled state due to an exception, the port enters the Learning state. In this case, the port can receive and send BPDUs and start to construct a MAC address table to prepare for forwarding user data frames. This state lasts for an interval of the Forward Delay timer. This prevents a large number of user data frames from being flooded before the MAC address table of the switch is established.
  Finally, the port enters the Forwarding state and starts to forward user data frames.

## Slide 11: Disadvantages of STP
STP ensures a loop-free network but is slow to converge, leading to service quality deterioration. If the network topology changes frequently, connections on the STP network are frequently torn down, causing frequent service interruption.
STP has the following disadvantages:
  STP does not differentiate between port roles according to their states, making it difficult for less experienced administrators to learn about and deploy this protocol.
    Ports in Listening, Learning, and Blocking states are the same for users because they are all prevented from forwarding service traffic.
    In terms of port use and configuration, the essential differences between ports lie in the port roles but not port states.
  The STP algorithm does not determine topology changes until the timer expires, delaying network convergence.
  The STP algorithm requires the root bridge to send configuration BPDUs after the network topology becomes stable, and other devices process and spread the configuration BPDUs through the entire network. This also delays convergence.

## Slide 12: STP Dependency on Timers
Initialization
SW2
SW3
SW1 (root bridge)
D
D
R
D
R
STP uses a timer to prevent temporary loops. After STP elects a port role, even if the port is a designated port or a root port, it still needs to wait for two intervals of the Forward Delay timer (30s) before forwarding packets.
Terminal Access
In the STP environment, after a terminal or server is connected to the network, the port needs to switch from the Disabled state to the Blocking, Listening, Learning, and Forwarding states in sequence. In this case, HostA needs to wait for two intervals of the Forward Delay timer before accessing the network service.
SW2
SW3
SW1 (root bridge)
D
D
R
D
R
New access device
HostA

## Slide 13: Slow STP Reconvergence
Direct Link Fault
SW2
SW1 (root bridge)
D
The blocked port changes from the Blocking state to the Listening and Learning states in sequence, and finally enters the Forwarding state.
If the directly connected link is faulty, the port status changes to Forwarding after 30s.
Indirect Link Fault
Because the blocked port does not receive BPDUs with a higher priority, the port changes from Blocking to Listening, Learning, and Forwarding in sequence after 20s.
If the indirect link is faulty, the recovery time is about 50s, which is equal to the value of the Max Age timer plus twice the value of the Forward Delay timer.
SW2
SW3
SW1 (root bridge)
D
D
R
D
R
D
R
Notes: Direct link fault:
  There are two links between two switches. One is the active link and the other is the standby link.
  When the network is stable, SW2 detects that the link of the root port is faulty. The blocked port starts the port state transition and finally enters the Forwarding state to forward user traffic.
Indirect link fault:
  When the network is normal, the blocked port of SW3 periodically receives BPDUs from the root bridge.
  When the link between SW1 and SW2 is faulty, SW2 can detect the fault immediately. In this case, SW2 considers itself as the new root bridge and sends its own configuration BPDU to SW3. The root bridge ID is its own bridge ID.
  The blocked port on SW3 receives the configuration BPDU, but the configuration BPDU is inferior to the configuration BPDU buffered on the port. Therefore, SW3 ignores the configuration BPDU.
  When the Max Age timer expires, the configuration BPDUs buffered on SW3 age and SW3 starts to send configuration BPDUs to SW2. The configuration BPDUs are triggered by the configuration BPDUs sent by the root bridge SW1. The value of the root bridge ID field in the configuration BPDUs is the bridge ID of SW1.
  After SW2 receives the configuration BPDU, it parses the BPDU and determines that SW1 is the root bridge. Therefore, SW2 changes the port connected to SW3 to the root port.

## Slide 14: STP Topology Change Mechanism
The STP topology change mechanism transmits topology change information to the root bridge, and then the root bridge floods the topology change information to downlink devices.
Root bridge
Configuration BPDU with the TCA bit set to 1
Configuration BPDU with the TC bit set to 1
TCN BPDU
1. TCN BPDU
Send TCN BPDUs and configuration BPDUs with the TCA bit set to 1
Root bridge
3. Configuration BPDU
with the TC bit set to 1
Root bridge sends configuration BPDUs with the TC bit set to 1
New switch
2. Configuration BPDU
with the TCA bit set to 1
New switch
Delete MAC address entries
Delete MAC address entries
Delete MAC address entries
Delete MAC address entries
Delete MAC address entries
Delete MAC address entries
Notes: STP processing when the topology changes:
  When a switch detects a topology change, it notifies the root bridge of the spanning tree. The root bridge then floods the topology change information to the entire network.
  Topology change process:
    If a switch is added to the network and the working topology changes, the switch at the change point can directly detect the change through the port status, but other switches cannot directly detect the change.
    The switch at the change point continuously sends TCN BPDUs to the uplink device through the root port at an interval of Hello time (2s by default) until it receives the configuration BPDUs with the TCA bit set to 1 from the uplink switch. The TCA bit is set to 1 to instruct the downlink device to stop sending TCN BPDUs.
    After receiving a TCN BPDU, the uplink switch replies with a configuration BPDU with the TCA bit set to 1 through the designated port and sends TCN BPDUs to the uplink switch through the root port at an interval of Hello time.
    This process repeats until the root bridge receives a TCN BPDU.
    After receiving the TCN BPDU, the root bridge sends a configuration BPDU in which the TC bit is set to 1 to notify all switches of the network topology change and instruct downlink devices to delete the bridge MAC address entry.

## Slide 15
Introduction to RSTP
  STP Review and Defects
  RSTP Overview
Improvements Made in RSTP
Working Mechanism of RSTP
RSTP Configurations

## Slide 16: RSTP Overview
RSTP defined in IEEE 802.1w was developed based on STP. RSTP optimizes STP in many aspects, provides a faster convergence speed, and is compatible with STP.
RSTP has the following improvements:
  Defines additional port roles to simplify the learning and deployment of STP.
  Redefines port states.
  Changes the configuration BPDU format and uses the Flags field to describe port roles.
  Processes configuration BPDUs differently from STP.
  Provides fast convergence.
  Adds protection functions.
Notes: RSTP can interoperate with STP, but doing so causes RSTP to lose its advantages, such as fast convergence.
  On a network with both STP-capable and RSTP-capable devices, STP-capable devices discard RST BPDUs. If a port on an RSTP-capable device receives a configuration BPDU from an STP-capable device, the port switches to the STP mode and starts to send configuration BPDUs after two Hello timer intervals.
  After STP-capable devices are removed, Huawei RSTP-capable devices can be switched back to the RSTP mode.

## Slide 17: RSTP Application on a Campus Network
...
...
...
Layer 3 network
Layer 2 network
RSTP
Internet

## Slide 18
Introduction to RSTP
Improvements Made in RSTP
Working Mechanism of RSTP
RSTP Configurations

## Slide 19: Improvement 1: Port Role
RSTP defines additional port roles to simplify the learning and deployment of the protocol.
R
Root port
D
Designated port
A
Alternate port
SW1 (root bridge)
SW2
SW3
D
D
R
R
A
D
SW1 (root bridge)
SW2
SW3
D
D
R
R
D
B
Alternate port
The alternate port is blocked after learning a configuration BPDU sent by another bridge. It is a backup of the root port and provides an alternate path from the designated bridge to the root switch.
Backup port
The backup port is blocked after learning a configuration BPDU sent by itself. It is a backup of the designated port and provides a backup path from the root switch to the corresponding network segment.
R
Root port
D
Designated port
B
Backup port
Notes: RSTP defines four port roles: root port, designated port, alternate port, and backup port.
The functions of the root port and designated port are the same as those defined in STP. The alternate port and backup port are defined as follows:
  From the perspective of configuration BPDU transmission:
    An alternate port is blocked after learning a configuration BPDU sent from another bridge.
    A backup port is blocked after learning a configuration BPDU sent from itself.
  From the perspective of user traffic:
    An alternate port acts as a backup of the root port and provides an alternate path from the designated bridge to the root bridge.
    A backup port backs up a designated port and provides a backup path from the root bridge to the related network segment.
After roles of all RSTP ports are determined, the topology convergence is completed.

## Slide 20: Improvement 2: Port States
RSTP defines three states, depending on whether a port forwards user traffic and learns MAC addresses.
  Discarding: The port does not forward user traffic or learn MAC addresses.
  Learning: The port does not forward user traffic but learns MAC addresses.
  Forwarding: The port forwards user traffic and learns MAC addresses.
STP Port State | RSTP Port State | Port Role
Forwarding | Forwarding | Root port or designated port
Learning | Learning | Root port or designated port
Listening | Discarding | Root port or designated port
Blocking | Discarding | Alternate port or backup port
Disabled | Discarding | Disabled port

## Slide 21: Improvement 3: Configuration BPDU — RST BPDU
RSTP configuration BPDUs use the Flag field in STP BPDUs to determine the port role.
RSTP has the following changes except that the format of RSTP is the same as that of STP:
  The value of the Type field is changed from 0 to 2. Devices running STP will discard configuration BPDUs sent from devices running RSTP.
  The Flags field uses the six bits reserved in STP. This configuration BPDU is called a Rapid Spanning Tree Bridge Protocol Data Unit (RST BPDU).
RST BPDU format:
PID | PVI | BPDU Type | Flag | Root ID | RPC | Bridge ID | Port ID | Message Age | Max Age | Hello Time | Forward Delay
0x02
Bit7 | Bit6 | Bit5 | Bit4 | Bit3 | Bit2 | Bit1 | Bit0
TCA | Agreement | Forwarding | Learning | Port Role |  | Proposal | TC
Topology Change
Acknowledgment Flag
Topology Change Flag
Port Role= 00 Unknown
01 Alternate/Backup port
10 Root port
11 Designated port
Notes: The format of an RST BPDU is different from that of an STP configuration BPDU, including the BPDU type and Flag field.
  BPDU Type: 1 byte. The value of an RST BPDU is 0x02.
  Flag: 1 byte
    Bit 7: TCA, indicating that the topology change is acknowledged
    Bit 6: Agreement, which is used in the P/A mechanism
    Bit 5: Forwarding
    Bit 4: Learning
    Bits 3 and 2: port role
    00 — unknown port
    01 — alternate or backup port
    10 — root port
    11 — designated port
    Bit 1: Proposal, which is used in the P/A mechanism
    Bit 0: TC, indicating a topology change

## Slide 22: Improvement 4: Configuration BPDU Processing (1)
SW2
SW3
SW1 (root bridge)
Hello Time: 2s
Hello Time: 2s
Hello Time: 2s
Configuration BPDU Transmission After the Topology Becomes Stable
RSTP improves the transmission mode of configuration BPDUs.
RSTP allows non-root bridges to send configuration BPDUs at an interval of Hello Time after the topology becomes stable, regardless of whether they have received configuration BPDUs from the root bridge.
RST BPDU
In STP, the root bridge sends configuration BPDUs at an interval of Hello Time after the topology becomes stable. Non-root bridges send configuration BPDUs only after they receive configuration BPDUs from uplink devices. This complicates the STP calculation and slows down network convergence.

## Slide 23: Improvement 4: Configuration BPDU Processing (2)
SW2
SW3
SW1 (root bridge)
Shorter BPDU Timeout Interval
If a port does not receive any configuration BPDU from the uplink device within the timeout interval (three intervals of the Hello timer), the device considers that the negotiation with the neighbor fails.
After 6s, the device considers the neighbor invalid and sends its own RST BPDU.
RST BPDU
STP needs to wait for the time specified by the Max Age timer.
Unidirectional link fault
LINK

## Slide 24: Improvement 4: Configuration BPDU Processing (3)
SW2
SW3
SW1 (root bridge)
If SW2 does not receive any RST BPDU from the uplink device, it considers itself as the root bridge and sends its own BPDU.
RST BPDU
Link fault
After receiving an inferior BPDU, SW3 compares it with the cached RST BPDU and immediately responds with its own RST BPDU.
Processing an Inferior BPDU
When a port receives an RST BPDU from the uplink designated bridge, the port compares the cached RST BPDU with its own RST BPDU.
If the number of RST BPDUs cached on the port is superior to the received RST BPDU, the port discards the received RST BPDU and immediately responds with the cached RST BPDU. This speeds up network convergence.
In STP, only the designated port can process the inferior BPDU immediately.
Notes: STP
  In STP, only the designated port immediately processes inferior BPDUs. Other ports ignore the inferior BPDUs. After the Max Age timer expires, the buffered inferior BPDUs age out and these ports send their superior BPDUs to implement a new round of topology convergence.
RSTP
  RSTP processes inferior BPDUs without using any timer (no longer depending on BPDU aging) to implement topology convergence. In addition, any port in RSTP can process inferior BPDUs to speed up topology convergence.

## Slide 25: Improvement 5: Fast Convergence Mechanism (1)
Fast Switchover of the Root Port
If a root port fails, the best alternate port becomes the root port and enters the Forwarding state. This is due to the fact that the network segment connected to this alternate port has a designated port that can access the root bridge.
R
SW1 (root bridge)
SW2
SW3
D
D
R
R
A
D
Fast Switchover of the Designated Port
If a designated port fails, the best backup port becomes the designated port and enters the Forwarding state. A backup port backs up a designated port and provides a backup path from the root bridge to the related network segment.
SW1 (root bridge)
SW2
SW3
D
D
R
R
D
B
R
Root port
D
Designated port
A
Alternate port
R
Root port
D
Designated port
B
Backup port
D

## Slide 26: Improvement 5: Fast Convergence Mechanism (2)
Edge Port
RSTP introduces the edge port. If a port is located at the edge of a network and directly connects to a terminal, it can be configured as an edge port.
An edge port does not participate in RSTP calculation and can directly enter the Forwarding state from the Discarding state.
An edge port becomes a common STP port once it is connected to a switching device and receives a configuration BPDU. The spanning tree needs to be recalculated, which leads to network flapping.
E
Edge port
SW2
SW3
SW1 (root bridge)
E
Notes: The Up and Down states of an edge port do not change the network topology.

## Slide 27: Improvement 5: Fast Convergence Mechanism (3)
P/A Mechanism
The Proposal/Agreement (P/A for short) mechanism enables the uplink port to quickly transition to Forwarding state.
In RSTP, after a port is elected as the designated port, the port enters the Discarding state and then rapidly enters the Forwarding state through the P/A mechanism.
In STP, the port enters the Forwarding state after at least one interval of Forward Delay (Learning state).
SW2
SW3
SW1 (root bridge)
Proposal=1
Agreement=1
RST BPDU
D
R
Rapidly enter the Forwarding state
Rapidly enter the Forwarding state
Notes: Although STP can select designated ports quickly, to prevent loops, all ports must wait at least one interval of the Forward Delay timer before forwarding traffic.
RSTP solves this problem by blocking non-root ports to prevent loops. The P/A mechanism shortens the time that an uplink port waits before transitioning to Forwarding state.

## Slide 28: P/A Mechanism (1)
A link is added between root bridge SW1 and SW2.
The three downlink ports of SW2 are the alternate port, designated port in Forwarding state, and edge port, respectively.
The two ports between SW1 and SW2 become designated ports and send RST BPDUs.
SW2
Root bridge
SW1
D
A
E
1
Add a link
SW2
Root bridge
SW1
D
A
E
D
D
Send RST BPDUs
2

## Slide 29: P/A Mechanism (2)
SW2
Root bridge
SW1
D
3
A
E
D
R
SW2’s port connected to SW1 receives a superior RST BPDU, so the port becomes a root port and stops sending RST BPDUs.
The designated port of SW1 enters the Discarding state and sends an RST BPDU with the Proposal bit set to 1.
(Blocked port)
(Port status not changed)
SW2
Root bridge
SW1
D
A
E
D
R
(Port status not changed)
After receiving the RST BPDU with the Proposal bit set to 1 from the root bridge, SW2 starts to synchronize all its ports.
After all ports are synchronized, all downlink ports (except edge ports) enter the Discarding state, and the uplink root port enters the Forwarding state and returns an RST BPDU with the Agreement bit set to 1 to SW1.
Proposal=1
SW1 and SW2 compare the received RST BPDUs.
Agreement=1
The downlink port enters the synchronization state, and the root port enters the Forwarding state.
4
Notes: The downlink ports of SW2 are synchronized as follows: The alternate port status remains unchanged; the edge port does not participate in calculation; the non-edge designated port is blocked.

## Slide 30: P/A Mechanism (3)
The RST BPDU with the Agreement bit set to 1 received by SW1 is a response to the sent RST BPDU with the Proposal bit set to 1 on SW1. Therefore, the designated port immediately enters the Forwarding state.
The downlink device continues P/A negotiation.
SW2
Root bridge
SW1
D
5
A
E
D
R
The designated port immediately enters the Forwarding state.
SW2
Root bridge
SW1
D
6
A
E
D
R
The downlink device continues the P/A process.

## Slide 31: Improvement 6: Topology Change Mechanism
RSTP considers that the network topology has changed when a non-edge port transitions to the Forwarding state.
Topology Change Mechanism
When detecting a topology change, RSTP devices react as follows:
  The local device starts a TC While timer on each non-edge designated port and root port. The TC While timer value is twice the Hello Time value. Within the TC While time, the local device deletes MAC address entries learned on ports whose states have changed.
  These ports send out RST BPDUs with the TC bit set to 1. When the TC While timer expires, the ports stop sending RST BPDUs.
  When other switches receive RST BPDUs, they clear MAC address entries learned on all their ports except the ports that receive the RST BPDUs. These switches also start a TC While timer on each non-edge designated port and repeat the preceding process.
In this manner, RST BPDUs are flooded on the network.
SW2
SW3
SW1 (root bridge)
R
R
D
D
D
A
Enable the timer and clear the MAC addresses learned by the port.
Send RST BPDUs with the TC bit set to 1.
Clear the MAC addresses learned by all ports except the receive port.
Perform steps 2 and 3.
RST BPDU, TC=1
Delete MAC addresses
A link fails.
Notes: If the topology of an STP network changes, TCN BPDUs are first sent to the root bridge. Then, the root bridge notifies the topology change and floods the configuration BPDUs with the TC bit set to 1.
RSTP uses a new topology change mechanism to rapidly flood RST BPDUs with the TC bit set to 1.
In the figure:
  If the root port of SW3 cannot receive RST BPDUs from the root bridge, the alternate port quickly becomes the new root port, starts the TC While timer, and clears MAC addresses learned by all ports. Then, the new root port sends RST BPDUs with TC bits set to 1.
  After receiving the RST BPDU, SW2 clears the MAC addresses learned by all ports except the receive port, starts the timer, and sends the RST BPDU with the TC bit set to 1.
  RST BPDUs are flooded on the entire network.

## Slide 32: Improvement 7: Protection Functions (1)
BPDU protection
On an RSTP network, an edge port does not receive RST BPDUs in normal situations. If a switching device receives malicious RST BPDUs on an edge port, the switching device automatically sets the edge port to a non-edge port and performs STP calculation. This causes network flapping.
BPDU protection enables a switch to set the state of an edge port to Error-Down if the edge port receives an RST BPDU. In this case, the port remains as the edge port, and the switch sends a notification to the NMS.
SW2
SW3
SW1 (root bridge)
E
New device's
RST BPDU
Enable BPDU protection
Device occupied by a malicious user
RST BPDU
Notes: On a switching device, ports directly connected to a user terminal such as a PC or file server are edge ports.
As shown in the figure:
  SW3 is connected to a host and is configured as an edge port.
  Then the host is used by a malicious user to forge RST BPDUs to attack SW3. Therefore, the edge port receives the RST BPDUs, loses the edge port role, and calculates the spanning tree.

## Slide 33: Improvement 7: Protection Functions (2)
Root protection
If root protection is enabled on a designated port, the port role cannot be changed.
Once a designated port that is enabled with root protection receives superior RST BPDUs, the port enters the Discarding state and does not forward packets. If the port does not receive any superior RST BPDUs within a specified period (two intervals of the Forward Delay timer by default), the port automatically enters the Forwarding state.
Root protection ensures that the role of the root bridge does not change due to network problems.
RST BPDU
SW2
SW3
SW1 (root bridge)
Device occupied by a malicious user
Superior
RST BPDU
D
Enable root protection
D
Notes: The root bridge on a network may receive superior RST BPDUs due to incorrect configurations or malicious attacks. When this occurs, the root bridge can no longer serve as the root bridge and the network topology will incorrectly change. As a result, traffic may be switched from high-speed links to low-speed links, leading to network congestion.
As shown in the figure:
  When the network is stable, SW1 functions as the root bridge and sends the optimal RST BPDU to downlink devices.
  If SW2 is occupied by a malicious user, for example, the bridge priority of SW2 is modified to make SW2 have a higher bridge priority than SW1, SW2 sends its own RST BPDU.
  After receiving the RST BPDU, the designated port of SW1 recalculates the spanning tree. SW1 then loses its role as the root bridge, causing the topology change.

## Slide 34: Improvement 7: Protection Functions (3)
Loop Prevention
If the root port or alternate port does not receive BPDUs from the uplink device for a long time, the device enabled with loop prevention sends a notification to the NMS. If the root port is used, the root port enters the Discarding state and becomes the designated port. If the alternate port is used, the alternate port keeps blocked and becomes the designated port. In this case, loops will not occur.
After link congestion is cleared or unidirectional link failures are rectified, the port receives BPDUs for negotiation and restores its original role and status.
RST BPDU
SW2
SW3
SW1 (root bridge)
D
D
R
R
A
D
LINK
Enable loop prevention
The unidirectional link is faulty, and packets sent by SW1 cannot reach SW3.
1
2
Loop
3
The alternate port of SW3 becomes the root port and enters the Forwarding state. The root port is switched to the designated port.
Notes: On an RSTP network, a switching device maintains the states of the root port and blocked ports based on RST BPDUs received from the uplink switching device. If the ports cannot receive RST BPDUs from the uplink switching device because of link congestion or unidirectional link failures, the switching device re-selects a root port.
As shown in the figure, when the unidirectional link between SW1 and SW3 fails, because the root port on SW3 does not receive BPDUs from the uplink device within the timeout interval, the alternate port becomes the root port and the root port becomes the designated port. As a result, a loop occurs.

## Slide 35: Improvement 7: Protection Functions (4)
TC BPDU attack defense
After enabling TC BPDU attack defense on a switching device, you can set the number of TC BPDUs that the device can process within a given period of time.
If the number of TC BPDUs that the switching device receives within a given time period exceeds the specified threshold, the switching device processes only the specified number of TC BPDUs.
After the time period expires, the device processes all the excess TC BPDUs in a batch. In this way, the switching device does not need to frequently delete MAC entries.
RST BPDU, TC=1
SW2
SW3
SW1 (root bridge)
R
R
D
D
D
A
Send a large number of RST BPDUs with the TC bit set to 1.
Frequently deleting MAC address entries causes a heavy burden on the device.
Device occupied by a malicious user
Enable TC BPDU attack defense
Notes: A switching device deletes its MAC address entries after receiving TC BPDUs. If an attacker sends a large number of malicious RST BPDU with the TC bit set to 1 to the switching device within a short period, the device will constantly delete MAC address entries. This increases the load on the switching device and threatens network stability.
As shown in the figure:
  If SW3 is occupied by a malicious user, the attacker forges a large number of RST BPDUs with TC bit set to 1 and sends them. After receiving the RST BPDUs, SW2 frequently deletes MAC address entries, which causes a heavy burden.

## Slide 36
Introduction to RSTP
Improvements Made in RSTP
Working Mechanism of RSTP
RSTP Configurations

## Slide 37: RSTP Topology Convergence Process (1)
SW2
SW3
SW1
D
D
D
D
D
D
Designated port
D
BID: 32768.0c-00-00-0a-00-01
BID: 32768.0c-00-00-0a-00-02
BID: 32768.0c-00-00-0a-00-03
RST BPDU
After RSTP is enabled on a switch, the switch considers itself as the root bridge and sends RST BPDUs.
All ports are designated ports and are in Discarding state.
Notes: The RSTP convergence process is similar to the STP convergence process.
During network initialization, all RSTP switches on the network consider themselves as the root bridge, configure each port as a designated port, and send RST BPDUs. SW1 has the optimal bridge ID and is elected as the root bridge.

## Slide 38: RSTP Topology Convergence Process (2)
SW2
SW3
SW1 (root bridge)
Proposal=1
Agreement=1
R
D
D
R
RST BPDU
R
Root port
D
Designated port
Blocked port
The uplink quickly enters the Forwarding state through the P/A mechanism.
After receiving a superior RST BPDU, SW2 considers that SW1 is the root bridge and the port on SW2 becomes the root port instead of the designated port. Then SW2 stops sending RST BPDUs.
The port on SW1 enters the Discarding state and sends RST BPDUs with the Proposal bit set to 1. After receiving the BPDU, SW2 blocks all ports except the edge port. This process is called synchronization.
After ports on SW2 synchronize information, the root port enters the Forwarding state and sends an RST BPDU with the Agreement bit set to 1 to SW1. After SW1 receives the BPDU, the designated port immediately enters the Forwarding state.
Uplink
Downlink
Notes: Each switch that considers itself as the root bridge generates an RST BPDU to negotiate the port status on the specified network segment. The Proposal bit in the Flag field of the RST BPDU needs to be set.
When a port receives an RST BPDU, it compares the received RST BPDU with the local RST BPDU. If the local RST BPDU is superior to the received RST BPDU, the port discards the received RST BPDU and sends a local RST BPDU with the Proposal bit set to 1 to reply to the peer device.
As shown in the preceding figure, the link between SW1 and SW2 is used as an example to describe the uplink convergence process.

## Slide 39: RSTP Topology Convergence Process (3)
SW2
SW3
SW1 (root bridge)
R
D
D
R
Proposal=1
D
A
Uplink
Downlink
The interconnection port of the downlink starts a new round of P/A negotiation.
The downlink port of SW2 is configured as the designated port and continuously sends RST BPDUs with the Proposal bit set to 1.
After receiving the BPDU, the downlink port of SW3 finds that the received BPDU is not the optimal one. Therefore, SW3 ignores the received BPDU and does not send an RST BPDU with the Agreement bit set to 1.
The downlink interface of SW2 does not receive any response packet with the Agreement bit set to 1. SW2 enters the Forwarding state after two intervals of the Forward Delay timer.
RST BPDU
R
Root port
D
Designated port
Blocked port
Notes: The interconnection port of the downlink enters the slow convergence process. SW2 and SW3 are used as an example.

## Slide 40
Introduction to RSTP
Improvements Made in RSTP
Working Mechanism of RSTP
RSTP Configurations

## Slide 41: Basic RSTP Configuration Commands (1)
[Huawei] stp mode { stp | rstp | mstp }
Configure a working mode.
The switch supports three working modes: STP, RSTP, and Multiple Spanning Tree Protocol (MSTP). By default, a switch works in MSTP mode.
[Huawei] stp root primary
(Optional) Configure the switch as the root bridge.
By default, a switch does not function as the root bridge of any spanning tree. After you run this command, the priority value of the switch is set to 0 and cannot be changed.
[Huawei] stp root Secondary
(Optional) Configure the switch as the secondary root bridge.
By default, a switch does not function as the secondary root bridge of any spanning tree. After you run this command, the priority value of the switch is set to 4096 and cannot be changed.

## Slide 42: Basic RSTP Configuration Commands (2)
[Huawei] stp priority priority
(Optional) Configure the STP priority of a switch.
The value ranges from 0 to 61440, with an increment of 4096. By default, the priority value of a switch is 32768.
[Huawei] stp pathcost-standard { dot1d-1998 | dot1t | legacy }
(Optional) Configure a path cost for a port.
Configure a path cost calculation method. By default, the IEEE 802.1t standard (dot1t) is used to calculate the path costs.
All switches on a network must use the same path cost calculation method.
[Huawei-GigabitEthernet0/0/1] stp cost cost
Set the path cost of the port.
Notes: The following describes the supported cost range for different calculation methods:
  dot1d-1998: Uses the IEEE 802.1d-1998 standard to calculate the path cost. The value ranges from 1 to 65535.
  dot1t: Uses the IEEE 802.1t standard to calculate the path cost. The value ranges from 1 to 200,000,000.
  Legacy: Uses Huawei calculation method to calculate the path cost. The value ranges from 1 to 200,000.

## Slide 43: Basic RSTP Configuration Commands (3)
[Huawei-GigabitEthernet0/0/1] stp priority priority
(Optional) Configure the interface priority.
The value is an integer that ranges from 0 to 240, with an increment of 16. By default, the priority of a switch port is 128.
[Huawei] stp enable
Enable STP or RSTP.
By default, STP or RSTP is enabled on a switch.
[Huawei-GigabitEthernet0/0/1] stp edged-port enable
Configure the port as an STP edge port.
By default, all the ports on a switch are non-edge ports.

## Slide 44: RSTP Protection Configuration Commands (1)
[Huawei] stp bpdu-protection
Enable BPDU protection on an edge port of a switch.
By default, BPDU protection is disabled on a switch.
[Huawei-GigabitEthernet0/0/1] stp root-protection
Configure root protection.
By default, root protection is disabled on a port. Root protection takes effect only on designated ports. Root protection and loop prevention cannot be configured on the same port.
[Huawei-GigabitEthernet0/0/1] stp loop-protection
Configure loop prevention on the root port or alternate port.
By default, loop prevention is disabled on a port.

## Slide 45: RSTP Protection Configuration Commands (2)
[Huawei] stp tc-protection interval interval-value
Configure TC BPDU attack defense.
Configure the time for a device to process the maximum number of TC BPDUs. By default, the device processes the maximum number of TC BPDUs at an interval of the Hello timer.
[Huawei] stp tc-protection threshold threshold
Set the number of times that a switch processes received TC BPDUs and updates forwarding entries within a given period of time. By default, the device processes only one TC BPDU within a specified period of time.
Notes: Within the time specified by stp tc-protection interval, the switch processes the number of TC BPDUs specified by stp tc-protection threshold. Packets that exceed this threshold are delayed, so spanning tree convergence may be affected. For example, the period is set to 10s and the threshold is set to 5. After the switch receives TC BPDUs, the switch processes the first five TC BPDUs within 10s. After 10s, the switch processes subsequent TC BPDUs.

## Slide 46: Case: Basic RSTP Configuration (1)
RSTP is configured on the three switches to eliminate Layer 2 loops.
The configuration roadmap is as follows:
  Configure SW1 as the root bridge and SW2 as the secondary root bridge.
  Configure the port connected to the PC as the edge port because this port does not participate in RSTP calculation.
  Configure root protection and BPDU protection to protect devices or links.
[SW1] stp mode rstp
[SW1] stp enable
[SW1] stp root primary
[SW2] stp mode rstp
[SW2] stp enable
[SW2] stp root secondary
[SW3] stp mode rstp
[SW3] stp enable
Enable RSTP on SW1.
Enable RSTP on SW2.
Enable RSTP on SW3.
SW2
SW3
E
GE0/0/1
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/2
PC
E0/0/1
SW1 (root bridge)

## Slide 47: Case: Basic RSTP Configuration (2)
RSTP is configured on the three switches to eliminate Layer 2 loops.
The configuration roadmap is as follows:
  Configure SW1 as the root bridge and SW2 as the secondary root bridge.
  Configure the port connected to the PC as the edge port because this port does not participate in RSTP calculation.
  Configure root protection and BPDU protection to protect devices or links.
[SW3-Ethernet0/0/1] stp edged-port enable
[SW1-GigabitEthernet0/0/1] stp root-protection
[SW1-GigabitEthernet0/0/2] stp root-protection
[SW3] stp bpdu-protection
Enable the edge port on SW3.
Enable root protection on SW1.
Enable BPDU protection on SW3.
SW2
SW3
SW1 (root bridge)
E
GE0/0/1
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
PC
E0/0/1
GE0/0/2

## Slide 48
(Multiple) Which of the following are RSTP port states? ( )
  Idle
  Discarding
  Forwarding
  Learning
(TorF) RSTP root protection must be configured on the root port of the device. ( )
Notes: BCD
False

## Slide 49
STP prevents loops on a LAN. Devices running STP exchange information with one another to discover loops on the network, and block certain ports to eliminate loops. With the growth in scale of LANs, STP has become an important protocol for a LAN.
Based on STP, RSTP has many improvements and greatly speeds up network convergence.
This document describes seven improvements of RSTP compared with STP, including the port role, port status, BPDU format, BPDU processing mode, fast convergence mechanism, topology change mechanism, and four protection features.