## Slide 1
Shi Miaomiao wx791350
2020
New

## Slide 2: Stack and CSS Features of Switches

## Slide 3
As the scale of enterprise networks increase, they pose higher requirements on network reliability, fault recovery time, and device manageability.
Traditional high reliability techniques on campus networks cannot achieve millisecond-level switchover. One active device and one standby device are typically deployed to ensure reliability; however, this deployment causes a great waste of resources. In addition, network management becomes more complex as more network devices are deployed. To build a reliable, easy-to-manage, highly efficient, and easy-to-expand switching network, the stacking and clustering techniques — stack and Cluster Switch System (CSS) — of switches are introduced.
This document mainly describes the stack and CSS implementation and networking modes.

## Slide 4
On completion of this course, you will be able to:
  Describe basic concepts involved in stack and CSS.
  Learn about the process of setting up a stack and CSS.
  Understand the MAD mechanism of stack and CSS.

## Slide 5
Overview of Stack and CSS
Implementation of Stack
Implementation of CSS
Basic Configuration

## Slide 6: Overview of Stack and CSS
A stack can have multiple stacking-capable switches connected through stack cables, which appear as one device when forwarding data.
A CSS combines two clustering-capable switches into a logical switch.
Generally, modular switches set up a CSS, and fixed switches set up a stack. Only two switches are supported in a CSS. The stack and CSS can be used together with link aggregation to build a highly reliable and loop-free campus network.
Stack link
Equivalent to
Virtual device
Eth-Trunk
CSS link
Equivalent to
Eth-Trunk
Stack
CSS
Virtual device

## Slide 7: Stack and CSS Architecture
By leveraging the stack or CSS technique, multiple independent switches are virtualized into a single logical switch. Generally, fixed switches at the access or aggregation layer set up a CSS, and modular switches at the aggregation or core layer set up a CSS.
Eth-Trunks can be deployed between logical switches to achieve high reliability, without the need to deploy STP or VRRP.
The use of Eth-Trunks also improves link utilization by allowing links between devices to transmit traffic simultaneously.
CSS
Stack
Stack
Eth-Trunk
Aggregation layer
Access layer

## Slide 8: Advantages of Stack and CSS (1)
Cluster
Stack
Stack and CSS effectively improve resource utilization, forwarding performance, and link bandwidth.
STP networking
Stack/CSS networking
Core devices work in active/standby mode.
Dual uplinks of each aggregation device work in active/standby mode.
Low device and link utilization
Eth-Trunk
Core devices are virtualized into a logical device and they can forward traffic simultaneously.
All links between the aggregation and core layers are bundled into Eth-Trunks to forward traffic simultaneously.
High device and link utilization

## Slide 9: Advantages of Stack and CSS (2)
CSS
Stack and CSS simplify network planning and management.
STP networking
Stack/CSS networking
It is complex to plan and configure Layer 2 VLANs and STP.
VRRP and STP are used together to implement load balancing between active and standby devices, which are complex to plan and configure.
All devices are managed and configured separately.
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Mgmt
Stack
Stack
Eth-Trunk
Eth-Trunk
Links between logical devices are bundled into Eth-Trunks, removing the need to deploy STP and VRRP.
This networking simplifies network planning and device configuration.
Only the logical devices need to be managed.

## Slide 10: Advantages of Stack and CSS (3)
Stack and CSS greatly reduce the service interruption time.
STP networking
Stack/CSS networking
If a fault occurs, for example, the active device or link is unavailable, an active/standby switchover is performed.
The switchover time depends on the STP convergence time, which is usually several seconds.
CSS
Stack
Eth-Trunk
The failure of a single device or link does not affect service forwarding. Traffic will be switched to other available member links of Eth-Trunks.
Users are unaware of the interruption.

## Slide 11
Overview of Stack and CSS
Implementation of Stack
Implementation of CSS
Basic Configuration

## Slide 12: Basic Concepts of Stack
Switches that join a stack are member switches. In a stack, member switches take on one of the three roles:
  Master switch: manages the stack. A stack has only one master switch.
  Standby switch: is the backup of the master switch. A stack has only one standby switch. If the master switch fails, the standby switch takes over all services from the master switch and assumes the master role.
  Slave switch: forwards service traffic. A stack may have multiple slave switches. The more slave switches in a stack, the higher forwarding performance the stack can provide. Apart from the master and standby switches, all the other member switches are slave switches. If the standby switch becomes unavailable, a slave switch assumes the standby role.
Stack priority: determines the role of a stack member in role election. A higher priority value for a stack member increases the probability of it being elected the stack master.
Stack
Master
Standby
Slave
Slave
Management
priority 200
priority 150
priority 100
priority 100

## Slide 13: Stack ID
A stack ID identifies a stack member and is the slot ID of the member. Each stack member must have a unique stack ID in the stack.
The default stack ID of a device is 0. In a stack, the master switch manages stack IDs of other member switches. When a new member switch joins the stack and its stack ID conflicts with that of another member switch in the stack, the master switch searches for the smallest available stack ID and assigns it to the new member switch.
You are advised to configure stack IDs for stack members before setting up a stack.
GE0/0/2
GE0/0/1
GE0/0/4
GE0/0/3
GE0/0/6
GE0/0/5
GE0/0/8
GE0/0/7
...
...
GE0/0/2
GE0/0/1
GE0/0/4
GE0/0/3
GE0/0/6
GE0/0/5
GE0/0/8
GE0/0/7
...
...
GE0/0/2
GE0/0/1
GE0/0/4
GE0/0/3
GE0/0/6
GE0/0/5
GE0/0/8
GE0/0/7
...
...
Stack ID 0
Stack ID 1
Stack ID 2
GE0/0/2
GE0/0/1
GE0/0/4
GE0/0/3
GE0/0/6
GE0/0/5
GE0/0/8
GE0/0/7
...
...
GE1/0/2
GE1/0/1
GE1/0/4
GE1/0/3
GE1/0/6
GE1/0/5
GE1/0/8
GE1/0/7
...
...
GE2/0/2
GE2/0/1
GE2/0/4
GE2/0/3
GE2/0/6
GE2/0/5
GE2/0/8
GE2/0/7
...
...
Stack (a logical switch)

## Slide 14: Logical Stack Port
Logical stack ports are logical ports used to set up a stack between switches. Each switch supports two logical stack ports: stack-port n/1 and stack-port n/2, where n indicates the stack ID of a member switch.
Multiple stack member ports can be bundled into a logical stack port to improve stack reliability and bandwidth.
Stack member ports of a logical stack port (stack-port n/1) on one switch must be connected to stack member ports of a logical stack port (stack-port m/2) on another switch.
GE1/0/1
GE1/0/2
Switch 1
Stack ID 1
GE2/0/1
GE2/0/2
Switch 1
Stack ID 2
Logical stack port
(stack-port)
1/2
2/1
Notes: If the logical stack ports on two ends (stack-port n/1 on one switch and stack-port m/2 on the other) both contain multiple stack member ports, the stack member ports can be connected in any sequence.

## Slide 15: Stack Setup
Physical connection setup
Master election
Standby switch election
Software version and configuration file synchronization
Multiple switches are connected in a required topology using the appropriate connection mode to establish a stack network.
Member switches exchange stack competition packets and elect the master switch according to master election rules.
The master switch collects topology information from other member switches and assigns them stack IDs. The standby switch is then elected.
The master switch synchronizes the topology of the stack to all member switches, and member switches synchronize their system software and configuration files with the master switch. The stack is then set up.

## Slide 16: Stack Connection Modes
Physical Connection Setup
Master Election
Standby Switch Election
Software Version and Configuration file Synchronization
Stack card connections
Service port connections
Dedicated or integrated stack cards are used, and stack member ports on the cards are connected through dedicated stack cables.
Stack member ports on switches are connected through ordinary Ethernet cables, optical fibers, or dedicated stack cables, and are added to logical stack ports.
Stack port 1
Stack port 2
Switch 1
Stack port 1
Stack port 2
Switch 2
Stack card
Dedicated stack cable
GE1/0/1
GE1/0/2
Switch 1
Stack ID 1
GE2/0/1
GE2/0/2
Switch 1
Stack ID 2
Logical stack port
1/2
2/1
Notes: Each member switch in a stack supports two logical stack ports: stack-port n/1 and stack-port n/2, where n indicates the stack ID of a member switch.

## Slide 17: Stack Topologies
Stack link
Stack link
Stack link
Stack link
Stack link
Master
Chain topology
Ring topology
Member switches are far from one another and a ring topology is difficult to deploy.
Low reliability: If any stack link fails, the stack splits.
Member switches are located near one another. This topology ensures high reliability and high link bandwidth efficiency.
High reliability: If a stack link fails, the topology changes from ring to chain, allowing the stack to function normally.
Master
Standby
Slave
Master
Standby
Slave
Physical Connection Setup
Master Election
Standby Switch Election
Software Version and Configuration file Synchronization

## Slide 18: Master Switch Election
After all member switches are connected and powered on, they elect a master switch.
Rules for electing a master switch
1
2
3
If multiple switches complete startup at the same time, the switch with the highest stack priority becomes the master switch.
If multiple switches complete startup at the same time and have the same stack priority, the switch with the smallest MAC address becomes the master switch.
The switch that starts first becomes the master switch.
The master election timeout interval is 20 seconds. The startup process may take different lengths of time on different member switches. When stack member switches are powered on or restart, some member switches may not participate in the first master election.
Physical Connection Setup
Master Election
Standby Switch Election
Software Version and Configuration file Synchronization

## Slide 19: Standby Switch Election
Topology information collection, stack ID assignment, and standby switch election
1
2
The switch with the highest stack priority becomes the standby switch.
If the switches have the same stack priority, the one with the smallest MAC address becomes the standby switch.
After the master switch is elected, it collects topology information from member switches and assigns a stack ID to each member switch. The standby switch is then elected to operate as a backup for the master switch.
The first switch that completes startup after the master switch becomes the standby switch.
If multiple switches complete the startup at the same time, the standby switch is elected according to the following rules:
Physical Connection Setup
Master Election
Standby Switch Election
Software Version and Configuration file Synchronization

## Slide 20: Software Version and Configuration File Synchronization
Software version and configuration file synchronization; stable running
1
2
Automatic software loading: If the standby and slave switches are running a different software version from that of the master switch, they download the system software of the master switch, restart with the new system software, and rejoin the stack. Member switches must have compatible software versions with one another to set up a stack.
Configuration file synchronization: The standby and slave switches download and apply the configuration files of the master switch. This enables member switches to work like a single switch and ensures that other switches continue working normally if the master switch fails.
After role election and topology information collection are complete, member switches synchronize their system software and configuration files with the master switch. The stack can now run.
Physical Connection Setup
Master Election
Standby Switch Election
Software Version and Configuration file Synchronization

## Slide 21: Stack Management and Configuration File
Stack management
Configuration file
You can log in to a stack using either of the following methods to manage the stack:
Log in through the console port of any stack member.
Log in through any reachable IP address in the stack using Telnet, STelnet, HTTP/HTTPS, or SNMP.
The master switch has the startup and running configuration files for the stack.
The standby switch synchronizes the configuration files with the master switch. If the master switch becomes unavailable, the standby switch takes over with the current running configuration.
Stack
Master
Standby
Slave
Slave
C
C
C
C
C
Console port
IP network
Telnet, STelnet
HTTP/HTTPS SNMP
Stack
Master
Standby
Slave
Slave
Configuration file synchronization
Notes: The configuration files record the following settings:
  System-level (global) settings such as IP, STP, VLAN, and SNMP settings that apply to all stack members. A new switch joining a stack uses the system-level settings of that stack. Likewise, if a device is moved to a different stack, that device loses its startup configuration file and uses the system-level configuration of the new stack.
  Stack member interface-specific settings that are specific for each stack member. The interface-specific configuration of each stack member is associated with its stack ID. If the stack ID changes, the new ID takes effect after that stack member restarts.
    If an interface-specific configuration does not exist for that new ID, the stack member uses its default interface-specific configuration.
    If an interface-specific configuration exists for that new ID, the stack member uses the interface-specific configuration associated with that ID.
A switch will retain its stack configuration after leaving a stack, so it will be elected as the master switch, forming a single-switch stack. To delete the stack configuration, run the reset stack configuration command. The cleared configuration includes:
  Switch slot ID
  Stack priority
  Reserved VLAN ID of the stack
  System MAC address switching delay
  Logical stack port configuration
  Logical stack port rate
  Note that running this command will cause the switch to restart.

## Slide 22: Removing a Stack Member
Depending on the role of the member switch that leaves a stack, the stack is affected in the following ways:
  If the master switch leaves the stack, the standby switch becomes the new master switch. It recalculates topology information, synchronizes updated topology information to the other member switches, and selects a new standby switch. Afterwards, the stack begins to run stably.
  If the standby switch leaves the stack, the master switch selects a new standby switch, recalculates the stack topology, and synchronizes updated topology information to the other member switches. Afterwards, the stack begins to run stably.
  If a slave switch leaves the stack, the master switch recalculates the stack topology and synchronizes updated topology information to the other member switches. Afterwards, the stack begins to run stably.
Stack
Master
Standby
Slave
Slave
Stack
Master
Standby
Slave
An administrator removes stack cables.
Independent running
Notes: A member switch leaves a stack after you disconnect its stack cables and remove it from the stack. When removing a member switch, pay attention to the following points:
  After removing a member switch from a ring stack topology, use a stack cable to connect the two ports originally connected to this member switch to ensure network reliability.
  In a chain topology, removing an intermediate switch will cause the stack to split. Analyze the impact on services before doing so.

## Slide 23: Adding a Switch to a Stack
A new member switch joins a running stack after the following sequence of events:
  The new switch is connected to the stack, is powered on, and starts. It is elected as a slave switch, while the roles of other stack members remain unchanged.
  The master switch updates stack topology information, synchronizes the updated topology information to the other member switches, and assigns a stack ID to the new member switch (if the new member switch has no stack ID configured or the configured stack ID conflicts with that of another member switch).
  The new member switch updates its stack ID, synchronizes its configuration files and system software with the master switch, and then runs stably.
Stack
Master
Standby
Slave
Powered off
Stack
Master
Standby
Slave
Slave
Notes: Note the following when connecting a switch that is powered off to a stack:
  If the stack has a chain topology, add the new switch to either end of the chain to minimize the impact on running services.
  If the stack has a ring topology, tear down a physical link to change the ring topology to a chain topology, add the new switch to either end of the chain, and then connect the switches at two ends to form a ring.

## Slide 24: Stack Merging
Two running stacks can merge into a single stack.
For example, a switch that has the stack configuration and has been powered on (forming a single-switch stack) is connected to a running stack through stack cables. This process is known as stack merging, which is different from the process of adding a member switch to a stack.
Stack
Master
Standby
Master
Stack
Participate in master election
1
Restart after the failure in master election
2
Stack
Master
Standby
Slave
Work as a slave switch
3
All member switches in the stack that fails the master election will restart. Therefore, merging two running stacks that are forwarding traffic is not recommended.
Notes: A single-switch stack is a standalone switch enabled with the stacking function. There is only one member switch in the stack, which operates as the master switch. Only a switch enabled with the stacking function can join a stack or set up a stack with other switches enabled with the stacking function.
The stack merging process is as follows:
  When two stacks merge, both master switches compete to be the master switch of the new stack.
  After a new master switch is elected, the remaining stack members in the same stack as this new master switch retain their roles and configurations, without affecting services.
  Switches in the other stack restart and join the new stack as slave switches. The master switch assigns new stack IDs to these switches. Then these switches synchronize their configuration files and system software with the master switch. During this period, services on these switches are interrupted.

## Slide 25: Stack Split
Stack
If you remove some member switches from a running stack without powering off the switches or if multiple stack cables fail, the stack splits into multiple stacks.
Stack
Master
Standby
Slave
Slave
Stack
Master
Standby
Master
Standby
Scenario 1
The previous master and standby switches are in the same stack after the stack split.
When removed slave switches detect that the timeout timer for stack protocol packets has expired, the switches restart and begin a new master election.
Stack
Stack
Master
Standby
Slave
Slave
Stack
Master
Master
Standby
Slave
Scenario 2
The previous master and standby switches are in different stacks after the stack split.
The previous master switch selects a new standby switch in its stack and updates the stack topology information.
The previous standby switch becomes the new master switch in its stack and selects a new standby switch.

## Slide 26: Problems Caused by a Stack Split
Stack
All member switches in a stack use the same IP address (VLANIF interface address) and MAC address (stack MAC address). After a stack splits, more than one stack may use the same IP address and MAC address. To prevent this situation, a mechanism is required to check for IP address and MAC address collision after a split.
Stack
Master
Standby
Stack
Master
IP address: 192.168.1.1
IP address: 192.168.1.1
Master
In the original stack, the IP and MAC addresses of VLANIF 1 are 192.168.1.1 and the system MAC address, respectively. After the stack splits, both the new stacks use the IP and MAC addresses of VLANIF 1.
Notes: A stack communicates with other network devices as one device using a unique MAC address. This MAC address is known as the stack MAC address.
Generally, the stack MAC address is the MAC address of the master switch. As such, if the master switch is unavailable or leaves the stack, the stack MAC address will be changed 10 minutes later by default. That is, the MAC addresses of the two new stacks are the same within 10 minutes.

## Slide 27: MAD
Multi-active detection (MAD) is a stack split detection protocol. If a stack splits due to a link failure, MAD provides split detection, multi-active handling, and fault recovery mechanisms to minimize the impact of a stack split on services.
MAD can be implemented in direct or relay mode. Direct and relay modes cannot be both configured in the same stack.
Stack
Stack
Master
Master
MAD link
MAD packet
Stack split
1
Competition
2
Stack
Stack
Master
Master
Fail in the competition
3
Physical port disabling
4
MAD process
Notes: The new stacks send MAD packets over a MAD link (an ordinary cable, which is manually configured as a MAD link) for competition. The stack that fails in the competition shuts down all physical ports (except the manually configured reserved ports) on its member switches to prevent IP or MAC address conflicts.
The MAD process is as follows:
  After a stack splits, the new stacks have the same IP address and MAC address (stack MAC address). As a result, network entries, such as ARP entries and MAC address entries of downstream devices, are incorrect, causing service exceptions.
  When MAD is enabled, the new stacks compete through the MAD link.
  The stack that fails in the competition shuts down all physical interfaces on its member switches to prevent IP or MAC address conflicts.

## Slide 28: MAD: Direct Mode
In direct mode, stack members use directly connected ordinary cables as dedicated MAD links. When the stack is running properly, member switches do not send MAD packets. After the stack splits, member switches each send a MAD packet every 1 second over a MAD link to check whether more than one master switch exists.
Stack
MAD link
Stack
MAD link
Directly connected to an intermediate device
Fully meshed with each other
All member switches are directly connected to an intermediate switch through ordinary cables.
In the full-mesh topology, at least one MAD link exists between any two member switches.
Notes: The use of an intermediate device can shorten the MAD links between member switches. This topology applies to stacks with a long distance between member switches.
The full-mesh topology prevents MAD failures caused by intermediate device failures, but occupies many interfaces on the member switches. Therefore, this topology applies to stacks with only a few member switches.

## Slide 29: MAD: Relay Mode
In relay mode, MAD relay detection is configured on an Eth-Trunk interface in the stack, and the MAD detection function is enabled on an agent. Each member switch must have a link to the agent, and these links must be added to the same Eth-Trunk. In contrast to the direct mode, the relay mode does not require additional interfaces because the Eth-Trunk interface can run other services while performing MAD relay detection.
Stack
MAD link
Eth-Trunk
MAD relay agent
Independent relay agent
Stack
MAD link
Eth-Trunk
Stack
Two stacks acting as each other's relay agent
Notes: In relay mode, when the stack is running properly, member switches send MAD packets at an interval of 30 seconds over the MAD links and do not process the received MAD packets. After the stack splits, the new stacks send MAD packets at an interval of 1 second over MAD links to check whether more than one master switch exists.

## Slide 30: Multi-Active Handling (1)
After a stack splits, the new stacks send MAD packets to perform MAD competition, and set their states to Detect or Recovery according to the competition result.
  Detect: The competition is successful, and the stack is working properly.
  Recovery: The competition fails. The stack that fails in the competition shuts down all physical ports except the manually configured reserved ports on member switches, and no longer forward service packets.
Stack
Stack
Detect
Recovery
All physical ports except reserved ones are shut down.

## Slide 31: Multi-Active Handling (2)
MAD competition rules
MAD competition follows similar guidelines to master switch competition.
2
When the stacks complete their startup at the same time, the stack in which the master switch has the highest stack priority enters the Detect state.
3
When the master switches in the stacks have the same stack priority, the stack with the smallest MAC address enters the Detect state.
1
The stack that completes its startup first enters the Detect state. If the difference in the time points when multiple stacks complete their startup is within 20 seconds, the stacks are considered to complete their startup at the same time.

## Slide 32: Master/Standby Switchover
If you want another switch in the stack to be the master switch, you can perform a master/standby switchover by running a command to change this switch to the new master switch.
In addition, a master/standby switchover can be triggered if the master switch restarts due to a fault.
Stack
Master
Standby
Slave
Restarts due to a fault
1
Stack
Master
Slave
The previous standby becomes the new master
2
Stack
Master
Standby
Becomes the new standby
3
Slave
Restarts and becomes a slave
4
Notes: The previous standby switch becomes the new master switch.
The new master switch selects a standby switch.
The previous master switch restarts, rejoins the stack, and becomes a slave switch.

## Slide 33: Stack Upgrade
A stack supports three upgrade methods:
  Intelligent upgrade: When a stack is set up or a new switch is added to the stack, standby and slave switches or the switch automatically synchronizes the system software with the master switch.
  Traditional upgrade: similar to an ordinary device upgrade. You need to specify the startup system software on the master switch and restart the entire stack to upgrade the software of member switches. This process will cause lengthy service interruptions.
  Smooth upgrade: A stack is divided into an active area and a backup area. Member switches in the two areas are upgraded in turn. The uplinks and downlinks of the stack work in redundancy mode, and the active and standby links are in the active and backup areas, respectively. In this way, services are not interrupted during the upgrade.
Stack
Master
Standby
Backup
Active
Eth-Trunk
Upgrade the switch in the backup area
1
Stack
Master
Standby
Backup
Active
Upgrade the switch in the active area
2
Smooth upgrade process
Notes: Active area: area where the master switch is located.
A smooth upgrade goes through three phases:
  The master switch issues the smooth upgrade command to the entire stack. Member switches in the backup area restart with the new system software.
  Member switches in the backup area set up an independent stack running the new system software and notify member switches in the active area. The master switch in the backup area starts to control the stack, and traffic is transmitted through the backup area. The active area then starts the upgrade.
  Member switches in the active area restart with the new system software and join the stack set up in the backup area. The master switch in the backup area displays the upgrade result depending on the stack setup result.

## Slide 34: Inter-device Link Aggregation (1)
A stack supports inter-device link aggregation, which allows physical interfaces on different member switches to bundle into an Eth-Trunk interface.
If a member link of an Eth-Trunk or a member switch fails, traffic on this link or switch can be distributed to other member links through the stack cables connecting member switches. Inter-device link aggregation implements link and device backup and ensures reliable data transmission.
Stack
Master
Standby
Eth-Trunk
Data forwarding paths when links and stacked devices are operating normally

## Slide 35: Inter-device Link Aggregation (2)
Eth-Trunk
Stack
Master
Standby
Data forwarding paths when a single uplink fails
Stack
Master
Standby
Data forwarding paths when a stack member fails
Notes: As shown in the figures, when an uplink or a member switch fails, the inter-device link aggregation technology can load balance traffic to other member interfaces through stack cables connecting member switches, thereby improving network reliability.
However, heavy inter-device traffic will greatly increase the load on stack cables.

## Slide 36: Local Preferential Forwarding (1)
Traffic is distributed to different member links of an Eth-Trunk based on traffic characteristics using the load balancing algorithm of link aggregation. For inter-device link aggregation, the outbound and inbound interfaces of packets may be on different member devices. In this case, traffic is forwarded through stack cables between stack members. This increases the load on stack cables and reduces the forwarding efficiency.
Stack
Master
Standby
Load balancing among member links of an inter-device link aggregation
20 Gbit/s
Example: The bandwidth of stack cables between member switches is 10 Gbit/s, and the inter-device traffic rate is 10 Gbit/s, so the load on stack cables is too heavy.
Notes: As shown in the figure, when traffic is load balanced through inter-device link aggregation, some traffic is forwarded through stack cables between member switches. This greatly increases the bandwidth load on stack cables. If the traffic to be forwarded through stack cables exceeds their bandwidth, some packets cannot be transmitted in a timely manner.

## Slide 37: Local Preferential Forwarding (2)
To improve the forwarding efficiency and reduce the load on stack cables, you can enable the local preferential forwarding function on a switch. This function allows traffic reaching the local switch to be preferentially forwarded through a local interface. If the local device has no outbound interface or all outbound interfaces fail, traffic is forwarded through an interface on the other member switch.
Stack
Master
Standby
Local preferential forwarding

## Slide 38
Overview of Stack and CSS
Implementation of Stack
Implementation of CSS
Basic Configuration
Notes: Implementation

## Slide 39: Introduction to CSS
A cluster switch system (CSS) combines two clustering-capable switches into a single logical switch. A CSS is also called a cluster.
CSS and stack are different only in their names and implementations, but they are actually the same function. CSS is used on modular switches, whereas stack is used on fixed switches.
The following mainly describes the peculiarities of CSS compared with stack.
Switches in a CSS appear as a logical switch. They have a unified control plane and are managed in a unified manner.
Physical switches in a CSS use a unified forwarding plane, and share and synchronize forwarding information in real time.
Links between physical switches in a CSS are bundled into a single Eth-Trunk for interconnection with downstream devices.
Characteristics of CSS

## Slide 40: Basic Concepts of CSS
Switches in a CSS are CSS members. Every CSS member plays one the following roles:
  Master switch: manages the CSS.
  Standby switch: acts as a backup to the master switch.
CSS ID: uniquely identifies a CSS member.
CSS link: is dedicated to setting up a CSS for data communication between the CSS master and standby switches.
CSS priority: determines the role of a CSS member in role election. A larger value indicates a higher priority.
CSS
CSS ID: 1
Priority: 2
CSS ID: 2
Priority: 1
Master
Standby
CSS link
Notes: The standby switch acts as a backup to the master switch. If the master switch fails, the standby switch takes over all services from the master switch and assumes the CSS master role. A CSS has only one standby switch.
A CSS link can be one link or a bundle of multiple links.
By default, the CSS ID of a switch is 1. Two switches with the same CSS ID cannot set up a CSS. Before setting up a CSS, you need to manually set the CSS ID of one member switch to 2.
A switch with a higher CSS priority is more likely to be elected as the master switch.

## Slide 41: CSS Control Plane
CSS
A CSS is automatically set up after you connect two switches using CSS cables, enable the CSS function, and complete the CSS configuration on the two switches, and restart them.
The master MPU on the master switch works as the control plane of the CSS and manages the CSS. The master MPU on the standby switch works as the standby control plane of the CSS. The standby MPUs of the master and standby switches work as candidate CSS standby MPUs.
Master MPU
Master MPU
Master switch
Standby switch
CSS link
CSS master MPU
CSS standby MPU
Candidate CSS standby MPU
Standby MPU
Standby MPU
Notes: The master switch in a CSS is elected in the same way as the master switch in a stack, and the other switch is elected as the standby switch.

## Slide 42: Physical Connections of a CSS
The physical connections of a CSS vary according to the CSS technology used:
  Traditional CSS: CSS cards on MPUs or service ports on LPUs are connected to set up a CSS.
  Cluster Switch System Generation 2 (CSS2): CSS cards on switch fabric units (SFUs) are connected to set up a CSS.
Master MPU
LPU
Master MPU
LPU
LPU
Standby MPU
Standby MPU
LPU
Physical member port
Logical CSS port
CSS link
Traditional CSS (service port clustering)
Notes: When service ports are connected to set up a CSS, the number and type of member ports at both ends must be the same, and there is no limitations on the connection sequence.
Service ports can be connected in either of the following ways according to link distribution:
  1+0 networking: Each member switch has one logical CSS port and connects to the other member switch through CSS member ports on one LPU.
  1+1 networking: Each member switch has two logical CSS ports and connects to the other member switch through CSS member ports on two LPUs. CSS links on the two LPUs implement link redundancy, as shown in the figure.
CSS2: CSS cards on SFUs are connected to set up a CSS. In addition to functions supported by traditional CSS, CSS2 supports 1+N backup of MPUs in a CSS.

## Slide 43: Traditional CSS
For modular switches that support only traditional CSS, inter-LPU traffic in a chassis and inter-chassis traffic must pass through MPUs. Therefore, if there is no MPU working normally on a chassis, traffic cannot be forwarded between LPUs on this chassis or from this chassis to another chassis.
LPU
LPU
LPU
LPU
CSS card
MPU
CSS card
MPU
LPU
LPU
LPU
LPU
CSS card
MPU
CSS card
MPU
Setting up a CSS through CSS cards on MPUs
LPU
LPU
LPU
LPU
MPU
MPU
LPU
LPU
LPU
LPU
MPU
MPU
Setting up a CSS through service ports

## Slide 44: CSS2
CSS2-capable modular switches adopt the forwarding-control separation architecture, so inter-LPU traffic in a chassis or inter-chassis traffic no longer needs to pass through MPUs. If a chassis in a CSS does not have any MPU that works properly, traffic forwarding on the chassis is not affected.
CSS2 allows LPUs on two switches in a CSS to forward packets normally as long as one MPU in either switch is running properly. This feature is known as 1+N backup of MPUs in a CSS.
LPU
SFU
MPU
MPU
LPU
CSS card
SFU
CSS card
LPU
SFU
MPU
MPU
LPU
CSS card
SFU
CSS card

## Slide 45
Overview of Stack and CSS
Implementation of Stack
Implementation of CSS
Basic Configuration

## Slide 46: Stack Configuration (1)
[Huawei] interface stack-port member-id/port-id
[Huawei-stack-port0/1] port interface { interface-type interface-number1 [ to interface-type interface-number2 ] } &<1-10> enable
Create a logical stack port and add stack member ports to it.
member-id specifies the stack ID of a member switch. port-id specifies the ID of the local logical stack port, which can be set to 1 or 2.
[Huawei] stack slot slot-id renumber new-slot-id
Configure a stack ID for a member switch.
By default, the stack ID of a member switch is 0. The new stack ID takes effect only after the current configuration is saved and the switch is restarted.
[Huawei] stack slot slot-id priority priority
Configure a stack priority for a member switch.
By default, the stack priority of a member switch is 100.

## Slide 47: Stack Configuration (2)
[Huawei-GigabitEthernet0/0/1] mad detect mode direct
Enable MAD in direct mode in the interface view.
[Huawei] interface eth-trunk trunk-id
[Huawei-Eth-Trunk1] mad detect mode relay
Configure MAD in relay mode when an independent relay agent is used.
In the stack, enable MAD on the Eth-Trunk interface connected to the relay agent.
[Huawei] interface eth-trunk trunk-id
[Huawei-Eth-Trunk1] mad relay
On the relay agent, enable MAD on the Eth-Trunk interface connected to the stack.

## Slide 48: Stack Configuration (3)
[Huawei] mad domain domain-id
Configure MAD in relay mode when two stacks function as each other's MAD relay agent.
By default, the MAD domain ID of a stack is 0.
[Huawei] interface eth-trunk trunk-id
[Huawei-Eth-Trunk1] mad detect mode relay
[Huawei-Eth-Trunk1] mad relay
MAD needs to be enabled on the Eth-Trunk interface connected to the MAD relay agent.
[Huawei] slave switchover
Perform a master/standby switchover.
Set a unique MAD domain ID for each stack.
Enable MAD in relay mode, and configure two stacks as each other's relay agent.

## Slide 49: Stack Configuration (4)
[Huawei] stack timer mac-address switch-delay delay-time
Set a period after which a stack changes its system MAC address.
By default, a stack changes the system MAC address after 10 minutes. When this period is set to 0, no stack MAC address switching will be performed. To configure a stack to change its system MAC address immediately, run the undo stack timer mac-address switch-delay command.
[Huawei] reset stack configuration
Clear all stack configuration.
The following stack configuration will be cleared: switch slot ID, stack priority, stack reserved VLAN, stack MAC address switching delay, logical stack port configuration, and logical stack port rate. For example, when switches are stacked using dedicated stack cables, to ensure that slot IDs are automatically generated for the switches based on the sequence in which dedicated stack cables are connected, you can run this command to clear all stack configuration.
Running this command will cause the stack to split and member switches to restart.

## Slide 50: Example for Configuring a Stack (1)
SW1
SW2
SW3
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/21
GE0/0/22
P1
P2
Stack port 1
Stack port 2
P1
P2
P1
P2
P2
P1
SW1, SW2, and SW3 are stacked in a ring topology.
SW1, SW2, and SW3 are the master, standby, and slave switches respectively. Their stack IDs are 0, 1, and 2, and their stack priorities are 200, 100, and 100, respectively.
[SW1] interface stack-port 0/1
[SW1-stack-port0/1] port interface gigabitethernet 0/0/23 enable
[SW1] interface stack-port 0/2
[SW1-stack-port0/2] port interface gigabitethernet 0/0/24 enable
SW1 configuration:
Configure logical stack ports and add stack member ports to them.
[SW2] interface stack-port 0/1
[SW2-stack-port0/1] port interface gigabitethernet 0/0/24 enable
[SW2] interface stack-port 0/2
[SW2-stack-port0/2] port interface gigabitethernet 0/0/23 enable
SW2 configuration:
GE0/0/23

## Slide 51: Example for Configuring a Stack (2)
SW1
SW2
SW3
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/23
GE0/0/21
GE0/0/22
P1
P2
Stack port 1
Stack port 2
P1
P2
P1
P2
P2
P1
SW1, SW2, and SW3 are stacked in a ring topology.
SW1, SW2, and SW3 are the master, standby, and slave switches respectively. Their stack IDs are 0, 1, and 2, and their stack priorities are 200, 100, and 100, respectively.
[SW3] interface stack-port 0/1
[SW3-stack-port0/1] port interface gigabitethernet 0/0/22 enable
[SW3] interface stack-port 0/2
[SW3-stack-port0/2] port interface gigabitethernet 0/0/21 enable
SW3 configuration:

## Slide 52: Example for Configuring a Stack (3)
SW1
SW2
SW3
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/23
GE0/0/21
GE0/0/22
P1
P2
Stack port 1
Stack port 2
P1
P2
P1
P2
P2
P1
Configure the stack ID and stack priority.
[SW1] stack slot 0 priority 2
SW1 configuration:
[SW2] stack slot 0 renumber 1
SW2 configuration:
[SW3] stack slot 0 renumber 2
SW3 configuration:
Save the configuration, power off SW1, SW2, and SW3, connect them using SFP+ cables, and then power them on.
Connect stack-port 0/1 on one switch to stack-port 0/2 on another switch. Otherwise, the stack will fail to be set up.
SW1, SW2, and SW3 are stacked in a ring topology.
SW1, SW2, and SW3 are the master, standby, and slave switches respectively. Their stack IDs are 0, 1, and 2, and their stack priorities are 200, 100, and 100, respectively.

## Slide 53: CSS Configuration (1)
[Huawei] set css id new-id
Configure a CSS ID for a member switch.
By default, the CSS ID of a member switch is 1. Two switches with the same CSS ID cannot set up a CSS. Therefore, you need to manually set the CSS ID of a member switch to 2 before setting up a CSS.
[Huawei] interface css-port port-id
[Huawei-css-port1] port interface { interface-type interface-number1 [ to interface-type interface-number2 ] } &<1-10> enable
Create a logical CSS port and add CSS member ports to it.
A service port is configured as a CSS member port and added to a logical CSS port.
[Huawei] set css priority priority
Configure a CSS priority for a member switch.
By default, the CSS priority of a member switch is 1.

## Slide 54: CSS Configuration (2)
[Huawei] css enable
Enable the CSS function.
By default, the CSS function is disabled on a switch. When enabling this function, the system asks you whether to restart the switch immediately to make the configuration take effect.
The CSS function must be enabled on both member switches.
[Huawei] set css mode { lpu | css-card }
Set the CSS connection mode.
The default CSS connection mode varies according to the device model.
Notes: The method and command for configuring the MAD function in a CSS are the same as those in a stack.

## Slide 55: Example for Configuring a CSS (1)
SW1
SW2
XGE1/0/1-2
XGE2/0/1-2
XGE1/0/1-2
XGE2/0/1-2
SW1 and SW2 have LPUs installed and are connected through CSS cables. To increase the bandwidth and improve reliability, the two switches are connected through four service ports on two LPUs of each switch.
Set the CSS connection mode on SW1 and SW2, and set their CSS IDs to 1 and 2, respectively. In addition, set their CSS priorities to 100 and 10, respectively, so that SW1 is more likely to be elected as the master switch.
[SW1] set css mode lpu
[SW1] set css id 1
[SW1] set css priority 100
SW1 configuration:
Configure the CSS connection mode, CSS ID, and CSS priority for each member switch.
[SW2] set css mode lpu
[SW2] set css id 2
[SW2] set css priority 10
SW2 configuration:

## Slide 56: Example for Configuring a CSS (2)
[SW1] interface css-port 1
[SW1-css-port1] port interface xgigabitethernet 1/0/1 to xgigabitethernet 1/0/2 enable
[SW1-css-port1] quit
[SW1] interface css-port 2
[SW1-css-port2] port interface xgigabitethernet 2/0/1 to xgigabitethernet 2/0/2 enable
[SW1-css-port2] quit
SW1 configuration:
Configure logical CSS ports.
Configure service ports XGE1/0/1 and XGE1/0/2 on SW1 as CSS member ports and add them to CSS port 1; configure service ports XGE2/0/1 and XGE2/0/2 on SW2 as CSS member ports and add them to CSS port 2.
The SW2 configuration is similar to the SW1 configuration, and is not mentioned here.
SW1 and SW2 have LPUs installed and are connected through CSS cables. To increase the bandwidth and improve reliability, the two switches are connected through four service ports on two LPUs of each switch.
Set the CSS connection mode on SW1 and SW2, and set their CSS IDs to 1 and 2, respectively. In addition, set their CSS priorities to 100 and 10, respectively, so that SW1 is more likely to be elected as the master switch.
SW1
SW2
XGE1/0/1-2
XGE2/0/1-2
XGE1/0/1-2
XGE2/0/1-2

## Slide 57: Example for Configuring a CSS (3)
[SW1] css enable
Warning: The CSS configuration will take effect only after the system is rebooted. The next CSS mode is LPU. Reboot now? [Y/N]:y
[SW2] css enable
Warning: The CSS configuration will take effect only after the system is rebooted. The next CSS mode is LPU. Reboot now? [Y/N]:y
Enable the CSS function.
SW1
SW2
XGE1/0/1-2
XGE2/0/1-2
XGE1/0/1-2
XGE2/0/1-2
SW1 and SW2 have LPUs installed and are connected through CSS cables. To increase the bandwidth and improve reliability, the two switches are connected through four service ports on two LPUs of each switch.
Set the CSS connection mode on SW1 and SW2, and set their CSS IDs to 1 and 2, respectively. In addition, set their CSS priorities to 100 and 10, respectively, so that SW1 is more likely to be elected as the master switch.

## Slide 58
(Essay) What are the differences between stack joining and stack merging?
(Essay) What is the purpose of MAD? What will happen in the stack that fails in MAD competition?
(Essay) What are the differences between CSS2 and traditional CSS?
Notes: Reference answers:
  In the stack joining scenario, a switch has been connected to a running stack through stack cables before being powered on. After the switch is powered on and starts, it becomes a slave switch since the stack already has a master switch. In the stack merging scenario, two stacks are connected through stack cables, and a new master switch is elected for the new stack and updates topology information.
  After a stack-enabled switch is powered on, it becomes a single-switch stack, with itself being the master switch. In this case, if this switch is connected to another stack through stack cables, the two stacks merge. This is a typical difference between stack merging and stack joining.
  If a stack or CSS splits, more than one stack or CSS may use the same IP address and MAC address, which will cause entry conflicts on other network devices. MAD prevents this situation to ensure normal data forwarding. The stack that fails in the MAD competition shuts down all ports except the reserved ones on its member switches. This prevents IP and MAC address conflicts between stacks, thereby preventing entry conflicts on other network.
  CSS2 supports 1+N backup of MPUs. That is, as long as one MPU on any member switch in a CSS is working and the control plane of the cluster is working normally, the data plane of the cluster can forward packets normally.

## Slide 59
The stack and CSS techniques greatly simplify network deployment and management, implement fast deployment of highly reliable and loop-free campus networks, and greatly reduce the impact of network faults.
The MAD function can be configured to prevent forwarding exceptions caused by IP and MAC address conflicts between stacks. MAD can be implemented in direct or relay mode. Member switches in the stack that fails the MAD competition will shut down all physical ports except the reserved ones.
To ensure packet forwarding efficiency, you are advised to configure local preferential forwarding when deploying Eth-Trunks in a stack or CSS.
CSS2 technology uses CSS cards on SFUs to set up a CSS, and supports the 1+N backup of MPUs by leveraging the forwarding-control separation architecture of switches.