## Slide 1
2020.06.13
Ding Yi/dwx66270
2020.03.03
He Junjian/hwx580230
New
Zhu Shigeng/00261992
Update
Update
Update
Update
Update

## Slide 2: ICMPv6 and NDP

## Slide 3
In IPv4, Internet Control Message Protocol (ICMP) allows hosts or devices to report errors. An ICMP message is encapsulated in an IP packet as the data, and forms a complete IP packet together with an IP header. Common ping and tracert commands are implemented based on ICMP.
In IPv6, the Internet Control Message Protocol for IPv6 (ICMPv6) provides functions similar to ICMP and extends it. The Neighbor Discovery Protocol (NDP) is implemented based on ICMPv6. As a key IPv6 protocol, NDP provides functions such as prefix discovery, duplicate address detection (DAD), address resolution, and redirection.
This course describes ICMPv6 and NDP in detail.

## Slide 4
On completion of this course, you will be able to:
  Describe the functions of ICMPv6.
  Describe the ICMPv6 message format.
  Describe ICMPv6 message types.
  Describe the functions of NDP.

## Slide 5
ICMPv6 Introduction
  ICMPv6 Overview
  ICMPv6 Message Format
  ICMPv6 Message Types and Functions
NDP Introduction

## Slide 6: ICMP
ICMP is an auxiliary protocol of IP.
Message
Message
PC1
Type | Code | Checksum
ICMP message content |  | 
Ethernet header | IP header | ICMP message | Ethernet trailer
Type | Code | Description
0 | 0 | Echo Reply
3 | 0 | Network unavailable
3 | 1 | Host unreachable
3 | 2 | Protocol unreachable
3 | 3 | Port unreachable
5 | 0 | Redirection
8 | 0 | Echo Request
ICMP is used to transmit error and control information between network devices. It plays an important role in collecting network information and diagnosing and rectifying network faults.
Notes: ICMP works at the network layer to ensure the correct forwarding of IP packets, and allows hosts or devices to report errors during packet transmission.
ICMP message:
  ICMP messages are encapsulated in IP packets. If the Protocol value in the IP header is 1, the used protocol is ICMP.
  Field description:
    The format of an ICMP message depends on the Type and Code fields. The Type field indicates the message type, and the Code field contains specific parameters of the message type.
    The Checksum field is used to check whether the message is complete.

## Slide 7: ICMP Error Check
ICMP Echo messages are used to check the network connectivity between the source and destination. In addition, they provide other information, such as the round-trip time of packets.
R1
Server 1
R2
10.0.0.0/24
20.0.0.0/24
.1
.2
.1
.2
[R1]ping 20.0.0.2
PING 20.0.0.2: 56 data bytes, press CTRL_C to break
Reply from 20.0.0.2: bytes=56 Sequence=1 ttl=254 time=70 ms
Reply from 20.0.0.2: bytes=56 Sequence=2 ttl=254 time=30 ms
Reply from 20.0.0.2: bytes=56 Sequence=3 ttl=254 time=30 ms
Reply from 20.0.0.2: bytes=56 Sequence=4 ttl=254 time=40 ms
Reply from 20.0.0.2: bytes=56 Sequence=5 ttl=254 time=30 ms
--- 20.0.0.2 ping statistics ---
5 packet(s) transmitted
5 packet(s) received
0.00% packet loss
round-trip min/avg/max = 30/40/70 ms
Echo Request
Echo Reply
Function: ping
Ping is a command used on network devices as well as the Windows, Unix, and Linux platforms. It is a small and practical application based on ICMP.
Ping is often used to check the network reachability to a destination node.
Notes: Ping is a typical application of ICMP. It is a common tool used to check network connectivity and collect information. You can configure various parameters in the ping command, such as the length of ICMP messages, number of sent ICMP messages, and timeout period for waiting for a reply. A device constructs and sends ICMP messages based on the configured parameters to perform a ping test.

## Slide 8: ICMP Error Report
ICMP defines various error messages for diagnosing network connectivity faults. Based on the error messages, the source can determine the cause of a data transmission failure. For example, when a network device cannot access a target network, it automatically sends an ICMP Destination Unreachable message to the sender.
[R1]tracert 10.0.23.2
traceroute to 10.0.23.2, max hops: 30 ,packet length: 40,press CTRL_C to break
1 10.0.12.2 80 ms 10 ms 10 ms
2 10.0.23.2 30 ms 30 ms 20 ms
Packet
ICMP Port Unreachable message
R1
Server 1
R2
10.0.12.0/24
10.0.23.0/24
.1
.2
.1
.2
Function: tracert
Tracert traces the packet forwarding path hop by hop based on the TTL value in the packet header. It is an effective method to check the packet loss and delay and to help administrators find routing loops on a network.

## Slide 9: ICMPv6 Overview
ICMPv6 is one of the basic IPv6 protocols.
If the Next Header field value in the IPv6 header is 58, the used protocol is ICMPv6.
ICMPv6 messages are used to advertise information or errors.
ICMPv6 messages are widely used in other protocols, such as NDP and path MTU discovery.
ICMPv6 controls key IPv6 processes, such as address autoconfiguration, address resolution, address conflict detection, route selection, and error control.

## Slide 10
ICMPv6 Introduction
  ICMPv6 Overview
  ICMPv6 Message Format
  ICMPv6 Message Types and Functions
NDP Introduction

## Slide 11: ICMPv6 Message Format
Message Type | Type | Name | Code
Error messages | 1 | Destination Unreachable | 0: no route to destination
 |  |  | 1: communication with destination administratively prohibited
 |  |  | 2: beyond scope of source address
 |  |  | 3: address unreachable
 |  |  | 4: port unreachable
 | 2 | Packet Too Big | 0
 | 3 | Time Exceeded | 0: hop limit exceeded in transit
 |  |  | 1: fragment reassembly time exceeded
 | 4 | Parameter Problem | 0: erroneous header field encountered
 |  |  | 1: unrecognized Next Header type encountered
 |  |  | 2: unrecognized IPv6 option encountered
Informational messages | 128 | Echo Request | 0
 | 129 | Echo Reply | 0
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header (58) | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
ICMPv6 header | 
ICMPv6 message payload | 
Type
Code
Checksum
Notes: The payload of an ICMPv6 message is determined by its type.
Type: indicates the message type.
Code: depends on the message type.
Checksum: indicates the ICMPv6 message checksum.

## Slide 12
ICMPv6 Introduction
  ICMPv6 Overview
  ICMPv6 Message Format
  ICMPv6 Message Types and Functions
NDP Introduction

## Slide 13: ICMPv6 Message Types
ICMPv6 messages are classified as error or informational messages.
The most significant bit of the Type field in error messages is 0. That is, ICMPv6 Type = [0, 127].
Error messages are used to report errors that occur during IPv6 packet forwarding, such as destination unreachable and timeout.
Error Messages
Informational Messages
The most significant bit of the Type field in informational messages is 1. That is, ICMPv6 Type = [128, 255].
Informational messages can be used to implement inter-node communication on a link and multicast member management on a subnet.

## Slide 14: ICMPv6 Error Message Application — Path MTU Discovery
In IPv6, an intermediate forwarding device does not fragment IPv6 packets, and packet fragmentation is performed on the source node.
Path MTU (PMTU) is the minimum interface MTU on a path.
Path MTU Discovery (PMTUD) is used to discover the MTU on a path, preventing fragmentation when a packet is forwarded from the source to the destination.
With PMTUD, the data sender can use the optimal PMTU discovered to communicate with the destination node. This prevents packets from being fragmented by intermediate routers during transmission from the source to the destination.
PC1
R1
R2
PC2
MTU = 1500 bytes
MTU = 1400 bytes
MTU = 1300 bytes
Packet with
MTU = 1500 bytes
ICMPv6 (Type = 2)
with the MTU of 1400 bytes
ICMPv6 (Type = 2)
with the MTU of 1300 bytes
Packet with
MTU = 1400 bytes
Packet with
MTU = 1300 bytes
1
2
3
4
5
Notes: PC1 sends an IPv6 packet with an MTU of 1500 bytes to PC2.
After checking that the packet is too large and the MTU of the outbound interface is 1400 bytes, R1 sends an ICMPv6 (Type = 2) message with the MTU of 1400 bytes to PC1.
PC1 sends an IPv6 packet with an MTU of 1400 bytes.
After the packet reaches R2, R2 checks that the MTU of the outbound interface is 1300 bytes and sends an ICMPv6 (Type = 2) message with the MTU of 1300 bytes to PC1.
PC1 sends an IPv6 packet with an MTU of 1300 bytes.

## Slide 15: ICMPv6 Informational Message Application — Ping
Ping is implemented based on ICMPv6 informational messages.
  Echo Request: is sent to a destination node, which responds with an Echo Reply message. The Type and Code field values in an Echo Request message are 128 and 0, respectively.
  Echo Reply: After receiving an Echo Request message, ICMPv6 responds with an Echo Reply message. The Type and Code field values in an Echo Reply message are 129 and 0, respectively.
2001:db8::1
2001:db8::2
R1
R2
1
ICMPv6 Echo Request
Type = 128, Code = 0
ICMPv6 Echo Reply
Type = 129, Code = 0
2

## Slide 16: Other Common ICMPv6 Messages
Neighbor Discovery (RFC 2461 and RFC 4861)
  Type = 133: Router Solicitation
  Type = 134: Router Advertisement
  Type = 135: Neighbor Solicitation
  Type = 136: Neighbor Advertisement
  Type = 137: Redirect
Multicast Listener Discovery (RFC 2710 and RFC 3810)
  Type = 130: Multicast Listener Query
  Type = 131: Multicast Listener Report
  Type = 132: Multicast Listener Done
  Type = 143: Version 2 Multicast Listener Report

## Slide 17
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 18: NDP Overview
RFC 2461 defines the IPv6 Neighbor Discovery Protocol (NDP), which is a core component in IPv6. Its functions are as follows:
NDP
Neighbor state tracing
Prefix readdressing
Redirection
Stateless address autoconfiguration
Discovers routers on a link and obtains information advertised by them.
A terminal automatically generates an IPv6 address based on the address prefix advertised by a router.
Discovers neighbors on a link through NDP and traces the neighbor state.
Router discovery
DAD
Detects duplicate addresses and ensures that no address conflict occurs.
Address resolution
Requests the link-layer address corresponding to a destination network address. This function is similar to ARP in IPv4.
A router flexibly sets an advertised address prefix to implement readdressing.
Informs other devices of the optimal next hop to a target network.

## Slide 19: NDP Message Types and Functions
NDP uses the following ICMPv6 messages:
  Router Solicitation (RS)
  Router Advertisement (RA)
  Neighbor Solicitation (NS)
  Neighbor Advertisement (NA)
ICMPv6 Message Function | RS (Type = 133) | RA (Type = 134) | NS (Type = 135) | NA (Type = 136) | Redirect (Type = 137)
Address resolution |  |  | ● | ● | 
Router discovery | ● | ● |  |  | 
Prefix readdressing | ● | ● |  |  | 
DAD |  |  | ● | ● | 
Redirection |  |  |  |  | ●

## Slide 20
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 21: Router Discovery
Router discovery is a process in which a host discovers a router on a local link and determines its configuration.
Router discovery can implement the following functions:
  Router discovery: A host locates neighboring routers and selects a router as the default gateway.
  Prefix discovery: A host discovers a group of IPv6 prefixes on a local link for address autoconfiguration.
  Parameter discovery: A host discovers operation parameters, such as the default hop limit of output packets and address configuration mode.
Used messages:
  RS message
  RA message
The protocol message exchange involves the following situations:
  A host sends RS messages, and routers respond with RA messages.
  Routers periodically send RA messages.

## Slide 22: Router Discovery Process — Triggered by a Host's Request
When a host starts, it sends RS messages to all the routers on a local link, triggering them to respond with RA messages. After discovering routers on the local link, the host automatically configures a router as the default router. In addition, the host sets up the default routing table and prefix list as well as sets other configuration parameters.
000D-88F8-03B0FE80::20D:88FF:FEF8:3B0
00E0-FC86-D6C4 FE80::2E0:FCFF:FE86:D6C4
PC1
R1
1
ICMPv6 Type: 133 (RS)
Source Address: FE80::20D:88FF:FEF8:3B0 Destination Address: FF02::2
ICMPv6 Type: 134 (RA)
Source Address: FE80::2E0:FCFF:FE86:D6C4 Destination Address: FF02::1
2
  A host starts and sends RS messages to all the routers on a local link.
  The routers respond with RA messages.
  After the preceding process is complete, the host generates a default route with the next hop address being the link-local address of the default router.

## Slide 23: Router Discovery Process — Triggered by Routers' Periodic RA Message Sending
Routers periodically send RA messages. The interval for sending RA messages is a random value in a valid range. The default maximum and minimum intervals are 600s and 200s, respectively.
The addresses of these RA messages must meet the following requirements:
  Source Address: must be the link-local address of an outbound interface.
  Destination Address: must be FF02::1.
00E0-FC86-D6C4
4000::1/64 FE80::2E0:FCFF:FE86:D6C4
PC1
R1
PC2
ICMPv6 Type: 134 (RA)
Source Address: FE80::2E0:FCFF:FE86:D6C4 Destination Address: FF02::1 Prefix: 4000::/64
Notes: The ipv6 nd ra { max-interval maximum-interval | min-interval minimum-interval } command configures an interval at which RA messages are sent.

## Slide 24
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 25: Address Resolution
IPv6 address resolution is implemented using ICMPv6 (NS and NA messages).
Layer 3 address resolution has the following advantages:
  Layer 3 address resolution enables Layer 2 devices to use the same address resolution protocol.
  Layer 3 security mechanisms are used to prevent address resolution attacks.
  Request messages can be multicast, reducing loads on Layer 2 networks.
PC1
PC2
000D-88F8-03B0
4000::D4B5:2A08:3AB8:F820
0013-7284-EFDC 4000::213:72FF:FE84:EFDC
ICMPv6 Type: 135 (NS)
Source Address: 4000::D4B5:2A08:3AB8:F820 Destination Address: FF02::1:FF84:EFDC
Target Address: 4000::213:72FF:FE84:EFDC
Source Link-Layer (Option): 000D-88F8-03B0
1
2
ICMPv6 Type: 136 (NA)
Source Address: 4000::213:72FF:FE84:EFDC Destination Address: 4000::D4B5:2A08:3AB8:F820
Target Address: 4000::213:72FF:FE84:EFDC
Target Link-Layer (Option): 0013-7284-EFDC
Notes: In this example, if PC1 wants to send a packet to PC2 but does not know PC2's link-layer address, the following protocol exchange process needs to be performed:
  PC1 sends an NS message with the destination address being PC2's solicited-node multicast address FF02::1:FF84:EFDC. The Option field of the message carries PC1's link-layer address 000D-88F8-03B0 of PC1.
  After listening to the NS message, PC2 checks that the destination address of the message is FF02::1:FF84:EFDC and determines that it is in the multicast group. Therefore, PC2 processes the message. In addition, PC2 updates its neighbor entries based on the source address and source link-layer address option of the NS message.
  PC2 responds to the NS message with an NA message in which the Target Link-Layer option carries the link-layer address 0013-7284-EFDC.
  After receiving the NA message, PC1 obtains PC2's link-layer address and creates a neighbor entry for the target node.
After the preceding process is complete, PC1 and PC2 obtain each other's link-layer addresses and establish neighbor entries, which are similar to ARP entries in IPv4. PC1 and PC2 can then communicate.

## Slide 26
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 27: IPv6 Neighbor State Table
An IPv6 neighbor state table caches the mapping between IPv6 and MAC addresses. You can run the display ipv6 neighbors command to check an IPv6 neighbor state table.
<Huawei>display ipv6 neighbors
-----------------------------------------------------------------------------
IPv6 Address : 2001:DB8::2
Link-layer : 00e0-fc23-26e3 State : REACH
Interface : GE0/0/0 Age : 0
VLAN : - CEVLAN: -
VPN name : Is Router: TRUE
Secure FLAG : UN-SECURE
IPv6 Address : FE80::2E0:FCFF:FE23:26E3
Link-layer : 00e0-fc23-26e3 State : REACH
Interface : GE0/0/0 Age : 0
VLAN : - CEVLAN: -
VPN name : Is Router: TRUE
Secure FLAG : UN-SECURE
-----------------------------------------------------------------------------
Total: 2 Dynamic: 2 Static: 0

## Slide 28: IPv6 Neighbor States
To monitor the state of each neighboring device, IPv6 nodes need to maintain a neighbor table. Five neighbor states are available: Incomplete, Reachable, Stale, Delay, and Probe.
State | Description
Incomplete | A neighbor is unreachable. This state indicates that a device is resolving a neighbor's link-layer address. If the device resolves the address successfully, it sets the neighbor state to Reachable.
Reachable | A neighbor is reachable. This state indicates that a neighbor is reachable within a specified period (30s by default). If the period expires but the neighbor entry is not used, this entry enters the Stale state.
Stale | Whether a neighbor is reachable is unknown. This state indicates that the neighbor entry is not used within a specified period (30s by default). A device does not check a neighbor's reachability unless it sends messages to the neighbor.
Delay | Whether a neighbor is reachable is unknown. A device has sent a message to a neighbor. If the device does not receive any response within a specified period, it sets the neighbor state to Probe.
Probe | Whether a neighbor is reachable is unknown. A device has sent an NS message to a neighbor to check whether the neighbor is reachable. If the device receives an NA message within a specified period, it sets the neighbor state to Reachable. Otherwise, it sets the neighbor state to Incomplete.

## Slide 29: Neighbor State Transition
R2
R1
NS/NA
Empty
Incomplete
Stale
R1 sends an NS message to R2.
R1 receives an NA message from R2.
Keeps idle for 30s
No response within a specified period
Probe
Reachable
Delay
R1 sends an NS message to R2 while sending data to R2.
Response within a specified period
Response
No response
By default, an NS message is sent every 1s. A total of three NS messages are sent.
R1's neighbor states
Notes: R1 sends an NS message and generates a neighbor entry. In this case, the neighbor state is Incomplete.
If R1 receives an NA message from R2, the neighbor state changes from Incomplete to Reachable. Otherwise, the neighbor state changes from Incomplete to Empty after a specified period.
After the neighbor reachable time (30s by default) times out, the neighbor state changes from Reachable to Stale, indicating that the neighbor reachable state is unknown.
  If R1 in the Reachable state receives an unsolicited NA message from R2, and the link-layer address of R2 carried in the message is different from that learned by R1, the neighbor state changes to Stale.
If R1 in the Stale state sends data to R2, the neighbor state changes from Stale to Delay and R1 sends an NS message.
After a specified period expires, the neighbor state changes from Delay to Probe. During this period, if R1 receives an NA message, the neighbor state changes from Delay to Reachable.
R1 in the Probe state sends a specified number of unicast NS messages at a specified interval (1s by default). If R1 receives an NA message, the neighbor state changes from Probe to Reachable. Otherwise, the neighbor state changes to Empty.

## Slide 30
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 31: DAD (1)
DAD enables a node to detect whether an IPv6 address is being used by another node before using this address for an interface. This ensures that no two duplicate unicast addresses exist on a network.
Before any unicast IPv6 address (including a link-local address) is used for an interface, DAD must be performed.
2000::1
Newly allocated address 2000::1
PC1
PC2
ICMP Type = 135 (NS)
Source = ::
Destination = FF02::1:FF00:1
Target Address = 2000::1
Query = Is anyone using this address?
1
2
ICMP Type = 136 (NA)
Source = 2000::1
Destination = FF02::1
Target Address = 2000::1
Answer = I am using this address
X
Duplicate
Notes: DAD is a process in which a node checks whether an address to be used is being used by another node. Before configuring a unicast IPv6 address for an interface automatically, a node must ensure that this address is unique on a local link and is not used by another node. A node sends an NS message onto a local link by default. If a node does not receive an NA message within a specified period, it considers that the temporary unicast address is unique on a local link and can be allocated to an interface. Otherwise, it considers that this address is duplicate and cannot be used.

## Slide 32: DAD (2)
An address is called a tentative address before it passes DAD. An interface cannot use a tentative address for unicast communication.
If DAD is performed for two nodes with the same address configured, the receiver does not use this address when receiving an NS message.
2000::1 (Tentative)
2000::1 (Tentative)
NS
NS
PC1
PC2
Notes: Special scenario: Two hosts are assigned the same IP address. Assume that both PC1 and PC2 want to use the address 2000::1. If PC1 sends an NS message first, PC2 does not send any NS message (or NA message) after receiving the NS message. Instead, PC2 stops using the address 2000::1 and waits for a new address to be generated in other modes. If both PC1 and PC2 receive an NS message, they do not use the address 2000::1.

## Slide 33
ICMPv6 Introduction
NDP Introduction
  NDP Overview
  Router Discovery
  Address Resolution
  Neighbor State Tracing
  DAD
  Redirection

## Slide 34: Redirection
When a sender sends packets to a gateway, the gateway sends a Redirect message to instruct the sender to send packets to another optimal gateway.
PC1
R1
R2
Server
Default gateway: R2
1
2
3
ICMPv6 redirection
Internet
If PC1 wants to send a packet to the server, it sends the packet to the default gateway R2.
After receiving the packet, R2 checks the packet's information and finds that the packet should be forwarded to the optimal gateway R1 that is on the same network segment as PC1. R2 then sends a Redirect message to PC1 to instruct PC1 to send the packet to R1.
After receiving the Redirect message, PC1 sends the packet to R1, which then forwards the packet to the server.

## Slide 35
(Multiple) What are ICMPv6 message types?
  Error messages
  Informational messages
  Other messages
  Parameter messages
(Multiple) Which of the following messages are used to implement IPv6 address resolution?
  RS
  RA
  NS
  NA
Notes: 1. A, B
2. C, D

## Slide 36
ICMPv6 is a basic IPv6 protocol that uses error or informational messages to report errors or information generated during packet processing. Error messages are used to report errors that occur during IPv6 packet forwarding, such as destination unreachable and timeout; informational messages are used to implement various functions, such as router discovery, DAD, and multicast member management.
NDP is implemented using five ICMPv6 informational messages. RS and RA messages are used to implement router discovery, gateway discovery, and address autoconfiguration; NS and NA messages are used to resolve link-layer addresses of neighbors and detect duplicate addresses; Redirect messages are used to implement redirection.