## Slide 1
Ding Yi/dwx66270
2020.03.05
New
Update
Update
Update
Update
Update

## Slide 2: IPv6 Address Configuration

## Slide 3
IPv6 is the core protocol of the next-generation Internet. It resolves many defects of IPv4, such as address scarcity, oversized routing table, and insufficient support for mobile devices.
IPv6 supports address autoconfiguration for network nodes and implements plug-and-play, significantly simplifying network management.
This course describes the fundamentals and implementation of IPv6 address autoconfiguration.

## Slide 4
On completion of this course, you will be able to:
  Describe the fundamentals of IPv6 stateless address autoconfiguration.
  Describe the fundamentals of DHCPv6 address autoconfiguration.
  Perform IPv6 address autoconfiguration.

## Slide 5
IPv6 Address Configuration Modes
IPv6 Stateless Address Autoconfiguration
DHCPv6
Implementation of IPv6 Address Autoconfiguration

## Slide 6: IPv6 Address Configuration Modes
IPv6 Address Configuration Modes
Dynamic
Manual configuration
Static address
Stateless address autoconfiguration
SLAAC
Stateful address autoconfiguration
DHCPv6
Static
IPv6 addresses can be configured statically or dynamically. Dynamic address configuration can be classified as stateless address autoconfiguration (SLAAC) or stateful address autoconfiguration.

## Slide 7: Classification of IPv6 Address Autoconfiguration
Stateless address autoconfiguration
IPv6 stateless address autoconfiguration does not require an IPv6 address allocation server to store and manage the status information of each node.
Stateless address autoconfiguration is implemented based on the Neighbor Discovery Protocol (NDP).
Stateful address autoconfiguration
IPv6 stateful address autoconfiguration requires an IPv6 address allocation server to store and manage the status information of each node.
Stateful address autoconfiguration is implemented based on the Dynamic Host Configuration Protocol for IPv6 (DHCPv6).

## Slide 8
IPv6 Address Configuration Modes
IPv6 Stateless Address Autoconfiguration
DHCPv6
Implementation of IPv6 Address Autoconfiguration

## Slide 9: IPv6 Stateless Address Autoconfiguration Process
PC1 automatically generates a link-local address based on a local interface ID.
PC1 performs duplicate address detection (DAD) on the link-local address. If the address does not conflict with another, it can be used. In this case, PC1 has the IPv6 connection capability.
PC1 sends RS messages to attempt to discover IPv6 routers on the link.
R1 sends an RA message, which carries the IPv6 address prefix that can be used for stateless address autoconfiguration. (The router can also send RA messages even if it does not receive RS messages.)
PC1 parses the RA message to obtain the IPv6 address prefix, and generates a unicast IPv6 address based on this prefix and local interface ID.
PC1 performs DAD on the unicast IPv6 address. If no conflict is detected, PC1 uses this address.
1
Generates a link-local address.
2
Performs DAD on the link-local address.
3
Sends RS messages to attempt to discover routers.
4
Responds with an RA message carrying the IPv6 address prefix.
5
Generates a unicast IPv6 address.
6
Performs DAD on the unicast IPv6 address.
R1
PC1

## Slide 10: IPv6 Stateless Address Autoconfiguration Example
IPv6 stateless address configuration is implemented by exchanging RS and RA messages.
IPv6 Address = 2001:DB8::1002
Link-local Address = FE80::1002
Link-local Address = FE80::1001
IPv6 Address = 2001:DB8::1/64
1
RA
Source: FE80::1001 Destination: FF02::1
(M=0, Prefix: 2001:DB8::/64)
RS
Source: FE80::1002 Destination: FF02::2
2
3
R1
PC1
Notes: The process of NDP-based IPv6 stateless address autoconfiguration is as follows (DAD is omitted):
  PC1 generates the link-local address FE80::1002 and sends RS messages to all routers on the local link.
  R1 sends an RA message carrying a prefix for stateless address autoconfiguration. In this example, the prefix is 2001:DB8::/64.
  After receiving the RA message, PC1 generates the IPv6 address 2001:DB8::1002 based on the prefix and interface ID.

## Slide 11: Flags Field in an RA Message
Internet Control Message Protocol V6
Type: 134 (Router Advertisement)
Code: 0
Checksum: 0x4a68 [Correct]
Cur Hop Limit: 64
Flags: 0x00
0 . . . . . . . = Not managed
. 0 . . . . . . = Not Other
. . 0 . . . . . = Not Home Agent
. . . 0 . . . . = Router Preference: Medium
. . . . . 0 . . = Not Proxied
Router Lifetime: 1800
Reachable time: 0
Retrans timer: 0
ICMPv6 Option (Source Link-layer address)
ICMPv6 Option (MTU)
ICMPv6 Option (Prefix information)
M bit: managed address configuration flag
  By default, the M bit is 0, and a terminal that receives an RA message uses the IPv6 address prefix contained in the message to construct a unicast address. That is, stateless address autoconfiguration is used.
  If the M bit is set to 1 in an RA message, a terminal that receives the message uses DHCPv6 to obtain an address and other information. When the M bit is 1, the terminal can ignore the O bit. That is, the terminal uses DHCPv6 to obtain the address and other information (such as DNS).
To set the M bit to 1, run the ipv6 nd autoconfig managed-address-flag command.
O bit: other stateful configuration flag
  By default, the O bit is 0, and a terminal that receives an RA message performs stateless address autoconfiguration. That is, a routing device advertises other configuration information except an IPv6 address to the terminal through the RA message.
  If the O bit is set to 1 in an RA message, a terminal that receives the message uses DHCPv6 to obtain other parameters except an address.
To set the O bit to 1, run the ipv6 nd autoconfig other-flag command.

## Slide 12: Optional Information in an RA Message: Address Prefix
Internet Control Message Protocol V6
Type: 134 (Router Advertisement)
Code: 0
...
Retrans timer: 0
ICMPv6 Option (Source Link-layer address)
ICMPv6 Option (Prefix information)
Type: Prefix information
Prefix-Length: 64
Flags: 0xc0
1 . . . . . . . = On-Link Flag (L): Set
. 1 . . . . . . = Autonomous Addr-conf flag (A): Set
. . 00 0000 = Reserved: 0
Valid lifetime: 2592000
Preferred lifetime: 604800
Reserved
Prefix: 2001:DB8::
IPv6 address prefix length
The A bit is used to indicate whether a terminal can use the prefix to perform stateless address autoconfiguration.
  If the A bit is set to 0, the terminal cannot use the prefix to perform stateless address autoconfiguration.
  If the A bit is set to 1, the terminal can use the prefix to perform stateless address autoconfiguration.
To set this bit to 0, run the ipv6 nd ra prefix 2001:DB8:: 64 2592000 604800 no-autoconfig command.
IPv6 address prefix

## Slide 13: Optional Information in an RA Message: Lifetime
Internet Control Message Protocol V6
Type: 134 (Router Advertisement)
Code: 0
...
Retrans timer: 0
ICMPv6 Option (Source Link-layer address)
ICMPv6 Option (Prefix information)
Type: Prefix information
Prefix-Length: 64
Flags: 0xc0
1 . . . . . . . = On-Link Flag (L): Set
. 1 . . . . . . = Autonomous Addr-conf flag (A): Set
. . 00 0000 = Reserved: 0
Valid lifetime: 2592000
Preferred lifetime: 604800
Reserved
Prefix: 2001:DB8::
DAD
Tentative
Preferred
Deprecated
Invalid
Valid lifetime
Preferred lifetime
After a terminal obtains a prefix and generating a unicast IPv6 address, the address enters the Tentative state. After passing DAD, the address enters the Preferred state and remains in this state within the preferred lifetime.
In the Preferred state, the terminal can send and receive packets normally. After the preferred lifetime expires, the address enters the Deprecated state and remains in this state within the valid lifetime.
In the Deprecated state, the address is still valid and can be used for existing connections, but cannot be used to establish new connections.
After the valid lifetime expires, the address enters the Invalid state, indicating that the address cannot be used.

## Slide 14
IPv6 Address Configuration Modes
IPv6 Stateless Address Autoconfiguration
DHCPv6
Implementation of IPv6 Address Autoconfiguration

## Slide 15: DHCPv6 Overview
DHCPv6 is designed for IPv6 addressing. It can be used to allocate IPv6 prefixes, IPv6 addresses, and other network configuration parameters to clients. In addition, DHCPv6 can record the information allocated to clients, facilitating network management.
DHCPv6 address allocation can be implemented in any of the following modes:
  DHCPv6 stateful autoconfiguration: A DHCPv6 server automatically configures IPv6 addresses/prefixes and other network configuration parameters, such as DNS, NIS, and SNTP server addresses.
  DHCPv6 stateless autoconfiguration: Host IPv6 addresses are automatically generated through RA messages. A DHCPv6 server allocates other configuration parameters such as the DNS server address except for IPv6 addresses.
  DHCPv6 prefix delegation (PD) autoconfiguration: A downstream device requests IPv6 address prefixes from an upstream device, and the upstream device allocates appropriate prefixes to the downstream device. In this way, you do not need to configure IPv6 address prefixes for user-side links on the downstream device. The downstream device divides the obtained prefix (which is typically less than 64 bits long) into subnet segments with 64-bit prefixes and sends an RA message on the link that IPv6 hosts directly connect to. This enables IPv6 hosts to automatically configure IPv6 addresses, implementing hierarchical address deployment.

## Slide 16: DHCPv6 Network Composition
The DHCPv6 architecture involves the following roles:
  DHCPv6 client: exchanges DHCPv6 messages with a DHCPv6 server to obtain an IPv6 address/prefix and other network configuration parameters.
  DHCPv6 server: processes requests for address allocation, lease renewal, and release from a DHCPv6 client or a DHCPv6 relay agent, and allocates IPv6 addresses/prefixes and other network configuration parameters to the client.
  DHCPv6 relay agent: relays DHCPv6 messages between a DHCPv6 client and server to help the client configure its address.
IPv6 network
DHCPv6 client
DHCPv6 client
DHCPv6 relay agent
DHCPv6 server

## Slide 17: Common DHCPv6 Concepts
Valid lifetime
Lifetime of an address/prefix.
Preferred lifetime
Used to calculate the renewal time and rebind time.
T1
Renew time of an IPv6 address. The default value is 0.5 times the preferred lifetime.
T2
Rebind time of an IPv6 address. The default value is 0.8 times the preferred lifetime.
IA
An identity association (IA) enables a DHCPv6 server and client to identify, group, and manage IPv6 addresses. IAs are classified as Identity Association for Non-temporary Addresses (IA_NA) or Identity Association for Prefix Delegation (IA_PD).
DUID
A DHCP unique identifier (DUID) uniquely identifies a DHCPv6 device. Each DHCPv6 client, server, or relay agent has its own DUID.
Message types
Solicit, Advertise, Request, Reply, Information-request, Renew, Rebind, Release, Confirm, Decline, Reconfigure, Relay-forward, Relay-reply, and so on.
Notes: Valid lifetime: lifetime of an address/prefix. After an address/prefix expires, all the users who use it are logged out. The valid lifetime must not be shorter than 3 hours or the preferred lifetime.
Preferred lifetime: used to calculate the renew time and rebind time. The preferred lifetime must not be shorter than 2 hours.

## Slide 18: DHCPv6 Stateful Autoconfiguration — Four-Message Exchange
In the four-message exchange, a DHCPv6 client and server exchange four messages to obtain parameters such as prefixes/addresses.
The DHCPv6 client sends a Solicit message to request the DHCPv6 server to allocate an IPv6 address/prefix and network configuration parameters.
The DHCPv6 server sends an Advertise message to the DHCPv6 client, notifying the client of the IPv6 addresses/prefixes and network configuration parameters that can be allocated.
If the DHCPv6 client receives Advertise messages from multiple DHCPv6 servers, it selects a server based on the sequence in which the messages are received and the server priorities. The client then sends a Request message to the server, requesting an IPv6 address/prefix and network configuration parameters.
The DHCPv6 server responds with a Reply message, which contains the allocated IPv6 address/prefix and network configuration parameters.
DHCPv6 client
DHCPv6 server
1
Solicit
3
Request
2
Advertise
4
Reply

## Slide 19: DHCPv6 Stateful Autoconfiguration — Two-Message Exchange
A DHCPv6 client sends a Solicit message that carries the Rapid Commit option, indicating that the client expects the server to quickly allocate an address/prefix and network configuration parameters.
DHCPv6 client
DHCPv6 server
1
Solicit
2
Reply
(carrying the Rapid Commit option)
The DHCPv6 client sends a Solicit message carrying the Rapid Commit option.
After receiving the Solicit message, the DHCPv6 server checks whether it supports fast address allocation. If so, the server returns a Reply message carrying the allocated IPv6 address/prefix and other network configuration parameters. If the DHCPv6 server does not support fast address allocation, the four-message exchange is used.
Notes: The two-message exchange improves the efficiency of DHCPv6 address allocation, but it is applicable when only one DHCPv6 server exists on a network. On a network with multiple DHCPv6 servers, these servers can allocate IPv6 addresses/prefixes and other configuration parameters to a DHCPv6 client. However, a client can use only the IPv6 address/prefix and configuration parameters allocated by a DHCPv6 server.

## Slide 20: Address/Prefix Lease Renewal (1)
An IPv6 address/prefix allocated by a DHCPv6 server has a valid lifetime. After the valid lifetime of an address/prefix expires, a DHCPv6 client cannot use the address/prefix. Therefore, if the DHCPv6 client wants to continue to use the address/prefix before the valid lifetime expires, the lease of the address/prefix needs to be renewed.
The DHCPv6 client sends a Renew message at T1 (half the preferred lifetime by default) to request address/prefix lease renewal.
If the DHCPv6 client can continue to use the address/prefix, the DHCPv6 server responds with a Reply message, indicating that the address/prefix lease is renewed successfully. Otherwise, the DHCPv6 server responds with a Reply message, indicating that the address/prefix lease fails to be renewed.
DHCPv6 client
DHCPv6 server
1
Renew
2
Reply
T1

## Slide 21: Address/Prefix Lease Renewal (2)
If no DHCPv6 server responds to a Renew message sent by a DHCPv6 client at T1, the client multicasts a Rebind message to all DHCPv6 servers at T2 (0.8 times the preferred lifetime by default) to request lease renewal.
T2
DHCPv6 client
DHCPv6 server
1
Renew
3
Reply
T1
2
Rebind
The DHCPv6 client sends a Renew message to request lease renewal at T1, but it does not receive a reply message from DHCPv6 servers.
The DHCPv6 client multicasts a Rebind message to all DHCPv6 servers at T2 to request lease renewal.
If the DHCPv6 client can continue to use the address/prefix, the DHCPv6 server responds with a Reply message, indicating that the address/prefix lease is renewed successfully. Otherwise, the DHCPv6 server responds with a Reply message, indicating that the address/prefix lease fails to be renewed.

## Slide 22: DHCPv6 Stateless Autoconfiguration
DHCPv6 stateless autoconfiguration enables a DHCPv6 server to allocate network configuration parameters except IPv6 addresses/prefixes to clients that already have the addresses/prefixes.
(carrying the network configuration parameters requested by the client)
(carrying the Option Request option)
DHCPv6 client
DHCPv6 server
1
Information-request
2
Reply
The DHCPv6 client multicasts an Information-request message with the Option Request option to the DHCPv6 server. This option specifies the configuration parameters that the client needs to obtain from the server.
After receiving the message, the server unicasts a Reply message containing the allocated network configuration parameters to the client. The client checks the allocated network configuration parameters in the Reply message. If these parameters are the same as those in the Information-request message, the client performs network configuration based on the allocated network configuration parameters. Otherwise, the client ignores the allocated parameters.
Notes: After a host generates a link-local address and detects no address conflict, it initiates a router discovery process. Specifically, the host sends an RS message, and the router replies with an RA message. If the M bit is 0 and the O bit is 1 in the RA message, the host obtains other configuration parameters except addresses/prefixes, such as DNS, SIP, and SNTP server configuration parameters, through DHCPv6 stateless autoconfiguration.

## Slide 23: DHCPv6 PD Autoconfiguration
On a hierarchical network, IPv6 addresses are generally configured manually, which has poor extensibility and is not beneficial for uniform IPv6 address planning and management. DHCPv6 PD can resolve this issue.
DHCPv6 client
DHCPv6 server
1
Solicit (IA_NA+IA_PD)
3
Request
2
Advertise
4
Reply
5
RA
PC
The DHCPv6 client sends a Solicit message, requesting an IA_NA address and IA_PD prefix from the DHCPv6 server.
The DHCPv6 server sends an Advertise message to notify the client of the allocated IPv6 address/prefix.
If multiple servers send Advertise messages to the client, the client selects the Advertise message from the server with the highest priority based on parameters such as the server priorities in the Advertise messages (if the server priorities are the same, the client selects the Advertise message that carries the required configuration parameters) and sends a Request message to the server, requesting the server to allocate an IPv6 address/prefix.
The DHCPv6 server responds with a Reply message, which carries the allocated IPv6 address/prefix.
After receiving the PD prefix, the DHCPv6 client exchanges RS/RA messages with the PC and delivers the obtained PD prefix to the PC through an RA message.
Notes: DHCPv6 PD applies to a scenario where a router (for example, the DHCPv6 client in this example) needs to allocate prefixes to its connected IPv6 hosts to implement automatic address configuration for the hosts. In this way, the hierarchical layout of the entire IPv6 network is implemented.
In Step 1, the DHCPv6 client requests the DHCPv6 server to allocate an IA_NA address and an IA_PD prefix, which are the address allocated to the client's WAN interface and the prefix allocated to the client's LAN side, respectively.

## Slide 24: Working Process of a DHCPv6 Relay Agent
If a DHCPv6 server and client are on different network segments, a DHCPv6 relay agent is required to obtain IPv6 addresses/prefixes and other network configuration parameters.
DHCPv6 client
DHCPv6 server
DHCPv6 relay agent
1
DHCPv6 message
2
Relay-forward
3
Relay-reply
4
DHCPv6 message
The DHCPv6 client sends a Request message to all DHCPv6 servers and the multicast address FF02::1:2 of the DHCPv6 relay agent.
After receiving the message, the DHCPv6 relay agent encapsulates it in the Relay Message option of a Relay-forward message and sends the Relay-forward message to the DHCPv6 server or next-hop relay agent.
The DHCPv6 server obtains the client's request from the Relay-forward message and selects an IPv6 address and other configuration parameters. The server then sends a Relay-reply message to the DHCPv6 relay agent.
The DHCPv6 relay agent obtains the server's reply message from the Relay-reply message and forwards the reply message to the DHCPv6 client.

## Slide 25: DHCPv6 Address Confirmation
In some scenarios, for example, when a DHCPv6 client is powered off, goes offline, or roams, it sends a Confirm message to confirm whether its IPv6 address is available. If the client confirms that the address is valid, the server responds. If the server does not respond, the client needs to restart the address application process.
DHCPv6 client
DHCPv6 server
1
Confirm
2
Reply

## Slide 26: DHCPv6 DAD
A DHCPv6 client performs DAD on an allocated address before using the address. If DAD detects an address conflict, the client sends a Decline message to notify the server that it does not use the address.
DHCPv6 client
DHCPv6 server
1
Decline
2
Reply

## Slide 27: DHCPv6 Address Release
When a DHCPv6 client does not need to use an address, it sends a Release message to a server, requesting address release.
DHCPv6 client
DHCPv6 server
1
Release
2
Reply

## Slide 28: DHCPv6 Message Summary
Message Type | Function
Solicit | A DHCPv6 client sends a Solicit message to request a DHCPv6 server to allocate an IPv6 address/prefix and network configuration parameters.
Advertise | A DHCPv6 server sends an Advertise message to a DHCPv6 client, notifying the client of the IPv6 addresses/prefixes and network configuration parameters that can be allocated.
Request | If a DHCPv6 client receives Advertise messages from multiple DHCPv6 servers, it selects a server based on the sequence in which the messages are received and the server priorities. The client then sends a Request message to the server, requesting an IPv6 address/prefix and network configuration parameters.
Reply | A DHCPv6 server responds with a Reply message, which contains the allocated IPv6 address/prefix and network configuration parameters.
Information-request | A DHCPv6 client multicasts an Information-request message with the Option Request option to DHCPv6 servers. This option specifies the configuration parameters that the client needs to obtain from a DHCPv6 server.
Renew | When the address/prefix lease reaches T1, a DHCPv6 client unicasts a Renew message to the DHCPv6 server that allocates the address/prefix to renew the address/prefix lease.
Rebind | If a DHCPv6 client sends a Renew message to renew the lease at T1 but does not receive any reply message from the corresponding DHCPv6 server, the client multicasts a Rebind message to all DHCPv6 servers at T2 to request lease renewal.
Confirm | In some scenarios, for example, when a DHCPv6 client is powered off, goes offline, or roams, it sends a Confirm message to confirm whether its IPv6 address is available.
Decline | When a DHCPv6 client detects an address conflict, it sends a Decline message to a DHCPv6 server.

## Slide 29: Address Autoconfiguration Comparison
Address Configuration | Based on DHCPv6 | Based on NDP
Address management | Stateful. A server stores information about address or prefix allocation and release. | Stateless. A server does not store information about user address allocation.
Deployment value | 128-bit addresses and prefixes with different lengths can be allocated, resulting in high extensibility. | Only 64-bit prefixes are supported, resulting in poor extensibility.
Implementation | Complex configuration. | Simple configuration.
Security | DHCPv6 works at the application layer and provides high security. | Low security.

## Slide 30
IPv6 Address Configuration Modes
IPv6 Stateless Address Autoconfiguration
DHCPv6
Implementation of IPv6 Address Autoconfiguration

## Slide 31: Basic IPv6 Configurations (1)
[Huawei] ipv6
Enable a device to forward IPv6 unicast packets.
[Huawei-GigabitEthernet0/0/0] ipv6 enable
[Huawei-GigabitEthernet0/0/0] ipv6 address ipv6-address link-local
Manually configure a link-local address for the interface.
[Huawei-GigabitEthernet0/0/0] ipv6 address auto link-local
Enable the interface to forward IPv6 unicast packets.
[Huawei-GigabitEthernet0/0/0] ipv6 address { ipv6-address prefix-length | ipv6-address/prefix-length }
Manually configure a global unicast address for the interface.
[Huawei-GigabitEthernet0/0/0] ipv6 address auto { global | dhcp }
Automatically configure a link-local address for the interface.
Automatically configure a global unicast address for the interface.

## Slide 32: Basic IPv6 Configurations (2)
[Huawei] display ipv6 interface [ interface-type interface-number | brief ]
Display IPv6 information on the interface.
[Huawei] display ipv6 neighbors
Display neighbor entry information.
[Huawei-GigabitEthernet0/0/0] undo ipv6 nd ra halt
Enable the interface to send RA messages.
By default, Huawei router interfaces do not send ICMPv6 RA messages. In such a case, hosts on the network cannot periodically receive information about updated IPv6 address prefixes. To enable an interface to periodically send RA messages that carry both the IPv6 address prefix and stateful address autoconfiguration flag to a host, run the undo ipv6 nd ra halt command.

## Slide 33: IPv6 Address Configuration Examples — Static Configuration
Enable IPv6 on R1, R2, and R3, and configure interfaces to automatically generate link-local addresses (use R1 as an example).
[R1]ipv6
[R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]ipv6 enable
[R1-GigabitEthernet0/0/0]ipv6 address auto link-local
Configure global unicast IPv6 address for R1's interfaces.
Configuration requirements:
  Manually configure IPv6 addresses for R1's GE 0/0/0 and GE 0/0/1.
  Configure R2's GE 0/0/0 to obtain an IPv6 address through stateless address autoconfiguration.
  Configure R3's GE 0/0/0 to obtain an IPv6 address through DHCPv6.
GE 0/0/0
R2
R1
R3
GE 0/0/0
2001:DB8:13::1/64
GE 0/0/1
GE 0/0/0
2001:DB8:12::1/64
Stateless address autoconfiguration
Address obtained using DHCPv6
[R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]ipv6 address 2001:DB8:13::1 64 [R1-GigabitEthernet0/0/0]interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1]ipv6 address 2001:DB8:12::1 64

## Slide 34: IPv6 Address Configuration Examples — Stateless Address Autoconfiguration
Enable RA message advertisement on R1.
[R1]interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1]undo ipv6 nd ra halt
[R2]interface GigabitEthernet 0/0/0
[R2-GigabitEthernet0/0/0]ipv6 address auto global
Configuration requirements:
  Manually configure IPv6 addresses for R1's GE 0/0/0 and GE 0/0/1.
  Configure R2's GE 0/0/0 to obtain an IPv6 address through stateless address autoconfiguration.
  Configure R3's GE 0/0/0 to obtain an IPv6 address through DHCPv6.
GE 0/0/0
R2
R1
R3
GE 0/0/0
2001:DB8:13::1/64
GE 0/0/1
GE 0/0/0
2001:DB8:12::1/64
Stateless address autoconfiguration
Address obtained using DHCPv6
Configure R2's GE 0/0/0 to automatically obtain an IPv6 address.

## Slide 35: IPv6 Address Configuration Examples — DHCPv6
Configure the DHCPv6 server function on R1.
[R1]dhcp enable
[R1]dhcpv6 pool pool1
[R1-dhcpv6-pool-pool1]address prefix 2001:DB8:13::/64
[R1-dhcpv6-pool-pool1]excluded-address 2001:DB8:13::1 [R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]dhcpv6 server pool1
Configuration requirements:
  Manually configure IPv6 addresses for R1's GE 0/0/0 and GE 0/0/1.
  Configure R2's GE 0/0/0 to obtain an IPv6 address through stateless address autoconfiguration.
  Configure R3's GE 0/0/0 to obtain an IPv6 address through DHCPv6.
GE 0/0/0
R2
R1
R3
GE 0/0/0
2001:DB8:13::1/64
GE 0/0/1
GE 0/0/0
2001:DB8:12::1/64
Stateless address autoconfiguration
Address obtained using DHCPv6
[R3]dhcp enable
[R3]interface GigabitEthernet 0/0/0
[R3-GigabitEthernet0/0/0]ipv6 address auto dhcp
Configure R3's GE 0/0/0 to obtain an IPv6 address through DHCPv6.

## Slide 36: IPv6 Address Autoconfiguration — Verification
[R2]display ipv6 interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 current state : UP
IPv6 protocol current state : UP
IPv6 is enabled, link-local address is FE80::2E0:FCFF:FEAD:675F
Global unicast address(es):
2001:DB8:12::2E0:FCFF:FEAD:675F,
subnet is 2001:DB8:12::/64 [SLAAC]
Joined group address(es):
FF02::1:FFAD:675F
FF02::2
FF02::1
MTU is 1500 bytes
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds
ND retransmit interval is 1000 milliseconds
Hosts use stateless autoconfig for addresses
Verify the IPv6 address obtained by R2 through stateless address autoconfiguration.
[R3]display dhcpv6 client
GigabitEthernet0/0/0 is in stateful DHCPv6 client mode.
State is BOUND.
Preferred server DUID : 0003000100E0FC401312
Reachable via address : FE80::2E0:FCFF:FE40:1312
IA NA IA ID 0x00000031 T1 43200 T2 69120
Obtained : 2020-06-17 09:49:58
Renews : 2020-06-17 21:49:58
Rebinds : 2020-06-18 05:01:58
Address : 2001:DB8:13::3
Lifetime valid 172800 seconds, preferred 86400 seconds
Expires at 2020-06-19 09:49:58(172159 seconds left)
Run the display dhcpv6 client command on R3 to check address allocation information.

## Slide 37
(Single) Which of the following statements about NDP-based stateless address autoconfiguration is true?
  NDP-based stateless address autoconfiguration can be used to allocate 128-bit IPv6 addresses to hosts.
  NDP-based stateless address autoconfiguration can be used to allocate IPv6 prefixes or addresses to hosts.
  NDP-based stateless address autoconfiguration can be used to allocate only IPv6 prefixes to hosts.
  NDP-based stateless address autoconfiguration can be used to allocate DNS information to hosts.
(Multiple) Which of the following processes use Reply messages in DHCPv6?
  DHCPv6 information obtaining
  DHCPv6 prefix allocation's two-message exchange
  DHCPv6 address allocation's four-message exchange
  DHCPv6 address release
  DHCPv6 address lease renewal
Notes: D
A, B, C, D, and E

## Slide 38
IPv6 addresses can be configured statically or dynamically. Usually, the interconnection IPv6 addresses of network devices and IPv6 addresses of loopback interfaces are statically configured, whereas terminals are dynamically configured.
This course mainly describes NDP-based stateless address autoconfiguration and DHCPv6-based stateful address autoconfiguration. Stateless address autoconfiguration can be used to allocate only 64-bit prefixes, resulting in poor extensibility as well as address management and control. Stateful address autoconfiguration provides more functions, such as PD prefix allocation.
The M and O bits in an RA message determine an IPv6 address autoconfiguration mode used by a client. Determine an appropriate address autoconfiguration mode based on an actual scenario.