## Slide 1
Wan Changli wwx408647
2020-03-11

## Slide 2: Huawei Firewall Technology

## Slide 3
The word "firewall" is first used in the construction field. The function of a firewall is to isolate the fire, preventing the fire from spreading from one area to another. In the communications field, a firewall is usually deployed to logically isolate networks for some purposes. The firewall defends against various attacks on the network to ensure transmission of communication packets.
This course describes what is a firewall in the communications field, why a firewall is required, and the working mechanism and configurations of the firewall.

## Slide 4
Upon completion of this source, you will be able to:
  Describe the definition, type, and development history of firewalls.
  Distinguish firewalls from routers and switches.
  Describe basic firewall concepts, such as the security zone, security policy, session table, and server map.
  Perform basic firewall configurations.

## Slide 5
Introduction to Firewalls
Basic Firewall Concepts
Basic Firewall Configurations

## Slide 6: Why Do We Need Firewalls?
Security is required everywhere. Routers and switches construct an interconnected network, which brings convenience and security risks.
For example, enterprises have the following security requirements at a network border:
  External network security isolation
  Internal network security control
  Content filtering
  Intrusion prevention
  Antivirus
Server
Server
Server
Core-Switch 1
Core-Switch 2
Firewall 1
Firewall 2
Internal network (trusted zone)
External network (untrusted zone)
External
Network
External
Network

## Slide 7: What Is a Firewall?
In the communications field, a firewall is a security device. It is used to protect a network area against attacks and intrusions from another network area. It is usually deployed at a network border, such as the enterprise Internet egress, enterprise internal service border, and data center border.
Firewalls are classified into modular firewalls, fixed firewalls, and software firewalls. Firewalls can be flexibly deployed locally and on the cloud.
Public cloud,
private cloud
Software firewall
Fixed firewall
Modular firewall
Notes: Firewalls have other models, such as desktop firewalls (a type of fixed firewalls). Desktop firewalls apply to small enterprises, industry branches, and chain business organizations. Huawei fixed firewalls support both the traditional and cloud management modes. In cloud management mode, the cloud manages secure access of branches in a unified manner, and supports plug-and-play devices, automatic service configuration, visualized O&M, and network big data analysis.
This course focuses on modular and fixed physical firewalls, and does not describe desktop firewalls and software firewalls.

## Slide 8: Comparison Between Firewalls and Switches and Routers
For example, on a campus network, switches are used to connect terminals and summarize internal routes to build a LAN for internal communication.
Routers are used for route distribution, addressing, and forwarding to construct an external connection network.
Firewalls are used to implement traffic control and security protection and to distinguish and isolate different security zones.
Abnormal traffic
Normal traffic
Switches constitute a LAN and perform Layer 2 or Layer 3 fast packet forwarding
Firewalls control packet forwarding and defend against attacks, viruses, and Trojan
Routers provide addressing and forwarding to ensure network interconnection
Internet

## Slide 9: Comparison Between Forwarding Processes of a Firewall and a Router
The forwarding process of a firewall is more complex than that of a router. A modular firewall is used as an example. In addition to interfaces, line processing units (LPUs), and switch fabric units (SFUs), a modular firewall has service processing units (SPUs) to implement security functions.
Interface
LPU
SFU
LPU
Outbound interface
ACL rule/QoS policy/Traffic management
ACL rule/QoS policy/Traffic management
Forwarding process of a router
Forwarding process of a firewall
Interface
LPU
SFU
LPU
Outbound interface
ACL rule/QoS policy/Traffic management
DDoS attack defense/session matching/status detection/authentication policy/security policy/NAT policy/content security/bandwidth policy
ACL rule/QoS policy/Traffic management
SPU

## Slide 10: Typical Application Scenarios of Firewalls
Enterprise Border Protection
Intranet Control and Security Isolation
DC Border Protection
DC Security Association
Internet
Traveling employee
Branch
Untrusted
DMZ
FTP server
Trusted
Spine
Leaf
Internal area of a DC
Individual customer
Enterprise customer
Untrusted
Internet
Enterprise campus/branch
Internet
R&D area
Egress gateway
Marketing Dept
Production Dept
Finance Dept
Notes: A Demilitarized Zone (DMZ) is originally a military term, referring to a partially controlled area between a military control area and a public area. A DMZ configured on a firewall is logically and physically separated from internal and external networks. In an enterprise, it is usually used to accommodate servers.
Data center networks often use the spine-leaf architecture. Spine nodes forward traffic at a high speed, and leaf nodes connect to servers, firewalls, or other devices. Spine and leaf nodes are fully meshed at Layer 3.

## Slide 11: Firewall Development History
1989
1994
1998
2004
2008
PC era
Network era era
Internet era
Web 2.0 era
2009–
Mobile Internet era
Basic access control
Session mechanism introduced
Performance improvement by a dedicated chip
Multi-function
Higher performance
Control based on applications, users, and contents
Now
AI era
Next-generation firewall (NGFW)
Packet filtering firewall
Stateful inspection firewall
ASIC-based firewall
Unified Threat Management (UTM)
Multi-core distributed architecture
AIFW
Throughout the firewall development history, the firewall has gone through the process from low-level to high-level and from simple functions to complex functions. Development of network technologies and emergence of new requirements promote the development of firewalls.
Firewalls develop from the packet filtering firewall, status detection firewall, UTM, and NGFW to AIFW, with the following characteristics:
  More refined access control
  More powerful protection capability
  Higher performance

## Slide 12: Packet Filtering Firewall
A packet filtering firewall checks each packet based on the 5-tuple and forwards or discards packets based on the configured security policies.
The packet filtering firewall uses access control lists (ACLs) to filter data packets.
Question: How to solve problems of the packet filtering firewall?
Untrusted
Internet
Trusted
Office area
192.168.10.0/24
R&D area
192.168.20.0/24
Source address: 192.168.10.0/24
Destination address: any
Port number: any
Protocol: HTTP
Action: permit
In this example, firewall security policies are configured to allow only IP addresses in the office area to access the Internet.
Problems of the packet filtering firewall:
  Per-packet detection has low performance.
  ACL rules cannot meet dynamic requirements.
  Application-layer data is not checked.
  The packet filtering firewall does not provide packet association analysis, so spoofing may easily occur.
Notes: A packet filtering firewall filters packets based on information such as the source/destination IP address, source/destination port number, IP identifier, and packet transmission direction in the packets.
The packet filtering firewall is simple in design, easy to implement, and cost-effective.
The disadvantages of the packet filtering firewall are as follows:
  With the increase of ACL complexity and length, filtering performance decreases exponentially.
  Static ACL rules cannot meet dynamic security requirements.
  The packet filtering firewall does not check the session status or analyze data, which makes it easy for attackers to escape. For example, an attacker sets the IP address of the host to an IP address permitted by a packet filtering firewall. In this way, packets from this host can easily pass through the packet filtering firewall.

## Slide 13: Stateful Inspection Firewall
The NGFW is also a stateful inspection firewall. The NGFW greatly improves content security and processing performance.
In this example, the stateful inspection firewall detects that a TCP connection is established between hosts at 10.0.0.1 and 20.0.0.1 and generates session information. The third handshake packet does not match any session entry and is discarded.
Stateful inspection firewalls are introduced based on packet filtering technology. It considers correlation between packets and detects the connection status but not a single packet.
Untrusted
Internet
Trusted
Office area
10.0.0.1
20.0.0.1
Suspected attack
TCP
SYN=1, Seq=2289, ACK=10002
TCP
SYN=1, Seq=9955, ACK(Seq=2289)
TCP
SYN=1, Seq=2288, ACK=0
tcp 10.0.0.1:52754-->20.0.0.1:4399
TCP three-way handshake
Session information:
TCP
SYN=1, Seq=2289, ACK=9956
Notes: The stateful inspection firewall detects the first data packet of a connection to determine the status of the connection. Subsequent data packets are forwarded or blocked based on the status of the connection.

## Slide 14: AIFW
The AIFW is a next-generation firewall that integrates AI technology. It further improves the security protection capability and performance of the firewall by using AI algorithms or AI chips.
Huawei AIFW has built-in core detection engine (CDE) — malicious file detection engine, deception sensor, APT inspection engine (AIE), and probe. It can interwork with the sandbox and Huawei Cybersecurity Intelligence System (CIS) — big data analytics platform for detection, building an intelligent defense system.
Big data-based security situation awareness system
Sandbox: APT defense detection system
CDE
Detection and association
Built-in probe
Built-in deception sensor
Built-in AIE
File restoration/mirroring
Collection
Joint detection
Huawei AIFW
Notes: Huawei HiSecEngine USG6000E series is the first AIFW launched in the industry. There is no unified standard for AIFWs. For example, firewalls are trained using a large amount of data and algorithms so that they can proactively identify threats. The built-in AI chip of firewalls helps improve application identification and forwarding performance.
Advanced Persistent Threats (APTs) persistently attack specific targets using advanced attack methods.
The sandbox is a security device used to detect viruses. It builds a virtual environment for suspected viruses and detects viruses by observing their subsequent behaviors. The sandbox is an important device for APT detection. Huawei FireHunter is a sandbox.
The CIS can effectively collect network traffic, and network and security logs of various devices. Based on real-time and offline analysis of big data and machine learning technology, expert reputation, and intelligence, the CIS can effectively detect potential and advanced threats on a network, implement security situation awareness of the entire network, and effectively complete the closed-loop handling of threats with the help of Huawei HiSec solution.
Huawei-developed CDE uses the PE Class 2.0 AI algorithm to restore all files and perform in-depth detection on file content. (Flow detection is the mainstream in the industry. This technology is fast, but it restores only the file header and does not check the file content.
Huawei's unique AIE APT detection engine uses AI algorithms to continuously defend against the latest threats.
For more information about AIFWs, see https://e.huawei.com/en/products/enterprise-networking/security.

## Slide 15
This section describes the basic concepts, application scenarios, and development history of firewalls.
  Firewalls are security devices and fall into fixed, modular, desktop, and software firewalls.
  Firewalls can be used for but not limited to enterprise border protection, intranet control and security isolation, DC border protection, and DC security association.
  The firewall technology is developing from the early packet filtering firewall to the current AIFW.

## Slide 16
Introduction to Firewalls
Basic Firewall Concepts
Basic Firewall Configurations

## Slide 17: Basic Firewall Concepts: Security Zone
GE1/0/1
GE1/0/2
GE1/0/3
DMZ
Trusted
Untrusted
Servers
A security zone is an important concept of a firewall. Most security policies are implemented based on security zones.
A security zone is a set of networks connected through interfaces. Users in a zone have the same security attributes.
GE1/0/1 of the firewall is added to the trusted zone, so the network connected to GE1/0/1 is considered to be in the trusted zone.
Internet
Question: Does a firewall interface belong to a security zone?
Security Zone
Security Policy
Session Table
Server Map

## Slide 18: Default Security Zones
Security Zone Name | Default Security Priority
Untrusted zone | 5 (low security level)
DMZ | 50 (medium security level)
Trusted zone | 85 (high security level)
Local zone | A local zone is a device itself, including interfaces on the device. The local zone has the highest security level, and its priority is 100.
Four security zones have been created on Huawei firewalls: untrusted, DMZ, trusted, and local zones. Security zones have the following characteristics:
  The default security zone cannot be deleted, and the security priority cannot be changed.
  Each security zone must be configured with a security priority. A larger value indicates a higher priority of the security zone.
  You can create customized zones as required.
GE1/0/1
GE1/0/2
GE1/0/3
DMZ
50
Trusted
85
Untrusted
5
Servers
Internet
Local
100
Local
100
Local
100
Security Zone
Security Policy
Session Table
Server Map
Notes: The default security zones are as follows:
Untrusted zone: defines an insecure network, such as the Internet.
DMZ: defines the zone where internal network servers reside. Internal network servers are frequently accessed by external network devices but cannot proactively access the external network, which causes huge security risks. These servers are deployed in a DMZ with a lower level than a trusted zone but a higher level than an untrusted zone.
  A DMZ is originally a military term, referring to a partially controlled area between a military control area and a public area. A DMZ configured on a firewall is logically and physically separated from internal and external networks.
  Devices that provide network services for external users are deployed in the DMZ. These devices such as web servers and FTP servers provide services for extranet devices. If the servers are placed on an internal network, their security vulnerabilities may be used by external malicious users to attack the internal network. If the servers are deployed on the external network, security cannot be ensured.
Trusted zone: defines the zone where internal network terminals reside.
A local zone is a device itself, including interfaces on the device. All packets constructed on and proactively sent from the device are regarded as packet sent from the local zone; the packets to be responded and processed by the device (including the packets to be detected or directly forwarded) are regarded as packets received in the local zone. Configurations of the local zone cannot be changed, for example, interfaces cannot be added to the local zone.
  A security policy for exchanging packets between the local zone and the security zone of a peer can be configured for applications where devices need to receive and send packets by themselves.

## Slide 19: Interzone Example
Internet
GE0/0/1
GE0/0/2
...
Local zone
Firewall
The source and destination addresses of the traffic determine the zones that can access each other. For , traffic from the PC to the firewall interface is transmitted from the trusted zone to the local zone. For , the traffic from the PC to Internet is transmitted from the trusted zone to the untrusted zone.
PC
Trusted zone
Untrusted zone
2
1
Security Zone
Security Policy
Session Table
Server Map
1
2

## Slide 20: Basic Firewall Concepts: Security Policy
A security policy is used by a firewall to control traffic forwarding and perform integrated detection over the traffic content.
When receiving traffic, the firewall identifies traffic attributes (5-tuple, user, and time range) and matches them with the conditions of the security policy. If the traffic matches the conditions, the corresponding action is performed on the traffic.
Untrusted
Internet
Trusted
Office area
192.168.10.0/24
R&D area
192.168.20.0/24
Security policy
Source address: 192.168.10.0/24
Destination address: any
User: office area
Time range: 9:00 to 17:00
Action: permit
Security Zone
Security Policy
Session Table
Server Map

## Slide 21: Security Policy Composition
Traffic
Source security zone
Destination security zone
Source address/region
Destination address/region
User
Service
Application
URL category
Condition
Permit
Deny
Action
Antivirus
Intrusion prevention
URL filtering
File filtering
Content filtering
Application behavior control
Mail filtering
APT defense
DNS filtering
Security Profile
Send
Do not send
Response packet
VLAN ID
Time range
A security policy consists of matching conditions, actions, and security profiles (optional). The security profile ensures content security.
If the action of the security policy is permit, the profile can be configured. If the action of the security policy is deny, the feedback packet can be configured.
Security Zone
Security Policy
Session Table
Server Map
Notes: Actions:
  Permit: If the action is permit, a firewall processes the traffic as follows:
    If content security detection is not configured, the firewall allows the traffic to pass through.
    If content security detection is configured, the firewall determines whether to permit the traffic based on the content security detection result. Content security detection includes antivirus and intrusion prevention, which are implemented by referencing security profiles in security policies. If one security profile blocks the traffic, the firewall blocks the traffic. If all security profiles permit the traffic, the firewall allows the traffic to pass through.
  Deny: The firewall does not allow the traffic that matches a security policy to pass through.
    If the action is deny, the firewall discards the packet and can send a corresponding feedback packet based on the packet type. After the client/server receives the blocking packets from the firewall, it can rapidly terminate sessions and users can detect that the requests have been blocked.
      Reset client: The firewall sends a TCP reset packet to the TCP client.
      Reset server: The firewall sends a TCP reset packet to the TCP server.
      ICMP unreachable: The firewall sends an ICMP unreachable packet to the client.
For details, see "Security Policy" in https://support.huawei.com/hedex/hdx.do?docid=EDOC1100092598&lang=en.

## Slide 22: Security Policy Matching Process
Rule
Source zone
Destination zone
Source address
Destination address
User
Application
Service
Time range
Action
Content security profile
Enable log recording
Condition
Action
Option
...
Rule
Source zone
Destination zone
Source address
Destination address
User
Application
Service
Time range
Action
Content security profile
Enable log recording
Rule
Source zone
Destination zone
Source address
Destination address
User
Application
Service
Time range
Action
Content security profile
Enable log recording
When multiple security policies are configured, they are matched according to their configuration sequence. That is, the security policies are matched one by one from the top of the security policy list. If a packet matches a security policy, it will no longer match the following security policies.
Therefore, the configuration sequence of security policies is important. You need to configure policies with precise conditions and then policies with loose conditions.
Matching Sequence
Security Zone
Security Policy
Session Table
Server Map
Notes: The system has a default security policy named default. The default security policy is located at the bottom of the policy list and has the lowest priority. All matching conditions of the default security policy are any and the default action is deny. If all the configured policies are not matched, the default security policy is used.

## Slide 23: Basic Firewall Concepts: Session Table
[FW] display firewall session table
http VPN:public --> public 192.168.1.1:52754-->10.1.1.1:80
2
[FW] display firewall session table
http VPN:public --> public 192.168.1.1:52754-->10.1.1.1:80
5
Return packets match session entries.
4
After the first packet reaches the firewall, the firewall creates a session entry.
6
PC2 (HTTP server)
10.1.1.1/24
Gateway: 10.1.1.254
Untrusted
PC1
192.168.1.1/24
Gateway address: 192.168.1.254
Trusted
GE1/0/1
192.168.1.254
GE1/0/2
10.1.1.254
1
3
A session table is used to record the connection status of protocols such as TCP, UDP, and ICMP. It is an important basis for a firewall to forward packets.
The firewall uses a stateful inspection mechanism which determines the status of a connection based on the first packet or the first several packets. Subsequent packets are then processed based on the connection status. The stateful inspection mechanism improves the detection and forwarding efficiency. The session table is used for maintaining the connection status. To forward TCP, UDP, and ICMP packets, the firewall must look up the session table for the connection status and then process the packets accordingly.
PC1 sends a packet.
The firewall permits the first packet.
PC2 replies with a packet.
The firewall forwards the packet.
Security Zone
Security Policy
Session Table
Server Map
Notes: In this example, PC1 initiates an HTTP connection to PC2, so the firewall marks the HTTP protocol and connection information in the session table and identifies that the traffic is forwarded based on the public routing table (VPN:public in the figure).

## Slide 24: Session Table Creation and Packet Processing
Query the session table
Match
a session
Determine whether a session can be set up through stateful detection
Query server map table
Query routing table
Query security policy
Query NAT policy
Enforce security policy
Perform subsequent packet processing
Forward the packet
Use security inspection
Yes
No
Receive the packet and perform basic processing
Use other first-packet processing
Update session
Create session
When stateful inspection is enabled on the firewall, a session entry is created for the first packet of the traffic, and subsequent packets can directly match the session entry.
Security Zone
Security Policy
Session Table
Server Map
Notes: The flowchart shows the basic processing sequence of each module of a Huawei firewall. In practice, packet processing may be different from the preceding flowchart (if there is no corresponding configuration) and depends on specific product implementation.
For details, see "Packet Forwarding Process" in the product documentation of the specified firewall model.

## Slide 25: Aging Time and Persistent Connection of the Session Table
Firewalls provide the session aging mechanism for protocols. A session that is not matched by any packet will be deleted from the session table. This mechanism prevents firewall resources from being consumed by a large number of useless and outdated session entries.
For some special services, however, the interval between two consecutive packets of a session can be very long. For example:
  When a user downloads large files through FTP, the interval between control packets along the control channel can be very long.
  A user may query the data on a database server now and then, and the interval between query operations may be far greater than the aging time of the TCP session.
If a session entry is deleted, the service is interrupted. The persistent connection mechanism can set an overlong aging time for some connections.
Security Zone
Security Policy
Session Table
Server Map

## Slide 26: Problems of Multi-Channel Protocols on a Firewall
If a strict unidirectional security policy is configured on a firewall, the firewall allows only unidirectional access. As a result, some special protocols, such as FTP, cannot work.
In FTP active mode, the client initiates a control connection to the server, and then the server initiates a data connection to the client. If the security policy configured on the firewall allows only packets from the client to pass through in one direction, FTP file transfer fails.
Similar to FTP, a multi-channel protocol occupies two or more interfaces during communication. This problem needs to be considered for all multi-channel protocols.
FTP Client
FTP Server
1
2
The client initiates a control connection.
The server initiates a data connection.
rule
From FTP Client to FTP Server
Permit
Unidirectional security policy
Security Zone
Security Policy
Session Table
Server Map
Notes: Single-channel protocol: uses only one port during communication. For example, WWW uses only port 80.
Multi-channel protocol: uses two or more ports for communication.
FTP is a typical multi-channel protocol. Two connections are set up between the FTP client and server: control and data connections. A control connection is used to transmit FTP instructions and parameters, including information required for establishing a data connection. A data connection is used to obtain server directories and transfer data. The port number used for the data connection is negotiated during the control connection. FTP works in either active (PORT) or passive (PASV) mode, determined by the mode of initiating a data connection. In active mode, port 20 of the FTP server initiates a data connection to the FTP client. In passive mode, the FTP server accepts the data connection initiated by the FTP client. The mode can be set on the FTP client. Here, the active mode is used as an example.
When multi-channel protocols exist, a firewall can be configured with security policies that define loose conditions to solve the problem of protocol unavailability. However, this brings security risks.

## Slide 27: Multi-Channel Protocol — FTP Process
IP | 192.168.1.2
Port | xxxx
IP | 192.168.1.2
Port | yyyy
IP | 10.1.1.2
Port | 20
IP | 10.1.1.2
Port | 21
SYN
SYN+ACK
ACK
...
...
User name/password
PORT Command (IP 192.168.1.2 Port yyyy)
PORT Command OK
SYN
SYN+ACK
ACK
LIST Command
Transmit data
...
Three-way handshake for the control connection
Three-way handshake for the data connection
Port negotiation by running the PORT command
xxxx/yyyy
Control connection
Data connection
Random port
FTP Client
FTP Server
The client uses a random port to send a control connection setup request to port 21 of the server.
Port 20 of the server sends a data connection setup request to the port (yyyy) negotiated by the client.
Question: How does a firewall permit data connections in a refined manner?
Security Zone
Security Policy
Session Table
Server Map
Notes: Most multimedia application protocols (such as H.323 and SIP), FTP, and NetMeeting use prescribed ports to initialize a control connection and then dynamically negotiate a port for data transmission. The port selection is unpredictable. Some applications may even use multiple ports at one time. Packet filtering firewalls can use ACLs to match applications of single-channel protocols to protect internal networks against attacks. However, ACLs can block only applications using fixed ports, and cannot match multi-channel protocol applications that use random ports, bringing security risks.

## Slide 28: ASPF and Server Map
To solve problems of multi-channel protocols, a firewall needs to identify addresses and ports negotiated at the application layer. The Application Specific Packet Filter (ASPF) function must be enabled.
ASPF is also called status-based packet filtering. It can automatically detect application-layer information of certain packets and define corresponding permit rules according to application-layer information. That is, a server map is generated.
The server map also records the connection status similar to that in the session table. The server map is equivalent to a simplified session table and is generated before actual traffic arrives. When the traffic reaches the firewall, the firewall generates a session table based on the server map and forwards the traffic.
ASPF is enabled to solve the multi-channel protocol problem. It is a method of generating a server map.
Security Zone
Security Policy
Session Table
Server Map
Notes: When ASPF, NAT server, or source NAT (SNAT) in No-PAT mode is configured on a firewall, the firewall generates corresponding server map entries.

## Slide 29: Example of ASPF and Server Map
[FW] display firewall server-map
Type: ASPF, 10.1.1.2 -> 192.168.1.2:2097, Zone:---
Protocol: tcp(Appro: ftp-data), Left-Time:00:00:10
Vpn: public --> public
[FW] display firewall session table
ftp VPN: public --> public 192.168.1.2:2095 +-> 10.1.1.2:21
ftp-data VPN: public --> public 10.1.1.2:20 --> 192.168.1.2:2097
Create a server map on the firewall.
FTP server
10.1.1.2/24
Gateway address: 10.1.1.1
Untrusted
FTP client
192.168.1.2/24
Gateway address: 192.168.1.1
Trusted
GE1/0/1
192.168.1.1
GE1/0/2
10.1.1.1
After ASPF is configured on a firewall, the firewall checks the negotiated data connection port information in the FTP control connection and generates a server map entry. The server map entry contains information about the data channel negotiated in the FTP control channel. Then the firewall creates a session table for the packets that match server map entries.
Create a session table on the firewall.
Security Zone
Security Policy
Session Table
Server Map
Notes: The relationship between a server map and a session table:
  A server map records key information about application-layer data. If a packet matches the server map, the security policy is invalid for the packet.
  A session table represents the connection status of two communication parties.
  The server map does not represent the current connection status. It predicts subsequent packets based on the analysis of an existing connection.
  When receiving a packet, a firewall first checks whether the packet matches the session table.
  If not, the firewall checks whether the packet matches the server map.
  The security policy is invalid for the packet matching the server map.
  Then the firewall creates a session table for the packet matching the server map.

## Slide 30: Server Map and Simplified Packet Forwarding Process
Perform other first-packet processing
Forward the packet
Generated a session table
Receive a packet
Does the packet match the session table?
Does the
packet match the
server map?
When a firewall receives a packet that does not match a session table, the firewall starts the first-packet processing to check whether the packet matches the server map. If so, the firewall generates a session table to forward packets. If not, the firewall performs other packet processing.
Y
Y
N
N
Security Zone
Security Policy
Session Table
Server Map

## Slide 31
This section describes basic concepts and features of firewalls, including:
  Security zone
  Security policy
  Session table
  Server map

## Slide 32
Introduction to Firewalls
Basic Firewall Concepts
Basic Firewall Configurations

## Slide 33: Basic Firewall Configurations — Interface
[Huawei] interface interface-type interface-number
Create an interface or enter the interface view.
The interface command on a firewall is used to create an interface or enter the view of a specified interface, which is similar to that on switches and routers.
[Huawei-GigabitEthernet0/0/1] service-manage { http | https | ping | ssh | snmp | netconf | telnet | all } { permit | deny }
Configure the protocol allowed by the interface.
The service-manage command allows or blocks access to a firewall through HTTP, HTTPS, ping, SSH, SNMP, NETCONF, or Telnet.
By default, an interface has the access control and management function enabled. HTTP, HTTPS, and ping permissions are enabled on the management interface only. All permissions on non-management interfaces are disabled.

## Slide 34: Basic Firewall Configurations — Security Zone
[Huawei] firewall zone name zone-name [ id id ]
Create a security zone and enter the security zone view.
firewall zone name creates a security zone and displays the security zone view. id specifies the ID of a security zone. The value ranges from 4 to 99 and increases in ascending order.
firewall zone displays the security zone view. The default four security zones of a firewall cannot be deleted.
[Huawei-zone-name] set priority security-priority
Set the priority of the security zone.
The priority value ranges from 1 to 100. It is unique. A larger value indicates a higher priority. Default security zones cannot be deleted, and their priorities cannot be reconfigured or deleted.
[Huawei] add interface interface-type { interface-number | interface-number.subinterface-number }
Add an interface to the security zone.
A security zone needs to be associated with a specific interface of a firewall. That is, the interface needs to be added to the security zone. The interface can be a physical or logical one.

## Slide 35: Basic Firewall Configurations — Security Policy (1)
[Huawei] security-policy
Enter the security policy view.
You can create, copy, move, or rename a security policy rule in the security policy view.
[Huawei-policy-security] rule name rule-name
Configure a security policy rule in the security policy view and enter the security policy rule view.
[Huawei-policy-security-rule-name] source-zone { zone-name &<1-6> | any }
Configure the source security zone of the security policy rule in the security policy rule view.
The security zone must exist in the system. You can add or delete a maximum of six security zones in a security policy rule at a time.
Configure the destination security zone of the security policy rule in the security policy rule view.
[Huawei-policy-security-rule-name] destination-zone { zone-name &<1-6> | any }

## Slide 36: Basic Firewall Configurations — Security Policy (2)
[Huawei-policy-security-rule-name] source-address ipv4-address { ipv4-mask-length | mask mask-address}
Configure the source IP address of the security policy rule.
In the command, mask-address is a wildcard mask.
[Huawei-policy-security-rule-name] destination-address ipv4-address { ipv4-mask-length | mask mask-address}
Configure the destination IP address of the security policy rule.
In the command, mask-address is a wildcard mask.
The service command configures a service. For example, the service protocol command references a TCP/UDP/SCTP port or an IP-layer protocol in a security policy.
Configure an action in the security policy rule.
[Huawei] action { permit | deny }
Configure a service.
[Huawei] service { service-name &<1-6> | any }
The default action of a firewall is deny.
Notes: The source and destination IP addresses specified in the security policy rule view can have many optional parameters, such as the IP address group, region, and region group. This course does not describe these optional parameters. For more information, see the product documentation.

## Slide 37: Firewall Configuration Examples
Create security zone OM
priority 95
Trusted
Untrusted
GE1/0/1
GE1/0/3
GE1/0/2
Description:
The firewall isolates the network into three security zones: trusted, untrusted, and OM. The priority of the OM zone is 95. The requirements are as follows:
  GE1/0/1 of the firewall can respond to ping requests.
  ICMP traffic in the OM zone can reach the untrusted zone.
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration
The configuration process consists of four steps:
Configure a firewall interface.
Configure a security zone.
Configure a security policy.
Verify the configuration.

## Slide 38: Configuration Example — Interface
# Configure an IP address for the interface and allow the ping service on GE1/0/1.
[FW] interface GigabitEthernet 1/0/1
[FW-GigabitEthernet1/0/1] ip address 1.1.1.1 24
[FW-GigabitEthernet1/0/1] service-manage ping permit
[FW-GigabitEthernet1/0/1] interface GigabitEthernet 1/0/2
[FW-GigabitEthernet1/0/2] ip address 2.2.2.1 24
[FW-GigabitEthernet1/0/2] interface GigabitEthernet 1/0/3
[FW-GigabitEthernet1/0/3] ip address 3.3.3.1 24
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration
Create security zone OM
priority 95
trust
untrust
GE1/0/1
1.1.1.1/24
GE1/0/3
3.3.3.1/24
GE1/0/2
2.2.2.1/24
Task list:
Configure an IP address for a firewall interface according to the planning.
Configure GE1/0/1 to allow the ping service.

## Slide 39: Configuration Example — Security Zone
Create security zone OM
priority 95
Trusted
Untrusted
GE1/0/1
GE1/0/3
GE1/0/2
# Create a security zone.
[FW] firewall zone name OM
[FW-zone-OM] set priority 95
[FW-zone-OM] quit
# Add interfaces to corresponding security zones.
[FW] firewall zone trust
[FW-zone-trust] add interface GigabitEthernet 1/0/1
[FW] firewall zone OM
[FW-zone-OM] add interface GigabitEthernet 1/0/2
[FW] firewall zone untrust
[FW-zone-untrust] add interface GigabitEthernet 1/0/3
Task list:
Create security zone OM and set its priority to 95.
Add interfaces to the planned security zones.
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration

## Slide 40: Configuration Example — Security Policy Configuration
# Create a security policy.
[FW-policy-security] rule name R1
[FW-policy-security-rule-R1] source-zone OM
[FW-policy-security-rule-R1] destination-zone untrust
[FW-policy-security-rule-R1] service icmp
[FW-policy-security-rule-R1] action permit
Task list:
Create security policy R1.
Configure a security policy rule, including the source and destination zones, service type, and action.
Create security zone OM
priority 95
Trusted
Untrusted
GE1/0/1
GE1/0/3
GE1/0/2
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration

## Slide 41: Configuration Example — Verification (1)
# Check the session table on the firewall.
[FW]display firewall session table
2020-03-11 10:31:21.010
Current Total Sessions : 4
icmp VPN: public --> public 1.1.1.2:14265 --> 1.1.1.1:2048
icmp VPN: public --> public 1.1.1.2:15289 --> 1.1.1.1:2048
icmp VPN: public --> public 1.1.1.2:14777 --> 1.1.1.1:2048
icmp VPN: public --> public 1.1.1.2:15033 --> 1.1.1.1:2048
Create security zone OM
priority 95
Trusted
Untrusted
GE1/0/1
1.1.1.1/24
GE1/0/3
3.3.3.1/24
GE1/0/2
2.2.2.1/24
The PC in the trusted zone initiates a ping test to GE1/0/1 of the firewall.
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration

## Slide 42: Configuration Example — Verification (2)
# Check the session table on the firewall.
[FW]display firewall session table
2020-03-11 10:30:15.150
Current Total Sessions : 4
icmp VPN: public --> public 2.2.2.2:63928 --> 3.3.3.2:2048
icmp VPN: public --> public 2.2.2.2:63672 --> 3.3.3.2:2048
icmp VPN: public --> public 2.2.2.2:63416 --> 3.3.3.2:2048
icmp VPN: public --> public 2.2.2.2:62904 --> 3.3.3.2:2048
Trusted
Untrusted
GE1/0/1
1.1.1.1/24
GE1/0/3
3.3.3.1/24
2.2.2.2
1.1.1.2
3.3.3.2
The device at 2.2.2.2 in security zone OM initiates a ping request to the device at 3.3.3.2 in the untrusted zone.
GE1/0/2
2.2.2.1/24
Create security zone OM
priority 95
Question: ICMP does not have a port number. What is the port number in the firewall session table?
Configure an interface
Configure a security zone
Configure a security policy
Verify the configuration
Notes: ICMP does not have a port. However, the firewall generates a port number when generating the session table corresponding to ICMP traffic to meet status detection requirements.

## Slide 43
This section describes basic configuration commands of the firewall. After learning basic firewall configurations, you can use commands to perform the following configurations:
  Configure firewall interfaces.
  Assign firewall security zones.
  Configure security policies.
  Check firewall session information.

## Slide 44
(Single) By default, a firewall has ( ) security zones.
A. 1 B. 2 C. 3 D. 4
(TorF) The firewall must generate a server map before generating a session table.
(Multiple) Which of the following statements about Huawei AIFWs are correct?
A. Built-in CDE - malicious file detection engine
B. Built-in probe
C. Built-in APT detection engine (AIE)
D. Built-in deception sensor
Notes: 1. D
2. F
3. ABCD

## Slide 45
Firewalls are one of the most important security devices in the communications field. This course helps you learn basic concepts, development history, and basic configurations of firewalls.
The security zone, security policy, session table, and server map are basic and important concepts of firewalls and are the prerequisite for further learning the firewall technology.
Firewalls provide more security functions, such as content security filtering, antivirus, and intrusion prevention. For more information about firewall technologies, see Huawei Certification — Security.

## Slide 46
Huawei HiSecEngine USG6000E series AIFW documents.
https://support.huawei.com/enterprise/en/security/usg6600e-pid-23176231

## Slide 47
For more training materials and videos, visit https://e.huawei.com/en/talent/#/home.