## Slide 1
Chen Qibiao/cwx47601
2020-03
He Junjian/hwx580230
New
YYYY-MM-DD
YYYY-MM-DD
YYYY-MM-DD
YYYY-MM-DD

## Slide 2: Security Features of Network Devices

## Slide 3
IP networks of large scales usually have numerous network devices and various communication protocols, adding complexity to network management. It is difficult to balance security and service flexibility, as well as security and management & maintenance convenience. When striking a balance between these, administrators with varying degrees of technical and management expertise perform differently. Administrators may ignore security protection capabilities in the pursuit of service availability, resulting in the failure to configure necessary security measures. The devices, therefore, cannot effectively defend against attacks as they are designed to.
This course describes common security hardening policies of network devices and provides examples for common security configurations.

## Slide 4
Upon completion of this course, you will be able to:
  Learn common device security hardening policies.
  Configure STelnet.
  Configure local attack defense.

## Slide 5
Common Security Hardening Policies
Examples for Security Hardening Policy Deployment

## Slide 6: Why Is Security Vital to Network Devices?
Network security is a systematic project. Everything on the network may become a target of attacks, and network devices are no exception.
Common attacks on network devices include the following:
  Malicious users log in to network devices to perform unauthorized operations (for example, restarting the devices), leading to malfunctioning networks.
  A large number of control packets (for example, ICMP packets) are forged and sent to the CPU of a target device, leading to a surge in the CPU usage.
<R1>telnet x.x.x.x
<Rn>reboot
…
…
1
<R2>ping x.x.x.x
2

## Slide 7: Common Security Hardening Policies
Common security hardening policies on network devices include the following:
  Disabling unused services and ports
  Discarding insecure access channels
  Access control based on trusted paths
  Local attack defense

## Slide 8: Disabling Unused Services and Ports
Based on service requirements analysis and the minimum authorization principle, disable unused services and ports.
  Disable unused physical ports, which then cannot be used for communication even when network cables are connected.
  Disable unused protocol ports, for example, common Telnet, FTP, and HTTP ports, which then cannot be accessed from external systems.
<SW1> system-view
[SW1] undo ftp server
Warning: The operation will stop the FTP server. Do you want to continue? [Y/N]:y
Info: Succeeded in closing the FTP server.
[SW1]port-group protgroup1
[SW1-port-group-protgroup1]group-member GigabitEthernet 0/0/4 to GigabitEthernet0/0/48
[SW1-port-group-protgroup1]shutdown
PC1
PC2
PC3
PC4
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/3
SW1
Disable the FTP function and unused ports on SW1.
Port Shutdown
Access Channel
URPF
Local Attack Defense

## Slide 9: Discarding Insecure Access Channels
The access requirements of services must be preferentially fulfilled based on service requirements analysis. When an access requirement involves multiple access channel services, secure channels must be selected and insecure ones must be discarded.
Access Requirement | Insecure Channel | Secure Channel
Remote login | Telnet | SSHv2
File transfer | FTP and TFTP | SFTP
NE management | SNMPv1 and SNMPv2 | SNMPv3
NMS login | HTTP | HTTPS
Port Shutdown
Access Channel
URPF
Local Attack Defense
Notes: When you log in to a device through the CLI, web UI, or NMS, you are advised to use the corresponding SSH, HTTPS, or SNMPv3 channel.
SFTP is recommended for data transmission between devices and between devices and terminals.

## Slide 10: Secure Data Access Channel
To ensure device security, select secure access channels as long as conditions permit.
Common scenarios and protocols for device data transmission security:
  Remote login:
    Telnet: transmits data in clear text using TCP.
    STelnet: provides secure information protection and powerful authentication functions based on SSH.
  File operations:
    FTP: supports file transfer and file directory operations, provides authorization and authentication functions, and transmits data in clear text.
    TFTP: supports only file transfer and transmits data in clear text. It does not support authorization or authentication.
    SFTP: supports file transfer and file directory operations; strictly encrypts data and protects data integrity.
Port Shutdown
Access Channel
URPF
Local Attack Defense

## Slide 11: SSH Overview
Secure Shell (SSH) provides secure remote login, file transfer, and TCP/IP tunnels on insecure networks. It encrypts not only the password during login, but also the executed command data after login.
After an authorized user logs in from the client and the user name and password are verified, the client attempts to establish a session with the server. Each session is an independent logical channel and can be used by different upper-layer applications.
STelnet and SFTP each use a logical channel to encrypt data through SSH, implementing secure data transmission.
SSH channel
STelnet
SFTP
Port Shutdown
Access Channel
URPF
Local Attack Defense
Notes: SSH is developed by the IETF. The latest version is V2.0. Earlier versions 1.3 and 1.5 have security risks and are gradually obsolete.
SSH supports two-way authentication between the server and client, and provides security services such as confidentiality and integrity protection.

## Slide 12: SSH Protocol Structure
The SSH protocol framework has three pillar protocols: transport protocol, user authentication protocol, and connection protocol.
  Transport protocol: provides version negotiation, encryption algorithm negotiation, key exchange, server authentication, and information integrity verification.
  User authentication protocol: authenticates clients for the server.
  Connection protocol: multiplexes an encrypted information tunnel into multiple logical channels, which are provided for upper-layer application protocols (STelnet and SFTP). Various upper-layer application protocols can be relatively independent of the SSH basic system. They also rely on this basic system to use the SSH security mechanism through the connection protocol.
TCP connection
Client
SSH transport protocol
SSH user authentication protocol
SSH connection protocol
Server
SSH transport protocol
SSH user authentication protocol
SSH connection protocol
SFTP/STelnet
Port Shutdown
Access Channel
URPF
Local Attack Defense
Notes: SSH uses the following types of algorithms:
  MAC algorithms for data integrity protection, such as HMAC-MD5 and HMAC-MD5-96
  Data encryption algorithms, such as 3DES-CBC, AES128-CBC, and DES-CBC
  Key exchange algorithm used to generate session keys, such as diffle-hellman-group-exchange-sha1
  Host public key algorithm used for digital signature and authentication, such as RSA and DSA

## Slide 13: Access Control Based on Trusted Paths
Configure access control policies based on trusted paths on network devices to improve network security.
Deploy URPF to determine whether the source address of a packet is valid. If the path of the packet is inconsistent with the path learned by URPF, the packet is discarded. In this way, URPF helps to prevent network attacks with spoofed IP source addresses.
Server
Forges the source address of PC1 to initiate access.
R1
R2
R3
PC1
PC2
1
R3 checks FIB information and finds that the outbound interface to PC1 is GE0/0/1.
2
GE0/0/0
GE0/0/1
3
Discards the packet.
Port Shutdown
Access Channel
URPF
Local Attack Defense
Notes: The openness of IP networks determines that anyone can access or attack the target host as long as routes are reachable.
For a host, the path of the packets sent to it from a client is fixed, especially at the edge of a network.
Unicast Reverse Path Forwarding (URPF) can be classified into strict URPF and loose URPF, and the mode in which matching the default route is allowed can be configured. During the URPF check, the device checks whether source IP addresses of packets are valid based on the routing table.
  In strict mode, if a packet matches a specific route and the inbound interface of the packet is the same as the outbound interface of the route, the packet is allowed to pass. Otherwise, the packet is discarded.
  In loose mode, if a packet matches a specific route, the packet is allowed to pass. Otherwise, the packet is discarded. In this mode, the interface is not checked. By default, the device does not match packets with the default route. You can configure the device to match packets with the default route.
  Matching the default route must work with strict URPF. When a packet matches a specific route or the default route and the inbound interface of the packet is the same as the outbound interface of the matched route, the packet is allowed to pass. Otherwise, the packet is discarded. Matching the default route cannot be configured with loose URPF because attack defense cannot be achieved in this way. Loose URPF and strict URPF are mutually exclusive.

## Slide 14: Local Attack Defense
In addition to numerous normal service packets, CPUs of devices on a network may also receive large numbers of attack packets. If a CPU is busy processing attack packets for an extended period, other services, or even the system itself, will experience interruption. Similarly, if a large number of normal packets are sent to the CPU, the CPU usage will surge and device performance will deteriorate, adversely affecting services.
To ensure that the CPU can properly process and respond to normal services, the device provides the local attack defense function, which has been specifically designed for packets sent to the CPU and is primarily used to protect the device from attacks and ensure consistency of existing services when an attack occurs.
Local attack defense includes CPU attack defense and attack source tracing.
  CPU attack defense can rate-limit packets destined for the CPU so that only a limited number of packets are sent to the CPU within a certain period of time. This ensures that the CPU can properly process services.
  Attack source tracing defends against Denial of Service (DoS) attacks. A device enabled with attack source tracing analyzes packets sent to the CPU, collects statistics on the packets, and allows a packet rate threshold to be set for the packets. Packets sent at a threshold-crossing rate are considered as attack packets. The device finds the source user address or source interface of the attacker by analyzing the attack packets and generates logs or alarms to alert a network administrator. The network administrator then takes measures to protect the device against the attack or configure the device to discard packets sent by the attack source.
Port Shutdown
Access Channel
URPF
Local Attack Defense

## Slide 15: CPU Attack Defense
Network devices employ four-level security mechanisms to protect their security:
  Level 1: filter invalid packets sent to the CPU by using blacklists.
  Level 2: Use Control Plane Committed Access Rate (CPCAR) to rate-limit the packets sent to the CPU based on the protocol type, preventing excess packets of a protocol from being sent to the CPU.
  Level 3: schedule packets sent to the CPU based on the protocol priority to ensure that packets with higher protocol priorities are preferentially processed.
  Level 4: uniformly rate-limit all packets sent to the CPU and randomly discard the excess packets to ensure CPU security.
Regarding rate limiting on packets sent to the CPU in active link protection, when a device detects the establishment of an SSH, Telnet, HTTP, FTP, or BGP session, it enables active link protection for the session. Subsequent packets that match the session characteristics will be sent to the CPU at a high rate, ensuring the reliability and stability of services related to the session.
Port Shutdown
Access Channel
URPF
Local Attack Defense

## Slide 16: Working Mechanism of Attack Source Tracing
Attack source tracing involves four steps: parsing packets, analyzing traffic, identifying an attack source, and sending logs or alarms to a network administrator or taking punishment measures.
The device locates the attack source, and the network administrator rate-limits the packets sent from the attack source by configuring ACLs or blacklists to protect the CPU.
Packet parsing
Attack source tracing
Traffic analysis
Attack source identification
Log & alarm
Punishment
Chip-based forwarding
Port Shutdown
Access Channel
URPF
Local Attack Defense

## Slide 17
Common Security Hardening Policies
Examples for Security Hardening Policy Deployment
  STelnet Configuration
  Local Attack Defense Configuration

## Slide 18: Basic SSH Configuration (1)
[Huawei] stelnet server enable
Enable the SSH server function.
[Huawei] ssh user user-name authentication-type { password | rsa | password-rsa | all }
Configure the authentication mode for an SSH user.
If RSA authentication is used, configure the public key of the SSH client on the SSH server. When the SSH client connects to the SSH server, the SSH client passes the authentication if its private key matches the configured public key.
[Huawei] rsa peer-public-key key-name [ encoding-type { der | openssh | pem } ]
[Huawei-rsa-public-key] public-key-code begin
Configure the public key generated by the SSH client.
The public key must be a hexadecimal character string in the public key encoding format, and generated by the SSH client.
[Huawei-rsa-key-code] public-key-code end
[Huawei-rsa-public-key] peer-public-key end
Exit the public key editing view, edit the public key view, and return to the system view.

## Slide 19: Basic SSH Configuration (2)
[Huawei] ssh user user-name assign { rsa-key | ecc-key } key-name
Assign an RSA public key to the SSH user.
[Huawei] rsa local-key-pair create
Generate the local RSA host and server key pairs.
If an RSA key pair exists, the system prompts you to confirm whether to replace the original key pair. After you run this command, the system prompts you to enter the number of bits of the host key. The difference between the bits in the server and host key pairs must be 128 bits or more. The host key pair length and server key pair length both range from 512 to 2048, in bits, and their default values are both 2048.
[Huawei] ssh client first-time enable
Enable first authentication on the SSH client.
When an SSH client accesses an SSH server for the first time and the public host key of the SSH server is not configured on the SSH client, enable the first authentication function. The SSH client then can access the SSH server and save the public host key on the SSH client. When the SSH client accesses the SSH server next time, the saved public host key is used to authenticate the SSH server.

## Slide 20: SSH Configuration Example
Configure STelnet for secure remote login to R3.
Configure two login users client001 and client002 on R3. R1 uses client001 to log in to R3 in password authentication mode, and R2 uses client002 to log in to R3 in RSA authentication mode. Configure a security policy to ensure that only users from R1 and R2 can log in to R3.
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Procedure:
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.

## Slide 21: SSH Configuration Commands (1)
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
[R3] rsa local-key-pair create
The key name will be: Host
RSA keys defined for Host already exist. Confirm to replace them? (y/n):y
The range of public key size is (512 ~ 2048).
NOTES: If the key modulus is less than 2048,
It will introduce potential security risks.
Input the bits in the modulus[default = 2048]:2048
Generating keys... ......................................................................................+++ ....+++ .......................................++++++++ ..............++++++++
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.

## Slide 22: SSH Configuration Commands (2)
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.
[R3] stelnet server enable
[R3] ssh server port 1025
[R3] user-interface vty 0 4
[R3-ui-vty0-4] authentication-mode aaa
[R3-ui-vty0-4] protocol inbound ssh
[R3-ui-vty0-4] quit
[R3] aaa
[R3-aaa] local-user client001 password irreversible-cipher Huawei@123
[R3-aaa] local-user client001 privilege level 3
[R3-aaa] local-user client002 password irreversible-cipher Huawei@123
[R3-aaa] local-user client002 privilege level 3
[R3-aaa] quit
[R3] ssh user client001 authentication-type password
[R3] ssh user client002 authentication-type rsa
[R3] aaa
[R3-aaa] local-user client001 service-type ssh
[R3-aaa] local-user client002 service-type ssh
[R3-aaa] quit

## Slide 23: SSH Configuration Commands (3)
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.
# Generate a local key pair on R2.
[R2] rsa local-key-pair create
The key name will be: Host
RSA keys defined for Host already exist.
Confirm to replace them? (y/n):y
The range of public key size is (512 ~ 2048).
NOTES: If the key modulus is less than 2048,
It will introduce potential security risks.
Input the bits in the modulus[default = 2048]:2048
Generating keys... ......................................................................................
+++ ....+++ .......................................++++++++ ..............++++++++
Notes: The configurations in this slide and the following two slides enable user client002 to log in to R3.

## Slide 24: SSH Configuration Commands (4)
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.
# Display the public key in the RSA key pair generated by R2.
[R2] display rsa local-key-pair public
Key code: 30820109 02820100 CB0E88EC A1C2CFEA F97126F9 36919C08 0455127B A3A48594 69517096 35626F55 E4FAF0EB FDA2B9E9 5E417B2B E09F38B0 D26FCA73 FE2E3FC4 DFBEC8CF 4ED0C909 E8D975E6 FFC73C81 D13FE71E 759DC805 B0F0E877 4FC9288E BE1E197C 2A7186B0 B56F5573 3A5EA588 29C63E3B 20D56233 8E63278D F941734F 6B359C69 BBAE5A52 EB842179 04B4204D 5DB31D72 97F0C085 DA771F66 0AAADC28 D264CEB9 5BADA92C CDE9F116 D6D99C48 CEBA3A1D 868B053A 32941D85 CCAA9796 A4B55760 0A8108ED DB45DA12 F61634C9 59431600 341FEDEF 5379D565 A8D1953D DEA018A2 72F99FFC 63DE04BF 2A6219BD DF13D705 27D63DEF 83D556BC 5B44D983 8D5EA126 C1EB71CB 0203 010001
=====================================================
Time of Key pair created: 2012-08-06 17:17:44+00:00 Key name: Server Key type: RSA encryption Key =====================================================
Key code: 3067 0260 DF8AFF3C 28213B94 2292852E E98657EE 11DE5AF4 8A176878 CDD4BD31 55E05735 3080F367 A83A9034 47D534CA 81250C1D 35401DC3 464E9E5F A50202CF A7AD09CD AC3F531C A763F0A0 4C8E51B9 18755400 76AF4A78 225C92C3 01FE0DFF 06908363 0203 010001

## Slide 25: SSH Configuration Commands (5)
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.
# Copy the RSA public key (the information in bold in the display command output in the previous slide) generated on R2 to the server.
[R3] rsa peer-public-key rsakey001
[R3-rsa-public-key] public-key-code begin
[R3-rsa-key-code] 30820109
[R3-rsa-key-code] 02820100
[R3-rsa-key-code] CB0E88EC A1C2CFEA F97126F9 36919C08 0455127B
[R3-rsa-key-code] ......
[R3-rsa-key-code] 010001
[R3-rsa-key-code] public-key-code end
[R3-rsa-public-key] peer-public-key end
# Bind the RSA public key of R2 to client002 on R3.
[R3] ssh user client002 assign rsa-key rsakey001

## Slide 26: Verifying the SSH Configuration
R1
192.168.1.2
R2
192.168.1.3
192.168.1.1
R3
SW1
Configure the SSH server (R3) to generate a local key pair for secure data exchange between the server and clients (R1 and R2).
Configure SSH users client001 and client002 on the SSH server.
Enable the STelnet server function on the SSH server.
Set the service type of SSH users client001 and client002 to STelnet on the SSH server.
Customize an SSH service port number on the SSH server. Then attackers cannot connect to the server through the standard SSH service port, ensuring security.
Log in to the SSH server as users client001 and client002 through STelnet.
[R2] ssh client first-time enable
[R2] stelnet 192.168.1.1 1025
Please input the username:client002
Trying 192.168.1.1 ... Press CTRL+K to abort Connected to 192.168.1.1 ...
The server is not authenticated. Continue to access it?(y/n)[n]:y
Save the server's public key?(y/n)[n]:y
The server's public key will be saved with the name 192.168.1.1. Please wait...
<R3> # The login is successful.
[R1] ssh client first-time enable
[R1] stelnet 192.168.1.1 1025
Please input the username:client001
Trying 192.168.1.1 ...
Press CTRL+K to abort
Connected to 192.168.1.1 ...
The server is not authenticated. Continue to access it?(y/n)[n]:y
Save the server's public key?(y/n)[n]:y
The server's public key will be saved with the name 192.168.1.1. Please wait... Enter password:
<R3> # The login is successful.

## Slide 27
Common Security Hardening Policies
Examples for Security Hardening Policy Deployment
  STelnet Configuration
  Local Attack Defense Configuration

## Slide 28: Basic Configuration of Local Attack Defense (1)
[Huawei] cpu-defend policy policy-name
Create an attack defense policy and enter the attack defense policy view.
[Huawei-cpu-defend-policy-test] blacklist blacklist-id acl acl-number
Configure a blacklist.
If multiple blacklists need to be configured in an attack defense policy, Layer 2 ACLs and basic ACLs, Layer 2 ACLs and advanced ACLs, or all the three types of ACLs cannot be used together in the blacklist group of the attack defense policy.
[Huawei-cpu-defend-policy-test] packet-type packet-type rate-limit rate-value
Configure the rate limit for packets sent to the CPU.
If a device receives attack packets or a large number of normal packets of a protocol type destined for the CPU, you can rate-limit the packets of this protocol type within a small range to reduce the impact on CPU's processing of normal services.
[Huawei-cpu-defend-policy-test] packet-type packet-type priority priority-level
Configure the priority for packets of a specified protocol type sent to the CPU.

## Slide 29: Basic Configuration of Local Attack Defense (2)
Enable active link protection.
[Huawei-cpu-defend-policy-test] cpu-defend application-apperceive [ ssh | telnet | bgp | ftp | http ] enable
By default, active link protection is enabled for SSH, Telnet, SSHv6, Telnetv6, FTP, BGP, and HTTP.
[Huawei-cpu-defend-policy-test] auto-defend enable
Enable attack source tracing.
[Huawei-cpu-defend-policy-test] auto-defend threshold threshold
Set the rate threshold of attack source tracing.
[Huawei-cpu-defend-policy-test] auto-defend alarm enable
Enable the event reporting function for attack source tracing.
Apply the attack defense policy.
[Huawei] cpu-defend-policy policy-name [ global | slot slot-id ]

## Slide 30: Configuration Example of Local Attack Defense
Net1
Net2
R2
R1
Net3
GE2/0/1
GE2/0/2
GE2/0/3
As shown in the figure, users on different LANs access the Internet through R1. To locate attacks on R1, attack source tracing needs to be configured to trace the attack source. The existing network conditions are as follows:
  A user on Net1 frequently initiates attacks to R1.
  R1 receives a large number of ARP Request packets, degrading its CPU performance.
  R1 cannot provide the FTP service.
  LAN users obtain IP addresses through DHCP, whereas R1 does not preferentially process DHCP packets sent to the CPU.
  R1 receives a large number of Telnet packets.
To address these issues, proper configurations are required on R1.
Notes: Net: network

## Slide 31: Local Attack Defense Configuration Commands (1)
Net1
Net2
192.168.1.1
R2
R1
Net3
GE2/0/1
GE2/0/2
GE2/0/3
  Configure a blacklist and add the attacker (0001-c0a8-0102) on network segment Net1 to the blacklist to prevent the attacker from accessing the network.
  Configure the rate limit for ARP Request packets sent to the CPU, reducing the impact on CPU's processing of normal services.
  Configure active link protection for FTP so that R1 can provide the FTP service.
  Configure a high priority for DHCP client packets so that R1 preferentially processes DHCP client packets sent to the CPU.
  Disable the Telnet server function on R1 so that R1 discards received Telnet packets.
# Configure an ACL to be referenced by a blacklist.
[R1] acl number 4001
[R1-acl-L2-4001] rule 5 permit source-mac 0001-c0a8-0102
[R1-acl-L2-4001] quit
# Create an attack defense policy.
[R1] cpu-defend policy devicesafety
# Configure attack source tracing.
[R1-cpu-defend-policy-devicesafety] auto-defend enable
[R1-cpu-defend-policy-devicesafety] auto-defend threshold 50
# Configure the blacklist.
[R1-cpu-defend-policy-devicesafety] blacklist 1 acl 4001

## Slide 32: Local Attack Defense Configuration Commands (2)
Net1
Net2
192.168.1.1
R2
R1
Net3
GE2/0/1
GE2/0/2
GE2/0/3
  Configure a blacklist and add attackers on the network segment Net1 to the blacklist to prevent users on Net1 from accessing the network.
  Configure the rate limit for ARP Request packets sent to the CPU, reducing the impact on CPU's processing of normal services.
  Configure active link protection for FTP so that R1 can provide the FTP service.
  Configure a high priority for DHCP client packets so that R1 preferentially processes DHCP client packets sent to the CPU.
  Disable the Telnet server function on R1 so that R1 discards received Telnet packets.
# Set the rate limit for ARP Request packets sent to the CPU.
[R1-cpu-defend-policy-devicesafety] packet-type arp-request rate-limit 64
# Set the rate limit for FTP packets after active link protection is enabled.
[R1-cpu-defend-policy-devicesafety] application-apperceive packet-type ftp rate-limit 2000
# Enable active link protection for FTP.
[R1] cpu-defend application-apperceive ftp enable
# Apply the attack defense policy.
[R1] cpu-defend-policy devicesafety
# Disable the Telnet server function.
[R1] undo telnet server enable
Notes: Application layer association does not need to be enabled. You only need to disable the Telnet server function on the router so that the router discards received Telnet packets.

## Slide 33: Verifying the Local Attack Defense Configuration
Net1
Net2
192.168.1.1
R2
R1
GE2/0/1
GE2/0/2
# Check the configured attack defense policy.
[R1] display cpu-defend policy devicesafety
Related slot : <0>
...
Slot<0> : Success
Configuration :
  Blacklist 1 ACL number : 4001
  Packet-type arp-request rate-limit : 64(pps)
  Packet-type dhcp-client priority : 3
  Rate-limit all-packets : 2000(pps)(default)
  Application-apperceive packet-type ftp : 2000(pps)
  Application-apperceive packet-type tftp : 2000(pps)
# Check the statistics on packets sent to the MPU. That some packets are discarded indicates that the rate limit is set for ARP Request packets.
<R1> display cpu-defend statistics |  | 
Packet Type | Pass Packets | Drop Packets
8021X | 0 | 0
arp-miss | 5 | 0
arp-reply | 8090 | 0
arp-request | 1446576 | 127773
bfd | 0 | 0
bgp | 0 | 0
bgp4plus | 0 | 0
dhcp-client | 879 | 0
dhcp-server | 0 | 0

## Slide 34
(TorF) STelnet is more secure than Telnet for remote login. This is because STelnet uses TCP encapsulation while Telnet uses UDP encapsulation.
(TorF) Local attack defense includes CPU attack defense and attack source tracing.
Notes: False
True

## Slide 35
When performing security hardening on a device, take all possible dimensions into consideration, including the management plane, control plane, and forwarding plane. Based on the innate vulnerabilities of the device, assess network security risks and sort out the overall security architecture and security hardening policies for the device.
Use secure protocols such as SSH and SFTP for device access and data transmission, unless the device does not support these. The CPU of a device is vulnerable to attacks. Therefore, local attack defense is of vital importance.