## Slide 1
Zhang Linrui/zwx570554
2020.6.18
Liu Peng/lwx529648
2020.02.11
New
Update
Update
Update
Update
Update

## Slide 2: Introduction to VPN Technology

## Slide 3
For a large-scale enterprise, the network access requirements are not limited only to the headquarters network. Branches, branch offices, employees on business trips, and partners also need to access the network resources of the headquarters. The virtual private network (VPN) technology can be used to meet this requirement. The VPN establishes virtual private connections without changing the existing network structure. It is widely used on the live network because of its advantages, such as low cost, dedication, and virtualization.
VPN is a general term for a type of technology. Different VPN technologies provide various features and implementation modes. Common VPN technologies include Internet Protocol Security (IPsec) VPN, Generic Routing Encapsulation (GRE) VPN, Layer 2 Tunneling Protocol (L2TP) VPN and Multiprotocol Label Switching (MPLS) VPN.
This course provides a simple and comprehensive introduction to VPN from the aspects of definitions, common types, and usage scenarios of VPN.
Notes: IPsec: Internet Protocol Security
GRE: Generic Routing Encapsulation
L2TP: Layer 2 Tunneling Protocol.
MPLS: Multiprotocol Label Switching

## Slide 4
Upon completion of this course, you will be able to:
  Understand VPN classification.
  Understand VPN implementation modes.

## Slide 5
What Is VPN?
Common VPN Technologies

## Slide 6: Technical Background
Before VPN technology is used, data transmission between enterprise branches depends on the existing physical network (for example, the Internet). Packets are prone to being stolen or tampered with by hackers due to various insecure factors on the Internet. As a result, data may be disclosed or important data may be damaged.
In addition to the Internet, a physical private network connection can be created to secure data transmission. However, the cost is high, and it is difficult to build and maintain a private network.
Office
Enterprise
HQ
Enterprise branch
Employees on business trips
Internet
Hacker
Enterprise internal data
If the shared and insecure Internet is directly used to transmit data, data may be stolen or tampered with.
Using the Internet to transmit data
Office
Enterprise
HQ
Enterprise branch
Employees on business trips
Private network
Enterprise internal data
Building a private network for data transmission
This effectively secures enterprise data transmission, but faces problems, such as high costs, low usage, and inflexible deployment.

## Slide 7: VPN Overview
A VPN is constructed on a public network using a VPN technology. VPN users transmit private network traffic on the virtual network, implementing secure and reliable connections without changing the current network status.
Office
Enterprise
HQ
Enterprise branch
Employees on business trips
E-LAN/Internet
Public network
Virtual private network
Private
A VPN is a network dedicated to VPN users. For VPN users, using a VPN is the same as using a traditional dedicated network. The VPN can provide sufficient security guarantee to ensure that the internal information of the VPN is not interfered by external networks. Resources of a VPN are independent of the transport network (usually an IP network). That is, VPN resources are not used by non-VPN users.
Virtual
VPN users communicate with one another through the public network. The public network can also be used by non-VPN users. VPN users obtain only a logical private network.
Tunnel
Tunnel
Tunnel
Notes: Compared with the traditional data private network, the VPN has the following advantages:
  Security: Reliable connections are created between the HQ and remote users, regional offices, partners, and suppliers to secure data transmission. This is particularly important for the integration of e-commerce or financial networks with communications networks.
  Cost-effective: Public networks are used for information communication, allowing enterprises to connect remote offices, employees on business trips, and business partners at lower costs.
  Support for mobile services: VPN users can access the network anytime and anywhere, meeting the increasing mobile service requirements.
  Scalability: A VPN is a logical network. Adding or modifying nodes on a physical network does not affect VPN deployment.
A public network is also called a VPN backbone network. The public network can be the Internet, a private network built by an enterprise, or a private network leased out by a carrier.

## Slide 8: VPN Classification — Based on Construction Organizations
Enterprise HQ
Carrier
MPLS VPN
private line
Enterprise branch 2
Enterprise branch 1
Leasing a carrier's VPN leased line to build an enterprise VPN
The most common scenario is leasing carriers' MPLS VPN private lines.
Self-built enterprise VPN network
Enterprise VPN networks are established based on Internet and include the IPsec VPN, L2TP VPN, and Secure Sockets Layer (SSL) VPN.
The VPN gateway is owned by the carrier.
Enterprise HQ
Enterprise branch
Employees on business trips
VPN gateway
VPN gateway

## Slide 9: VPN Classification — Based on Networking Modes
Enterprise branch
Remote access VPN
This mode applies to VPN dial-up access of employees on business trips. Employees can access enterprise intranet resources through the VPN anywhere they can access the Internet. Such VPNs usually include the L2TP VPN and SSL VPN.
LAN-to-LAN VPN (site-to-site VPN)
It is applicable to the interconnection of LANs of two geographically dispersed divisions of a company. Such VPNs usually include the MPLS VPN and IPsec VPN.
Enterprise HQ
Internet
Employees on business trips
Location A
Enterprise HQ
Internet
VPN gateway
Employees on business trips
Location B
VPN gateway

## Slide 10: VPN Classification — Based on Network Layers
Application layer
TCP/IP reference model
Transport layer
Network layer
Data link layer
Physical layer
SSL VPN
IPsec VPN, GRE VPN
L2TP VPN, Point-to-Point Tunneling Protocol (PPTP) VPN
MPLS VPN
Notes: VPNs working at the network layer and data link layer are also called Layer 3 and Layer 2 VPNs, respectively.

## Slide 11: Key VPN Technology — Tunneling Technologies
The VPN technology is to use a tunneling technology to encapsulate packets, and establish a dedicated data transmission channel over a VPN backbone network to implement secure packet transmission.
The VPN gateways on both ends establish a point-to-point virtual communication tunnel by encapsulating and decapsulating original packets.
Enterprise
HQ
Enterprise branch
VPN gateway 1
VPN gateway 2
Internet
Original packet
VPN tunnel
Decapsulated
packet
Encapsulated packet
Encapsulation
Decapsulation
Notes: A tunnel provides a path between two nodes so that data can be transparently transmitted along the path. A VPN tunnel is a virtual connection established between VPN nodes on a VPN backbone network to transmit VPN data. A tunnel is an indispensable part for constructing a VPN, and is used to transparently transmit VPN data from one VPN node to another.
The tunnel is established using a tunneling protocol. Currently, there are many tunneling protocols, such as GRE and L2TP. The tunneling protocol adds a tunneling protocol header to the data on one end of the tunnel for encapsulation, so that the encapsulated data can be transmitted on a network. The tunneling protocol then removes the tunneling protocol header carried in the data on the other end of the tunnel for decapsulation. Packets are encapsulated and decapsulated before and after being transmitted within a tunnel, respectively.
Some tunnels can be used together, for example, forming a GRE over IPsec tunnel.

## Slide 12: Key VPN Technologies — Identity Authentication, Data Encryption, and Verification
Identity authentication, data encryption, and authentication technologies can effectively ensure the security of VPN networks and data.
  Identity authentication: This function can be used in remote VPN access scenarios. The VPN gateway authenticates user identities to ensure that only authorized users can access the network. It can also be used by VPN gateways to authenticate each other's identity.
  Data encryption: The clear text data is encrypted into ciphertext. Even if the data is intercepted by hackers, the hackers cannot obtain information in the data.
  Data verification: The data verification technology is used to check the integrity and authenticity of packets and discard the packets that are forged and tampered with.
VPN | User Identity Authentication | Encryption of Sensitive Data | Remarks
GRE | Not supported | Supports simple keyword verification, verification, and verification. | Can be used together with IPsec to encrypt and verify data.
L2TP | PPP-based Challenge-Handshake Authentication Protocol (CHAP), Password Authentication Protocol (PAP), and Extensible Authentication Protocol (EAP) authentication | Not supported | 
IPsec | Supported | Supported | Supports pre-shared key authentication or certificate authentication. Internet Key Exchange version 2 (IKEv2) EAP authentication is supported.
SSL | Supported | Supported | Supports username/password or certificate authentication.
MPLS | Not supported | Not supported | Generally, it runs on a dedicated VPN backbone network.

## Slide 13
What Is VPN?
Common VPN Technologies

## Slide 14: IPsec Overview
IPsec VPN is usually deployed between egress devices of an enterprise. Through encryption and authentication, IPsec VPN implements various functions, such as data origin authentication data encryption, data integrity protection, and anti-replay.
Enterprise egress
Enterprise HQ
Enterprise branch
Internet
Enterprise egress
Encryption of sensitive data
Encryption of sensitive data
Data encrypted
IPsec tunnel
Clear text data
Ciphertext data
IPsec
L2TP
MPLS
GRE
Notes: Data origin authentication: The receiver verifies the identity of the sender.
Data encryption: The sender encrypts data and transmits the data in ciphertext on the Internet. The receiver decrypts the received encrypted data for processing or directly forwards the data.
Data integrity: The receiver verifies the received data to determine whether the packet has been tampered with.
Anti-replay: The receiver rejects old or repetitive data packets to prevent malicious users from repeatedly sending obtained data.

## Slide 15: IPsec Protocol System
IPsec is not an independent protocol. It provides a complete set of data security architecture on the IP network, including Authentication Header (AH), Encapsulating Security Payload (ESP) and Internet Key Exchange (IKE).
IPsec
L2TP
MPLS
GRE
Security protocol
Encryption
Authentication
Key exchange
ESP
DES
3DES
AES
SM1/SM4
AH
Not supported
MD5
SHA1
SHA2
SM3
MD5
SHA1
SHA2
SM3
IKE, including Internet Security Association and Key Management Protocol (ISAKMP) and Diffie-Hellman (DH)
IPsec protocol system
Notes: IPsec uses two security protocols, AH and ESP, to transmit and encapsulate data and provide security services, such as authentication and encryption.
  The security functions provided by AH and ESP depend on the authentication and encryption algorithms used by these protocols.
  AH supports only authentication but not encryption. ESP supports both authentication and encryption.
  Keys are required by the security protocol that provides security services, such as authentication or encryption.
There are two key exchange modes:
  Out-of-band shared key: Static encryption and verification key are manually configured on the transmit and receive devices. Both parties maintain key consistency through out-of-band sharing (for example, by phone or email). The disadvantages of this mode are that poor scalability is provided and that the workload of configuring keys on a P2MP network doubles. In addition, this mode makes it difficult to change keys periodically to improve network security.
  Automatic key negotiation through IKE: IKE is built based on the framework defined by the Internet security association (SA) and the key management protocol ISAKMP. IKE uses the DH algorithm to securely distribute keys on insecure networks. This mode is easy to configure and has good scalability, especially on large-scale dynamic networks. In addition, both communication parties exchange key exchange materials to calculate the shared key. Even if a third party intercepts all exchanged data used to calculate the key, the real key cannot be calculated.

## Slide 16: IPsec Principles
During the establishment of an IPsec tunnel, IPsec SAs must be negotiated. Generally, an IPsec SA is generated through IKE negotiation.
IPsec peer A
IPsec tunnel
IPsec peer B
IKE module
User data
User data
Encryption and authentication module
IKE SA negotiation
IKE module
Encryption and authentication module
Encrypts, decrypts, and authenticates interested flows based on the IPsec SA.
Unidirectional IPsec SA
SA negotiation
IKE SA-based encryption
Packets in the IPsec SA negotiation phase
IKE negotiation phase 1
IKE negotiation phase 2
Unidirectional IPsec SA
IPsec SA negotiation
Encrypted data transmission
1
2
3
IPsec
L2TP
MPLS
GRE
Notes: An SA is uniquely identified by a triplet, which consists of a security parameter index (SPI), destination IP address, and security protocol ID (AH or ESP). The SPI is a 32-bit value generated to uniquely identify an SA, and is transmitted in an AH header and an ESP header. When manually configuring the SA, you have to manually specify the SPI value. When the SA is generated through IKE negotiation, the SPI is randomly generated.
An SA is a unidirectional logical connection. Therefore, at least two SAs must be established to protect data flows in opposite directions.
As a key negotiation protocol, IKE has two versions: IKEv1 and IKEv2. This course uses IKEv1 as an example. For details about IKEv2, see product documentation.
  IKEv1 negotiation phase 1 is to establish an IKE SA. After an IKE SA is established, all ISAKMP messages exchanged between IKE peers are encrypted and authenticated. This secure tunnel ensures that IKEv1 negotiation in phase 2 can be performed securely. An IKE SA is a bidirectional logical connection. Only one IKE SA is established between two IPsec peers.
  IKEv1 negotiation phase 2 is to establish an IPsec SA for secure data transmission and derive a key for data transmission. In this phase, the key generated in phase 1 of IKEv1 negotiation is used to authenticate the integrity and identity of ISAKMP messages and encrypt these messages, securing the message exchange.
Successful IKE negotiation indicates that a bidirectional IPsec tunnel has been established. You can define an IPsec interested flow using an ACL or an IPsec profile. All data that matches the characteristics of the interested flow is forwarded to the IPsec tunnel for processing.
Interested flows: data flows that need to be protected by IPsec.

## Slide 17: GRE Overview
GRE is a Layer 3 VPN encapsulation technology. GRE encapsulates packets of certain network layer protocols, such as Internetwork Packet Exchange (IPX), IPv4, and IPv6, so that the encapsulated packets can be transmitted over another network, for example, an IPv4 network. This solves the problem of packet transmission over heterogeneous networks.
IPsec
L2TP
MPLS
GRE
Internet
IPv4 network
Enterprise egress
IPv6 network
IPv6 network
Enterprise egress
Data re-encapsulated or re-decapsulated
GRE tunnel
IPv6 data
IPv4 data
IPv6 header
Data
IPv6 header
Data
GRE header
IPv4 header
IPv6 header
Data
Notes: As shown in the figure, a GRE tunnel is established on the IPv4 network to enable communication between two IPv6 networks.
GRE can also encapsulate multicast packets. Dynamic routing protocols use multicast packets. Therefore, GRE is often used in scenarios where multicast routing data needs to be transmitted. This is where GRE's name comes from.

## Slide 18: GRE Principles
GRE consists of three parts: passenger protocol, encapsulation protocol, and transport protocol.
  A passenger protocol refers to an original network protocol for data transmission.
  An encapsulation protocol encapsulates the packets of the passenger protocol so that the original packets can be transmitted on the new network.
  A transport protocol transmits an encapsulated packet on the new network.
IPsec
L2TP
MPLS
GRE
Internet
IPv4 network
IPv6 network
IPv6 network
Encapsulates the outer header.
The device forwards the packet on the underlying network based on the outer IP header.
Decapsulates the outer header.
S: IP1, D: IP2
Data
S: IP1, D: IP2
Data
GRE
S: IPA, D: IPB
GRE tunnel interface
GRE tunnel interface
S: IP1, D: IP2
Data
GRE
S: IPA, D: IPB
S: IP1, D: IP2
Data
IPA
IPB
IP1
IP2
R1
R2
Notes: A tunnel interface is a point-to-point virtual interface used to encapsulate packets. Similar to a loopback interface, a tunnel interface is a logical interface.
As shown in the figure, the passenger protocol is IPv6, the encapsulation protocol is GRE, and the transport protocol is IPv4. The overall forwarding process is as follows:
  When R1 receives an IPv6 packet from IP1, R1 searches the routing table and finds that the outbound interface is a tunnel interface. R1 then forwards the packet to the tunnel interface.
  The tunnel interface adds a GRE header to the original packet and then adds an IP header to the packet based on the configuration. The source address of the IP header is the source address of the tunnel, and the destination address of the IP header is the destination address of the tunnel.
  The encapsulated packet is forwarded on the IPv4 network through a common IPv4 route and finally reaches the destination R2.
  The decapsulation process is opposite to the encapsulation process, and is not described here.

## Slide 19: GRE over IPsec
GRE does not support encryption or authentication, and GRE data transmission cannot be secured.
The major disadvantage of IPsec is that it supports only the IP protocols and does not support multicast.
GRE over IPsec can be deployed to combine the advantages of the two VPN technologies.
Enterprise egress
Enterprise
HQ
Enterprise branch
Internet
Enterprise egress
Data encrypted
IPsec tunnel (outer layer)
GRE tunnel (inner layer)
IPsec
L2TP
MPLS
GRE

## Slide 20: L2TP Overview
L2TP is a virtual private dial-up network (VPDN) tunneling protocol that extends point-to-point (P2P) applications. L2TP provides access services for employees on business trips or enterprise branches to remotely access intranet resources.
An L2TP network consists of L2TP access concentrators (LACs) and L2TP network servers (LNSs).
LNS
LAC
Enterprise branch
Enterprise HQ
L2TP tunnel
Internet
L2TP tunnel
LAC
IPsec
L2TP
MPLS
GRE
Notes: The VPDN uses the dial-up function of the public network (such as the ISDN and PSTN) and the access network to implement the VPN and provide access services for enterprises, ISPs, and mobile office personnel. The VPDN uses the dedicated encryption-capable communication protocol to establish a secure virtual private network for enterprises on the public network. Geographically dispersed divisions and employees on business trips can remotely connect to the headquarters through virtual encrypted tunnels over the public network. However, other users on the public network cannot access the internal resources of the enterprise network through the virtual encryption tunnels. There are multiple VPDN tunneling protocols, among which L2TP is the most widely used.
An LAC is a device that can process PPP and L2TP packets. The LAC establishes an L2TP tunnel with the LNS. The types of devices function as the LAC vary according to the networking environment. For instance, a gateway or terminal can function as the LAC. The LAC can initiate the establishment of multiple L2TP tunnels to isolate data flows.
The LNS is the peer of the LAC, and an L2TP tunnel is established between them. The LNS is located on the border between the private and public networks of the enterprise headquarters and is usually the gateway of the enterprise headquarters.

## Slide 21: L2TP Messages
The L2TP protocol uses two types of messages: control and data messages, which are transmitted between the LAC and LNS.
  Control messages are used to establish, maintain, and tear down L2TP tunnels and session connections.
  Data messages are used to encapsulate PPP data frames and are transmitted over tunnels.
Control packet structure
Data packet structure
IP Header | UDP Header | L2TP Header | L2TP Control Data
New IP Header | UDP Header | L2TP Header | PPP Header | Original IP Header | Traffic Data
IPsec
L2TP
MPLS
GRE
Notes: Control message
  It is used to establish, maintain, and tear down L2TP tunnels and session connections. During the transmission of control messages, mechanisms, such as retransmission of dropped messages and periodic detection of tunnel connectivity, are used to ensure the reliability of control message transmission. Traffic control and congestion control of control messages are supported.
  Control messages are transmitted over the L2TP control channel. The control channel encapsulates control messages into L2TP headers and transmits them over the IP network.
Data message
  Encapsulates PPP data frames and are transmitted over tunnels. Data messages are not transmitted reliably. Dropped data packets are not retransmitted, and flow control and congestion control are not supported for the data messages.
  PPP frames carried in data messages are transmitted over unreliable data channels. The PPP frames are encapsulated using L2TP and then transmitted over the IP network.

## Slide 22: L2TP Working Process
L2TP works in the following scenarios:
  NAS-initiated scenario: Dial-up users access the enterprise intranet through the NAS.
  Client-initiated scenario: Mobile office users access the enterprise intranet.
  Call-LNS scenario: The LAC automatically dials up for enterprise intranet interconnection.
IPsec
L2TP
MPLS
GRE
LNS
LAC
(Client)
Enterprise HQ
Internet
L2TP tunnel
1. L2TP tunnel establishment
2. L2TP session establishment
3. PPP connection establishment
4. Data encapsulation and forwarding
Private IP address
Data
Private IP address
Data
L2TP client
software initiates a connection.
PPP header
L2TP header
UDP header
Public IP address
46 bytes
Private IP address
Data
L2TP tunnel establishment and data forwarding in the client-initiated scenario
Notes: NAS-initiated scenario: A remote dial-up user initiates a request to establish a tunnel. The remote system dials up to log in to the LAC through the PSTN/ISDN. The LAC then initiates a request to establish a tunnel to the LNS through the Internet. The LNS assigns IP addresses to dial-up users. The authentication and accounting for remote dial-up users can be performed by the LAC proxy or LNS.
  Users must access the Internet through PPP or PPPoE.
  The carrier's access device (mainly a BAS device) needs to have the corresponding VPN service enabled. Users need to apply for the service from the carrier.
  The two ends of an L2TP tunnel reside on the LAC and LNS. An L2TP tunnel can carry multiple sessions.
Client-initialized scenario: The LAC client (local user supporting L2TP) initiates a request to establish a tunnel. The LAC client needs to know the IP address of the LNS. The LAC client can directly initiate a tunnel connection request to the LNS without passing through an independent LAC. After receiving the request from the LAC client, the LNS authenticates the LAC client based on the username and password, and assigns a private IP address to the LAC client.
  You have to install L2TP dial-up software. Some operating systems have built-in L2TP client software.
  There is no restriction on the Internet access mode or location, which eliminates the need of the ISP to be involved.
  The two ends of an L2TP tunnel reside on the user and LNS sides. An L2TP tunnel carries a single L2TP session.

## Slide 23: L2TP Working Process
L2TP works in the following scenarios:
  NAS-initiated scenario: Dial-up users access the enterprise intranet through the NAS.
  Client-initiated scenario: Mobile office users access the enterprise intranet.
  Call-LNS scenario: The LAC automatically dials up for enterprise intranet interconnection.
IPsec
L2TP
MPLS
GRE
LNS
LAC
(Client)
Enterprise HQ
Internet
L2TP tunnel
1. L2TP tunnel establishment
2. L2TP session establishment
3. PPP connection establishment
4. Data encapsulation and forwarding
Private IP address
Data
Private IP address
Data
L2TP client
software initiates a connection.
PPP header
L2TP header
UDP header
Public IP address
46 bytes
Private IP address
Data
L2TP tunnel establishment and data forwarding in the client-initiated scenario
Notes:   The setup process in this scenario is as follows:
    A mobile user establishes an L2TP tunnel with the LNS.
    The mobile user establishes an L2TP session with the LNS: In Step 3, the mobile user establishes a PPP connection to the LNS. The L2TP session is used to record and manage the PPP connection status. Therefore, before a PPP connection is established, the two ends of the tunnel need to negotiate an L2TP session for the PPP connection. The session carries the LCP negotiation information and user authentication information of the mobile user. After authenticating the received information, the LNS notifies the mobile user that the session is successfully established. An L2TP session is identified by a session ID.
    The mobile user establishes a PPP connection to the LNS. The mobile user establishes a PPP connection to the LNS to obtain the intranet IP address assigned by the LNS.
    The mobile user sends service packets to access the server at the enterprise headquarters.
Call-LNS scenario: In addition to providing remote access services for employees on business trips, L2TP can also be used for interconnection between enterprise branches and the headquarters to implement mutual access between branch users and headquarters users. Generally, the branch router functions as the LAC to establish an L2TP tunnel with the LNS. In this way, data can be transmitted between the branch and headquarters through the L2TP tunnel.

## Slide 24: L2TP over IPsec
When an enterprise has high requirements on data and network security, L2TP cannot provide sufficient protection for packet transmission. In this case, L2TP can be used together with IPsec to protect transmitted data and prevent data interception or attacks.
PC
Enterprise branch
Enterprise HQ
PC
L2TP client
LNS
L2TP encapsulation
IPsec encapsulation
Internet
IPsec
L2TP
MPLS
GRE
Notes: Users on business trips communicate with the headquarters. L2TP is used to establish VPN connections, and the LNS is deployed in the headquarters to authenticate access users. When traveling users need to transmit confidential information to the headquarters, L2TP cannot provide sufficient protection for packet transmission. In this case, L2TP can be used together with IPsec to protect transmitted data. Dial-up software can be installed on the PC of a user on a business trip to encapsulate data packets through L2TP and then IPsec, and then send the packets to the headquarters. IPsec policies are deployed on the headquarters gateway to restore data. In this mode, IPsec protects all packets that originate at the LAC and are destined for the LNS.

## Slide 25: MPLS VPN Overview
MPLS
backbone
Multiprotocol Label Switching (MPLS) uses labels to forward packets. It was originally proposed to improve the forwarding rate of IP packets. Currently, MPLS is mainly used in VPN, traffic engineering, and QoS scenarios.
MPLS VPNs are classified into the MPLS L2VPN and MPLS L3VPN.
Enterprises can build their own MPLS networks or lease carriers' MPLS networks to obtain MPLS VPN access services.
Branch
MPLS domain
PE
PE
P
CE
HQ
CE
IPsec
L2TP
MPLS
GRE
Notes: An MPLS VPN is usually constructed by a carrier. VPN users purchase VPN services to implement route transmission and data exchange between user networks (branches and headquarters shown in the figure).
A basic MPLS VPN consists of customer edge (CE), provider edge (PE), and provider (P) devices.
  CE: an edge device on the user network. A CE has interfaces that are directly connected to a carrier network. A CE can be a router, switch, or host. Generally, CEs are unaware of VPNs and do not need to support MPLS.
  PE: an edge device on a carrier network and is directly connected to a CE. On an MPLS network, VPN processing is performed on PEs, which poses high requirements on PE performance.
  P: a backbone router on the carrier's network and is not directly connected to a CE. Ps only need to have basic MPLS forwarding capabilities and do not need to maintain VPN information.
For more information about BGP/MPLS IP VPN, see materials of related HCIP-Datacom-Advance courses.

## Slide 26
(TorF) L2TP VPN works at the network layer.
  True
  False
  (Multiple) Which of the following are included in an IPsec SA?
  SPI
  Secure transmission protocol
  Source address
  Destination IP address
Notes: Answers:
  1. B
  2. ABD

## Slide 27
The VPN technology provides a series of advantages, such as security, low cost, support for mobile services, and flexibility, and has become the most widely deployed technology on the live network.
This course briefly introduces the following common VPN technologies based on the basic concepts and classifications of VPNs:
  IPsec VPN: a set of protocols and services that provide secure transmission for IP networks.
  GRE VPN: provides a mechanism to encapsulate packets of a protocol into packets of another protocol, solving the transmission problem of heterogeneous networks.
  L2TP VPN: a Layer 2 VPN technology that provides remote access services for mobile users.
  MPLS VPN: a VPN technology that implements interconnection between sites through label switching.