## Slide 1
New
Update
Update
Update
Update
Update

## Slide 2: Introduction to VRF

## Slide 3
Looking back on the previous courses, would you recall certain protocols or technologies whose names contain the letter "V"? What are the characteristics or similarities of these protocols or technologies?
Virtual routing and forwarding (VRF) technology creates multiple routing tables on a Layer 3 forwarding device to isolate data or services. This technology is often used in isolation-related scenarios, such as when Multiprotocol Label Switching (MPLS) VPN and firewalls are deployed.
This course describes basic concepts and configurations of VRF technology.

## Slide 4
Upon completion of this course, you will be able to:
  Understand basic VRF concepts.
  Understand typical VRF applications.
  Implement basic VRF configurations.

## Slide 5
Basic Concepts of VRF
Typical VRF Configuration Examples

## Slide 6: Network Requirements
An enterprise network has a production network and a management network. Each network exclusively uses an aggregation switch and access switches and shares a core switch with the other one.
The core switch connects to a server cluster on each of the production and management networks. The two network segments are 192.168.100.0/24.
Requirements: Implement data communication within the production and management networks and isolate the communication between the two networks.
Clients on the production network
Production network servers
192.168.100.0/24
Management network servers
192.168.100.0/24
Clients on the management network

## Slide 7: Implementation by Deploying ACLs
Clients on the production network
Production network servers
192.168.100.0/24
Management network servers
192.168.100.0/24
Configure an ACL on the core switch to prevent mutual access between the production and management networks.
Disadvantages:
  The configuration is complex, and scalability is poor.
  The problem that two networks use overlapping network segments cannot be resolved. Additional configurations must be performed to prevent the use of overlapping network segments.
Clients on the management network

## Slide 8: Adding a Core Switch
Add a core switch so that an exclusive core switch serves each network to physically isolate the two networks.
Disadvantage: Additional equipment expenditures are required.
Clients on the production network
Production network servers
192.168.100.0/24
Management network servers
192.168.100.0/24
Clients on the management network

## Slide 9: Using VRF Technology
VRF, also called VPN instance, is a virtualization technology. Multiple VPN instances are created on a physical device. Each VPN instance has its own interfaces, a routing table, and routing protocol processes.
VPN instance: VPNA
VPN instance: VPNB
VLANIF100
VLANIF101
VLANIF201
VLANIF200
Destination/ Mask | Protocol | Interface | NextHop
192.168.100.0/24 | OSPF | VLANIF100 | 192.168.100.1
192.168.1.0/24 | OSPF | VLANIF101 | 192.168.101.1
PC1 192.168.1.1
Gateway 192.168.1.254
PC2 172.16.1.1
Gateway 172.16.1.254
Destination/ Mask | Protocol | Interface | NextHop
192.168.100.0/24 | OSPF | VLANIF200 | 192.168.100.1
172.16.1.0/24 | Static | VLANIF201 | 192.168.201.1
VPNA's routing table
VPNB's routing table
Production network
clients
Production network servers
192.168.100.0/24
Management network servers
192.168.100.0/24
Management network
clients

## Slide 10: VRF Implementation
A VRF is a logical unit on a physical device. Each logical unit is called a VPN instance, and instances are isolated on the routing plane. VRF implementation is as follows:
  Create an instance and bind each involved Layer 3 interface (physical interface, sub-interface, or VLANIF interface) to the instance.
  (Optional) Configure a routing protocol or static route and bind it to the VPN instance.
  A VPN instance routing table is created using information about the interfaces and routing protocols bound to the instance. Then data is forwarded using entries contained in the instance routing table, and instance isolation is implemented.
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/3
1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/3
2
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/3
Deploy OSPF.
Deploy IS-IS.
3
VPN instance: VPNA
VPN instance: VPNB
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/3
VPNA's routing table
VPNB's routing table
...
How many routing tables are there on this router?
Notes: By default, all interfaces on a network device belong to the same forwarding instance, that is, the root instance of the device.

## Slide 11: Example: Before VRF Deployment
Destination/Mask | Protocol | Interface | NextHop
192.168.1.0/24 | Direct | VLANIF10 | 192.168.1.254
172.16.1.0/24 | Direct | VLANIF200 | 172.16.1.254
192.168.100.0/24 | Direct | VLANIF11 | 192.168.100.1
172.16.100.0/24 | Direct | VLANIF201 | 172.16.100.1
1.1.1.0/24 | Static | VLANIF11 | 192.168.100.2
2.2.2.0/24 | Static | VLANIF201 | 172.16.100.2
GE0/0/0
192.168.100.2
VLANIF10
192.168.1.254
VLANIF11
192.168.100.1
PC1 192.168.1.1
Gateway 192.168.1.254
GE0/0/0
172.16.100.2
2.2.2.0/24
VLANIF201
172.16.100.1
VLANIF200
172.16.1.254
PC2 172.16.1.1
Gateway 172.16.1.254
Core switch's routing table
Background: PC1, R1, and network segment 1.1.1.0/24 connected R1 belongs to a service network.
PC2, R2, and network segment 2.2.2.0/24 connected to R2 belong to the management network. All direct routes on the core switch and routes destined for remote networks and discovered by the core switch are stored in the core switch's routing table (also called the global routing table). With such a routing table, the core switch enables the service and management networks to communicate.
Requirements: Configure the core switches to isolate the service and management networks.
1.1.1.0/24
Core switch
R1
R2

## Slide 12: Example: Creating VPN Instances
Core switch
GE0/0/0
192.168.100.2
VLANIF10
192.168.1.254
VLANIF11
192.168.100.1
PC1 192.168.1.1
Gateway 192.168.1.254
GE0/0/0
172.16.100.2
2.2.2.0/24
VLANIF201
172.16.100.1
VLANIF200
172.16.1.254
PC2 172.16.1.1
Gateway 172.16.1.254
1.1.1.0/24
Destination/Mask | Protocol | Interface | NextHop
192.168.1.0/24 | Direct | VLANIF10 | 192.168.1.254
192.168.100.0/24 | Direct | VLANIF11 | 192.168.100.1
1.1.1.0/24 | Static | VLANIF11 | 192.168.100.2
Core switch's global routing table
(Root device's routing table)
VPN instance 1
Destination/Mask | Protocol | Interface | NextHop
172.16.1.0/24 | Direct | VLANIF200 | 172.16.1.254
172.16.100.0/24 | Direct | VLANIF201 | 172.16.100.1
VPN instance 1's routing table on the core switch
R1
R2

## Slide 13: Example: Configuring a Dynamic Routing Protocol
Core switch
GE0/0/0
192.168.100.2
VLANIF10
192.168.1.254
VLANIF11
192.168.100.1
PC1 192.168.1.1
Gateway 192.168.1.254
GE0/0/0
172.16.100.2
2.2.2.0/24
VLANIF201
172.16.100.1
VLANIF200
172.16.1.254
PC2 172.16.1.1
Gateway 172.16.1.254
1.1.1.0/24
Destination/Mask | Protocol | Interface | NextHop
192.168.1.0/24 | Direct | VLANIF10 | 192.168.1.254
192.168.100.0/24 | Direct | VLANIF11 | 192.168.100.1
1.1.1.0/24 | Static | VLANIF11 | 192.168.100.2
Core switch's global routing table
(Root device's routing table)
Destination/Mask | Protocol | Interface | NextHop
172.16.1.0/24 | Direct | VLANIF200 | 172.16.1.254
172.16.100.0/24 | Direct | VLANIF201 | 172.16.100.1
2.2.2.0/24 | OSPF | VLANIF201 | 172.16.100.2
VPN instance 1's routing table on the core switch
VPN instance 1
Either multiple dynamic routing protocols or multiple processes of a specific dynamic routing protocol can run on a device. A dynamic routing protocol process associated with a VPN instance serves the instance, and the device installs the routes learned from the process to the routing table of the VPN instance.
Deploy OSPF.
R1
R2

## Slide 14: Common Usage Scenarios
Firewall Virtual System
BGP/MPLS IP VPN
Virtual system A
Virtual system B
Virtual system C
Root system
...
Virtual systems (VSs) are logical devices divided from a physical device and are working separately. A virtual system has the following characteristics:
Resource virtualization: Each VM has exclusive resources, including interfaces, VLANs, policies, and sessions.
Route virtualization: Each VM has its own routing table and is isolated from the other VMs.
Route virtualization is implemented by creating VPN instances.
P
PE
PE
CE
CE
CE
CE
P
PE
VPN1
site
MPLS VPN network
VPN1
site
VPN2
site
VPN2
site
BGP/MPLS IP VPN is a PE-based L3VPN technology. It runs BGP to advertise VPN routes and MPLS to forward VPN packets over the backbone network of a service provider (SP).
VPN instances are created on PEs to distinguish routes of different VPNs.
Notes: For more information about BGP/MPLS IP VPN, see the related HCIP-Datacom-Advance courses.

## Slide 15
Basic Concepts of VRF
Typical VRF Configuration Examples

## Slide 16: Basic VRF Configuration Commands (1)
[Huawei] ip vpn-instance vpn-instance-name
Create a VPN instance and enter the VPN instance view.
The ip vpn-instance command creates a VPN instance and displays the VPN instance view. By default, no VPN instance is configured.
[Huawei-vpn-instance-InstanceName] ipv4-family
Enable IPv4 route advertisement and data forwarding for the VPN instance.
The ipv4-family command creates an IPv4 address family for a VPN instance and displays the VPN instance IPv4 address family view. By default, no IPv4 address family is created for a VPN instance. An interface cannot be bound to a VPN instance that has no address family created.
[Huawei-GigabitEthernet0/0/0]ip binding vpn-instance vpn-instance-name
Bind an interface to the VPN instance.
The ip binding vpn-instance command binds an interface on a PE to a VPN instance. By default, an interface is not bound to any VPN instance and belongs to the root instance. After an interface is bound to a VPN instance or unbound from a VPN instance, the IP address, Layer 3 features, and IP-related routing protocols on the interface are deleted. You have to reconfigure them if needed.

## Slide 17: Basic VRF Configuration Commands (2)
[Huawei] ip route-static vpn-instance vpn-instance-name ip-address { mask | mask-length } { nexthop-address | interface-type interface-number }
Add a static route to the routing table of the VPN instance.
[Huawei] ospf [ process-id | router-id router-id ] vpn-instance vpn-instance-name
Create a dynamic routing protocol process (for example, OSPF) bound to the VPN instance.
Note: The process IDs of different VPN instances must be different.
[Huawei] display ip routing-table vpn-instance vpn-instance-name
Use the following commands to maintain VPN instances.
[Huawei] ping -vpn-instance vpn-instance-name host
[Huawei] tracert -vpn-instance vpn-instance-name host
Note: If the ping command does not carry the vpn-instance keyword, the ping is performed on the root device by default, and the generated ICMP messages are forwarded using entries in the global routing table, which also applies to the tracert operation.

## Slide 18: Configuration Case — Background and Requirement Analysis
Production network
192.168.100.0/24
Management network
192.168.200.0/24
PC1 192.168.1.1
Gateway 192.168.1.254
VLAN 10
PC2 192.168.2.1
Gateway 192.168.2.254
VLAN 20
GE0/0/0
GE0/0/0
GE0/0/1
IP: 192.168.101.1/24
GE0/0/2
IP: 192.168.102.1/24
R1
S1
Background: An enterprise has a production network and a management network, shown on the left figure.
  PC1 belongs to the production network, PC2 belongs to the management network, and S1 is the access switch for the two PCs. PC1 is added to VLAN 10, and PC2 is added to VLAN 20.
  Sub-interfaces are configured on R1 functioning as a gateway for PC1 and PC2.
Requirements: Isolate the production network from the management network and use static routes for communication within each network.
Destination/Mask | Protocol | Interface | NextHop
192.168.100.0/24 | Static | GE0/0/1 | 192.168.101.254
192.168.200.0/24 | Static | GE0/0/2 | 192.168.102.254
192.168.1.0/24 | Direct | GE0/0/0.1 | 192.168.1.254
192.168.2.0/24 | Direct | GE0/0/0.1 | 192.168.2.254
Routing table before VRF is deployed on R1

## Slide 19: Configuration Example — Procedure (1)
1. Configure VLANs on the switch. The configuration details are not provided.
[R1]ip vpn-instance production
[R1-vpn-instance-production]ipv4-family
[R1-vpn-instance-production-af-ipv4]quit
[R1-vpn-instance-production]quit
[R1]ip vpn-instance management
[R1-vpn-instance-management]ipv4-family
[R1-vpn-instance-management-af-ipv4]quit
[R1-vpn-instance-management]quit
2. Create VPN instances for the production and management networks and configure the IPv4 address family for each VPN instance.
Production network
192.168.100.0/24
Management network
192.168.200.0/24
PC1 192.168.1.1
Gateway 192.168.1.254
VLAN 10
PC2 192.168.2.1
Gateway 192.168.2.254
VLAN 20
GE0/0/0
GE0/0/0
GE0/0/1
IP: 192.168.101.1/24
GE0/0/2
IP: 192.168.102.1/24
R1
S1

## Slide 20: Configuration Example — Procedure (2)
3. Bind involved interfaces to the VPN instances.
[Huawei]interface GigabitEthernet 0/0/0.1
[Huawei-GigabitEthernet0/0/0.1]ip binding vpn-instance production
Info: All IPv4 related configurations on this interface are removed!
//After an interface is bound to an instance, the IP address of the interface is deleted and has to be reconfigured.
[Huawei-GigabitEthernet0/0/0.1]ip address 192.168.1.254 24
[Huawei-GigabitEthernet0/0/0.1]quit
[Huawei]interface GigabitEthernet 0/0/0.2
[Huawei-GigabitEthernet0/0/0.2]ip binding vpn-instance management
Info: All IPv4 related configurations on this interface are removed!
[Huawei-GigabitEthernet0/0/0.2]ip address 192.168.2.254 24
[Huawei-GigabitEthernet0/0/0.2]quit
Production network
192.168.100.0/24
Management network
192.168.200.0/24
PC1 192.168.1.1
Gateway 192.168.1.254
VLAN 10
PC2 192.168.2.1
Gateway 192.168.2.254
VLAN 20
GE0/0/0
GE0/0/0
GE0/0/1
IP: 192.168.101.1/24
GE0/0/2
IP: 192.168.102.1/24
R1
S1

## Slide 21: Configuration Example — Procedure (3)
4. Configure static routes and bind them to the instance.
[R1]ip route-static vpn-instance production 192.168.100.0 24 192.168.101.254
[R1]ip route-static vpn-instance management 192.168.200.0 24 192.168.102.254
Production network
192.168.100.0/24
Management network
192.168.200.0/24
PC1 192.168.1.1
Gateway 192.168.1.254
VLAN 10
PC2 192.168.2.1
Gateway 192.168.2.254
VLAN 20
GE0/0/0
GE0/0/0
GE0/0/1
IP: 192.168.101.1/24
GE0/0/2
IP: 192.168.102.1/24
R1
S1
5. Verify the configuration.
[R1] display ip routing-table vpn-instance production
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing Tables: production
Destinations : 5 Routes : 5
Destination/Mask Proto Pre Cost Flags NextHop Interface
192.168.100.0/24 Static 60 0 RD 192.168.101.254 GigabitEthernet0/0/1

## Slide 22
(Single) At which of the following layers can VRF technology be used to implement isolation?
  Physical layer
  Network layer
  Data link layer
  Application layer
(TorF) By default, all Layer 3 interfaces on Huawei data communication products belong to the root instance.
  True
  False
Notes: B
A

## Slide 23
VRF technology implements logical isolation between different networks on the same physical device. When multiple VRF instances are deployed on the physical device, each VRF instance is equivalent to a virtual network device. The interfaces and routes between VRF instances are isolated. When a physical device is connected to the same network segment that belongs to different VPN instances, you have no worries about IP address conflicts.
The VRF technology is widely used in firewall virtual systems and BGP/MPLS IP VPN scenarios.