## Slide 1
Chen Jianyuan/cwx652820
2020-03-18

## Slide 2: BFD Implementation and Configuration

## Slide 3
As network applications are widely deployed, network faults may cause service anomalies. To minimize the impact of device faults on services and improve network reliability, a network device must be able to quickly detect faults in communication with adjacent devices. Measures can then be taken to promptly rectify the faults to ensure service continuity.
Bidirectional Forwarding Detection (BFD) is a fast fault detection mechanism that rapidly detects link faults and monitors IP connectivity on the entire network independent of media and routing protocols.
This document describes the implementation and typical application scenarios of BFD.

## Slide 4
Upon completion of this course, you will be able to:
  Describe functions of BFD.
  Describe BFD implementation.
  Configure and apply BFD.

## Slide 5
Introduction to BFD
BFD Implementation
BFD Application Scenarios
Basic BFD Configurations

## Slide 6: You May Encounter in Problems in Network Fault Detection
On R1, a default route to the gateway R2 is configured. Can R1 quickly detect the fault on the link between SW1 and R2?
R1 and R2 establish an OSPF neighbor relationship through a Layer 2 switch. Can R1 and R2 quickly detect a fault on the link between SW1 and SW2?
In a system where hardware signals cannot be used to detect faults, applications usually use the Hello mechanism of an upper-layer routing protocol to detect network faults.
The detection duration is more than 1 second, which is too long for some applications. When data transmitted on the network exceeds 1 Gbit/s, the second-level detection will cause a large amount of data to be lost.
On a Layer 3 network, static routes do not have a fault detection mechanism.
R1
R2
SW1
SW2
OSPF neighbor
[R1]ip route-static 0.0.0.0 0.0.0.0 10.0.12.2
R1
SW1
R2
10.0.12.1/30
10.0.12.2/30
Internet
Dynamic Route Fault Detection
Static Route Fault Detection

## Slide 7: BFD Overview
BFD provides a universal, standard, media-independent, and protocol-independent fast fault detection mechanism. It has the following advantages:
  Uses a low-overhead, short-duration method to detect faults in a path between adjacent forwarding engines.
  Provides uniform detection for all media and protocol layers in real time.
BFD is a simple Hello protocol. A BFD session channel is established between two systems and BFD packets are periodically sent over the channel. If a system does not receive BFD packets from the remote end within a specified period, the system considers that a fault occurs on the channel.
Application layer
Transport layer
Network layer
Data link layer
Physical layer
Application layer
Transport layer
Network layer
Data link layer
Physical layer
BFD session detection
Notes: Only one BFD session can be established on a data path. If different applications need to use different BFD protocol parameters on the same data path, you can configure a unique BFD session by using the parameters that match needs of all applications. The BFD session status change is reported to all bound applications.

## Slide 8
Introduction to BFD
BFD Implementation
BFD Application Scenarios
Basic BFD Configurations

## Slide 9: BFD Packet Format
BFD is implemented by maintaining the BFD session between two systems. The system establishes a session by sending BFD packets to each other.
BFD control packets are encapsulated differently based on scenarios. A BFD control packet consists of mandatory fields and optional authentication fields.
Ver | Diag | Sta | P | F | C | A | D | M | Detect Mult | Length
My discriminator |  |  |  |  |  |  |  |  |  | 
Your discriminator |  |  |  |  |  |  |  |  |  | 
Desired Min TX Interval |  |  |  |  |  |  |  |  |  | 
Required Min RX Interval |  |  |  |  |  |  |  |  |  | 
Required Min Echo RX Interval |  |  |  |  |  |  |  |  |  | 
Mandatory fields
Optional authentication fields
Auth-Type | Auth-Len | Authentication Data
Notes: Sta: indicates the status of the local BFD system.
Detect Mult: indicates the detection multiplier flag. It is used by the detector to calculate the detection timeout interval.
My Discriminator: indicates the local discriminator of the BFD session. It is a unique non-zero value generated by the transmitting system. Local discriminators are used to distinguish multiple BFD sessions in a system.
Your Discriminator: indicates the remote discriminator of the BFD session. If this value is received from the remote system, the value of the received My Discriminator field is used. If this value is unknown, the system returns value 0.
Desired Min Tx Interval: indicates the minimum interval for sending BFD packets on the local end.
Required Min RX Interval: indicates the minimum interval for receiving BFD packets on the local end.
Required Min Echo RX Interval: indicates the minimum interval for receiving Echo packets on the local end. If the local end does not support the Echo function, the field is set to 0.

## Slide 10: BFD Packet Format
BFD is implemented by maintaining the BFD session between two systems. The system establishes a session by sending BFD packets to each other.
BFD control packets are encapsulated differently based on scenarios. A BFD control packet consists of mandatory fields and optional authentication fields.
Ver | Diag | Sta | P | F | C | A | D | M | Detect Mult | Length
My discriminator |  |  |  |  |  |  |  |  |  | 
Your discriminator |  |  |  |  |  |  |  |  |  | 
Desired Min TX Interval |  |  |  |  |  |  |  |  |  | 
Required Min RX Interval |  |  |  |  |  |  |  |  |  | 
Required Min Echo RX Interval |  |  |  |  |  |  |  |  |  | 
Sta: indicates the status of the local BFD system.
Detect Mult: indicates the detection multiplier flag. It is used by the detector to calculate the detection timeout interval.
My Discriminator: indicates the local discriminator of the BFD session. It is a unique non-zero value generated by the transmitting system. Local discriminators are used to distinguish multiple BFD sessions in a system.
Your Discriminator: indicates the remote discriminator of the BFD session. If this value is received from the remote system, the value of the received My Discriminator field is used. If this value is unknown, the system returns value 0.
Desired Min Tx Interval: indicates the minimum interval for sending BFD packets on the local end.
Required Min RX Interval: indicates the minimum interval for receiving BFD packets on the local end.
Required Min Echo RX Interval: indicates the minimum interval for receiving Echo packets on the local end. If the local end does not support the Echo function, the field is set to 0.
Mandatory fields
Optional authentication fields
Auth-Type | Auth-Len | Authentication Data
Notes: Ver: indicates the BFD version number. The current version number is 1.
Diag: indicates the cause of the session status change on the local BFD system.
P: indicates the flag that the sender of a BFD packet must set in the BFD packet when parameters are changed. The receiver must respond to the BFD packet immediately.
F: indicates the flag of the packet used to respond to the packet with the P flag.
C: indicates the forwarding/control separation flag. Once this flag is set, the change of the control plane does not affect BFD detection.
C: indicates whether authentication is performed. Value 1 indicates authentication is enabled.
D: indicates whether the demand mode is used. If the flag is set, the sender wants to monitor links in demand mode.
M: This bit is reserved for BFD to support P2MP extensions in the future.
Length: indicates the packet length, in bytes.

## Slide 11: BFD Session Setup
BFD sessions can be established in either static or dynamic mode. BFD distinguishes sessions according to local and remote discriminators of control packets. Static and dynamic BFD sessions differ in that local and remote discriminators are configured in different modes.
R1
R2
Local discriminator
(Local Discriminator=A)
Remote discriminator
(Remote Discriminator=B)
Local discriminator
(Local Discriminator=B)
Remote discriminator
(Remote Discriminator=A)
BFD session
Static Establishment
BFD session parameters, including the local and remote discriminators, are manually specified. A request for BFD session establishment is distributed manually.
Dynamic Establishment
The local discriminator for dynamically establishing a BFD session is dynamically allocated by the system that triggers the establishment of the BFD session. The remote discriminator is learned from the value of Local Discriminator in the BFD packet received from the remote end.
R1
R2
Local Discriminator=A
Remote Discriminator=0
Local Discriminator=B
Remote Discriminator=0
Local Discriminator=A
Remote Discriminator=B
Local Discriminator=B
Remote Discriminator=A
BFD session
Send information to each other
Learn discriminators
1
2
Notes: When a BFD session is set up dynamically, the system processes the local and remote discriminators as follows:
  Dynamic allocation of the local discriminator: When an application triggers setup of a dynamic BFD session, the system allocates a dynamic local discriminator within a specified range to the BFD session. Then the local system sends a BFD control packet with the remote discriminator of 0 to the remote system for BFD session negotiation.
  Automatically learning the remote discriminator: When one end of a BFD session receives a BFD control packet with the remote discriminator of 0, this end checks whether the packet matches parameters the BFD session. If the packet matches parameters of the BFD session, this end learns the value of Local Discriminator in the received control BFD packet and obtains the remote discriminator.

## Slide 12: States of BFD Sessions
A BFD session has the following states: Down, Init, Up, and AdminDown. The State field of a BFD control packet shows the session status. The system changes the BFD session status based on the local session status and the received BFD session status of the remote end. The BFD state machine implements a three-way handshake for BFD session setup or deletion to ensure that the two systems detect the status change.
Down
Init
Up
Sta:Down
Sta:Init/up
Timer
Timer
Sta:Init
Sta:Down
Sta:Init/up
Sta:Up
Timer: specifies the timeout interval of BFD control packets.
down
down
R1
R2
Down -> Init
Down -> Init
Init
Init
Init -> Up
Init -> Up
Up
Up
BFD session
Sta:Down
Sta:Down
Sta:Init
Sta:Init
Sta:Up
Sta:Up
State transition during BFD session establishment
State transition of a BFD session
Notes: A BFD session often involves three states. The BFD sessions are established in Init and Up states, and the Down state indicates that the BFD session is terminated. A three-way handshake is required for establishing and disconnecting a BFD session to ensure that both systems can detect the setup or disconnection. The AdminDown state is special and means that the shutdown command is configured in the BFD session view. Each system sends the local status through the State field in outgoing BFD control packets, and learns the remote end status through the State field in the received BFD control packets.
The Down state indicates that the BFD session is Down. A BFD session remains in Down state until the local end receives a packet from the remote end, where the State field indicates that the remote end is not in Up state. If a BFD control packet with the State field set to Down is received, the state machine transits from the Down state to the Init state. If a BFD control packet with the State field set to Init is received, the state machine transits from the Down state to the Up state. If a BFD control packet with the State field set to Up is received, the state machine maintains the Down state.
The Init state indicates that the local end is communicating with the remote end and the local session is expected to go Up, but the remote end does not respond. A BFD session in Init state transitions to the Up state until it receives a BFD control packet with the State field set to Init or Up from the remote end. Otherwise, the BFD session enters the Down state after the detection timer expires, indicating that the communication with the remote end is terminated.
The Up state indicates that the BFD session is successfully established and the link connectivity is being checked. The BFD session remains Up until the link is faulty or the shutdown command is configured in the BFD session view. If the local end receives a BFD control packet with the State field set to Down from the remote end or the detection timer expires, the BFD session changes from Up to Down.
The AdminDown state indicates that the remote system enters the Down state and remains in Down state until the local system exits the AdminDown state. The AdminDown state does not mean that the forwarding path is unreachable.

## Slide 13: BFD Detection Modes
Two systems establish a BFD session and periodically send BFD control packets along the path between them. If one system does not receive BFD control packets within a specified period, the system considers the path faulty. BFD detection modes include asynchronous and demand modes.
Asynchronous Mode
In asynchronous mode, two systems periodically send BFD control packets to each other. If a system does not receive any BFD control packet from the remote end within the detection period, the system advertises that the BFD session is Down.
Demand Mode
In a scenario where connectivity needs to be verified, the system sends multiple BFD control packets consecutively. If it does not receive any return packets within a specific period of time, it considers the BFD session Down.
R1
R2
BFD session
...
R1
R2
BFD session
BFD control packet
BFD control packet
BFD control packet
BFD control packet
BFD control packet
BFD control packet
Send BFD control packets periodically
Send
BFD control packets on demand
Notes: The asynchronous mode differs from the demand mode in the detection location. In asynchronous mode, the local end sends BFD control packets at a given period of time. The detection location is the remote end. The remote end detects whether the local end periodically sends BFD control packets. In demand mode, the local end checks whether there is a response packet for the BFD control packet sent by itself.

## Slide 14: BFD Detection Time
The detection time of a BFD session is determined by the local detection multiplier (Detect Multi), minimum interval for receiving BFD packets (Required Min RX Interval), and minimum interval for sending BFD packets (Desired Min TX Interval). The actual interval at which BFD packets are received or sent depend on BFD session negotiation.
Detection time = Received Detect Multi of the remote system x Max (Local RMRI/Received DMTI)
  Detect Multi: local detection multiplier
  Required Min Rx Interval (RMRI): minimum interval for receiving BFD packets
  Desired Min Tx Interval (DMTI): minimum interval for sending BFD packets
R1
R2
BFD Session
Configured time parameters:
TX: 100ms
RX: 200ms
DM: 3
Configured time parameters:
TX: 150 ms
RX: 50 ms
DM: 4
Negotiated time parameters:
TX: 100 ms
RX: 200 ms
DM: 3
Negotiated time parameters:
TX: 200 ms
RX: 100 ms
DM: 4
Parameter negotiation
Actual detection time of R1 in asynchronous mode = 4 x 200 ms
Actual detection time of R1 in demand mode = 3 x 200 ms
Notes: Default BFD time parameters
  By default, the interval for sending BFD packets is 1000 ms, the interval for receiving BFD packets is 1000 ms, and the local detection multiplier is 3.
  The WTR time of a BFD session is 0, and the delay for the BFD session to go Up is 0.
The detection timeout multiplier, used by the detecting party to calculate the detection timeout interval:
  Demand mode: The local detection multiplier takes effect.
  Asynchronous mode: The remote detection multiplier takes effect.

## Slide 15: BFD Echo
BFD Echo is a detection mechanism in which the local system sends BFD echo packets and the remote system loops back the packets.
One of the two directly connected devices supports BFD (R1), and the other device does not support BFD (R2) and supports only basic forwarding at the network layer. To quickly detect faults between the two devices, you can create a one-arm BFD Echo session on the BFD-capable device. The BFD-capable device initiates an Echo request. After receiving the Echo request, the BFD-incapable device loops back the Echo request to implement connectivity detection on forwarding links.
R1
R2
BFD-capable device
BFD-incapable device
Initiate an Echo request
1
Loop back the request at the network layer
2
Determine whether the link is normal
3

## Slide 16
Introduction to BFD
BFD Implementation
BFD Application Scenarios
Basic BFD Configurations

## Slide 17: BFD Association
Association functions involve the detection module, track module, and application module.
Monitoring module
BFD detection
module
Track module
Application module
VRRP
Static route
Policy-based routing (PBR)
Interface backup
Notes: The monitoring module monitors the link status and network performance, and notifies the track module of the detection result.
After receiving the detection result from the monitoring module, the track module changes the status of the track item immediately and notifies the application module.
The application module performs corresponding processing according to the status of the track item.

## Slide 18: Association Between the Static Route and BFD
A static route does not have a detection mechanism. When a static route is associated with BFD, the BFD session is used to detect the status of the link where the static route resides.
Association between static routes and BFD is widely used. As shown in the figure, R1 connects to ISP 1 and ISP 2 through two links. In normal cases, the default route points to the link connected to ISP 1. When the link connected to ISP 1 fails, the BFD session can rapidly detect the fault and instructs R1 to switch traffic to the link connected to ISP 2.
R1
R2
R3
ISP 1
ISP 2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
Campus network
10.0.12.0/30
10.0.13.0/30
BFD session

## Slide 19: BFD for OSPF (1)
If OSPF is not bound to BFD, the link fault detection time is determined by the Hello mechanism and is usually in seconds. BFD can be bound to implement millisecond-level fault detection.
BFD for OSPF associates BFD with OSPF. BFD notifies OSPF of the fast detection result of a link fault.
OSPF uses the Hello mechanism to discover neighbors and establishes a neighbor relationship.
OSPF notifies BFD of neighbor information including source and destination addresses.
BFD establishes a session based on the received neighbor information. After the session is established, BFD starts to detect link faults.
In normal situations, R1 selects the path R2 -> R4 based on the OSPF path cost.
R1
R2
R3
R4
GE0/0/1
GE0/0/2
Cost 1
Cost 10
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
Cost 1
Cost 10
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session

## Slide 20: BFD for OSPF (2)
After the BFD session is set up, devices periodically send BFD packets. If a device does not receive a response within a specified detection period, the device considers the forwarding path faulty. BFD will then notify the upper-layer application for processing.
When the link between R1 and R2 fails, BFD quickly detects the fault. The BFD session goes Down and BFD notifies R1.
R1 processes the neighbor Down event and notifies the local OSPF process that the neighbor is unreachable. Then R1 recalculates the route and sends the route to R4 through R3.
R1
R2
R3
R4
GE0/0/1
GE0/0/2
Cost 1
Cost 10
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
Cost 1
Cost 10
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session
OSPF Neighbor
BFD session

## Slide 21
Introduction to BFD
BFD Implementation
BFD Application Scenarios
Basic BFD Configurations

## Slide 22: BFD Configuration Commands (1)
[Huawei] bfd session-name bind peer-ip ip-address [ vpn-instance vpn-name ] interface interface-type interface-number [ source-ip ip-address ]
Create a BFD session and enter the BFD session view.
By default, no BFD session is created. When creating a single-hop BFD session for the first time, you must bind the single-hop BFD session to the peer IP address and local interface. In addition, the configuration of the single-hop BFD session cannot be changed after being created. To change a configured BFD session, delete it and recreate a BFD session.
[Huawei] bfd session-name bind peer-ip default-ip interface interface-type interface-number [ source-ip ip-address ]
Create a BFD session using the multicast address as the peer address, and enter the BFD session view.
[Huawei] bfd session-name bind peer-ipv6 ip-address [ vpn-instance vpn-name ] interface interface-type interface-number [ source-ipv6 ip-address ]
Create a BFD6 session and enter the BFD6 session view.
When creating a single-hop BFD6 session for the first time, bind the single-hop BFD6 session to the peer IPv6 address and local interface. In addition, the configuration of the single-hop BFD6 session cannot be changed after being created.

## Slide 23: BFD Configuration Commands (2)
[Huawei] bfd session-name bind peer-ip ip-address [ vpn-instance vpn-name ] interface interface-type interface-number [ source-ip ip-address ] auto
Create a static BFD session with automatically negotiated discriminators.
[Huawei-bfd-session-test] discriminator local discr-value
Configure a local discriminator for the BFD session.
[Huawei-bfd-session-test] discriminator remote discr-value
Configure a remote discriminator for the BFD session.
The local discriminator of the local system must be the same as the remote discriminator of the remote system; otherwise, BFD sessions cannot be established. In addition, the local and remote discriminators cannot be modified after being configured.
Assume that the BFD session name is test.
[Huawei] bfd session-name bind peer-ip ip-address [ vpn-instance vpn-name ] interface interface-type interface-number [ source-ip ip-address ] one-arm-echo
Create a one-arm BFD echo session.
Notes: Use the commit command to commit the configuration so that the configuration takes effect.

## Slide 24: Configuring Association Between the Static Route and BFD
Configuration requirements:
  As shown in the figure, a floating static route to the network segment 4.4.4.4/32 of Loopback0 on R4 is configured on R1. In normal cases, R1 accesses R4 through R2. When R2 fails, R1 automatically selects the route to access Loopback0 on R4 through R3.
  A BFD session needs to be established between R1 and R2 and is bound to the static route to implement fast fault detection and fast convergence.
[R1]bfd
[R1]bfd 12 bind peer 10.0.12.2 interface GigabitEthernet 0/0/1
[R1-bfd-session-12]discriminator local 10
[R1-bfd-session-12]discriminator remote 20
[R1-bfd-session-12]commit
[R2]bfd
[R2]bfd 21 bind peer 10.0.12.1 interface GigabitEthernet 0/0/1
[R2-bfd-session-21]discriminator local 20
[R2-bfd-session-21]discriminator remote 10
[R2-bfd-session-21]commit
Establish a static BFD session between R1 and R2.
[R1] ip route-static 4.4.4.4 32 10.0.12.2 track bfd-session 12
[R1] ip route-static 4.4.4.4 32 10.0.13.2 preference 100
On R1, configure a static route and bind the static route to a BFD session.
10.0.12.0/30
10.0.13.0/30
10.0.24.0/30
10.0.34.0/30
Loopback0
4.4.4.4/32
R1
R2
R3
R4
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/1
Other configurations are not provided here.

## Slide 25: Verifying the BFD Session Configuration
[R1]display bfd session all verbose
Session MIndex : 256 (One Hop) State : Up Name : 12
Local Discriminator : 1 Remote Discriminator : 2
Session Detect Mode : Asynchronous Mode Without Echo Function
BFD Bind Type : Interface(Vlanif10)
Bind Session Type : Static
Bind Peer IP Address : 10.0.12.2
NextHop Ip Address : 10.0.12.2
Bind Interface : GigabitEthernet0/0/1
FSM Board Id : 0 TOS-EXP : 7
Min Tx Interval (ms) : 1000 Min Rx Interval (ms) : 1000
Actual Tx Interval (ms): 1000 Actual Rx Interval (ms): 1000
Local Detect Multi : 3 Detect Interval (ms) : 3000
Echo Passive : Disable Acl Number : -
Destination Port : 3784 TTL : 255
----more----
BFD session in Up state
Static BFD session
Minimum intervals for receiving and sending BFD control packets
Actual minimum intervals for receiving and sending BFD control packets after system negotiation
System detection count and fault detection interval

## Slide 26: Configuring BFD for OSPF
Configuration requirements:
  R1, R2, and R3 run OSPF and belong to area 0.
  Configure BFD for OSPF and set BFD session parameters for all OSPF interfaces to further speed up OSPF convergence when the link status changes.
  Set the maximum intervals for receiving and sending BFD control packets to 100 ms, and retain the default detection count.
[R1]bfd
[R1]interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1]ip address 10.0.12.1 30
[R1]ospf 1
[R1-ospf-1]area 0
[R1-ospf-1-area-0.0.0.0]network 10.0.12.0 0.0.0.3
[R1-ospf-1-area-0.0.0.0]quit
[R1-ospf-1]bfd all-interfaces enable
[R1-ospf-1]bfd all-interfaces min-tx-interval 100 min-rx-interval 100 detect-multiplier 3
R1 configuration:
10.0.12.0/30
10.0.23.0/30
GE0/0/1
GE0/0/1
GE0/0/2
GE0/0/2
R1
R2
R3
OSPF Area 0
The configurations of R2 and R3 are similar to the configuration of R1, and are not provided.

## Slide 27: Verifying the BFD Configuration
[R1]display ospf 1 bfd session all
OSPF Process 1 with Router ID 10.0.12.1
Area 0.0.0.0 interface 10.0.12.1(GigabitEthernet0/0/0)'s BFD Sessions
NeighborId:10.0.12.2
AreaId:0.0.0.0
Interface:GigabitEthernet0/0/0
BFDState:up rx :100 tx :100
Multiplier:3
BFD Local Dis:8192
LocalIpAdd: 10.0.12.1
RemoteIpAdd:10.0.12.2
Diagnostic Info:No diagnostic information
[R1]display bfd session all verbose
Session Mince : 256 (One Hop) State : Up Name : dyn_8192
Local Discriminator : 8192 Remote Discriminator : 8192
Session Detect Mode : Asynchronous Mode Without Echo Function
BFD Bind Type : Interface(GigabitEthernet0/0/0)
Bind Session Type : Dynamic
Bind Peer IP Address : 10.0.12.2
NextHop Ip Address : 10.0.12.2
Bind Interface : GigabitEthernet0/0/0
FSM Board Id : 0 TOS-EXP : 7
Min Tx Interval (ms) : 100 Min Rx Interval (ms) : 100
Actual Tx Interval (ms): 100 Actual Rx Interval (ms): 100
Local Detect Multi : 3 Detect Interval (ms) : 300
Echo Passive : Disable Acl Number : -

## Slide 28
(Multiple) Which of the following states are involved in the establishment of a BFD session?
  Down
  Init
  Up
  Establish
(Multiple) Which of the following BFD detection modes are available?
  Asynchronous mode
  Synchronous mode
  Demand mode
  Echo mode
Notes: Answer 1: ABC
Answer 2: ACD

## Slide 29
This document describes the working principles of BFD, including the session establishment process, detection mode, detection time, and detection process.
A BFD session experiences three states: Down, Init, and Up. The state of the BFD session is changed according to the State field in the received BFD packet. The BFD detection modes are classified into asynchronous and demand modes. The two modes differ in the detection packet sending mode, detection position, detection time, and detection process.
BFD can quickly detect link faults. However, only application modules, such as OSPF and static routes, can invoke BFD to implement fast traffic path switching. Therefore, BFD is widely used on the live network.