## Slide 1
Chen Jianyuan/cwx652820
2019.12.20

## Slide 2: VRRP Implementation and Configuration

## Slide 3
User terminals on a LAN usually use a default gateway to access an external network. If the default gateway fails, all user terminals' traffic to the external network will be interrupted. Multiple gateways can be deployed to prevent single points of failure. To this end, the conflict between multiple gateways must be resolved.
The Virtual Router Redundancy Protocol (VRRP) can implement gateway backup and solve the conflict between multiple gateways, thus improving network reliability.
This course describes the working mechanism, basic configuration, and typical application scenarios of VRRP on a network.

## Slide 4
Upon completion of this course, you will be able to:
  Analyze problems faced by a single gateway on a LAN.
  Explain the basic concepts and working mechanism of VRRP.
  Describe the active/standby VRRP switchover process.
  Perform basic VRRP configurations.

## Slide 5
Introduction to VRRP
VRRP Implementation
Typical Application Scenarios of VRRP
Basic VRRP Configurations

## Slide 6: Problems Faced by a Single Gateway
When the gateway (router) is faulty, the hosts that use the router as the gateway cannot communicate with the Internet.
Router
Ethernet
Switch
IP: 192.168.1.254/24
Is it feasible to configure multiple gateways to implement redundancy?
Ethernet
Switch
IP: 192.168.1.254/24
Router
HostA
IP: 192.168.1.1/24
Gateway: 192.168.1.254
HostB
IP: 192.168.1.2/24
Gateway: 192.168.1.254
HostC
IP: 192.168.1.3/24
Gateway: 192.168.1.254
HostA
IP: 192.168.1.1/24
Gateway: 192.168.1.254
HostB
IP: 192.168.1.2/24
Gateway: 192.168.1.254
HostC
IP: 192.168.1.3/24
Gateway: 192.168.1.254

## Slide 7: Overview of VRRP
VRRP groups several routers into a virtual router. If one of routers fails, traffic can be switched to another router, ensuring service continuity and reliability.
Logical network topology
Physical network topology
Virtual router
Virtual IP address: 192.168.1.254/24
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
VRRP
R1
R2
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
Switch
Switch
Notes: VRRP sets up a virtual router on a LAN.
In this example:
  There are two routers on the LAN: R1 and R2. The IP addresses of R1 and R2 are 192.168.1.251/24 and 192.168.1.252/24, respectively.
  Configure R1 and R2 to constitute a virtual router. The virtual router uses IP address 192.168.1.254.
  All PCs use IP address 192.168.1.254 as the default gateway address.

## Slide 8: Basic VRRP Concepts (1)
VRRP router: A router running VRRP, such as R1 and R2. VRRP is configured on interfaces of routers and works based on interfaces.
Virtual router ID (VRID): A VRRP group consists of multiple routers (interfaces) that work together and are identified by the same VRID. Routers in the same VRRP group exchange VRRP packets and form a virtual router. Only one master router can exist in a VRRP group.
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
VRRP
R1
R2
VRRP VRID: 1
Switch

## Slide 9: Basic VRRP Concepts (2)
Virtual router: Each VRRP group forms a virtual router that is a logical device. A VRRP group forms only one virtual router.
Virtual IP address and virtual MAC address: A virtual router has its own IP address and MAC address. The IP address is specified by the network administrator during VRRP configuration. A virtual router can have one or more IP addresses. Generally, this IP address is used as the gateway address. The format of the virtual MAC address is 0000-5e00-01xx, where xx is the VRID.
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
VRRP
R1
R2
Virtual IP address: 192.168.1.254
Virtual MAC address: 0000-5e00-0101
Switch

## Slide 10: Basic VRRP Concepts (3)
Master router: The master router forwards packets in a VRRP group. In each VRRP group, only the master router responds to the ARP Request packet destined for the virtual IP address. The master router periodically sends VRRP packets to notify the backup router in the same VRRP group of its own status.
Backup router: The backup router listens to the VRRP packets sent by the master router in real time and is ready to take over services of the master router.
Priority: The priority value is used to elect the master and backup routers. The priority value ranges from 0 to 255. A larger value indicates a higher priority. If the values are the same, the interface IP addresses are compared. The interface with the largest IP address is preferred.
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
VRRP
R1
R2
Master
Backup
Priority: 200
Priority: 100
Switch

## Slide 11: VRRP Packet Format
VRRP has only one packet type — Advertisement packets. Advertisement packets are multicast packets and can be transmitted only in the same broadcast domain. The destination multicast address of Advertisement packets is 224.0.0.18.
Ver | Type | Virtual Rtr ID | Priority | Count IP Addrs
Auth Type |  | Adver Int | Checksum | 
IP Address (1) |  |  |  | 
… |  |  |  | 
IP Address (n) |  |  |  | 
Authentication Data (1) |  |  |  | 
Authentication Data (2) |  |  |  | 
Ethernet Header
IP Header
VRRP Packet
DMAC 01-00-5E-00-00-12
(multicast MAC address)
SMAC: 00-00-5E-00-01-XX (virtual router MAC address)
DIP: 224.0.0.18
SIP: IP address of the master router's port
Protocol: 0x70
(VRRP protocol number: 112)
Notes: Fields in a VRRP Advertisement packet:
  Ver: VRRP has two versions. VRRPv2 applies only to IPv4 networks, and VRRPv3 applies to both IPv4 and IPv6 networks.
  Virtual Rtr ID: Virtual router ID associated with the packet.
  Priority: Priority of the VRRP router that sends the VRRP packet.
  Count IP Addrs: Number of virtual IP addresses contained in the VRRP packet.
  Auth Type: VRRP supports non-authentication, plain-text password authentication, and MD5 authentication, corresponding to values 0, 1, and 2, respectively.
  Adver Int: Interval for sending VRRP Advertisement packets. The default value is 1s.
  IP Address: Virtual IP address of the associated virtual router. Multiple IP addresses can be configured.
  Authentication Data: Password required for authentication.

## Slide 12: VRRP Timers
VRRP defines two timers:
  ADVER_INTERVAL timer: specifies the interval at which the master router sends VRRP Advertisement packets. The default value is 1s.
  MASTER_DOWN timer: indicates that the backup router preempts the Master state after the MASTER_DOWN timer expires. The MASTER_DOWN timer is calculated as follows:
    MASTER_DOWN = (3*ADVER_INTERVAL) + Skew_time (offset time)
    Skew_Time = (256 – Priority)/256

## Slide 13
Introduction to VRRP
VRRP Implementation
Typical Application Scenarios of VRRP
Basic VRRP Configurations

## Slide 14: VRRP State Machine
The VRRP state machine has three states: Initialize, Master, and Backup.
Initialize
Master
Backup
Receive the startup event with the priority of 255
Receive the startup event with the priority lower than 255
Receive the shutdown message
Receive the shutdown message
The MASTER_DOWN timer expires, or a VRRP Advertisement packet with the priority of 0 or a VRRP Advertisement packet with a priority lower than the local priority is received.
Receive a packet with a priority higher than the local priority
Notes: A startup event can be automatically triggered by the system after VRRP is configured or triggered by the change of the lower-layer link from unavailable to available on the interface configured with VRRP.

## Slide 15: VRRP States
Device in Master State
  Sends a VRRP Advertisement packet each time the ADVER_INTERVAL timer expires.
  Uses the virtual MAC address to respond to ARP Request packets destined for the virtual IP address.
  Forwards IP packets sent to the virtual MAC address.
  Allows a virtual IP address to be pinged by default.
  When multiple devices are in Master state, they compare their IP addresses in received packets with the same priority. If the IP address in the packet is greater than the local IP address, the device switches to the Backup state. If the IP address in the packet is less than or equal to the local IP address, the device remains in the Master state.
Device in Backup State
  Receives VRRP Advertisement packets from the master router and checks whether the master router is working properly based on information in the packets.
  Does not respond to an ARP Request packet carrying a virtual IP address.
  Discards IP packets sent to the virtual MAC address.
  Discards IP packets sent to the virtual IP address.
  Resets the MASTER_DOWN timer but does not compare IP addresses if it receives a VRRP Advertisement packet carrying a VRRP priority higher than or equal to the local VRRP priority.

## Slide 16: VRRP Master/Backup Election (1)
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
R1
R2
Master
Backup
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
Backup
Backup
Master
Backup
Priority: 200
Priority: 100
Master/Backup election when VRRP priorities are different
The VRRP priority of R1's interface is 200, and that of R2's interface is 100. When the two devices are initialized, they both switch to the Backup state.
R1 and R2 switch from the Backup state to the Master state after the MASTER_DOWN timer expires. Therefore, R1 switches to the Master state faster than R2.
R1 and R2 send VRRP packets to each other to elect the master. The router with a higher priority is elected as the master, so R1 is elected as the master.
After R1 is elected as the master, it immediately sends gratuitous ARP packets to advertise the virtual MAC address to the connected devices and hosts.
1
1
2
2
3
4
Gratuitous ARP packet
Switch
Notes: If a VRRP-enabled device in Initialize state receives an interface Up message and its priority is lower than 255, it switches to the Backup state. The device switches to the Master state when the MASTER_DOWN timer expires.
If the device with a higher priority and the device with a lower priority start in sequence, the device with a higher priority enters the Master state first. After receiving a VRRP Advertisement packet with a higher priority, the device with a lower priority remains in Backup state.
If the device with a lower priority and the device with a higher priority start in sequence, the device with a lower priority switches from the Backup state to the Master state first. After receiving the VRRP Advertisement packet with a lower priority, the device with a higher priority switches to the Master state.

## Slide 17: VRRP Master/Backup Election (2)
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
R1
R2
Master
Backup
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
Backup
Backup
Master
Master
Priority: 200
Priority: 200
1
1
2
2
3
4
Gratuitous ARP packet
Master/Backup election when VRRP priorities are the same
The VRRP priorities of GE0/0/0 interfaces on R1 and R2 are both 200. When the two devices are initialized, they both switch to the Backup state.
Because the priorities of R1 and R2 are the same, R1 and R2 switch from the Backup state to the Master state after the MASTER_DOWN timer expires.
R1 and R2 exchange VRRP packets with the same priority. R1 and R2 compare their interface IP addresses to select the master. Because the interface IP address of R2 is greater than that of R1, R2 is selected as the master.
After R2 is elected as the master, it immediately sends gratuitous ARP packets to advertise the virtual MAC address to the connected devices and hosts.
Switch
Notes: If a VRRP-enabled device in Initialize state receives an interface Up message and its priority is lower than 255, it switches to the Backup state. The device switches to the Master state when the MASTER_DOWN timer expires.
If the device with a higher priority and the device with a lower priority start in sequence, the device with a higher priority enters the Master state first. After receiving a VRRP Advertisement packet with a higher priority, the device with a lower priority remains in Backup state.
If the device with a lower priority and the device with a higher priority start in sequence, the device with a lower priority switches from the Backup state to the Master state first. After receiving the VRRP Advertisement packet with a lower priority, the device with a higher priority switches to the Master state.

## Slide 18: VRRP Master/Backup Election (3)
GE0/0/0
192.168.1.254/24
GE0/0/0
192.168.1.253/24
Master/Backup election process when a device interface is configured as the IP address owner
The VRRP priorities of GE0/0/0 interfaces on R1 and R2 use the default value — 100. However, the IP address of GE0/0/0 on R1 is the same as the virtual IP address.
R1's GE0/0/0 directly switches to the Master state, and R1 becomes the master.
When a router interface is configured as the VRRP IP address owner (the interface IP address is the same as the virtual IP address), the router can directly switch to the Master state without waiting for any timer to expire.
VRRP VRID: 1
Priority: 100
VRRP VRID: 1
Priority: 100
R1
R2
Master
Backup
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.254
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
Switch
Notes: In most cases, the interface IP address of a VRRP router does not overlap with the IP address of a virtual router. That is, an independent IP address is planned for the virtual router instead of the interface IP address of a router. There is also an exception. For example, if IP addresses are insufficient on some networks, the interface IP address of a router may be used as the IP address of the virtual router. In this case, the router becomes the master.
The priority of a VRRP-enabled interface cannot be manually set to 255. When the IP address of an interface is configured as the IP address owner, the priority of the interface automatically changes to 255.

## Slide 19: VRRP Active/Standby Switchover
The Master or Link Fails
Master
Backup
Master
2
The Master Is Deleted from the VRRP Group
Master
Backup
Master
VRRP packet priority = 0
Switching time = Skew_time
Switching time = 3*ADVER_INTERVAL + Skew_time
R1 is deleted from the VRRP group, for example, the VRRP configuration of the interface is deleted.
1
2
3
1
VRRP packets cannot reach R2 due to a link fault.
PC1
PC2
R1
R2
PC3
PC1
PC2
R1
R2
PC3
Switch
Switch
Notes: If the master gives up the master role (for example, the master is deleted from the VRRP group), it sends VRRP Advertisement packets carrying a priority of 0 to the backups. Without waiting for the MASTER_DOWN timer to expire, the backup router with the highest priority switches to the Master state after a specified switching time. This switching time is called Skew_Time.
If the master cannot send VRRP Advertisement packets due to network faults, the backups cannot learn the running status of the master immediately. In this situation, the backup router with the highest priority switches to the Master state after the MASTER_DOWN timer expires.

## Slide 20: VRRP Active/Standby Switchback (1)
Priority = 200
Priority = 150
When R1 fails, a new VRRP master/backup election is performed. As shown in the figure, R2 becomes the new master to forward user packets.
PC1
PC2
VRRP
R1
R2
PC3
Master
Backup
Priority = 200
Priority = 150
PC1
PC2
VRRP
R1
R2
PC3
Master
Backup
Switch
Switch
In normal situations, the master forwards user packets. As shown in the figure, all user traffic reaches the Internet through R1.

## Slide 21: VRRP Active/Standby Switchback (2)
VRRP preemption mode:
  Preemption mode (enabled by default): If the backup is enabled with the preemption function, it immediately switches to the Master state when detecting that the priority of the master is lower than its own priority.
  Non-preemption mode: If the preemption function is disabled on the backup, the backup remains in Backup state until the master fails even when detecting that the priority of the master is lower than that of the backup.
After R1 recovers, a new VRRP master/backup election is performed. R1 becomes the new master to forward user packets because R1 has a higher priority than R2.
Priority = 200
Priority = 150
PC1
PC2
VRRP
R1
R2
PC3
Master
Backup
Switch
Notes: When the preemption mode is enabled for a VRRP group and an active/standby switchover is performed, the switching time is as follows:
Switching time = 3*ADVER_INTERVAL + Skew_time + Delay_time
In preemption mode, if the master is unstable or the network quality is poor, the VRRP group frequently switches, causing frequent update of ARP entries. To resolve this problem, you can set a preemption delay. After the preemption delay plus the value of the MASTER_INTERVAL timer, if the master becomes stable, a switchback is performed.

## Slide 22
Introduction to VRRP
VRRP Implementation
Typical Application Scenarios of VRRP
Basic VRRP Configurations

## Slide 23: VRRP Load Balancing
In the scenario where multiple virtual routers (VRRP groups) are created and each physical router plays different roles in different VRRP groups, the virtual IP addresses of different virtual routers function as different intranet gateway addresses to implement load balancing.
Vrid 1 Master
Virtual ip: 192.168.1.254
Priority: 200
Vrid 2 Backup
Virtual ip: 192.168.1.251
Priority: 100
Vrid 1 Backup
Virtual ip: 192.168.1.254
Priority: 100
Vrid 2 Master
Virtual ip: 192.168.1.251
Priority: 200
VRRP
R1
R2
PC3
IP: 192.168.1.3/24
Gateway: 192.168.1.251
PC1
IP: 192.168.1.1/24
Gateway: 192.168.1.254
PC2
IP: 192.168.1.2/24
Gateway: 192.168.1.254
Switch

## Slide 24: VRRP Monitoring the Uplink Interface Status
GE0/0/1
PC1
PC2
VRRP
R1
R2
PC3
Master
Backup
Switch
VRRP can monitor the status of the uplink interface. When a device detects a fault on the uplink interface or link, the device reduces the VRRP priority. This ensures that the backup with a normal uplink can be elected as the Master to forward packets.
Notes: If association between VRRP and the uplink interface is not configured and the uplink interface or link of R1 (master) in the VRRP group fails, the VRRP group cannot detect the fault and the master cannot forward traffic. In this case, the active/standby switchover cannot be performed, causing a traffic blackhole.

## Slide 25: Association Between VRRP and BFD
With association between VRRP and BFD enabled, when the backup detects a fault through BFD, the backup switches to the Master state immediately without waiting for the MASTER_DOWN timer to expire. This implements millisecond-level active/standby switchover.
192.168.1.251/24
192.168.1.252/24
GE0/0/0
GE0/0/0
BFD session
R1
R2
Master
Backup
PC3
PC1
PC2
Switch
Notes: If the link between devices in a VRRP group fails, VRRP Advertisement packets cannot be exchanged to negotiate the Master or Backup state. A backup switches to the Master state when the MASTER_DOWN timer expires. During the waiting period, user traffic is still forwarded to the master, resulting in user traffic loss.
A BFD session is established between the master and backup in a VRRP group and is bound to the VRRP group. BFD immediately detects communication faults in the VRRP group and instructs the VRRP group to perform an active/standby switchover, minimizing service interruptions.
For association between VRRP and BFD, a VRRP group adjusts priorities according to the BFD session status and determines whether to perform an active/standby switchover according to the adjusted priorities. In practice, delayed preemption is configured on the master and immediate preemption is configured on the backup. When the backup detects that the BFD session goes Down, it increases its priority to be higher than the priority of the master to implement a fast switchover. After the fault is rectified and the BFD session goes Up, the new master reduces its priority and sends a VRRP Advertisement packet. After the delay, the new master becomes the backup again.

## Slide 26: Application of VRRP and MSTP
Instance 1 vlan 10 primary
Instance 2 vlan 20 secondary
Instance 1 vlan 10 secondary
Instance 2 vlan 20 primary
VRID 1 : Master
VRID 2 : Backup
VRID 1 : Backup
VRID 2 : Master
HostA
IP: 192.168.1.1/24
Gateway: 192.168.1.254
GE0/0/23
GE0/0/24
Trunk
Trunk
SW1
SW2
SW3
VRRP
VLAN 10
HostB
IP: 192.168.2.1/24
Gateway: 192.168.2.254
VLAN 20
MSTP prevents loops.
VRRP active/standby switchover can be used.
Blocked port in MSTI 2
Blocked port in MSTI 1
Notes: MSTP maps one or more VLANs to an MSTI. Multiple VLANs share a spanning tree, and MSTP implements load balancing.
The VRRP-enabled gateway can be automatically switched based on network topology changes, improving network reliability.
VRRP+MSTP can implement load balancing while ensuring network redundancy.

## Slide 27
Introduction to VRRP
VRRP Implementation
Typical VRRP Applications
Basic VRRP Configurations

## Slide 28: Basic VRRP Configuration Commands (1)
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id virtual-ip virtual-address
Create a VRRP group and configure a virtual IP address for the VRRP group.
The virtual IP address of a VRRP group must be unique. Interfaces in the same VRRP group must use the same VRID.
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id priority priority-value
2. Configure a priority for each device in the VRRP group.
In most cases, the priority of the master is higher than that of the backup.
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id preempt-mode timer delay delay-value
3. Configure a preemption delay for the VRRP group.
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id preempt-mode disable
4. Configure the VRRP group to work in non-preemption mode.
By default, the preemption mode is enabled.

## Slide 29: Basic VRRP Configuration Commands (2)
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id track interface interface-type interface-number [ increased value-increased | reduced value-decreased ]
5. Associate the VRRP group with an interface.
You can configure the device to increase or decrease its priority when detecting an uplink interface or link fault. The IP address owner and Eth-Trunk member interfaces cannot be associated with VRRP.
[interface-GigabitEthernet0/0/0] vrrp vrid virtual-router-id track bfd-session { bfd-session-id | session-name bfd-configure-name } [ increased value-increased | reduced value-reduced ]
6. Associate the VRRP group with a BFD session.
If session-name bfd-configure-name is specified, the VRRP group can be associated only with static BFD sessions with automatically negotiated discriminators or static BFD session discriminators.
If bfd-session-id is specified, a VRRP group can be bound to only static BFD sessions.

## Slide 30: VRRP Configuration Example
Requirements:
  R1 and R2 form a VRRP group. R1 is the master and R2 is the backup.
  The preemption mode is used when the master recovers. The preemption delay is 10 seconds.
  The master monitors the status of the uplink interface to implement automatic VRRP active/standby switchover.
[R1] interface GigabitEthernet0/0/0
[R1-GigabitEthernet0/0/0] ip address 192.168.1.253 24
[R1-GigabitEthernet0/0/0] vrrp vrid 1 virtual-ip 192.168.1.254
[R1-GigabitEthernet0/0/0] vrrp vrid 1 priority 120
[R1-GigabitEthernet0/0/0] vrrp vrid 1 preempt-mode timer delay 10
[R1-GigabitEthernet0/0/0] vrrp vrid 1 track interface GigabitEthernet0/0/1 reduced 30
[R2] interface GigabitEthernet0/0/0
[R2-GigabitEthernet0/0/0] ip address 192.168.1.252 24
[R2-GigabitEthernet0/0/0] vrrp vrid 1 virtual-ip 192.168.1.254
[R2-GigabitEthernet0/0/0] vrrp vrid 1 priority 110
R1 configuration:
R2 configuration:
R1
R2
Master
Backup
HostA
IP: 192.168.1.1/24
Gateway: 192.168.1.254
HostB
IP: 192.168.1.2/24
Gateway: 192.168.1.254
HostC
IP: 192.168.1.3/24
Gateway: 192.168.1.254
GE0/0/0
GE0/0/0
GE0/0/1
192.168.1.253/24
192.168.1.252/24
Switch

## Slide 31: Verifying Basic VRRP Configurations
[R1]display vrrp
GigabitEthernet0/0/0 | Virtual Router 1 # Set the VRID to 1.
State : Master The device is in Master state in the VRRP group.
Virtual IP : 192.168.1.254
Master IP : 192.168.1.253
PriorityRun : 120 #Set the priority of the interface in the VRRP group to 120.
PriorityConfig : 120
MasterPriority : 120
Preempt : YES Delay Time : 10 s # Enable the preemption mode and set the preemption delay to 10s.
TimerRun : 1 s
TimerConfig : 1 s
Auth type : NONE
Virtual MAC : 0000-5e00-0101
Check TTL : YES
Config type : normal-vrrp
Track IF : GigabitEthernet0/0/1 Priority reduced : 30
IF state : UP
[R2]display vrrp
GigabitEthernet0/0/0 | Virtual Router 1
State : Backup # The device is in Backup state in the VRRP group.
Virtual IP : 192.168.1.254
Master IP : 192.168.1.253
PriorityRun : 110 #The priority of the interface in the VRRP group is 110.
PriorityConfig : 110
MasterPriority : 120
Preempt : YES Delay Time : 0 s # Enable the preemption mode and set the preemption delay to 0.
TimerRun : 1 s
TimerConfig : 1 s
Auth type : NONE
Virtual MAC : 0000-5e00-0101
Check TTL : YES
Config type : normal-vrrp

## Slide 32
(Multiple) Which of the following statements about the IP address in VRRP packets are true?
  The source IP address is the IP address of an interface on the master.
  The source IP address is the virtual IP address of the virtual router.
  The destination IP address is a broadcast IP address.
  The destination IP address is the IP address of the multicast group.
(Multiple) Which statements about VRRP timers are true?
  The default interval for sending VRRP Advertisement packets is 1s. The interval for sending VRRP Advertisement packets associated with a VRRP router must be the same.
  If the preemption delay is set to 4s, the backup becomes the new master if it does not receive a VRRP Advertisement packet from the master within 4 seconds.
  Set the preemption delay to 4s and the interval for sending VRRP Advertisement packets to 2s. If the backup does not receive a VRRP Advertisement packet from the master within 6s, the backup becomes the new master.
  On a busy network, set the preemption delay to a large value to prevent VRRP flapping.
Notes: AD
AD

## Slide 33
As an important reliability technology, VRRP is often used to implement gateway redundancy. VRRP improves network reliability and implements load balancing.
The VRRP priority is used to control VRRP master/backup election, and active/standby switchover and switchback. To ensure network stability, the preemption delay mechanism is designed for VRRP to reduce network flapping.
VRRP can monitor the status of uplink interfaces to detect network faults and associate with VRRP to ensure network reliability. VRRP can also be bound to BFD sessions to implement fast convergence. In addition, VRRP can be used together with MSTP, which is a common networking solution in campus networks.