## Slide 1
Chen Jianyuan/cwx652820
2020-02-26

## Slide 2: DHCP Implementation and Configuration

## Slide 3
As the network scale increases continuously and networks become increasingly complex, locations of terminals such as hosts, mobile phones, and tablets on networks change frequently. When a terminal accesses a network, the IP address, gateway address, and DNS server address need to be configured. Manually configuring these parameters for terminals is inefficient and inflexible.
The Internet Engineering Task Force (IETF) released the Dynamic Host Configuration Protocol (DHCP) in 1993. DHCP implements automatic configuration of network parameters, reducing the configuration and maintenance costs of clients.
This course describes the working mechanism, application scenarios, and basic configurations of DHCP.

## Slide 4
Upon completion of this course, you will be able to:
  Describe DHCP implementation.
  Describe DHCP address allocation rules.
  Differentiate application scenarios of DHCP and DHCP relay.
  Perform basic DHCP configurations.

## Slide 5
DHCP Background
DHCP Working Mechanism and Configuration
DHCP Relay Working Mechanism and Configuration

## Slide 6: Problems in Manually Configuring Network Parameters
Address planning
Address allocation
Address configuration
Address maintenance
Manually configuring network parameters has the following problems:
  Inflexibility
  Being vulnerable to errors
  Low IP address usage
  Heavy workload
  High requirements on personnel skills
Manually configure network parameters
IP address
Network mask
Gateway address
DNS server address
Notes: When network parameters such as the host IP address, network mask, gateway address, and DNS server address are manually configured, complex operation processes such as address planning, allocation, configuration, and maintenance are required. As a result, address allocation is inflexible, the IP address resource usage is low, the configuration is error-prone due to heavy workload, and there are high requirements on personnel skills.

## Slide 7: Basic Concepts of DHCP
The Dynamic Host Configuration Protocol (DHCP) dynamically assigns IP addresses to hosts and centrally manages host configurations.
DHCP uses the client/server (C/S) communication mode. Protocol packets are exchanged in UDP mode. Port 67 (DHCP server) and port 68 (DHCP client) are used.
  In normal cases, a client applies for configurations from the server.
  The server returns the configuration such as the IP address allocated to a client.
Compared with manual configuration, DHCP has the following advantages:
  High efficiency
  Strong flexibility
  Easy management
DHCP server
Response
Request
DHCP client
Notes: Network terminals, such as hosts, printers, laptops, mobile phones, and APs, function as DHCP clients to request network parameters from the DHCP server. The DHCP server dynamically allocates network parameters based on the requests from the DHCP clients.

## Slide 8
DHCP Background
DHCP Working Mechanism and Configuration
DHCP Relay Working Mechanism and Configuration

## Slide 9: DHCP Working Mechanism When a DHCP Client Connects to a Network for the First Time
Discovery stage: The DHCP client detects DHCP servers.
  The DHCP client broadcasts a DHCP Discover message to detect DHCP servers. The DHCP Discover message carries the client's MAC address, parameter request list, and broadcast flag.
Offer stage: A DHCP server offers network parameters to the DHCP client.
  A DHCP server selects an address pool on the same network segment as the IP address of the interface receiving the DHCP Discover message, and selects an idle IP address from the address pool. The DHCP server then sends a DHCP Offer message carrying the allocated IP address to the DHCP client.
Request stage: The DHCP client selects an IP address.
  If multiple DHCP servers reply with a DHCP Offer message to the DHCP client, the client accepts only the first received DHCP Offer message. The client then broadcasts a DHCP Request message carrying the selected DHCP server identifier and IP address.
Acknowledgment stage: The DHCP server acknowledges the IP address offered to the client.
  After receiving the DHCP ACK message, the DHCP client broadcasts a gratuitous ARP packet to detect whether other terminals on the network segment use the IP address allocated by the DHCP server.
1
3
4
2
Discovery stage: The DHCP client broadcasts a DHCP Discover message.
Offer stage: The DHCP server unicasts or broadcasts a DHCP Offer message.
Request stage: The DHCP client broadcasts a DHCP Request message.
Acknowledgment stage: The DHCP server unicasts a DHCP ACK message.
DHCP client
DHCP server
Layer 2 broadcast domain
Notes: The DHCP Request message is broadcast so as to notify all the DHCP servers that the DHCP client has selected the IP address offered by a DHCP server. Then the other servers can allocate IP addresses to other clients.
In the acknowledgement stage, IP address conflicts may occur in the following situations:
  After receiving the DHCP Discover message, the DHCP server sends a ping packet to the client before assigning an IP address to the client. If the IP address can be pinged, the IP address is unavailable and another IP address is assigned to the client.
  After the client successfully obtains an IP address, it immediately sends a gratuitous ARP packet. If a response packet is received, the client sends a DHCP Decline message to notify the DHCP server that the allocated IP address conflicts. The DHCP server then sets the IP address status to conflicting. Then, the client sends another DHCP Discover message to request a new IP address.

## Slide 10: DHCP Message Format
Key fields:
  Op (Operation Code): indicates the message type:
    1: DHCP Discover message
    2: DHCP Offer message
  Secs (seconds): is filled by a client, indicating the number of seconds elapsed since a client obtained or renewed an IP address. The default value is 3600s.
  Flags: indicates the format of the response message sent by a server, which is requested by a client. Only the leftmost bit in this field is used, and the other 15 bits are set to 0. The leftmost bit specifies the mode a DHCP server uses to transmit a DHCP Offer message.
  Yiaddr (your client ip address): indicates the IP address that a DHCP server allocates to a client. The DHCP server fills this field into a DHCP Reply message.
  Siaddr (server ip address): indicates the IP address of the DHCP server.
  Chaddr (client hardware address): indicates the IP address of a DHCP client.
  Options: contains the configuration allocated by the DHCP server to a client.
0
7
15
31
DHCP message format
Op | Htype | Hlen | Hops
Xid |  |  | 
Secs |  | Flags | 
Ciaddr |  |  | 
Yiaddr |  |  | 
Siaddr |  |  | 
Giaddr |  |  | 
Chaddr |  |  | 
Sname |  |  | 
File |  |  | 
Options(variable) |  |  | 
23
Notes: Htype (hardware type): indicates the type of the hardware address.
Hlen (hardware length): indicates the length of the hardware address.
Hops: indicates the number of DHCP relay agents that DHCP messages pass through. This field is set to 0 by a client. The value of this field is increased by 1 each time the DHCP message passes a DHCP relay agent. This field is used to limit the number of DHCP relay agents that DHCP messages pass through.
Xid: indicates a random number selected by a DHCP client to exchange messages with a DHCP server.
Sname (server host name): indicates the name of the server from which a client obtains the configuration. This field is optional and is filled in by a DHCP server. This field must be filled in with a character string that ends with 0.
File (file name): indicates the name of the configuration file for starting DHCP on the client. The DHCP server fills this field and delivers it together with the IP address to the client. This field is optional and must be filled in with a character string that ends with 0.

## Slide 11: Options Field
The options field has variable length and a maximum of 312 bytes. It contains the DHCP message type and configuration parameters allocated by a DHCP server to a client. The configuration parameters include the gateway IP address, DNS server IP address, and IP address lease.
The options field consists of Type, Length, and Value. The value of the Type sub-field ranges from 1 to 255. The following table lists the common values of Type, Length, and Value.
Type | Length (Byte) | Value | Function
1 | 4 | Subnet Mask | Specifies a subnet mask.
3 | 4 | Router (gateway) | Specifies a gateway address.
50 | 4 | Requested IP Address | Specifies a requested IP address.
51 | 4 | IP Address Lease Time | Specifies an IP address lease.
53 | 1 | Message Type | Specifies a DHCP message type.
54 | 4 | DHCP Server Identifier | Specifies a DHCP server identifier.
55 | 9 | Parameter Request List | Sets the parameter request list. A DHCP client uses this option to request specified configuration parameters.
58 | 4 | Rebinding Time Value | Specifies the lease renewal time (T1), which is 50% of the lease time.
59 | 4 | Renewal Time Value | Specifies the extended period of the lease (T2). Generally, the value is 87.5% of the lease time.

## Slide 12: DHCP Message Types
The Type subfield in the Options field of a DHCP message is set to 53, indicating the DHCP message type. In the figure, when Type is 53 and Length is 1, the Value sub-field ranges from 01 to 08, indicating a DHCP message type.
Type
Length
Value
1-DHCP DISCOVER
2-DHCP OFFER
3-DHCP REQUEST
4-DHCP DECLINE
5-DHCP ACK
6-DHCP NAK
7-DHCP RELEASE
8-DHCP INFORM
1 Byte
1 Byte
N Byte
53
Notes: DHCP Discover message: A DHCP client broadcasts this message to locate a DHCP server when the client attempts to connect to a network for the first time.
DHCP Offer message: A DHCP server sends this message in response to a DHCP Discover message. A DHCP Offer message carries configuration information.
DHCP Request message: A DHCP client broadcasts a DHCP Request message to respond to a DHCP Offer message sent by a DHCP server after the client starts; a DHCP client broadcasts a DHCP Request message to confirm the configuration (including the allocated IP address) after the client restarts; a DHCP client unicasts or broadcasts a DHCP Request message to renew the IP address lease after the client obtains an IP address.
DHCP Decline message: A DHCP client sends this message to notify the DHCP server when detecting that the IP address assigned by the DHCP server conflicts with another IP address.
DHCP ACK message: A DHCP server sends this message to acknowledge a DHCP Request message sent from a DHCP client.
DHCP NAK message: A DHCP server sends this message to reject a DHCP Request message from a DHCP client.
DHCP Release message: A DHCP client sends this message to release its allocated IP address.
DHCP Inform message: A DHCP client sends this message to obtain network configuration parameters, such as the gateway address and DNS server address, after it has obtained an IP address.

## Slide 13: User-defined Options
In addition to the options specified in the standard protocol, some options, such as Option 82 and Option 43, are not specified uniformly and are referred to as user-defined options.
  Relay agent information option (Option 82)
    The Option 82 field contains a maximum of 255 sub-options. If the Option 82 field is defined, at least one sub-option must be defined.
    The DHCP relay agent or a device enabled with DHCP snooping appends the Option 82 field to the DHCP Request message sent from a DHCP client, and then forwards the DHCP Request message to the DHCP server. An administrator can obtain information about the DHCP client from the Option 82 field, such as the VLAN ID of the switch interface connected to the DHCP client, Layer 2 port number, and MAC address of the relay agent.
  Vendor-specific information option (Option 43)
    DHCP servers and DHCP clients exchange vendor-specific information through Option 43. When a DHCP server receives a DHCP Discover message with parameter 43 encapsulated in Option 55, it encapsulates Option 43 in a DHCP Offer message and sends the message to the DHCP client.
    When a device functions as the DHCP server on a WLAN, it can deliver the AC's IP address to connected APs, which facilitates the connection setup between the AC and APs.
Notes: Commonly used sub-options:
  Sub-Option1 (Agent Circuit ID Sub-option) The sub-option is usually configured on the DHCP relay agent. It defines the VLAN ID and Layer 2 port number of the switch interface connected to the DHCP client when messages are transmitted. Sub-Option 1 and Sub-Option 2 are used together to identify the DHCP source.
  Sub-Option 2 (Agent Remote ID Sub-option) This sub-option is usually configured on the DHCP relay agent. It defines that the MAC address of the DHCP relay agent carried in the messages to be transmitted.
  Sub-Option 5 (Link-selection Suboption): This sub-option contains the IP address added by the DHCP relay agent. In this way, the DHCP server can assign an IP address that is on the same network segment as the IP address to the DHCP client.

## Slide 14: Application Example of Option 43
On a Layer 3 WLAN, when an AP goes online, it needs to obtain the IP address of the AC and establish a CAPWAP tunnel with the AC.
The IP address of the AP is allocated by the DHCP server. If the IP address of the AC and that of the AP are in different broadcast domains, the AP cannot obtain the IP address of the AC in broadcast mode. As a result, the CAPWAP tunnel cannot be set up.
The AP obtains the AC's IP address from the Option 43 field in DHCP messages. After obtaining the AC's IP address, the AP establishes a CAPWAP tunnel with the AC and goes online.
The IP address of the AC is 10.23.101.2, and the gateway address of the network where the AP is located is 10.23.100.1. The AP obtains the IP address from the IP address pool Huawei1 through DHCP. The DHCP server advertises the IP address of the AC to the AP through the Option 43 field.
DHCP Client
10.23.100.0/24
AC
SW
AP1
AP2
IP: 10.23.101.2
DHCP Server
ip pool Huawei1
Option 43
AC IP: 10.23.101.2

## Slide 15: DHCP Address Lease Renewal
When the lease reaches 50% (T1) of its validity period, the DHCP client sends a unicast DHCP Request message to the DHCP server to request lease renewal. If the DHCP client receives a DHCP ACK message from the DHCP server, the lease is successfully renewed.
If no response is received from the DHCP server when the lease reaches 87.5% (T2) of its validity period, the DHCP client sends a broadcast DHCP Request message to request lease renewal. If the DHCP client receives a DHCP ACK message from the DHCP server, the lease is successfully renewed.
If no response is received when the lease expires, the DHCP client stops using the IP address and sends a DHCP Discover message to apply for a new IP address.
The client unicasts a DHCP Request message.
The client broadcasts a DHCP Request message.
DHCP Client
DHCP Server
Layer 2 broadcast domain
T1
T2
Question: Why is the same IP address assigned to a computer each time?
The DHCP client generates different renewal requests based on the remaining lease of the IP address.
Notes: The DHCP server defines a validity period for each IP address allocated to a DHCP client. The validity period is called the lease. If the DHCP client still needs to use the IP address before the lease expires, the DHCP client can request to extend the lease. If the IP address is not required, the DHCP client can release it. If no idle IP address is available, the DHCP server assigns the IP address released by the client to another client.
If the DHCP client receives a DHCP NAK message after sending a DHCP Request message at T1 or T2, the DHCP client sends a DHCP Discover message to request a new IP address.
If a DHCP client does not need to use the allocated IP address before the lease expires, the DHCP client sends a DHCP Release message to the DHCP server to request IP address release. The DHCP server saves the configuration of this DHCP client and records the IP address in the allocated IP address list. The IP address can then be allocated to this DHCP client or other clients. A DHCP client can send a DHCP Inform message to the DHCP server to request configuration update.

## Slide 16: DHCP Client Reuse of an IP Address
Offer stage
  The DHCP client broadcasts a DHCP Request message carrying the IP address that the client has used. The requested IP address is added in the Option 50 field.
Acknowledgment stage
  After receiving the DHCP Request message, the DHCP server checks whether there is a lease record based on the MAC address in the message. If there is a lease record matching the MAC address, the DHCP server replies with a DHCP ACK message to notify the DHCP client that the requested IP address can be used. If there is no lease record, the DHCP server does not respond to the message.
DHCP Client
DHCP Server
Layer 2 broadcast domain
1
2
DHCP Request (broadcast) in the offer stage
DHCP ACK (unicast) in the acknowledgment stage
If a DHCP client reconnects to the network, it can reuse an IP address that has been allocated to it. For example, a host on a network functions as a DHCP client. When the host is powered off and then powered on, it needs to obtain related network parameters again. In this case, the host can request to allocate an IP address that has been used.
Notes: Not all clients can reuse IP addresses that have been allocated to them.

## Slide 17: IP Address Allocation Sequence
A DHCP server assigns IP addresses to a client in the following sequence:
  IP address that is in the database of the DHCP server and is statically bound to the MAC address of the client
  IP address that has previously been assigned to the client, that is, IP address in the requested IP Addr Option of the DHCP Discover message sent by the client
  IP address that is first found when the DHCP server searches the DHCP address pool for available IP addresses
  If the DHCP address pool has no available IP address, the DHCP server searches the expired IP addresses and conflicting IP addresses, and then assigns a valid IP address to the client. If all the IP addresses are in use, an error message is reported.
IP address statically bound to the MAC address
Used IP address
IP address in idle state
IP address whose lease expires
Conflicting IP address

## Slide 18: DHCP Configuration Commands (1)
[Huawei]ip pool ip-pool-name
Create a global address pool.
[Huawei-ip-pool-HW]gateway-list ip-address
Configure the gateway address of the DHCP client.
[Huawei-ip-pool-HW]network ip-address [ mask { mask | mask-length } ]
Configure the range of IP addresses that can be allocated dynamically in the global address pool.
[Huawei-ip-pool-HW]excluded-ip-address start-ip-address [ end-ip-address ]
Configure the IP addresses that are not automatically allocated in the address pool.
[Huawei-ip-pool-HW] lease { day day [ hour hour [ minute minute ] ] | unlimited }
Set the lease for IP addresses in the address pool.
[Huawei-ip-pool-HW] static-bind ip-address ip-address mac-address mac-address [ option-template template-name | description description ]
Configure the DHCP server to allocate a fixed IP address to a specified DHCP client.
Notes: In this example, the name of the IP address pool is HW.
By default, a DHCP server does not allocate fixed IP addresses to specified clients.

## Slide 19: DHCP Configuration Commands (2)
[Huawei]interface interface-type interface-number [subinterface-number ]
Configure an interface address pool.
[Huawei-GigabitEthernet0/0/1]dhcp server gateway-list ip-address
Configure a gateway IP address in the interface address pool.
[Huawei-GigabitEthernet0/0/1]dhcp server static-bind ip-address ip-address mac-address mac-address [ description description ]
Configure the DHCP server to allocate a fixed IP address to a specified DHCP client.
[Huawei-GigabitEthernet0/0/1]dhcp server excluded-ip-address start-ip-address [ end-ip-address ]
Configure the IP addresses that are not automatically allocated in the address pool.
[Huawei-GigabitEthernet0/0/1]dhcp server lease { day day [ hour hour [ minute minute ] ] | unlimited }
Set the lease for IP addresses in the address pool.
[Huawei-GigabitEthernet0/0/1]ip address ip-address { mask | mask-length }
The IP address segment of the interface is the interface address pool. The interface address mask cannot be set to 31; otherwise, the interface address pool may fail to be configured.
Notes: GigabitEthernet0/0/1 is used as an example.

## Slide 20: DHCP Configuration Example
Requirements:
  Assign an IP address to PC1 based on the global address pool.
  Assign IP addresses to PC2 and PC3 based on the interface address pool, and assign fixed IP addresses to PC3.
[R1]dhcp enable
[R1]ip pool HW
[R1-ip-pool-HW]gateway-list 192.168.1.1
[R1-ip-pool-HW]network 192.168.1.0 mask 24
[R1-ip-pool-HW]excluded-ip-address 192.168.1.200 192.168.1.254
[R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]dhcp select global # Select a global address pool.
DHCP server
SW1
PC1
R1
PC2
GE0/0/0
GE0/0/1
SW2
DHCP client
PC3
IP address: 192.168.2.2/24
MAC address: 00e0-fc00-00aa

## Slide 21: DHCP Configuration Example
Requirements:
  Assign an IP address to PC1 based on the global address pool.
  Assign IP addresses to PC2 and PC3 based on the interface address pool, and assign fixed IP addresses to PC3.
[R1]interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1]ip address 192.168.2.1 24
[R1-GigabitEthernet0/0/1]dhcp select interface # Select an interface address pool.
[R1-GigabitEthernet0/0/1]dhcp server excluded-ip-address 192.168.2.254
[R1-GigabitEthernet0/0/1]dhcp server static-bind ip-address 192.168.2.2 mac-address 00e0-fc00-00aa #Assign a fixed IP address to PC3.
DHCP server
SW1
PC1
R1
PC2
GE0/0/0
GE0/0/1
SW2
DHCP client
PC3
IP address: 192.168.2.2/24
MAC address: 00e0-fc00-00aa

## Slide 22: DHCP Configuration Result
IP addresses in an address pool can be in one of the following states:
  Used: indicates that the IP address is used.
  Idle: indicates that the IP address is idle.
  Expired: indicates that the lease of the IP address expires and the IP address is idle.
  Conflict: indicates that the IP address conflicts with another IP address on the network.
  Disable: indicates that the IP address cannot be used.
[R1]display ip pool
Pool-name : HW
Gateway-0 : 192.168.1.1
Mask : 255.255.255.0
IP address Statistic
Total: 253
Used: 2 Idle: 198
Expired: 0 Conflict: 0 Disable: 55
PC3>ipconfig
IPv4 address......................: 192.168.2.2
Subnet mask.......................: 255.255.255.0
Gateway...........................: 192.168.2.1
Physical address..................: 54-89-98-86-2B-F4
PC3 obtains a statically bound IP address.

## Slide 23
DHCP Background
DHCP Working Mechanism and Configuration
DHCP Relay Working Mechanism and Configuration

## Slide 24: Introduction to DHCP Relay
As the network scale expands and the number of network devices increases, different users in an enterprise may be distributed on different network segments. In normal cases, a DHCP server cannot meet address allocation requirements of multiple network segments. If the DHCP server is required to allocate IP addresses, DHCP messages need to be sent across network segments.
A DHCP relay agent transparently transmits DHCP messages between a DHCP client and a DHCP server that reside in different broadcast domains. The DHCP relay function allows DHCP clients and DHCP server that are in different broadcast domains to communicate.
R1
SW1
Client A
SW2
Client B
DHCP Discover
DHCP Discover
R1
SW1
Client A
SW2
Client B
DHCP Discover
DHCP Discover
DHCP relay
DHCP server
Layer 2 broadcast domain C
DHCP server
Layer 2 broadcast domain B
Layer 2 broadcast domain A
Layer 2 broadcast domain A
Layer 2 broadcast domain B
Layer 2 broadcast domain C

## Slide 25: DHCP Relay Message Format
A DHCP relay agent forwards DHCP messages between a DHCP client and a DHCP server, so the DHCP relay agent modifies only some fields in DHCP messages. The message format remains unchanged, as shown in the following figure.
Op | Htype | Hlen | Hops
Xid |  |  | 
Secs |  | Flags | 
Ciaddr |  |  | 
Yiaddr |  |  | 
Siaddr |  |  | 
Giaddr |  |  | 
Chaddr |  |  | 
Sname |  |  | 
File |  |  | 
Options(variable) |  |  | 
Hops: indicates the number of DHCP relay agents that a DHCP message passes through. This field is set to 0 by a DHCP client or server. Its value increases by 1 each time the message passes through a DHCP relay agent.
Giaddr (gateway ip address): indicates the IP address of the first DHCP relay agent. When a client sends a DHCP Request message, the first DHCP relay agent fills its IP address in this field when forwarding the message to the DHCP server.
Notes: The Hops field limits the number of DHCP relay agents that a DHCP message can pass through. A maximum of 16 DHCP relay agents are allowed between a DHCP server and a DHCP client. If the value of this field is larger than 16, DHCP messages are discarded.
The DHCP server determines the network segment address of a client based on the Giaddr field, so the DHCP server can select an appropriate address pool and assign an IP address on the network segment to the client. The DHCP server returns a DHCP Offer message to the DHCP relay agent.The DHCP relay agent then forwards the DHCP Offer message to the client. If the DHCP Discover message passes through multiple DHCP relay agents before reaching the DHCP server, the value of this field is the IP address of the first DHCP relay agent and remains unchanged. However, the value of the Hops field increases by 1 each time the DHCP Discover message passes through a DHCP relay agent.

## Slide 26: Working Mechanism of DHCP Relay
Discovery stage: After receiving the DHCP Discover message broadcast by a DHCP client, the DHCP relay agent unicasts the DHCP Discover message to the DHCP server or the next-hop relay agent through routing.
Offer stage: The DHCP server selects an address pool based on the Giaddr field in the DHCP Discover message to allocate network parameters to the DHCP client. After receiving the DHCP Offer message, the DHCP relay agent unicasts or multicasts the message to the DHCP client.
Request stage: The DHCP relay agent processes the DHCP Request message from the client using the same method described in the Discovery stage.
Acknowledgment stage: The DHCP relay agent processes the DHCP ACK message from the server using the same method described in the Offer stage.
DHCP Client
DHCP Relay
DHCP Server
1
3
4
2
DHCP Discover message in the discovery stage
DHCP Offer message in the offer stage
DHCP Request message in the request stage
DHCP ACK message in the acknowledgment stage
Unicast DHCP Discover message by the relay agent
Send DHCP offer message by the DHCP server
Unicast DHCP Request message by the relay agent
Send DHCP ACK message by the DHCP server
Working mechanism when a DHCP client connects to a network for the first time in the scenario where a DHCP relay agent is deployed
Notes: After receiving a DHCP Discover message, the DHCP relay agent processes the message as follows:
  Checks the value of the Hops field. If this value exceeds 16, the DHCP relay agent discards the message. Otherwise, the DHCP relay agent increases this value by 1 and proceeds to the next step.
  Checks the value of the Giaddr field. If this value is 0, the DHCP relay agent sets the Giaddr field to the IP address of the interface receiving the DHCP Discover message. If not, the DHCP relay agent does not change the field and proceeds to the next step.
  Changes the destination IP address of the DHCP Discover message to the IP address of the DHCP server or the next-hop DHCP relay agent, and changes the source IP address to the IP address of the interface connecting the DHCP relay agent to the client. The message is then unicast to the DHCP server or the next-hop DHCP relay agent.
After receiving the DHCP Discover message, the DHCP server selects an address pool on the same network segment as the value of the Giaddr field in the message, allocates parameters such as an IP address to the client, and unicasts a DHCP Offer message to the DHCP relay agent identified by the Giaddr field. After receiving the DHCP Offer message, the DHCP relay agent performs the following operations:
  Checks the value of the Giaddr field. If this value is not the IP address of the interface receiving the DHCP Offer message, the DHCP relay agent discards the message. Otherwise, the DHCP relay agent proceeds to the next step.
  Checks the value of the Flags field. If this value is 1, the DHCP relay agent sends a broadcast DHCP Offer message to the DHCP client. Otherwise, the DHCP relay agent sends a unicast DHCP Offer message.

## Slide 27: DHCP Relay Configuration Commands
[Huawei-GigabitEthernet0/0/0]dhcp select relay
Enable the DHCP relay function on an interface.
[Huawei-GigabitEthernet0/0/0]dhcp relay server-ip ip-address
Specify an IP address for the DHCP server in the interface view.
[Huawei]dhcp server group group-name
Create a DHCP server group.
[Huawei-dhcp-server-group-HW]dhcp-server ip-address [ ip-address-index ]
Add DHCP servers to the DHCP server group.
[Huawei-GigabitEthernet0/0/0]dhcp relay server-select group-name
Configure a DHCP server group for the interface.
[Huawei-GigabitEthernet0/0/0]ip address dhcp-alloc
Enable the DHCP client function on the interface.

## Slide 28: DHCP Relay Configuration Example (1)
The configuration requirements are as follows:
  R1 obtains an IP address through DHCP.
  The DHCP relay function is enabled on GE0/0/0 of R2 and the IP address of the DHCP server is set to 10.1.1.2.
  An address pool named HW-1 is created on R3, with the IP address range of 192.168.10/24 and gateway address of 192.168.1.1.
DHCP Client
DHCP Relay
DHCP Server
R1
R2
R3
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
.1
.2
10.1.1.0/24
192.168.1.0/24
.1
[R2]dhcp server group HW
[R2-dhcp-server-group-HW]dhcp-server 10.1.1.2
[R2-dhcp-server-group-HW]quit
[R2]interface GigabitEthernet 0/0/1
[R2-GigabitEthernet0/0/1]ip address 10.1.1.1 24
[R2-GigabitEthernet0/0/1]quit
[R2]interface GigabitEthernet 0/0/0
[R2-GigabitEthernet0/0/0]ip address 192.168.1.1 24
[R2-GigabitEthernet0/0/0]dhcp select relay
[R2-GigabitEthernet0/0/0]dhcp relay server-select HW
[R2-GigabitEthernet0/0/0]quit
[R1]interface GigabitEthernet0/0/0
[R1-GigabitEthernet0/0/0]ip address dhcp-alloc
[R1-GigabitEthernet0/0/0]quit
Configuration of R1 and R2:
Notes: Before configuring DHCP on each device, run the dhcp enable command in the system view to enable DHCP.

## Slide 29: DHCP Relay Configuration Example (2)
The configuration requirements are as follows:
  GE0/0/0 on R1 obtains an IP address through DHCP.
  The DHCP relay function is enabled on GE0/0/0 of R2 and the IP address of the DHCP server is set to 10.1.1.2.
  An address pool named HW-1 is created on R3, with the IP address range of 192.168.10/24 and gateway address of 192.168.1.1.
DHCP Client
DHCP Relay
DHCP Server
R1
R2
R3
GE0/0/0
GE0/0/0
GE0/0/1
GE0/0/1
.1
.2
10.1.1.0/24
192.168.1.0/24
.1
Configuration of R3:
[R3]ip pool HW-1
[R3-ip-pool-HW-1]network 192.168.1.0 mask 24
[R3-ip-pool-HW-1]gateway-list 192.168.1.1
[R3-ip-pool-HW-1]quit
[R3]interface GigabitEthernet 0/0/1
[R3-GigabitEthernet0/0/1]ip address 10.1.1.2 24
[R3-GigabitEthernet0/0/1]dhcp select global
[R3-GigabitEthernet0/0/1]quit
[R3]ip route-static 192.168.1.0 255.255.255.0 10.1.1.1

## Slide 30: DHCP Relay Configuration Verification
The command output shows that GE0/0/0 on R1 has obtained an IP address and a gateway address.
Check the DHCP relay information on R2.
<R2>display dhcp relay all
DHCP relay agent running information of interfaceGigabitEthernet0/0/0 :
Server group name : HW
Gateway address in use : 192.168.1.1
<R2>display dhcp relay statistics
The statistics of DHCP RELAY:
DHCP packets received from clients : 2
DHCP packets sent to clients : 2
DHCP packets received from servers : 2
DHCP packets sent to servers : 2
……
<R1>display dhcp client
DHCP client lease information on interface GigabitEthernet0/0/0 :
Current machine state : Bound
Internet address assigned via : DHCP
Physical address : 00e0-fce6-4691
IP address : 192.168.1.254
Subnet mask : 255.255.255.0
Gateway ip address : 192.168.1.1
DHCP server : 10.1.1.2
……
Check the IP address obtained by GE0/0/0 on R1.
The command output shows that the DHCP relay function is enabled on GE0/0/0 of R2, and R2 functions as the DHCP relay agent to exchange messages with the DHCP client and DHCP server for four times.

## Slide 31
(Single) Which of the following messages is sent by the DHCP client to the DHCP server to renew the lease?
  DHCP DISCOVER
  DHCP OFFER
  DHCP REQUEST
  DHCP ACK
(Single) Which of the following commands can be used to enable the DHCP relay function on a router interface?
  dhcp select server
  dhcp select global
  dhcp select interface
  dhcp select relay
Notes: C
D

## Slide 32
This course describes the format of DHCP messages and functions of key fields. It describes how a DHCP server assigns network parameters, such as IP addresses, to DHCP clients through message exchange. In addition, this course describes how a DHCP client renews its IP address lease and obtains an IP address after restart.
When a DHCP client and a DHCP server are in different broadcast domains, the DHCP relay function enables DHCP messages to be transmitted across network segments. This function implements message negotiation between the DHCP client and the DHCP server.