## Slide 1
Shi Miaomiao/swx791350
2020
New

## Slide 2: BGP Path Attributes and RRs

## Slide 3
Each BGP route has multiple path attributes. When a router advertises a BGP route to its peer, the route carries multiple path attributes. These attributes describe route characteristics that affect BGP route selection in some scenarios.
IBGP split horizon prevents routing loops in an AS, but also brings the following problem: A BGP route can be only transmitted to one next hop in an AS. If IBGP peers establish full-mesh connections, the load on devices increases.
This course describes BGP path attributes and route reflectors (RRs).

## Slide 4
Upon completion of this course, you will be able to:
  Describe common BGP path attributes and their functions.
  Describe the concept and application scenarios of BGP RRs.
  Describe the rules and working mechanism of BGP RRs.

## Slide 5
BGP Path Attributes
BGP RRs

## Slide 6: Path Attributes
Each BGP route has multiple path attributes.
When a router advertises a BGP route to its peer, it also advertises the path attributes carried in the route.
BGP path attributes affect route selection.
BGP Update
…..
Path Attribute: Origin
Path Attribute: AS_PATH
Path Attribute: Local_Pref
AS 200
AS 300
BGP speaker
BGP speaker
BGP Update

## Slide 7: Path Attribute Classification
Optional transitive
Optional
non-transitive
Well-known attributes can be identified by all BGP routers.
Well-known attributes are classified into the following types:
  Well-known mandatory: It must be included in each Update message.
  Well-known discretionary: It may be included in some Update messages.
Not all optional attributes need to be identified by BGP routers.
Optional attributes are classified into the following types:
  Optional transitive: A BGP device may not identify this type of attribute but still accepts and advertises them to peers.
  Optional non-transitive: A BGP device may not identify this type of attribute, in which case it ignores them without advertising them to peers.
Well-known mandatory
Well-known discretionary
Origin
AS_Path
Next_hop
Local_Preference
Atomic_aggregate
Aggregator
Community
MED
Cluster-List
Originator-ID
Well-known
Optional
Notes: There are many BGP attributes. This section lists only common BGP attributes.

## Slide 8: Example of BGP Update Messages
Border Gateway Protocol - UPDATE Message
Marker: ffffffffffffffffffffffffffffffff
Length: 53
Type: UPDATE Message (2)
Withdrawn Routes Length: 0
Total Path Attribute Length: 28
Path attributes
Path Attribute - ORIGIN: IGP
Path Attribute - AS_PATH: 65536 1 2 3
Path Attribute - NEXT_HOP: 172.16.1.1
Network Layer Reachability Information (NLRI)
30.0.0.0/8
NLRI prefix length: 8
NLRI prefix: 30.0.0.0
Path attribute in a BGP Update message

## Slide 9: AS_Path
This attribute is a well-known mandatory attribute. It is a list of AS numbers that the route to the destination network passes through.
Function: Ensures that routes are transmitted between EBGP peers without loops. In addition, it is one of the attributes used for route selection.
When a route is advertised to an EBGP peer, the router adds the local AS number to the AS_Path of the route. When a route is advertised to an IBGP peer, the AS_Path remains unchanged.
AS 300
AS 200
AS 100
R2
R3
R1
BGP Update
10.0.1.0/24
BGP Update
AS_Path: 100
NLRI: 10.0.1.0/24
BGP Update
AS_Path: 200 100
NLRI: 10.0.1.0/24
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 10: AS_Path Prevents Loops
The AS_Path attribute in the BGP Update message sent by R1 to R4 is 400 300 200 100. R1 does not accept the route because it has its own AS number. This prevents routing loops.
AS 300
AS 200
AS 100
R2
R1
AS 400
R3
R4
1
2
3
4
BGP Update
BGP Update
AS_Path: 400 300 200 100
NLRI: 10.0.1.0/24
10.0.1.0/24
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 11: AS_Path Affects Route Selection
AS 400
AS 500
AS 200
R5
R2
AS 300
R4
R3
R1
10.0.1.0/24
BGP Update
BGP Update
AS_Path: 200 100
NLRI: 10.0.1.0/24
AS 100
BGP Update
AS_Path: 400 300 100
NLRI: 10.0.1.0/24
The AS_Path attribute affects BGP route selection. As shown in the figure, R5 learns BGP routes to the 10.0.1.0/24 network segment from both R2 and R4. If other conditions are the same, R5 preferentially selects the routes advertised by R2. This is because the AS_Path attribute of the route is short, that is, the number of AS numbers is small.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 12: AS_Path Types
AS_SEQENCE
AS_SET
AS 300
AS 200
AS 100
R2
R3
R1
AS numbers in the AS_Path are in an ordered list. By default, the AS_Path is of this type.
BGP Update
AS_PATH
type=AS_SEQENCE
value=200 100
AS 300
R3
R1
R2
AS 100
AS 200
R4
AS 400
10.0.1.0/24
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
Summarize the route 10.0.0.0/16 on R3 and add the AS_SET keyword. The AS_PATH attribute value is as follows:
AS_PATH=300 {100，200}
(including AS_SEQENCE and AS_SET)
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive
Notes: Route summarization reduces the device burden and shields specific routes to reduce the impact of route flapping. After routes are summarized, the AS_Path attribute is lost, which may cause routing loops. Therefore, the AS_Path of the AS_SET type can be used to carry AS numbers before route summarization.
If the summarized route needs to carry the numbers of ASs through which all specific routes pass so as to prevent routing loops, you can specify the as-set parameter in the aggregate command.
In the example of AS_SET, if routes are summarized in AS 300 and the as-set parameter is configured, the AS_Paths of specific routes are represented by an AS-Set set. The AS numbers in the brackets ({}) are not listed in sequence. The summarized route carries AS numbers to prevent loops.
In addition to AS_SET and AS_AS_SEQENCE, AS_Path also has two types: AS_Confed_Sequence and AS_Confed_Set, which are used in BGP confederation and are not involved in this course.

## Slide 13: Changing the AS_Path
You can use a route-policy to modify the AS_Path attribute of a BGP route in one of the following modes:
AS_Path: 100
apply as-path 300 additive
AS_Path: 300 100
Add a new AS_Path value, which is placed preceding original AS_Path value.
additive
overwrite
none overwrite
Replace the existing AS_Path value with a new value.
AS_Path: 100 200 300
apply as-path 400 overwrite
AS_Path: 400
apply as-path none overwrite
AS_Path:
Delete the existing AS_Path value.
AS_Path: 100 200 300
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 14: Origin
This attribute is a well-known mandatory attribute and identifies the origin of a BGP route. As described in the table, the Origin attribute is classified into three types based on the mode in which routes are imported to BGP.
If multiple routes with different Origin attributes are destined for the same destination and other conditions are the same, routes with Origin attributes of IGP, EGP, and Incomplete are in descending order of priority.
Type | Flag | Description
IGP | i | If the route is imported to BGP by the originating BGP router through the network command, the Origin attribute of the BGP route is IGP.
EGP | e | If the route is learned through an EGP, the Origin attribute of the BGP route is EGP.
Incomplete | ? | If the route is learned in other modes but not the preceding two modes, the Origin attribute is Incomplete. For example, routes are imported to BGP using the import-route command.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 15: Origin Attribute in the BGP Routing Table
[R2] display bgp routing-table
BGP Local router ID is 10.0.2.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 4
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 10.0.1.0/24 10.0.12.1 0 200 0 i
* i 10.0.23.3 0 100 0 i
Origin
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 16: Next_Hop
This attribute is a well-known mandatory attribute and is used to specify the next-hop address to the destination network.
After a router learns a BGP route, it checks the Next_Hop attribute of the BGP route. The Next_Hop attribute (IP address) must be reachable on the local router. If the Next_Hop attribute is unreachable, the BGP route is unavailable.
The rules for setting the default Next_Hop attribute of BGP routes in different scenarios are as follows:
  When advertising a BGP route to its EBGP peer, a router sets the Next_Hop attribute of the route to the source IP address of a TCP connection.
  When receiving a BGP route advertised by an EBGP peer, the router does not change the Next_Hop attribute of the route that is advertised to its IBGP peer.
  If a router receives a BGP route whose Next_Hop value is on the same network segment as the EBGP peer, the router retains the Next_Hop value of the route and advertises the route to its BGP peer.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 17: Default Operation for Next_Hop (1)
When advertising a BGP route to its EBGP peer, a router sets the Next_Hop attribute of the route to the source IP address of a TCP connection.
AS 100
AS 200
R1
R2
R3
BGP Update
10.0.1.0/24
10.0.12.1
10.0.12.2
10.0.23.2
10.0.23.3
BGP Update
Next_Hop: 10.0.12.1
NLRI: 10.0.1.0/24
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 18: Default Operation for Next_Hop (2)
When receiving a BGP route advertised by an EBGP peer, the router does not change the Next_Hop attribute of the route that is advertised to its IBGP peer.
AS 100
AS 200
R1
R2
R3
BGP Update
10.0.1.0/24
10.0.12.1
10.0.23.2
10.0.23.3
BGP Update
Next_Hop: 10.0.12.1
NLRI: 10.0.1.0/24
10.0.12.2
BGP Update
Next_Hop: 10.0.12.1
NLRI: 10.0.1.0/24
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 19: Default Operation for Next_Hop (3)
If a router receives a BGP route whose Next_Hop value is on the same network segment as the EBGP peer, the router retains the Next_Hop value of the route and advertises the route to its BGP peer.
AS 100
AS 200
R2
R3
BGP Update
10.0.2.0/24
10.0.123.1
The Next_hop attribute of the route 10.0.2.0/24 received by R3 is 10.0.123.2.
R1
EBGP
IBGP
10.0.123.2
10.0.123.3
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 20: Changing the Next_Hop Attribute
The peer next-hop-local command can be used to configure a BGP device to set the value of the Next_Hop attribute to the source address of a TCP connection for peer relationship setup when the BGP device advertises routes to an IBGP peer or a peer group.
AS 100
AS 200
R1
R2
R3
BGP Update
10.0.1.0/24
10.0.12.1
10.0.23.2
10.0.23.3
BGP Update
Next_Hop: 10.0.23.2
NLRI: 10.0.1.0/24
10.0.12.2
BGP Update
Next_Hop: 10.0.12.1
NLRI: 10.0.1.0/24
bgp 200
peer 10.0.23.3 as-number 200
peer 10.0.23.3 next-hop-local
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive
Notes: By default, the Next_Hop attribute of the BGP route 10.0.1.0/24 advertised by R2 to R3 is 10.0.12.1. If R2 does not advertise the route 10.0.12.0/24 to the IGP of AS 200, R3 cannot learn the route to 10.0.12.1. In this case, the next hop of the BGP route 10.0.1.0/24 is unreachable, so the route is considered invalid.

## Slide 21: Local_Preference
The Local_Preference attribute is a well-known discretionary attribute. It can be used to inform routers in an AS of the preferred path to leave the AS.
A larger value of the Local_Preference attribute indicates a better BGP route. The default value is 100.
This attribute can be advertised only to IBGP peers but not EBGP peers.
AS 200
IBGP
R2
R1
R3
R4
R5
10.0.45.0/24
EBGP
EBGP
BGP Update
BGP Update
Local_Preference: 200
NLRI: 10.0.45.0/24
BGP Update
Local_Preference: 100
NLRI: 10.0.45.0/24
On R1 and R3, configure a routing policy for R2 so that the value of the Local_Preference attribute in the route 10.0.45.0/24 sent by R1 to R2 is 200 and R3 retains the default value of Local_Preference. In this case, the route 10.0.45.0/24 advertised by R1 is preferred.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 22: Checking the Local_Preference Attribute in the BGP Routing Table
The BGP route with the Local_Preference value of 200 takes precedence over the BGP route with the Local_Preference value of 100. In the BGP routing table, the BGP route from 10.0.12.1 is the optimal route.
[R2] display bgp routing-table
BGP Local router ID is 10.0.2.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 4
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 10.0.45.0/24 10.0.12.1 0 200 0 i
* i 10.0.23.3 0 100 0 i
Local_Preference
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 23: Precautions for Local_Preference
The Local_Preference attribute can be transmitted only between IBGP peers (the Local_Preference value is not lost during transmission between IBGP peers unless a policy is configured), but cannot be transmitted between EBGP peers. If the AS_Path attribute of a route received between EBGP peers carries Local_Preference, errors may occur in the BGP process.
However, you can use the inbound policy on the AS border router to change the Local_Preference value. That is, after a route is received, the local device assigns the Local_Preference value to the route.
You can run the bgp default local-preference command to change the default Local_Preference value. The default value is 100.
When a router sends a route update to its EBGP peer, the route update cannot carry the Local_Preference attribute. After the peer receives the route, the peer assigns the default Local_Preference value (100) to the route and then advertises the route to its IBGP peer.
For the routes imported by using the network or import-route commands, the Local_Preference value is 100 by default and can be transmitted to other IBGP peers in the AS. During the transmission, the Local_Preference value remains unchanged unless it is affected by a routing policy.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 24: Background of the Community Attribute (1)
AS 200
AS 100
R3
R1
Route to the production network
10.1.0.0/24
10.1.1.0/24
10.1.2.0/24
...
Route to the office network
10.2.0.0/24
10.2.1.0/24
10.2.2.0/24
...
BGP Update
In AS 100, a large number of routes are imported to BGP. These routes are used on the production and office networks. Currently, BGP routers in AS 200 need to apply different policies to these routes. If filters such as the ACL and IP prefix list are used, the matching efficiency is low.
R2
BGP routes
BGP routes
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 25: Background of the Community Attribute (2)
AS 200
AS 100
R3
R1
With the Community attribute, different Community attribute values can be added to different types of routes. These attribute values are updated to AS 200 with BGP routes. Therefore, BGP routers in AS 200 only need to implement differentiated policies based on Community attribute values, without considering the specific route prefix.
R2
BGP routes
Community 100:10
BGP routes
Community 100:20
Route to the production area
10.1.0.0/24
10.1.1.0/24
10.1.2.0/24
...
Route to the office area
10.2.0.0/24
10.2.1.0/24
10.2.2.0/24
...
BGP Update
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 26: Community
The Community attribute is an optional transitive attribute. It is a route tag used to simplify the execution of routing policies.
You can assign a specific Community attribute value to certain routes. Then the routes can be filtered based on the Community attribute value but not the network prefix or mask and the corresponding policy can be executed.
AS 200
AS 100
R1
R2
10.0.1.0/24
10.0.1.0/24
Community = 12:10000
10.0.1.0/24
Community = 12:10000
BGP Update
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 27: Community Attribute Format
The Community attribute has 32 bits, that is, 4 bytes. The value can be in either of the following formats:
  The value is an integer in decimal notation.
  The value is in AA:NN format, in which AA indicates the AS number and NN indicates a user-defined number.
RFC format
12
10000
0x000C
0x2710
AA
NN
0x000C2710
796432
Community
Hexadecimal notation
2 bytes
2 bytes
Decimal notation
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive
Notes: The Community attribute includes self-defined and well-known community attributes.

## Slide 28: Well-known Community Attribute
Community Attribute | Value | Description
Internet | 0 (0x00000000) | A BGP device can advertise the received route with the Internet attribute to all peers. By default, all routes belong to the Internet community.
No_Advertise | 4294967042 (0xFFFFFF02) | A BGP device does not advertise the received route with the No_Advertise attribute to any peer.
No_Export | 4294967041 (0xFFFFFF01) | A BGP device does not advertise the received route with the No_Export attribute to devices outside the local AS.
No_Export_Subconfed | 4294967043 (0xFFFFFF03) | A BGP device does not advertise the received route with the No_Export_Subconfed attribute to devices outside the local AS or to devices outside the local sub-AS.
RFC 1997 defines several well-known community attributes, as described in the table.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive
Notes: The No_Export_Subconfed community attribute involves the concept of BGP confederation and is not involved in this course.

## Slide 29: MED
The multi-exit discriminator (MED) is an optional non-transitive attribute. It helps determine the optimal route when traffic enters an AS. That is, when there are multiple ingresses to the local AS, the AS can use the MED attribute to dynamically affect the path that other ASs select.
A smaller MED value indicates a better BGP route.
The MED is used for BGP route selection between ASs. After an MED is advertised to an EBGP peer, the route advertised by the peer in the AS carries the MED. When the route is advertised to the EBGP peer again, the route does not carry the MED by default.
AS 200
AS 100
R2
R3
R4
R5
BGP Update
AS 300
BGP route 10.0.23.0/24
MED = 10
10.0.23.0/24
BGP route 10.0.23.0/24
MED = 20
BGP route 10.0.23.0/24
MED not carried
Configure a routing policy on R2 and R3 so that the MED value of the BGP route advertised by R2 to R4 is 10 and the MED value of the BGP route advertised by R3 is 20. If other conditions are the same, R4 preferentially selects the BGP routes advertised by R2.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 30: Precautions for the MED
By default, a router compares the MED values of only the BGP routes from the same neighboring AS. That is, if two routes to the same destination are from different neighboring ASs, the router does not compare the MED values of the two routes.
A BGP router determines whether to carry the MED attribute in a route advertised to its EBGP peers as follows (assume that no policy is configured on the EBGP peers):
  If the BGP route is locally originated (imported using the network or import-route command), the BGP route carries the MED attribute by default and is sent to the EBGP peer.
  If a BGP route is learned from a BGP peer, the route advertised to an EBGP peer does not carry the MED attribute by default.
  When a route is transmitted between IBGP peers, the MED value is retained and transmitted with the route. The MED value will not be changed or lost during the transmission unless a policy is deployed.
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 31: Default Operation for the MED Attribute (1)
If a router learns a route through an IGP and imports the route to its BGP routing table using the network or import-route command, the MED value of the generated BGP route inherits the IGP metric value of the route. For example, in the preceding figure, R2 learns the route 10.0.1.0/24 through OSPF and the OSPF cost of the route is 100 in the global routing table of R2. When R2 imports the route into its BGP table using the network command, the MED value of the generated BGP route is 100.
If a router imports a locally direct or static route to BGP using the network or import-route command, the MED of the BGP route is 0 because the cost of the direct or static route is 0.
AS 200
AS 100
R1
R2
R3
10.0.1.0/24
BGP route 10.0.1.0/24
MED = 100
OSPF
BGP Update
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 32: Default Operation for the MED Attribute (2)
If a router learns a route from a peer through BGP, the router does not transmit the MED value by default when updating the route to its EBGP peer. That is, the MED attribute is not transmitted across ASs. As shown in the figure, if R3 learns a BGP route with the MED attribute from R2, it advertises the route without the MED attribute to R4 by default.
You can run the default med command to change the default MED value. The default med command takes effect only for the local routes imported using the import-route command and BGP summarized routes. For example, if default med 999 is configured on R2, R2 advertises the MED value 999 to R3 with the route imported using the import-route command or generated using the aggregate command.
AS 200
AS 100
R1
R2
R3
R4
AS 300
BGP route 10.0.1.0/24
without the MED attribute
10.0.1.0/24
BGP route 10.0.1.0/24
MED = 999
OSPF
BGP Update
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 33: Atomic_Aggregate and Aggregator
Atomic_Aggregate is a well-known discretionary attribute, while Aggregator is an optional transitive attribute.
AS 300
R3
R1
R2
AS 100
AS 200
R4
AS 400
10.0.1.0/24
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
On R3, specific routes are summarized to 10.0.0.0/16.
Atomic_Aggregate
The summarized route loses path attributes of specific routes, so an alarm needs to be reported to the downstream peer. The alarm contains the summarization device and the AS number of the summarization device.
bgp 300
aggregate 10.0.0.0 16 detail-suppressed
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive
Notes: The aggregate command on R3 summarizes BGP routes 10.0.1.0/24, 10.0.2.0/24, 10.0.3.0/24, and 10.0.4.0/24 into 10.0.0.0/16, and detail-suppressed is specified to prevent specific routes from being advertised. That is, R3 advertises only the summarized BGP route to R4.
Atomic_Aggregate is a well-known discretionary attribute. It is a warning flag and does not carry any information. When a router receives a BGP route update and finds that the route carries the Atomic_Aggregate attribute, the router knows that the path attribute of the route may be lost. In this case, the router advertises the route with the Atomic_Aggregate attribute to other peers. In addition, the router that receives the route update cannot further redefine the route.
The Aggregator attribute is an optional transitive attribute. When route summarization is performed, the router that summarizes routes can add the Aggregator attribute to the summarized route and record the local AS number and its router ID in the attribute. The Aggregator attribute is used to identify the AS and BGP router where routes are summarized.

## Slide 34: Checking the Summarized Route
In detailed information about BGP routes, the Aggregator attribute records the AS number and router ID of the summarization device. In addition, the Atomic-Aggregate attribute indicates that the route is a summarized route.
[R4]display bgp routing-table 10.0.0.0 16
BGP local router ID : 10.0.4.4
Local AS number : 400
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.0.0.0/16:
From: 10.0.34.3 (10.0.3.3)
Route Duration: 00h00m21s
Direct Out-interface: GigabitEthernet0/0/0
Original nexthop: 10.0.34.3
Qos information : 0x0
AS-path 300, origin igp, pref-val 0, valid, external, best, select, active, pre 255
Aggregator: AS 300, Aggregator ID 10.0.3.3, Atomic-aggregate
Not advertised to any peer yet
Well-known Mandatory
Well-known Discretionary
Optional Transitive
Optional Non-transitive

## Slide 35: Preferred-Value
Preferred-Value is a Huawei-specific attribute and is valid only on the local device. If multiple routes are available to the same destination, the route with the largest PreVal value is selected as the optimal route.
The value ranges from 0 to 65535. A larger value indicates a higher route priority.
The Preferred-Value attribute can be configured only on the local router and affects only route selection of the local router. This attribute is not advertised to any BGP peer.
AS 200
AS 100
EBGP
R2
R1
R3
10.0.13.0/24
Configure a routing policy (import policy) on R2 to set the Preferred-Value value of the route 10.0.13.0/24 advertised by R1 to 300 and the Preferred-Value value of the route 10.0.13.0/24 advertised by R3 to 200. In this way, R2 preferentially selects the route sent from R1 to reach 10.0.13.0/24.
R2 accesses 10.0.13.0/24.

## Slide 36: Checking the Preferred-Value in the BGP Routing Table
The BGP route with the Preferred-Value of 300 takes precedence over the BGP route with the Preferred-Value of 200. The BGP route from 10.0.12.1 in the BGP routing table is the optimal route.
[R2] display bgp routing-table
BGP Local router ID is 10.0.2.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 4
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.0.13.0/24 10.0.12.1 0 300 100 i
* 10.0.23.3 0 200 100 i
Preferred-Value
Notes: The Preferred-Value attribute is abbreviated as PrefVal in the routing table.

## Slide 37
BGP Path Attributes
BGP RRs

## Slide 38: IBGP Issues in the Transit AS
To ensure that all BGP routers in AS 200 can learn complete BGP routes, IBGP peers in an AS must establish full-mesh connections. However, there are the following disadvantages:
  Routers need to maintain a large number of TCP and BGP connections, especially when there are a large number of routers.
  The BGP network in an AS has poor scalability.
Therefore, route reflector (RR) technology can be used.
AS 100
AS 300
OSPF
AS 200
BGP peer relationship

## Slide 39: RR
After the RR is imported, there are two roles:
  RR
  Client
An RR reflects learned routes so that IBGP routes are advertised within an AS without establishing full-mesh IBGP connections.
When specifying a BGP router as an RR, you need to specify its client. The client does not need to be configured and does not know that an RR exists on the network.
AS 300
R5
OSPF
AS 200
RR
Reflection
R3
R2
Client
IBGP
AS 100
R4
*>i 10.0.4.0/24
IBGP
BGP Update message
R1

## Slide 40: Route Reflection Rules
When an RR receives BGP routes:
  If the RR learns an IBGP route from a non-client peer, the RR reflects the route to all clients.
  If the RR learns an IBGP route from its client, the RR reflects the route to all non-clients and all clients except the client that sends the IBGP route.
  If a route is learned from an EBGP peer, the route is advertised to all clients and non-client IBGP peers.
Notes: An RR reflects only the optimal BGP routes that it uses.

## Slide 41: Reflection Rule Example (1)
Client
AS 200
R1
R2
R4
R5
R3
RR
AS 100
Rule 1
If the RR learns an IBGP route from a non-client peer, the RR reflects the route to all clients.
Rule 2
Route update sent by BGP
Route update reflected by a BGP RR
Client
AS 200
R1
R2
R4
R5
R3
RR
Client
If the RR learns an IBGP route from its client, the RR reflects the route to all non-clients and all clients except the client that sends the IBGP route.
Route update sent by BGP
Route update reflected by a BGP RR
AS 100
10.0.3.0/24
10.0.3.0/24

## Slide 42: Reflection Rule Example (2)
Pay attention to the difference between "reflection" and "sending".
"Sending" refers to traditional BGP route transmission (scenario where the RR does not exist).
"Reflection" refers to route transmission performed by an RR in compliance with route reflection rules. The RR inserts special path attributes into the reflected routes.
Rule 3
Client
AS 200
R1
R2
R4
R5
R3
RR
Route update sent by BGP
Route update reflected by a BGP RR
If a route is learned from an EBGP peer, the route is advertised to all clients and non-client IBGP peers.
AS 100
10.0.1.0/24
Notes: When reflecting routes, the RR does not modify the following BGP path attributes: Next_Hop, AS_Path, Local_Preference, and MED. If the RR modifies these attributes, routing loops may occur.

## Slide 43: Routing Loop Prevention in RR Scenarios
RR deployment breaks the split horizon rule, which may cause routing loops. To prevent routing loops, the RR adds two special path attributes to BGP routes:
  Originator_ID
  Cluster_List
Originator_ID and Cluster_List are optional transitive attributes.
AS 200
RR
R3
R2
Client
IBGP
R1
Route update sent by BGP
Route update reflected by a BGP RR
RR
1
2
3
BGP route reflection may cause routing loops.

## Slide 44: Originator ID
When reflecting a BGP route, an RR adds the Originator_ID attribute to the reflected route. The Originator_ID attribute value is the router ID of the BGP router that advertises the route in the local AS.
If multiple RRs exist in an AS, the Originator_ID attribute is created by the first RR and is not changed by subsequent RRs (if any).
When a BGP router receives an IBGP route with the Originator_ID attribute and the Originator_ID attribute value is the same as its router ID, the BGP router ignores the route update.
After R3 receives the BGP route 10.0.2.0/24 from R2, it adds the Originator_ID 10.0.2.2 to the route before reflecting the route to R1. After receiving the route, R1 reflects the route with the Originator_ID attribute to R2. After R2 receives the route, it finds that the Originator_ID attribute contains its own router ID and ignores the route update.
RR
BGP route 10.0.2.0/24
Originator_ID 10.0.2.2
RR
R1
R3
R2
Router ID 10.0.2.2
1
2
3
10.0.2.0/24
BGP route 10.0.2.0/24
Originator_ID 10.0.2.2
Route update sent by BGP
Route update reflected by a BGP RR
IBGP peer

## Slide 45: RR Cluster
Each RR cluster consists of an RR and clients. An AS can have multiple RR clusters, as shown in the following figure.
Each cluster has a unique cluster ID (Cluster_ID, which is the BGP router ID of an RR by default).
Before an RR reflects a route, the RR places the local Cluster_ID on top of the Cluster_List.
When an RR receives a BGP route carrying the Cluster_list attribute and the Cluster_ID of the RR is contained in the Cluster_List attribute, the RR considers that a loop occurs for the route and ignores the route update.
R1
R2
R3
Client
RR
Client
RR
IBGP
IBGP
RR cluster 1
RR cluster 2

## Slide 46: Cluster_List
A route is sent from R2 to R1. When reflecting the route to R3, R1 adds the Originator_ID and Cluster_List (10.0.1.1) to the route. When R3 reflects the route to R4, the Cluster_List value is 10.0.3.3 10.0.1.1. When R4 reflects the route to R1, the Cluster_List value is 10.0.4.4 10.0.3.3 10.0.1.1.
When R4 reflects the route to R1, R1 finds that the Cluster_List contains its own Cluster_ID and determines that a loop exists. Therefore, R1 ignores the route update.
Route update sent by BGP
Route update reflected by a BGP RR
RR
R1
R2
R3
RR
Originator_ID 10.0.2.2
Cluster_List 10.0.1.1
Originator_ID 10.0.2.2
Cluster_List 10.0.3.3 10.0.1.1
RR
Originator_ID 10.0.2.2
Cluster_List 10.0.4.4 10.0.3.3 10.0.1.1
R4
1
2
3
4
AS 200
The router IDs of all devices are 10.0.x.x, where x indicates the device ID.

## Slide 47: Example of RR Application
AS 200
R1
R2
AS 100
10.0.1.0/24
R4
R5
R3
Route update sent by BGP
Route update reflected by a BGP RR
RR
EBGP
IBGP
IBGP
IBGP
R1 advertises the route 10.0.1.0/24 to BGP. R2 learns the route from R1 and advertises the route to R3. However, the IBGP route learned by R3 from R2 cannot be advertised to R4 or R5 because of the split horizon rule. Therefore, you can configure R3 as an RR and configure R4 and R5 as clients so that R4 and R5 can learn the BGP route 10.0.1.0/24.

## Slide 48: BGP Configuration
[Huawei-bgp] peer {group-name | ipv4-address } reflect-client
Specify an RR and its client.
By default, the RR and its client are not configured.
[Huawei-bgp] reflector cluster-id cluster-id
Configure the cluster ID of the RR.
By default, each RR uses its router ID as the cluster ID.

## Slide 49: Configuration Example (1)
The IP address of Loopback0 on a device is 10.0.x.x/32, where x is the device ID. All devices use the address of Loopback0 as the BGP router ID.
R1, R2, and R3 belong to AS 100. OSPF runs in AS 100, and IP addresses of all directly connected interfaces are advertised to OSPF.
In AS 100, the IP address of the loopback interface is used as the source address for IBGP update. R2 functions as the RR, and R3 functions as the client.
R4 belongs to AS 200 and uses the IP address of the interconnected interface to establish an EBGP peer relationship with R3. R4 advertises 10.4.4.0/24 to BGP.
[R1] bgp 100
[R1-bgp] router-id 10.0.1.1
[R1-bgp] peer 10.0.2.2 as-number 100
[R1-bgp] peer 10.0.2.2 connect-interface LoopBack0
R1 configuration:
[R2] bgp 100
[R2-bgp] router-id 10.0.2.2
[R2-bgp] peer 10.0.1.1 as-number 100
[R2-bgp] peer 10.0.1.1 connect-interface LoopBack0
[R2-bgp] peer 10.0.3.3 as-number 100
[R2-bgp] peer 10.0.3.3 connect-interface LoopBack0
[R2-bgp] peer 10.0.3.3 reflect-client
R2 configuration:
AS 100
EBGP Peer
AS 200
IBGP Peer
R1
R2
R3
R4
10.0.34.3/24
OSPF
10.0.34.4/24
10.4.4.0/24
RR
Client
IBGP Peer

## Slide 50: Configuration Example (2)
The IP address of Loopback0 on a device is 10.0.x.x/32, where x is the device ID. All devices use the address of Loopback0 as the BGP router ID.
R1, R2, and R3 belong to AS 100. OSPF runs in AS 100, and IP addresses of all directly connected interfaces are advertised to OSPF.
In AS 100, the IP address of the loopback interface is used as the source address for IBGP update. R2 functions as the RR, and R3 functions as the client.
R4 belongs to AS 200 and uses the IP address of the interconnected interface to establish an EBGP peer relationship with R3. R4 advertises 10.4.4.0/24 to BGP.
R3 configuration:
[R4] bgp 200
[R4-bgp] router-id 10.0.4.4
[R4-bgp] peer 10.0.34.3 as-number 100
[R4-bgp] network 10.4.4.0 24
R4 configuration:
AS 100
EBGP Peer
AS 200
IBGP Peer
R1
R2
R3
R4
10.0.34.3/24
OSPF
10.0.34.4/24
10.4.4.0/24
RR
Client
IBGP Peer
[R3] bgp 100
[R3-bgp] router-id 10.0.3.3
[R3-bgp] peer 10.0.2.2 as-number 100
[R3-bgp] peer 10.0.2.2 connect-interface LoopBack0
[R3-bgp] peer 10.0.34.4 as-number 200

## Slide 51: Configuration Example (3)
Check the BGP route 10.4.4.0/24 on R3 and R1.
[R3-bgp]display bgp routing-table 10.4.4.0 24
BGP local router ID : 10.0.3.3
Local AS number : 100
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.4.4.0/24:
From: 10.0.34.4 (10.0.4.4)
Route Duration: 00h04m36s
Direct Out-interface: GigabitEthernet0/0/1
Original nexthop: 10.0.34.4
Qos information : 0x0
AS-path 200, origin igp, MED 0, pref-val 0, valid, external, best, select, active, pre 255
Advertised to such 1 peers:
10.0.2.2
[R1]display bgp routing-table 10.4.4.0 24
……….
BGP routing table entry information of 10.4.4.0/24:
From: 10.0.2.2 (10.0.2.2) #The route is originated from R2.
Route Duration: 00h00m19s
Relay IP Nexthop: 10.0.12.2
Relay IP Out-Interface: GigabitEthernet0/0/0
Original nexthop: 10.0.34.4 # The next-hop address remains unchanged.
Qos information : 0x0
AS-path 200, origin igp, MED 0, localpref 100, pref-val 0, valid, internal, best, select, active, pre 255, IGP cost 3
Originator: 10.0.3.3 #The route is originated from 10.0.3.3.
Cluster list: 10.0.2.2 #Cluster_ID is the router ID of R2.
Not advertised to any peer yet

## Slide 52
(Single) What is the type of the AS_Path attribute? ( )
  Optional transitive
  Optional non-transitive
  Well-known mandatory
  Well-known discretionary
(Essay) What is the function of MED? Can the MED be transmitted across ASs?
(Essay) Which path attributes are used by an RR to prevent routing loops?
Notes: C
When the local AS has multiple ingresses, the MED can be used to determine the path through which other ASs enter the local AS. The MED is an optional non-transitive attribute and cannot be transmitted across ASs.
Originator_ID and Cluster_ID

## Slide 53
BGP carries various path attributes when advertising routes. These attributes describe route characteristics and affect BGP route selection in some scenarios.
BGP path attributes are classified into well-known and optional attributes. All BGP routers must identify well-known attribute. Optional attributes do not need to be identified by all BGP routers.
To solve the problem of IBGP split horizon, you can use full-mesh IBGP connections. However, a large number of IBGP peer relationships need to be maintained. You can deploy RRs to reduce the number of IBGP peer relationships.
To prevent routing loops during RR deployment , BGP adds two path attributes: Originator_ID and Cluster_ID.