## Slide 1
Lu Yueyue/lwx445705
2020-04
New

## Slide 2: MSTP Implementation and Configuration

## Slide 3
The Rapid Spanning Tree Protocol (RSTP), an enhancement to the Spanning Tree Protocol (STP), allows for fast network topology convergence. When RSTP/STP runs on a VLAN-based network, all VLANs on a local area network (LAN) use the same spanning tree. The blocked link does not carry any traffic, and traffic cannot be load balanced among VLANs. As a result, the link bandwidth usage and device resource usage are low.
To offset disadvantages of RSTP/STP, IEEE introduced the Multiple Spanning Tree Protocol (MSTP) in 2002, which is standardized as IEEE 802.1s. MSTP is compatible with STP and RSTP. Multiple loop-free trees are set up to prevent broadcast storms and implement redundancy.
This document describes the improvements of MSTP compared with RSTP/STP, basic concepts and working mechanism of MSTP, and MSTP configurations.

## Slide 4
Upon completion of this course, you will be able to:
  Describe weaknesses of RSTP/STP.
  Describe MSTP improvements compared with RSTP/STP.
  Describe concepts of MSTP.
  Describe the working mechanism of MSTP.
  Complete basic MSTP configurations.

## Slide 5
Introduction to MSTP
Basic Concepts of MSTP
Working Mechanism of MSTP
MSTP Configurations

## Slide 6: Disadvantages of RSTP/STP (1)
SW2
SW3
SW1
(root bridge)
VLAN 2
LAN A
LAN B
VLAN 2
VLAN 3
VLAN 3
D
R
D
R
D
Disadvantage 1: Traffic Cannot Be Load Balanced
Background:
SW3 is an access switch connected to a terminal network segment. SW3 is connected to SW1 and SW2 through two links, and all the links allow packets from VLAN 2 and VLAN 3 to pass through.
SW1 is configured as the gateway of terminals in VLAN 2 and SW2 as the gateway of terminals in VLAN 3. Terminals in VLAN 2 and VLAN 3 are required to use different links to connect to the corresponding gateways.
Issue:
If there is only one spanning tree on the network and we assume that the port connecting SW3 to SW2 is a blocked port, data of VLAN 2 and VLAN 3 can be transmitted to aggregation switch through only one link. This means that traffic cannot be load balanced.
Gateway of VLAN 2
Gateway of VLAN 3
VLAN 2
VLAN 3
The link is blocked, and traffic cannot be load balanced.
R
Root port
D
Designated port
Blocked port

## Slide 7: Disadvantages of RSTP/STP (2)
SW2
SW3
SW1
(root bridge)
VLAN 2
LAN A
LAN B
VLAN 2
VLAN 3
VLAN 3
The path for terminals in VLAN 3 to access the gateway is the sub-optimal path.
D
R
D
R
D
Gateway of VLAN 2
Gateway of VLAN 3
Disadvantage 2: Layer 2 Sub-optimal Path
Background:
SW3 is an access switch connected to a terminal network segment. SW1 and SW2 are aggregation switches. SW1 is configured as the gateway of terminals in VLAN 2 and SW2 as the gateway of terminals in VLAN 3. All links are configured to allow packets from VLAN 2 and VLAN 3 to pass through.
After a single spanning tree is run, the loop is broken, and data of VLAN 2 and VLAN 3 is directly sent to SW1.
Issue:
The link between SW3 and SW2 is blocked, so the path from SW3 to the gateway is the sub-optimal path. The optimal path should be the path from SW3 to SW2.
R
Root port
D
Designated port
Blocked port

## Slide 8: Overview of MSTP
MSTP, which is standardized as IEEE 802.1s, is compatible with STP and RSTP. It can implement fast convergence and provide multiple redundant paths for forwarding data, effectively load balancing traffic for VLANs.
MSTP maps one or more VLANs to a Multiple Spanning Tree Instance (MSTI), and then calculates the spanning tree based on the MSTI. The VLANs mapped to the same MSTI share the same spanning tree.
SW2
SW3
SW1
D
R
D
R
D
MSTI 1: VLANs 1, 2, 3 , ..., 10
Root bridge
SW2
SW3
SW1
D
R
D
D
R
MSTI 2: VLANs 11, 12, 13 , ..., 20
Root bridge
R
Root port
D
Designated port
Blocked port
Data traffic
Data traffic
Notes: As shown in the figure, two spanning trees are generated after calculation.
  The spanning tree corresponding to MSTI 1 uses SW1 as the root bridge to forward packets of VLAN 1 to VLAN 10.
  The spanning tree corresponding to MSTI 2 uses SW2 as the root bridge to forward packets of VLAN 11 to VLAN 20.
  Packets of different VLANs are forwarded along different paths, implementing load balancing.
Note: The spanning tree runs based on MSTIs instead of VLANs.

## Slide 9
Introduction to MSTP
Basic Concepts of MSTP
Working Mechanism of MSTP
MSTP Configurations

## Slide 10: MST Region
MSTP network hierarchy:
  MSTP divides a switching network into multiple Multiple Spanning Tree (MST) regions, each of which has multiple spanning trees that are independent of each other.
MST region:
  An MST region contains multiple switches and their network segments.
  A LAN can comprise several MST regions that are directly or indirectly connected. You can add multiple switching devices to an MST region using MSTP configuration commands.
  An MSTP network contains one or more MST regions, and each MST region contains one or more MSTIs.
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: The switches in one MST region all share the following characteristics:
  MSTP-enabled
  Same region name
  Same VLAN-MSTI mappings
  Same MSTP revision level

## Slide 11: MSTI
MSTI:
  An MST region can contain multiple spanning trees, each of which is called an MSTI.
  MSTIs are identified by IDs. The value ranges from 0 to 4094 on Huawei devices.
VLAN mapping table
  Each MST region has a VLAN mapping table. The VLAN mapping table maps VLANs to MSTIs.
  As shown in the figure, the VLAN mapping of MST region 4 is as follows:
    VLAN 1 is mapped to MSTI 1.
    VLAN 2 is mapped to MSTI 2.
    Other VLANs are mapped to MSTI 3.
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
SW1
SW2
SW4
SW3
A
B
D
C
MSTI 1
A
B
D
C
MSTI 2
A
B
D
C
MSTI 3
Root bridge
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: MSTI 0 exists by default. By default, all VLANs on Huawei switches are mapped to MSTI 0.
MSTP maps VLANs to MSTIs in the VLAN mapping table.
  Each VLAN can be mapped to only one MSTI. This means that traffic of a VLAN can be transmitted in only one MSTI. An MSTI, however, can correspond to multiple VLANs.

## Slide 12: CST
Common Spanning Tree (CST)
  A CST connects all MST regions on a switching network.
  The CST is calculated using a spanning tree protocol, with each MST region being considered as a single node.
  In the figure, the regions that are connected through dark blue thick lines form a CST.
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
CST
1
2
3
4
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
MSTP
Network

## Slide 13: IST
Internal Spanning Tree (IST)
  An IST resides within an MST region.
  An IST is a special MSTI with an MSTI ID of 0.
  In the figure, the switches that are connected through black thin lines in MST region 4 form an IST.
IST
1
2
3
4
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 14: CIST
Common and Internal Spanning Tree (CIST)
  A CIST connects all the switches on a switching network and is calculated using a spanning tree protocol.
  As shown in the figure, all ISTs and the CST form a CIST.
CIST
1
2
3
4
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 15: SST
Single Spanning Tree (SST)
  A switch running a spanning tree protocol belongs to only one spanning tree.
  An MST region has only one switch.
  As shown in the figure, a switch in MST region 3 forms an SST.
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 16: CIST Root, Regional Root, and Master Bridge
CIST root
  The CIST root is the root bridge of the CIST, for example, SW1 in the figure.
Regional root
  Regional roots are classified into IST and MSTI regional roots.
  The switches that are closest to the CIST root are IST regional roots, for example, SW2, SW3, and SW4 in the figure.
  An MSTI regional root is the root of the MSTI.
Master bridge
  The master bridge is the switch closest to the CIST root in a region, for example, SW1, SW2, SW3, and SW4 in the figure.
  If the CIST root is in an MST region, the CIST root is the master bridge of the region.
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
SW1
SW2
SW3
SW4
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: The master bridge consists of the CIST root and the IST regional root.

## Slide 17: Summary
Role | Description
MST region | A switching network is divided into multiple regions. An MST region can contain one or more switches. The switches in the same MST region must be configured with the same region name, revision level, and VLAN mapping table.
MSTI | Instance-based spanning tree
VLAN mapping table | VLAN-MSTI mappings
CST | A spanning tree that connects all MST regions
IST | Internal spanning tree with the MSTI ID of 0 in an MST region
CIST | It connects all switching devices on a switching network.
SST | There is only one switching device in the MST region, and the switching device belongs to only one spanning tree.
CIST root | Root bridge of the CIST
IST regional root | Switch that is closest to the CIST root in an MST region
MSTI regional root | Root bridge in the MSTI
Master bridge | Switching device nearest to the CIST root, including the CIST root and IST regional root
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 18: MSTP Port Roles (1)
MST region 1
MSTP defines the following port roles:
  Root port, designated port, alternate port, backup port, master port, regional edge port, and edge port.
SW1 (master bridge)
SW2
SW3
D
D
R
R
A
D
B
Port Role | Description
Root port | A root port sends data to a root bridge and is the port closest to the root bridge.
Designated port | The designated port on a switch forwards BPDUs to a downstream switch.
Alternate port | Alternate ports provide an alternate path to the root bridge. This path is different from the path through the root port. An alternate port is blocked from sending BPDUs after a BPDU sent by another bridge is received.
Backup port | Backup ports provide a backup path to a segment already connected by a designated port. Backup ports are blocked from sending BPDUs after a BPDU sent by itself is received.
R
Root port
D
Designated port
A
Alternate port
B
Backup port
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: Except edge ports, all ports participate in MSTP calculation.
A port can play different roles in different MSTIs.

## Slide 19: MSTP Port Roles (2)
MSTP defines the following port roles:
  Root port, designated port, alternate port, backup port, master port, regional edge port, and edge port.
Port Role | Description
Master port | A master port is on the shortest path connecting MST regions to the CIST root. BPDUs of an MST region are sent to the CIST root through the master port. Master ports are special regional edge ports, functioning as root ports on ISTs or CISTs and master ports in instances.
Regional edge port | A regional edge port is located at the edge of an MST region and connects to another MST region or an SST.
SW1 (master bridge)
SW2
(IST regional root)
SW3
MST region 1
MST region 2
M
SW4
(CIST root)
MST region 3
RE
SW5
M
Master port
RE
Regional Edge port
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 20: MSTP Port Roles (3)
MSTP defines the following port roles:
  Root port, designated port, alternate port, backup port, master port, regional edge port, and edge port.
Port Role | Description
Edge port | An edge port is located at the edge of an MST region and does not connect to any switching device. Generally, edge ports are directly connected to terminals.
MST region 1
SW1 (master bridge)
SW2
SW3
E
PC
E
Edge port
MSTP Network Hierarchy
MSTP Ports
MST BPDUs

## Slide 21: MSTP Port States
MSTP port states are the same as those used in RSTP.
  Forwarding: A port in this state can send and receive BPDUs. It can also forward user traffic and learns MAC addresses.
  Learning: A port in this state can send and receive BPDUs. It learns MAC addresses but cannot forward user traffic.
  Discarding: A port in this state only receives BPDUs. It does not forward user traffic or learn MAC addresses.
MSTP Port State | Port Role
Forwarding | Root port, designated port, master port, and regional edge port
Learning | Root port, designated port, master port, and regional edge port
Discarding | Root port, designated port, master port, regional edge port, alternate port, and backup port
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: A port in Learning state learns MAC addresses from user traffic to construct a MAC address table.

## Slide 22: MST BPDUs
MSTP calculates spanning trees based on Multiple Spanning Tree Bridge Protocol Data Units (MST BPDUs).
Switches on an MSTP network transmit MST BPDUs to calculate spanning tree topologies, maintain network topologies, and communicate topology changes.
Protocol ID
Protocol Version ID
BPDU Type
CIST Flags
CIST Root ID
CIST External Path Cost
CIST Regional Root ID
CIST Port ID
Message Age
Max Age
Hello Time
Forward Delay
Version 1 Length=0
Version 3 Length
MST Configuration ID
CIST Internal Root Path Cost
CIST Bridge ID
CIST Remaining Hops
MSTI Configuration Messages
Format of an MST BPDU
First 36 bytes
Same as those of RST BPDUs
Starting from 37th byte
MSTP-specific fields
Version | Type | Name
0 | 0x00 | Configuration BPDU
0 | 0x80 | TCN BPDU
2 | 0x02 | RST BPDU
3 | 0x02 | MST BPDU
3
0x02
MSTP Network Hierarchy
MSTP Ports
MST BPDUs
Notes: The first 36 bytes of an MST BPDU are the same as those of an RST BPDU. Fields starting from the 37th byte of an MST BPDU are MSTP-specific. The MSTI Configuration Messages field consists of configuration messages of multiple MSTIs.
Main fields in an MST BPDU:
  Protocol Identifier: has 2 bytes and identifies a protocol.
  Protocol Version Identifier: has 1 byte and indicates the protocol version identifier.
    0: STP
    2: RSTP
    3: MSTP
  BPDU type: has 1 byte and indicates the BPDU type.
    0x00: Configuration BPDU for STP
    0x80: Topology Change Notification (TCN) BPDU for STP
    0x02: Rapid Spanning Tree (RST) BPDU or Multiple Spanning Tree (MST) BPDU
  CIST Flags: has 1 byte and indicates the CIST flag field.
  CIST Root Identifier: has 8 bytes and indicates the ID of the CIST root switch.
  CIST External Path Cost: has 4 bytes and indicates the total path cost from the MST region where the switch resides to the MST region where the CIST root switch resides. This value is calculated based on link bandwidth.

## Slide 23
Notes:   CIST Regional Root Identifier: has 8 bytes and indicates the ID of the regional root switch on the CIST. If the root is in this region, the CIST Regional Root Identifier is the same as the CIST Root Identifier.
  CIST Port Identifier: has 2 bytes and indicates the ID of the designated port in the IST.
  Message Age: has 2 bytes and indicates the lifecycle of a BPDU.
  Max Age: has 2 bytes and indicates the maximum lifecycle of a BPDU. If the Max Age timer expires, the link to the root is considered faulty.
  Hello Time: has 2 bytes and indicates the value of the Hello timer. The default value is 2s.
  Forward Delay: has 2 bytes and indicates the value of the Forward Delay timer. The default value is 15s.
  Version 1 Length: has 1 byte and indicates the BPDUv1 length, which has a fixed value of 0.
  Version 3 Length: has 2 bytes and indicates the BPDUv3 length.
  MST Configuration Identifier: has 51 bytes and indicates the MST configuration identifier, which has four fields.
  CIST Internal Root Path Cost: has 4 bytes and indicates the total path costs from the local port to the IST master. This value is calculated based on link bandwidth.
  CIST Bridge Identifier: has 8 bytes and indicates the ID of the designated switch in the CIST.
  CIST Remaining Hops: has 1 byte and indicates the number of remaining hops of a BPDU in the CIST.
  MSTI Configuration Messages: has 16 bytes and indicates an MSTI configuration message. Each MSTI configuration message occupies 16 bytes. If there are n MSTIs, MSTI configuration messages are n*16 bytes long.

## Slide 24
Introduction to MSTP
Basic Concepts of MSTP
Working Mechanism of MSTP
MSTP Configurations

## Slide 25: MSTP Topology Calculation
MSTP topology calculation:
  MSTP can divide the entire Layer 2 network into multiple MST regions. The CST is calculated between regions, and the IST is generated in each region. The CST and ISTs constitute the CIST of the entire switching device network.
  Multiple spanning trees can be generated based on MSTIs in a region. Each spanning tree is called an MSTI.
Both the CIST and MSTIs are calculated based on vectors, carried in MST BPDUs. Devices exchange MST BPDUs to calculate the CIST and MSTIs.
  Vectors used in CIST calculation:
    {Root ID, external root path cost, regional root ID, internal root path cost, designated switch ID, designated port ID, receiving port ID }
  Vectors used in MSTI calculation:
    {Regional root ID, internal root path cost, designated switch ID, designated port ID, receiving port ID}
  The preceding vectors are listed in descending order of priority from left to right.
Notes: Vectors are described as follows:
  Root ID: identifies the root switch for the CIST.
    The root identifier consists of the priority value (16 bits) and MAC address (48 bits).
    The priority value is the priority of MSTI 0.
  External root path cost (ERPC): indicates the path cost from a CIST regional root to the root.
    ERPCs are the same on all switches in an MST region.
    If the CIST root is in an MST region, all ERPCs in that MST region are set to 0.
  Regional root ID: identifies the MSTI regional root.
    It consists of the priority value (16 bits) and MAC address (48 bits).
    The priority value is the priority of MSTI 0.
  Internal root path cost (IRPC): indicates the path cost from the local bridge to the regional root.
    The IRPC saved on a regional edge port must be greater than the IRPC saved on a non-regional edge port.

## Slide 26
Notes:   Designated switch ID: identifies the nearest upstream bridge on the path from the local bridge to the regional root (designated switch of the CIST or MSTI).
    If the local bridge is the root or the regional root, this ID is the same as the local bridge ID.
  Designated port ID: identifies the port on the designated switch connected to the root port on the local bridge.
    The designated port ID consists of the priority value (4 bits) and port number (12 bits).
    The priority value must be a multiple of 16.
  Receiving port ID: identifies the port receiving the BPDU.
    The receiving port ID consists of the priority value (4 bits) and port number (12 bits).
    The priority value must be a multiple of 16.
A smaller vector has a higher priority.
Vectors are compared based on the following rules:
  Root IDs
  ERPCs
  Regional root IDs
  IRPCs
  Designated switch IDs
  Designated port IDs
  Receiving port IDs
  If the vectors being compared are the same, the next vector in the list is compared. If the vectors being compared are different, the remaining vectors are not compared
If the priority of a vector carried in the configuration message of a BPDU received by a port is higher than the priority of the vector in the configuration message saved on the port, the port replaces the saved configuration message with the received one. In addition, the port updates the global configuration message saved on the device. If the priority of a vector carried in the configuration message of a BPDU received on a port is equal to or lower than the priority of the vector in the configuration message saved on the port, the port discards the BPDU.

## Slide 27: CIST Calculation
After comparing the vectors, the switch with the highest priority on the entire network is selected as the CIST root.
MSTP calculates an IST for each MST region, treats each MST region as a single device, and calculates a CST to interconnect MST regions. The CST and ISTs form a CIST for the entire network.
MST region 1
MST region 3
MST region 2
MST region 4
MSTP
Network
CIST
1
2
3
4

## Slide 28: MSTI Calculation
In an MST region, MSTP independently calculates an MSTI for each VLAN based on mappings between VLANs and MSTIs.
The calculation process is similar to that used by STP to calculate a spanning tree.
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
1
2
4
3
MSTI 1
1
2
4
3
MSTI 2
1
2
4
3
MSTI 3
Root bridge
MST region 4
MSTP
Network
Notes: MSTI characteristics:
  Spanning trees of MSTIs are independent of each other.
  The spanning tree calculation method of each MSTI is similar to that of STP.
  Spanning trees of MSTIs can have different roots and topologies.
  Each MSTI sends BPDUs in its spanning tree.
  The topology of each MSTI is determined using commands.
  A port can be configured with different parameters for different MSTIs.
  A port can play different roles or have different states in different MSTIs.
MSTP can calculate the root bridge or you can manually configure the root bridge or secondary root bridge for a specified spanning tree.
  A switch can function as a root bridge or a secondary root bridge in a spanning tree. It can also function as the root bridge or secondary root bridge of another spanning tree. In a spanning tree, a device can function as either the root bridge or secondary root bridge.
  In a spanning tree: Only one root bridge takes effect. If two or more root bridges are specified in a spanning tree, the device with the smallest MAC address is used.
  Multiple secondary root bridges can be specified. When the root bridge fails or is powered off, a secondary root bridge becomes the new root bridge unless a new root bridge is specified. If there are multiple secondary root bridges, the one with smallest MAC address becomes the root bridge of the spanning tree.

## Slide 29: MSTP Network Data Forwarding
On an MSTP network, a VLAN packet is forwarded as follows:
  Along MSTI in an MST region
  Along CST among MST regions
MST region 1
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MST region 3
VLAN 1 -> MSTI 1
MST region 2
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
MST region 4
VLAN 1 -> MSTI 1
VLAN 2 -> MSTI 2
Other VLANs -> MSTI 3
MSTP
Network
1
2
4
3
MSTI 2
1
2
3
MSTI 2
1
2
4
3
MSTI 2
Root bridge in VLAN 2
1
2
4
PC2
PC1
Data access for VLAN 2
Notes: Data transmission in VLAN 2 is used as an example.

## Slide 30
Introduction to MSTP
Basic Concepts of MSTP
Working Mechanism of MSTP
MSTP Configurations

## Slide 31: MSTP Configuration Commands
[Huawei] stp mode mstp
Configure a working mode of a switching device.
A switching device supports three working modes: STP, RSTP, and MSTP. By default, the device works in MSTP mode.
[Huawei] stp enable
Enable MSTP.
Enable STP/RSTP/MSTP on a switching device or an interface. By default, STP, RSTP, or MSTP is enabled globally and on an interface.
Therefore, to ensure rapid and stable spanning tree calculation, before enabling STP, RSTP, or MSTP, perform basic configurations on the switching device and its interfaces.
Notes: stp mode mstp
  MSTP can recognize RSTP BPDUs and, conversely, RSTP can recognize MSTP BPDUs. However, MSTP and STP cannot recognize each other's BPDUs. To enable devices running different spanning tree protocols to interwork with each other, interfaces of an MSTP-enabled switch connected to devices running STP automatically transition to STP mode; other interfaces continue to work in MSTP mode.

## Slide 32: Configuring and Activating an MST Region (1)
[Huawei] stp region-configuration
[Huawei-mst-region]
Enter the MST region view.
[Huawei-mst-region] region-name name
Configure the name of the MST region.
By default, the MST region name is the bridge MAC address of a switching device.
[Huawei-mst-region] instance instance-id vlan { vlan-id1 [ to vlan-id2 ] }
Configure the mapping between VLANs and MSTIs.
Map a VLAN to an MSTI. By default, all VLANs are mapped to the CIST, namely, MSTI 0.
Notes: stp region-configuration
  By default, three parameters of MST regions use default settings.
region-name name
  Specifies the region name of a switching device. The value is a case-sensitive string of 1 to 32 characters without spaces.
instance instance-id vlan { vlan-id1 [ to vlan-id2 ]
  instance-id specifies the ID of an MSTI. The value is an integer that ranges from 0 to 4094. The value 0 indicates the CIST.

## Slide 33: Configuring and Activating an MST Region (2)
[Huawei-mst-region] revision-level level
(Optional) Configure the revision level of the MST region.
[Huawei-mst-region] active region-configuration
Activate the configuration of the MST region.
Make the region name, VLAN mapping table, and MSTP revision level take effect.
Configure the revision level of the MST region for a switching device. By default, the revision level of an MST region is 0.
Notes: revision-level level
  level specifies the revision level of an MST region. The value is an integer that ranges from 0 to 65535.
  MSTP is a standard protocol; therefore, the MSTP revision level of a device is 0 by default. If the revision level of some devices from a specified manufacturer is not 0, you must change the value to 0 to facilitate tree calculation in an MST region.

## Slide 34: Optional MSTP Configuration Commands (1)
[Huawei] stp [ instance instance-id ] root { primary | secondary }
Configure the root bridge and secondary root bridge.
Configure the switch as the root bridge or secondary root bridge in a spanning tree.
Set the priority of the switching device in a spanning tree. By default, the priority of a switching device in a spanning tree is 32768.
[Huawei] stp [ instance instance-id ] priority priority
Set the priority of a switching device in a specified MSTI.
[Huawei] stp pathcost-standard { dot1d-1998 | dot1t | legacy }
Set the path cost of an interface in the specified MSTI.
Configure the path cost calculation method. By default, IEEE 802.1t is used to calculate the path cost.
[Huawei-GigabitEthernet0/0/1] stp [ instance instance-id ] cost cost
Set the path cost of a port in a spanning tree. By default, the path cost of a port in a spanning tree is the path cost corresponding to the port rate.
Notes: stp [ instance instance-id ] root { primary | secondary }
  instance instance-id specifies the ID of an MSTI. If instance instance-id is not specified, the device in MSTI 0 is a root bridge or a secondary root bridge.
  primary indicates that the device functions as the root bridge of a spanning tree. After the configuration is complete, the priority of the device is 0 and cannot be changed.
  secondary: indicates that the device functions as the secondary root bridge of a spanning tree. After the configuration is complete, the priority of the device is 4096 (this value cannot be modified).
stp [ instance instance-id ] priority priority
  priority specifies the priority of a switching device. A smaller priority value indicates a higher priority of the switching device. The value is an integer that ranges from 0 to 61440 and is a multiple of 4096, such as 0, 4096, and 8192. The default value is 32768.
stp pathcost-standard { dot1d-1998 | dot1t | legacy }
  dot1d-1998: uses the IEEE 802.1d-1998 standard to calculate the path cost.
  dot1t: uses the IEEE 802.1t standard to calculate the path cost. The value ranges from 1 to 200,000,000.
  legacy: uses the Huawei standard to calculate the path cost. The value ranges from 1 to 200,000.

## Slide 35: Optional MSTP Configuration Commands (2)
[Huawei-GigabitEthernet0/0/1] stp [ instance instance-id ] port priority priority
Set a priority for a port in an MSTI.
Sets the priority of a port in a spanning tree. By default, the priority of a port on a switching device is 128.
Notes: stp [ instance instance-id ] port priority priority
  priority: specifies the priority of a port when it participates in spanning tree calculation. The value is an integer that ranges from 0 to 240 and is a multiple of 16, such as 0, 16, and 32.

## Slide 36: Case: Single-Region Multi-Instance Configuration (1)
Scenario:
  To implement redundancy on a complex network, network designers tend to deploy multiple physical links between two devices, one of which is the primary link and the others are the backup. Loops may occur in this situation. To this end, MSTP can be deployed on the network to prevent loops.
  MSTP blocks redundant links on a Layer 2 network and trims the network into a loop-free tree. In addition, MSTP can be deployed to implement load balancing among VLANs.
Requirements:
  Configure MSTP on SW1, SW2, SW3, and SW4.
  To load balance traffic from VLANs 2 and 3, configure MSTP multi-instance.
  Configure a VLAN mapping table to associate VLANs with MSTIs.
  Configure the port connected to the PC as the edge port because the port does not need to participate in MSTP calculation.
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
192.168.1.1/24
192.168.2.1/24
Notes: Configure SW1 as the gateway of VLAN 2 (VLANIF 2: 192.168.1.254/24) and SW2 as the gateway of VLAN 3 (VLANIF 3: 192.168.2.254/24). In this way, PC1 can ping VLANIF 2 of SW1 and PC2 can ping VLANIF 3 of SW2.

## Slide 37: Case: Single-Region Multi-Instance Configuration (2)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
[SW1] vlan batch 2 to 3
[SW1] interface GigabitEthernet 0/0/1
[SW1-GigabitEthernet0/0/1] port link-type trunk
[SW1-GigabitEthernet0/0/1] port trunk allow-pass vlan 2 to 3
[SW1-GigabitEthernet0/0/1] quit
[SW1] interface GigabitEthernet 0/0/2
[SW1-GigabitEthernet0/0/2] port link-type trunk
[SW1-GigabitEthernet0/0/2] port trunk allow-pass vlan 2 to 3
[SW1-GigabitEthernet0/0/2] quit
SW1 configuration:
Configure interface-based VLAN assignment to implement Layer 2 communication.
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
Note: The configuration of SW2 is similar to that of SW1, and is not provided here.

## Slide 38: Case: Single-Region Multi-Instance Configuration (3)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
[SW3] vlan batch 2 to 3
[SW3] interface GigabitEthernet 0/0/1
[SW3-GigabitEthernet0/0/1] port link-type trunk
[SW3-GigabitEthernet0/0/1] port trunk allow-pass vlan 2 to 3
[SW3-GigabitEthernet0/0/1] quit
[SW3] interface GigabitEthernet 0/0/2
[SW3-GigabitEthernet0/0/2] port link-type trunk
[SW3-GigabitEthernet0/0/2] port trunk allow-pass vlan 2 to 3
[SW3-GigabitEthernet0/0/2] quit
[SW3] interface Ethernet 0/0/1
[SW3-Ethernet0/0/1] port link-type access
[SW3-Ethernet0/0/1] port default vlan 2
[SW3-Ethernet0/0/1] quit
SW3 configuration:
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
Note: The configuration of SW4 is similar to the configuration of SW3, and is not provided here.

## Slide 39: Case: Single-Region Multi-Instance Configuration (4)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
[SW1] stp region-configuration
[SW1-mst-region] region-name 1
[SW1-mst-region] instance 1 vlan 2
[SW1-mst-region] instance 2 vlan 3
[SW1-mst-region] active region-configuration
[SW1-mst-region] quit
Configure an MST region and mapping between VLANs and MSTIs on SW1.
Configure basic MSTP functions.
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
Note: The configurations of SW2, SW3, and SW4 are similar to the configuration of SW1, and are not provided here.
Notes: By default, the MSTP function is enabled on the device. If the MSTP function is not enabled, run the stp enable command to enable the MSTP function on the switching device or port.

## Slide 40: Case: Single-Region Multi-Instance Configuration (5)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
[SW1] stp instance 1 root primary
[SW2] stp instance 1 root secondary
Configure SW1 as the root bridge and SW2 as the secondary root bridge in MSTI 1.
Configure the root bridge and secondary root bridge for MSTI 1 and MSTI 2.
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
[SW1] stp instance 2 root secondary
[SW2] stp instance 2 root primary
Configure SW2 as the root bridge and SW1 as the secondary root bridge in MSTI 2.
Note: The configurations of SW2, SW3, and SW4 are similar to the configuration of SW1, and are not provided here.

## Slide 41: Case: Single-Region Multi-Instance Configuration (6)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
[SW3] interface Ethernet 0/0/1
[SW3-Ethernet0/0/1] stp edged-port enable
[SW3-Ethernet0/0/1] quit
Configure Ethernet0/0/1 on SW3 as an edge port.
Enable MSTP and configure the port connected to the PC as the edge port.
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
MST region 1
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
Note: The edge port configuration of SW4 is similar to that of SW3, and is not provided here.

## Slide 42: Verifying the Configuration (1)
[SW1] display stp brief
MSTID Port Role STP State Protection
0 GigabitEthernet0/0/1 DESI FORWARDING NONE
0 GigabitEthernet0/0/2 ROOT FORWARDING NONE
1 GigabitEthernet0/0/1 DESI FORWARDING NONE
1 GigabitEthernet0/0/2 DESI FORWARDING NONE
2 GigabitEthernet0/0/1 ROOT FORWARDING NONE
2 GigabitEthernet0/0/2 DESI FORWARDING NONE
[SW2] display stp brief
MSTID Port Role STP State Protection
0 GigabitEthernet0/0/1 ROOT FORWARDING NONE
0 GigabitEthernet0/0/2 ALTE DISCARDING NONE
1 GigabitEthernet0/0/1 ROOT FORWARDING NONE
1 GigabitEthernet0/0/2 DESI FORWARDING NONE
2 GigabitEthernet0/0/1 DESI FORWARDING NONE
2 GigabitEthernet0/0/2 DESI FORWARDING NONE
[SW3] display stp brief
MSTID Port Role STP State Protection
0 Ethernet0/0/1 DESI FORWARDING NONE
0 GigabitEthernet0/0/1 DESI FORWARDING NONE
0 GigabitEthernet0/0/2 DESI FORWARDING NONE
1 Ethernet0/0/1 DESI FORWARDING NONE
1 GigabitEthernet0/0/1 DESI FORWARDING NONE
1 GigabitEthernet0/0/2 ROOT FORWARDING NONE
2 GigabitEthernet0/0/1 ALTE DISCARDING NONE
2 GigabitEthernet0/0/2 ROOT FORWARDING NONE
[SW4] display stp brief
MSTID Port Role STP State Protection
0 Ethernet0/0/1 DESI FORWARDING NONE
0 GigabitEthernet0/0/1 ROOT FORWARDING NONE
0 GigabitEthernet0/0/2 DESI FORWARDING NONE
1 GigabitEthernet0/0/1 ALTE DISCARDING NONE
1 GigabitEthernet0/0/2 ROOT FORWARDING NONE
2 Ethernet0/0/1 DESI FORWARDING NONE
2 GigabitEthernet0/0/1 DESI FORWARDING NONE
2 GigabitEthernet0/0/2 ROOT FORWARDING NONE

## Slide 43: Verifying the Configuration (2)
VLAN 2 -> MSTI 1
VLAN 3 -> MSTI 2
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
R
Root port
D
Designated port
A
Alternate port
D
D
D
R
R
D
D
A
R
Root bridge
SW3
SW4
SW1
GE0/0/1
PC1
E0/0/1
SW2
PC2
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
E0/0/1
192.168.1.1/24
192.168.2.1/24
R
D
D
D
R
A
D
R
D
Root bridge

## Slide 44
(Single) The following figure shows port roles of a switch running MSTP. What is the state of GigabitEthernet0/0/1 in MSTI 1? ( )
  Blocking
  Discarding
  Forwarding
  Learning
(TorF) The CIST is a tree that consists of the ISTs and CST. ( )
[Switch] display stp brief
MSTID Port Role
0 Ethernet0/0/1 DESI
0 GigabitEthernet0/0/1 ROOT
0 GigabitEthernet0/0/2 DESI
1 GigabitEthernet0/0/1 ALTE
1 GigabitEthernet0/0/2 ROOT
2 Ethernet0/0/1 DESI
2 GigabitEthernet0/0/1 DESI
2 GigabitEthernet0/0/2 ROOT
Notes: B
True

## Slide 45
On an MSTP network, one or more VLANs can be mapped to an MSTI, and MSTP calculates the spanning tree based on the MSTI. The MSTI is an instance-based spanning tree. MSTP maintains a spanning tree for each independent MSTI. The VLANs mapped to the same MSTI share the same spanning tree.
MSTP can implement the following functions on the Ethernet:
  Forms multiple loop-free trees to prevent broadcast storms and implement redundancy.
  Multiple spanning trees perform load balancing and transmit traffic in different VLANs along different paths.