## Slide 1
Datacom
V1.0
Shi Miaomiao/swx791350
2021.03.20
Zhu Shigeng/z00261992
New

## Slide 2: Enterprise Network and Solution Overview

## Slide 3
Nowadays, data has become a new factor of production, and data communications networks have become the foundation of digital society. How to design data communications networks according to enterprise service requirements is an important topic.
Generally, the entire data communications world is divided into the following parts: wide area network (WAN), metropolitan area network (MAN), campus network, and data center network (DCN). Network security is involved in all the preceding fields and needs to be considered in an end-to-end manner.
Enterprise WANs enable network interconnection across the country or even across the globe.
An enterprise MAN is a medium-scale computer network that connects multiple LANs in the same area. It provides network access for office campuses, schools, hospitals, and other organizations. It is located between the LAN and WAN and covers a geographic region of the size of a metropolitan area.
Enterprise campus networks can be classified into large and midsize campus networks and small and midsize campus networks based on the scale.
Enterprise DCNs implement access of servers and storage devices. Typically, enterprise DCNs can be divided into financial cloud data centers and e-Government cloud data centers by industry.

## Slide 4
Upon completion of this course, you will be able to:
  Know the definition of enterprise networks
  Understand the WAN, MAN, campus network, and DCN architecture
  Describe typical enterprise network scenarios
  Describe Huawei enterprise network solutions

## Slide 5
Enterprise Network Overview
Typical Enterprise Network Scenarios
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 6: Data Communications Network Builds the Foundation of Digital Society
DC
SD-WAN
Office
Online meeting
Manufacturing
Computing power
Enterprise
Individual
Carrier metro/backbone network
O&M
Security
Site
Home
Terminal

## Slide 7: Enterprise Network
MAN
WAN
DCN
Campus network
After more than 30 years of development, the network has laid a solid foundation for the intelligent society. With the acceleration of enterprise digitalization, enterprise networks need to carry more and more key services, playing an important role in the digitalization process.

## Slide 8: Enterprise Network Architecture
Branches, employees on business trips, and visitors
DCN
WAN
MAN
Campus network
Internet
WAN
A network that connects nodes at different levels, such as the headquarters, branches, data centers (DCs), and mobile offices, across a large geographical area through leased carrier links or self-built links.
A medium-scale network that connects multiple LANs in the same area.
MAN
A network used in the campus where we work and live.
Campus network
A network that connects to DC resources and provides IT services for enterprises.
DCN
National backbone network
Provincial backbone network
Municipal backbone network
County-level backbone network
Notes: Backbone network: a core network that connects primary nodes for network interconnection

## Slide 9: Enterprise WAN Overview
District/County core
County-level MAN
Government, finance, electric power, railway, civil aviation, and so on
Municipal core
Provincial core
WAN backbone network
Large enterprises build their own WANs to meet the interconnection requirements of nodes at different levels, such as the headquarters, branches, DCs, and mobile offices.
Typical industry WANs include government WANs, financial WANs, electric power communication networks, railway bearer networks, and civil aviation bearer networks.

## Slide 10: Enterprise MAN Overview
Campus network
Campus network
DC
Internet
Metro Core
Metro Aggregation
Metro Aggregation
Generally, the enterprise MAN adopts a hierarchical design. Based on the scale, the enterprise MAN is divided into the three-layer architecture (core layer-aggregation layer-access layer) or the two-layer architecture (core layer-access layer).
The enterprise MAN provides the access function for campus networks in the same area to implement communication between the campus networks, and connects to the enterprise WAN to implement cross-region communication on the enterprise network.
WAN

## Slide 11: Enterprise Campus Network Overview
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
Management and O&M zone
DC
An enterprise campus network uses a hierarchical and modular design. Based on the number of terminal users or NEs, campus networks can be classified into small-, medium-, and large-sized ones. A typical large-sized campus network consists of the following modules:
Egress zone: the border between the campus internal network and external network. It is used for internal users to access the public network and for external users to remotely access the internal network.
Core layer: the core of campus data switching that connects all components of the campus network, such as the DC, management and O&M zone, and campus egress.
Aggregation layer: forwards horizontal traffic between users and vertical traffic to the core layer. The aggregation layer can function as the switching core of a department or area and can connect more terminals to the network.
Access layer: provides various access modes for users and is the first network layer to which terminals connect.
Terminal layer: involves various terminals that access the campus network, such as PCs, printers, IP phones, mobile phones, and cameras.
DC: deploys servers and application systems to provide data and application services for internal and external users of an enterprise.
Management and O&M zone: deploys the network management system (such as the NMS and authentication server) and O&M system.

## Slide 12: Enterprise DCN Overview
Management and O&M zone
Test environment
zone 1
Test environment
zone 2
Production environment zone 1
Production environment zone 2
FW
FW
Leaf
FW
FW
WAN access zone
WAN
Switching core
Non-production extranet core
Internet
access zone
Campus access zone
Spine
VXLAN domain
VXLAN domain
VXLAN domain
VXLAN domain
Extranet
access zone
A DCN connects general-purpose computing, storage, and high-performance computing resources, carries communication between internal resources of the DC, and implements communication between the DC and external networks.
A mainstream DCN uses the spine-leaf architecture. Switches are connected through Layer 3 interfaces, and the underlay network runs a dynamic routing protocol. Traffic can be load balanced between spine and leaf nodes through equal-cost multi-path routing (ECMP), implementing a DCN that features high-bandwidth, non-blocking forwarding, and fast network convergence upon faults.
    To isolate services and tenants, VXLAN and EVPN technologies are deployed in DCs to build virtualized networks.
VTEP
Leaf
Leaf
Leaf
Spine
Spine
Spine
Border-Leaf
Border-Leaf
Border-Leaf
Border-Leaf
Production extranet core
Notes: DCNs do not have a fixed zone division mode. Different industries and enterprises have different area division modes.
The zone division in the slide uses the financial industry as an example:
  WAN access zone: connects to the WAN built by the enterprise.
  Campus access zone: accesses traffic from enterprise campus users.
  Extranet access zone: connects to external networks, such as networks of other enterprises and partners.
  Internet access zone: accesses user traffic from the Internet.
  Production environment zone: runs services.
  Test environment zone: provides services for external systems informally. Before a service is brought online to the production environment zone, the service is developed, tested, and verified in the test environment zone.

## Slide 13
Enterprise Network Overview
Typical Enterprise Network Scenarios
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 14: Education Network
P
P
P
Education backbone network
Higher education campus
Scientific research institutes
Provincial education MAN
Municipal education MAN
Primary/secondary education campus
County-level education MAN
Primary/secondary education campus
Primary/secondary education campus
Primary/secondary education campus
An education network is a basic network platform that provides services such as interconnection, resource sharing, and Internet access for education institutions, scientific research institutions, higher education campuses, and primary/secondary education campuses.
An education network can be divided into the education backbone network, education MAN, higher education campus network, and primary/secondary education campus network.
Education
Finance
Railway
Electric Power

## Slide 15: Education Backbone Network
P
P
PE
PE
PE
PE
PE
Higher education institution
Higher education institution
Higher education institution
Higher education institution
Higher education institution
P
P
International interconnection control center
Internet
The education backbone network connects universities, education institutions, and scientific research institutions across the country. As the upper-level network of the education MAN, the backbone network functions as the egress for the MANs to access external networks and the hub for communication between MANs.
Education
Finance
Railway
Electric Power

## Slide 16: Education MAN
Smart Education
DC
e-Schoolbag
Health
monitoring
Personnel locating
AR/VR
The education MAN implements interconnection between education administrative organizations and schools. It is a regional network platform that carries functions such as education information resource sharing and education information management.
The primary/secondary education campus network is not directly connected to the education backbone network due to its small scale. Instead, it is planned and constructed by the upper-level network management department and connected to the education MAN to implement full data convergence.
Education MAN
Center in district X
Center in district Y
Center in district Z
School
School
School
School
School
School
Distance education
AR
VR
Internet
CERNET
Municipal management center
Education
Finance
Railway
Electric Power

## Slide 17: Higher Education Campus Network
School campus DC
Internet
CERNET
Private line or VPN link
Main campus
Branch campus
Dormitory
Lecture hall
Library
Digital library
Distance education
Virtual experiment
Mobile learning
The campus network is a computer network that provides teaching, scientific research, and comprehensive information services for teachers and students (including their family members and visitors).
The higher education campus network refers to the campus network of higher education institutions.
The higher education campus network is generally divided into dormitories, living areas, teaching areas, and public areas. It provides wired and wireless network access services to help the campus enter the digital era and improve talent cultivation and innovation capabilities.
Internet
Education
Finance
Railway
Electric Power
School campus network management
center
Multimedia classroom
Teaching building
Notes: China Education and Research Network (CERNET): a nationwide education and research computer network that is funded by the Chinese government and directly managed by the Chinese Ministry of Education. It is constructed and operated by Tsinghua University and the other leading Chinese universities.

## Slide 18: Financial Backbone Network Architecture
To meet their own business development and operation management requirements, financial enterprises generally build their own backbone networks across the country to support the development of enterprise informatization and core services.
The DC and its branches are connected through the backbone network. Network services are mainly centralized in the DC. Users are widely distributed inside and outside the banks. Branches access the DC of the head office through the backbone network.
P
P
P
DC A
DC B
DC N
Level-1 branch
Level-2 branch
Sub-branch
Education
Finance
Railway
Electric Power
Financial backbone network

## Slide 19: Financial Service Transport
From the perspective of service transport, the backbone network of financial enterprises has two construction models. One is two physical networks (as shown in the left figure) that carry different types of services independently, and the other is one single physical network that carries converged services.
In the first model, networks that carry different services do not communicate with each other. A small number of services that need to be accessed across networks are accessed through firewalls.
Production service zone
Production service zone
OA service zone
OA service zone
Level-1 branch
Level-1 branch
Carries production and critical services.
Carries services such as office and video services.
DC A
DC B
DC A
DC B
Level-2 branch
Education
Finance
Railway
Electric Power

## Slide 20: Railway Data Communications Network
Core node
Aggregation node
Access node
Backbone network
Regional network
Ticket hall
OA
Video conferencing
PIS
GSM-R/wireless
CTC/RBC/TCC
The railway system in China is used as an example.
In the railway system, the network provides unified transmission services for signaling, dispatching, ticketing, integrated services, and GSM-R services.
The railway data communications network uses a two-layer architecture:
  A backbone network consisting of multiple high-performance core routers located at regional nodes and railway bureaus.
  A regional network set by each railway bureau. The regional network is connected to the backbone network through the backbone network's regional node of the local railway bureau to implement communication between railway bureaus.
As an independent autonomous system, the backbone network forwards traffic between the head office and railway bureaus and between railway bureaus.
Each railway bureau is configured with a backbone network access node and multiple backbone network forwarding nodes. The head office node functions as the service aggregation node of the entire railway system and does not forward traffic.
Education
Finance
Railway
Electric Power
Head office node
Regional node 1
Regional node 2
Regional node N
Notes: Generally, the regional nodes of the backbone network are deployed in the equipment rooms of each railway bureau.
GSM-R: Global System for Mobile Communications - Railway
CTC: Centralized Traffic Control
RBC: Radio Block Center
PIS: Passenger Information System
TCC: Track Communications Center

## Slide 21: Railway Regional Data Network
Core node
Aggregation node
Access node
Backbone network
In this example, the core node consists of two routers, which are respectively connected to the regional node of the local railway bureau and another geographically adjacent regional node.
An aggregation node is directly connected to two routers of a core node. The aggregation node and the core node can form a mesh or partial mesh connection. Two access routers should be configured on each access node of the railway bureau; dispatch station, comprehensive maintenance center, and train detection base for the passenger dedicated line; and general packet radio service (GPRS). The access routers can be directly connected to the core nodes of the local network.
Two routers on each access node (for a station or depot) can be directly connected to two routers of the same aggregation node or two geographically adjacent aggregation nodes.
Regional node 1
Regional node 2
Education
Finance
Railway
Electric Power
Notes: General Packet Radio Service (GPRS).

## Slide 22: Integrated Data Network for the Electric Power Industry
Provincial access network
P
P
P
Backbone layer
P
P
P
Provincial border
Backbone network
PE
PE
CE
Municipal access network
PE
CE
DR center
DR center
DR center
Provincial DC
Provincial companies, subordinate organizations, municipal companies, county access networks, MANS of municipal companies, and so on
Core layer
The electric power industry in China is as an example.
The electric power industry network is divided into two independent networks based on the carried services: dispatching network and integrated data network.
The dispatching network, as one of the core networks for electric power informatization, mainly carries power-related service control systems.
The integrated data network carries applications such as OA, production management, lightning weather information, and remote monitoring of unmanned substations. It is physically independent and parallel with the power dispatching network.
The integrated data network adopts a multi-level architecture, including the national backbone network, provincial integrated data network, and municipal integrated data network. The national backbone network is divided into the core layer (consisting of multiple core nodes deployed in the country) and the backbone layer (consisting of backbone nodes distributed in provincial companies in the country).
The data networks of provincial companies and branches are connected to the provincial border nodes of the backbone network to implement communication between provincial networks.
Education
Finance
Railway
Electric Power

## Slide 23
Enterprise Network Overview
Typical Enterprise Network Scenarios
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 24: Industry Digital Transformation, Improving Production Efficiency and Customer Satisfaction
Digital OA
Digital manufacturing
Source: According to Worldwide Digital Transformation 2019 Predictions released by IDC, "at least 55% of organizations will be digitally determined by 2020."
Source: IDC's 2018 manufacturing industry survey results shows that 84.9% manufacturing enterprises are undergoing digital transformation, driving business model innovations and reshaping the business ecosystem.
Digital education
Source: Gartner's 2019 CIO Agenda: Higher Education Industry Insights reveals that 86% of higher education CIOs would regard IT as a key factor in enabling education business transformation.
Always-online mass terminals/sensors, real-time production data collection, and automatic and precise control
All-wireless access, OA anytime and anywhere, one-click conference scheduling using an app, and automatic adjustment of lighting and temperature
Change from stuffing the duck to immersion, high-quality teaching resources on demand, and real-world teaching
DC
WAN
Campus Network

## Slide 25: In the Digital Era, How Campus Networks Support Digital Transformation Across Industries?
On-demand services
Quick service deployment and adjustment
Rapid rollout of value-added applications
Access anytime, anywhere
High-quality service transport
Ubiquitous connectivity
Accurate measurement and evaluation of user experience
AI-powered automatic adjustment of resource allocation
Perceptible experience
Service-based configuration delivery
Quick and accurate fault locating
Easy O&M
DC
WAN
Campus Network

## Slide 26: Service Requirements and Challenges of Large- and Medium-Sized Campus Networks
Converged transport
Requirements:
Access terminals and services are diversified, and a converged transport network is required.
Challenges:
Wi-Fi and IoT services are independently planned, deployed, and managed. The overall network construction cost is high.
The workload of network management and O&M is heavy.
User experience awareness
Requirements:
Network O&M needs to be automated and intelligent to perceive user experience anytime and anywhere.
Challenges:
Service faults cannot be detected in a timely manner.
After a fault occurs, the fault cause is determined based on the O&M experience of professional personnel, and the fault cannot be quickly located.
The network cannot be automatically optimized.
Network automation
Requirements:
Networks need to be automated to cope with the complexity of deployment and policies caused by the surge of applications and services.
Challenges:
The workload is repetitive and heavy, and manual configuration is complex.
New services need to be configured on devices one by one, which is time-consuming and costly.
The workload of network policy deployment and adjustment is heavy.
DC
WAN
Campus Network

## Slide 27: Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Plug-and-play network devices, improving deployment efficiency
The network configurations of multiple sites are centrally delivered, reducing onsite configuration and commissioning workload and improving deployment efficiency.
The network is plug-and-play and able to be expanded on demand, requiring low costs for upgrades.
Centralized O&M on the cloud, simplifying O&M of multiple sites
Scattered campus branch networks are centrally managed on the cloud through the Internet, and automation tools for troubleshooting, monitoring, and other management operations are integrated, implementing remote automated O&M.
Open APIs, accelerating integration of business applications
With open APIs and big data analytics capabilities, multiple management systems can be combined and interconnected to achieve unified network management. More value-added applications are available, leading enterprises into digital transformation.
Sites' network devices
Unified management and centralized configuration
Plug-and-play,
on-demand expansion
Centralized management of multiple branches on the cloud and remote automatic O&M
Site network 1
Site network 2
Site network N
Site network
Site network
Site network
Open and big data analytics capability
Cloud management platform
DC
WAN
Campus Network

## Slide 28: Development of Enterprise SD-WAN Technologies
Migration of enterprise services to the cloud
Enterprise services are migrated to the cloud, and enterprise egress traffic increases sharply.
Proportion of egress traffic to total traffic on the enterprise network
Source: IDC
Intelligence
Cloudification
Video
Mobility
2016
2020
20%
80%
Emergence of Software defined networking (SDN)
Unified management and centralized configuration
High-speed development of the Internet
Rapidly narrowing gap between the quality of the Internet and traditional private lines
The coverage and network performance of the Internet are continuously improving, and the gap between the quality of the Internet and traditional private lines is narrowing rapidly. As such, more and more enterprises and organizations are using the Internet for interconnection.
Traditional carrier private lines/MPLS
Internet
SDN introduces a new role, that is, the centralized controller, so that it can not only understand the network requirements proposed by the administrator, but also fully manage and configure the physical network, implementing automatic deployment and fast provisioning of applications on the network.
The business and technology trends related to enterprise WANs are changing rapidly, which will in turn have a profound impact on the development of enterprise WANs.
DC
WAN
Campus Network

## Slide 29: Service Requirements and Challenges of Multi-Campus Network Interconnection
Service provisioning period
Service experience
Management and O&M
Unified management
Branch interconnection cost
Requirements:
The cost of WAN interconnection between branches needs to be reduced.
Challenges:
Carriers' transmission private lines or MPLS VPN private lines are of high quality but expensive.
Requirements:
The network deployment efficiency needs to be improved and the service provisioning period needs to be shortened.
Challenges:
It takes a long time to provision traditional private lines.
Service provisioning is mainly performed by network engineers on site, which has high skill requirements and low efficiency.
Requirements:
The application identification capability needs to be enhanced to ensure key service experience.
Challenges:
Different enterprise applications have different requirements on link quality.
Traditional private lines cannot detect the application status and cannot guarantee key services at any time.
Requirements:
Visualized O&M is required to simplify management and O&M.
Challenges:
CLI-based O&M is inefficient and lacks visualized O&M methods.
If an enterprise has a large number of branches, onsite O&M will increase costs.
Requirements:
LAN-side and WAN-side services need to be managed in a unified manner.
Challenges:
Unified configuration management and O&M cannot be implemented.
DC
WAN
Campus Network

## Slide 30: Cloud + Intelligence, Accelerating HPC
Supercomputing — the core of high-performance computing (HPC) — provides the computing power needed to drive development of the digital economy and plays a key role in numerous scientific and technological fields.
Speed is still the primary factor in supercomputing realizing faster and more accurate computing and simulation. This is where cloud and intelligence come in. In addition, the supercomputing of cloudification and artificial intelligence is gradually integrated, which poses higher requirements on the DCN that carries supercomputing services.
Weather forecast
21.8% -> 90%
Weather forecast accuracy
Life science
13 years -> 1 day
Gene sequencing duration
Drug R&D
500 days -> 100 days
New drug R&D and identification
Supercomputing center
Cloud
High-performance computing
Intelligence
Network requirements
Cloud-network synergy
Fast deployment
High-speed interconnection
Zero delay
Low packet loss rate
DC
WAN
Campus Network

## Slide 31: Three IT transformations, Driving Full Ethernet Evolution of DCNs
With the development of enterprise digital transformation, data has become a key production factor. DCs are responsible for data computing, storage, and forwarding, and are the most critical digital infrastructure in the new infrastructure. The IT architecture, computing, and storage of DCs are undergoing significant changes, driving DCNs to evolve from the multi-protocol mode to the full-Ethernet mode.
100x
Scale
Centralized -> Distributed
IT architecture
Computing unit
Storage media
PCIE
IB
Ethernet
CPU/GPU Ethernet interconnection
100x
Performance
or
AS-IS
TO-BE
1000x
Capacity
SCSI
NVMe
FC (32G)
RoCE (400G)
PCIe is removed
HDD -> SSD
All-flash storage Ethernet interconnection
Server Ethernet interconnection
Ethernet
Ethernet
Centralized
Distributed
DC
WAN
Campus Network
Notes: InfiniBand (IB): an input/output (I/O) switching technology that uses a central InfiniBand switch to establish a single link between remote storage devices, networks, and servers as well as to direct traffic. It has a compact structure, greatly improving system performance, reliability, and effectiveness, and relieving data traffic congestion between hardware devices.
Remote Direct Memory Access over Converged Ethernet (RoCE): a network protocol that allows remote direct memory access (RDMA) over the Ethernet. There are two RoCE versions: RoCEv1 and RoCEv2. RoCEv1 is a data link layer protocol that allows any two hosts in the same Ethernet broadcast domain to communicate with each other. RoCEv2 is a network layer protocol and its packets can be routed.

## Slide 32: Three Challenges Facing DCN Full-Ethernet Evolution
More complex for large-scale network O&M
Zero packet loss required for dual-active storage
Zero packet loss required for high-performance computing
The packet loss rate increases exponentially with the increase of network nodes on traditional Ethernet.
Traditional Ethernet lacks effective O&M methods,
and the network is too complex to be handled manually.
0.2–0.3% packet loss rate
The delay increases in intra-city (long distance) transmission, and it is difficult to perform flow control across DCNs on traditional Ethernet.
0.15%
0.02%
>70 km
DC A
DC B
1000 nodes, million-level configuration
DC
WAN
Campus Network

## Slide 33: 5G + Cloud, Increasingly Complex WAN Transport Services
With the advent of the 5G and cloud era, various innovative services such as VR/AR, live streaming, and autonomous driving are emerging. The traffic on the entire network increases explosively, and the dynamic complexity of services also increases the complexity of the entire network.
Enterprise campus, DC, and branch
WAN
MANs at all levels
4K
DC
WAN
Campus Network

## Slide 34: Service Requirements and Challenges Facing the WAN
Slow service provisioning
High SLA requirements
Complex O&M
The network passively adapts to various new services, such as enterprise private line services. Service provisioning is time-consuming and customer response is slow.
With the development of new services such as enterprise application migration to the cloud, network traffic in carriers' pipes is more dynamic and unpredictable. Traditional network planning and optimization have poor adaptability, and service SLA assurance faces great challenges.
As the network scale and complexity increase, the O&M complexity also increases. Carriers urgently need to deploy automation measures to reduce the skill requirements for O&M personnel and effectively control the OPEX in the long term.
Network policy
Service requirements
< 1s
10s
Failover time
L3VPN
L2VPN
DC
WAN
Campus Network
Notes: Service Level Agreement (SLA): an agreement between a service provider and a user. The SLA defines the service type and quality provided by the service provider for the user, and the commitment to the performance and reliability of the user assurance service. For example, the SLA ensures that the service reliability is higher than 99.99%, the fault response time is within 30 minutes.
Operating Expense (OPEX): the sum of the maintenance cost, marketing expense, labor cost, and depreciation expense during the enterprise operations.

## Slide 35
Enterprise Network Overview
Typical Enterprise Network Scenarios
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 36: iMaster NCE Builds an Autonomous Driving Network
Self-service
portal
Mobile
app
Third-party app
Cloud platform
WAN/DCI
DC Fabric
DC Fabric
SD-WAN
WAN/DCI
Application layer
Network
management and control layer
Network layer
Campus
Branch
CPE
CPE
AP
...
Manager
Controller
Analyzer
Campus
Branch
CPE
CPE
AP

## Slide 37: What Is iMaster NCE?
iMaster NCE is a network automation platform that integrates management, control, analysis, and AI capabilities.
3
4
2
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting
Automated + Intelligent
Manage + Control + Analyze
Plan + Construct + Maintain + Optimize
Unified data base
Centralized detection and locating
Full lifecycle management
Simulation/Verification/Monitoring/Optimization
Network management system
Controller
Analyzer
=
Autonomous driving network system
Network

## Slide 38: All-New iMaster NCE
DC
iMaster NCE-Fabric
Enterprise campus
iMaster NCE-Campus
SD-WAN
iMaster NCE-WAN
WAN transmission
iMaster NCE-T
IP WAN
iMaster NCE-IP

## Slide 39: One-Stop Autonomous Driving Solution for Campus Networks: CloudCampus
Automated network design, accurately matching service intents
Accurate conversion between service requirements and configuration commands through the network management platform
Automated network deployment, achieving minute-level rollout
Plug-and-play devices, automated deployment of physical networks
Network resource pooling, one network for multiple purposes, and automatic service provisioning
Intelligent policies (such as access policies, bandwidth, and priorities) based on virtual networks, security groups, and applications, implementing refined control
Analysis
Control
Design
Deploy
Policy
One-stop management platform
NETCONF/YANG
WAN/
Internet
Multi-service campus
Simple-service campus
Campus interconnection
OA VN
R&D VN
OA VN
R&D VN
Security group 1
Security group 2
Security group 4
Security group 5
Access policy
bandwidth
Priority
Automated intelligent O&M, improving network performance
Real-time experience visualization: network experience visualization at any moment, for any user, and in any area
Precise fault analysis: proactively identifies typical network problems and provides suggestions
Intelligent network optimization: predictive optimization of wireless networks based on historical data
Management
DC
WAN
Campus Network
Notes: In the campus network scenario, iMaster NCE-Campus is used as the controller.

## Slide 40: All-Scenario: Full Coverage from Single Campuses to Multi-Branch Interconnection Campuses
Multi-branch interconnection
Multi-service campus
Simple-service campus
Internet
Hotel reservation
Large enterprise
Primary/
Secondary education
Service center
Higher education and large enterprise
VN 1
VN 2
VN 3
Internet
MPLS
 | Simple-service Campus | Multi-service Campus | Multi-branch Interconnection
Network Characteristics | Small scale, simple services Large numbers of sites, with similar models | Large scale, complex services, and coexistence of multiple services | Multiple branch sites, which need to communicate with each other through hybrid WAN links
Typical Scenarios | Multi-branch small-sized enterprise campuses, such as hotels and primary/secondary schools | higher education institutions, governments, large enterprise campuses | Large enterprises, financial services outlets
DC
WAN
Campus Network

## Slide 41: Full Convergence: One Controller Manages both LAN and WAN Services
Huawei CloudCampus Solution integrates the configuration and management models of LAN and WAN services on the campus network. In addition to configuring and managing LAN services for campus networks, this solution can also manage WAN interconnection services, implementing integrated management of LAN and WAN services.
Simplified configuration
Easy deployment
Simplified O&M
Forwarding-control separation
Value extension
One set of controller manages only LAN or manages both LAN and WAN services
WAN side
LAN side (large or small- and medium-sized campus)
IPsec VPN
EVPN
Centralized management
GUI
GUI, flexible networking, device plug-and-play
Central management of the control plane implements flexibly control while improving scalability
Control plane
User plane
Regional controller
Visualized network service data for monitoring and analyzing the status of the entire network
Services provided by the carrier can be extended from WAN to LAN and even value-added services
WAN side
LAN side
MPLS
Internet
WAN side
LAN side
Real-time monitoring
Topology visualization
Various reports
Intelligent analysis
Wired
Wireless
WAN
DC
WAN
Campus Network

## Slide 42: SD-WAN Solution
Branch 2
Branch 1
Traditional network
Internet
LTE
MPLS
Public cloud
HQ/DC
RR
O&M
Deployment
Adjustment
Optimization
Visualization
Automation
Cost reduction
Reduced O&M cost
Improved enterprise WAN link utilization
Simplified O&M
Full-process automation, plug-and-play
Visualization of applications, branches, devices, and links
Optimized experience
Layer 3 to Layer 7 application identification based on application intelligent traffic steering
Intelligent A-FEC for optimized video transmission
Virtual network
Logical network based on inter-branch WAN links
Logical network-based routing and forwarding
Edge
Edge
IWG
Edge
Edge
XDSL/Ethernet
/LTE...
DC
WAN
Campus Network
Notes: Adaptive Forward Error Correction (A-FEC): The intelligent data analysis engine is used to adjust the FEC protection window and protection mode based on the link quality to achieve high recovery and low redundancy.

## Slide 43: Huawei CloudFabric Solution for Intelligent DCNs
Service intent/Strategy
Simplification elements
Telemetry & ERSPAN
NETCONF & SNMP
Analysis
Management
Control
+AI
iMaster NCE-Fabric provides full lifecycle services for DCNs, including planning, construction, O&M, and optimization.
Integrated planning and construction
Planning tool interconnected with iMaster NCE, implementing integrated planning and construction
Zero Touch Provisioning (ZTP)
Simplified deployment
Service intent self-understanding, conversion, and deployment
Network change simulation evaluation, preventing human errors
Intelligent O&M
Quick fault detection and locating based on knowledge graph and expert rules
Fast fault rectification based on expert rules and simulation analysis
Real-time optimization
Local inference and online model training and optimization for intelligent lossless traffic
User behavior prediction and resource optimization suggestions
DC
WAN
Campus Network

## Slide 44: AI-based Intelligent O&M for DCNs
Collect
Analysis
Decision
Multi-dimensional data of DCs
Service flow data/Telemetry data...
Root cause analysis
Knowledge-based inference engine
Intelligent analysis engine
Manual recovery
Recommended best contingency plans:
Port isolation
Configuration rollback
Capacity expansion recommendations
Huawei 30+ years of O&M
Expert experience
Continuous learning and training
based on real site faults
Model application
Risk prediction
Exception detection
Intent-based troubleshooting in a closed-loop manner
Data cleansing
AI-based exception identification
Network object modeling
Knowledge point 1
Knowledge point 2
Knowledge point 3
Knowledge point 4
DC
WAN
Campus Network

## Slide 45: Huawei Intelligent IP Network Solution
Analysis
Management
Control
Transport network
IP network
Access network
Access network
Site automation: Devices are plug-and-play, the platform is interconnected with the resource management system, and the configuration delivery is driven by work orders. The entire process is automated.
Network path navigation: automatic tunnel separation, intelligent traffic steering, and batch path deployment.
Network slicing: one network for multiple purposes, resource isolation, management isolation, and SLA assurance.
O&M automation
Service SLA awareness: iFIT-based in-band flow measurement and real-time SLA awareness through Telemetry.
Closed-loop processing: Network/service traffic and latency deterioration drive network self-optimization.
Network automation
DC
WAN
Campus Network
Notes: In this scenario, iMaster NCE-IP is used as the controller.
In-situ Flow Information Telemetry (iFIT): a method of directly measuring service packets to obtain performance indicators of an IP network, such as the packet loss rate and delay.

## Slide 46: Key Features of the Intelligent IP Network Solution
IP network
Service abstraction
Service abstraction
Automated service provisioning
Network path navigation
IP network optimization
Capability openness
EVPN
L3VPN
PWE3
...
50M
100M
20M
30M
MPLS TE
Real-time analysis
Unified scheduling
Centralized route computation
Path1
Path2
RESTful
SNMP
XML
FTP
OPEN API
Northbound open interfaces
Abundant northbound open interfaces simplify northbound OSS/IT system integration and provide an open programmable framework.
Telemetry
Second-level network data collection
WAN
Traffic-based scheduling
DC
WAN
Campus Network
Notes: iMaster NCE automates service provisioning on IP networks through service abstraction and model-driven development. For mainstream services such as EVPN, L3VPN, and PWE3, iMaster NCE provides multiple service configuration templates, greatly reduces service provisioning parameter settings, supports batch service provisioning and automatic parameter verification, and automatically creates tunnels through service triggering, greatly shortening the service provisioning period and improving the service provisioning efficiency.
Network path navigation: iMaster NCE performs real-time analysis, centralized path computation, and unified scheduling on the MPLS TE network to compute optimal E2E paths for MPLS TE tunnels, implementing global network traffic balancing and differentiated service management, and ensuring experience of high-priority services.
iMaster NCE collects the link traffic bandwidth and direction of the IP network in real time. Based on the topology, traffic, and link quality of the entire network, iMaster NCE provides one-hop scheduling for cross-domain inbound and outbound traffic on the native IP network in DC egress and public network interconnection scenarios, implementing elastic bandwidth for VIP traffic, intra-city traffic localization, and egress link balancing. Optimal DC egress traffic is then provided to ensure the SLA of VIP services. In addition, iMaster NCE provides one-hop and multi-hop optimization capabilities to improve backbone network resource utilization and operation efficiency.

## Slide 47
(Single-answer question) Which of the following is the management and control platform used in Huawei's solution for data center scenarios? ( )
  iMaster NCE-IP
  iMaster NCE-Fabric
  iMaster NCE-WAN
  iMaster NCE-DCN
Notes: B

## Slide 48
This course describes the overall architecture of enterprise networks, typical topologies of WANs, MANs, campuses, and DCs, and typical enterprise networks in some industry scenarios.
With the development of new technologies such as 5G and cloud and the trend of digital transformation in the industry, enterprises raise new requirements for networks. Enterprise networks are facing unprecedented transformation.
Finally, this course briefly introduces Huawei's solutions for different enterprise network scenarios, including CloudCampus, SD-WAN, CloudFabric, and IP WAN. We will learn more about these solutions in subsequent courses.