## Slide 1
Datacom
V1.0
Zhang Linrui/wx570554
2021.2
Li Xianzhi/00354681
New

## Slide 2: Campus Network Architecture and Key Technology Applications

## Slide 3
Campuses are everywhere in a city except roads and households. Typical campus examples include factories, government buildings and facilities, shopping malls, office buildings, school campuses, and parks. According to statistics, 90% of urban residents work and live in campuses, 80% of gross domestic product (GDP) is created in campuses, and each person stays in campuses for 18 hours every day. Campus networks, as the infrastructure for campuses to connect to the digital world, are an indispensable part of campus construction and play an increasingly important role in daily working, R&D, production, and operations management.
This course describes campus networks, common architectures and technologies of campus networks, and typical applications of these technologies. This information helps readers better understand the campus network design.

## Slide 4
Upon completion of this course, you will be able to:
  Describe what a campus network is like.
  Describe the typical architecture of a campus network.
  Understand common technologies used on campus networks.
  Understand typical applications of campus network technologies.

## Slide 5
Introduction to Campus Networks
Typical Campus Network Technologies
Typical Applications of Campus Network Technologies

## Slide 6: Campuses Are Everywhere
5 h & 22 h
90%+
80%+
90%+
of city residents work and live in campuses.
spent in using smart terminals & staying in the campus every day
of GDP is created in campuses.
of innovations are made in campuses.

## Slide 7: Overview of a Campus Network
A campus network refers to the internal network of an enterprise or organization, which is connected to the wide area network (WAN) and data center network.
A campus network is built to ensure that key enterprise services are running more efficiently.
Campus networks can be classified into large- and medium-sized campus networks and small- and medium-sized campus networks in terms of scale.
Some enterprises have branches dispersed in different geographical locations. Each branch network can be considered as a single campus network.

## Slide 8: Campus Network Classification (1)
Large campus network
Classified by the number of terminals or NEs
Midsize campus network
Small campus network
Number of terminals > 2000
Number of NEs > 100
Number of terminals: 200–2000
Number of NEs: 25–100
Number of terminals < 200
Number of NEs < 25
Classified by served objects of campus networks
Users: internal personnel only
Security requirements: network access control and external threat defense
Users: including external personnel, such as the public
Security requirements: access control, identity identification, behavior control, security protection, etc.
Closed campus network
Open campus network
Scale
Served
objects
Networks of different scales have different requirements and pain points.
A running campus network usually has both closed and open subnets.

## Slide 9: Campus Network Classification (2)
Single-service campus network
Classified by services carried on campus networks
Multi-service campus network
Single services
Simple network architecture
The network needs to carry a large number of services, and the
network scale is large. Different services need to be isolated
and guaranteed.
The campus network architecture is becoming complex and virtualized.
Wired campus network
Classified by campus network access modes
Wireless
campus network
Each device accessing a network must be connected to the preset network port through a network cable.
The architecture is structured and hierarchical, and the logic is clear, so faults are easy to locate.
The network is based on the 802.11 protocol (Wi-Fi) and is also called WLAN.
AP deployment and installation affect the coverage effect. Interference and conflicts exist, so the network needs to be optimized periodically.
Faults are difficult to locate.
Service
Access
mode
Currently, most campus networks are a mix of wired and wireless networks.
The complexity of the campus network architecture depends on the complexity of services carried on the campus network.

## Slide 10: Campus Network Classification (3)
To meet requirements of different industries, the campus network architecture is designed based on the characteristics of the industries that campus networks serve, ultimately building industry-specific campus network solutions.
Enterprise campus network
It refers to the Ethernet-based enterprise office network.
The enterprise campus network focuses on network reliability and advancement, continuously improves employees' office experience, and ensures the efficiency and quality of operation and production.
School campus network
School campus networks are classified into primary/secondary education and higher education campus networks.
Higher education campus networks are complex and usually have teaching and research networks, student networks, and operational dormitory networks.
There are high requirements on network manageability and security, and specific requirements on network advancement.
Government campus network
It usually refers to the internal network of a government agency.
High security is required. Generally, the internal network and external network are isolated to ensure high security of confidential information.
Business campus network
This type of campus networks apply to shopping malls, supermarkets, hotels, and parks.
Such networks mainly serve consumers. In addition, they include subnets for internal office work.
Such networks provide Internet access services and help build business intelligence (BI) systems for a better user experience, lower O&M cost, higher efficiency, and value transfer.

## Slide 11: Typical Physical Architecture of a Campus Network
Egress zone: serves as the border between the campus internal network and the external network. Through this egress zone, internal users can access the public network and external users (including customers, partners, branch users, and remote users) can access the internal network. Firewalls can be deployed at the egress zone to ensure the security of the internal network.
Core layer: serves as the core of data switching on the campus network. It connects various parts of the campus network, such as the data center, O&M zone, and egress zone.
Aggregation layer: forwards not only horizontal traffic between users, but also vertical traffic to the core layer. It can also function as the switching core for a department or zone and further extend the quantity of access terminals.
Access layer: provides various access modes for users and is the first layer of the network to which a terminal accesses.
Terminal layer: has terminals deployed to connect to the campus network. Terminals include computers, printers, IP phones, mobile phones, and cameras.
Data center: has servers and application systems deployed to provide data and application services for internal and external users of the enterprise.
O&M zone: manages network servers such as the NMS and authentication server.
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
Data center

## Slide 12
Introduction to Campus Networks
Typical Campus Network Technologies
Typical Applications of Campus Network Technologies

## Slide 13: VLAN
Virtual Local Area Network (VLAN) technology logically divides a physical LAN into multiple broadcast domains, each of which is called a VLAN.
All devices in a VLAN belong to the same broadcast domain. Different VLANs specify different broadcast domains. Devices in a VLAN can directly communicate with each other, whereas devices in different VLANs cannot communicate directly, but require a Layer 3 device for mutual communication.
Typically, a VLAN is a logical subnet.
Members of a VLAN are assigned based on interfaces of a switch. After an interface of a switch is added to a VLAN, the device connected to the interface is also added to this VLAN.
Core switch
Access switch 1
Access switch 2
Terminal 1
1.1.1.1/24
Terminal 2
1.1.1.2/24
Terminal 3
1.1.1.3/24
Terminal 4
2.2.2.1/24
VLAN 10 (office)
VLAN 20
(monitoring)
Notes: In addition to interface-based VLAN assignment, you can also use the following methods to assign VLANs:
  MAC address-based assignment: assigns VLANs based on the source MAC addresses of frames. This mode applies to small-scale networks where physical locations of user terminals frequently change but their network adapters seldom change.
  IP subnet-based assignment: assigns VLANs based on the source IP addresses of frames. This mode applies to scenarios where there are high requirements for mobility and simplified management and low requirements for security.
  Protocol-based assignment: assigns VLANs based on the protocol (suite) types and encapsulation formats of frames. This mode applies to networks running multiple protocols.
  Policy-based assignment: assigns VLANs based on a specified policy, which means VLANs are assigned based on combinations of interfaces, MAC addresses, and IP addresses. This mode applies to complex networks.

## Slide 14: Voice VLAN
Multiple types of flows are usually transmitted on a network simultaneously. Packet loss and delay seriously affect voice communication quality. Users are more sensitive to the quality of the voice service than to the quality of data and video services. Therefore, voice data flows must be preferentially transmitted when there is limited bandwidth available.
A voice VLAN is used to exclusively transmit voice data.
After a voice VLAN is configured on a switch, the switch can identify voice data flows, transmit the voice data flows in the voice VLAN, and provide QoS guarantee for the voice data flows.
Network
PC
IP Phone
Switch
You can use a single interface of a switch to transmit both voice and data services.
Network
IP phone
Switch
An IP phone is connected to a switch independently.
Typical networking of voice VLAN technology
Notes: A device configured with voice VLAN can identify voice flows in either of the following modes:
  MAC address-based identification: A device identifies voice flows based on the source MAC addresses of received data packets. If a source MAC address of a packet matches the organizationally unique identifier (OUI) of a voice device, the packet is considered a voice packet. OUIs must be preconfigured and are used in scenarios where IP phones send untagged voice packets.
  VLAN-based identification: Configuring OUIs for a large number of IP phones is time-consuming. In this case, you can configure a switch to identify voice packets based on VLAN IDs. If the VLAN ID of a received packet matches the configured voice VLAN ID, the packet is considered a voice packet. This simplifies configuration when a large number of IP phones are connected to the switch. However, the IP phones must be able to obtain voice VLAN information from the switch.

## Slide 15: Spanning Tree Protocol (STP)
R
Root port
D
Designated port
Non-designated port
SW2
SW3
SW1 (root bridge)
D
D
R
D
R
On a switching network with physical loops, switches running STP automatically generate a loop-free working topology, which is also called an STP tree. Each node of an STP tree is a specific switch, and each branch is a specific link.
STP transmits configuration BPDUs between switches to elect the root switch (or root bridge) and determine the role and status of each switch port.
Each switch proactively sends configuration BPDUs during initialization. After the network topology becomes stable, only the root bridge periodically sends configuration BPDUs. Other switches send their own configuration BPDUs only after receiving configuration BPDUs from upstream devices.
PID | PVI | BPDU Type | Flag | Root ID | RPC | Bridge ID | Port ID | Message Age | Max Age | Hello Time | Forward Delay
Configuration BPDU
Format of a configuration BPDU
Notes: How is an STP tree generated?
  STP compares four parameters: root bridge ID, root path cost (RPC), bridge ID (BID), and port ID (PID). A smaller value indicates a higher priority. All these parameters are BPDU fields.
    Root bridge election: The device with the smallest root bridge ID is elected as the root bridge.
    Root port election: A device compares the RPC, peer BID, peer PID, and local PID of its ports in sequence. The port with the smallest value is elected as the root port.
    Designated port election: A device compares the RPC, local BID, and local PID of its ports in sequence. The port with the smallest value is elected as the root port.
    After the root port and designated port are determined, all the non-root ports and non-designated ports on the switch will be blocked.

## Slide 16: Rapid Spanning Tree Protocol (RSTP)
As LANs are increasing in scale, the problem of slow STP topology convergence is becoming more prominent. To address this problem, the IEEE released the 802.1w standard in 2001 that defined the RSTP protocol. RSTP is an enhanced version of STP and implements rapid convergence of the switching network.
RSTP makes the following improvements over STP:
  Defines more port roles, making the spanning tree protocol easier to understand and configure.
  Eliminates the listening state, reducing the number of port states from 4 to 3.
  Uses the Flags field of STP configuration BPDUs to define port roles.
  Processes configuration BPDUs differently from STP. For example, it allows non-root bridges to proactively generate and send configuration BPDUs, and reduces the BPDU timeout interval to three times that of the Hello Time.
  Provides rapid convergence mechanisms, such as the Proposal/Agreement (PA) mechanism and edge port mechanism.
  Provides protection mechanisms to ensure the stability of the switching network.
SW1 (root bridge)
SW2
SW3
D
D
R
D
D
B
R
Root port
D
Designated port
A
Alternate port
B
Backup port
R
A
E
Edge port
E
E

## Slide 17: Multiple Spanning Tree Protocol (MSTP)
Defined in IEEE 802.1s and compatible with STP and RSTP, MSTP implements fast convergence while providing multiple redundant paths for forwarding data, effectively load balancing traffic for VLANs.
An MSTP network is composed of one or more MST regions, and each MST region contains one or more multiple spanning tree instances (MSTIs). An MSTI is a tree network that consists of switches running STP, RSTP, or MSTP.
The switches in the same MST region share the following characteristics:
  Have MSTP enabled.
  Have the same region name.
  Have the same VLAN-to-MSTI mappings.
  Have the same MSTP revision level.
SW2
SW3
SW1
Instance 1:
VLAN 1, 2, 3 ... 10
Data traffic
Instance 2:
VLAN 11, 12, 13 ... 20

## Slide 18: OSPFv2
On a large-scale enterprise network, the aggregation layer may consist of Layer 3 devices, such as routers and switches. In such scenarios, static routes are not flexible because the configuration is complex and they cannot quickly respond to topology changes. Therefore, a dynamic routing protocol — typically OSPF in IGP — can be deployed on the enterprise intranet.
The aggregation devices are divided into different non-backbone OSPF areas based on the network structure.
Core devices, network egress devices, and uplink interfaces of aggregation devices belong to Area 0. The downlink interfaces of aggregation devices and the access devices are added to Area X.
Redundancy links and the OSPF triggered update mechanism are used to implement backup of intranet paths.
Aggregation devices function as area border routers (ABRs) to execute route filtering policies.
Area 0
Area 1
Area 2

## Slide 19: Policy-Based Routing (PBR)
In the conventional routing and forwarding process, devices search their IP routing tables for routes based on packets' destination addresses and then forward the packets accordingly. However, more and more users require packet routing based on user-defined policies.
Traffic classifier
Configure a traffic classifier for matching interested data flows.
Matching criteria: VLAN ID, source or destination MAC address, Ethernet protocol type, DSCP priority, IP precedence, inbound or outbound interface, ACL rule
Traffic behavior
Redirects interested packets.
You can set the next-hop IP address or outbound interface for redirection.
Traffic policy
Traffic classifier > Traffic behavior
Apply the traffic policy
Apply the traffic policy to the inbound direction of an interface.
Apply the traffic policy to the incoming packets that belong to the VLAN and match the criteria defined in the traffic classifier.
Apply the traffic policy globally or to a card.
PBR can be configured using the modular QoS command line interface (MQC) or an ACL-based simplified traffic policy.
Enterprise intranet
Internet
①
②
③
④
Notes: PBR is used in agile campus service orchestration, multi-egress, and anti-DDoS off-path deployment scenarios.

## Slide 20: WLAN Network Architectures (1)
Fat AP
Internet
Networking characteristics: A Fat AP works independently and needs to be configured separately. It provides only simple functions and is cost-effective.
Application scenarios: families or mini-stores
AC + Fit AP
Networking characteristics: A Fit AP provides a wide range of functions and is used with an AC. Fit APs are managed and configured by an AC in a unified manner, posing high requirements on skills of maintenance personnel.
Application scenarios: medium- and large-sized enterprises
Fat AP
Fit AP
AC

## Slide 21: WLAN Network Architectures (2)
Leader AP
Networking characteristics: A leader AP can work independently or manage a small number of common APs to implement basic roaming functions. A leader AP has a low price and low requirements for maintenance skills.
Application scenarios: small and micro enterprises
Agile distributed AP
Networking characteristics: The agile distributed architecture divides APs into central APs and remote units (RUs). A central AP can manage multiple RUs, and this architecture provides good coverage and reduces costs. RUs can be used in the Fat AP, AC + Fit AP, and cloud management architectures.
Application scenarios: scenarios where rooms are densely distributed
Internet
Leader AP
Central AP
Room1
Room2
Room3
RoomN
Central AP
Room1
Room2
Room3
RoomN
AC
RU
RU

## Slide 22: WLAN Network Architectures (3)
Networking characteristics: APs are centrally managed and configured on iMaster NCE-Campus. They provide rich functions and support plug-and-play.
Application scenarios: small- and medium-sized enterprises
Internet
Cloud AP
Cloud management mode

## Slide 23: WLAN Network Architectures (4)
Native AC
Networking characteristics: This architecture uses the native AC function of switches to manage APs on a network, implementing wired and wireless network convergence. This architecture also leverages big data and AI technologies to implement simplified, smart, and secure campus networks.
Application scenarios: large- and medium-sized enterprises
Egress zone
Core layer
Aggregation layer
Access layer
Data center
Native AC
Native AC
O&M zone
iStack/CSS link
Internet
WAN

## Slide 24: VRRP
Basic VRRP application
Typical application of MSTP+VRRP
Aggregation switch 1
Aggregation switch 2
Access switch
Aggregation switch 1
Aggregation switch 2
Access switch
VRRP
Virtual router
192.168.1.254
IP address: 192.168.1.1/24
Default gateway: 192.168.1.254
Redundancy
Load balancing
Association
VLANs 11, 12...20
VLANIF11-20 VRRP Master
VLANIF21-30 VRRP Backup
MSTI 10 Primary root bridge
MSTI 20 Secondary root bridge
MSTP
VLANIF11-20 VRRP Backup
VLANIF21-30 VRRP Master
MSTI 10 Secondary root bridge
MSTI 20 Primary root bridge
MSTP
VRRP
VRRP
VLANs 21,12...30
VRRP and MSTP are used together to implement gateway redundancy, load balancing, Layer 2 loop prevention, and reliability.
Notes: Generally, all hosts on the same network segment are configured with the same default route with the gateway address as the next-hop address. The hosts use the default route to send packets to the gateway, which then forwards the packets to other network segments, enabling hosts to communicate with external networks. If the gateway fails, hosts using this gateway address as the next hop of their default route cannot communicate with external networks.
The Virtual Router Redundancy Protocol (VRRP) virtualizes several routing devices into a virtual router and uses the IP address of the virtual router as the default gateway address for the communication between users and external networks. If a gateway fails, VRRP selects another gateway to forward traffic, thereby ensuring reliable communication.
  Redundancy: Multiple routing devices enabled with VRRP constitute a VRRP group and the VRRP group is used as the default gateway. When a single point of failure (SPOF) occurs, services are transmitted through the backup link. This reduces the possibility of network faults and ensures non-stop transmission of services.
  Load balancing: VRRP enables multiple available routers to share the load, reducing the traffic burden on the master.
  Association: VRRP can monitor faults on uplinks. When the uplink interface or uplink is faulty, the priority of the original master decreases, and an optimal backup becomes the master, ensuring proper traffic forwarding. Association between VRRP and BFD speeds up the active/standby switchover. To speed up the active/standby switchover in the VRRP group, configure a BFD session between the master and backup and associate the BFD session with the VRRP group. This is because BFD can fast detect faults. When the link between the master and backup becomes Down, the backup immediately switches to the master and takes over traffic.

## Slide 25: Link Aggregation, iStack, and CSS
Ethernet link aggregation, also known as Eth-Trunk, bundles multiple physical links into a logical link to increase link bandwidth, without having to upgrade hardware.
Intelligent stack (iStack) enables multiple stacking-capable switches to function as a single logical switch. iStack is applicable to Huawei fixed switches.
A cluster switch system (CSS), also known as a cluster, combines two clustering-capable switches into a single logical switch. CSS is applicable to Huawei modular switches.
Link aggregation can be used with iStack/CSS to implement link-level and device-level reliability and increase network bandwidth.
iStack
CSS
iStack
iStack
iStack/CSS Link
Eth-Trunk
Network

## Slide 26: Network Quality Analysis (NQA)
To visualize the quality of network services and allow users to check whether the quality of network services meets requirements, the following measures must be taken:
  Enable the device to provide network service quality information.
  Deploy probe devices to monitor network service quality.
The preceding measures require devices to provide statistical parameters such as the delay, jitter, and packet loss ratio and require dedicated probe devices. These requirements increase investments on devices.
NQA can precisely test the network operating status and output statistics without using dedicated probe devices, effectively reducing costs.
NQA measures network performance and collects statistics on the delay, jitter, and packet loss ratio in real time.
Network
TCP test
DNS test
HTTP test
NQA test instance
NQA client
NQA server
ICMP test
Notes: NQA measures the performance of various protocols running on networks, which helps users collect statistics about network operation indexes in real time.

## Slide 27: Port Isolation
VLAN 10 (office VLAN)
Core switch
Access switch 1
Terminal 1
1.1.1.1/24
Terminal 2
1.1.1.2/24
Users in the same VLAN are isolated to enhance user communication security and prevent invalid broadcast packets from affecting services.
Data exchanged between different users in the same VLAN can be forwarded by the upper-layer device in a centralized manner.
Requirements
Port isolation can isolate ports in the same VLAN.
To implement Layer 2 isolation between ports, simply add these ports to a port isolation group.
There are two port isolation modes: Layer 2 isolation and Layer 3 interworking, and Layer 2 and Layer 3 isolation.
  To isolate broadcast packets in the same VLAN but allow users connected to different interfaces to communicate at Layer 3, you can set the port isolation mode to Layer 2 isolation and Layer 3 interworking.
  To prevent interfaces in the same VLAN from communicating at both Layer 2 and Layer 3, you can set the port isolation mode to Layer 2 and Layer 3 isolation.
Solution
Terminal 3
1.1.1.3/24
Enable port isolation and add the ports to the same port isolation group
Notes: Port isolation provides more secure and flexible networking solutions.
In some scenarios, data exchanged between terminals in a VLAN needs to be forwarded by an upper-layer device instead of an access switch. This ensures that traffic is forwarded by the upper-layer device instead of the access switch, so that traffic management and control policies can be deployed on the upper-layer device. This mode is called centralized forwarding mode. In this mode, port isolation is configured for all downstream Layer 2 devices. Therefore, proxy ARP should be configured on the gateway. In most cases, intra-VLAN proxy ARP is used.

## Slide 28: Ethernet Port Security
Point where port security can be configured
Core switch
Access switch 1
Access switch 2
Terminal 1
Terminal 2
Terminal 3
Terminal 4
An enterprise requires that each access switch interface connected to terminals allow only one PC to access the network so as to limit the number of MAC addresses.
If an employee attempts to connect a small switch or hub to an interface to increase the number of Internet access interfaces, this behavior should be detected and prohibited.
Some enterprises may require that a switch forward only data frames sent by terminals with trusted MAC addresses to the upper-layer network. Employees are not allowed to change their locations, that is, change access interfaces of the switch.
Requirements
Port security converts the dynamic MAC addresses learned on an interface into secure MAC addresses (including dynamic and static secure MAC addresses, and sticky MAC addresses). This function prevents unauthorized users from using this interface to communicate with the switch, thereby enhancing device security.
Solution
Notes: Configuring port security on an interface of a switch can limit the number of MAC addresses learned by the interface. Then punishment measures can be taken when a violation occurs.
The interface configured with port security can convert the learned MAC addresses into secure MAC addresses, preventing devices with other MAC addresses from accessing the network through the interface.

## Slide 29: Media Access Control Security (MACsec)
Site 1
Site 2
Internet
MACsec
MACsec
IPsec
Background
Most data is transmitted in plaintext on LAN links, failing to meet security requirements in scenarios demanding high security.
MACsec overview
Media Access Control Security (MACsec), in compliance with the IEEE 802.1AE standard, defines a method for secure data communication based on the Ethernet. It provides hop-by-hop encryption to secure data transmission.
Data integrity check
User data encryption
Data source authenticity verification
Replay protection
Typical application scenarios
MACsec is deployed between switches to ensure data security. For example, MACsec is deployed between access switches and uplink aggregation or core switches.
When transmission devices exist between switches, MACsec can be deployed to ensure data security.

## Slide 30: DHCP Snooping
Some attacks are launched against DHCP on the network, including bogus DHCP server attacks, DHCP server DoS attacks, and bogus DHCP message attacks.
DHCP snooping ensures that DHCP clients obtain IP addresses from authorized DHCP servers and records mappings between IP addresses and MAC addresses of DHCP clients, preventing DHCP attacks on the network.
DHCP client
DHCP client
Authorized DHCP server
Unauthorized DHCP server
Invalid DHCP ACK, NAK, and Offer messages
2
3
Obtain an incorrect IP address
1
2
Notes: The DHCP snooping-enabled device forwards DHCP Request messages of users (DHCP clients) to an authorized DHCP server through the trusted interface, and then generates DHCP snooping binding entries based on the DHCP ACK messages received from the DHCP server. When receiving DHCP messages from users through the DHCP snooping-enabled interfaces, the device checks the messages against the binding table, thereby preventing attacks initiated by unauthorized users. In addition, DHCP snooping supports multiple security features, such as limiting the rate for sending DHCP messages.

## Slide 31: Dynamic ARP Inspection (DAI)
ARP attacks are frequently launched on networks. A man-in-the-middle (MITM) attack is a common ARP spoofing attack.
To defend against MITM attacks, configure DAI on a switch.
DAI defends against MITM attacks using a DHCP snooping binding table. When a switch receives an ARP packet, it compares the source IP address, source MAC address, VLAN ID, and interface number of the ARP packet with those in DHCP snooping binding entries.
  If the ARP packet matches a binding entry, the switch considers the ARP packet valid and allows the packet to pass through.
  If the ARP packet does not match any binding entry, the switch considers the ARP packet invalid and discards the packet.
ARP packet:
Sender IP address: 1.1.1.1
Sender MAC address: 0000-0000-2222
DHCP snooping binding table
PC1
with MAC 0000-0000-1111
obtains IP address 1.1.1.1/24
PC2
with MAC 0000-0000-2222
obtains IP address 1.1.1.2/24
Authorized DHCP server
GE0/0/1
GE0/0/2
IP Address | MAC Address | VLAN ID | Interface
1.1.1.1 | 0000-0000-1111 | 10 | GE0/0/1
1.1.1.2 | 0000-0000-2222 | 10 | GE0/0/2
Notes: An MITM attacker establishes independent connections with two parties that intend to communicate and relays messages between them. The two parties consider that they are directly communicating with each other over a private connection, but the entire conversation is in fact controlled by the attacker. In an MITM attack, the attacker can intercept all packets exchanged between the two parties and insert new ones.
To defend against MITM attacks, configure DAI on a switch.
  DAI defends against MITM attacks using a DHCP snooping binding table. When the switch receives an ARP packet, it compares the source IP address, source MAC address, VLAN ID, and interface number of the ARP packet with those in DHCP snooping binding entries. If the ARP packet matches a binding entry, the switch considers the ARP packet valid and allows the packet to pass through. If the ARP packet does not match any binding entry, the switch considers the ARP packet invalid and discards the packet.
  DAI is available only when DHCP snooping is configured. A DHCP snooping-enabled switch automatically generates DHCP snooping binding entries when DHCP users go online. If a user is configured with a static IP address, you need to manually configure a static binding entry for the user.
  When an attacker connected to the DAI-enabled switch sends bogus ARP packets, the switch detects the attack based on the binding entries and discards the bogus ARP packets. If the packet discarding alarm function is also enabled on the DAI-enabled switch, the switch will generate an alarm when the number of ARP packets discarded due to failure to match any binding entry exceeds the alarm threshold.

## Slide 32: IP Source Guard (IPSG)
IPSG implements source IP address filtering based on Layer 2 interfaces. IPSG prevents malicious hosts from simulating authorized hosts using forged IP addresses. In addition, IPSG prevents unauthorized hosts from accessing or attacking networks using forged IP addresses.
IPSG checks IP packets on Layer 2 interfaces against a binding table that contains the bindings of source IP addresses, source MAC addresses, VLAN IDs, and inbound interfaces. Only packets matching the binding table are forwarded, and other packets are discarded.
Authorized terminal 1
1.1.1.2/24
0000-0000-2222
Unauthorized terminal
1.1.1.2/24
0000-0000-FFFF
1
The authorized terminal is powered off.
2
An unauthorized terminal accesses the network using authorized terminal 1's IP address.
Binding table
GE0/0/1
GE0/0/2
3
The unauthorized terminal sends data.
4
The switch identifies and discards invalid traffic based on the binding table.
IP Address | MAC Address | VLAN ID | Interface
1.1.1.1 | 0000-0000-1111 | 10 | GE0/0/1
1.1.1.2 | 0000-0000-2222 | 10 | GE0/0/2
Notes: As networks continue to increase in scale, a growing number of attackers are forging source IP addresses to initiate network attacks (IP address spoofing attacks). Some attackers forge IP addresses of authorized users to obtain network access rights and access networks. As a result, authorized users are unable to access networks or sensitive information may be intercepted.
IPSG provides a mechanism to effectively defend against IP address spoofing attacks.
  The binding table can be a static binding table or a dynamic DHCP snooping binding table.
  IPSG only checks the IP packets from hosts. It does not check non-IP packets such as ARP packets.

## Slide 33: Network Admission Control (NAC)
User terminal
Authentication server
Internet
WAN
AC
AC
Data
center
O&M zone
How to ensure that terminals are valid and secure?
How to ensure that authorized terminals are authorized correctly?
NAC is an end-to-end security technology that authenticates clients and users to ensure network security.
NAC provides three authentication modes: 802.1X authentication, MAC address authentication, and Portal authentication.
Authentication device
Notes: In addition to using NAC to authenticate access users and control their rights, a campus network also needs to authenticate and control rights of administrators (also called login users) who can log in to devices through FTP, HTTP, SSH, Telnet, or console ports.

## Slide 34: DHCP
Using DHCP to automatically configure IP addresses
Typical application of DHCP on a large-scale campus network
DHCP client
Layer 2 switch
DHCP server
The DHCP client broadcasts a DHCP Discover message.
1
2
The DHCP server responds with a DHCP Offer message.
The DHCP client broadcasts a DHCP Request message.
3
4
The DHCP server responds with a DHCP ACK message.
Search for the DHCP server on the network
Provide information such as the IP address
Specify the IP address provided by a DHCP server
Allocate the specified IP address
DHCP server
DHCP client
DHCP client
Layer 3 gateway
enabled with DHCP relay
DHCP is widely used on various campus networks to implement automatic IP address configuration for wired or wireless terminals.
A DHCP relay agent forwards DHCP messages between a DHCP server and DHCP clients to help the DHCP server to dynamically allocate network parameters to the DHCP clients.
Layer 3 gateway
enabled with DHCP relay
Notes: DHCP dynamically configures and uniformly manages IP addresses of hosts. DHCP is defined in RFC 2131 and uses the client/server communication mode. A DHCP client requests configuration information from a DHCP server, and the DHCP server returns the configuration information allocated to the DHCP client.
  Instead of statically specifying an IP address for a host, DHCP enables a host to obtain an IP address dynamically.
  DHCP can allocate other configuration parameters, such as the startup configuration file of a client, so that the client can obtain all the required configuration information by using only one message.
  DHCP supports dynamic and static IP address allocation. A network administrator can select different address allocation modes for hosts as required.
    Dynamic allocation: DHCP allocates an IP address with a limited validity period (known as a lease) to a client. This mechanism applies to scenarios where hosts temporarily access the network or the number of idle IP addresses is less than the total number of hosts that do not require permanent connections.
    Static allocation: DHCP allocates fixed IP addresses to clients. Compared with manual IP address configuration, DHCP static allocation prevents manual configuration errors and enables unified maintenance and management.
DHCP has the following benefits:
  Reduced client configuration and maintenance cost
  Centralized management of limited IP addresses

## Slide 35: DHCP Options
DHCP client
DHCP server
DHCP Offer
IP address assigned to a DHCP client
…
Options
The Options field stores control information and parameters allocated to a DHCP client.
A DHCP message can carry multiple options.
DHCP predefines a large number of options for various purposes, for example, setting the gateway address and DNS server address.
Options field in DHCP messages
The Options field can be used to set the IP address of the NTP server.
The Options field can be vendor-defined. For example, the CloudCampus solution uses Option 148 to implement plug-and-play of network devices. The information is used to notify the DHCP client of controller information so that the device can obtain the controller address and port number.
Option 43 is used to register an AP with an AC that resides on a different network segment from the AP in WLAN scenarios.
Typical application scenarios

## Slide 36: Network Time Protocol (NTP)
NTP is an application layer protocol in the TCP/IP suite that synchronizes time between time servers and clients. NTP is implemented based on IP and UDP. NTP packets are transmitted over UDP using port 123.
Key concepts in the NTP network architecture:
  Synchronization subnet: consists of the primary time server, stratum-2 time servers, PC clients, and transmission paths connecting them.
  Primary time server: directly synchronizes its clock with a standard reference clock through a cable or radio. Typically, the standard reference clock is either a radio clock or the Global Positioning System (GPS).
  Stratum-2 time server: synchronizes its clock with either the primary time server or other stratum-2 time servers on the network. Stratum-2 time servers use NTP to transmit time information to other hosts in a LAN.
  Stratum: is a hierarchical standard for clock synchronization. It represents the precision of a clock. The value of a stratum ranges from 1 to 16. A smaller value indicates higher precision. The value 1 indicates the highest clock precision, and the value 16 indicates that the clock is not synchronized.
Host2
Host3
Host1
Host4
SwitchA
SwitchB
SwitchD
Stratum-2 time server
Stratum 2
Stratum-2 time server
Stratum 2
Stratum-2 time server
Stratum 3
Stratum-2 time server
Stratum 3
Primary time server
Stratum 1
SwitchC
SwitchE
Clock source

## Slide 37: SNMP
SNMP is a network management protocol widely used on TCP/IP networks.
SNMP provides a method for managing devices through a central computer that runs network management software — known as a network management station (NMS).
Using in-band management, SNMP achieves efficient and batch network device management. In addition, SNMP enables unified management of different types of network devices from different vendors.
Overview of SNMP
SNMP
NMS (SNMP server)
Example: iMaster NCE
Managed device (SNMP client)
Example: routers and switches
Agent
MIB

## Slide 38: Network Configuration Protocol (NETCONF)
NETCONF provides a set of mechanisms for managing network devices. To be specific, users can use NETCONF to add, modify, and delete configurations of network devices, as well as obtain configurations and status of network devices.
NETCONF Server
Device
Device 1
Device 2
Device 3
Network
Management platform
SDN controller
NETCONF Client
NETCONF
NETCONF has three objects:
  NETCONF client
  NETCONF server
  NETCONF message
Notes: The plug-and-play of a device is implemented by establishing a NETCONF session between the device and the controller, so that the controller can deliver configurations to the device.

## Slide 39: Basic Operations of NETCONF
NETCONF defines a series of operations:
Scenario | Operation | Function
Query data | <get-config> | Queries configuration data.
 | <get> | Queries the current configuration and status data of the device.
Edit data | <edit-config> | Creates, modifies, or deletes configuration data.
Backup/Restoration | <copy-config> | Exports configuration data, or replaces one configuration datastore with another configuration datastore.
 | <delete-config> | Deletes the configuration datastore and clears the startup configuration.
Locking/Unlocking | <lock> | Exclusively occupies the permission to modify the configuration datastore.
 | <unlock> | Releases the exclusive permission to modify the configuration datastore.
Transactional operations | <commit> | Copies the candidate configuration to the device's running configuration.
 | <cancel-commit> | Cancels an ongoing confirmed commit.
 | <discard-changes> | Discards uncommitted changes to the candidate configuration.
 | <validate> | Checks whether the syntax and semantics of the specified configuration data are correct.
Session operations | <close-session> | Normally ends the NETCONF session.
 | <kill-session> | Forcibly terminates other NETCONF sessions. You must have the administrator permission to perform this operation.

## Slide 40: LLDP
Network management requirements and overview of LLDP
Application of LLDP in Huawei CloudCampus solution
Most network management systems (NMSs) can detect Layer 3 network topologies, but cannot detect detailed Layer 2 topologies or configuration conflicts.
LLDP provides a standard link-layer discovery method. It can:
  Obtain the topology status of the connected devices.
  Display paths between devices.
  Detect configuration conflicts between devices and queries network failure cause.
You can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.
SW1
SW2
SW3
GE1/0/1
GE1/0/1
[SW3] display lldp neighbor brief
Local Intf Neighbor Dev Neighbor Intf Exptime(s)
GE1/0/1 SW2 GE1/0/1 101
The device reports LLDP information to the controller.
1
2
3
The controller restores and displays the network topology based on the LLDP information reported by devices.
Notes: LLDP is a standard Layer 2 topology discovery protocol defined in IEEE 802.1ab. LLDP collects local device information including the management IP address, device ID, and port ID and advertises the information to neighboring devices. Neighboring devices save the received information in their management information bases (MIBs). The NMS can query required information in MIBs to determine link status.
As networks grow in scale, network devices are increasing in diversity with complex configurations, posing higher requirements on network management capabilities. Most NMSs can detect Layer 3 network topologies, but they cannot detect detailed Layer 2 topologies or configuration conflicts. To address the network management problems, a standard protocol is required to exchange Layer 2 information between network devices.
LLDP provides a standard link-layer discovery method. By obtaining Layer 2 information from devices, LLDP allows users to detect the topology of neighboring devices, and display paths between clients, switches, routers, application servers, and network servers. The information also helps detect configuration conflicts between network devices and identify causes of network failures. Enterprise users can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.

## Slide 41: Telemetry
Telemetry, also called network telemetry, is a technology that remotely collects data from physical or virtual devices at a high speed. Devices periodically send information such as interface traffic statistics, CPU usage, and memory usage to collectors in push mode. Compared with the conventional pull mode (request-response interaction), the push mode provides faster and real-time data collection.
Analyzer
Device
Collector
Controller
Telemetry-based data reporting

## Slide 42: Key Technologies for Virtualized Campus: VXLAN-based Multi-purpose Network
OA
VC
Security protection
Internet
OA
VC
Security protection
Internet
OA
VC
Security protection
VXLAN
VN1
OA VN
VN2
VC VN
VN3
Security protection VN
Multiple services carried on one network
Automated physical network deployment
Automated VN provisioning
Automated service policy delivery
Notes: Using virtualization technologies, multiple virtual networks (VNs) can be created on top of a physical network. Different VNs are used for different services, such as OA, videoconferencing, and security protection.

## Slide 43: VXLAN
VXLAN is essentially a VPN technology that is used to build a Layer 2 virtual network (overlay network) on top of any physical network (underlay network) that is reachable at Layer 3. VXLAN tunnels can be built between VXLAN gateways to implement communication within a VXLAN network as well as communication between a VXLAN network and a non-VXLAN network.
VXLAN uses MAC-in-UDP encapsulation to extend Layer 2 networks and encapsulate Ethernet packets into IP packets. VXLAN can be deployed together with BGP EVPN and VRF to implement multi-purpose campus network, on which different VNs are isolated from each other.
Underlay
Local LAN
VXLAN tunnel
Overlay
Local LAN
Local LAN

## Slide 44: Underlay and Fabric
Underlay network
Fabric network
The underlay network is the foundation of the entire virtual campus network. It is a physical network consisting of physical network devices and provides interoperability for all services on a campus network.
Uses a multi-layer architecture (core, aggregation, and access).
Has multiple topologies, such as tree, ring, and mesh.
Underlay information includes device interconnection VLANs, interconnection IP addresses, and IGP.
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
IGP (OSPF)
BGP EVPN peer relationship
BGP EVPN peer relationship
A campus fabric is a network resource pool that is abstracted from physical network devices on the underlay network so as to create a multiple-purpose network.
A fabric includes the following:
Overlay network resource pool (BD IDs and VNIs) for terminal access
VLAN ID pool for terminal access
Access point pool (switch ports for wired access or SSIDs for wireless access) for terminals
These resource pools can be used to create multiple VNs.
Border
Edge
Edge
Access
Access
Loopback

## Slide 45: Overlay
Underlay and overlay in real life
Urban roads (infrastructure)
Vehicle carrying passengers
Extend in all directions
Underlay and overlay on a virtualized campus network
Underlay
Overlay
Service A
Service B
Service A
Service B
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
VXLAN encapsulation
VXLAN encapsulation
Fabric
Notes: An overlay network is a logical network that is built on top of a physical network, uses the tunneling technology, and separates the forwarding plane from the control plane.

## Slide 46: BGP EVPN
BGP EVPN extends BGP by defining several new types of BGP EVPN routes using Network Layer Reachability Information (NLRI) in the MP_REACH_NLRI attribute.
These BGP EVPN routes can be used to transmit VTEP addresses and host information. Therefore, when BGP EVPN is used on a VXLAN network, VTEP discovery and host information learning can be transferred from the data plane to the control plane.
SW1
SW2
BGP EVPN peer relationship
Type 2 routes (MAC/IP routes): are used to advertise host MAC addresses, ARP entries, and IP routes.
Type 3 routes (inclusive multicast routes): are used to transmit Layer 2 VNI and VTEP IP address information, so as to implement automatic VTEP discovery, dynamic VXLAN tunnel establishment, and BUM packet forwarding.
Type 5 routes (IP prefix routes): are used to advertise host MAC addresses, ARP entries, and IP routes, as well as external network routes.
Notes: In a network virtualization overlay (NVO) scenario, BGP EVPN is used together with VXLAN and functions as the control plane protocol for VXLAN.

## Slide 47: Using VRF for VN Isolation
Terminal 4
2.2.2.1/24
Terminal 1
1.1.1.1/24
Terminal 3
1.1.1.2/24
Terminal 4
2.2.2.2/24
VN1 (office)
VN2 (monitoring)
Isolation
Isolation
Isolation
VXLAN
Multiple logical networks, such as the office network and monitoring network, can be built on a simple physical campus network.
The office network is completely isolated from the monitoring network.
Deploying ACLs: ACLs can be used to isolate traffic between VLANs. However, ACL configuration is complex and ACLs do not apply to all scenarios.
Build independent physical networks: Separate physical networks can be built for office and monitoring purposes, so services can be isolated. However, this increases network construction costs.
Virtual Routing and Forwarding (VRF): It is also called a VPN instance, which is similar to a virtual device. A VPN instance uses a routing table independent of the root device to completely isolate the VPN instance from the root device, without increasing hardware costs.
Solution
Requirements

## Slide 48: Network Address Translation (NAT)
Private network
Source IP:
192.168.1.10
Destination IP:
200.1.2.3
Source IP:
200.1.2.3
Destination IP:
192.168.1.10
Egress router
PC
192.168.1.10/24
Web server
200.1.2.3
Source IP: 200.1.2.3
Destination IP: 122.1.2.1
2
3
Source IP: 122.1.2.1
Destination IP: 200.1.2.3
Internet
1
4
NAT technology translates IP addresses in IP data packets. It is widely used on live networks and is usually deployed on network egress devices, such as routers or firewalls.
Typical application scenarios:
  When users with private IP addresses attempt to access the Internet, NAT deployed on the egress device of the campus network can translate the source IP addresses of data packets sent from the intranet to the Internet into specific public IP addresses.
  The campus network provides some services for Internet users. When Internet users access these services using public IP addresses, NAT can translate the destination IP addresses of data packets from the Internet.

## Slide 49: Generic Routing Encapsulation (GRE)
R1
PC1
2001:0DB8:0:0::1/64
R2
PC2
2001:0DB8:0:1::1/64
1.1.1.1
2.2.2.2
GRE tunnel
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data
Source IP | 1.1.1.1
Destination IP | 2.2.2.2
GRE header | 
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data
GRE is a protocol that encapsulates data packets of some network layer protocols, such as IPX, IPv6, and IPv4. The encapsulated data packets can then be transmitted over a network using a different network layer protocol, such as IPv4 and IPv6.
GRE is a Layer 3 tunneling technology that transparently transmits packets over GRE tunnels. It solves the transmission problems on the network that uses different network-layer protocols.
  GRE is easy to implement and increases only a few loads on devices at both ends of a tunnel.
  GRE sets up tunnels over an IPv4 network to connect networks running different protocols, reusing the original network architecture and reducing costs.
  GRE connects non-contiguous subnets and sets up VPNs to ensure secure connections between the enterprise headquarters and branches.
  GRE provides only simple password authentication and does not provide the encryption function.
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data

## Slide 50: IPsec VPN
R1
PC1
192.168.1.1/24
R2
PC2
172.16.1.1/24
1.1.1.1
2.2.2.2
IPsec VPN tunnel
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Source IP | 1.1.1.1
Destination IP | 2.2.2.2
Security protocol header | 
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Internet Protocol Security (IPsec) is a set of open network security protocols defined by the Internet Engineering Task Force (IETF) to secure data transmission and reduce the risk of information leakage.
Through encryption and authentication, IPsec ensures secure service data transmission over the Internet from the following dimensions:
  Data source authentication
  Data encryption
  Data integrity verification
  Anti-replay

## Slide 51: L2TP VPN
LAC
Remote OA user
L2TP VPN tunnel
Enterprise headquarters
External network
LAC
Enterprise branch
L2TP VPN tunnel
Layer 2 Tunneling Protocol (L2TP) extends the application of the Point-to-Point Protocol (PPP). It is a VPN tunneling protocol that allows traveling employees or enterprise branches to remotely access intranet resources.
The L2TP network architecture includes an L2TP access concentrator (LAC) and an L2TP network server (LNS).
  An LAC provides PPP and L2TP processing capabilities, and establishes an L2TP tunnel with the LNS. LACs can be different devices in different networking environments, for example, an LAC can be a gateway or a terminal. An LAC can initiate requests for establishing multiple L2TP tunnels to isolate data flows.
  An LNS is the peer of an LAC. That is, an L2TP tunnel is established between the LAC and the LNS. The LNS is located at the border between the private network of the enterprise headquarters and public network, and is usually the gateway of the enterprise headquarters.

## Slide 52: SSL VPN
DMZ
Remote OA user
SSL VPN tunnel
Server
Intranet
Secure Shell (SSL) VPN is an SSL-based remote access VPN technology. It allows mobile users (referred to as remote users in SSL VPN) to securely and conveniently access enterprise intranets and intranet resources, improving work efficiency.
SSL VPN uses the browser/server (B/S) architecture. Remote users can directly use a web browser to access intranet resources securely and quickly, without the need to install extra client software. SSL VPN provides the following functions:
  Fine-grained permission control based on the type of intranet resources accessed by remote users
  Flexible identity authentication
  Host check policies that check whether the operating systems, ports, processes, and antivirus software of remote users' devices meet security requirements. It also provides anti-nested remote desktop connection and anti-snapshot functions to eliminate security risks from remote users' devices.
External network

## Slide 53
Introduction to Campus Networks
Typical Campus Network Technologies
Typical Applications of Campus Network Technologies

## Slide 54: Case 1 - Traditional Campus Network
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
Data center
There are about 3000 wireless and wired terminals in total, so the campus network needs to provide both wireless and wired access services.
Network segments are divided based on departments and services. The gateways are configured on aggregation switches, and terminal addresses are automatically allocated.
Network devices are centrally managed and monitored.
Unified policy control is implemented for access users, and the intranet is protected from attacks from external networks.
Network reliability must be ensured.
Network requirements
Access, aggregation, and core switches are stacked or set up a CSS, and Eth-Trunks are configured on uplinks to ensure reliability.
The AC + Fit AP wireless networking mode is used, and hot standby is configured between ACs to ensure wireless network reliability. VLANs are configured on access switches to differentiate users on different service network segments, and IP addresses are allocated to these users by the corresponding aggregation switches through DHCP. Single-area OSPF is deployed on aggregation devices and upper-layer devices.
Access authentication is deployed for all users on the network, and corresponding policies are configured using ACLs.
Firewalls are deployed in the egress zone and security groups are configured to control traffic.
SNMP is enabled on all devices on the network, and the network management software is used to manage and maintain network devices in a unified manner.
Solution

## Slide 55: Case 2 - Virtualized Campus Network
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
Data center
VN 1
VN 2
VN 3
Reliability and security requirements similar to those of traditional campus networks
Plug-and-play and centralized management of network devices, and flexible provisioning of service configurations and policies
Isolation of multiple services on the campus network
Access control of terminals, and consistent network access rights and experience for users while they are moving within the campus so long as their identities remain unchanged
Network requirements
iMaster NCE-Campus is used to manage network-wide devices. Protocols such as NETCONF and Telemetry are used to implement unified management and maintenance of network devices as well as quick onboarding of devices.
VXLAN, BGP EVPN, and VRF technologies are used to divide VNs based on service requirements. iMaster NCE-Campus implements simplified deployment of the underlay and overlay networks as well as VN isolation.
iMaster NCE-Campus is used to authenticate users on the entire network. Free mobility is deployed to define different user groups or resources on the network as different security groups and implement policy control based on security groups.
Solution

## Slide 56: Case 3 - Small- and Medium-Sized Cloud Managed Campus Network
Internet
Store 1
Store N
Advertisement push
ESL
Store 2
There are a large number of stores, most of which use wireless networks and have simple network topologies. In addition, onsite personnel do not have network O&M skills.
There are many types of wireless terminals, including common wireless terminals and IoT terminals such as electronic shelf labels (ESLs).
The stores want to push product discounts and promotion activity advertisements to customers who are connecting to the Wi-Fi network in the stores.
Network requirements
Deployment by scanning barcodes achieves minute-level AP onboarding and quick provisioning of wireless network services. The cloud management platform provides one-stop management of the entire lifecycle (from planning and construction to maintenance and optimization) of all store networks.
Deploy IoT APs and use the IoT slots built in the IoT APs to implement co-site deployment of IoT and Wi-Fi, unified planning, and shared network for data backhaul. The ESL management system connects to and interacts with the supermarket management and ERP systems to dynamically display real-time price changes and issue out-of-stock warnings.
Customers access the network through Portal authentication, and can view customized advertisements displayed on the authentication page.
Solution

## Slide 57
(Multiple-Answer Question) Which of the following technologies can be used to improve network reliability? ( )
  STP
  Eth-Trunk
  iStack
  CSS
(True or False) On an MSTP network, devices in the same MST region must be configured with the same VLAN-to-MSTI mappings. ( )
  True
  False
Notes: BCD
A

## Slide 58
This course provides the definition of campus networks, common technologies used in campus networks, and application scenarios of these technologies.
In subsequent courses, we will discuss how to design networks based on customer requirements, which requires a comprehensive and in-depth understanding of campus network technologies. Due to limited space, this document cannot list every technology used on campus networks. To better understand subsequent courses, you can read related documents for more campus network technologies and a deeper understanding of the key technologies discussed in this course.