## Slide 1
Datacom
V1.0
Lu Yueyue/WX445705
2021.02
Zhu Shigeng/00261992
Update

## Slide 2: Large- and Medium-Sized Virtualized Campus Network Design

## Slide 3
Huawei CloudCampus 3.0 Solution adopts a new philosophy of Intent-Driven Network (IDN), and introduces big data analytics and Artificial Intelligence (AI) technologies into cloud and software-defined networking (SDN). It helps enterprises build intelligent, simplified, converged, open, and secure networks.
This course describes the planning and design process for large- and medium-sized virtualized campus networks that use the CloudCampus 3.0 Solution, including the underlay network design, fabric design, overlay network design, admission control and free mobility design, WLAN design, network security design, and O&M design.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the network layers and network architecture of large- and medium-sized virtualized campus networks.
  Complete the underlay network design for a virtualized campus network based on actual requirements.
  Complete the fabric and overlay network design for a virtualized campus network based on actual requirements.
  Complete the admission control design, free mobility design, WLAN design, network security design, and O&M design for a virtualized campus network based on actual requirements.

## Slide 5
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 6: Large- and Medium-Sized Campus Networks
Different from the wide area network (WAN) and data center network, a campus network typically refers to the internal network of an enterprise or organization. A campus network is built for more efficient running of key enterprise services.
In terms of network scale, campus networks can be classified into large- and medium-sized campus networks as well as small- and medium-sized campus networks. A large- or medium-sized campus network typically has:
  Over 2,000 end users
  Over 100 network elements (NEs)
Some enterprises have branches dispersed across different areas, and each branch network can be considered a single campus network.

## Slide 7: Service Requirements and Challenges of Large- and Medium-Sized Campus Networks
Enterprises' campus networks are the cornerstone of their digital transformation. Nowadays, mobile office, cloud computing, SDN, Internet of Things (IoT), artificial intelligence (AI), and big data are gaining momentum. Driven by this, new technologies and applications are constantly emerging and are making inroads to enterprise campus networks, which poses many new challenges for the campus networks.
Converged network
Requirements:
Diversified access terminals and services require a converged campus network.
Challenges:
Wi-Fi and IoT services are independently planned, deployed, and managed, resulting in high network construction costs.
The network management and O&M workload is heavy.
User experience awareness
Requirements:
Network O&M should become automated and intelligent, with insights into user experience anytime, anywhere.
Challenges:
Service faults cannot be detected in a timely manner.
Fault locating heavily relies on the O&M skills and experience of professionals, so faults cannot be quickly located.
The network cannot be self-optimized.
Automated network deployment
Requirements:
Network deployment should be automated to address the growing complexity in deployment and policies due to the surge in applications and services.
Challenges:
Manual configuration is repetitive, complex, and labor-intensive.
New service rollout requires configuring devices one by one, which is time-consuming and costly.
The workload of network policy deployment and adjustment is heavy.

## Slide 8: Huawei CloudCampus 3.0 Solution (CloudCampus Solution)
Analysis
Management
Control
Design
Deployment
Policy
One-stop management platform
NETCONF/YANG
WAN/
Internet
Large- and medium-sized campus
Small- and medium-sized campus
Campus interconnection
OA VN
R&D VN
OA VN
R&D VN
Security group 1
Access policy
Bandwidth
Priority
Rapid network provisioning, improving deployment efficiency
Device plug-and-play: simplified device deployment, scenario-specific guided configuration, template-based configuration
Simplified network deployment: network resource pooling, multi-purpose network, automatic service provisioning
Fast service provisioning, improving user experience
Free mobility: GUI-based policy configuration; access anytime anywhere, with consistent permission and experience during roaming
Intelligent terminal identification: anti-spoofing for terminal access, with the accuracy of intelligent terminal identification reaching over 95%
Intelligent HQoS: application-based traffic scheduling and shaping and fine-grained bandwidth management ensure service experience of VIP users
Quick intelligent O&M, improving network performance
Real-time experience visualization: uses Telemetry for network experience visualization at any moment, for any user, and in any area
Precise fault analysis: proactively identifies typical network issues and provides suggestions; compares and analyzes real-time data to predict faults
Intelligent network optimization: predictive optimization of wireless networks based on historical data, improving overall network performance
Security group 2
Security group 3
Security group 4
Security group 5

## Slide 9: Three Deployment Modes of CloudCampus
Operations entity
Customer
MSP, carrier
Huawei
On-Premise
MSP-owned Cloud
Scenario definition
Target customer
Huawei Public Cloud
Customers purchase and own software entities, such as the controller and analyzer, which can be deployed in their data centers or on the public cloud platform.
MSPs purchase software, such as the controller and analyzer, for operational purposes. The software can be deployed in their data centers or on the public cloud platform.
Huawei operates the public cloud and customers do not need to purchase the controller or analyzer software. Instead, customers just purchase Huawei's cloud managed network service.
Customers in industries such as government, education, large enterprise, retail, and financial services
MSP, carrier
Customers in industries such as government, education, large enterprise, retail, and financial services
Software transaction mode
Perpetual license + SnS
TBL subscription mode
SaaS mode
Notes: Managed service provider (MSP): delivers and manages network-based services, applications, and devices. The serviced objects include enterprises, residential areas, and other service providers.
Perpetual license + SnS: The perpetual license is sold together with SnS services, such as software patches, software upgrades (including new features of new releases), and remote support. In the perpetual license + SnS mode, a customer needs to pay SnS fee for a certain period of time, in addition to purchasing the license upon the first purchase. If the customer does not renew the SnS annual fee after it expires, the customer can only use functions provided in the license for the current version and cannot use the service functions covered in the SnS annual fee.
SaaS mode: MSPs are responsible for deploying or leasing hardware infrastructure, and O&M and management of the hardware and software. Software is provided for customers as cloud services and customers need to periodically pay for the cloud services.
Term Based License (TBL) mode: This mode differs from the perpetual license + SnS mode in that the licenses purchased by customers have limited validity periods. If a customer does not renew the subscription after the license expires, the customer can no longer use the software product.
SnS: refers to Subscription and Support. It consists of two parts: software support and software subscription. The complete software charging mode consists of the annual software SnS fee and software license fee.
Note: This course uses the on-premise deployment as an example.

## Slide 10: CloudCampus Solution Components: iMaster NCE-Campus
iMaster NCE-Campus is the configuration and management platform used in the CloudCampus Solution. It provides a portal for CloudCampus service configuration, O&M, and monitoring.
Manage + Control + Analyze
Unified data base
Centralized detection/locating/processing
Plan + Construct + Maintain + Optimize
Full lifecycle management
Simulation/Verification/Monitoring/Optimization
iMaster NCE-Campus, an autonomous driving campus network management and control system
Application service layer
Infrastructure layer
Management-control-analysis layer
MDM
e-Schoolbag
Asset management
Health management
...
Intelligent OAM
Automated + Intelligent
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting
Converged

## Slide 11: CloudCampus Solution Components: iMaster NCE-CampusInsight
AS-IS: Device-centric network management
TO-BE: User experience-centric AI-powered intelligent O&M
Device-centric management: User experience cannot be perceived.
Passive response: Potential faults cannot be identified.
Professional engineers locate faults on site.
SNMP
Network data collection within minutes
Topology management
Performance management
Alarm management
Configuration management
Experience visibility: Telemetry-based second-level data collection, enabling visible experience for each client, in each application, and at each moment.
Identification of potential faults and location of root causes within minutes:
  Identification of potential faults based on dynamic baselines and big data correlation analysis.
  KPI correlation analysis and protocol trace, helping accurately locate root causes of faults.
Predictive network optimization: intelligently analyzes load trends of APs through AI algorithms, implementing predictive optimization of wireless networks.
Traditional NMS
Telemetry
Network data collection within seconds
Visualized experience management
User journey playback
Identification of potential faults
Location of root causes
Predictive network optimization
Notes: Using algorithms to improve efficiency and leveraging scenario-specific continuous learning and expert experience, intelligent O&M frees O&M personnel from nerve-wracking alarms and noises, making O&M automated and intelligent.

## Slide 12: CloudCampus Solution Components: Network Hardware Products
CloudEngine S series switches
AirEngine Wi-Fi 6 APs
High-performance campus switches
Campus APs
Models that apply to all scenarios: indoor settled, indoor wall plate, agile distributed, and outdoor AP models
NetEngine AR routers
Campus egress routers
Integrate routing, switching, Wi-Fi, 5G, and security functions
HiSecEngine AI firewalls
Firewalls
Provide comprehensive and integrated network security protection capabilities

## Slide 13: Network Architecture of the CloudCampus Solution (VXLAN-based Virtualized Campus Network)
The following figure shows the typical network architecture of the CloudCampus Solution, which consists of the network layer, management layer, and application layer.
Application layer
Network layer
Management layer
MDM
e-Schoolbag
Asset management
Health management
AAA
…
Intelligent OAM
VN 1
VN 3
VN 2
Virtual network
Internet/
WAN
Native AC
AP
Switch
Switch
Switch
Switch
Switch
Firewall
Physical network
Open APIs
SNMP
NETCONF/
YANG
Telemetry
Notes: Network layer
  Virtualization technologies are introduced to divide the network layer into a physical network and a virtual network.
    Physical network: is also called the underlay network and provides basic connection services for a campus network. To meet access requirements of multiple types of terminals, the physical network provides converged access for three networks, allowing simultaneous access of wired, wireless, and IoT terminals.
    Virtual network: is also called the overlay network. Virtualization technology is used to construct one or more overlay networks on top of the underlay network. Service policies are deployed on the overlay networks and are separated from the underlay network, decoupling services from networks. Multiple overlay networks can serve different services or customer segments.
Management layer
  The management layer provides management capabilities, such as configuration management, service management, maintenance and fault detection, as well as security threat analysis. Traditional campus networks use a network management system (NMS) for network management. Although the NMS can display the network status, it lacks flexibility and automatic management capability. Once service requirements change, the network administrator needs to re-plan services and manually modify configurations on network devices (including routers, switches, and firewalls), which is inefficient and error-prone. Therefore, maintaining network flexibility is critical in rapidly changing service environments, which requires the use of automation tools to assist in network and service management. Huawei's CloudCampus Solution uses iMaster NCE-Campus to implement automatic network and service provisioning.

## Slide 14
Notes:   iMaster NCE-Campus abstracts network devices and applications, and rapidly develops and automatically deploys applications through orchestration and by invoking abstract models. iMaster NCE-Campus illustrates the entire network but not independent devices (such as switches, routers, and APs) or discrete configurations (such as access control, QoS, and routing policies) on devices.
Application layer
  Based on iMaster NCE-Campus, Huawei CloudCampus Solution provides open standards-compliant APIs, through which various information including user identities, network resources, service quality, location information, and network topology, is opened up to upper-layer services. Third parties can use these APIs to customize innovative service applications based on service demands, meeting service requirements in multiple fields such as education, commerce, enterprise, and government.

## Slide 15: Architecture of a Virtualized Campus Network
Underlay (physical network layer)
Fabric
Core
Aggregation
Aggregation
Access
Access
Border
BGP EVPN
BGP EVPN
External network
Network service resources
Edge
Edge
Wired access
Wireless access
Overlay (virtual network layer)
VN 1
VN N
VRF+VNI
VRF+VNI
Network egress
IP/VLAN
Access point
Network services
Fabric instantiation
OSPF
VXLAN
Underlay: a physical topology consisting of physical network devices (such as switches, APs, firewalls, and routers) that provide interconnection capabilities for all services on the campus network. It is the basic bearer network for campus service data forwarding.
Fabric: a network with pooled resources abstracted from the underlay network. When creating an instantiated VN, you can select network resources on the fabric.
Virtual network (VN): a logically isolated virtual network instance that is constructed by instantiating a fabric. One VN corresponds to one isolated network (service network), for example, R&D network.
Notes: On a large- or medium-sized campus network, the virtualization solution may need to be used to decouple services from the network, so as to build a multi-purpose network and achieve flexible, fast service deployment without changing the basic network infrastructure. Using such a solution means that the virtualized campus network architecture must be different from the traditional network architecture.
This slide presents the virtualized campus network architecture. The underlay is the physical network layer, and the overlay is the virtual network layer constructed on top of the underlay using the Virtual Extensible LAN (VXLAN) technology.

## Slide 16: Network Nodes on a Virtualized Campus Network
Egress gateway: is an egress device of the campus network, which can be an AR router or a firewall.
Firewall node: This node is required when Layer 4 to Layer 7 security policies are deployed. It can be deployed in off-path mode or at the campus egress.
Border node: implements communication between the fabric and external networks. It is typically a core switch.
Transparent node: It does not need to support VXLAN.
Edge node: is a fabric edge device that connects user-side devices to the fabric. Data packets from wired users enter the VXLAN network through edge nodes.
Access node: is typically an access switch (wired access node) or an AP (wireless access node). Wired access nodes can function as edge nodes, that is, VXLAN is deployed across core and access nodes. If wired access nodes do not need to support VXLAN, aggregation nodes can function as edge nodes — that is, VXLAN is deployed across core and aggregation nodes — in which scenario policy association can be deployed on wired access nodes and edge nodes.
Fabric domain (VXLAN)
Access domain
Border node
Transparent node
Edge node
Access node
VXLAN-capable nodes
Egress gateway
Firewall node
Notes: On a fabric network, a VXLAN tunnel endpoint (VTEP) can function as either a border or edge node:
  Border node: It corresponds to a physical network device and forwards data between the fabric and external networks. In most cases, border nodes are VXLAN-capable core switches.
  Edge node: It corresponds to a physical network device. User traffic enters the fabric from the edge node. Typically, edge nodes are VXLAN-capable access or aggregation switches.
Policy association:
  Policy association provides a solution to contradiction between policy strengths and complexity on large campus networks. In the solution, user access policies are centrally managed on the gateway devices and enforced by gateway and authentication access devices.
  After policy association is configured, authentication access devices can transparently transmit BPDUs and report user logout and user access positions in real time. In addition, the authentication control device requests authentication access devices to enforce user access policies, thus controlling user access to the network.

## Slide 17: Key Technologies for Virtualized Campus: DHCP-based Plug-and-Play of Network Devices
The network administrator has deployed the DHCP service on the network. (It is recommended that the DHCP service be deployed on the AR router.)
In addition to delivering an IP address to the device to be deployed, the DHCP server uses DHCP Option 148 to notify the device of the iMaster NCE-Campus IP address and port number.
AR
1
2
DHCP request
3
The DHCP server responds to the device with required information, including the IP address, DNS, working mode, and Option 148 (containing the iMaster NCE-Campus IP address and port number).
4
The switch initiates a registration request to iMaster NCE-Campus.
Devices supported: AR routers, switches, APs
Switch to be deployed

## Slide 18: Key Technologies for Virtualized Campus: VXLAN-based Multi-purpose Network
OA
VC
Security protection
Internet
OA
VC
Security protection
Internet
OA
VC
Security protection
VXLAN
VN1
OA VN
VN2
VC VN
VN3
Security protection VN
Multiple services carried on one physical network
Automated physical network deployment
Automated VN provisioning
Automated service policy delivery
Notes: Using virtualization technologies, multiple virtual networks (VNs) can be created on top of a physical network. Different VNs are used for different services, such as OA, videoconferencing, and security protection.
VC: Video Conference

## Slide 19: Key Technologies for Virtualized Campus: Admission Authentication
Authentication point
VXLAN
Border
Core
Aggregation
Access
Egress
AP
Edge
Edge
Built-in server of iMaster NCE-Campus
RADIUS server & Portal server
Sales
(802.1X)
Guest
(Portal)
Request for user identity authentication
Transfer of user identity credential
User identity verification
User policy authorization
1
2
3
4
Phone
(MAC)
Notes: Request for user identity authentication: The terminal sends its identity credential to the admission device.
User identity authentication: The admission device sends the identity credential to the admission server for identity authentication.
User identity verification: The admission server stores user identity information and manages users. After receiving the identity credential of the terminal, the admission server verifies the identity of the terminal, determines whether the terminal identity is valid, and delivers the verification result and policy to the admission device.
User policy authorization: As a policy enforcement device, the admission device implements policy control over the terminal based on the authorization result provided by the admission server, for example, permitting or denying network access, or performing more complex policy control on the terminal. Complex policy control can be increasing or decreasing the forwarding priority of the terminal, or restricting the network access rate of the terminal.

## Slide 20: Key Technologies for Virtualized Campus: Policy Association
If access switches do not support VXLAN, policy association can be deployed between access and aggregation switches (gateways). The gateway manages user access policies in a unified manner, and the access switch enforces user access policies.
  Authentication control points and enforcement points are connected through CAPWAP tunnels (which are the management tunnels used by policy association).
  CAPWAP tunnels implement user association, message transmission, user authorization policy delivery, user information synchronization, and other functions.
  After policy association is configured, authentication enforcement points can transparently transmit BPDUs, report user logout and access locations in real time, and enforce user access policies, thereby controlling user access to the network.
CSS/iStack
Authentication control point
Authentication enforcement point
CAPWAP tunnel
VXLAN
Border
Edge
Edge
Edge
L2
L3
Access
AP
Access
Policy association
Policy association
Link aggregation
Core
Aggregation
Access
Egress
Notes: CAPWAP: Control and Provisioning of Wireless Access Points

## Slide 21: Key Technologies for Virtualized Campus: Free Mobility
Free mobility manages policies and controls permissions based on security groups. Regardless of user locations and IP addresses in use, this technology ensures that users can obtain consistent network permissions and corresponding policies can be enforced on the users.
Campus network
User A
User B
User C
Admission authentication
Admission authentication
Admission authentication
Security group and policy delivery
3
4
2
Sales user
security group
R&D user
security group
Server
resource group
Permission control policies
1
Create security groups. A security group is a group of users or network resources that have the same network access policies.
Define permission control policies based on security groups and deliver the policies to network devices.
Authorized security groups are assigned to the users who pass admission authentication.
After user traffic enters the network, network devices enforce policies based on the corresponding source and destination security groups of the traffic.
Notes: Free mobility introduces the concept of security group. Security groups are related only to user identities and are completely decoupled from network information such as user VLANs and IP addresses.
User policy management and permission control are performed based on security groups.

## Slide 22: Overview of Large- and Medium-Sized Virtualized Campus Network Design
Virtualized campus network design
Underlay
network design
Network architecture design
Basic service design
LAN automation design
Fabric design
Networking and node design
External network interconnection design
Network service resource planning
Access management
Overlay
network design
VN design
Policy design
VN access design
Admission control and free mobility design
User management design
Admission control design
Free mobility design
WLAN design
Networking scheme
Network security design
Egress security
Intranet security
O&M design
Telemetry
Visualization
Analysis
Optimization

## Slide 23
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 24: Underlay Design Outline
1. Network architecture design
Network architecture design
Network egress design
2. Basic service design
VLAN planning
IP address planning
DHCP service design
Routing design
3. LAN automation design
Network deployment design
Underlay network automation

## Slide 25: Network Architecture Design Overview
Overall design principles:
  Tree and ring network topologies
Reliability considerations:
  High reliability of nodes: CSS, iStack, and hot standby (AC, firewall, etc.)
  High reliability of links: redundant links and Eth-Trunk
Network layer design principles:
  Two-layer networking: The network layers are simple, and faults are easy to locate.
  Three-layer networking: applies to campuses with multiple buildings or regions.
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
DC
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Large- and medium-sized campus networks often use the tree topology with the core layer as the root, as shown in the figure. This topology is stable and easy to expand and maintain. A campus network can be divided into the following layers: access layer, aggregation layer, core layer, and multiple zones including the egress zone, DC zone, and O&M zone. Internal changes within a module have limited impact on other modules, facilitating fault location.
Terminal layer
  The terminal layer involves various types of terminals that access the campus network, such as PCs, printers, IP phones, mobile phones, and cameras.
Access layer
  The access layer provides various access modes for users and is the first network layer for terminals to access a campus network. The access layer is usually composed of access switches. There are a large number of access switches that are sparsely distributed in different places on the network. In most cases, an access switch is a simple Layer 2 switch. If the terminal layer has wireless terminals, the access layer provides APs that access the network through access switches.
Aggregation layer
  The aggregation layer connects the access layer to the core layer. The aggregation layer forwards horizontal traffic between users and forwards vertical traffic to the core layer. It can also function as the switching core for a department or zone and connect the department or zone to the exclusive server zone. In addition, the aggregation layer can further extend the quantity of access terminals.

## Slide 26
Notes: Core layer
  The core layer is the core for data exchange on a campus network. It connects various components of a campus network, such as the DC zone, aggregation layer, and egress zone. The core layer is responsible for high-speed interconnection of the entire campus network. High-performance core switches need to be deployed to implement high bandwidth utilization and fast convergence upon network faults. It is recommended that the core layer be deployed if a campus has more than three departments. For a wireless network, the core layer includes ACs. After a wireless terminal accesses the network through an AP, the AP communicates with an AC using a CAPWAP tunnel.
Egress zone
  The campus egress is the boundary between a campus network and an external network. Internal users of the campus network can access the external network through the campus egress zone, and external users can access the internal network through the campus egress zone. The campus egress zone typically has routers and firewalls deployed. The routers enable interconnection between internal and external networks, and the firewalls provide border security protection.
DC zone
  In the DC zone, service servers such as the file server and email server are managed, and services are provided for internal and external users.
O&M zone
  In the O&M zone, network servers such as the network management system and authentication server are managed. The standard NMS interacts with network devices through the Simple Network Management Protocol (SNMP) and provides configuration, management, and maintenance functions. For example, it provides network topology and port display management, network device configuration management, network fault diagnosis and alarm, as well as network performance and status analysis. Huawei CloudCampus Solution provides intelligent O&M based on NETCONF and telemetry.
In addition to these, a campus may have a demilitarized zone (DMZ). The DMZ contains public servers that can be accessed by guests (non-employees), therefore the access permission to this zone is strictly controlled.

## Slide 27: Network Architecture Design (1)
In actual applications, you can choose the three-layer or two-layer architecture based on the network scale or service requirements.
Block 1
Block N
Three-layer architecture
Two-layer architecture
Core layer
Aggregation layer
Access layer
Core layer
Access layer
Application scenario: large campus networks with a large number of users or involving multiple buildings (for example, campus networks of high education institutions)
Application scenario: small- and medium-sized campus networks involving only one building
Layered design
Modular design
Redundancy design
Symmetric design
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Layered design:
  Each layer can be considered a well-structured module with specific roles and functions. This layered structure is easy to expand and maintain, reducing the design complexity and difficulty.
Modular design:
  Each module corresponds to a department, function, or service area. Modules can be expanded flexibly based on the network scale, and adjustment in a department or area does not affect other departments or areas, which facilitates fault locating.
Redundancy design:
  Dual-node redundancy design can ensure device-level reliability. Appropriate redundancy improves reliability, but excessive redundancy makes O&M difficult. If dual-node redundancy cannot be implemented, you may consider card-level redundancy, such as dual main control boards or switch fabric units (SFUs), for modular core switches or egress routers. In addition, Eth-Trunk can be deployed for important links to ensure link-level reliability.
Symmetric design:
  A symmetric network structure makes the topology clearer and facilitates service deployment, protocol design and analysis.

## Slide 28: Network Architecture Design (2)
During network design, you can use the bottom-up method to determine the type of architecture based on the network scale.
1. Determine the number of access ports
2. Select access switches
3. Calculate the number of access switches
4. Select aggregation switches
5. Calculate the number of uplinks of access switches
6. Calculate the number of aggregation switches
Three-layer architecture
Two-layer architecture
Single-layer architecture
If a single port corresponds to a single user or a specific number of users, you can determine the number of required access ports based on the network scale.
Determine the appropriate access switches (including access capability, port density, and uplink mode) based on the port rates of terminals' NICs.
Quantity = Number of access ports/Number of downlink ports on a switch
Select the appropriate aggregation switches based on the uplink port rates of access switches.
Quantity = Required network bandwidth/Uplink port rate of an access switch
Quantity = (Number of access ports x Access port rate x Bandwidth oversubscription ratio)/Uplink port rate of an access switch
Quantity = Number of uplinks of access switches/Number of downlink ports of an aggregation switch
N
Y
Y
N
Quantity > 1?
Quantity > 1?
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Design method of the hierarchical model for common network architectures:
  Determine the number of access switch ports based on the network scale. Typically, one port corresponds to one terminal or one network access point (for example, AP).
  Select switches based on the port rates of terminals' NICs.
  Calculate the number of access switches.
    Number of access switches required = Number of access ports/Number of downlink ports on a switch
    If the calculation result is greater than 1, aggregation switches need to be deployed. Otherwise, use the single-layer architecture.
  Select aggregation switches based on the uplink port rates of access switches.
  Calculate the number of uplinks of access switches using either of the following methods:
    Based on the network bandwidth: Number of uplinks = Network bandwidth/Uplink port rate of an access switch
    Based on the network scale: Number of uplinks = (Number of access ports x Access port rate x Bandwidth oversubscription ratio)/Uplink port rate of an access switch

## Slide 29
Notes:   Calculate the number of aggregation switches.
    Number of aggregation switches required = Number of uplinks of access switches/Number of downlink ports of an aggregation switch
    If the result is greater than 1, select the three-layer architecture. Otherwise, use the two-layer architecture.
Notes:
  In the preceding calculations, the calculation results need to be rounded up.
  Bandwidth oversubscription ratio = Actual downlink bandwidth of a service/Maximum physical bandwidth provided by a single switch
    Traffic of the service may exhaust the maximum physical bandwidth. However, this probability is low in most cases. Generally, network planning focuses on service experience in common situations. That is, certain bandwidth redundancy is designed when actual possible bandwidth is met.
    Before designing a network traffic oversubscription ratio, we need to understand the service applications and features to be deployed on the network and determine the network services and traffic models. Additionally, the volume and ratio of traffic must be thoroughly considered before designing an oversubscription ratio and selecting devices.

## Slide 30: Network Egress Design Overview
As the boundary between a campus network and external networks (including the Internet and WAN), the egress zone is responsible for communication and security protection between internal and external networks.
The requirements for the egress zone design are as follows:
  Network connectivity: Internal users can access external networks. If the campus network provides access for external users, external users should be able to access the internal network.
  Network security: To ensure that the campus network is secure and controllable, especially border security, firewalls and the Intrusion Prevention System (IPS) devices need to be configured. Security components are selected based on security requirements and investment scales.
  Flexible access modes: Various access modes are provided, including LAN-side and WAN-side access.
  Strong service control capability: Service deployment and isolation are easy to implement, and various VPN access modes are provided, including IPsec VPN, SSL VPN, and MPLS VPN.
Core layer
Aggregation layer
Access layer
iStack/CSS link
Terminal layer
DC
O&M zone
Internet
WAN
Egress zone
Network Architecture Design
Basic Service Design
LAN Automation Design

## Slide 31: Egress Network Service Scenarios (1)
Internet
Egress zone
Security
NAT
Remote access
Multi-campus interconnection
Security
Multi-campus interconnection
WAN
Service Scenario | Sub-scenario | Description | Applicable Network
Security | Firewall | A firewall uses security zones to divide networks and identify packet forwarding paths. When a packet is transmitted between security zones, the firewall can perform a security check and enforce corresponding security policies. | Internet and leased line
 | URL filtering | URL filtering controls internal users' access to external URLs. It allows or forbids users to access certain web page resources, thereby regulating online behaviors. | Internet
NAT | Source NAT | Intranet users usually use private IP addresses to access the Internet. To ensure successful access to Internet services, private IP addresses must be translated into public IP addresses. | Internet
 | NAT server | Servers deployed on the campus network, such as the file server, can be mapped to the Internet using public IP addresses or public IP addresses and port numbers through the NAT server, so that they can be accessed from the Internet. | Internet
Network Architecture Design
Basic Service Design
LAN Automation Design

## Slide 32: Egress Network Service Scenarios (2)
Internet
Egress zone
Security
NAT
Remote access
Multi-campus interconnection
Security
Multi-campus interconnection
WAN
Service Scenario | Sub-scenario | Description | Applicable Network
Remote access | SSL VPN access | The SSL VPN gateway connects to the Internet and provides SSL VPN services for mobile office users (employees on business trips). After a mobile user uses a terminal (such as a laptop or smart phone) to establish an SSL VPN tunnel with the gateway, the user can remotely access intranet resources such as the web server, file server, and mail server through the SSL VPN tunnel. | Internet
Multi-campus interconnection | Traditional MPLS VPN interconnection | CE devices can be connected to the MPLS VPN network. | Leased line
 | IPsec VPN interconnection | IPsec VPN tunnels are established between multiple campuses to ensure secure data transmission on a low-security bearer network. | Internet and leased line
Network Architecture Design
Basic Service Design
LAN Automation Design

## Slide 33: Network Egress Design: WAN-side Connection
Internet
WAN
Internet
Internet2
/WAN
Internet1
Optional
WAN
Internet
WAN
Internet
LTE
Single router and single egress
Single router and dual egresses
Dual routers and single egress
Dual routers and dual egresses
Dual routers and multiple egresses
Optional
Optional
Optional
Optional
Router as egress
Firewall as egress
Internet
WAN
Internet
Internet2
/WAN
Internet1
Internet2
/WAN
Internet1
Single firewall and single egress
Single firewall and dual egresses
Dual firewalls and single egress
Dual firewalls and dual egresses
Hot standby heartbeat link
The following factors need to be considered during the WAN-side connection design:
Egress link type
SD-WAN requirements
Protocol interconnection requirements
Must be ARs
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: To ensure reliability, routers and firewalls are usually deployed in redundancy mode. It is recommended that devices be deployed in redundancy mode at the egress of a large- or medium-sized campus network.
WAN-side connection design:
  Egress link type
    Ethernet: Select routers (NE or AR series) or firewalls as egress devices.
    For non-Ethernet links, such as EI, CE1, and CPOS links, select routers as egress devices.
  SD-WAN requirements:
    If there are SD-WAN requirements, select AR routers as egress devices.
    If there is no SD-WAN requirement, select firewalls or NE routers as egress devices.
  Protocol interconnection requirements:
    If BGP runs between egress devices and external networks, it is recommended that routers be used as the egress devices. This is because routers have a larger number of routing table entries and higher performance and many routing policies need to be deployed on egress devices.

## Slide 34: Network Egress Design: LAN-side Connection
CSS
A single firewall is connected to a single core switch
Two firewalls are connected to a CSS of core switches in square-looped mode
CSS
A single router is connected to a single core switch
Two routers are connected to a CSS of core switches in square-looped mode
CSS
Two firewalls are connected to a CSS of core switches in dual-homed mode
CSS
Two routers are connected to a CSS of core switches in dual-homed mode
LAN-side connection design
It is recommended that core switches be deployed in cluster or stack mode to form a logical switch, thereby ensuring reliability of core switches.
Egress gateways are usually deployed in a two-node cluster to meet reliability requirements. Different types of gateways differ slightly in their two-node cluster deployment capabilities. For example, the link between the active and standby firewalls in a two-node cluster is used only for heartbeat and entry synchronization, and not for traffic forwarding. The link between routers functioning as gateways can be used for service interconnection and for synchronizing and backing up information between them.
It is recommended that egress gateways and core switches be connected in dual-homed mode and link aggregation be used to enhance the link-level reliability and forwarding bandwidth between devices.
Hot standby heartbeat link
CSS
Link aggregation
Network Architecture Design
Basic Service Design
LAN Automation Design

## Slide 35: Network Egress Design: Firewall Deployment in Off-Path Mode
Deploying firewalls in off-path mode
In addition to in-path deployment, firewalls can be deployed in off-path mode. Generally, off-path deployment of firewalls is selected based on the following principles:
  Whether traffic passes through a firewall can be flexibly defined.
  Expansion is easy, for example, in the network reconstruction scenario.
  A firewall fault has little impact on services.
On a campus network:
  If a firewall is used as the egress gateway, the firewall usually provides functions such as security policies, NAT, and VPN gateway. If the north-south traffic must pass through the firewall and if scalability is not considered, in-path deployment is recommended for the firewall.
  If a router is used as the egress gateway and the firewall only provides high-level security functions, such as intrusion prevention, antivirus, and URL filtering, off-path deployment can be used for the firewall.
Hot standby heartbeat link
Stack
Link aggregation
Two firewalls are connected to border nodes in off-path mode
Traffic from PC1 to the Internet
Traffic from PC2 to PC3
WAN
Internet
OA PC1
OA PC2
R&D PC3
Network Architecture Design
Basic Service Design
LAN Automation Design

## Slide 36: VLAN Design
You are advised to assign consecutive VLAN IDs to ensure proper use of VLAN resources.
You are advised to reserve a certain number of VLANs for future expansion.
VLANs are classified into service VLANs, management VLANs, and interconnection VLANs.
Typically, VLANs are assigned based on interfaces. According to different design principles, interfaces of access switches are added to different VLANs so that users of different service types can be isolated.
Service VLAN design
Management VLAN design
VLAN assignment based on geographical areas
VLAN assignment based on logical areas
VLAN assignment based on the personnel structure
VLAN assignment based on service types
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
In most cases, a Layer 2 switch uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches use the same management VLAN and their management IP addresses be on the same network segment.
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Service VLAN:
  Assign VLANs by logical area, geographical area, personnel structure, or service type.
    Assign VLANs by logical area. For example, VLANs 100 to 199 are used in the core network zone, VLANs 200 to 999 are used in the server zone, and VLANs 2000 to 3499 are used on the access network.
    Assign VLANs by geographical area. For example, VLANs 2000 to 2199 are used in area A, and VLANs 2200 to 2399 are used in area B.
    Assign VLANs by personnel structure. For example, department A uses VLANs 2000 to 2009, and department B uses VLANs 2010 to 2019.
    Assign VLANs by service type. For example, VLANs 200 to 299 are used in the web server zone, VLANs 300 to 399 are used in the app server zone, and VLANs 400 to 499 are used in the database server zone.
  If users are sensitive to the voice latency, the voice service must be preferentially guaranteed. It is recommended that the voice VLAN be planned for the voice service. Huawei switches can automatically identify voice data, transmit voice data in the voice VLAN, and perform QoS guarantee. When network congestion occurs, voice data can be preferentially transmitted.

## Slide 37
Notes:   If different users have the same multicast data service, you are advised to plan a multicast VLAN and bind the user VLANs to the multicast VLAN. This prevents the upstream gateway from copying multicast data in multiple user VLANs.
  Do not use VLAN 1 as a service VLAN.
Management VLAN:
  It is recommended that the management VLAN be planned for a Layer 2 switch and the VLANIF interface of the management VLAN be used as the management interface, through which the NMS manages the switch. It is recommended that all Layer 2 switches use the same management VLAN.
  It is recommended that service interfaces be used as management interfaces of Layer 3 devices (gateways and their upstream devices), and no management VLAN needs to be planned for these devices.
Interconnection VLAN:
  An interconnection VLAN is usually configured between two Layer 3 switches or between a Layer 3 switch and a router. Create VLANIF interfaces for Layer 3 interconnection.

## Slide 38: IP Address Design
IP addresses of a campus network are classified into service, management, and interconnection IP addresses.
Management IP address
A Layer 2 device uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches connected to a gateway be on the same network segment.
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
Service and interconnection IP addresses
Service IP addresses are the IP addresses of servers, hosts, and gateways.
It is recommended that gateway IP addresses have the same last octet, for example, .254.
The IP address range of each service must be clearly differentiated. The IP addresses for each type of service terminals must be contiguous and can be aggregated.
You are advised to use IP address segments with a 24-bit mask.
It is recommended that the interconnection IP address use a 30-bit mask. The core device uses an IP address with a small host address.
Employee
192.168.40.0/24
Partner
192.168.50.0/24
Guest
192.168.100.0/24
VLANIF 200: 192.168.200.1/30
VLANIF 200: 192.168.200.2/30
Interconnection VLAN 200
Service VLAN 40/50/100
VLANIF 40: 192.168.40.254
VLANIF 50: 192.168.50.254
VLANIF 100: 192.168.100.254
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: IP address planning complies with the following principles:
  Unique: Each host on an IP network must have a unique IP address.
  Contiguous: Node addresses of the same service must be contiguous to facilitate route planning and summarization. Contiguous addresses facilitate route summarization, thereby reducing the size of the routing table and speeding up route calculation and convergence.
  Scalable: Some IP addresses need to be reserved at each layer, so that no address segments or routing entries need to be added when the network is expanded.
  Easy to maintain: Device and service address segments need to be clearly distinguished from each other, facilitating subsequent statistics monitoring and security protection based on address segments. IP addresses can be planned based on VLANs.

## Slide 39
Notes: Pay attention to the following points when designing the three types of IP addresses:
  Service IP address:
    Considering the scope of a broadcast domain and easy planning, it is recommended that an IP address segment with a 24-bit mask be reserved for each service. If the number of service terminals exceeds 200, another IP address segment with a 24-bit mask is reserved.
  Management IP address:
    It is recommended that a Layer 3 device use a Layer 3 interface for management and deployment. The interface address is used as the management IP address for local login and communication with iMaster NCE-Campus.
  Interconnection IP address:
    Interconnection addresses are usually aggregated before being advertised. Therefore, you need to use contiguous and aggregatable addresses during planning.
In addition, if devices at the aggregation and access layers are interconnected, you need to plan IP addresses for policy association in some cases. The IP addresses must be planned based on the entire CloudCampus network and cannot conflict with other service IP addresses.

## Slide 40: Terminal-Oriented DHCP Service Design
Plan an independent DHCP server to allocate IP addresses to terminals.
You are advised to configure DHCP snooping on access devices to defend against attacks.
Network administrators can use either of the two mechanisms to assign IP addresses to hosts based on network requirements:
  Dynamic IP address assignment: An IP address is assigned to a host with a lease. This mode applies to scenarios where hosts require temporary access or IP addresses are insufficient, for example, portable computers of traveling employees and mobile terminals in cafes.
  Static IP address assignment: Fixed IP addresses are assigned to specified hosts or servers such as DNS servers.
When planning an address pool, filter out static IP addresses.
The lease needs to be planned based on the online duration of a client.
On a large or midsize campus network, the DHCP server and hosts are usually not on the same network segment. Therefore, you need to enable the DHCP relay function on the gateway.
DHCP server
DHCP clients
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Note: It is recommended that egress devices provide the DHCP service for network deployment. For details, see the network deployment section.

## Slide 41: Routing Design
Three-layer networking: scenario 1
Three-layer networking: scenario 2
OSPF area 0
OSPF area 1
OSPF area 2
Core (border)
Aggregation
Access (edge)
OSPF area 0
Core (border)
Aggregation
Access (edge)
Three-layer networking:
  Scenario 1 (multi-area): The interconnection links between core switches belong to OSPF area 0, and the links connecting the core switch to each aggregation switch belong to an independent OSPF area.
  Scenario 2 (single-area): Core, aggregation, and access switches all work in OSPF area 0. If the number of switches to be deployed in a network area is fewer than 100, scenario 2 is recommended.
  Two-layer networking:
  OSPF runs only between core switches and access switches. In this case, only OSPF area 0 needs to be planned on the entire network.
CSS/iStack link
Network Architecture Design
Basic Service Design
LAN Automation Design
CSS/iStack link
Notes: The routing design includes internal and egress routing design for a campus network.
  Internal routing design:
    The routing design must support communication between devices, between terminals, and between devices and terminals on the campus network, as well as communication between these devices/terminals and the external network.
    It is recommended that you design internal routes based on the gateway location.
      If gateways are deployed at the aggregation layer, routes need to be deployed at core and aggregation layers. Routing tables can be dynamically updated along with network topology changes, so an Interior Gateway Protocol (IGP), such as Open Shortest Path First (OSPF), is recommended.
      If gateways are deployed at the core layer, you only need to configure routes at the core layer. It is recommended that static routes be used preferentially.
  Egress routing design:
    Egress routes must enable internal terminals to access the Internet and WAN.
    A large or medium-sized campus network usually has a large number of branches. The egress needs to support multiple links for Internet access and mutual communication between enterprise branches. For this purpose, a large number of routes need to be imported to the campus network. Therefore, you are advised to plan a dynamic routing protocol such as OSPF.

## Slide 42
Notes: It is recommended that OSPF be planned for a campus network. The OSPF design precautions are as follows:
  You are advised to use the IP addresses of loopback interfaces as the router IDs.
  Areas are divided according to the core, aggregation, and access layers. It is recommended that egress routers and core switches be deployed in the backbone area. The design of non-backbone areas depends on the geographical location and performance of devices.
Note:
  This slide describes the routing design in the scenario when VXLAN is deployed across core and access layers.
  In the scenario where VXLAN is deployed across core and aggregation layers, the routing design (for example, OSPF area division) is the same as when VXLAN is deployed across core and access layers. The only difference is that the aggregation device is the border of the routing domain.

## Slide 43: Network Deployment Design
CSS/iStack link
Native AC
Core
Aggregation
Access
Traditional deployment
Plug-and-play
Traditional deployment (via CLI or web system):
Egress router
Egress firewall
Core switch
Standalone AC
Plug-and-play:
Aggregation switch
Access switch
AP
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Typically, egress and core devices on large- and medium-sized campus networks are centrally deployed in a core equipment room. Services transmitted on these devices are complex and their locations on the network are important. In most cases, network engineers need to commission devices onsite during the deployment. Therefore, you are advised to use the web system or CLI to deploy devices at the core layer and upper layers (including core devices, standalone ACs connected in off-path mode, and egress devices).
A large number of devices (including aggregation devices, access devices, and APs) are deployed at lower layers of the core layer, and service configurations of these devices are similar. Therefore, you are advised to use the DHCP option mode to achieve plug-and-play of devices, thereby simplifying the deployment.
Note: Core switches obtain basic configurations such as IP addresses using the CLI. Once they establish management channels with iMaster NCE-Campus, iMaster NCE-Campus will automatically deliver services to them.

## Slide 44: Network Deployment Process: Device Onboarding Before Planning
Core
Aggregation
(device to be deployed)
Internet
Egress gateway
(DHCP server)
Preparations
An administrator deploys the DHCP server function on the egress gateway or deploys an independent DHCP server on the network, and then configures DHCP Option 148.
The administrator imports switch information (ESN, device model, etc.) to iMaster NCE-Campus. (Batch import is supported.)
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
Switch onboarding process
After an aggregation switch is powered on, it proactively sends Link Layer Discovery Protocol Data Units (LLDPDUs) to negotiate with the core switch in an effort to obtain the PnP VLAN ID.
The aggregation switch uses the PnP VLAN to obtain an IP address and Option 148 from the DHCP server.
The aggregation registers with iMaster NCE-Campus based on iMaster NCE-Campus information obtained from the DHCP server.
After an access switch is powered on, it follows a similar process as the aggregation switch (steps 1-3).
Switches use LLDP to discover the network topology and report their topology information to iMaster NCE-Campus through NETCONF. iMaster NCE-Campus then discovers the network topology based on the received topology information.
The administrator performs network planning and configuration provisioning on iMaster NCE-Campus.
Access
(device to be deployed)
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: In the Huawei's CloudCampus Solution, a DHCP server helps implement plug-and-play (PnP) of switches, eliminating the need to manually enable NETCONF and configure iMaster NCE-Campus address on switches.
  After switch starts with empty configuration, it sends a Request message containing VLAN 1 (default PnP VLAN ID) to the DHCP server.
  Alternatively, a user-defined VLAN can be used by the device to initiate a DHCP request. This VLAN is called PnP VLAN.
In this example, assume that a VLAN different from VLAN 1 is used as the PnP VLAN. To achieve this, you need to configure the PnP VLAN on the core switch or configure the PnP VLAN on iMaster NCE-Campus after the core switch is managed by iMaster NCE-Campus.
In this deployment mode, devices are deployed and onboarded before the network topology is determined.
  During network deployment, the administrator uses the recommended method to deploy and onboard devices. Link aggregation has not been configured when the devices are installed and onboarded. Therefore, if there are aggregated links between the devices, redundant links will be blocked by STP. After the devices are onboarded and register with iMaster NCE-Campus, the administrator checks the topology and deploys link aggregation and service configurations on iMaster NCE-Campus.
This deployment process applies to scenarios with scattered installation time.

## Slide 45: Network Deployment Process: Planning Before Device Onboarding
Preparations
An administrator deploys the DHCP server function on the egress gateway or deploys an independent DHCP server on the network, and then configures DHCP Option 148.
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
The administrator plans the network topology using the template (an Excel file) provided by iMaster NCE-Campus and then imports the template containing the planned data to iMaster NCE-Campus.
Switch onboarding process
After aggregation and access switches are powered on, they each complete PnP VLAN negotiation and DHCP message exchange processes, and then register with iMaster NCE-Campus.
Aggregation and access switches are then managed by iMaster NCE-Campus and report LLDP neighbor information to iMaster NCE-Campus. Subsequently, iMaster NCE-Campus compares the received LLDP information with that in the network topology planning document uploaded by the administrator. If any inconsistency is found, it reports an error. In this way, the administrator can correct the topology error as prompted.
The administrator performs offline device pre-configuration on iMaster NCE-Campus.
Switches automatically obtain their configurations after they are onboarded.
Core
Aggregation
(device to be deployed)
Internet
Egress gateway
(DHCP server)
Access
(device to be deployed)
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: This deployment process is applicable to scenarios with concentrated installation time. The administrator is advised to plan the network before onboarding devices. If the network cannot be planned in advance, the administrator can onboard devices first and then determine the network topology.
In this deployment mode, the network is planned before devices are deployed and onboarded.
  During network deployment, the administrator plans the network topology by entering device ESNs and specifying stack members and aggregated links on iMaster NCE-Campus.
  Alternatively, the administrator can import the preceding planning information in batches using a template. Using a template to import data in batches simplifies operations and is therefore recommended.
  Then, the administrator uses the recommended method to deploy and onboard devices.
  After devices go online and register with iMaster NCE-Campus, iMaster NCE-Campus automatically checks whether the actual topology of the devices is the same as the planned one. If cables are incorrectly connected during installation, iMaster NCE-Campus immediately notifies the administrator.
Note: Parameters can be planned for an Eth-Trunk interface. After a device goes online, it automatically obtains the corresponding Eth-Trunk configuration.

## Slide 46: Underlay Network Automation
Complete automatic deployment of the underlay network on iMaster NCE-Campus.
Border
Edge
Edge
The administrator specifies roles of fabric nodes on iMaster NCE-Campus.
iMaster NCE-Campus automatically discovers the network topology.
1
2
Border
Edge
Edge
OSPF Area 0
OSPF adjacency
3
Automatically completes OSPF configuration.
When enabling automatic routing domain configuration, you can define OSPF areas (single-area or multi-area) and configure the packet authentication function.
Network Architecture Design
Basic Service Design
LAN Automation Design
Notes: Automatic routing domain configuration: After this function is enabled, the underlay network can be automatically configured. You can specify sites for automatic routing domain configuration and specify OSPF routing parameters. Currently, the following parameters are supported:
  Area: In the single-area scenario, all devices belong to Area 0. In the multi-area scenario, border nodes belong to Area 0, and each edge node and its connected border node belong to an area.
  Network type: You can set the OSPF network type to broadcast, P2MP, or P2P.
  Encryption: You can set the encryption mode between adjacent devices to HMAC-SHA256, MD5, or none.
  OSPF GR: You can enable OSPF GR.
Before enabling the automatic routing domain configuration function, you need to plan network resources required for underlay network automation.
  Underlay devices (corresponding network scope of the fabric) are connected through VLANIF interfaces at Layer 3, and you need to assign a VLAN to each interconnection link.
  The VLANIF interfaces for connecting devices are automatically assigned interconnection IP addresses with a 30-bit subnet mask.

## Slide 47
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 48: Fabric Design Overview
Underlay (physical network layer)
Fabric
Fabric
External network
Network service resource
Wired access
Wireless access
Fabric design
The campus fabric is a resource pooling network abstracted from the underlay network. The fabric virtualizes underlay network resources into a resource pool to implement "one network for multiple purposes".
The fabric design involves the following:
Fabric networking and node design
Design for the interconnection between the fabric and external network
Fabric network service resource planning
Fabric access management
External network
IP/VLAN segment
Access point
VN
Network service resource
Notes: Fabric network service resource planning:
  In the resource model design for the fabric network, network service resources are created on the border node so that service terminals on the campus network can access service resources in the network management zone, such as the DHCP server and admission server.
  Multiple network service resources can be created, and one network service resource model can contain access addresses of multiple service resources.
  If only a few network service resources need to be accessed in the network management zone, you are advised to plan these resources in the same network service resource model. This saves interconnection VLAN and IP address resources and simplifies route configuration for the network management zone.
Fabric access management:
  Configuring access management for the fabric involves configuring authentication control points and planning access point resources for VN creation.
  The wired access point resource refers to switch interfaces to which terminals will connect, and the wireless access point resource refers to SSIDs with which terminals will associate.

## Slide 49: Fabric Networking Scenarios
In Layer 2 or Layer 3 networking, border or edge nodes can function as gateways.
  Centralized gateway: A border node functions as the gateway to implement centralized management and simplify O&M.
  Distributed gateway: Edge nodes function as gateways to facilitate network expansion.
Recommended networking scenario:
  Centralized gateway, VXLAN across core and access layers, and native AC deployed at the core layer
  Distributed gateways, VXLAN across core and aggregation layers, and native AC deployed at the aggregation layer
Networking | Border Node Location | Edge Node Location | AC Deployment Mode | Recommended
Centralized gateway | Core | Access | Native AC on a core device | Yes
 |  |  | Independent AC attached to a core device in off-path mode | No
 |  | Aggregation | Native AC on a core device | No
 |  |  | Independent AC attached to a core device in off-path mode | No
Distributed gateway | Core | Aggregation | Native AC on an aggregation device | Yes
 |  |  | Independent AC attached to a core device in off-path mode | No
 |  | Access | Independent AC attached to a core device in off-path mode | No

## Slide 50: Fabric Networking Design: VXLAN Coverage Range
Core layer
Aggregation layer
Access layer
VXLAN
VXLAN
CAPWAP
CAPWAP
VXLAN range | VXLAN across core and access layers | VXLAN across core and aggregation layers
Application scenarios | Automatic end-to-end service deployment is required on the entire network. Recommended: Number of switch nodes < 1,000 | Existing access switches on the live network need to be reused. Alternatively, low-cost Huawei switches that do not support VXLAN need to be deployed at the access layer to reduce costs. Recommended: Number of switch nodes < 3,000
Network construction costs | Compared with the VXLAN solution from the core layer to the aggregation layer, this solution has higher network construction costs. | Compared with the VXLAN solution from the core layer to the access layer, this solution has lower network construction costs.
VXLAN not supported
VXLAN not supported

## Slide 51: Fabric Networking Design: Centralized and Distributed Gateways
Layer 3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
Layer 2 gateway
Layer 2 gateway
PC2
192.168.2.1/24
The Layer 3 gateway is deployed on a single device. All inter-subnet traffic is forwarded by the gateway to implement centralized traffic management.
Advantage: Inter-subnet traffic is managed in a centralized manner, simplifying gateway deployment and management.
Disadvantage: The forwarding path is not optimal.
Layer 3 gateways are deployed on multiple devices, and VTEPs function as both Layer 2 and Layer 3 gateways.
Advantage: The forwarding path of inter-subnet traffic is optimal.
Disadvantage: Gateway deployment, fault locating, and network O&M of the distributed gateway networking are more complex than those of the centralized gateway networking. VTEPs need to exchange and maintain host routes.
Centralized gateway (recommended)
Distributed gateway
Layer 2/3 gateway
Layer 2/3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
PC2
192.168.2.1/24
Notes: In large- and medium-sized campus networks, the virtualization solution is classified into the centralized gateway solution and distributed gateway solution based on the user gateway location. You can select a gateway solution when creating a fabric on iMaster NCE-Campus.
In the centralized gateway solution, a border node functions as the gateway of all users, and all inter-subnet traffic is forwarded by the border node. In the distributed gateway solution, multiple edge nodes function as user gateways, and inter-subnet traffic is forwarded through these edge nodes.

## Slide 52: Fabric Networking Design: Gateway Solution Selection
Item | Centralized Gateway | Distributed Gateway
User gateway location | Border node | Edge node
Recommended edge location | Access switch | Aggregation switch
O&M deployment | A border node functions as the gateway of all users, and the native AC function is typically enabled on the border node to configure wireless services, simplifying O&M deployment. | Multiple edge nodes function as user gateways. This ensures that only part of the network is affected upon the failure of one gateway and facilitates network expansion. The native AC function is typically enabled on these edge nodes. Wireless services need to be configured on all edge nodes, complicating O&M deployment.
Terminal scale | ≤ 50,000 (calculated based on the number and specifications of centralized gateways). This solution is recommended when the number of terminals does not exceed 50,000. | ≤ 100,000 (calculated based on the number and specifications of distributed gateways). This solution is recommended when the number of terminals exceeds 50,000.
Core layer
Aggregation layer
Access layer
VXLAN
VXLAN
CAPWAP
CAPWAP
VXLAN not supported
VXLAN not supported
Notes: When designing the virtualization solution, first determine the gateway solution to be used. After the gateway solution is determined, you can perform end-to-end design on the entire campus network based on the selected gateway solution.
The centralized gateway solution supports only one border node, whereas the distributed gateway solution supports multiple border nodes.

## Slide 53: Fabric Node Design: Single-Border Networking
Core layer design:
  Deploy a cluster of core switches or a single core switch. It is recommended that large-capacity modular switches set up a cluster and S12700E series switches be used as core switches.
  It is recommended that ENP cards be used for interconnection with aggregation switches and that Eth-Trunk be deployed.
Aggregation layer design:
  Deploy a stack of aggregation switches or a single aggregation switch. It is recommended that a cluster of modular switches or a stack of fixed switches be deployed. Large-capacity switches (S12700E or S6700 series switches) are recommended.
  Eth-Trunk is recommended for interconnection with the core layer and access layer.
Access layer design:
  Wired access node: Each node can be a stack or a single device.
  Wireless access node: Fit AP
Server zone design:
  It is recommended that iMaster NCE-Campus, analyzer, and DHCP server be connected to the campus network through switches in the server zone.
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
DHCP server
Server zone
Border
Notes: An Ethernet Network Processor (ENP) card is embedded with the Huawei-developed ENP. The card can function as a common LPU to provide data access and switching services and also as a WLAN AC to provide wireless access control functions. In this way, the card achieves wired and wireless convergence.

## Slide 54: Fabric Node Design: Dual-Border Networking
Core layer design:
  Core switches are two logical devices. Large-capacity switches (S12700E series switches) are recommended. It is recommended that ENP cards be used for interconnection with aggregation switches and that Eth-Trunk be deployed.
Aggregation layer design:
  It is recommended that aggregation switches set up a stack to implement load balancing with core switches.
Access layer design:
  The design is similar to that in the single-border networking scenario.
Server zone design:
  It is recommended that iMaster NCE-Campus, analyzer, and DHCP server be connected to the campus network through switches in the server zone. It is recommended that aggregation switches set up a stack to implement load balancing with core switches.
Core layer
Access layer
Egress zone
DHCP server
Server zone
Border
Border
Aggregation layer
CSS/iStack link
Load balancing
Load balancing
Load balancing
Load balancing

## Slide 55: Fabric Node Design: Single/Dual-Border Networking Selection
 | Single-Border Networking | Dual-Border Networking
Description | The core switch is a logical device, which can be a physical standalone device or a CSS/iStack system. | Core switches are two logical devices, which can be two standalone physical devices or two CSS/iStack systems.
Characteristics | Easy management, configuration, and maintenance. Services may be affected during the device upgrade. | Complex management, configuration, and maintenance. The upgrade of core switches has little impact on services.
Application scenario | Simple network management, configuration, and maintenance are required. | The device upgrade has little impact on services. Core switches do not support clustering or stacking due to some reasons (such as the deployment distance).
Restrictions | There is no restriction. The single-border networking design is applicable to both centralized and distributed VXLAN gateway networking. | The dual-border networking design is applicable only to distributed VXLAN gateway networking.

## Slide 56: Fabric Node Design: Multi-Border Networking
Data Center
Border1
Edge
Edge
Internet
Border2
VXLAN
Scenario description: On a single campus network, multiple border nodes are connected to the same egress for egress redundancy.
Application scenario: A single campus network has multiple border nodes that are connected to the same external network, implementing reliability in non-stacking scenarios.
Border1
Edge
Edge
Internet
Border2
VXLAN
Scenario description: On a single campus network, multiple border nodes are connected to different egresses, and different services are transmitted through different border nodes.
Application scenario: A single campus network is connected to multiple external networks.
Internet
Border1
Edge
Edge
Internet
Border2
VXLAN
Scenario description: There are multiple campuses, and each campus is connected to its external network through an independent border node.
Application scenario: Multiple campus networks belong to the same fabric, and each campus network has an independent border node and egress network.
Campus 1
Campus 2

## Slide 57: Design for the Interconnection Between the Fabric and External Networks
L3 shared egress
L3 exclusive egress
L2 shared egress
Application scenario:
Multiple VNs need to access external networks, and these VNs use the same security policies.
Application scenario:
Multiple VNs need to access external networks, and each VN uses differentiated security policies.
Application scenario:
The border node does not function as the user gateway, and the user gateway must be located outside the fabric.
VRF
VRF
VRF
Shared VRF
Green VRF
VN1
Red VRF
VN2
VRF
Green VRF
VN1
Border
Border
Edge1
Border
L2 shared port
Edge2
Trust zone
VRF
Red VRF
VN2
Trust zone
Red zone
(user-defined zone)
Trust zone
User gateway
Notes: Terminals' network access traffic inside the campus network is forwarded through VXLAN tunnels. When the campus network needs to communicate with an external network, the data must pass through the border node. For example, a campus network communicates with an external network such as the Internet, DC, or another branch through the border node.
There are three interconnection modes between the fabric network and egress device: L3 shared egress, L3 exclusive egress, and L2 shared egress. The L3 shared egress mode is applicable to the scenario where the firewall does not need to perform security check on VNs and traffic of all VNs is transmitted in the same security zone. The L3 exclusive egress mode is suitable for the scenario where the firewall needs to perform security check on VNs and traffic of VNs is transmitted in multiple security zones. The L2 shared egress mode applies to the scenario where the user gateway must be located outside the fabric, and the border node and egress firewall are connected at Layer 2.
  In L3 shared egress mode, all VNs shares the same VPN instance (VRF) when accessing an external network, and static routes or dynamic BGP routes can be used for route advertisement between the border node and egress firewall.

## Slide 58
Notes:     Notes for static route design
      A border node learns global internal routes and it has a default route that points to the egress firewall.
      A VPN instance on the border node is configured with a static default route that points to the interface connected to the egress firewall.
      If there are multiple egress firewalls, you can deploy association between Network Quality Analysis (NQA) or Bidirectional Forwarding Detection (BFD) and static routes for route switching.
    Notes for BGP route design
      The border node establishes a BGP connection with a firewall, summarizes user routes in VPN instances, and imports the summarized routes to BGP.
  L3 exclusive egress mode: A firewall is partitioned into security zones with the same number as VPN instances and connects to the border node through physical interfaces or sub-interfaces. On the border node, a VPN instance is configured with a static default route that points to the corresponding physical interface or sub-interface of the security zone.
  L2 shared egress mode: The border node connects to the egress device through a Layer 2 interface, and the egress device is used as the user gateway to provide access to the external network.
Application scenario:
  Typically, there are only a few egress routes between the campus network and external network. Therefore, the L3 shared egress mode is recommended, and static routes are used for route advertisement between the border node and egress firewall.
  When the egress firewall needs to perform security check on each VN based on security zones, the L3 exclusive egress mode can be used.
  The L2 shared egress mode applies only to the scenario where the user gateway must be located outside the fabric. In higher education scenarios, if a BRAS is used as the user authentication point and PPPoE dialup is required on the network, the L2 shared egress mode can be used.

## Slide 59
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 60: VN Design Process
Fabric
VN1: OA network
VN2: R&D network
VN3: production network
VN design
Create multiple VNs based on the fabric.
Policy design
Divide users into security groups and define inter-group policies (policy control matrix).
Define inter-VN access policies based on the policy control matrix.
VN access design
Plan the mapping between VLANs of physical networks and BDs of VNs.
Plan terminal access modes.
VN1: OA network
VN2: R&D network
VN3: production network
VIP
Sales
Guest
Marketing
Testing
Code library
Server
Operations
…
…
Server
Programmer
VN1: OA network
VN2: R&D network
VN3: production network
5W1H
5W1H
5W1H
1
2
3
Security groups
Security groups
Security groups
Notes: VN design:
  VNs are generally divided based on services on a campus network. An independent service is assigned a VN, and VNs are isolated from each other by default. For example, on a school campus network, guest, teaching, IoT, and video surveillance services can each be assigned a separate VN. On an enterprise campus network, office network services, production network services, and R&D services can be allocated to different VNs.
Policy design:
  Some isolation requirements caused by different user roles can be fulfilled by deploying policy control technologies (such as free mobility).
  VNs are isolated by default. To enable mutual access between user groups within a VN, additional VN interworking configuration is required.
VN access design:
  Service data enters from a physical network to a VN through an edge node. Service data of users enters different VNs depending on the VLANs to which users belong. Therefore, during network design, you need to plan the mappings between VLANs of physical networks and BDs of VNs, and configure VLANs for wired and wireless users.

## Slide 61
Notes: 5W1H:
  Who: identity of an access user, for example, a company leader, a common employee, or a guest.
  Where: user access location, for example, access from within the campus, or remote access.
  What: type of the terminal used by the access user, for example, mobile phone or PC/laptop.
  When: time when a user accesses the network, for example, whether the user accesses the network in the daytime or at night.
  Whose: device owner, for example, whether the device is company-issued or BYOD.
  How: access mode of a user, for example, wired or wireless access.

## Slide 62: VN Design
Overlay (virtual network layer)
VN 1
VN 2
VN 3
VRF+VNI
VRF+VNI
VRF+VNI
1. Network service abstraction
Physical network resources are pooled through orchestration, and the network is abstracted into Fabric as a Service (FaaS). A VN is a FaaS instance and includes:
IP/VLAN segment
External network
Network service resource: The IP/VLAN segment is the capability provided by the VN for clients to use network resources.
Access point: Terminals access VNs through access points.
2. Network service orchestration
Deliver the mappings between VNIs and BDs.
Deliver the mappings between BDs and VLANs.
Deliver the IP address segments corresponding to VBDIF interfaces.
Deliver VRFs and bind them to VBDIF interfaces.
Deploy VNs
Underlay (physical network layer)
Fabric
Fabric
External network
Network service resource
Wired access
Wireless access
External network
IP/VLAN segment
Access point
VN
Network service resource
Deliver configurations

## Slide 63: VN Access Design
Service data enters from a physical network to VNs through the edge node. Service data of different users enters different VNs depending on the VLANs to which the users belong.
Wired user traffic is directly transmitted to VNs based on VLANs. After wireless user traffic is forwarded to the native AC, the native AC decapsulates CAPWAP packets and forwards the packets to the corresponding BDs based on the VLANs.
Static VLANs
A static VLAN is configured for wired users on an interface of an access switch.
A static service VLAN is configured for wireless users on an SSID.
Dynamically authorized VLANs
Authorized VLANs of wired users are delivered to the corresponding authentication points, which then send received user traffic to different VLANs.
For wireless users, 802.1X authentication and MAC address authentication support dynamic authorized VLANs, but Portal authentication does not. In Portal authentication, only the configured service VLAN takes effect.
Native AC
Native AC
VN1
VN2
Configure a static VLAN
Deliver the static service VLAN
VN1
VN2
Deliver the authorized user VLAN
Deliver the authorized user VLAN
Notes: Application scenarios:
  The static VLAN mode applies when terminals access the network at fixed locations and do not need to be authenticated. This access mode is more secure but lacks flexibility. When the locations of terminals change, you need to configure static VLANs again.
  The dynamically authorized VLAN mode applies when terminals need to access the network from any place and need to be authenticated based on the VLAN information delivered during user authentication. This access mode is flexible and the configuration does not need to be changed when the locations of terminals change. Dynamic access is more automated, easy to manage and use, and is therefore recommended.
VN access design for wireless users:
  If distributed gateways are used and edge nodes have the native AC function deployed, traffic of wireless users is forwarded to the edge nodes through CAPWAP tunnels. After the edge nodes decapsulate CAPWAP packets, the decapsulated packets enter different VNs depending on the VLANs to which the wireless users belong.
  If centralized gateways are used and border nodes have the native AC function deployed, it is recommended that traffic of wireless users be directly forwarded to the border nodes through CAPWAP tunnels. The border nodes then decapsulate CAPWAP packets and forward them to different BDs based on the VLANs. The administrator needs to configure different VLAN ranges for wired and wireless terminals. The VLANs of wired terminals are bound to BDs on the edge nodes, whereas the VLANs of wireless terminals are bound to BDs on the border nodes.

## Slide 64: Inter-VN Communication Design
Inter-VN communication through a border node (centralized gateway scenario)
Inter-VN communication through an external gateway
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
Traffic for inter-VN communication is forwarded through the border node. VRFs on the border node need to import routes from each other.
This mode applies to the scenario where two VNs belong to the same security zone and there are low security control requirements.
Traffic for inter-VN communication is forwarded to the border node and then diverted to the external gateway. Subsequently, the external gateway performs a security check or forwards the traffic back to the border node, which then forwards the traffic to the destination.
This mode applies to the scenario where two VNs belong to different security zones and there are high security control requirements (for example, application-based policy control).
VRF1 and VRF2 on the border node import each other's network segment routes.
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
Firewall
Notes: Inter-VN communication can be implemented through a border node or an external gateway.
  Through a border node
    If two VNs belong to the same security zone and have low security control requirements, devices on the two VNs can directly communicate with each other through a border node. In addition, permission control can be implemented based on the free mobility policy. To implement communication between VNs, the border node needs to import their respective network segment routes that are reachable to each other.
  Through an external gateway
    If two VNs belong to different security zones and have high security control requirements, it is recommended that devices on the two VNs communicate through an external gateway (a firewall) and that a security zone policy be configured on the firewall for permission control.

## Slide 65: Mapping Between the Logical Network and Physical Network
Border
Edge
Edge
Router
R&D
Production
OA
VNs
Router
Border
Edge
Zone1
Zone2
Zone3
Security policy
Zone4
IP packet
V
R
F
1
V
R
F
2
V
R
F
3
Public
VLAN
VLAN
VLAN
VLAN
VLAN
VLAN
VXLAN Tunnel
VBDIF: Layer 3 VXLAN gateway interface
IP packet
IP packet
IP packet
IP packet
FW
Traffic of end users
Notes: Each VN corresponds to a VRF.
Each VN corresponds to multiple subnets, and each subnet corresponds to a BD and VNI.
Traffic from a terminal enters the VN based on the VLAN to which the terminal belongs.

## Slide 66
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 67: User Management Solution Design
User management solution design involves confirming the user data source server. Typical user data source servers of enterprises include RADIUS, AD, and LDAP servers.
Confirm the user data source server
RADIUS server
AD server
LDAP server
If an enterprise has no data source server, it is recommended that Huawei iMaster NCE-Campus be used as the data source server.
If an enterprise has used the AD/LDAP server as the user data source server, the enterprise can continue to use the legacy AD/LDAP server. iMaster NCE-Campus can synchronize user data with such a server and finally perform network authorization.
Same principles as the AD server
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 68: User Authentication Technology Selection
Common authentication technologies include 802.1X, MAC address, and Portal authentication. The following table compares these authentication methods.
Item | 802.1X Authentication | MAC Address Authentication | Portal Authentication
Client required or not | Required | Not required | Not required
Advantage | High security | No need to install a client | Flexible deployment
Disadvantage | Inflexible deployment | MAC addresses need to be registered, complicating management | Low security
Application scenario | Network authentication of office users with high security requirements | Access authentication of dumb terminals such as printers and fax machines | Network authentication of guests who move frequently and use different types of terminals
User Management
User Authentication
Terminal Identification
Policy Control
On large- and medium-sized campus networks, 802.1X authentication is recommended for employees, Portal authentication for guests, and MAC address authentication for dumb terminals.
If a customer wants to use more than one authentication method on the same access point, a combination of authentication methods (hybrid authentication) can be used. After hybrid authentication is configured, terminals can access the network after passing any authentication in the combination. This mode is applicable to scenarios where one port provides access for multiple types of users. For example, if a PC is connected upstream to an IP phone, you can configure hybrid authentication (MAC address authentication + 802.1X authentication). In this way, the IP phone uses MAC address authentication, and the PC uses 802.1X authentication.
Notes: If 802.1X or MAC address authentication (Layer 2 authentication technologies) is used, the authentication point must be on the same network segment as the user host. It is recommended that the access device function as the authentication point.
  If a large number of access devices are deployed, the aggregation or core device needs to be deployed as the authentication point. You can also deploy policy association. The gateway functions as the authentication control point, and the access device functions as the authentication enforcement point, thereby simplifying policy deployment.
If Portal authentication is used, the authentication point can be deployed anywhere as long as it is routable to the user host. Layer 2 Portal authentication is recommended.

## Slide 69: Association Between Authenticated Users and VNs
1. Create VNs on iMaster NCE-Campus.
2. Authenticated users obtain authorized VLANs and are then associated with VNs based on the VLANs.
The administrator creates VNs and specifies the IP network segments and VLANs for the VNs.
The administrator configures user authentication rules, authorization results, and authorization rules, so that users can obtain corresponding VLANs after being authenticated. For example, the administrator configures user test to obtain the authorized VLAN 10 after passing 802.1X authentication.
OA VN
VLAN 10: 10.1.10.0/24
VLAN 20: 10.1.20.0/24
R&D VN
VLAN 30: 10.1.30.0/24
VLAN 40: 10.1.40.0/24
1
User test attempts to access the network.
Send an authentication request.
Issue the authorization result (VLAN 10) after successful user authentication.
2
3
4
User Test accesses the OA VN.
test
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 70: Multi-Level Design for Access Policies
Network access policies can be logically divided into two levels:
  VN-level access policy: By default, VNs cannot communicate with each other, and service data of each VN is isolated. The CloudCampus Solution enables VNs to communicate within a fabric or through an external network.
  Security group-level access policy: Users and network resources are divided into different security groups for efficient management and control of inter-group traffic. The free mobility policy enforcement point executes inter-group access policies.
Fabric
HR group
R&D group
Guest group
Internet
OA server resource group
OA VN
R&D VN
R&D group 1
Sensitive data
resource group
HR server resource group
R&D code library
resource group
R&D group 2
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 71: Policy Design: Create Security Groups
Define security groups for enterprise employees based on the enterprise organizational structure.
Define a security group for a special group of people in the organizational structure, such as the VIP group.
Define a security group for non-employees that access the network, such as the guest group.
Define a security group for dumb terminals connected to the network, such as printers and access control devices.
Dynamic security groups
Terminals and users accessing the network are divided into different security groups through NAC authorization.
Static resource groups
Configure a group of IP address resources as a static resource group.
Hardware development Dept.
Software development Dept.
Testing Dept.
Financial Dept.
Human resources Dept.
Marketing Dept.
Dynamic security groups are authorized based on the 5W1H principle.
Aggregate the IP addresses of dispersed data center applications into a resource group, thereby simplifying deployment.
Define security groups, such as the OA resource group and R&D resource group, for intranet resources based on security requirements.
If Internet access control is required, define an Internet resource group.
Internet
Internet resource group
General office resources, such as websites and email addresses
OA resource group
Internal private applications, files, code, etc.
R&D resource group
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 72: Policy Design: Design the Policy Control Matrix
Create dynamic and static security groups for free mobility based on actual requirements, and design the policy control matrix based on network access permissions.
Dynamic security groups
HR
R&D
Sales
Guest
Static security groups
OA server
R&D code library
Marketing document library
Internet
 | OA server | R&D code library | Marketing document library | Internet | HR | R&D | Sales | Guest
HR | Permit | Deny | Deny | Permit |  | Permit | Permit | Deny
R&D | Permit | Permit | Deny | Permit | Permit |  | Permit | Deny
Sales | Permit | Deny | Permit | Permit | Permit | Permit |  | Deny
Guest | Deny | Deny | Deny | Permit | Deny | Deny | Deny | 
Source
Destination
Policy control matrix:
User Management
User Authentication
Terminal Identification
Policy Control
Notes: An inter-group policy directly reflects whether two security groups can communicate with each other. When planning an inter-group policy, simply set the inter-group policy to permit or deny based on whether the two groups can communicate with each other. The administrator can configure inter-group policies through an intuitive policy control matrix on iMaster NCE-Campus. If no inter-group policy is created between source and destination security groups, the default policy between them is permit.
Take the policy direction into account when planning inter-group policies. Typically, packets are transmitted in two directions between two terminals.
  Huawei switches consider that traffic from A to B is unrelated to traffic from B to A, so they match policies for the two types of traffic separately and determine whether to forward the traffic based on the corresponding policies. This means that a Huawei switch enforces policies on a packet by considering only the source and destination security groups of that packet. For example, the policy "A ->B permit, B -> A deny" means that all packets sent from A to B will be permitted, whereas all packets sent from B to A will be discarded, regardless of whether A or B initiates the access. The default inter-group policy on a switch is permit.

## Slide 73: Location Selection for Authentication Points and Policy Enforcement Points
Typically, the user gateway functions as both an authentication point and policy enforcement point, on which the free mobility function is deployed, due to the following considerations:
  There are a large number of access switches. Configuring the authentication function on each access switch brings a heavy workload and leads to difficulties in management.
  iMaster NCE-Campus needs to synchronize permission control policies to policy enforcement points. If access switches are used as authentication points, the number of policy enforcement points will increase significantly due to the large number of access switches. This increases the workload and difficulty in device management on iMaster NCE-Campus and prolongs the policy synchronization time as well.
To prevent users connected to the same upstream user gateway from communicating with each other at Layer 2, you can configure Layer 2 isolation. In this way, traffic between these users must pass through the user gateway.
User Management
User Authentication
Terminal Identification
Policy Control
Notes: If an authentication point and policy enforcement point are deployed on different devices, the IP-security group entries of authenticated users need to be pushed to the specified policy enforcement point. To achieve this, the administrator needs to configure IP-security group entry subscription, that is, specify to which policy enforcement point the IP-security group entries of a certain network segment or security group need to be pushed.

## Slide 74: IP-Security Group Entry Synchronization
Technical background
IP-security group entry synchronization principle
iMaster NCE-Campus synchronizes the mappings between user IP addresses and security groups to the switches functioning as policy enforcement points. In this way, authentication points and policy enforcement points can be separated, thereby implementing flexible networking. In addition, hybrid networking with third-party devices can be easily achieved.
1
3
IP | Group
1.1.1.1 | Group1
2.2.2.2 | Group2
PC1 1.1.1.1
PC2 2.2.2.2
User access
2
User authentication
4
Proactively synchronize IP-security group entries through HTTP/2.
5
Enforce the inter-group policy when the traffic arrives.
Third-party device
These devices do not support free mobility, so how to realize free mobility if a solution includes these devices?
Switches that do not support free mobility
ACs
Routers
Third-party devices (non-Huawei)
Free mobility supported
Free mobility not supported
Generate an IP-security group entry.
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 75: Free Mobility Solution (1)
Scenario description
Centralized authentication point + centralized policy enforcement point.
The authentication point and policy enforcement point are combined on the core device.
Devices do not support VXLAN.
Scenario characteristics
The core device functions as the centralized authentication point for both wired and wireless users on the entire network.
The core device also works as the policy enforcement point for free mobility.
The core device stores authentication information about all users on the network. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by the administrator.
The network does not need to support or deploy VXLAN.
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
Core
AGG1
AGG2
Access1
Access2
PC2 2.2.2.2
R&D user
User Management
User Authentication
Terminal Identification
Policy Control
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Security group
Security group-based policy control matrix

## Slide 76: Free Mobility Solution (2)
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Core
AGG1
AGG2
Access1
Access2
Security group
Security group-based policy control matrix
Scenario description
Distributed authentication points + centralized policy enforcement point.
Authentication points are separated from the policy enforcement point.
Devices do not support VXLAN.
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
The core device functions as the centralized policy enforcement point for free mobility.
iMaster NCE-Campus proactively synchronizes IP-security group entries to the core device. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by the administrator.
The network does not need to support or deploy VXLAN.
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
IP Address | Group ID
1.1.1.1 | 1
2.2.2.2 | 2
3.3.3.3 | 3
… | …
IP-security group mapping table
Proactively synchronize IP-security group entries
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
Device enabled with IP-security group
entry subscription
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 77: Free Mobility Solution (3)
Core
AGG1
AGG2
Access1
Access2
Scenario description
VXLAN-based virtualized campus network, with automatic service provisioning.
Distributed authentication points + policy enforcement points.
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
VXLAN
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
User Management
User Authentication
Terminal Identification
Policy Control
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Security group
Security group-based policy control matrix

## Slide 78: Free Mobility Solution (4)
Host1
Sales user
A-Agg
B-Agg
B-Access
1
2
3
4
5
AP
A terminal attempts to go online and initiates authentication.
Authenticate the user.
Generate an IP-security group entry.
Deliver the IP-security group entry.
Enforce the inter-group policy when the traffic arrives.
Device enabled with IP-security group
entry subscription
A-Access
(third party)
Host4
Guest
Scenario description
VXLAN-based virtualized campus network.
Distributed authentication points + policy enforcement points.
The third-party device functions as a user authentication point.
Scenario characteristics
A third-party switch exists on the network and functions as a user authentication point.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
VXLAN
User Management
User Authentication
Terminal Identification
Policy Control
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Proactively synchronize IP-security group entries

## Slide 79: Free Mobility Solution (5)
Scenario description
VXLAN-based virtualized campus network
The AC functions as the authentication point for wireless users, and the core switch functions as the gateway for wireless users.
Scenario characteristics
The AC functions as the authentication point for wireless users and interacts with iMaster NCE-Campus to complete user authentication.
The core switch functions as the free mobility policy enforcement point, to which iMaster NCE-Campus synchronizes IP-security group entries.
Core
VXLAN
AC
Device enabled with IP-security group
entry subscription
User Management
User Authentication
Terminal Identification
Policy Control
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Proactively synchronize IP-security group entries

## Slide 80: Terminal Identification and Policy Automation Overview
Terminal identification methods
Passive fingerprint-based identification: Network devices collect fingerprints of packets sent by terminals and report the fingerprints to iMaster NCE-Campus for terminal type identification.
Proactive scanning and identification: iMaster NCE-Campus proactively detects or scans terminals, and identifies terminal types based on fingerprint information of the terminals.
Terminal identification and policy automation
Automatic authentication
Recognized as a printer
Automatic MAC address authentication, without the need of manual MAC address input.
Terminal type-based
Automatic authorization
Recognized as a camera
Automatically added to a video surveillance group.
Terminal type-based
Terminal type-based
Bogus terminal detection
Recognized as an IP phone first and then a PC
Report a bogus terminal alarm.
Terminal fingerprint database
Information reporting
Proactive scanning
>>
User Management
User Authentication
Terminal Identification
Policy Control
Notes: On large- and medium-sized campus networks, access terminals include smart terminals (such as PCs and mobile phones) and dumb terminals (such as IP phones, printers, and IP cameras). Currently, terminal management on campus networks faces the following challenges:
  The network management system (NMS) can only display the IP and MAC addresses of access terminals, but cannot identify the specific terminal type. As a result, the NMS cannot provide refined management for network terminals.
  Network service configurations and policies vary according to the terminal type. Consequently, administrators need to manually configure different services and policies for each type of service terminals, complicating service deployment and operations.
To address these challenges, Huawei provides the automatic terminal identification and policy delivery solution, which delivers the following functions:
  iMaster NCE-Campus can display the network-wide terminal types and operating systems, for example, dumb terminals including printers, IP cameras, smart all-in-one card, and access control system. iMaster NCE-Campus can also collect statistics and display traffic by terminal type.
  Administrators do not need to manually configure different services and policies for different types of dumb terminals such as IP phones, printers, and IP cameras on the campus network. iMaster NCE-Campus can automatically identify these terminals and deliver the corresponding admission policies and service configurations to them.

## Slide 81: Terminal Identification Method Design (1)
To view terminal types and perform network management based on the terminal types through iMaster NCE-Campus, the network administrator needs to perform the following operations:
Collect the types of terminals on the network, such as PCs, mobile phones, printers, IP cameras, and access control devices.
Determine whether to deploy Portal authentication.
Determine whether IP addresses of terminals are assigned using DHCP or in static mode.
Analyze the network.
Method | Identifiable Terminal Type | Applicable Scenario
MAC OUI | All IP terminals (only device vendors can be identified). | General scenarios
HTTP UserAgent | Mobile phones, tablets, PCs, and workstations, as well as smart audio and video terminals. | Portal authentication scenarios only
DHCP Option | Mobile phones, tablets, PCs, workstations, IP cameras, IP phones, printers, etc. | Dynamic IP address assignment scenarios only
LLDP | IP phones, IP cameras, network devices, etc. | General scenarios
mDNS | Printers, IP cameras, etc. | General scenarios
SNMP Query | Network devices, printers. | On-premises scenario
Nmap | PCs, workstations, printers, IP phones, IP cameras, etc. | On-premises scenario
Traverse items one by one according to the following table.
Based on the collected information, traverse the items listed in the following table one by one and select the required terminal identification methods. All the identification methods that meet requirements must be enabled.
1
2
User Management
User Authentication
Terminal Identification
Policy Control
Notes: In this slide, "general scenarios" refer to authentication, non-authentication, and dynamic/static IP address assignment scenarios.
In non-authentication scenarios, iMaster NCE-Campus can display information about wired terminals only after the ARP snooping function is enabled on access devices.

## Slide 82: Terminal Identification Method Design (2)
If the network administrator cannot determine which terminal identification method is to be used, the following passive fingerprint-based identification methods are recommended: MAC OUI, HTTP UserAgent, DHCP Option, LLDP, and mDNS.
It is recommended that Nmap be disabled by default because this identification takes a long time. If the preceding passive fingerprint-based identification methods cannot meet requirements, enable Nmap.
Enable the terminal identification function.
Identification Method | Enabled On … | Other Functions to Be Enabled
MAC OUI | Access switch and AP | -
HTTP UserAgent | Device enabled with Portal authentication | -
DHCP Option | Access switch and AP | DHCP snooping must be enabled on access switches. By default, DHCP snooping is already enabled on APs.
LLDP | Access switch and AP | -
mDNS | Access switch and AP | mDNS snooping must be enabled on access switches and APs.
SNMP Query | iMaster NCE-Campus | -
Nmap | iMaster NCE-Campus | -
3
User Management
User Authentication
Terminal Identification
Policy Control

## Slide 83: Terminal Policy Design
The network administrator can use iMaster NCE-Campus to automatically deliver policies to terminals, eliminating the need to manually configure different policies for each type of service terminals.
Terminal policies can be delivered based on the terminal type, operating system, or vendor.
Enable terminal-type-based automatic policy delivery, so that policies are authorized based on the admission authentication result.
Deploy admission authentication on access switches and APs.
Enable MAC address authentication on access switches and APs when dumb terminals are deployed.
Perform policy design.
Enable the terminal identification function on the network.
Sort out the types of terminals that require automatic policy delivery on the network, design corresponding authorization policies, and configure the policies on iMaster NCE-Campus.
Item | Admission Policy | Authorization Policy
Operating system: Android | User admission | Authorized ACL 1
Operating system: iOS | User admission | Authorized ACL 2
Terminal type: printer | Automatic admission | Authorized VLAN 10
Terminal type: IP camera | Automatic admission | Authorized VLAN 20
Terminal type: IP phone | Automatic admission | Authorized VLAN 30; DSCP 48
Terminal type: access control device | Automatic admission | Authorized VLAN 40
Vendor: ABC | User admission | Authorized ACL 100
1
2
3
User Management
User Authentication
Terminal Identification
Policy Control
Notes: It is recommended that admission and authorization policies be automatically delivered to dumb terminals (such as printers, IP phones, and IP cameras) based on terminal types. This helps implement automatic service provisioning and plug-and-play for dumb terminals.

## Slide 84
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 85: WLAN Service Solution
Native AC solution
Switches provide the native AC function.
Free mobility is supported. Policies for both wired and wireless users are centrally enforced on the switches.
Unified O&M for both wired and wireless users.
Standalone AC solution
Standalone AC (connected to the core switch in off-path mode).
The free mobility solution is supported for wireless users, but it must be used together with the IP-security group entry synchronization solution.
Separate O&M for wired and wireless users.
Native AC
Standalone AC
Standalone AC
Native AC
Native AC
The native AC function can be applied to aggregation or core switches.
Notes: On a large- or medium-sized campus network, the WLAN typically uses the "AC + Fit AP" networking architecture. An AC can be deployed in in-path or off-path mode, depending on its location. A native AC (integrated on a switch) must be deployed in in-path mode, whereas a standalone AC can be deployed in either in-path or off-path mode (off-path mode is recommended).

## Slide 86: Native AC Solution Deployment on a VXLAN-based Virtualized Campus Network (1)
Distributed gateway scenario
Scenario 1 (recommended): The switch used as the edge node provides the native AC function to manage downstream APs.
When the number of wireless users on the entire network exceeds 50K, it is recommended that native AC be deployed on edge nodes. In this scenario, it is recommended that the AP use the tunnel forwarding mode.
Traffic of wireless users enters into VNs through the native AC, and the edge node functions as the gateway of wireless users.
Inter-group policies for wireless users are enforced on the edge node, and free mobility is supported.
Border
Edge
Layer 3 gateway
Scenario 2: The switch used as the border node provides the native AC function to manage network-wide APs.
When the number of wireless users on the entire network is fewer than 50K, it is recommended that native AC be deployed on the border node. In this scenario, the tunnel forwarding mode is recommended for APs.
Edge
Layer 3 gateway
Native AC
CAPWAP tunnel
Native AC
CAPWAP tunnel
Edge
Layer 3 gateway
Border
Edge
Layer 3 gateway
Notes: Description of Scenario 1:
  User gateway:
    Edge node
  Authentication point:
    Wired users: edge node; Wireless users: edge node (native AC)
  Forwarding mode:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the edge node. The tunnel forwarding mode is recommended. Traffic enters VNs through the native AC (edge node).
Description of Scenario 2:
  User gateway:
    Wired users: edge node; Wireless users: border node (in tunnel forwarding mode)
  Authentication point:
    Wired users: edge node; Wireless users: border node (native AC)
  Forwarding mode:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node. The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (native AC).

## Slide 87: Native AC Solution Deployment on a VXLAN-based Virtualized Campus Network (2)
Centralized gateway scenario
Scenario: The switch used as the border node provides the native AC function to manage network-wide APs.
It is recommended that native AC be deployed on the border node and APs use the tunnel forwarding mode.
Traffic of wireless users enters into VNs through the native AC, and the border node functions as the gateway of wireless users.
Inter-group policies for wireless users are enforced on the border node, and free mobility is supported.
Border
Layer 3 gateway
Edge
Native AC
CAPWAP tunnel
Edge
Notes: Scenario description:
  User gateway:
    Border node
  Authentication point:
    Wired users: edge node; Wireless users: border node (native AC)
  Forwarding mode:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node. The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (native AC).

## Slide 88: Standalone AC Solution Deployment on a VXLAN-based Virtualized Campus Network
Centralized gateway scenario
Border
Layer 3 gateway for wireless users
Edge
Edge
CAPWAP tunnel
Distributed gateway scenario
The AC centrally manages APs. The tunnel forwarding mode is used. Traffic of wireless users is encapsulated by the AP using the CAPWAP protocol and then sent to the AC. After being decapsulated by the AC, the traffic enters VNs through the border node.
The border node functions as the gateway for wireless users.
Inter-group policies for wireless users are enforced on the border node, and free mobility is supported.
Standalone AC
Border
Layer 3 gateway for wireless users
Edge
Layer 3 gateway for wired users
Edge
Layer 3 gateway for wired users
CAPWAP tunnel
Standalone AC
The AC centrally manages APs. The tunnel forwarding mode is used. Traffic of wireless users is encapsulated by the AP using the CAPWAP protocol and then sent to the AC. After being decapsulated by the AC, the traffic enters VNs through the border node.
The border node functions as the gateway for wireless users.
Inter-group policies for wireless users are enforced on the border node, and free mobility is supported.
Notes: Description of the centralized gateway scenario:
  User gateway:
    Border node
  Authentication point:
    Wired users: edge node; Wireless users: standalone AC
  Forwarding mode:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node (the border node needs to subscribe to IP-security group entries). The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (traffic is forwarded from the standalone AC to the border node and then enters VNs).
Description of the distributed gateway scenario:
  User gateway:
    Wired users: edge node; Wireless users: border node (in tunnel forwarding mode)
  Authentication point:
    Wired users: edge node; Wireless users: AC
  Forwarding mode:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: The tunnel forwarding mode is recommended. Traffic enters VNs through the border node, and the border node enforces free mobility policies (the border node needs to subscribe to IP-security group entries).

## Slide 89: Deployment of WLAN Deployment Solutions on a VXLAN-based Virtualized Campus Network
The following table lists the recommended WLAN deployment solutions for centralized and distributed gateway networking.
In new deployment scenarios or wired and wireless network reconstruction scenarios, the native AC is recommended and tunnel forwarding mode is preferentially selected for APs.
Networking Type | AC | Gateway for Wireless Terminals | AP Forwarding Mode | Wireless Traffic Virtualization Location | Number of Terminals Supported | Applicable Scenario
Centralized gateway | Native AC on the border node | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the number of terminals does not exceed 50,000 and centralized forwarding is implemented for wireless terminals.
 | Standalone AC connected to the border node in off-path mode | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the wired network is reconstructed first and centralized forwarding is implemented for wireless terminals.
Distributed gateway | Native AC on the edge node | Edge node | Tunnel forwarding | Edge node | 50,000~100,000 | Recommended when the number of terminals exceeds 50,000 and centralized forwarding is implemented for wireless terminals.

## Slide 90
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 91: Overall Security Design
Campus network security design principles
  There is no absolutely secure network but only more comprehensive protection measures.
  Security is changing dynamically. Different networks have different security requirements. Therefore, on-demand network security design is the best choice.
  Security is a system issue. Security design is required in all aspects of the network. In addition to egress security, campus networks also need to consider intranet security and security compliance.
Campus network security system
  Egress security
  Intranet security: wired network security and wireless network security
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
Server zone
Egress
security
Intranet security
Notes: On a traditional campus network, the intranet is often considered secure, and threats mainly come from external networks. Firewalls are often deployed to ensure security on campus borders. As security challenges increase, border defense at the egress cannot meet requirements. The security model needs to shift from passive into proactive and the security scope needs to be expanded from external networks to the intranet to solve security problems from the source (terminals), improving enterprise-wide information security level.

## Slide 92: Egress Network Security Design
Egress security requirement analysis
  For external networks: Deploy security policies and intrusion prevention to prevent unauthorized access and attacks.
  For the intranet: Deploy antivirus and URL filtering to implement virus detection and URL access control.
Egress security solution design
  Dedicated security devices, such as firewalls and intrusion prevention systems, are recommended.
  Routers with the preceding security functions can also be used.
Security zone division
  The Trust zone is a security zone with a high security level. It is typically used to define the zone where intranet terminal users are located.
  The DMZ is a security zone with a medium security level. It is typically used to define the zone where the servers that need to provide services for external networks are located.
  The Untrust zone is a security zone with a low security level. It is typically used to define insecure networks such as the Internet.
Function | Description
Intrusion prevention | Compares traffic against the intrusion prevention signature database to prevent application-layer attacks, such as buffer overflows, Trojan horses, backdoor attacks, and worms.
Antivirus | Inspects the files transmitted on the network for viruses to protect the intranet from data breaches and system crashes caused by viruses.
URL filtering | Permits or denies access to URLs to control the online behavior of users.
Access Zone | Access Source | Trustworthiness | Recommended Security Policy
Internet | External users | Untrusted | Intrusion detection, URL filtering, and antivirus
 | Employees on the go | Medium | 
WAN | Enterprise branches | Medium | URL filtering and antivirus
Intranet | Enterprise employees | High | URL filtering and antivirus
 | Guests | Low | 

## Slide 93: Wired Network Security Design
Security Risk | Protection Measure
Broadcast storm | Enable traffic suppression and storm control.
DHCP attack | Enable DHCP snooping and configure uplink interfaces as trusted interfaces.
Impersonating legitimate users | Enable IP source guard (IPSG) and dynamic ARP inspection (DAI).
Mutual access | Enable port isolation.
CPU attack | Enable CPU attack defense.
Denial of service (DoS) attack | Enable attack source tracing.
 | Enable port attack defense.
 | Enable user-level rate limiting.
Notes: Security measures:
  Enable traffic suppression and storm control.
    Control broadcast, multicast, and unknown unicast packets to prevent broadcast storms. Traffic suppression limits the traffic using the configured threshold, and storm control blocks the traffic by shutting down interfaces.
  Enable DHCP snooping and configure uplink interfaces as trusted interfaces.
    DHCP snooping defends against bogus DHCP server attacks, DHCP server DoS attacks, bogus DHCP packet attacks, and other DHCP attacks. DHCP snooping allows administrators to configure trusted and untrusted interfaces, so DHCP clients can obtain IP addresses from authorized DHCP servers. A trusted interface forwards the DHCP packets it receives, whereas an untrusted interface discards the DHCP ACK packets and DHCP Offer packets received from a DHCP server.
    An interface directly or indirectly connected to the DHCP server trusted by the administrator needs to be configured as a trusted interface, and other interfaces are configured as untrusted interfaces. This ensures that DHCP clients obtain IP addresses only from authorized DHCP servers and prevents bogus DHCP servers from assigning IP addresses to DHCP clients.
  Enable IPSG and DAI.
    IPSG prevents unauthorized hosts from using IP addresses of authorized hosts or specified IP addresses to access or attack the network.

## Slide 94
Notes:     You can configure DAI to defend against man-in-the-middle (MITM) attacks and prevent theft of authorized user information. When a device receives an ARP packet, it matches the source IP address, source MAC address, VLAN ID, and interface number of the ARP packet against binding entries. If a match is found, the device considers the ARP packet valid and allows it to pass through. Otherwise, the device discards the packet.
  Enable port isolation.
    You are advised to configure port isolation on the interfaces connecting an access switch to terminals. This configuration secures user communication and prevents invalid broadcast packets from affecting user services.
  Enable CPU attack defense.
    CPU attack defense limits the rate of packets sent to the CPU so that only a limited number of packets are sent to the CPU within a certain period of time. This ensures that the CPU can properly process services.
    Control Plane Committed Access Rate (CPCAR) is the core of CPU attack defense. CPCAR limits the rate of protocol packets sent to the control plane to ensure security of the control plane.
  Enable attack source tracing.
    Attack source tracing defends against DoS attacks. A device enabled with attack source tracing analyzes packets sent to the CPU, collects statistics on the packets, and allows a user to set a packet rate threshold for the packets. Packets sent at a threshold-crossing rate are considered as attack packets. The device finds the source user address or source interface of the attacker by analyzing the attack packets and generates logs or alarms to alert a network administrator. The network administrator then takes measures to defend against the attack or configure the device to discard packets sent by the attack source.
  Enable port attack defense.
    Port attack defense is an anti-DoS attack method. It defends against attacks based on ports and prevents protocol packets on ports from occupying bandwidth and causing other packets to be discarded.
    By default, port attack defense is enabled on the device for common user protocol packets, such as ARP, ICMP, DHCP, and IGMP packets. If a user attack occurs, the device restricts the attack impact within the port, reducing the impact on other ports.
  Enable user-level rate limiting.
    User-level rate limiting identifies users based on MAC addresses, and rate-limits specified protocol packets, such as ARP, ND, DHCP Request, DHCPv6 Request, IGMP, 802.1X, and HTTPS-SYN packets. If a user undergoes a DoS attack, other users are not affected.
    Host CAR is the core of user-level rate limiting. By default, user-level rate limiting is enabled.

## Slide 95: Overview of Wireless Network Security Design
On a WLAN, service data is transmitted through radio signals. Such open channels are vulnerable to service data interception and tampering during transmission, such as rogue STAs, spoofing APs, and DoS attacks of malicious terminals.
In addition to the security risks of wired networks, wireless networks also face security risks of wireless air interfaces. Therefore, the security risks of wireless networks mainly involve the security of wireless air interfaces.
WLAN security design involves the following:
  Air interface security: identifies and defends against attacks such as rogue APs, rogue STAs, unauthorized ad-hoc networks, and DoS attacks.
  STA access security: ensures the validity and security of STAs' access to the WLAN.
  Service security: protects service data of authorized users from being intercepted by unauthorized users during transmission.
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
Rogue STA
A rogue STA goes online
STAs access through a rogue AP
Rogue AP
Illegal data theft

## Slide 96: Wireless Network Security Design
Wireless air interface security design:
Security Risk | Defense Measure
Wireless attack and spoofing | WIDS
 | WIPS
 | Attack detection
Unencrypted management frames | Protected management frame (PMF)
Security Risk | Defense Measure
Air interface encryption and access authentication | WPA/WPA2
 | WAPI
Terminal access security | STA blacklist and whitelist
Brute-force cracking | Brute-force attack defense and dynamic blacklist
STA access security design:
Wireless service security design:
  The wired network between APs and ACs also faces common security threats, for example, interception, tampering, and spoofing, on IP networks.
  To improve data transmission security, CAPWAP tunnels between APs and ACs support Datagram Transport Layer Security (DTLS) encryption, including DTLS encryption of CAPWAP tunnels for management packets, DTLS encryption of CAPWAP tunnels for service data packets, encryption of sensitive information, and integrity check.
Notes: Wireless air interface security design:
  The Wireless Intrusion Detection System (WIDS) can detect rogue and interfering APs, bridges, and STAs, as well as ad-hoc devices.
  The Wireless Intrusion Prevention System (WIPS) can disconnect authorized users from rogue APs, disconnect rogue and interfering devices from the WLAN, and contain such devices.
  Attack detection: The WIDS and WIPS can also detect attacks such as flood attacks, weak initialization vector (IV) attacks, spoofing attacks, brute force WPA/WPA2/WAPI pre-shared key (PSK) cracking, and brute force WEP shared key cracking in a timely manner. The two systems then record logs, statistics, and alarms to notify network administrators of such attacks. The WLAN device adds devices that initiate flood attacks and brute force key cracking attacks to the dynamic blacklist and rejects packets from such devices within the aging time of the dynamic blacklist.
  PMF: Management frames on a WLAN are not encrypted, which may cause security problems. The PMF standard is released by the Wi-Fi Alliance based on IEEE 802.11w. It aims to apply security measures defined in WPA2 to unicast and multicast management action frames to improve network trustworthiness.

## Slide 97
Notes: STA access security design:
  Four WLAN security policies are available: Wired Equivalent Privacy (WEP), Wi-Fi Protected Access (WPA), WPA2, and WLAN Authentication and Privacy Infrastructure (WAPI). Each security policy has a series of security mechanisms, including link authentication used to establish a wireless link, user authentication used when users attempt to connect to a wireless network, and data encryption used during service transmission.
    WEP uses a shared key to authenticate users and encrypt service packets. Since the shared key is easy to decipher, the WEP security policy is not recommended due to its low security.
    WLAN devices support the STA blacklist and whitelist function to filter access requests from STAs based on specified rules, allowing authorized STAs to access the WLAN and rejecting unauthorized STAs.
    When a WLAN uses WPA/WPA2-PSK, WAPI-PSK, or WEP-Shared-Key as the security policy, attackers can use the brute force method to decrypt the password. Defense against brute-force key cracking can prolong the time needed to decrypt passwords.
  The STA access security design is to properly plan and design the access policies of STAs, securing and facilitating STA access.
  The following is an example of the STA access authentication policy. The following access authentication modes are recommended on enterprise wireless networks:
    Enterprise employees: WPA/WPA2-802.1X authentication
    Guests: WPA/WPA2-PPSK or Portal authentication
    Dumb terminals: MAC address authentication
  In addition, if users do not need to communicate with each other, it is recommended that user isolation be configured.
Wireless service security design:
  Sensitive information encryption: When sensitive information is transmitted between an AP and an AC, the information can be encrypted to ensure security. Sensitive information includes the FTP user name, FTP password, AP login user name, AP login password, and service configuration key. During inter-AC roaming, the sensitive information encryption function can also be configured to protect data transmitted between ACs.
  Integrity check: When CAPWAP packets are transmitted between an AP and an AC, these packets may be forged or tampered with or attackers may construct malformed packets to launch attacks. Integrity check can protect CAPWAP packets between the AP and AC. If the AP and AC are both located on the intranet, this function does not need to be enabled. It is recommended that this function be enabled when the AP is connected to the AC across the Internet or the ACs are distributed across the Internet.

## Slide 98
CloudCampus Solution and Virtualized Campus Network Overview
Underlay Network Design
Fabric Design
Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Network Security Design
O&M Design

## Slide 99: Challenges Facing Campus Network O&M
Precise detection
Fault identification
Experience perception
During traditional O&M, network faults can be detected only after receiving clients' complaints. As a result, faults cannot be effectively and proactively identified and analyzed.
Traditional O&M is based on SNMP and therefore data collection takes minutes. Once a fault occurs, data generated at the time when the fault occurred cannot be obtained in real time. In addition, no convenient backtracking method is available.
In traditional O&M systems, only device metrics are monitored. User experience may be poor even if the metrics are normal. In addition, traditional O&M systems do not provide correlative analysis for clients and networks.
Key requirements: intelligent fault identification
Key requirements: client & network profiling, experience perception
Key requirements: Telemetry-based precise detection

## Slide 100: Intelligent O&M Panorama
Visualized management and monitoring
Device management
Log management
File/Configuration management
Alarm management
File/Configuration management
NE management
Service quality monitoring
Link management
Wireless network monitoring
Network management
Terminal management
Customer flow analysis
User management
Terminal management
Device dimension
User roaming dimension
User application dimension
User access dimension
User throughput dimension
Network health
Intelligent troubleshooting
Device diagnosis and test
SLA management
Packet header obtaining
Packet path tracing
Fault locating
Access analysis
Protocol trace
Issue analysis
Performance analysis
Fault analysis
Access analysis
Protocol trace
Radio calibration
Performance analysis
Network optimization
Controller
Analyzer
CloudCampus
APP

## Slide 101: Using Telemetry to Monitor Metrics of Wireless Networks
Measured Object | Measurement Metrics | Supported Device Type | Default Collection Interval
AP | CPU usage, memory usage, and number of online clients | AP | 1 minute
Radio | Number of online clients, channel utilization, noise, traffic, backpressure queue, interference rate, and power | AP | 1 minute
Client | RSSI, negotiated rate, packet loss rate, and latency | AP | 1 minute
Uses telemetry to monitor KPI metrics of wireless networks, displays the wireless network quality from the AP, radio, and client dimensions, and proactively identifies air interface performance issues, such as weak-signal coverage, high interference, and high channel utilization.
Real-time data display
Automatic issue identification
Display key metrics of wireless networks and highlight abnormal metrics.
Automatically identify air interface performance issues based on AI algorithms, correlative analysis, and exception modes.
Telemetry-based metrics collection for wireless networks
Automatically identify air interface performance issues based on telemetry metrics, AI algorithms, correlative analysis, and exception modes.
Display KPI metrics of wireless networks in the AP dimension and highlight abnormal metrics.
Visualization
Optimization
Analysis
Telemetry
Notes: RSSI: Received Signal Strength Indicator

## Slide 102: Using Telemetry to Monitor Metrics of Wired Networks
Use Telemetry to collect metrics of devices and interfaces on wired networks, and analyze the metrics, so as to proactively monitor and predict network faults.
Measured Object | Measurement Metrics | Supported Device Type | Default Collection Interval
Device/ Card | CPU usage | Switch and AC | 1 minute
 | Memory usage | Switch and AC | 1 minute
Interface | Number of received/sent broadcast packets, number of received/sent multicast packets, number of received/sent unicast packets, number of received/sent packets that are discarded, and number of received/sent error packets | Switch and AC | 1 minute
Display key metrics on wired networks in real time, including top N devices and historical trend.
Use AI algorithms to predict the baselines of KPI metrics, such as the CPU/memory usage. Identify deteriorating network metrics before service interruptions through comparison with dynamic baselines.
Multiple metric display methods
Identify devices with abnormal metrics
Real-time display of
KPI metrics
Exception detection based on dynamic baselines
Establish baselines/benchmarks, and identify abnormal metrics through comparison with the benchmarks.
Visualization
Optimization
Analysis
Telemetry
Telemetry-based metric collection for wired networks

## Slide 103: Campus Network Health: Intuitive Insights into Network Quality
Wireless
Continuously drive network optimization based on KQIs/KPIs
Wired
Detect and handle faults in a timely manner based on accurate issue reporting
Wired network health
Portal for routine O&M
Centralized wired/wireless network monitoring
Intuitive, clear, and efficient display in terms of buildings
Device capacity
Network status
Network performance
Device environment
Wireless network health
Access success rate, time taken
Roaming success rate, time taken
Signal and interference
Air interface capacity
Air interface throughput
Campus network health
Visualization
Optimization
Analysis
Telemetry
Notes: Provides insights into campus network health, including both wired and wireless network health, based on visualized topology monitoring, implementing intelligent, simplified campus network O&M.
Network health topology as a uniform portal for rapidly handling network and device problems in a local building, simplifying network O&M.
KQI: Key Quality Indicator

## Slide 104: Real-Time or Periodic Quality Evaluation Reports, Providing Reference for Optimization
Network overview
Provides a full picture of network-wide information, including resources, clients, and quality statistics.
Indicator details
Ranks sites by multiple network health metrics, presenting the site quality trend.
Rectification suggestions
Identifies root causes of top network problems and provides rectification suggestions for continuously improving network quality.
Visualization
Optimization
Analysis
Telemetry
Notes: iMaster NCE-CampusInsight provides professional evaluation report services. Specifically, it generates network quality evaluation reports including the network overview, indicator details, and rectification suggestions in real time or periodically, delivering measurable network experience.

## Slide 105: Individual and Group Issue Analysis
During campus network O&M, administrators encounter the following types of issues:
Individual issues: for example, access failures caused by incorrect client configurations.
Group issues: for example, group authentication failures caused by authentication server faults and group weak-signal coverage issues caused by insufficient AP coverage.
Solution to individual issues
Per-metric: second-level data collection and exception detection.
Per-client: protocol-level access process analysis, client journey playback and experience analysis, and audio/video application quality perception.
Solution to group issues
Identification of four types of issues: intelligently identifies connectivity, air interface performance, roaming, and device issues.
Visualization
Optimization
Analysis
Telemetry

## Slide 106: Fault Inference
Rule 1
Rule 2
Rule 3
Rule 4
Fault knowledge base
Fault inference
Accurately matches fault scenarios
Automatically identifies root causes
Provides optimal rectification suggestions
Provides 120+ fault inference rules
Long-lasting expert-level O&M expertise of Huawei engineers
Continuous inputs from fault troubleshooting at real sites
Symptom: Client access fails at the authentication phase.
The authentication mode is 802.1X authentication.
The last packet for protocol interaction is EAP-Failure.
The packet before the EAP-Failure packet is sent from the client to the AP.
The interval between the EAP-Failure packet and the previous packet is less than 2 seconds.
Failure cause: The user name or password is incorrect or the certificate is installed incorrectly, causing the access denial by the authentication server.
Rectification suggestion: Check whether the user name and password of the client are correct and whether the certificate is installed correctly.
Fault occurs
Telemetry
Syslog
Data collection
Rule matching
Precise root cause analysis
Visualization
Optimization
Analysis
Telemetry

## Slide 107: AI-powered Intelligent Radio Calibration Improves Network-wide Performance
Scenario 1: manual calibration
Real-time simulation feedback
Provide prediction and simulation tools based on real-time feedback of environment changes to drive network optimization.
Predictive Calibration
Provide the service weight balancing and optimization capability based on big data analytics and AI.
About 20% of customers choose to manually plan channels. However, they may face the following challenges:
Real-time network awareness is not supported.
The network environment is complex and interference changes rapidly.
Channels planned in manual mode are not the optimal ones.
Load balancing is not considered during load balancing calibration.
Scenario 2: automatic calibration
About 80% of customers choose automatic calibration. However, they may face the following challenges:
Only the current network status can be detected.
Unable to detect historical loads and interference.
Visualization
Optimization
Analysis
Telemetry

## Slide 108: Intelligent O&M Solution Deployment Design
Huawei iMaster NCE-CampusInsight is totally different from the traditional monitoring mode that focuses on resource status. This platform applies AI to the O&M field and uses Telemetry technology to collect performance indicators and log data of network devices. By using big data, AI algorithms, and more advanced analytics technologies as well as leveraging scenario-specific continuous learning and expert experience, iMaster NCE-CampusInsight frees O&M personnel from nerve-wracking alarms and noises, making user experience visualized and O&M automated and intelligent.
The intelligent O&M solution integrates iMaster NCE-CampusInsight, iMaster NCE-Campus, and devices. Currently, iMaster NCE-CampusInsight can manage and provide intelligent analysis for Huawei cloud switches and cloud APs.
Devices need to periodically report data to iMaster NCE-CampusInsight. Therefore, the campus network needs to reserve bandwidth for data reporting. The average bandwidth consumed by each device is 3 kbit/s.
Network bandwidth design
iMaster NCE-CampusInsight and iMaster NCE-Campus can be deployed at different locations. They can collaborate with each other as long as network connectivity is available. To avoid the instability of the intermediate network, you are advised to deploy them in the same location, for example, in the same DC.
Deployment location design

## Slide 109: Precautions for Intelligent O&M Design
During network deployment, ensure that there are reachable routes between network devices and the analyzer iMaster NCE-CampusInsight so that the network devices can send KPI data and log information to iMaster NCE-CampusInsight.
During network deployment, ensure that devices are clock-synchronized with iMaster NCE-CampusInsight. You are advised to deploy an NTP server to synchronize the system clocks on the network.
Network deployment design
To identify DHCP-related connectivity issues and implement protocol trace, you need to use the AC as the DHCP server or enable DHCP snooping on the AC.
Protocol trace function design
The audio and video quality analysis function requires devices to send related log information to iMaster NCE-CampusInsight. You are advised to configure the same log sending interval for switches and WLAN devices. The maximum difference between the log sending intervals cannot exceed 20s.
Audio and video quality analysis function design
Intelligent radio calibration and traditional radio calibration cannot be both deployed on APs in the same region.
Intelligent radio calibration function design

## Slide 110
(Multiple-Answer Question) For a large-scale campus network with more than 50,000 terminals, the recommended fabric networking mode is ( ), the gateway is located on the ( ), and the ( ) functions as the edge node.
  Centralized gateway
  Distributed gateway
  Edge node
  Border node
  Access switch
  Aggregation switch
Notes: BCF

## Slide 111
To meet requirements of digital transformation, campus networks need to be reconstructed systematically. Based on the IDN concept, Huawei CloudCampus 3.0 Solution helps enterprises build intelligent, simplified, converged, open, and secure networks.
This course focuses on large- and medium-sized campus networks, illustrates the solution architecture and technical solutions used for such networks, and provides suggestions on engineering design and O&M design. With this information, this course helps trainees understand Huawei CloudCampus 3.0 Solution technologies and design the optimal campus network solution.

## Slide 112
CloudCampus 3.0 Solution V100R020C00 Product Documentation
  https://support.huawei.com/hedex/hdx.do?docid=DOC1100733970&lang=en
Design Guide of Huawei CloudCampus 3.0 Solution for Large- and Medium-Sized Network Scenario (Virtualization)
  https://e.huawei.com/en/material/networking/campusnetwork/1720e83a99cc47cc8bd5785741421fd0