## Slide 1
Datacom
V1.0
Shi Miaomiao/swx791350
2021.3.1
He Junjian/hwx580230
New

## Slide 2: Small- and Medium-Sized Cloud-Managed Campus Network Design

## Slide 3
With the development of technologies and digitalization of industries, services in small- and medium-scale scenarios, such as chain stores and branch offices, are gradually connected to the enterprise intranet through cloud-managed networks. A report of IDC reveals the radical difference between traditional products and cloud-based products in terms of annual growth rate from 2014 to 2018. For example, the annual growth rate of traditional Wi-Fi was only 5%, while that of cloud Wi-Fi was 38%. And the annual growth rate of traditional switches and access routers was just 2%, whereas that of cloud switches and access routers was as high as 61%.
The above-mentioned data shows that cloud-managed networks have become the trend in constructing small- and medium-sized campus networks. Cloud-based solutions help enterprises improve management efficiency and build networks that can quickly support the development of new services.
Huawei's CloudCampus Solution uses cloud computing technology to implement automatic and centralized network management, and provides data collection and analysis capabilities that are unavailable on traditional networks, so as to achieve network (LAN/WLAN) as a service (NaaS).
This document mainly describes the design and planning methods of small- and medium-sized campus networks in terms of the solution architecture, technical solution comparison, engineering design suggestions, and O&M.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the architecture of Huawei's CloudCampus Solution for small- and medium-sized campus networks.
  Describe typical networking schemes for small- and medium-sized campus networks.
  Independently design the CloudCampus solution for small- and medium-sized campus networks based on user requirements, including networking design, physical network design, site deployment design, basic network service design, WLAN design, and admission control design.

## Slide 5
Small- and Medium-Sized Campus Network Trends and Challenges
Overview of Huawei's CloudCampus Cloud-Managed Network Solution for Small- and Medium-Sized Campus Networks
Design of Small- and Medium-Sized Campus Networks with Huawei's CloudCampus Cloud-Managed Network Solution

## Slide 6: Challenges Faced by Small- and Medium-Sized Campus Networks
Accelerated industry changes
Problems in traditional deployment and management solutions
Low deployment efficiency, which slows down service provisioning
Site survey, planning, deployment, software commissioning, configuration, and optimization must be completed onsite by professional IT personnel.
Complex network management and high OPEX
Local professional O&M results in low O&M efficiency and high labor costs. The network management system (NMS), policy control server, charging system, and data analysis platform are deployed independently, causing high management and maintenance costs.
Poor network openness
The open data provided by multiple management systems on the traditional network needs to be further integrated. In addition, due to the incompatibility of API, the network and applications are connected at a slower speed than application development.
Network cloudification brings rapid development in new ICT technologies, such as cloud computing, cloud security, big data, and IoT, leading to tremendous changes in all industries.
Traditional retailers such as shopping malls and supermarkets offer free Wi-Fi as a way to attract and retain customers, and they also use wireless positioning and customer flow analytics to carry out precision marketing.
In the education sector, e-classrooms are becoming more and more popular, and diversified multimedia teaching methods further stimulate students' interest in learning.
Smart healthcare enables hospitals and other healthcare institutions to connect to each other through networks. This implements unified management and analysis of medical data and facilitates medical treatment.
As a pipe that carries upper-layer services and data, the network is becoming more and more complex with a growing number of nodes.

## Slide 7: Service Requirement Analysis for Small- and Medium-Sized Campus Networks
Configurations of multiple sites are centrally delivered, reducing onsite configuration and commissioning workload and improving deployment efficiency.
Network devices are plug-and-play and able to be expanded on demand, requiring low cost for upgrades.
Network devices at a site
Unified management and centralized configuration
Plug-and-play and on-demand expansion
Plug-and-play network devices improve deployment efficiency
Geographically dispersed campus branch networks are centrally managed on the cloud through the Internet.
Troubleshooting and monitoring tools as well as many other automation tools are integrated for remote automatic O&M.
Centralized cloud management of multiple branches and remote automatic O&M
Site network 1
Site network 2
Site network N
Cloud-based centralized O&M simplifies multi-site O&M
With open APIs and big data analytics capabilities, the cloud management platform can interconnect with multiple management systems to achieve unified network management.
It is also able to provide diversified value-added applications to lead enterprises into digital transformation.
Site network
Site network
Site network
Openness and big data analytics capability
Cloud management platform
Open APIs accelerate business application integration

## Slide 8: Small- and Medium-Sized Campus Network Trends
Network cloudification
Due to evolution to the cloud architecture, enterprises can focus more on their mission-critical services, without paying too much attention to IT architecture construction.
To support service cloudification, enterprises need to create a ubiquitous, intelligent, controllable, and on-demand network.
The network needs to become more a service than a solution.
Cloud security
Cloud security become more important than ever.
Facing cloudification, enterprises are vulnerable to attacks that are fundamentally different from those on traditional networks when providing various services.
Security has shifted from passive defense to proactive defense.
Detection and response have become as important as defense.
IoT
The rise of IoT leads to a huge increase in the number and types of terminals accessing the network, and these terminals generate a large amount of data.
Diversified IoT sensing networks need to be smoothly connected to the existing campus network.
The types of terminals connected to the campus network are more complex than ever. As a result, the campus network becomes a converged network that accommodates multiple types of terminals and media.

## Slide 9
Small- and Medium-Sized Campus Network Trends and Challenges
Overview of Huawei's CloudCampus Cloud-Managed Network Solution for Small- and Medium-Sized Campus Networks
Design of Small- and Medium-Sized Campus Networks with Huawei's CloudCampus Cloud-Managed Network Solution

## Slide 10: Huawei CloudCampus Cloud-Managed Network Solution
Ultra-broadband connection, improving network and application quality
Simplified management, reducing OPEX
AI-powered cloud-based Intelligent O&M
Industry-specific applications
Multi-tenant network
Cloud management platform
Value-added SaaS platform
All-scenario WLAN: large bandwidth, high concurrency, and low latency
Secure, reliable platform and network: in compliance with the laws and regulations of the industry and countries concerned
Open APIs: key driver of industry-specific applications and digital transformation
Online network planning platform for both indoor and outdoor scenarios: customized network planning templates; support for automatic generation of network planning reports
Diversified scenario-specific configuration packages: one-stop configuration of topologies as well as related device models and parameters
O&M based on GIS maps, logical topologies, and an easy-to-use mobile app
Online centralized inspection of multiple branches; automatic inspection report generation
Intelligent network O&M: proactively predicts potential faults, ensuring user and application access experience
SD-WAN: intelligently ensures WAN interconnection of mission-critical services, delivering ultimate experience to branches
Notes: In this slide, CloudCampus Network refers to Huawei's CloudCampus Cloud-Managed Network Solution for Small- and Medium-Sized Campus Networks.

## Slide 11: Architecture of Huawei's Cloud-Managed Network Solution
Hotel
Mini-store
Supermarket/Shopping mall
Firewall
Switch
AP
AP
AP
Firewall
Switch
Central AP
RU
AR
Shopping center, primary/secondary school
Firewall
Switch
DCN
AR
Multi-tenant network
Cloud management platform
Value-added SaaS platform
Internet
Internet
Internet
Internet
Big data analytics
Customer flow analysis
ESL
App
...
RESTful API
WAC
Huawei public cloud scenario
MSP-owned cloud scenario
On-premises scenario
Cloud-based network planning
Cloud-based deployment
Cloud-based O&M
Cloud-based inspection
Notes: Huawei's CloudCampus Solution applies to three deployment scenarios: Huawei public cloud, MSP-owned cloud, and on-premises. The on-premises scenario applies to large- and medium-sized campus networks. The Huawei public cloud and MSP-owned cloud scenarios apply to small- and medium-sized campus networks. This document focuses on the Huawei public cloud scenario, which is a cloud management scenario.
Huawei's CloudCampus Solution for small- and medium-sized campus networks uses cloud computing technology to implement automatic and centralized network management, and provides data collection and analysis capabilities that are unavailable on traditional networks, so as to achieve network (LAN/WLAN) as a service (NaaS).
There are three layers in the architecture of Huawei CloudCampus Solution for small- and medium-sized campus networks: multi-tenant network, cloud management platform, and value-added SaaS platform.
Multi-tenant network: It consists of over one hundred network devices, including APs, switches, firewalls, and ARs, and is deployed at the customer side to provide user access.

## Slide 12
Notes: Cloud management platform: iMaster NCE-Campus — an SDN controller — is the core component of the CloudCampus Solution. It is also a cloud-based network management, O&M, and control system. In addition to offering basic management and configuration for cloud-based devices, remote O&M and monitoring, and user admission control, iMaster NCE-Campus can implement various value-added services based on the big data platform. iMaster NCE-CampusInsight is an intelligent network analysis engine and provides intelligent O&M services for user networks. It integrates AI to the O&M. Based on data such as device performance indicators and terminal logs, iMaster NCE-CampusInsight digitalizes user experience on the network through big data analytics, AI algorithms, and more advanced analysis technologies, helping customers detect network problems in a timely manner and improve user experience.
Value-added SaaS platform: iMaster NCE-Campus provides open interfaces to interconnect with other service systems (such as the big data platform) to offer tenants a variety of value-added application services, such as customer flow analysis, business portal push, electronic shelf label (ESL), asset management, and medical IoT.

## Slide 13: Components of Huawei's CloudCampus Network Solution
Cloud-managed devices and a mobile app (for remote O&M)
Deployment environment
Cloud management platform
Huawei support system
ESDP platform (for licenses)
Huawei's support website
(for software versions & patches)
PKI platform
(for device certificates)
ServiceTurbo-Cloud
Mobile app
Firewall
AR
Switch
AP
Central AP
RU
Registration center
Huawei public cloud
Cloud
WAC
Notes: ServiceTurbo-Cloud (https://serviceturbo-cloud.huawei.com/) is an enterprise tool service cloud platform. It provides one-stop tool services for Huawei, partners, and customer service engineers in government and enterprise service scenarios.

## Slide 14: Solution Component: iMaster NCE-Campus
iMaster NCE-Campus is a main configuration and management platform in the CloudCampus Solution. It is a main portal for CloudCampus service configuration, O&M, and monitoring.
Management + Control + Analysis
Plan + Construct + Maintain + Optimize
iMaster NCE-Campus, an autonomous driving campus network management and control system
Application service layer
Infrastructure layer
Management, control, and analysis layer
MDM
e-Schoolbag
Asset management
Health management
…
Intelligent OAM
Automated + Intelligent
All-in-one
Unified data base
Centralized detection/locating/processing
Full-lifecycle management
Simulation/Verification/Monitoring/Optimization
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting

## Slide 15: Solution Component: Registration Center
At branches, devices can automatically go online on the cloud management platform without additional configuration.
Synchronizes device information (ESN and MAC address)
Huawei registration center
Network devices at branches
Internet
Query the IP address and port number of the cloud management platform
Initiate a registration request after obtaining the cloud management platform address
Devices are already preset with the registration center domain (register.naas.huawei.com) before factory delivery. No additional configuration is required.
Bidirectional authentication and encryption are performed for query channels based on HTTP/2, ensuring that user device information is not disclosed.
Multiple registration centers are deployed around the world.
The smart DNS returns the address of the registration center server nearest to devices, ensuring fast query.
1
2
Work out of the box
Secure transmission
Wide coverage
Quick response

## Slide 16: Solution Component: iMaster NCE-CampusInsight
Topology mgmt.
Performance mgmt.
Alarm mgmt.
Configuration mgmt.
AS-IS: device-centric network management
TO-BE: AI-powered intelligent O&M centered on user experience
Device-centric, lacking insights into user experience
Passive response, unable to identify potential faults
Heavy reliance on onsite fault locating by experienced engineers
SNMP
Minute-level network data collection
Visualized experience: Telemetry-based second-level data collection, visualizing experience of any user, in any application, at any moment
Minute-level identification and root cause locating for potential faults
Identifies potential faults based on dynamic baselines and big data correlation analysis.
Accurately locates root causes using KPI correlation analysis and protocol trace.
Predictive network optimization: AI is used to intelligently analyze the load trends of APs so as to complete predictive optimization of wireless networks.
In addition to using algorithms to improve efficiency, intelligent O&M leverages scenario-based continuous learning and accumulated expert experience to free O&M personnel from complex alarms and alerts, making O&M more automated and intelligent.
Traditional NMS
Telemetry
Second-level network data collection
Visualized experience management
User journey playback
Potential fault identification
Root cause identification
Predictive network optimization
Notes: AS-IS: the current status
TO-BE: future ideal status

## Slide 17: Solution Component: WLAN Planner
The WLAN Planner is an efficient WLAN network planning tool. It enables signal simulation, helping determine AP deployment locations and signal coverage results.
Efficient support for WLAN network planning
Installation-free
All scenarios supported
High efficiency
High quality
Cloud-based tool, without software installation
Indoor, outdoor, agile distributed, and high-density scenarios
Higher simulation efficiency than the standalone edition
Field-proven in 10,000+ WLAN projects

## Slide 18: Solution Component: CloudCampus APP
Site survey
Network planning
Deployment
O&M
Acceptance
Mobile APP that covers full lifecycle management for campus networks
Connects to the cloud-based WLAN Planner to record photos and texts based on drawings.
Connects to the cloud-based WLAN Planner to display network planning results, heat maps, and AP attributes anytime anywhere.
One-click test, single service test, project test
Deployment position acceptance based on the cloud-based network planning project
Deployment by scanning barcode
Mobile O&M, device and application monitoring
AP access through Bluetooth/management VAP, AP offline diagnosis
E2E simplicity from planning and deployment, all the way to O&M

## Slide 19: Solution Component: Hardware Products
CloudEngine S series switches
AirEngine Wi-Fi 6 APs
High-performance campus switches
Campus APs
(e.g., indoor settled APs, indoor wall plate APs, agile distributed APs, and outdoor APs)
NetEngine ARs
Campus egress routers
(integrating routing, switching, Wi-Fi, 5G, and security functions)
HiSecEngine AI firewalls
Firewalls
(providing comprehensive network security protection capabilities)

## Slide 20: Solution Technology: Plug-and-Play of Devices
Simplified network deployment
The time and labor costs for initial device installation and configuration as well as upgrade are reduced.
After devices on the campus are powered on and connected to the Internet, they can obtain the IP address of the controller iMaster NCE and register with it through multiple methods. All subsequent operations can be performed on the controller, without the need of onsite visits.
Services are deployed on the iMaster NCE in advance, greatly shortening the deployment time.
The configuration error rate is reduced due to GUI-based operations.
Internet
Firewall
AP
Internet
AR
Internet
Site network
Site network
Site network

## Slide 21: Plug-and-Play of Devices (1)
Through CloudCampus APP (barcode scanning)
Through registration center
Devices supported: AP
Devices supported: AR, firewall, switch, AP
Internet
Scan barcode
Tenant: Tenant X
Site: Site Y
Device: AP (ESN...)
1
2
The CloudCampus APP obtains the ESN and MAC address of the AP.
Report AP information.
3
4
5
Register and get managed.
Site network
1.1.1.1:8080
Huawei registration center
1
Record device information.
2
Synchronize device information.
4
Automatically initiate a query request to Huawei registration center to obtain the IP address and port number of iMaster NCE.
Internet
6
Register and get managed.
Tenant: Tenant X
iMaster NCE: 1.1.1.1:8080
Device: AP (ESN...)
3
5
Proactively initiate a registration request to iMaster NCE.
Site network

## Slide 22: Plug-and-Play of Devices (2)
Through web system
Through CLI
Devices supported: AR, firewall, switch, AP
Devices supported: AR, firewall, switch, AP
Internet
2
Register and get managed.
1
In the web system, configure Internet access parameters and IP address/URL and port number of iMaster NCE.
Web
Site network
Internet
2
Register and get managed.
1
On the CLI, configure Internet access parameters and IP address/URL and port number of iMaster NCE.
CLI
Site network

## Slide 23: Plug-and-Play of Devices (3)
Through DHCP Option 148
Internet
AR
1
The network administrator has deployed the DHCP service on the network in advance (by deploying the DHCP service on the egress device or deploying an independent DHCP server.)
In addition to delivering IP addresses to the devices to be deployed, the DHCP server uses DHCP Option 148 to notify the devices of the iMaster NCE IP address and port number.
2
DHCP request
3
DHCP response carrying Option 148
4
Proactively initiate a registration request to iMaster NCE.
Devices supported: AR, switch, AP
Switch to be deployed
Site network

## Slide 24: Plug-and-Play of Devices (4)
Email-based deployment
Devices supported: AR
Internet
1
Network administrator
Email server
Site deployment personnel
AR
2
3
4
The network administrator configures ZTP and selects the email-based deployment mode on iMaster NCE.
iMaster NCE packs the deployment configuration into a series of character strings and sends them to the email address specified by the administrator.
The site deployment personnel log in to the email box on a PC at the site and receive the deployment email.
During site deployment, the site deployment personnel connect the PC to the AR in wired or wireless mode and click the hyperlink in the email body. The PC then automatically logs in to the AR, parses the parameters in the hyperlink to obtain the deployment configuration of the AR, and writes the configuration into the AR.
The AR connects to the Internet and automatically sends a registration request to iMaster NCE.
Site network
3
5

## Slide 25: Solution Technology: Cloud Management
Analysis
Management
Control
One-stop management platform
Firewall
Switch
AP
AP
Firewall
AR
AR
Small- and medium-sized campus network
Internet
Internet
Site management
Device management
User management
Inter-site VPN
Portal page customization
WLAN experience
Customer flow analysis
Higher management and O&M efficiency
After devices go online, iMaster NCE provisions all required configurations and services. iMaster NCE delivers configurations to devices at the branch sites through NETCONF, without the need of CLI-based operations. This simplifies network O&M.
iMaster NCE performs intelligent analysis and display of the operating status of branch sites, presenting intuitive insights into site health.
iMaster NCE provides operating status monitoring, intelligent analysis, and remote O&M, so that O&M personnel do not need to visit sites. This improves O&M efficiency and reduces O&M costs.
NETCONF/YANG

## Slide 26: Highlights of Huawei CloudCampus Solution for Small- and Medium-Sized Campus Networks
Automatic deployment: Devices can be easily and quickly deployed.
Cloud-based network planning and mobile O&M: WLAN design and device O&M are simplified.
Diversified product portfolios: Huawei provides different product portfolios, including full series of network devices (switches, firewalls, ARs, and APs), meeting diversified network requirements of tenants.
Dual-working-mode: All network devices used in this solution can work in either cloud-based or traditional management mode. Tenants can implement cloud management of traditional devices after devices are upgraded.
VASs: Terminal behavior analysis is a value-added application of iMaster NCE-Campus. More VASs can be developed based on terminal behavior analysis.

## Slide 27
Small- and Medium-Sized Campus Network Trends and Challenges
Overview of Huawei's CloudCampus Cloud-Managed Network Solution for Small- and Medium-Sized Campus Networks
Design of Small- and Medium-Sized Campus Networks with Huawei's CloudCampus Cloud-Managed Network Solution

## Slide 28: Overall Design Process
Overall design
Networking design
Service design
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M

## Slide 29: Choose the Network Management Mode
Which management mode to use: cloud management or on-premises?
On-Premises
MSP-owned Cloud
Scenario definition
Target application scenario
Huawei Public Cloud
Customers purchase and own software such as the controller and analyzer, and deploy the software in their data center or on a public cloud IaaS platform to manage their own networks. They do not provide network management services.
MSPs purchase cloud management platform software, such as the controller and analyzer, and deploy the software in their data center or on a public cloud IaaS platform to provide network management services.
Customers purchase Huawei public cloud management services and manage their networks using the cloud management SaaS services deployed on Huawei public cloud platform.
Large- and medium-sized campus networks
Small- and medium-sized campus networks
Small- and medium-sized campus networks
Huawei's CloudCampus Solution
Small- and medium-sized campus networks are small in scale and are sensitive to CAPEX and OPEX. Therefore, the public cloud management mode is recommended for such networks. In this mode, Huawei or MSPs provide SaaS services to manage the networks.
Notes: The public cloud management mode can be Huawei public cloud management mode or MSP-owned cloud management mode. The two modes are essentially the same. The only difference lies in the operational entity and the provider that offers cloud management services.
Unless otherwise specified, the Huawei public cloud management mode is used as an example in this document.

## Slide 30: Choose the Network O&M Mode
Which O&M mode to use: enterprise-managed O&M (enterprises perform O&M by themselves) or MSP-managed O&M (enterprises authorize network O&M to MSPs)?
  The network O&M mode is closely related to the network management mode. If an enterprise manages the network by itself, O&M is also performed by the enterprise. This is called enterprise-managed O&M. If an enterprise authorizes network O&M to an MSP, this is called MSP-managed O&M.
  Huawei's CloudCampus Solution supports both enterprise-managed O&M and MSP-managed O&M. Enterprises can flexibly choose either of them as required.
Enterprises themselves have O&M capabilities
Enterprise-managed O&M
Enterprises require managing their own networks
Enterprises themselves do not have O&M capabilities
Enterprises have many branches and authorize MSPs to construct and maintain their networks
MSP-managed O&M
or
or
Platform operator
Tenant 1
Site
MSP 1
Tenant 2
Tenant N
Site
Site
Site
Authorizing network O&M to MSP
Authorizing network O&M to MSP
Notes: With certain IT capabilities, a tenant administrator can deploy and maintain a campus network. This scenario is called tenant-managed construction and maintenance. The tenant administrator is the main implementer, and the MSP administrator only provides simple deployment assistance. The tenant administrator can apply to the MSP for the managed construction and maintenance services. After being authorized, the MSP constructs and maintains the campus network for the tenant. This scenario is called MSP-managed construction and maintenance, in which the MSP administrator is the main implementer.
The following lists the differences between the deployment processes in the tenant-managed construction and maintenance and MSP-managed construction and maintenance scenarios:
Tenant-managed construction and maintenance:
  The tenant administrator installs cloud managed devices onsite and registers the cloud managed devices.
  The tenant administrator logs in to iMaster NCE using their own account and deploys services.

## Slide 31
Notes: MSP-managed construction and maintenance:
  The MSP administrator helps the tenant install cloud managed devices onsite and register the cloud managed devices.
  The tenant administrator logs in to iMaster NCE using their own account, chooses System > System Management > Tenant Information, enables Authorize MSP, and sets the authorization scope. Alternatively, when creating a tenant administrator, the MSP administrator can enable Authorize MSP. By default, the permission of the tenant administrator role is granted.
  The MSP administrator logs in to iMaster NCE using their own account. In Tenant List on the home page, the MSP administrator selects a tenant who applies for MSP-managed construction and maintenance and has been authorized. The Authorization status column is displayed as Authorized.
  Click the tenant name to access the page for MSP-managed construction and maintenance. The MSP administrator helps the tenant deploy services.

## Slide 32: Choose the License Transaction/Purchase Mode
Select the cloud management deployment scenario (Huawei public cloud or MSP-owned cloud), then select the license transaction or purchase mode accordingly.
Scenario 1: Huawei public cloud
Scenario 2: MSP-owned cloud
Licenses control the available resources of tenants.
Online transaction mode is supported. That is, licenses can be purchased online from HUAWEI CLOUD. License pooling is not supported in this mode.
Offline transaction mode is also supported. License activation codes need to be loaded on the CloudCampus cloud management platform. License pooling and co-termination are supported in this mode.
Huawei's customer (tenant)
Channel
partners
Strategic/
Core NAs
Retail
customers
License transaction mode
Offline
transaction
Online transaction
Offline purchase
CloudCampus cloud management platform
Licenses control the available resources of the CloudCampus cloud management platform, but not the available resources of tenants.
Only offline transaction mode is supported. The license file needs to be loaded on the CloudCampus cloud management platform. License pooling and co-termination are supported in this mode.
Huawei's customer (MSP)
MSP, carrier
License transaction mode
Offline transaction
CloudCampus cloud management platform
MSP's customer (tenant)
Tenant 1
Tenant N

## Slide 33: Choose the License Consumption and Termination Modes
In the Huawei public cloud scenario, both the co-termination and non-co-termination licensing models are supported.
Co-termination licensing mode
Licenses are pooled and shared by all devices, and co-terminate for all devices.
Co-termination of licenses cannot be undone. Therefore, the license termination time must be properly designed.
Non-co-termination licensing mode
Licenses are pooled and shared by device type. License resources are exclusive to devices of one type and not shared by devices of other types.
Licenses for different types of devices terminate separately, while licenses for devices of the same type co-terminate.
Notes: For small- and medium-sized campus networks, the co-termination licensing model is recommended, facilitating device management and operations. If the license validity periods of devices of different types need to be precisely controlled, use the non-co-termination licensing model.

## Slide 34: Overall Design Process
Network architecture
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Networking scheme
Reliability
WAN interconnection
Network management mode
Network O&M mode
License scheme
Overall design
Networking design
Service design

## Slide 35: Network Architecture Design: Intranet Architecture (1)
Internet
AP
Internet
AR
Internet
Firewall
Single-device networking architecture
Internet
Firewall or AR
AP
Switch
AP
Single-layer networking architecture
Internet
Firewall or AR
AP
Switch
AP
Two-layer networking architecture
Switch
Access layer
Access layer
Aggregation layer

## Slide 36: Network Architecture Design: Intranet Architecture (2)
Internet
Firewall or AR
AP
Switch
AP
Three-layer networking architecture
Switch
Access layer
Aggregation layer
Switch
Core layer
Internet
Firewall or AR
AP
Switch
AP
Highly reliable networking architecture
Switch
Access layer
Aggregation layer
Switch
Core layer
Internet
Stack link
(Note: Unless otherwise specified, the symbol indicates stacking.)
Link aggregation

## Slide 37: Network Architecture Design: WAN Interconnection
Hub
HQ
Branch 1
Spoke
Branch 2
Spoke
Branch 3
Spoke
HQ
Branch 1
Branch 2
Branch 3
HQ
Branch 1
Branch 2
Branch 3
Hub-spoke networking
Full-mesh networking
Partial-mesh networking
Notes: Hub-spoke: Generally, the enterprise headquarters or DC functions as a hub site. Each branch site of an enterprise can communicate with the hub site and can communicate with other branch sites through the hub site. This model is applicable to scenarios where traffic between all branch sites of an enterprise must pass through the headquarters for centralized security monitoring.
Full-mesh: All sites of an enterprise can communicate with each other. If traffic needs to be transmitted between the headquarters and branches or between branches, data is directly exchanged without traversing an intermediate node. This model is applicable to scenarios where all sites of an enterprise need to directly access each other. This model eliminates the delay caused by traffic transmission through the headquarters.
Partial-mesh: Most sites of an enterprise can directly communicate with each other. However, the underlay WAN networks of a small number of sites cannot directly communicate with each other. For example, in the figure, branch 1 and branch 3 need to communicate with each other through the headquarters.

## Slide 38: Network Architecture Design Considerations
Determine the intranet architecture
(Optional) Determine the WAN interconnection model
(Optional) Determine
reliability requirements
Determine the network architecture layers based on the number of access terminals or device capabilities. Determine the device model at each layer and the mapping between upper-layer and lower-layer devices.
Single-device networking architecture
Single-layer networking architecture
Two-layer networking architecture
Three-layer networking architecture
Determine the WAN interconnection model based on the communication requirements between sites.
Hub-spoke networking
Full-mesh networking
Partial-mesh networking
Determine the highly reliable networking model based on the device type and capability
Firewalls are deployed in hot standby mode
Switch stacking
Eth-Trunk
1
2
3

## Slide 39: Overall Design Process
Network architecture
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Networking scheme
Reliability
WAN interconnection
Network management mode
Network O&M mode
License scheme
Overall design
Networking design
Service design

## Slide 40: Single-Device Networking
Internet
AP
Internet
AR
Internet
Firewall
Network scale
Networking type
Overview
Applicable to single stores and small stores (such as agent stores and gas stations)
A single device provides gateway features, such as PPPoE dialup, DHCP, and NAT.
An AP is deployed if only wireless access is required and only one wired Internet egress is available.
An AR is deployed if wired access is needed and multiple uplinks, especially a 3G/4G backup link, are required.
A firewall is deployed if security-sensitive stores, such as small logistics, office, and finance organizations, require advanced security features, including URL filtering, security protection, and antivirus.
Constraints
Wireless features such as roaming and load balancing are not supported.
The AP supports only one Internet link.
The AP and AR support wired user access, but do not support wired user authentication.
The AR supports wireless user authentication in only Open, PSK, and Portal authentication modes, but not 802.1X or MAC address authentication mode. The firewall provides wired user authentication and supports only Portal authentication.
Currently, no firewall model supports Wi-Fi and LTE, and therefore it is not recommended in actual deployments.
< 50 terminals; area < 50 m2
3G/4G

## Slide 41: Egress Gateway + AP
Overview
Applies to small- and medium-sized clothing stores, supermarkets, shopping malls, etc.
The egress gateway provides features such as PPPoE, DHCP, NAT, and LTE.
This networking mode supports continuous coverage of multiple APs, as well as multiple uplinks, including a 3G/4G backup uplink.
APs support mesh networking.
A firewall is deployed at the egress for scenarios where advanced security features, including URL filtering, security protection, and antivirus, need to be met.
Constraints
The AP and AR support wired user access, but do not support wired user authentication.
The firewall provides wired user authentication and supports only Portal authentication.
If the AR or firewall does not support PoE, the AP can use an external PoE power adapter.
AR + AP
Firewall + AP
Network scale
Networking type
< 200 terminals; area < 300 m²
Internet
3G/4G
Internet

## Slide 42: Egress Gateway + Layer 2 Switch + AP
Overview
Applies to small- and medium-sized clothing stores, retail stores, etc.
The egress gateway provides features, such as WAN access, DHCP, and NAT.
The Layer 2 switch provides PoE extended access and wired terminal access functions.
APs provide access services for wireless terminals at the site.
APs support mesh networking.
A firewall is deployed at the egress for scenarios where advanced security features, including URL filtering, security protection, and antivirus, need to be met.
Constraints
The AR and firewall in cloud management mode do not support Eth-Trunks and cannot connect to the switch through Eth-Trunks.
If switches need to be stacked, it is recommended to deploy multiple layers of switches.
The AR can be deployed only in a single-node system.
AR + Layer 2 switch + AP
Network scale
Networking type
Internet
3G/4G
Internet
< 2000 terminals; area < 3000 m²
Firewall + Layer 2 switch + AP

## Slide 43: Egress Gateway + Layer 2 Switch + Distributed AP
Overview
Applies to dense-room building scenarios, such as dormitories and hotels, where network planning is not required and each room transmits signals separately.
The AR functions as the egress gateway and provides features, such as WAN access, DHCP, and NAT.
The Layer 2 switch provides PoE extended access and wired terminal access functions.
APs provide access services for wireless terminals at the site.
APs support mesh networking.
A firewall is deployed at the egress for scenarios where advanced security features, including URL filtering, security protection, and antivirus, need to be met.
Constraints
The AR and firewall in cloud management mode do not support Eth-Trunks and cannot connect to the switch through Eth-Trunks.
If switches need to be stacked, it is recommended to deploy multiple layers of switches.
The AR can be deployed only in a single-node system.
AR + Layer switch + distributed AP
Internet
3G/4G
Internet
Network scale
Networking type
< 2000 terminals; area < 3000 m²
Firewall + Layer switch + distributed AP

## Slide 44: Summary of Typical Networking Schemes (1)
Deployment Scenario | Network Scale | Key Networking Requirements | Networking Model |  | Remarks
Many branches, where they are no demands for branch interconnection | < 50 terminals; area < 50 m2 | Single store; wireless access only; single Internet egress | Singe-device networking | AP | 
 |  | Single store; mainly wireless access; Ethernet or LTE uplink |  | AR | 
 |  | Single store; wired and wireless authentication and access; multiple Internet uplinks and LTE uplinks; high security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall | Currently, firewalls have no Wi-Fi/LTE models.
 | < 200 terminals; area < 300 m² | Wireless access only; multiple Internet uplinks and LTE uplinks | Egress gateway + AP | AR + AP | Currently, ARs and firewalls do not have PoE models. APs need to connect to external power supplies.
 |  | Wired and wireless authentication and access; multiple Internet uplinks; high security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall + AP | 
 | < 2000 terminals; area < 3000 m² | Wired and wireless access; multiple Internet uplinks and LTE uplinks | Egress gateway + Layer 2 switch + AP | AR + Layer 2 switch + AP | 
 |  | Wired and wireless authentication and access; multiple Internet uplinks; high security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall + Layer 2 switch + AP | 
Notes: Cloud management for small- and medium-sized campus networks applies to small- and medium-sized enterprises (SMEs) and branches, such as shopping malls/supermarkets, retail stores, hotels, educational institutions, and financial services organizations. Different networking models are used based on different network scales.

## Slide 45: Summary of Typical Networking Schemes (2)
Deployment Scenario | Network Scale | Key Networking Requirements | Networking Model |  | Remarks
Many branches, where they are no demands for branch interconnection | < 2000 terminals; area < 3000 m² | Dense-room scenarios such as hotels and dormitories; wired and wireless access; multiple Internet uplinks and LTE uplinks | Egress gateway + Layer 2 switch + distributed AP | AR + Layer 2 switch + central AP + RU | 
 |  | Dense-room scenarios such as hotels and dormitories; wired and wireless access; multiple Internet uplinks; high security requirements (URL filtering/IPS/security defense/antivirus) |  | Firewall + Layer 2 switch + central AP + RU | 
Multiple branches, where there are demands for communication with the headquarters | Same as that in the "many branches, branches, where they are no demands for branch interconnection" scenario | Only basic communication between branches and the headquarters is required. Third-party VPN gateways may be deployed at the headquarters. | IPsec VPN interconnection | AP/AR/firewall as the egress gateway | 
 |  | Multiple links are deployed between the headquarters and branches, and intelligent traffic steering is required. | SD-WAN Interconnection | AR as the egress gateway | 

## Slide 46: Overall Design Process
Network architecture
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Networking scheme
Reliability
WAN interconnection
Network management mode
Network O&M mode
License scheme
Overall design
Networking design
Service design

## Slide 47: Network Reliability Design
Internet
Firewall or AR
AP
Switch
AP
Highly reliable networking architecture
Switch
Access layer
Aggregation layer
Switch
Core layer
Internet
Networking reliability refers to the reliability design of the tenant network. You can add devices or links in any typical networking scheme to enhance network reliability. Network reliability design can be classified into three levels based on the involved scope:
  Link-level reliability design
  Device-level reliability design
  Network-level reliability design (which combines link and device reliability)

## Slide 48: Link-Level Reliability Design (1)
Intranet link reliability
Multiple links can be deployed between switches and bonded using Eth-Trunks to improve link reliability.
When switches are stacked, it is recommended that Eth-Trunks be used across switches to ensure link reliability.
Stacking
Stacking
Stacking
Stacking
Stacking

## Slide 49: Link-Level Reliability Design (2)
Egress link reliability
Multiple links are deployed at the campus egress and work in active/standby mode. The networking scheme is as follows:
The "single device, multiple egress links" scheme or the "multiple devices, at least one egress link for each device" scheme can be used. The latter scheme is recommended.
To further improve reliability, it is recommended that different egress links be connected to different carrier networks.
ISP 1
ISP 2
ISP 1
ISP 2
Dual devices, dual egress links
Single device, dual egress links
ISP 1
ISP 2
Heartbeat link
ISP 1
ISP 2

## Slide 50: Device-Level Reliability Design
Egress firewalls in hot standby
Heartbeat link
Dual AR egress gateways
ISP 1
ISP 2
ISP 1
ISP 2
Switch stacking
Switch
Switch
Switch
Stacking
Stacking
Notes: Device reliability: Fixed-configuration devices are generally used on small- and medium-sized campus networks.
Device reliability design includes the following two aspects:
Redundant components are used to improve device reliability.
  In addition to selecting devices with high reliability, you can further improve the reliability of the devices by using dual power supplies or redundant components (e.g. boards).
Joint networking is used to provide device reliability.
  Multiple devices are deployed together to improve device reliability, for example, active/standby or stacking.
  Two devices are deployed in the egress zone of the campus network to work in active/standby mode. Currently, in a two-node system, firewalls support only the hot standby mirroring mode. ARs support dual-CPE networking, and the two devices and two egress links can work concurrently.
  Intranet network devices, such as LAN switches at the core or aggregation layer, are stacked to implement device-level backup. Currently, only switches can be stacked.

## Slide 51: Network-Level Reliability Design
Internet
AR
AP
Switch
AP
Switch
Access layer
Aggregation layer
Switch
Core layer
Internet
Typically, Eth-Trunk and stacking technologies are used in dual-device and multi-link scenarios to improve network-wide reliability.
Egress reliability design:
Dual-device: active/standby, load balancing
Multi-link, multi-carrier network
Intranet reliability design: switch networking
Dual-/multi-device: stacking
Dual-/multi-link: Eth-Trunk
Stacking
Stacking

## Slide 52: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Overall design
Networking design
Service design

## Slide 53: CloudCampus WAN Interconnection Solution
Static IPsec VPN
Internet
Branch
HQ
An IPsec VPN is a type of static VPN, in which IPsec tunnels are established between devices at different sites to create VPN tunnels. Traffic is diverted to the VPN tunnels based on the configured static routes to implement inter-site communication.
Egress devices can be APs, ARs, or firewalls (firewalls can be deployed in standalone or hot standby mode).
IPsec VPN tunnel
SD-WAN interconnection
EVPN can be used to establish tunnels between sites and dynamically advertise routes on demand. The forwarding plane supports GRE or GRE over IPsec. In addition, high-quality links can be selected based on applications and policies for data transmission, implementing application- and policy-based intelligent traffic steering.
The egress devices must be ARs (in standalone or hot standby mode).
Internet
Branch
HQ
MPLS
GRE or GRE over IPsec tunnel
Notes: The multi-campus network interconnection solution is a sub-solution provided in the CloudCampus Solution for the interconnection between branch campuses and between branches and the HQ or DCs. With the SD-WAN solution integrated, the multi-campus network interconnection solution provides two models for WAN interconnection: static IPsec VPN and EVPN.
An IPsec VPN is a type of static VPN, in which IPsec tunnels are established between devices at different sites to create VPN tunnels. Traffic is diverted to the VPN tunnels based on the configured static routes so that services between sites can be accessed through the VPN tunnels.
An EVPN is a type of dynamic VPN that can establish tunnels between sites and dynamically advertise routes on demand. EVPN establishes GRE tunnels between sites to establish VPN tunnels and supports IPsec encryption on GRE tunnels to ensure tunnel encryption security. In addition, the EVPN solution offers application- and policy-based intelligent traffic steering, allowing high-quality links to be selected based on applications and policies for data transmission.

## Slide 54: IPsec VPN Interconnection Networking Model
Internet
Internet
Network interconnection model
The hub-spoke and full-mesh models are supported.
The hub-spoke model is applicable when data traffic is mainly transmitted between branches and the HQ. In this model, branches can also communicate with each other through the HQ.
If branches are of similar scales and a large amount of traffic is transmitted between the branches, the full-mesh model can be used. In this case, all egress devices must use public IP addresses, and only firewalls support this model. In the full-mesh model, the number of sites is limited (32 at most). Therefore, the hub-spoke model is recommended for IPsec interconnection.
Site networking
APs, ARs, or firewalls can be used as egress devices based on site requirements.
In some scenarios requiring high reliability, two egress links can be deployed. In scenarios requiring wireless uplinks, the egress gateway must be an LTE-capable device.
For large campus networks, the egress gateways can be deployed in hot standby mode to ensure high reliability. Currently, only firewalls support hot standby.
In the hub-spoke model, the hub site is usually the HQ or DC site, which requires high-performance devices, rich policies, and security configurations. Currently, the cloud management mode supports only a few security and policy features. Therefore, it is recommended that the traditional management mode be configured for devices at the hub site, and the devices work in hot standby mode.
Hub-spoke
Full-mesh
Network interconnection model
Site networking
Internet
AP
Internet
Internet
AR
Firewall
Internet
Internet
Heartbeat link

## Slide 55: SD-WAN Solution Overview (1)
MPLS
Data center
HQ
Internet
Branch
Branch
GRE/IPsec VPN
iMaster NCE
UI
Southbound NE layer
Site configuration
VN
O&M
Management channel
Control plane: BGP EVPN peer relationship
RR
Solution overview
The EVPN interconnection mode of the SD-WAN solution is applicable to the scenarios where a large number of branches communicate with the HQ/DC (hub site). This mode can meet the networking requirements of multiple HQs/regional centers. In this mode, the branches can communicate with the HQ through multiple links. In addition, this mode supports application- and quality-based intelligent traffic steering, QoS scheduling, and link quality display.
The hub-spoke, full-mesh, and partial-mesh networking models are supported.
Hub sites can work in active/standby mode to improve network access reliability at the HQ.
Multi-VPN (VRF) and WAN-side multi-VPN interconnection are supported.
In scenarios requiring high security, such as the finance industry, both firewalls and ARs can be deployed at sites.
Solution constraints
ARs deployed at the HQ and branches must support SD-WAN.

## Slide 56: SD-WAN Solution Overview (2)
Network model design
Select a network model based on the site scale and data access model.
Single-layer model
  WAN sites of an enterprise can be directly connected or connected through one or more hub sites. Typically, this model is used by small- and medium-sized enterprises as well as large enterprises with fewer than 100 sites.
  This model can be further classified into hub-spoke, full-mesh, and partial-mesh.
  Hierarchical model
  This model is applicable to large enterprises that span multiple areas. In this model, the entire overlay network is divided into multiple areas. Traffic between sites in different areas is forwarded through a border site. The hub-spoke, full-mesh, or partial-mesh topology can be used in an area.
Physical network design
A single AR and a single egress link can be deployed at a small branch site.
Multi-link and dual-AR networking can be deployed at sites that require highly reliable egress links and gateways.
In network reliability-sensitive scenarios, it is recommended that the RR be deployed independently. In network reliability-insensitive scenarios, the RR can be co-deployed with the AR at the HQ.
Notes: The single-layer network model is also called the flat network model. In this model, WAN sites of an enterprise can be directly connected or connected through one or more hub sites. Typically, this model is used by small- and medium-sized enterprises as well as large enterprises with fewer than 100 sites. The single-layer network model can be further classified into hub-spoke, full-mesh, and partial-mesh.
The hierarchical network model is applicable to large enterprises that span multiple areas. In this model, the entire overlay network is divided into multiple areas. Traffic between sites in different areas is forwarded through a border site. The hub-spoke, full-mesh, or partial-mesh topology can be used in an area.

## Slide 57: SD-WAN Solution: Service Design
VPN planning: A network can be divided into multiple VPNs based on services or departments. Policies can be independently configured for services of each VPN, and VPNs can be isolated from each other.
Intelligent traffic steering: Traffic policies can be defined (based on network segments or applications) to design intelligent traffic steering, so that high-reliability links (such as MPLS links) are preferentially selected for high-priority applications (such as audio and video services) and low-priority links are selected to transmit common data.
QoS application: Multi-level QoS scheduling, such as three-level QoS scheduling for ports, VPNs, and applications
Security: ACL-based traffic filtering, URL filtering, firewall, and IPS are configured to ensure traffic security.
Site-to-Internet access: The local Internet access, centralized Internet access, and hybrid Internet access modes are supported. If the Internet egress link is available, local Internet access can be configured. If centralized traffic policing is required, centralized Internet access will suffice.
Interworking with traditional networks: The solution supports interworking with traditional networks.

## Slide 58: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Overall design
Networking design
Service design

## Slide 59: VLAN Planning
Classify VLANs into service VLANs, management VLANs, and interconnection VLANs.
Allocate consecutive VLAN IDs to ensure proper use of VLAN resources.
Reserve a specific number of VLANs for future use.
Typically, VLANs are divided based on interfaces. According to different design principles, interfaces of access switches are added to different VLANs so that users of different service types can be isolated.
VLAN Assignment | Example
VLAN assignment by logical area | Core network area: VLANs 100–199 Server area: VLANs 200–999 (VLANs 1000–1999 are reserved.) Access network area: VLANs 2000–3499 Service network area: VLANs 3500–3999
VLAN assignment by geographic area | Area A: VLANs 2000–2199 Area B: VLANs 2200–2399
VLAN assignment by personnel structure | Department A in area A: VLANs 2000–2009 Department B in area A: VLANs 2010–2019
VLAN assignment by service type | Web server area: VLANs 200–299 Application server area: VLANs 300–399 Database server area: VLANs 400–499

## Slide 60: IP Address Planning (1)
Management IP address
Interconnection IP address
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
Service IP address
Shop assistant
192.168.1.0/24
Partner
192.168.5.0/24
Guest
192.168.100.0/24
192.168.1.254
192.168.5.254
192.168.100.254
A Layer 2 device uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches connected to a gateway be on the same network segment.
It is recommended that the interconnection IP address use a 30-bit mask. The core device uses a smaller host IP address.
The service IP address is the IP address of a server, host, or gateway.
It is recommended that the gateway addresses use the same rightmost three digits, such as .254.
The IP address range of each service must be clearly distinguished. The IP addresses of each type of service terminals must be contiguous and can be aggregated.
You are advised to use an IP address segment with a 24-bit mask.

## Slide 61: IP Address Planning (2)
Egress gateway
Internet
Carrier CPE
IP addresses of WAN interfaces on egress gateways are assigned by the carrier in static, DHCP, or PPPoE mode. The IP addresses of these interfaces need to be obtained from the carrier in advance.
IP addresses of WAN interfaces: assigned in static, DHCP, or PPPoE mode
Egress gateway
Devices such as servers and printers
End user
Internet
AP
Egress gateway
It is recommended that servers and special terminals (such as punch-card machines, printing servers, and IP video surveillance devices) use static IP addresses.
It is recommended that end users be assigned IP addresses in DHCP mode and the gateway provide the DHCP service.

## Slide 62: IP Address Planning (3)
LAN-side devices
Internet
Layer 3 switch
Egress gateway
AP
Egress gateway
Layer 3 interconnection
Internet
When the egress gateway interconnects with a Layer 3 switch, it is recommended that the interconnection IP addresses be manually configured in static mode.
It is recommended that the DHCP server be deployed on the gateway to dynamically allocate IP addresses to APs.

## Slide 63: Routing Design
Static routes are recommended for small- and medium-sized campus networks.
Internal routing design of the campus network:
  APs: After an AP obtains an IP address through DHCP, a default route is generated by default.
  Switches and gateways: Static routes can be used to meet requirements. No complex routing protocol needs to be deployed.
Routing design for the campus egress:
  You are advised to configure static routes on the egress device.
Internet
Layer 2 switch
Egress gateway
AP
AP

## Slide 64: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Overall design
Networking design
Service design

## Slide 65: Network Deployment and Automated Device Registration
Huawei registration center
On-site deployment personnel
MSP/Tenant administrator
  Automated network deployment
Huawei's Cloud-Managed Network Solution supports device plug-and-play. If the following prerequisites are met, a device can automatically connect to a given cloud management platform after being powered on and obtain complete service configurations from the platform, achieving device plug-and-play and fast service provisioning.
Prerequisites for implementing device plug-and-play
The administrator has registered the device ESN on the cloud management platform (by scanning the barcode or manually entering the ESN) and bound a valid license authorization package to the device.
The administrator has pre-configured the device or device group offline on the cloud management platform.
The device has obtained a valid IP address and DNS service through the DHCP server (another cloud managed device or deployed by the customer), and the IP address can be used to communicate with the Internet.
Internet
Notes: Traditional network deployment requires the participation of engineering installation personnel and network commissioning personnel. This results in long installation and commissioning periods and slow service provisioning, and consumes a large amount of manpower. The CloudCampus Cloud-Managed Network Solution supports automated network deployment.

## Slide 66: Device Registration
Device | Registration Mode |  |  |  |  | 
 | Registration Center | DHCP Option | USB Flash Drive | Mobile App | Web/CLI | Email
AP | √ | √ |  | √ | √ | 
Firewall | √ |  | √ |  | √ | 
Switch | √ | √ |  |  | √ | 
AR | √ | √ | √ |  | √ | √
  Enterprise network scenarios are complex, and different device registration modes are required in different scenarios. Huawei devices support multiple registration modes to meet complex networking requirements. The registration model also varies with device model. The following table lists the registration modes of different devices:
  On the same network, devices at different locations may use different registration modes. Typically, devices to be registered on a network are classified into:
  Egress gateway
  Intranet (LAN-side) device

## Slide 67: Egress Gateway Registration
  Egress line configuration of the egress gateway usually depends on the carrier network. Therefore, the registration mode is complex.
  In the CloudCampus Solution, ARs, firewalls, and APs can function as egress gateways.
  The registration modes of egress gateways vary with scenarios. For details, see the following table.
  If a DHCP server exists on the live network, the egress gateway can be registered using the DHCP option only when the DHCP server supports DHCP Option 148.
  In LAN-WAN convergence scenarios, ARs support email-based and DHCP option-based registration modes. However, in the DHCP option-based registration mode, the DHCP server must support DHCP Option 148.
Networking Scenario |  | Recommended Egress Gateway Registration Mode |  | 
 |  | AR | Firewall | AP
Huawei public cloud scenario | The egress gateway cannot automatically obtain an IP address. | Web system | Web system | CloudCampus APP
 | The egress gateway can automatically obtain an IP address. | Registration center |  | 
MSP-owned cloud scenario | The egress gateway cannot automatically obtain an IP address. | Web system | Web system | CloudCampus APP
 | The egress gateway can automatically obtain an IP address. | DHCP option | Web system | DHCP option
LAN-WAN convergence scenario (where the SD-WAN function needs to be configured on the egress gateway) |  | Email | --- | ---

## Slide 68: Intranet (LAN-Side) Device Registration
  A LAN-side network refers to the network under the egress gateway, which is mainly built on LAN switches and APs.
  In Huawei public cloud scenarios, the Huawei registration center-based registration mode is recommended.
  If an enterprise does not want to synchronize device information to the registration center, the DHCP option-based registration mode can be used.
Networking Scenario |  | LAN-Side Device Registration Mode | 
 |  | LAN Switch | AP
Huawei public cloud scenario | DHCP options cannot be configured on the network. | Registration center | 
 | DHCP options can be configured on the network. | Registration center or DHCP option | 
MSP-owned cloud scenario | DHCP options cannot be configured on the network. | Web system | CloudCampus APP
 | DHCP options can be configured on the network. | Registration center or DHCP option | 

## Slide 69: Scenario-Specific Automated Deployment
  Solution overview
  The scenario-specific automated deployment function is provided to further simplify network deployment.
  Network configurations, such as SSIDs, can be automatically generated based on the industry scenario selected by a customer. This means that users do not need to plan or configure the network in advance, eliminating the need for complex configuration design and planning. In addition, users can customize a scenario template to plan the site network so that the site network configuration can be quickly generated for deployment.
  Currently, templates for small- and medium-sized office scenarios are preset in the solution. Templates for other scenarios will be added in the future.
  Key design points:
  Select a service scenario, that is, select a scenario template.
  Select related devices and network topologies.
  Confirm the related configuration or adjust the preset configuration.
Notes: A scenario template includes the following contents and functions related to network deployment:
  Various networking modes: typical networking models of small- and medium-sized campus networks
  Automated DHCP server configuration
  Dual uplinks (active/standby mode by default) on the firewall egress for higher reliability
  Automated Eth-Trunk configuration
  Automated configuration of network services, including SSID, PSK password, QoS, access authentication, traffic monitoring, and application monitoring

## Slide 70: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
WLAN Planning
Networking Planning
SSID Planning
Roaming
Radio Calibration
Overall design
Networking design
Service design

## Slide 71: WLAN Planning: Wireless Signal Coverage (1)
Coverage Area | Field Strength Requirements | Typical Scenario
Key coverage area | –40 to –65 dBm | Dormitory room, library, hotel room, lobby, conference room, office, and exhibition hall
Common coverage area | > –75 dBm | Corridor, kitchen, storeroom, and dressing room
Special coverage area | N/A | Areas that have limitations on or do not allow coverage or installation due to considerations such as service security or property management
Field strength reference
Scenario | Coverage Recommendation
Indoor scenario | Plan the coverage radius of 15–20 m for each AP.
Outdoor scenario | Plan the coverage radius of 50–80 m for each AP.
Indoor high-density scenario | Use small-angle directional antennas. During network planning, select AP positions and spacing based on the antenna angle.
Physical coverage reference
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
  To guarantee a good access and roaming experience, you need to plan proper signal coverage depending on different application scenarios; select proper AP models based on signal coverage demands and AP capabilities; and design a proper WLAN using the WLAN Planner.

## Slide 72: WLAN Planning: Wireless Signal Coverage (2)
  Observe the following rules when deploying APs:
  When installing an AP, try to reduce the number of obstacles that signals pass through.
  Ensure that the front side of an AP faces the target coverage area for good coverage.
  Place APs away from interference sources, such as electronic devices. Do not deploy microwave ovens, wireless cameras, wireless phones, or other electronic devices in the coverage area.
  For areas with roaming requirements, keep a 10% to 15% signal overlap between the coverage areas of neighboring APs to ensure smooth STA roaming between APs.
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration

## Slide 73: WLAN Planning: AP Deployment Planning
Log in to Huawei cloud-based WLAN Planner.
https://serviceturbo-cloud-cn.huawei.com/serviceturbocloud/dist/#/toolappmarket
2
4
1
3
Obtain the floor plan.
With Huawei cloud-based WLAN Planner, users can complete WLAN planning in just five steps.
Use the network planning report to provide guidance for onsite construction.
The network planning result can be imported into iMaster NCE.
1. Environment setting
2. Region setting
3. Device deployment
4. Signal simulation
5. Report export
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: After WLAN signal coverage requirements are determined based on scenarios, AP deployment can be planned using the WLAN Planner.
  This tool can be used to create network planning projects based on drawings or Amap.
  This tool supports region settings, obstacle generation, automated or manual AP deployment with one click, and WLAN signal coverage simulation.
  This tool can generate network planning files and allows users to export the files. Users can import network planning results on the tenant management page of iMaster NCE to display AP locations and help tenants install APs.
  CampusInsight allows users to import network planning files. After network deployment, users can view the actual signal heatmap of the network.

## Slide 74: Network Planning
Internet
Layer 2 switch
Egress gateway
AP
AP
Number of APs: Determine the number of APs based on the WLAN planning result.
Access switch selection: PoE switches are recommended. Select switches based on the number of APs and PoE power supply requirements of APs.
Number of access switches: Determine the number of access switches based on the number of APs, access relationships, and the number of ports on the selected switches.
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration

## Slide 75: SSID Planning
SSID service planning
Authentication and encryption modes for an SSID
An SSID represents a type of services. Plan the number of SSIDs based on project requirements. Different authentication modes can be deployed for different SSIDs.
SSIDs can also be used to distinguish different groups of users or different services/permissions. For example, employees and guests are configured with different SSIDs.
Different authentication and encryption modes can be deployed for office users and guests who have different security requirements.
802.1X and MAC address authentication can be configured for enterprise offices that have high security requirements. For an SSID that is not intended for end users, for example, the SSID planned for printers and scanners, you can hide this SSID to prevent it from being detected by end users.
Open, PSK, Portal, or social media authentication can be configured for guests or open access users.
SSID parameter settings
Effective scope of SSIDs: Select the effective radio (2.4/5 GHz by default) and effective APs (all APs at the site by default).
Plan the service VLAN corresponding to the SSID, and configure the corresponding gateway and IP address.
Advanced service parameters: band steering, user isolation, and SSID hiding
Advanced application functions: rate limiting, ACL application, application filtering, and URL filtering
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: SSIDs are used to represent WLANs. They are WLAN names displayed on a STA such as a mobile phone when you search for WLANs available for access on the STA. You can select an SSID to access the corresponding WLAN.
Generally, SSIDs are planned based on user roles or services. Different authentication modes, network access rights, and control policies can be deployed for different SSIDs.
Portal authentication can be used on open networks (for example, networks for external user access). PSK or PPSK authentication can be used on semi-open networks (such as guest room networks of hotels). 802.1X authentication can be used on secure networks (such as office networks). MAC address authentication can be used for dumb terminals such as printers.
For an SSID that is not intended for end users, for example, the SSID planned for printers and scanners, you can hide this SSID to prevent it from being detected by end users.

## Slide 76: Roaming: Layer 2 Roaming Design
Definition of Layer 2 roaming
When a STA moves between APs, the STA smoothly switches from the original AP to a new AP. This process is called roaming. The SSID, service VLAN, and gateway of the STA remain unchanged before and after roaming.
Roaming neighbor: An AP detects neighboring APs at the same site through the air interface. If SSIDs of the detected APs are the same as that of the local AP, these APs then are considered roaming neighbors of the local AP.
Implementation of Layer 2 roaming
In Layer 2 roaming, traffic of STAs does not detour and is directly forwarded by the foreign AP (FAP).
Design points of Layer 2 roaming
The service VLANs for the SSIDs of APs must be the same, and the uplink switch must allow traffic from the service VLANs to pass through.
Roaming neighbors are discovered through the air interface, which has high requirements on AP deployment. APs in the continuous roaming area must be able to detect each other.
Guest SSID
VLAN 100
192.168.1.25
192.168.1.25
AP1
AP2
Guest SSID
VLAN 100
Network
Signal coverage of AP1
Signal coverage of AP2
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: Definition of Layer 2 roaming: When a STA moves between APs, the STA smoothly switches from the original AP to a new AP. This process is called roaming. The SSID, service VLAN, and gateway of the STA remain unchanged before and after roaming.
Implementation of Layer 2 roaming:
  Roaming neighbor: An AP detects neighboring APs at the same site through the air interface. If SSIDs of the APs are the same as that of the local AP, and they can detect each other, these APs are considered roaming neighbors of the local AP. (An AP can establish a maximum of 64 roaming neighbors.).
  Each AP establishes a wired CAPWAP tunnel (control plane tunnel) with a roaming neighbor to transmit roaming information.
  The establishment of roaming neighbors is irrelevant to the calibration group. The calibration group is divided based on the management VLAN. Layer 2 roaming neighbors are established based on whether service VLANs are the same.

## Slide 77
Notes:   When a STA goes online through an AP, the AP synchronizes information such as the STA's MAC address to all roaming neighbors of the AP. If the STA roams to a new AP (FAP), the AP checks whether the STA roams from another AP, and synchronizes the STA entry from the home AP (HAP). The entry includes the VLAN, IP address, authentication result, and authorization group of the STA. The FAP then generates the STA entry. In this case, identity authentication does not need to be performed for the STA again. After roaming completes, the FAP notifies its neighboring APs to prepare for the STA's subsequent roaming. In addition, after roaming is complete, the HAP deletes the STA entry.
  In Layer 2 roaming, traffic of STAs does not detour and is directly forwarded by the FAP.
Design points of Layer 2 roaming:
  The service VLANs for the SSIDs of APs must be the same, and the uplink switch must allow traffic from the service VLANs to pass through.
  Roaming neighbors are discovered through the air interface, which has high requirements on AP deployment. APs in the continuous roaming area must be able to detect each other.

## Slide 78: Roaming: Layer 3 Roaming Design (1)
Definition of Layer 3 roaming
Layer 3 roaming: The service VLANs for the SSIDs before and after STA roaming are different and correspond to different gateways. In this case, to keep the IP address of the roaming STA unchanged, the STA traffic needs to be detoured to an AP that resides on the same network segment as the AP through which the STA goes online for the first time.
AP through which the STA goes online for the first time: AP that the STA first associates with in a mobility group
Home AP (HAP): is selected using the hash algorithm from the neighbors that belong to the same Layer 2 roaming domain as the AP through which the STA goes online for the first time. Once selected, the HAP forwards Layer 3 roaming traffic of the STA.
Network
192.168.1.25
192.168.1.25
Guest SSID
VLAN 100
Guest SSID
VLAN 200
HAP
VLAN 100
VLAN 200
Roaming neighbors of the AP through which the STA goes online for the first time
AP through which the STA goes online for the first time
FAP
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration

## Slide 79: Roaming: Layer 3 Roaming Design (2)
Implementation of Layer 3 roaming
When a STA goes online, the network uses the hash algorithm to select an AP from the candidate HAPs as the HAP for the STA. When the STA roams at Layer 3, Layer 3 roaming traffic is forwarded to the HAP. This solution avoids traffic from being sent to the same AP after Layer 3 roaming, preventing performance bottlenecks.
As shown in the figure, the STA roams from the HAP to the foreign AP (FAP). The FAP obtains STA information and corresponding HAP information from the AP through which the STA goes online for the first time. In addition, the FAP establishes a CAPWAP data tunnel with the HAP. When the STA sends data packets, the packets are forwarded to the HAP through the CAPWAP data tunnel. If the STA roams back to the Layer 2 domain where it goes online for the first time, the STA traffic does not need to be forwarded to the HAP. Instead, the traffic is directly forwarded by the new AP (FAP).
Network
192.168.1.25
192.168.1.25
Guest SSID
VLAN 100
Guest SSID
VLAN 200
HAP
VLAN 100
VLAN 200
Roaming neighbors of the AP through which the STA goes online for the first time
AP through which the STA goes online for the first time
FAP
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: Design points of Layer 3 roaming
  Layer 3 roaming traffic will be detoured to the HAP. Therefore, a large Layer 2 domain needs to be planned at the entrance of the entrance hall so that the detoured traffic can be distributed to different APs during roaming.
  Each AP supports up to 64 Layer 3 roaming STAs. When there are a large number of Layer 3 roaming STAs, the roaming fails and the STAs need to go offline and go online again. (In actual deployment scenarios, you are advised to deploy Layer 2 roaming on the same floor or in the same area based on the service VLAN planning.)

## Slide 80: Radio Calibration: AP Grouping Design
The number of APs that the leader AP can manage is limited.
If the number of APs exceeds the management capability of a leader AP, network planning is required. Management VLANs need to be planned for AP grouping. When there are a large number of APs in a management VLAN, the APs are automatically divided into multiple groups.
Radio calibration is performed on WLANs in a continuous area. Therefore, it is recommended that APs be grouped by geographic location such as by floor to ensure that APs in a group are in the same area. This maximizes the calibration effect.
Random grouping
F1
F2
F3
Grouping based on management VLANs
F1
F2
F3
VLAN 1000
VLAN 1001
VLAN 1002
If manual intervention is not performed when the number of APs exceeds the upper limit, APs are randomly grouped, affecting the calibration effect.
In a continuous area (such as adjacent APs or APs on the same floor), management VLANs are planned for AP grouping. A leader AP is elected in each group.
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: A cloud AP is essentially a Fat AP and is independent of each other. Some WLAN services, such as radio calibration, need to be processed centrally. However, no WAC is deployed. To ensure high network reliability and performance and meet local computing requirements, a global control role similar to a WAC is required.
A leader AP is an AP with strong capabilities in an AP group. It is responsible for global calibration of the entire group (automatically elected in a Layer 2 domain).
The calibration region is automatically divided based on the management VLAN. On a small network, a leader AP can manage all APs (no more than 128 high-performance APs and no more than 50 low-performance APs). In this case, only one management VLAN needs to be planned for APs.
When the number of APs exceeds the management specifications of the leader AP, you can divide multiple management VLANs to manage the network. You are advised to plan management VLANs based on floors or physical continuous coverage areas to ensure the continuity of the calibration regions.
Port isolation cannot be configured on the uplink access switch of the cloud AP. (The calibration group is negotiated through wired-side broadcasting.)

## Slide 81: Radio Calibration: Calibration Mode Selection
Campus
1
2
4
5
3
All APs perform detection.
The leader AP performs computing and calibration.
The APs report detection data.
iMaster NCE delivers the calibration command.
iMaster NCE supports three radio calibration modes:
  Automatic mode: APs periodically perform global calibration based on the calibration time and interval.
  Manual mode: APs do not proactively perform radio calibration, and you need to manually perform global or local calibration for APs at the site on iMaster NCE.
  Scheduled mode: APs perform global calibration at a scheduled time every day.
APs perform calibration detection according to the configured mode and switch to other channels to scan neighboring APs. The scanning lasts for 15 minutes.
During the detection, the APs report the detected data to the leader AP every 10s.
The leader AP performs computing and calibration every 5 minutes and performs computing for three times to achieve algorithm convergence.
The leader AP delivers the calibration result to each AP in the group, including the calculated channel and power.
The leader AP delivers the calibration result.
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration
Notes: During scheduled radio calibration, you can enable intelligent radio calibration and use the analyzer to analyze historical data of the WLAN and predict interference sources on the network. During network optimization, APs can avoid possible interference sources on the network in advance to improve the quality of the entire WLAN.
During deployment, you are advised to perform manual calibration to automatically plan the channels and power of APs after APs are deployed and go online.

## Slide 82: Radio Calibration: Channel and Frequency Bandwidth Selection
AP channel selection
2.4 GHz frequency band: Channel sets 1, 6, and 11 are recommended. If APs are densely deployed, channel sets 1, 5, 9, and 13 are recommended.
5 GHz frequency band: When an AP uses a single 5 GHz radio, it is recommended that high and low frequency channels of neighboring APs be staggered. When an AP uses dual 5 GHz radios, it is recommended that two 5 GHz radios be planned at low and high frequencies respectively.
Frequency bandwidth selection
2.4 GHz frequency band: Only the 20 MHz frequency bandwidth can be selected.
5 GHz frequency band: The 40 MHz frequency bandwidth is recommended. The 80 or 160 MHz frequency bandwidth can be used in bandwidth-hungry scenarios.
WLAN Planning
Network Planning
SSID Planning
Roaming
Radio Calibration

## Slide 83: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Overall design
Networking design
Service design

## Slide 84: Access Control Scenarios (1)
Authentication type: HACA Portal, 802.1X, and MAC address authentication
Scenario description: iMaster NCE functions as an authentication server.
iMaster NCE functions as an authentication server
Authentication point
Third-party (HTTP/HTTPS) Portal server
Authentication type: HACA Portal relay solution
Scenario description: A Portal server has been deployed, and interconnects with iMaster NCE through APIs. iMaster NCE functions as a relay agent.
API
Relay agent
iMaster NCE interconnects with a third-party Portal server
Internet
Authentication point
Internet
Notes: Deployment mode recommendation:
  It is recommended that iMaster NCE functions as an authentication server to implement authentication and policy control.
  If an enterprise has its own authentication server, the authentication server can interconnect with a third-party server in proxy mode. In addition, iMaster NCE can also implement user management and some policy management functions.
  If an enterprise uses a third-party authentication server to provide the access authentication function, the device that functions as an authentication point can directly interconnect with the third-party authentication server.

## Slide 85: Access Control Scenarios (2)
Third-party authentication server (Portal + RADIUS)
Authentication type: Portal, HTTPS Portal, 802.1X, and MAC address authentication
Scenario description: The network device that functions as an authentication point directly interconnects with a third-party server. (Note: HTTPS Portal is configured using CLIs.)
Third-party RADIUS server
Authentication type: HACA Portal-to-RADIUS solution
Scenario description: A RADIUS server has been deployed, and interconnects with iMaster NCE through RADIUS. iMaster NCE functions as a RADIUS relay agent.
RADIUS
iMaster NCE interconnects with a third-party RADIUS server
The authentication point directly interconnects with a third-party authentication server
Internet
Relay agent
Internet
Authentication point
Authentication point

## Slide 86: Authentication Solution Deployment
Terminal Role | Guest | Enterprise employee | Dumb terminal
Access Mode | Wireless | Wireless/Wired | Wired
Authentication Type | Portal authentication | Portal authentication (recommended for wireless users) 802.1X authentication (optional for both wireless and wired users) | MAC address authentication
Authentication Point | Access devices are recommended as authentication points. This has the following advantages: Multiple access devices perform user authentication separately, reducing the authentication load. Authentication points are closer to terminals, improving authentication security. The configuration planning is simple. If authentication points are deployed at the upper layer, the following factors must be considered: performance specifications of the devices acting as authentication points, Layer 2 isolation at the access layer, and configuration for transparent transmission of 802.1X protocol packets at the access layer. |  | 
Networking Scenario | Single-device networking: The authentication point is the local device, and Portal authentication is recommended. (In the cloud management scenario, ARs and firewalls do not support 802.1X or MAC address authentication.) Other networking scenarios: APs are used as authentication points for wireless users. Access switches are used as authentication points for wired users. |  | 
Authentication point for wireless users
Authentication point for wired users
Internet

## Slide 87: Overall Design Process
Network management mode
Network O&M mode
License scheme
Network architecture
Networking scheme
Reliability
WAN interconnection
Network basic services
Network deployment
WLAN
NAC
VAS and O&M
Overall design
Networking design
Service design

## Slide 88: Panorama of Open Cloud Management Capabilities
Platform layer
Application layer
Network layer
Terminal layer
Provided by partners
MSP
Log analysis
Business
Marketing reach
Education
e-Schoolbag
Manufacturing
AGV navigation
Healthcare
Baby wristband
OA
Asset management
Infrastructure API
Basic service API
VAS API
Policy service API
HTTPS + RADIUS
Third-party authentication API
LBS API
App data API
AP RSSI API
IoT API
NETCONF/Telemetry/Syslog/SNMP/NetStream
Firewall
AR
Switch
AP
Supports multiple open interfaces such as NETCONF and Telemetry, improving device manageability.
Third-party IoT cards can be installed on APs to provide IoT functions.
Provides four types of APIs.
Supports the industry's standard network interconnection protocols.
Focus on mainstream application scenarios.
All network service data is open, meeting data monetization and operational requirements.
Supports access of IoT terminals (such as ZigBee, RFID, and BLE).
Supports access of wired and wireless terminals.
Bluetooth
RFID
ZigBee
IoT card
ESL
Asset tag
Smart wrist strap
Baby wristband
Notes: Open capabilities at all layers, for all services, and in all scenarios help MSPs, VAS application partners, and customers quickly implement system interconnection, service convergence, and data monetization.

## Slide 89: Network Management Design: Management Level
  Key points of network management design:
  Management level design is performed to determine whether multiple or multi-level organizations are needed to manage different sites. Huawei's Cloud-Managed Network Solution supports the design of multiple or multi-level organizations for a tenant, which meets the requirements of managing large branches. Each organization can manage multiple sites or sub-organizations.
  (Optional) Organization planning and design: A large organization with multiple branches needs to be managed by area. That is, the organization is divided into multiple areas to manage the branches on demand.
  Site planning: A network with independent network management services is managed as a site. It can be an independent campus/branch network, or a relatively independent network on a campus/branch network, for example, a network of a building or even a floor. Sites can be flexibly planned based on actual management requirements.
  Rights- and domain-based management of network administrators' rights is adopted.
MSP 1
Site
Organization 1
Organization n
Site
Site
Site
Platform carrier
Tenant 2
Tenant 1

## Slide 90: Network Management Design: Rights- and Domain-Based Management
Authorization Scope | Tenant Level | MSP Level
Rights-based: controls the functions that can be performed | The super administrator can grant different rights to tenant administrators. To facilitate rights assignment and management, the system presets three roles with different rights: Monitor, Open API Operator, and Tenant Administrator. Tenant administrators authorize MSP administrators based on the preceding three roles. | The super administrator can assign different rights to MSP administrators. Similarly, there are three types of roles: Monitor, Open API Operator, and MSP Administrator
Domain-based: controls the range of devices that an administrator can manage | The minimum granularity of domain-based management is site. That is, tenant administrators perform authorization by site. Different tenant administrators can manage devices at different sites. When a tenant administrator authorizes an MSP administrator to manage its network, domain-based management is not supported. Instead, the MSP administrator can manage all sites of the tenant. | Domain-based management cannot be configured for MSPs at different levels. Once a tenant authorizes an MSP administrator, the MSP administrator can manage all devices of the tenant whatever level the MSP administrator is at.

## Slide 91: O&M Function Panorama of CloudCampus
Intelligent troubleshooting
Visualized network management and monitoring
Device management
Alarm management
File/Configuration management
NE management
WLAN monitoring
Link management
Service quality monitoring
Network
management
Network health
Fault locating
Packet header obtaining
Packet path tracing
SLA management
Device diagnosis and testing
Protocol tracing
Performance analysis
Fault analysis
User roaming dimension
User application dimension
User throughput dimension
Device dimension
User access dimension
Log management
Issue analysis
Access analysis
Controller
Analyzer
User management
Customer flow analysis
Terminal management
Terminal
management
Protocol tracing
Performance analysis
Network optimization
Radio calibration
Access analysis
CloudCampus APP
Notes: Similar to the network management mode, the network O&M mode is classified into the following two types based on the O&M operators:
  Self-O&M: Enterprises perform network O&M by themselves.
  O&M by MSPs: MSPs are responsible for network O&M. After a tenant submits an application to an MSP, the MSP can directly maintain services of this tenant. In this case, the MSP uses an authorized tenant account to log in to iMaster NCE for network O&M.

## Slide 92
(Multiple-answer question) Which of the following device deployment solutions can be used on small- and medium-sized campus networks to ensure device reliability? ( )
  Deploy firewalls in hot standby mode.
  Deploy two ARs as egress gateways.
  Deploy switches in stacking mode.
  Deploy multi-chassis link aggregation.
(True or false) 802.1X authentication is recommended for Wi-Fi networks deployed in stores. ( )
  True
  False
Notes: ABC. Multi-chassis link aggregation is a link reliability mechanism.
B. Portal authentication is recommended.

## Slide 93
This course describes how to use Huawei's CloudCampus Cloud-Managed Network Solution to design small- and medium-sized campus networks. Key design points include the overall design (network management mode design, network O&M mode design, and license scheme design), networking design (network architecture design, networking solution design, WAN interconnection design, and reliability design), and service design (network basic service design, network deployment design, WLAN design, NAC design, security design, QoS design, VAS design, as well as network O&M design).

## Slide 94
Huawei's CloudCampus Solution V100R020C00 Product Documentation
  https://support.huawei.com/hedex/hdx.do?docid=EDOC1100172638&lang=en
Design Guide of Huawei CloudCampus Solution for Small and Medium Sized Campus Networks Scenario
  https://e.huawei.com/en/material/networking/campusnetwork/5133b49714a04ab08d5851d0e44e59a1