## Slide 1
Datacom
V1.0
Wu Yue/WX291773
2021.03
Li Xianzhi/00354681
New

## Slide 2: Enterprise WAN Interconnection Design

## Slide 3
After years of development and evolution, WAN interconnection has undergone significant changes. In the past, WAN interconnection was centered on the network, and there were few applications. As the main component of WAN interconnection, the network took the most important position. However, with the rise of cloud computing, the potential of applications is fully exploited, and WAN interconnection gradually become application-centric.
To address the challenges posed by cloud computing to WAN interconnection, Huawei launches the SD-WAN Solution.
This course will provide insights into the functions available in the SD-WAN Solution and the design scheme for this solution.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the challenges faced by enterprise WAN interconnection.
  Describe the architecture and functions of Huawei SD-WAN Solution.
  Describe the SD-WAN networking design scheme.
  Describe the SD-WAN service design scheme.
  Describe the SD-WAN reliability design scheme.
  Describe the SD-WAN security design scheme.

## Slide 5
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 6: Challenges Brought by Cloud Computing to Enterprise WAN Interconnection
Before cloud computing is widely used, there are only a small number of network applications. The network service quality depends only on the bandwidth, and service traffic does not need to be managed in a refined manner. The Internet is built on a network-centric design.
The advent of the cloud computing era leads to a significant increase in the number of network applications. Enterprises have difficulty in striking a balance between the line price and service quality in the face of soaring traffic.
HQ
Branch site
WAN
Branch site
Branch site
Growing services of the enterprise

## Slide 7: Challenges Brought by Multiple Services to Enterprise WAN Interconnection
Enterprises are unable to detect service quality in real time and therefore cannot effectively guarantee key services. In addition, enterprises cannot monitor service traffic in real time, and therefore are unable to quickly adjust service traffic.
Internet backup link: low bandwidth utilization
Unknown application
MPLS primary link: congested during peak hours
Unknown application
HQ
SaaS application traffic diverted through HQ, causing high delay
Cloud
Cloud
No application visibility, causing difficulty in traffic scheduling
Bandwidth conflict leads to frame freezing in video conferences
Smooth video conference when idle bandwidth is available
Priority conflict: Key applications cannot be identified and therefore have a low scheduling priority.
Bandwidth conflict: During peak hours, the burst traffic is three to five times the average traffic, affecting key applications.
600+
Cross-WAN application
(An enterprise)
Difficulty in managing key services such as voice, video, and SaaS applications

## Slide 8: Challenges Brought by Large Numbers of Branches to Enterprise WAN Interconnection
With the development of an enterprise, it will have more and more cross-city, cross-province, and cross-country branches, causing the following problems in managing branch site networks:
  Too many branches result in high O&M costs.
  It takes a long time to provision new services in branches.
  It is difficult to rectify faults on branch networks.
Approval process
(2~5 days)
Hardware installation
(1~3 days)
Hardware transportation
(2~5 days)
Software commissioning
(1~3 weeks)
On-site survey
(1~3 days)
Device selection
(1~3 days)
Network planning
(2~5 days)
Branch 1
…
Time-consuming service provisioning in branches
Branch 2
Branch 3
Difficult troubleshooting on branch networks, resulting in high O&M costs
Branch site
Branch site
Branch site
Branch site

## Slide 9: Emergence of SD-WAN
Software Defined Wide Area Network (SD-WAN) technology can better address the challenges faced by enterprise WAN interconnection in the cloud computing era.
SD-WAN is a combination of software-defined technology and WAN technology. It leverages SDN to reshape WANs by applying the SDN architecture and concepts to WANs.
Top 10 SD-WAN requirements defined by ONUG
SD-WAN characteristics defined by Gartner
SD-WAN characteristics defined by MEF
Uses Zero Touch Provisioning (ZTP) to implement fast deployment and provisioning of branches, improving deployment efficiency.
Dynamically adjusts traffic paths by application type, making traffic steering more flexible and convenient.
Provides automatic and intelligent O&M capabilities to implement centralized management and control and network-wide status visualization.
Provides value-added services (VASs) such as WAN optimization and security to implement fast service provisioning.
Characteristics of SD-WAN
Notes: ONUG: refers to Open Networking User Group. ONUG is an influential user organization led by large enterprises and comprised mainly of IT users. It was founded by IT technical executives of well-known large enterprises in North America and is dedicated to driving IT implementation and network technology transformation for large enterprises. ONUG members include large enterprises in industries such as finance, insurance, medical care, and retail. ONUG serves as a platform for high-end customers in North America to discuss and communicate IT requirements.
Gartner: It is the world's most authoritative IT research and advisory company. Its research scope covers all IT industries. It provides objective and fair demonstration reports and market research reports for customers in terms of IT research, development, evaluation, application, and market, thereby assisting customers in market analysis, technology selection, project demonstration, and investment decision-making.

## Slide 10
Notes: The Metro Ethernet Forum (MEF) is a non-profit organization dedicated to solving the technical problems of the Metro Ethernet. It aims to widely apply the Ethernet technology to the construction of the Metro Ethernet as switching and transmission technology. The objective of MEF is to promote the implementation of existing and new standards, Ethernet service definitions, test procedures, and technical specifications, developing Ethernet-based MANs into carrier-class networks. The major tasks of MEF also include providing LSO-based solutions (LSO is short for Lifecycle Service Orchestration) and architectures for carriers' managed service markets and defining northbound interfaces (NBIs) to enable multi-vendor interoperability.

## Slide 11
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
  Huawei SD-WAN Solution
  Major Functions of Huawei SD-WAN Solution
  Application Scenarios of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 12: Overview of Huawei SD-WAN Solution
Cloud applications
Self-service portal
...
Branch 2
Hybrid WAN
Branch 1
ERP, video...
Legacy
network
Edge
Edge
IWG
xDSL/Ethernet
/LTE...
Internet
LTE
MPLS
Public cloud
HQ/DC site
Subscription
Deployment
O&M
Adjustment
Optimization
Automation
Insights
Visualization
Benefits for Enterprises
Lower O&M cost
Higher WAN utilization
Minute-level service provisioning (location independent)
Improved O&M efficiency, cloud management & automation
Increased revenue
Develop new B2B business fields: VAS, connectivity, Managed LAN
Smooth evolution, openness, and quick integration
RESTful API, CPE/vCPE
Customer Benefits
Key Technologies
5G uplink: 5G supported by all CPE series products
Large bandwidth: 230 Mbit/s for uplink, 900 Mbit/s for downlink
Support for all network generations: 5G/4G/3G/2G networks
High performance: no congestion during forwarding
CPU+NP heterogeneous forwarding architecture
Optimal experience: application-based intelligent traffic steering, ensuring experience of key applications
Application-based intelligent traffic steering, enabling on-demand 5G+fiber scheduling.
Simplified O&M: full-process automation and plug-and-play
Visibility of application, branch, device, and link status, and centralized management
Edge
Edge

## Slide 13: Architecture of Huawei SD-WAN Solution
Management layer: iMaster NCE-WAN manages the entire process of enterprise interconnection services in a refined manner. It uses NETCONF to manage CPEs in the southbound direction and provides standard RESTful APIs in the northbound direction to connect to third-party applications.
Control layer: iMaster NCE-WAN works with the distributed control component to transmit routes between different sites in a region and implement inter-region network interconnection.
Network layer: The overlay technology is used together with cost-effective CPEs to connect branches, headquarters, and the cloud platform, thereby achieving on-demand full-network connectivity by fully leveraging all types of links such as the Internet and traditional private lines.
Network layer
Control layer
Management layer
NETCONF
BGP/DTLS
HTTP/2
Orchestration
Control
RESTful API
Third-party BSS/OSS
Management
Public cloud site
HQ/DC site
MPLS
legacy site
Branch site
Branch site
CPE
vCPE
IWG
CPE
CPE
MPLS
Internet
Notes: In terms of functions, the overall architecture of the SD-WAN Solution consists of the network layer, control layer, and management layer. The layers are associated with each other through standards-compliant interfaces and communication protocols.
iMaster NCE-WAN is the controller for Huawei SD-WAN Solution and consists of the management layer (built-in portal) and control layer.
Enterprise sites include enterprise branches, headquarters, data centers, and IT infrastructure deployed on the cloud.

## Slide 14: Key Components of the SD-WAN Solution
Public cloud site
HQ/DC site
MPLS
legacy site
Branch site
Branch site
CPE
Southbound NE layer
Northbound network service layer
VPN/Traffic steering/QoS/Security/WOC
O&M
CPE-VIM
RR
vCPE
GW
CPE
No. | Component | Functions
1 | iMaster NCE-WAN | Network service orchestration Network element (NE) control Basic network O&M CPE orchestration and management Basic performance monitoring (provides link quality information, application quality information, traffic information, and multi-dimensional statistics for single sites and between sites)
2 | RR | Distributes VPN routes and tunnel information between CPEs based on VPN topology policies.
3 | CPE | Egress CPE of a site, which can be a traditional CPE or an NFV vCPE.
4 | GW | Intermediate gateway device that connects the SD-WAN network and non-SD-WAN networks.
1
2
3
4
3
CPE
MPLS
Internet
3
Network layer
3
Management layer
Control layer
Notes: CPE: Customer Premises Equipment

## Slide 15: Architecture of Huawei iMaster NCE-WAN
Southbound
interfaces
Service functions
Basic functions
Northbound
interfaces
NETCONF
Traffic policy
Security policy
Plug-and-play
Visualized O&M
Multi-tenant management
Cluster management
Alarm management
Log management
Device configuration
Tunnel management
Network PMI
Device upgrade
Network devices
CPE
vCPE
VASs
OSS/BSS
Analysis system
Other applications
RESTful
SNMP Trap
HTTP/2
Syslog

## Slide 16: Network Layer Overview
An enterprise SD-WAN network can be divided into two layers: physical network (underlay) and virtual network (overlay), which are completely decoupled from each other.
  Physical network: refers to the underlay WAN provided by a carrier or built by the enterprise, including the private line network and the Internet.
  Virtual network: also called the overlay network. Huawei SD-WAN Solution uses the IP overlay virtualization technology to build one or more virtual overlay networks on top of the physical network. Service policies are deployed on virtual networks and are decoupled from the physical network, thereby separating services from the WAN.
Carrier network/
Self-built network
Branch site
Branch site
HQ
Legacy site
Overlay
Virtual network
Underlay
Physical network
CPE
CPE
GW
CPE/RR
Notes: Multiple virtual networks can be deployed to provide different services for the same tenant (for example, services for multiple departments) or provide different services for different tenants.
In terms of network device functions, the network layer of the SD-WAN Solution consists of two types of NEs: CPE and gateway (GW).

## Slide 17: CPE Overview
A CPE is essentially an edge node of the SD-WAN network and is also called an Edge-CPE. CPEs are interconnected using the IP overlay tunneling technology.
Traditional hardware CPEs are typically used on the HQ and branch sites, and vCPE software virtual devices can be deployed at sites on the public cloud.
All SD-WAN CPEs of an enterprise are centrally managed and maintained in iMaster NCE-WAN by the tenant administrator.
VPC/vNet
vCPE
CPE
Branch site
Branch site
HQ
Branch site
Overlay
Virtual network
CPE
CPE
CPE
CPE/RR
Central management
IP overlay tunnel
IP overlay tunnel
IP overlay tunnel

## Slide 18: RR Overview
A route reflector (RR) is used to transmit BGP routes.
In Huawei SD-WAN Solution, RRs also control routes and network topologies. Therefore, RRs are also called regional controllers in this solution.
Both RRs and CPEs at edge sites are managed by iMaster NCE-WAN.
Control channels are established between RRs as well as between RRs and edge sites.
RRs are managed by iMaster NCE-WAN and control route sending and receiving at edge sites based on the overlay network topology model. In this way, sites can communicate with each other based on the user-configured overlay topology model.
HQ/DC site
Branch site
Branch site
Management channel
BGP EVPN peer relationship
RR
Regional controller
CPE
HQ edge
CPE
Branch edge
CPE
Branch edge
MPLS
Internet
Filter overlay routes
Control overlay topology
Notes: RR site: The CPE at the site functions as an RR and distributes EVPN routes between CPE gateways at edge sites based on VPN topology policy.
If the tenant administrator assigns the role of "gateway + RR" to an egress CPE when adding the CPE, the site where the CPE resides is an RR site. If no device at a site is assigned the "gateway + RR" role, the site is an edge site.
An edge site can establish IBGP peer relationships with two RRs that back up each other.
Multiple RRs can be deployed for a tenant. All RRs are connected in full-mesh mode on the control plane.

## Slide 19: Gateway Overview
New SD-WAN sites of an enterprise need to communicate with its legacy sites or third-party services. Some legacy sites are interconnected through MPLS VPN, and SD-WAN sites are interconnected through IP overlay tunnels. Therefore, the legacy network and SD-WAN network cannot directly communicate with each other.
An SD-WAN gateway can connect to both the SD-WAN and legacy networks. It can function as an intermediate gateway to implement interconnection between SD-WAN and legacy networks.
Legacy MPLS domain
SD-WAN domain
PE
Gateway
PE
MPLS
SD-WAN
network
Enterprise 1
Enterprise 2
Enterprise 1
Enterprise 2
Enterprise 3
ASBR-PE
Notes: A gateway has different roles in different service scenarios. For example, a gateway connected to a legacy site may be referred to as an interworking gateway (IWG), and a gateway connected to the cloud may be called a cloud gateway. These gateways can extend functions by interconnecting with each other to establish a Point of Presence (PoP) network, where these gateways are referred to as PoP gateways.

## Slide 20: Huawei CPE Devices: NetEngine AR Routers
NetEngine AR6300
SRU-400H/SRU-600H
NetEngine AR6300/AR6200 series
Small enterprise
Ethernet + Wi-Fi + LTE
AR610 series
Branches in small or midsize enterprises
HQ/Large branch
NetEngine AR6280
SRU-400H/SRU-600H
NetEngine
AR6100 series
AR6140 series
AR6120 series
NetEngine
AR650 series
AR650 series
Ethernet + Wi-Fi + LTE (MIC)
SOHO
NetEngine
AR610 series
CPE
RR
Gateway
An AR router can be used as a CPE, RR, or gateway.

## Slide 21
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
  Huawei SD-WAN Solution
  Major Functions of Huawei SD-WAN Solution
  Application Scenarios of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 22: Major Functions of Huawei SD-WAN Solution
Huawei SD-WAN Solution provides the following functions:
  ZTP, enabling service provisioning to be completed within 1 hour
  Forwarding-control separation, enabling flexible networking
  Application optimization, enabling service controllability and visibility
  Complete security protection system, eliminating security risks
  Visualized O&M for quick fault locating
Carrier network/
Self-built network
Branch site
Branch site
HQ
Branch site
Overlay
Virtual network
Underlay
Physical network
CPE
CPE
CPE
CPE
ZTP
IP overlay tunnel 1 (congested)
Application optimization
IP overlay tunnel 2 (unblocked)
Security hardening
Control channel
Forwarding-control separation
Management channel
RR
Visualized O&M
Notes: ZTP: Multiple ZTP modes are available to enable CPEs to quickly register with iMaster NCE-WAN.
Forwarding-control separation enables flexible networking: Each CPE establishes a management channel with iMaster NCE-WAN through NETCONF, and iMaster NCE-WAN delivers configurations to CPEs to establish IP overlay tunnels between the CPEs.
Application optimization for service controllability and visibility: The service awareness (SA) technology is used to identify applications. TCP Flow Performance Measurement (FPM) and IP FPM technologies are used to implement application-based quality measurement. The IP FPM technology can also be used for link quality measurement. Smart Policy Routing (SPR) technology provides intelligent link switchover based on the application quality.
Complete security protection system ensures service security: Multiple VPN technologies, such as IPsec and MPLS, are leveraged to provide end-to-end protection. The firewall function is supported to provide comprehensive security protection at the hardware, pipe, and application levels.
Visualized O&M for quick fault locating: iMaster NCE-WAN collects network-wide data and displays key indicators, helping O&M personnel quickly locate faults.

## Slide 23: ZTP Overview
With the development of network technologies such as SDN and cloud computing, a growing number of enterprise networks are using cloud-based management mode, but most sites still need to be deployed by technical engineers onsite, leading to high deployment costs and long deployment periods. To address these problems, Huawei develops the Zero Touch Provisioning (ZTP) function.
ZTP process
Network administrator
Site deployment personnel
CPE
Internet/MPLS
PC for site deployment
Configure the ZTP file.
1
Transfer the ZTP configuration file through an email or a USB flash drive.
2
Log in to the PC.
3
Deploy ZTP configurations.
4
The CPE registers with iMaster NCE-WAN.
5
Notes: Huawei SD-WAN Solution supports the following ZTP modes:
  Email-based deployment
  DHCP-based deployment
  USB-based deployment

## Slide 24: Flexible Networking Overview
The primary function of SD-WAN is to provide flexible and reliable networking for enterprise WANs.
Huawei SD-WAN Solution leverages the IP overlay technology together with traditional network technologies — such as Layer 2 switching, Layer 3 routing, and VPN isolation — to achieve on-demand, flexible, and automatic connections between enterprise branches, DCs, and the cloud, with full management support provided by iMaster NCE-WAN.
Huawei SD-WAN Solution uses the following channels to implement flexible networking:
  Management channel
  Control channel
  Data channel
Management channel
NETCONF
Control channel
BGP EVPN
RR
CPE
CPE
Branch site
HQ/DC site
Data channel
GRE/GRE over IPsec
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE/GRE over IPsec (data channel)
1
2
3
Notes: Management channel:
  iMaster NCE-WAN sets up management channels with all devices through NETCONF, so as to manage NEs and orchestrate services on the entire network.
Control channel:
  CPEs set up control channels with the RR.
  The RR centrally controls and distributes service routes between branch sites.
  The enhanced BGP EVPN protocol is used to implement separate transmission of tenants' VPN route and next hop information, and IPsec SA negotiation.
Data channel:
  CPEs set up data channels with each other.
  CPEs forward data based on GRE or GRE over IPsec tunnels. The extended GRE header carries VN IDs to differentiate tenants or departments, thereby transmitting data of multiple VNs over the same tunnel.

## Slide 25: Application Optimization Overview
The traditional WAN has the following disadvantages that make it unable to meet network requirements:
  Applications of different values are carried on the same link.
  Dynamic path selection cannot be implemented when link quality deteriorates.
  No effective measure is available when link quality deteriorates.
To address these problems, Huawei SD-WAN Solution provides the application experience optimization solution that offers the following functions:
  Application identification
  Intelligent traffic steering
  QoS
  Packet loss mitigation
Application identification
Receive packets
CPE
Intelligent traffic steering
QoS
Packet loss mitigation
Forward packets
Typical application optimization process

## Slide 26: Security Overview
The advent of SD-WAN stimulates the transition of the enterprise WAN architecture from the traditional closed architecture to an open one. This increases the attack surface and brings new security challenges, such as unauthorized access, data leakage, and network attacks.
The security of Huawei SD-WAN Solution involves two aspects:
  System security: includes inter-component security and component security.
  Service security: includes firewall, IPS, and URL filtering.
RR
CPE
CPE
Branch site
HQ/DC site
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE/GRE over IPsec (data channel)
Management channel security
Control channel security
Security hardening for iMaster NCE-WAN
Data channel security
Service traffic security
1
1
1
1
2
Security hardening for CPEs
1

## Slide 27: Visualized O&M Overview
    Real-time alarm monitoring
    Customized dashboard (by role or preference)
    Network-wide real-time alarms (minute-level)
Quickly obtain abnormal traffic
Optimize WAN investment and configuration policies
    Visualized topology status
    Displays topology based on sites and links
    Provides real-time status and performance of sites and links
Quickly locate faulty devices or sites
    45+ customized views
    Site, link, application, device, and health status views
Bandwidth utilization for a site
Top N sites by throughput
Top N applications by traffic
Link throughput trend...

## Slide 28
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
  Huawei SD-WAN Solution
  Major Functions of Huawei SD-WAN Solution
  Application Scenarios of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 29: SD-WAN Business Model: Enterprise-Built
Legacy site
Enterprise HQ/DC
Enterprise branch
iMaster NCE-WAN
  SD-WAN: iMaster NCE-WAN is deployed on the WAN to centrally manage CPEs and implement ZTP, thereby shortening the service provisioning time. This helps enterprises cope with challenges brought by cloud services and change services on demand.
  Large enterprises with a vast number of branches, such as financial institutions, retail chains, and gas stations, can deploy iMaster NCE-WAN at the headquarters to set up SD-WAN networks and manage SD-WAN services on their own.
RR
CPE
CPE
SD-WAN gateway
Cloud
CPE
Products Involved | Functions
iMaster NCE-WAN | As the core of the SD-WAN Solution, it centrally manages CPEs, automatically delivers services, and uniformly controls the overlay network.
RR | It is the distributed control component that distributes VPN routes between CPEs based on VPN topology policies.
CPE | Egress CPEs of enterprise branches, headquarters, and DCs.
SD-WAN gateway | An intermediate gateway device that connects an SD-WAN network with a non-SD-WAN network.
Internet
MPLS
LTE

## Slide 30: SD-WAN Business Model: MSP Resale
Enterprise HQ/DC
Enterprise branch
iMaster NCE-WAN
  A managed service provider (MSP) provides a unified SD-WAN controller (iMaster NCE-WAN) to offer SD-WAN services for multiple enterprises. The MSP builds a PoP backbone network, to which an enterprise can connect through the nearest PoP provided by the MSP, thereby achieving high-quality enterprise interconnection. A PoP supports multiple tenants and provides PoP access for multiple enterprises at the same time.
  Enterprises, as tenants, lease SD-WAN services provided by MSPs. An enterprise tenant can manage the SD-WAN services of all sites belonging to it, but it cannot view the SD-WAN services of other tenants.
RR
CPE
CPE
MSP's multi-PoP backbone network
PoP
PoP
LTE
Internet
MPLS
LTE
Internet
MPLS

## Slide 31: SD-WAN Business Model: Carrier Resale
  A carrier provides SD-WAN services for multiple enterprises through iMaster NCE-WAN.
  Enterprises, as tenants, lease SD-WAN services provided by carriers. An enterprise tenant can manage the SD-WAN services of all sites belonging to it, but it cannot view the SD-WAN services of other tenants. Enterprises either manage and control their SD-WAN services based on the tenant permissions assigned by carriers, or they can entrust their SD-WAN services to carriers for management and control.
  SD-WAN gateways are used to implement flexible interconnection and fast compatibility between SD-WAN networks and carriers' legacy backbone networks.
Retail company HQ/DC
Carrier DC
Enterprise network
Carrier network
Carrier's management center
RR
RR
SD-WAN gateway
SD-WAN gateway
SD-WAN gateway
CPE
CPE
CPE
CPE
CPE
CPE
iMaster NCE-WAN
Carrier's backbone network
LTE
Internet
Internet
MPLS
Retail company HQ/DC

## Slide 32
SD-WAN solves the problems of difficult management, and expensive construction and maintenance costs in multi-branch interconnection scenarios. It also guarantees the quality of key services.
Huawei SD-WAN Solution provides the following functions:
  ZTP, enabling service provisioning to be completed within 1 hour
  Forwarding-control separation, enabling flexible networking
  Application optimization, enabling service controllability and visibility
  Complete security protection system, eliminating security risks
  Visualized O&M for quick fault locating
Huawei SD-WAN Solution is offered in three business models: enterprise-built, MSP resale, and carrier resale.

## Slide 33
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
  SD-WAN Networking Design Overview
  SD-WAN Site Design
  SD-WAN Tunnel Design
  SD-WAN VPN Design
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 34: Overview of Networking Design for Huawei SD-WAN Solution
SD-WAN networking design includes site design, tunnel design, and VPN design.
Branch site
Branch site
Active DC
Standby DC
Overlay
(virtual network)
Underlay
(physical network)
CPE
CPE
CPE/RR
CPE/RR
Tunnel design
Site design
GRE or GRE over IPsec (data channel)
VPN1
VPN2
VPN design
Carrier network/
enterprise-built network

## Slide 35: Networking Design Process for Huawei SD-WAN Solution
1. Site design
WAN-side network design
VPN design
2. Tunnel design
Topology design
LAN-side network design
VPN route design
RR networking design
NAT traversal design
Data tunnel design
Dual-CPE interconnection design
Specifications-exceeded network design
3. VPN design

## Slide 36
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
  SD-WAN Networking Design Overview
  SD-WAN Site Design
  SD-WAN Tunnel Design
  SD-WAN VPN Design
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 37: Site Design Panorama
SD-WAN sites refer to sites for which SD-WAN is deployed for interconnection, and are managed and monitored by iMaster NCE-WAN.
Site design generally covers:
  WAN-side network design
  LAN-side network design
  Dual-CPE interconnection design
MPLS
Internet
Hub
RR1
RR2
CPE
CPE
CPE
CPE/RR
CPE/RR
Branch site
WAN-side network design
Branch site
Dual-CPE interconnection design
LAN-side network design

## Slide 38: WAN-Side Networking Model
Enterprise intranet
Enterprise intranet
Enterprise intranet
Enterprise intranet
Enterprise intranet
Enterprise intranet
Enterprise intranet
Single-device networking
Dual-device networking
MPLS
/Internet
MPLS
Internet
MPLS
Internet
LTE/5G
MPLS
Internet
MPLS
Internet
MPLS
Internet
MPLS
Internet
LTE/5G
WAN-Side Network Design
Dual-CPE Interconnection Design
LAN-Side Network Design
Notes: An SD-WAN site can be deployed with a single CPE or dual CPEs. For small sites, a single CPE can be deployed. For sites with high reliability requirements, dual CPEs are recommended to provide device-level redundancy.
It is recommended that multiple links be deployed on the WAN side of a CPE. These links can back up each other, offering link-level reliability. In addition, services can easily select the active and standby links among these WAN-side links with differentiated quality.
A maximum of 10 WAN links can be deployed for each CPE at an SD-WAN site. During actual deployments, to enhance reliability and facilitate O&M, it is recommended that a maximum of three WAN links be deployed for a single CPE at a site, and a maximum of six WAN links be deployed for a site with two CPEs.

## Slide 39: Typical WAN-Side Networking
Single-CPE multi-link networking
For small and midsize sites or branch sites with low reliability requirements, only one CPE needs to be deployed. Multiple WAN links can be deployed and enterprise application traffic of different importance is transmitted over different links.
Typically, one MPLS link and one Internet link are deployed on the WAN side. The MPLS link has guaranteed SLA and is used to carry enterprises' critical applications. Non-critical applications are carried on the Internet link.
Enterprise intranet
MPLS
Internet
Dual-CPE multi-link networking
In large sites or branch sites with high reliability requirements, dual CPEs are generally deployed. To ensure service transmission reliability, at least two WAN links are deployed for each CPE.
Two CPEs are deployed at a branch site. The MPLS link is deployed for one CPE, and the Internet link is deployed for the other CPE. To ensure reliability, an interlink is deployed between the two CPEs to prevent data forwarding failures when a CPE fails.
Enterprise intranet
MPLS
Internet
Non-critical services
Critical services
Primary path for non-critical services
Primary path for critical services
Backup path for critical services
Backup path for non-critical services
WAN-Side Network Design
Dual-CPE Interconnection Design
LAN-Side Network Design

## Slide 40: WAN-Side Underlay Route Design
WAN interfaces of CPEs support OSPF, EBGP, and static routing protocols. The routing protocol to be used must be the same as that of the LAN-side network device.
On the live network, if static routes are used, services may be interrupted because WAN network faults on indirect links cannot be detected.
BGP used to access WANs
Enterprise intranet
MPLS
Internet
OSPF/BGP
Static route
CPE
WAN-Side Network Design
Dual-CPE Interconnection Design
LAN-Side Network Design

## Slide 41: LAN-Side Networking Model
LAN side connected to Layer 2 networks
LAN side connected to Layer 3 networks
Layer 2 switch
VRRP
VRRP
BGP
OSPF
Direct
Static route
BGP
OSPF
Direct
Static route
BGP
OSPF
Direct
Static route
Layer 2 switch
Layer 2 switch
BGP
OSPF
Direct
Static route
Layer 3 switch
Terminal
Dual-CPE Interconnection Design
LAN-Side Network Design
WAN-Side Network Design
Layer 3 switch
Layer 3 switch
Layer 3 switch
Notes: LAN side connected to Layer 2 networks:
  At small sites with a simple intranet structure, and CPEs typically connect to the intranet of the site at Layer 2.
LAN side connected to Layer 3 networks:
  In Layer 3 interconnection scenarios, SD-WAN routers support the direct connection, dual-homing, and partial-ring networking.
  In such scenarios, routing protocols simply need to be configured for CPEs based on the requirements of the LAN device.

## Slide 42: Typical Scenario for Connecting the LAN Side to Layer 2 Networks
In the single-CPE architecture, LAN-side interfaces can be directly connected to terminals at small sites.
If the number of required LAN-side interfaces is beyond the CPE specifications, access switches can be connected to the CPE.
In a dual-CPE architecture, VRRP is usually deployed.
Switches can be deployed on the LAN side to form a stack.
An interlink needs to be established between CPEs to forward service packets between CPEs.
CPE
Layer 2 switch
CPE
VRRP
CPE
AP
CPE
Layer 2 switch
Single CPE: LAN side connected to a Layer 2 network
Dual CPEs: LAN side connected to a Layer 2 network
Dual-CPE Interconnection Design
LAN-Side Network Design
WAN-Side Network Design
Notes: In the single-CPE structure, the LAN connection is simple.
  For small sites, for example, SOHO sites, LAN-side interfaces can be directly connected to terminals at the sites.
  If the number of required LAN-side interfaces is beyond the CPE specifications, access switches can be connected to the CPE. In this case, access switches can be connected to the CPE in one-armed mode.
In the dual-CPE architecture, VRRP is usually configured for the CPEs to prevent the dual-CPE architecture from affecting the LAN side.
  Multiple switches can be deployed on the LAN side to form a stack. If two CPEs are deployed at a site, they can be interconnected directly or through the LAN.
  CPEs can be directly connected through an Eth-Trunk link. In addition, an interlink needs to be established between the active and standby CPEs to forward service packets between the CPEs.

## Slide 43: Typical Scenario for Connecting the LAN Side to Layer 3 Networks
In the Layer 3 interconnection scenario, if only one CPE is deployed, the network structure is simple. In such a scenario, only the routing protocol needs to be configured on the LAN side based on requirements of LAN-side devices.
CPE
Layer 3 switch
CPE
Layer 3 switch
CPE
Static route
OSPF
BGP
Static route
OSPF
BGP
Single or dual CPEs: LAN side connected to a Layer 3 network
Dual-CPE Interconnection Design
LAN-Side Network Design
WAN-Side Network Design
Notes: For large enterprise sites, the network structure is complex as Layer 3 core devices are deployed on the network. Therefore, egress routers must support interconnection with Layer 3 devices. They can be connected to a Layer 3 network directly or in dual-homing mode. BGP, OSPF, and static routes are supported.
In the Layer 3 interconnection scenario, if only one CPE is deployed, the network structure is simple. In such a scenario, only the routing protocol needs to be configured on the LAN side based on requirements of LAN-side devices.

## Slide 44: Dual-CPE Interconnection Networking Model
In dual-CPE dual-link networking, if an uplink fails, the interlink between CPEs is used to transmit data.
In addition to exchanging routes between two CPEs at a site, the interlink is also used to synchronize key information between the two CPEs, including link information, tunnel connection information, SLA information about tunnel connections, IPsec SA, and application identification result.
With such information, resources on the two CPEs at each SD-WAN site can be regarded as a whole. Then services such as cross-device traffic steering can be implemented.
LAN
MPLS
Internet
Site A
CPE1
CPE2
Interlink
Dual-CPE Interconnection Design
LAN-Side Network Design
WAN-Side Network Design

## Slide 45: Dual-CPE Interconnection Networking Solution
If CPE interface resources are limited, the interlink can be established between Layer 2 service interfaces on the LAN side of CPEs.
Dual-CPE interconnection networking solution 1
A direct link is used as the interlink for interconnection. If service traffic of a site is heavy and CPE interfaces are sufficient, using two interlink interfaces is recommended. iMaster NCE-WAN automatically orchestrates the two interlink interfaces into an Eth-Trunk interface to increase the interlink bandwidth and ensure interlink reliability.
LAN
MPLS
Internet
Site A
CPE1
CPE2
Interlink
LAN
MPLS
Internet
Site A
CPE1
CPE2
Interlink
Dual-CPE interconnection networking solution 2
Dual-CPE Interconnection Design
LAN-Side Network Design
WAN-Side Network Design
Notes: Solution 1 is recommended. In this solution, the interlink and service links are independent of each other. When WAN-side links are adjusted, the interlink will not be affected, and the service flow direction is clear.

## Slide 46
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
  SD-WAN Networking Design Overview
  SD-WAN Site Design
  SD-WAN Tunnel Design
  SD-WAN VPN Design
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 47: Tunnel Design Overview
Tunnels in the SD-WAN Solution can be classified into: management tunnel, control tunnel, and data tunnel. Control tunnels are established between RRs and CPEs, and data tunnels are established between CPEs. Data tunnels carry services.
Tunnel design generally covers:
  Data tunnel design
  RR design
  NAT traversal design
  Specifications-exceeded network design
Branch
MPLS
Internet
Hub
Branch
RR1
RR2
CPE
CPE
CPE
CPE/RR
CPE/RR
RR design
NAT device
NAT traversal design
Specifications-exceeded network design
Data tunnel design

## Slide 48: Basic Concepts of Tunnels
Transport network (TN): a carrier-provided WAN network that implements branch interconnection of enterprises over WANs.
Routing domain (RD): If different TNs are reachable to each other (for example, the Internet provided by ISP B and ISP C in the left figure can communicate with each other), they are considered to be in the same RD.
Site ID: global unique identifier of a tenant site, which is allocated by iMaster NCE-WAN.
CPE router ID: global unique identifier of a CPE at a site. A site can contain one or two CPEs. Generally, the device loopback address is used as the CPE router ID.
  WAN link: a link connecting to a WAN interface. A WAN link has a one-to-one mapping with a WAN interface. The IP address obtaining mode, link negotiation rate, and bandwidth can be configured for a WAN link.
Transport network port (TNP): WAN interface through which a CPE connects to a TN. Key information includes the site ID, CPE router ID, transport network ID, public IP address, private IP address, and tunnel encapsulation.
HQ site
RD: Internet
RD: MPLS
Branch site 1
Site-ID: AAA
Site ID: BBB
CPE1
CPE2
Site ID: CCC
Branch site 2
3.3.3.3
(CPE router ID)
4.4.4.4
(CPE router ID)
5.5.5.5
(CPE router ID)
1.1.1.1
(CPE router ID)
2.2.2.2
(CPE router ID)
GE0
GE1
GE0
GE1
GE0
GE1
GE0
CPE3
CPE4
MPLS-ISP-A
(TN)
Internet-ISP-B (TN)
Internet-ISP-C (TN)
CPE5
WAN link
WAN link
TNP
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: The TN and RD are used to set up overlay tunnels in enumerated mode.
The site ID is used as the next hop of a routing entry.
The CPE router ID is used to establish BGP peer relationships between different sites.
TNPs are used to establish tunnels.

## Slide 49: TNP
A TNP mainly describes WAN link information of a site and is mainly used to establish control and data tunnels.
The main information about a TNP is as follows:
TNP Information | Example |  | Description
Site ID | 111 |  | Site of the TNP.
CPE router ID | 1.1.1.1 |  | CPE to which the TNP belongs.
TNP ID | 1 | 2 | TNP ID.
Transport network | TN1 | TN2 | TN to which the TNP belongs.
Routing Domain | RD1 | RD1 | RD to which the TNP belongs.
Public IP | 10.2.1.1 | 202.2.2.1 | WAN-side public IP address (post-NAT).
Private IP | 10.2.1.1 | 10.2.2.1 | WAN-side private IP address (pre-NAT).
Encapsulation | GRE | GRE | Encapsulation mode.
Site ID: 111
1.1.1.1
(CPE router ID)
GE0
10.2.1.1/30
CPE1
MPLS-ISPA
(TN1)
Internet-ISPB (TN2)
GE0
202.2.2.1/30
GE1
10.2.2.1/30
Carrier's NAT device
RD: RD1
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: TNs and RDs are mainly used to enumerate tunnels.
  Tunnel enumeration: All tunnels that can be established are enumerated.
Router IDs are mainly used to establish control channels.
A site ID is used as the next hop for data forwarding.
A TNP ID can be considered as the interface number.
The public and private IP addresses are used as the source or destination IP addresses of control and data channels.
  Some CPEs are deployed behind the NAT device. To establish data channels between CPEs, you need to know the post-NAT public IP address.
    CPEs typically use the Session Traversal Utilities for NAT (STUN) technology to detect public IP addresses.

## Slide 50: Tunnel Enumeration
CPEs enumerate tunnels based on the RD and TN in TNP information.
Tunnel enumeration ensures SD-WAN network reliability and guarantees service quality.
Tunnel enumeration rules:
  Connections can be enumerated only between TNPs in the same RD. Full-mesh connections are set up between interfaces of the same RD.
  Connections cannot be enumerated between TNPs in different RDs.
RD: Internet
CPE1
CPE2
CPE3
MPLS-ISPA
(TN)
Internet-ISPB (TN)
Internet-ISPC (TN)
Full-mesh connections are set up between interfaces of the same RD.
GE0
GE1
RD: MPLS
GE0
GE1
GE0
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: Data tunnels are enumerated before being established to ensure that all available data tunnels are established.
Tunnels can be enumerated only when the following conditions are met:
  The CPE has learned service routes of the peer site.
  The CPE has learned the TNP information of the peer site.

## Slide 51: SD-WAN Tunnel Establishment Process
The process of establishing SD-WAN tunnels is as follows:
Management channel establishment
The administrator configures WAN link parameters for CPEs or RRs on iMaster NCE-WAN.
The installation engineer delivers the configuration to CPEs or RRs through ZTP.
CPEs or RRs proactively register with iMaster NCE-WAN and establish a NETCONF channel (management channel) with iMaster NCE-WAN.
Control channel establishment
After iMaster NCE-WAN delivers configurations to CPEs and RRs through the management channel, the CPEs and RRs establish a DTLS management channel with iMaster NCE-WAN.
CPEs exchange TNP and IPsec SA information with RRs.
A BGP EVPN control channel is established based on TNP and SA information.
Data channel establishment + data forwarding
CPEs reflect their respective TNP and IPsec SA information through RRs.
CPEs reflect their service routes through RRs.
After the TNP and IPsec SA information is advertised, a data channel is established through routes.
Network administrator
1
2
3
Installation engineer
NETCONF
(management channel)
CPE/RR
CPE
CPE
Data channel
TNP
IPsec SA
Service route
TNP
IPsec SA
Service route
3
1
2
DTLS management channel
DTLS management channel
BGP (control channel)
BGP (control channel)
CPE
CPE
RR
2
1
3
TNP
IPsec SA
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: The management channel is used to establish control channels and deliver basic configurations.
Control channels are used to establish data channels.
  Datagram Transport Layer Security (DTLS) is a security protocol for the packet transport layer, which is used to ensure TCP data security.
Data channels are used to transfer user data.
TNP information is exchanged twice:
  During the control channel establishment phase, TNP information is exchanged to exchange information about channel establishment between RRs and CPEs.
  During the data channel establishment phase, TNP information is exchanged to exchange information about channel establishment between CPEs.

## Slide 52: Tunnel Networking Model
Sites A and B are connected through two links and can communicate with each other on the underlay network. They are planned in different RDs. Two tunnels are established between the sites.
Sites A and B are connected through two links and can communicate with each other on the underlay network. They are planned in the same RD and set up a full-mesh network.
Sites A and B are connected through two links and are isolated on the underlay network. Different RDs are planned. Two tunnels are established between the sites.
Site A
Site B
Site A
Site B
Internet-A
Internet-B
MPLS-A
Internet-A
TN | RD
MPLS-A | RD1
Internet-A | RD2
Different RDs
Different TNs, same RD
Network in the same RD, different RDs created logically
TN | RD
Internet-A | RD1
Internet-B | RD1
TN | RD
Internet-A | RD1
Internet-B | RD2
Site A
Site B
Internet-A
Internet-B
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 53: Tunnel Networking Reliability
Same RD for different TNs: The networking reliability is enhanced, but more virtual connection resources of the device are consumed.
MPLS-A
Internet-A
MPLS-A
Internet-A
Site A
Site B
Site A
Site B
Site A
Site B
MPLS-A
Internet-A
Site A
Site B
MPLS-A
Internet-A
Fault scenario A
Fault scenario B
Fault scenario A
Fault scenario B
Different RDs and TNs
Different TNs, same RD
Different RDs for different TNs: The number of connections is reduced, and the networking scale is expanded. However, the networking is less reliable.
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 54: RR Deployment Mode
Multiple areas are created, in each of which at least one pair of RRs are deployed. RRs in different areas establish BGP EVPN peer relationships with each other to advertise and learn VPN routes of different areas.
A site that functions as an RR not only implements control on the control layer but also forwards service traffic of the site on the forwarding layer.
Method 1: co-deployment of the RR and CPE
Method 2: independent deployment of RRs
Method 3: deployment of RRs in multiple areas
Sites that function as RRs do not have LAN-side networks and do not function as hubs for other sites to communicate with each other. The RR does not process service data and only performs control-layer operations.
Branch 1
Branch 2
HQ/DC
CPE
CPE
CPE (RR)
MPLS
Internet
RR site
Branch 1
Branch 2
HQ/DC
CPE
CPE
CPE
MPLS
Internet
RR
CPE
MPLS
Internet
RR
Area B
CPE
RR
Area C
CPE
RR
Area A
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: RR deployment suggestions are as follows:
  To prevent site network adjustment from affecting the stability of RRs, you are advised to use method 2, that is, independent deployment of RRs.
  Use high-performance devices as RRs. For details about the devices that can function as RRs, see the specifications list.
  Configure a public IP address for an RR, or deploy a NAT device before the RR. Only 1:1 static NAT is supported.
  An edge site can connect to a maximum of two RR sites. Two CPEs can be deployed at each RR site deployed for a tenant. If there are a large number of CPEs, multiple RRs can be deployed, and each RR serves some edge sites.
  When one CPE is connected to two RR sites, the CPE establishes a BGP connection with each RR at the RR sites.
  If a branch site has a standby link, for example, the branch or the RR has a standby link, and the active link is normal, no control channel is established for the standby link. When all active links from the branch site to the RR are down, the standby link is involved in the establishment of control channels.

## Slide 55
Notes:   It is not recommended that standby links be established at RR sites.
  If the number of CPEs on the network exceeds the RR control specification, you are advised to assign sites to different areas. An independent RR is deployed in each area, and BGP peer relationships are established between RRs in each area to exchange routes between areas.
  When deploying RRs, consider the total number of routes on the LAN side of each site to prevent the route specifications of the RR from being exceeded.
  The BGP peer relationship is established between the CPE and RR using the loopback address. If multiple tunnel connections are available between the CPE and RR, a random connection is used to establish the BGP peer relationship. When a WAN link fails, BGP automatically switches services to another link, and services between sites are not affected. When all RRs are faulty, the connections with CPEs are unavailable, interrupting services between sites. Therefore, RR reliability must be ensured during actual deployment. For example, deploy two CPEs at an RR site, specify two RR sites for the edge, and use distributed RR sites (each RR site is responsible for some CPEs). This prevents network-wide service interruption caused because the only RR deployed on the network is faulty.

## Slide 56: RR Deployment Principles
Considering the importance of RRs, follow the principles below when deploying RRs:
  Redundancy must be implemented for RRs. That is, at least two RRs must be deployed on the live network. This prevents network-wide services from being interrupted because the only RR deployed on the network fails.
  An edge site must be connected to two RRs to implement egress backup.
  It is recommended that RRs be independently deployed to ensure stability.
  If RRs cannot be deployed independently, select routers at core positions as RRs and ensure that the device performance can meet the requirements.
  Use the RR models recommended in the specifications list.
Branch
MPLS
Internet
Hub
Branch
RR1
RR2
CPE
CPE
CPE
CPE/RR
CPE/RR
Independent RR deployment
Co-deployment of the RR and CPE
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: A CPE can be connected to a maximum of two RR sites (four RRs).
For small networks (for example, a network with fewer than 50 sites), RRs and hubs can be deployed in co-located mode.
RRs require strong BGP connection capabilities (number of BGP peers), large number of EVPN connections, and high route reflection capability and efficiency. In actual deployments, select the RR models recommended in the specifications list, for example, AR6300/AR6280.

## Slide 57: Typical RR Networking: Enterprise-Built
Independent RR deployment
Co-deployment of the RR and CPE
Large enterprises have a large number of sites. If these enterprises have high network reliability requirements, independent RR deployment is recommended.
Small and midsize enterprises have a small number of branch sites. If the traffic between branches and the HQ/DC is not heavy, it is recommended that the RR be co-deployed with the CPE. The hub site functions as the RR to carry the control plane.
Branch 1
Branch 2
Hub
CPE
CPE
CPE (RR)
MPLS
Internet
RR site
Branch 1
Branch 2
Hub
CPE
CPE
CPE
MPLS
Internet
RR
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 58: Typical RR Networking: Carrier/MSP Resale
In the carrier/MSP resale scenario, it is recommended that RRs be deployed independently. The MSP administrator creates RRs, divides access areas, and allocates RRs to the corresponding access area for management.
Advantages:
The control plane of SD-WAN networks of all enterprise customers is centrally managed.
RRs can be flexibly allocated to different tenants.
In addition to RRs deployed by MSPs, carriers or MSPs can provide multi-tenant gateway access services for enterprise customers.
Enterprise A
Branch 1
Branch 2
HQ/DC
CPE
CPE
CPE
MPLS
Internet
Enterprise B
Branch 1
Branch 2
HQ/DC
CPE
CPE
CPE
MPLS
Internet
Carrier/MSP DC
RR access area 1
RR access area 2
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: An MSP administrator deploys independent RRs as a service provided by carriers or MSPs for enterprise users to access. Two RR service modes are available: sharing and exclusive. In sharing mode, one RR is shared by multiple tenants. In exclusive mode, one RR is exclusively used by a tenant.
  MSP RR sharing by multiple tenants: For small and midsize enterprises, it is recommended that one RR be shared by multiple tenants, if there are a small number of sites. Sites of different enterprise tenants are connected to the same multi-tenant RR, which carries the control plane.
  MSP RR exclusive to a tenant: Carriers can specify an independent RR in an access area for a large enterprise with a large number of sites to use exclusively. Based on actual scenarios, carriers or MSPs can deploy RRs in co-deployment mode, independently, and based on areas for tenants.

## Slide 59: NAT Traversal
On the live network, some enterprise branches use home broadband to access the network.
  In this case, traffic needs to pass through the NAT device. Therefore, tunnels cannot be directly established for such enterprise branches.
In SD-WAN scenarios, NAT traversal technology is required for interconnection between such enterprise branches.
Establishing a data channel for NAT traversal
Private IP Address: Port Number | Public IP Address: Port Number
IP1:Port1 | IP2:Port2
Private network
Private network
Internet
NAT device
NAT device
IP1
Port1
IP2
Port2
IP3
Port3
IP4
Port4
RR (STUN server)
CPE
(STUN client)
CPE
(STUN client)
Private IP Address: Port Number | Public IP Address: Port Number
IP4:Port4 | IP3:Port3
Learn the peer TNP and routes through BGP.
1
2
3
Establish a data channel for NAT traversal.
4
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
STUN binding response
STUN binding response
2
STUN binding request
STUN binding request
1

## Slide 60: NAT Traversal: Connection Between CPEs and iMaster NCE-WAN
A CPE proactively sends a registration request to iMaster NCE-WAN. To implement this, the southbound IP address of iMaster NCE-WAN must be reachable.
On the live network, iMaster NCE-WAN may be deployed behind a NAT device. In this case, the NAT Server needs to be deployed on the NAT device and the following ports need to be mapped:
  10020: southbound port, which is used by devices to register with iMaster NCE-WAN.
  10031: southbound port, which is used by devices to connect to iMaster NCE-WAN through HTTP.
  18008: northbound port, which is used for web login.
  80: northbound port, which is used for web login.
  18018: northbound port, which is used by PCs to upload files to iMaster NCE-WAN.
  18021: file server port, which is used by iMaster NCE-WAN to update files.
The NAT Server can be deployed. Therefore, NAT traversal is not involved in this scenario.
Branch
Branch
Internet
CPE
CPE
NAT device
NAT device
NAT device
Configure a public IP address and deploy a NAT server.
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 61: NAT Traversal: Connection Between CPEs and RRs
An RR must have a public IP address or be configured with 1:1 static NAT. Therefore, NAT traversal is not involved in communication between CPEs and RRs.
Branch
Branch
Internet
CPE
CPE
NAT device
NAT device
NAT device
RR
RR
The RR uses a public IP address.
Configure a public IP address for the NAT device and deploy 1:1 static NAT.
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 62: NAT Traversal: Connection Between CPEs
A data channel is established between CPEs, and traffic between sites is transmitted through the data channel. If a CPE is deployed on the private network behind the NAT device, NAT traversal is required for communication with another CPE, especially in scenarios where two CPEs at two sites are deployed on the private network behind the NAT device.
Branch
Branch
Internet
CPE
CPE
NAT device
NAT device
STUN session
NAT traversal
STUN server
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design

## Slide 63: Networking Specification Calculation
Area 1
Area 2
Area 3
Area 4
When planning a network, consider the device performance specifications. In the SD-WAN Solution, the number of BGP peers, number of tunnels, and bandwidth also need to be considered.
Networking specification calculation
  Number of BGP peers of hubs/RRs = Number of sites with dual gateways x 2 + Number of sites with a single gateway
    Number of BGP peers = 200 x 2 + 100 = 500
  Number of hub tunnels = Total number of tunnels of each gateway at a hub site
    The two hubs at a dual-hub site share the tunnel specification. For example, if a single CPE supports 1000 tunnels, the two hubs at a dual-hub site share the tunnel specification.
    Number of hub tunnels = 300 x 4 = 1200
  Network bandwidth of a hub site = Number of branch sites x Bandwidth required by sites
    Total network bandwidth required by the hub = 300 x 10 Mbps = 3 Gbps
  iMaster NCE-WAN can manage a large number of sites. In most cases, you do not need to pay attention to the networking specification calculation.
HQ/DC
30
170
15
85
Hub(RR)
Spoke
MPLS
Internet
LTE
(standby link)
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: Different device models have different BGP peer specifications and tunnel specifications.
For details about the product specifications, see the product documentation.
LAN侧有效路由约束：
vRR管理有效路由数量与该租户下的物理vRR数量成反比，即：单设备原管理路由规格/vRR物理设备数量
VRR建议：
1、在设备选型时，需要考虑设备的路由规格，以避免路由超规格，造成部分业务无法互通；
2、建议在站点LAN侧网络进行路由聚合，以避免全网路由条目过多，超出部分设备的路由表规格。分别连接到两个RR站点
BGP peers约束：
CPE采用Loopback地址与RR建立BGP连接，每个分支cpe和RR之间建立1个BGP连接。BGP连接束与链路条目数多少无关，即使CPE与RR之间有多条链路，二者之间依然只有1个BGP连接（CPE与RR无法互通时，二者无法建立BGP邻居）。
EVPN隧道规格约束：
EVPN隧道数和链路数，以及链路所属的Routing Domain强相关，链路属于同一Routing Domain，两两之间均会建立EVPN隧道。站点采用双网关模式进行部署时，每台网关上消耗的EVPN隧道规格相同，均为该站点与其他站点建立的总的EVPN隧道数（原因：站点双网关时，两台网关之间需要进行EVPN隧道信息的同步，同步的EVPN隧道信息也占用网关的EVPN隧道规格，因此每台网关上的EVPN隧道规格消耗为两台网关实际建立EVPN隧道数量之和，即该站点的总EVPN隧道数）

## Slide 64: Specifications-Exceeded Network Design
When there are a large number of branches on the network, the specifications of the hub device are easy to exceed, regardless of whether the flattened topology or hierarchical topology is used. To solve this problem, the following two solutions are available:
If the specifications are exceeded at the hub site, multiple hub sites can be deployed, and multiple areas can be created within a tenant, forming the area-based networking.
Area-based networking
Tenant-based networking
If the specifications are exceeded at the hub site and rights- and domain-based management is required, networks can be created based on tenants and centrally managed by the MSP administrator.
HQ
Hub
CPE
CPE
Branch
CPE
MPLS
/Internet
HQ
Hub
CPE
CPE
Branch
CPE
MPLS
/Internet
Area1
Area2
HQ
Hub
CPE
CPE
Branch
CPE
MPLS
/Internet
HQ
Hub
CPE
CPE
Branch
CPE
MPLS
/Internet
Tenant 1
Tenant 2
MSP administrator
RR
RR
RR
RR
RR
RR
RR
RR
Basic Concepts of Tunnels
NAT Traversal Design
RR Design
Specifications-Exceeded Network Design
Data Tunnel Design
Notes: Area-based networking:
  Multiple areas are created under a tenant, and multiple hub sites are deployed in the HQ/DC. Each area is associated with one or two hub sites.
  Branch sites are added to corresponding hub sites by area.
  RRs can be independently deployed. Each pair of RRs are associated with sites in an area.
  Traffic between inter-area sites is transmitted through the LAN side of the hub.
Tenant-based networking:
  The MSP administrator creates multiple tenants, and multiple hub sites are deployed in the HQ/DC. Each tenant is associated with one or two hub sites.
  Branch sites are grouped by their geographical areas and are added to different tenants.
  RRs can be independently deployed. Each pair of RRs are associated with sites in an area.
  Traffic between inter-area sites is transmitted through the LAN side of the hub.

## Slide 65
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
  SD-WAN Networking Design Overview
  SD-WAN Site Design
  SD-WAN Tunnel Design
  SD-WAN VPN Design
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 66: VPN Design Panorama
The SD-WAN Solution uses VPNs to isolate services for multiple departments of a single tenant. In this case, the network of each department under a tenant is an independent service VPN.
VPN design generally covers:
  VPN design
  Topology design
  VPN route design
Overlay
(virtual network)
CPE
CPE
CPE
IP overlay tunnel 1
IP overlay tunnel 2
VPN route design
RR
Core switch
Core switch
Core switch
BGP EVPN
Branch
Branch
HQ
VPN1
VPN2
VPN design
Topology design

## Slide 67: SD-WAN VPN
VPN is short for virtual private network on SD-WAN. Each VPN is an independent IP Layer 3 private network. Multiple VPNs are logically isolated from each other, from the tunnel established at a site to the CPE at the site. Therefore, these VPNs cannot directly communicate with each other.
  Each VPN can use an independent topology model, including hub-spoke, full-mesh, partial-mesh, and hierarchical networking.
  Service policies, such as traffic steering policies and QoS policies, can be independently configured for each VPN.
Virtual network (overlay network)
Physical network (underlay network)
VPN1
HQ edge
Branch edge
Branch edge
Branch edge
VPN2
MPLS
Internet
VPN Design
VPN Route Design
Topology Design

## Slide 68: VPN Planning and Design
VPN planning suggestions:
  Determine the number of departments, for example, R&D department, finance department, and marketing department, whose services need to be isolated based on service isolation requirements.
  Assign LAN-side physical interfaces and VLANs to different departments. One department can have an independent LAN-side physical interface, or all departments share one physical interface and are isolated through VLANs.
  Plan initial policies for different departments, including traffic steering policies, Internet access policies, QoS policies, legacy site access policies, and URL, IPS, and firewall policies.
...
VPN1
Traffic steering policy
QoS policy
Security policy
...
VPN2
Traffic steering policy
QoS policy
Security policy
R&D dept
Finance dept
LAN-side physical interface
WAN-side physical interface
Data tunnel
CPE
VLANIF interface
VPN Design
VPN Route Design
Topology Design

## Slide 69: Overlay Topology Design
Hierarchical networking topology
Partial-mesh networking topology
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Border 1
Border 2
Full-mesh networking topology
Hub-spoke networking topology
VPN Design
VPN Route Design
Topology Design
Notes: Hub-spoke:
  Generally, the enterprise HQ/DC functions as a hub site, and enterprise branches function as spoke sites. Server applications deployed in the HQ/DC are accessed through the WAN in a centralized manner.
Full-mesh:
  In the topology, different branches can directly communicate with each other, without the need to divert traffic through intermediate nodes.
Partial-mesh:
  Partial-mesh can be considered as a special type of full-mesh networking. If an underlay network is available between two sites, traffic can be directly transmitted between the two sites. Otherwise, the two sites communicate with each other through a redirect site.
Hierarchical networking:
  The hierarchical networking model can be considered as the combination of the single-layer networking model. A WAN is divided into multiple areas, which are interconnected through a centralized backbone area to implement inter-area communication between sites.

## Slide 70: Hub-Spoke Networking
HQ/DC
MPLS
Internet
Branch
Branch
Spoke
Hub
Solution Overview
  Generally, the enterprise HQ/DC functions as a hub site, and enterprise branches function as spoke sites. Server applications deployed in the HQ/DC are accessed through the WAN in a centralized manner.
  If branches of an enterprise need to communicate with each other, traffic between them is transmitted through the hub site. All external access traffic of branch sites is first sent to the hub site.
Application Scenario
  This mode is generally applicable to enterprises where traffic is mainly sent from branch sites to the hub site.
  Enterprise applications are centrally stored on servers at the HQ/DC. The main service traffic is from branch sites to the hub site.
  Only small traffic is transmitted between branch sites.
  A typical example is chain stores. The major traffic of a chain store is destined to the HQ/DC, and there is almost no traffic between chain stores.
VPN Design
VPN Route Design
Topology Design

## Slide 71: Full-Mesh Networking
HQ/DC
MPLS
Internet
Branch
Branch
Edge
Edge
Solution Overview
  In the full-mesh topology, branches can directly communicate with each other, without the need to divert traffic through intermediate nodes.
Application Scenario
  The full-mesh topology is applicable to small enterprises with a small number of sites or large enterprises whose branches need to collaborate with each other.
  Collaborative services, for example, high-value applications including VoIP and video conferencing, have stringent requirements on network performance such as the packet loss rate, delay, and jitter. To meet requirements of such services, branches are recommended to directly communicate with each other.
  The full-mesh topology is simple, and service communication is efficient. However, the full-mesh topology has average network scalability and applies to a network with 10 to 100 branch sites.
VPN Design
VPN Route Design
Topology Design

## Slide 72: Partial-Mesh Networking
HQ/DC
MPLS
Internet
Branch
Branch
Branch
Edge
Edge (Redirect)
Solution Overview
  A partial-mesh network can be considered a type of special full-mesh network. If direct underlay network connections are available between sites, traffic is directly transmitted between the sites. Otherwise, traffic between sites is forwarded through a redirect site, to which both sites are connected.
Application Scenario
  Branch sites cannot directly communicate with each other over the underlay network and use a redirect site for communication instead.
  In full-mesh networking, branch sites directly communicate with each other over the underlay network. To enhance reliability, a redirect site can be deployed. When the underlay network is faulty and sites cannot directly communicate with each other, traffic between branch sites is transmitted through the redirect site.
VPN Design
VPN Route Design
Topology Design

## Slide 73: Hierarchical Networking
Solution Overview
  The hierarchical networking model can be considered as the combination of the single-layer networking model. A WAN is divided into multiple areas, which are interconnected through a centralized backbone area to implement inter-area communication between a large number of sites.
  For example, a multinational enterprise can be divided into multiple areas (China, Europe, America, etc.) based on its management structure. Each area uses a single-layer networking model, which can be hub-spoke or full-mesh. In addition, each area uses one or more sites as their border sites. The border sites of each area form the backbone area for interconnection between areas, that is, the level-1 network. In this way, border sites connect to both the level-2 area network and level-1 network.
Application Scenario
  The hierarchical networking is applicable to enterprises with a large number of sites or multinational enterprises with widely distributed sites. The hierarchical networking has a clear network structure and good network scalability.
MPLS
Internet
MPLS
Internet
MPLS
Internet
Level-1 network
Level-2 network
Edge
Border
Edge
VPN Design
VPN Route Design
Topology Design

## Slide 74: VPN Route Design
The VPN routes of the local CPE are collected using the LAN-side routing protocol and then sent to the peer CPE through the BGP EVPN protocol of the WAN.
  LAN-side routes: LAN-side interfaces of CPEs support OSPF, BGP, and static routing protocols. The routing protocol to be used must be the same as that of the LAN-side network device.
  WAN-side overlay routes: Generally, BGP EVPN is deployed to establish BGP peer relationships with RRs and advertise overlay network domain routes. The configuration is automatically orchestrated by the controller.
  LAN- and WAN-side routes can be filtered using routing policies.
MPLS
Internet
CPE
CPE
RR
HQ
Branch
BGP, OSPF
Direct, static route
BGP, OSPF
Direct, static route
BGP EVPN
BGP EVPN
VPN Design
VPN Route Design
Topology Design

## Slide 75
SD-WAN networking design includes site design, tunnel design, and VPN design.
  Site design: includes WAN/LAN networking design and dual-CPE design.
  Tunnel design: includes data tunnel design, RR design, NAT design, and specifications-exceeded network design.
  VPN design: includes VPN design, topology design, and VPN route design.

## Slide 76
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
  SD-WAN Service Design Overview
  SD-WAN Application Service Design
  SD-WAN Network Service Design
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 77: Overview of Service Design for Huawei SD-WAN Solution
SD-WAN service design includes application service design and network service design.
Branch site
Branch site
Active DC
Standby DC
Overlay
(virtual network)
CPE
CPE
CPE/RR
CPE/RR
Application service design
Service 1
Service 2
Service 1
Service 2
GRE or GRE over IPsec (data channel)
Service 2: SLA: delay: 150 ms; jitter: 10%; packet loss rate: 10%; TN2 preferred
Service 1: SLA: delay: 50 ms; jitter: 5%; packet loss rate: 5%; TN1 preferred
Internet
Network service design
Legacy network
GW

## Slide 78: Service Design Process for Huawei SD-WAN Solution
1. Application service design
Intelligent traffic steering design
2. Network service design
Packet loss optimization design
Internet access design
QoS design
Legacy site access design

## Slide 79
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
  SD-WAN Service Design Overview
  SD-WAN Application Service Design
  SD-WAN Network Service Design
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 80: Application Service Design Panorama
Enterprises have diverse applications, such as production, coordination, and entertainment applications. Different applications have different requirements on bandwidth and link quality.
Application service design generally covers:
  Intelligent traffic steering design
  QoS design
  Packet loss optimization design
MPLS
Internet
Branch
SPR module
TCP, UDP, GRE, etc.
Source IP, source port, destination IP, etc.
DSCP, VPN, TCP-flag…
Based on protocol types
Based on packet applications
Based on packet information
Application identification
Intelligent traffic steering design
QoS design
Packet loss optimization design
1
2
3
4

## Slide 81: Application Identification
Traditional routing and switching devices cannot identify application-layer information. Therefore, it is difficult to manage networks based on applications. Smart Application Control (SAC) technology helps routing and switching devices identify and classify applications.
SAC first checks whether an application has been identified. If an application has not been identified, SAC checks the first-packet inspection (FPI) signature database and service awareness (SA) signature database in sequence.
Network device
FPI signature database
Service traffic
Signature matching
SA signature database
Signature matching
Application identification record
SAC
Layer 3 forwarding for identified applications
Voice
Video
Web browsing
Download
Forwarding table
Notes: After a packet enters the device, the device determines whether the corresponding application has been identified based on the 5-tuple information carried in the packet. If the application has been identified, the device forwards the packet at Layer 3 without identifying the application again. If the application has not been identified, the device performs the SAC application identification process. The device then processes the packet based on the SAC identification result and forwards the packet at Layer 3.
SAC identifies an application as follows: SAC first identifies an application according to ACL rules in FPI. If the application fails to be identified, the application is identified according to the DNS association table in FPI. If the application fails to be identified, the device identifies the application based on the protocol port table in the FPI. If the application still fails to be identified, the device attempts to identify the application using SA.

## Slide 82: Intelligent Traffic Steering Design: Link Quality-based Traffic Steering
Different applications have different requirements on link quality. For example, voice and video services have stringent requirements on the delay and packet loss rate. Generally, the delay must be within 150 ms and the packet loss rate must be less than 1% for these services.
To guarantee voice and video services, the MPLS link that offers good quality can be configured as the active link for the services, with the Internet link functioning as the standby link. In addition, you can configure SLA requirements for the services to implement traffic steering based on the link SLA.
HQ
Branch
Intelligent Traffic Steering Design
QoS Design
Packet Loss Optimization Design
5
4
3
2
1
CPE
CPE
5
4
Dynamic switchover
Link quality deterioration
High-quality link
Low-quality link
HQ
Branch
5
4
CPE
CPE
High-quality link
Low-quality link
3
2
1
Link quality deterioration
QoS Design
Packet Loss Optimization Design

## Slide 83: Intelligent Traffic Steering Design: Load Balancing-based Traffic Steering
If an enterprise with multiple links wants to fully utilize the link bandwidth resources and steer traffic in load balancing mode based on the link bandwidth, load balancing-based traffic steering can be configured.
For example, the two MPLS links can be configured as primary links for the voice service. If the quality of both links meets the SLA requirements of the voice service, voice service flows can be carried over the two MPLS links in load balancing mode. Through real-time bandwidth utilization monitoring, the bandwidth utilization can reach 85%, fully utilizing the link bandwidth.
4
3
2
1
4
3
2
1
4
3
2
1
HQ
Branch
CPE
CPE
High-bandwidth link
Low-bandwidth link
Intelligent Traffic Steering Design
QoS Design
Packet Loss Optimization Design

## Slide 84: Intelligent Traffic Steering Design: Application Priority-based Traffic Steering
If multiple types of service packets are transmitted on the same link, application priority-based traffic steering can be used, so that traffic of high-priority applications is preferentially processed when congestion occurs, ensuring experience of high-priority applications.
For example, voice, video, and file transfer services are carried on an MPLS link. If the link bandwidth is insufficient, the experience of the voice and video services is preferentially guaranteed.
Network congestion
5
4
5
4
HQ
Branch
CPE
CPE
High-quality link
Low-quality link
5
4
5
4
High-priority applications
Low-priority applications
3
2
1
3
2
1
HQ
Branch
CPE
CPE
High-quality link
Low-quality link
5
4
5
4
High-priority applications
Low-priority applications
3
2
1
3
2
1
Traffic switching of low-priority applications
Intelligent Traffic Steering Design
QoS Design
Packet Loss Optimization Design

## Slide 85: QoS Design: HQoS
VPN1
40%
Child traffic policy
Parent traffic policy
Bind the parent policy to an interface.
Multiple applications within a department
  Enterprise applications have different link requirements and different importance. The experience of important applications should be preferentially guaranteed if the egress link bandwidth is limited.
Multiple departments of an enterprise
  An enterprise usually has multiple departments of different importance. Traffic of each department needs to be isolated, and different bandwidths need to be allocated to each department.
Solution
  Different HQoS policies, including queue scheduling, CAR, and shaping, can be configured for each VPN based on applications.
  The ratio of the minimum guaranteed bandwidth can be specified for each VPN. This prevents failures of services in some VPNs when bandwidth resources of these VPNs are preempted by other VPNs with heavy traffic upon network congestion.
Overlay
60%
Local breakout
40%
WAN interface
100 Mbit/s
VPN2
60%
Overlay
70%
Local breakout
30%
VoIP
Email
SaaS
VoIP
Email
SaaS
QoS at the service layer
Overlay local breakout traffic measurement
Interface-based rate limiting
Intelligent Traffic Steering Design
QoS Design
Packet Loss Optimization Design
Notes: An enterprise usually has multiple departments of different importance. Traffic of each department needs to be isolated, and different bandwidths need to be allocated to each department.
  A specified bandwidth quota is assigned to each department to meet its service requirements.
  If some departments do not fully use their bandwidth quotas, the idle bandwidth resources can be used by other departments with insufficient bandwidth.
  Internet access traffic and traffic for communication with legacy sites needs to be controlled separately.

## Slide 86: Packet Loss Optimization Design
Forward error correction (FEC) technology can mitigate packet loss. During data transmission, FEC adds redundant packets carrying check information at the transmit end and performs check at the receive end. If a packet is lost or damaged on the network, the redundant packet can be used to recover it.
The following FEC modes are supported:
  Adaptive forward error correction (A-FEC): A CPE automatically detects the packet loss rate and adjusts the number of redundant packets in real time based on the packet loss rate. This mode reduces the number of redundant packets and saves bandwidth when the packet loss rate is low. When the packet loss rate increases, redundant packets are increased to improve the packet loss mitigation performance. However, if the packet loss rate suddenly increases greatly, it takes a period of time for the CPE to detect the event and adjust the number of redundant packets. As a result, packet loss occurs for a short period of time.
  Determined forward error correction (D-FEC): The number of redundant packets is calculated based on the configured packet loss rate. This mode can recover the lost packets within the configured maximum packet loss rate. Although the redundancy of this mode is greater than that of A-FEC, packet loss does not occur when the packet loss rate suddenly changes.
After FEC is deployed and the network runs for a period of time, you can view the packet loss mitigation effect on iMaster NCE-WAN to determine whether the FEC design is proper.
Intelligent Traffic Steering Design
QoS Design
Packet Loss Optimization Design

## Slide 87
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
  SD-WAN Service Design Overview
  SD-WAN Application Service Design
  SD-WAN Network Service Design
Reliability and Security Design for Huawei SD-WAN Solution

## Slide 88: Network Service Design Panorama
SD-WAN sites may also need to access the Internet or legacy sites. Therefore, specific network services need to be deployed.
Network service design generally covers:
  Internet access design
  Legacy site access design
Branch
Branch
Internet
CPE
CPE
HQ
CPE
Internet resources
Internet access design
Legacy site
Gateway
Legacy site access design

## Slide 89: Internet Access Solution
The SD-WAN Solution provides the following Internet access modes:
  Local Internet access: The Internet access traffic of a site is routed from the local CPE to the Internet.
  Centralized Internet access: The Internet access traffic of all sites is diverted to the centralized Internet access site and then to the Internet.
  Hybrid Internet access: combination of local Internet access and centralized Internet access.
    Local Internet access (default) + centralized Internet access: By default, all Internet access traffic is routed out from the local device. When the local Internet access interface is faulty, Internet access traffic is forwarded through the centralized gateway.
    Centralized Internet access (default) + Local Internet access for specified traffic: By default, Internet traffic is routed out through the centralized Internet access site. Traffic of some specified services is directly routed to the Internet through the local WAN-side link.
Branch
Branch
Internet
CPE
CPE
HQ
CPE
Internet resources
Local Internet access
Centralized Internet access
Internet Access Design
Legacy Site Access Design

## Slide 90: Local Internet Access Design
Internet
MPLS
Description
The Internet access traffic of a site is routed out from the local Internet link to the Internet.
Local Internet access policies can be configured on a per-department and per-site basis.
Local Internet access can be implemented in the following modes: 1. All Internet access traffic is routed out from the local device to the Internet. 2. Internet access traffic of specified applications is routed out from the local device to the Internet.
Outbound interfaces must be configured for local Internet access. A maximum of three outbound interfaces can be configured. If multiple outbound interfaces are configured, they back up each other, and the outbound interface is selected based on the priority.
In local Internet access mode, whether to enable the NAT function can be configured based on the outbound interface. Currently, NAT in Easy IP mode is provided. That is, the IP address of the outbound interface is used as the post-NAT public IP address.
CPE2
CPE1
Branch
Branch
IWG
Application scenario
Local Internet access is applicable to small enterprises or scenarios where centralized security control is not required for Internet access traffic and links for accessing the Internet are available on the WAN side.
Internet Access Design
Legacy Site Access Design
Notes: Traffic cannot be transmitted to the Internet through multiple links in load balancing mode. The links can work only in active/standby mode based on their priorities.
If local Internet access is configured for specified application traffic and centralized Internet access is also configured, local Internet access for specified application traffic is implemented by orchestrating policy-based routing (PBR).
If local Internet access is enabled, the default route on the underlay WAN needs to be configured. The default route can be a static route (mainly for Internet access through the Internet network interface) or BGP/OSPF route (mainly for Internet access through the MPLS network interface).

## Slide 91: Centralized Internet Access Design
Internet
MPLS
CPE2
CPE1
Branch
HQ (centralized Internet access gateway)
Description
All sites of a tenant access the Internet through a centralized Internet access site.
Either of the following solutions can be used for Internet access through the centralized gateway site:
  If the centralized Internet access site has the Internet egress on the LAN side, all Internet access traffic is routed out through the LAN side of the centralized Internet access site. In this mode, you need to configure a default route or dynamic routing protocol on the LAN side so that the default route can be learned from the LAN side.
  If the centralized Internet access site accesses the Internet through the WAN-side interface, all Internet access traffic is transmitted to the Internet through the WAN side of the centralized Internet access site. (Note: For the site that functions as a centralized gateway, the local Internet access function must also be enabled.)
Application scenario
This mode is applicable to scenarios where no link is available for a site to access the Internet or centralized security control is required for Internet access traffic. A centralized Internet access gateway is configured so that traffic from other sites can be forwarded to the centralized Internet access gateway through the overlay network.
Internet Access Design
Legacy Site Access Design

## Slide 92: Hybrid Internet Access Design: Local Internet Access (Default) + Centralized Internet Access
Internet
MPLS
CPE2
CPE1
Branch
HQ
Description
Both local Internet access and centralized Internet access are configured on the SD-WAN network.
Local Internet access is configured for all traffic at a site.
If a site has two Internet access links, that is, one for local Internet access and one for centralized Internet access, the link for local Internet access has a higher default route preference.
By default, all Internet access traffic is routed out from the local Internet access interface. When the local Internet access interface is faulty, Internet access traffic is diverted to the centralized gateway and then routed out.
Application scenario
This mode applies to small enterprises or scenarios where Internet access traffic does not need to be centrally managed.
The WAN side of the site has links to access the Internet, and the site has high requirements on Internet access reliability.
Internet Access Design
Legacy Site Access Design

## Slide 93: Hybrid Internet Access Design: Centralized Internet Access (Default) + Local Internet Access for Specified Traffic
Internet
MPLS
CPE2
CPE1
Branch
HQ
Description
Configure both local Internet access and centralized Internet access on the SD-WAN network.
Local Internet access is configured at the centralized Internet access site, where all traffic is routed out in local Internet access mode.
Local Internet access is enabled at other sites and is configured for specified applications.
By default, Internet access traffic is routed out through the centralized Internet access site, and specific experience-sensitive service traffic is directly transmitted to the Internet through the local WAN-side link.
Application scenario
This mode applies to the scenario where a site has Internet access links, most Internet access traffic needs to be centrally managed, and traffic of some applications can be directly routed out to meet SLA requirements.
Internet Access Design
Legacy Site Access Design

## Slide 94: Internet Access Link Reliability
Internet 1
Internet 2
Internet 3
Standby link solution design:
  Links for Internet access are configured on a per-site basis. A maximum of three WAN links can be configured for Site-to-Internet access.
  A priority is configured for each WAN link. Currently, each link has a unique priority. That is, only one WAN link is used as the active link for accessing the Internet at a time.
  When a WAN link with the highest priority fails, traffic to the Internet is automatically switched to the link with the second highest priority.
  The standby link and hybrid Internet access mode can be used together.
CPE2
Branch
Priority = 1
Priority = 2
Priority = 3
Internet Access Design
Legacy Site Access Design

## Slide 95: Legacy Site Communication Solution
Before deploying the SD-WAN Solution, enterprises may have legacy sites that are interconnected through traditional WAN private lines (such as MPLS). After the SD-WAN Solution is deployed, SD-WAN sites and legacy sites may need to communicate with each other. To implement this, a solution for communication with legacy sites must be deployed.
Communication between SD-WAN sites and legacy sites involves the following scenarios:
  Communication through enterprise sites: Enterprise sites are directly connected to legacy networks. Two communication solutions are available in this scenario:
    Communication through dedicated lines
    Local access
  Communication through the IWG: Carriers use this mode to provide communication with legacy sites for multiple enterprises. Generally, three communication solutions are available in this scenario:
    Inter-AS Option B
    Inter-AS Option A (Layer 3 VXLAN)
    Inter-AS Option A (Layer 3 VLAN)
Internet Access Design
Legacy Site Access Design

## Slide 96: Communication Through Enterprise Sites: Communication Through Dedicated Lines
When the underlay network connected to an SD-WAN site cannot communicate with a legacy MPLS network, select an SD-WAN CPE and a legacy CPE, which are logically considered as a gateway site.
When an enterprise has multiple VPNs and users on the SD-WAN and legacy networks belong to the same VPN, multiple logical links can be created on the dedicated link of a gateway site and added to the VRFs corresponding to different VPNs. In this way, back-to-back communication between multiple VPNs is implemented.
Communication through dedicated lines
MPLS 1
MPLS 2
Legacy network
SD-WAN network
Gateway site
VPN1
VPN2
Legacy site
Legacy site
SD-WAN site
SD-WAN site
Routes are transmitted through OSPF/BGP.
SD-WAN CPE
Legacy CPE
Legacy CPE
SD-WAN CPE
Internet Access Design
Legacy Site Access Design
Notes: A dedicated link is established between user-side interfaces on both the legacy CPE and SD-WAN CPE. The dedicated link runs a protocol such as BGP or OSPF to exchange routes between the legacy MPLS network and SD-WAN network. In this way, users on the two networks can communicate with each other through the dedicated link.

## Slide 97: Communication Through Enterprise Sites: Local Access
When the underlay network connected to an SD-WAN site is the legacy MPLS network or can communicate with the legacy MPLS network, local breakout technology can be used to transmit user traffic of the SD-WAN site to the underlay MPLS network. Then the traffic is transmitted to the legacy sites over the underlay network.
In the local access solution, only traffic of users in one SD-WAN VPN can be transmitted to users of the VPN at the corresponding legacy sites on the underlay network through local breakout.
Local access design
MPLS 1
Legacy network
SD-WAN network
Legacy site
Legacy site
SD-WAN site
SD-WAN site
Local breakout
Legacy CPE
SD-WAN CPE
Internet Access Design
Legacy Site Access Design
Notes: Multiple traffic models are supported in this scenario, and you can choose one based on your service requirements.
  Distributed local access: This model applies if all SD-WAN sites can access legacy sites over the underlay MPLS network through local breakout. In this model, traffic of each site is directly forwarded through the local site, without the need of being forwarded through overlay tunnels.
  Centralized local access: If some SD-WAN sites cannot access legacy sites through local breakout, you can configure a site that can communicate with the legacy sites as the centralized access site. Traffic from other SD-WAN sites is sent to the centralized access site through overlay tunnels, and then forwarded to the legacy sites through local breakout.
  Hybrid local access: The SD-WAN Solution enables multi-link sites using the distributed local access model to use local access preferentially, with centralized local access as a backup. This enhances reliability. Traffic from a site that uses the distributed local access model is preferentially transmitted to a legacy site through local breakout. If the MPLS link for local access fails, traffic is automatically switched to the overlay tunnel of another link and transmitted to the centralized access site. The centralized access site then forwards the traffic to legacy sites.

## Slide 98: IWG
The IWG can connect both SD-WAN sites and legacy MPLS VPN sites for multiple enterprise tenants. Each time a tenant is added, only one MP-EBGP peer needs to be configured to interconnect with the peer ASBR-PE.s
Solution design for multiple tenants to communicate with legacy sites
MPLS 1
MPLS 2
Legacy network
SD-WAN network
Enterprise A
Enterprise B
Enterprise A
Enterprise B
IWG
Legacy CPE
SD-WAN CPE
Legacy CPE
ASBR-PE
PE
MP-BGP
VRF1
VRF2
Tenant 1: VPN 1
Tenant 2: VPN 2
Establish BGP peer relationships
Internet Access Design
Legacy Site Access Design

## Slide 99: Communication Through the IWG: Inter-AS Option B
Similar to the inter-AS Option B solution in MPLS VPN, in the inter-AS Option B solution in SD-WAN, MP-EBGP is used between the IWG and ASBR-PE on legacy networks to exchange labeled VPN-IPv4 routes received from PEs in their respective ASs.
A pair of public interfaces are configured on the IWG and ASBR-PE, and MPLS is enabled. MP-EBGP is used to exchange labeled VPN-IPv4 routes. BGP is used to transmit inter-AS labels. Therefore, LDP is not required between the IWG and ASBR-PE.
Inter-AS Option B
MPLS 1
MPLS 2
Legacy network
SD-WAN network
Enterprise A
Enterprise B
Enterprise A
Enterprise B
IWG
Legacy CPE
SD-WAN CPE
Legacy CPE
ASBR-PE
PE
MP-BGP
MP-BGP
VRF1
VRF2
VRF1
VRF2
Internet Access Design
Legacy Site Access Design

## Slide 100: Communication Through the IWG: Inter-AS Option A (Layer 3 VXLAN)
Similar to the inter-AS Option A solution in MPLS VPN, in the inter-AS Option A solution for SD-WAN, IWGs are interconnected with ASBR-PEs through Layer 3 VXLAN tunnels, and the EBGP or IBGP peer relationship is established at both ends of VXLAN tunnels to exchange routes between SD-WAN sites and legacy sites.
Inter-AS Option A (Layer 3 VXLAN) solution design
MPLS 1
MPLS 2
Legacy network
SD-WAN network
Enterprise A
Enterprise B
Enterprise A
Enterprise B
IWG
Legacy CPE
SD-WAN CPE
Legacy CPE
ASBR-PE
PE
MP-BGP
VRF1
VRF2
VRF1
VRF2
Establish BGP peer relationships
VXLAN tunnel
Internet Access Design
Legacy Site Access Design

## Slide 101: Communication Through the IWG: Inter-AS Option A (Layer 3 VLAN)
Between the IWG of the SD-WAN network and the PE of the legacy MPLS network, a pair of specific interfaces (VLANIF interfaces or Ethernet sub-interfaces) are configured for each user VPN and are added to the corresponding VRF. In addition, EBGP is configured based on the VPN instance to exchange routes between the SD-WAN and MPLS domains.
Inter-AS Option A (Layer 3 VLAN) solution design
MPLS 1
MPLS 2
Legacy network
SD-WAN network
Enterprise A
Enterprise B
Enterprise A
Enterprise B
IWG
Legacy CPE
SD-WAN CPE
Legacy CPE
ASBR-PE
PE
MP-BGP
VRF1
VRF2
VPN1
VPN2
Establish BGP peer relationships
Internet Access Design
Legacy Site Access Design

## Slide 102
SD-WAN service design includes application service design and network service design.
  Application service design: includes intelligent traffic steering design, QoS design, and packet loss optimization design.
  Network service design: includes Internet access design and legacy site access design.

## Slide 103
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution
  Reliability and Security Design Overview
  Site Reliability Design
  Controller Reliability Design
  Security Design

## Slide 104: Overview of Reliability and Security Design for Huawei SD-WAN Solution
Reliability and security design for Huawei SD-WAN Solution mainly includes three parts: site reliability design, controller reliability design, and security design.
Branch
MPLS
Internet
Hub
Branch
RR1
RR2
CPE
CPE
CPE
CPE/RR
CPE/RR
NAT device
iMaster NCE-WAN
MPLS
IWG
Security design
Legacy site
Site reliability design
Controller reliability design
Site reliability design
Site reliability design

## Slide 105: Reliability and Security Design Process for Huawei SD-WAN Solution
1. Site reliability design
2. Controller reliability design
Controller deployment reliability design
Controller networking reliability design
Hub site reliability design
RR site reliability design
IWG site reliability design
3. Security design
System security design
Service security design

## Slide 106
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution
  Reliability and Security Design Overview
  Site Reliability Design
  Controller Reliability Design
  Security Design

## Slide 107: Site Reliability Design Overview
SD-WAN sites are typically classified into edge sites, hub sites, and RR sites, as well as gateway sites connected to traditional networks. In Huawei SD-WAN Solution, hub sites, RR sites, and gateway sites are key sites, and their reliability greatly affects the reliability of the entire SD-WAN network.
Site reliability design generally covers:
  Hub site reliability design
  RR site reliability design
  IWG site reliability design
Branch
MPLS
Internet
Hub1
Branch
RR site 1
RR site 2
CPE
CPE
CPE
CPE/RR
CPE/RR
NAT device
MPLS
Active IWG
Hub2
CPE/RR
CPE/RR
Standby IWG
Hub site reliability design
RR site reliability design
Legacy site
IWG site reliability design

## Slide 108: Hub Site Reliability Design
DC
DC
DC
DC
MPLS
Internet
MPLS
Internet
Spoke
Hub1
Hub2
DCI
Production services
Office services
Production services
Office services
Spoke
Hub1
Hub2
DCI
Region A
Region B
Spoke
Active-active hub site networking based on spoke sites
Active-active hub site networking based on service network segments
Office services are mainly destined for Hub1.
Production services are mainly destined for Hub2.
Branch services in Region A are mainly destined for Hub1.
Branch services in Region B are mainly destined for Hub2.
Primary path
Backup path
Hub Site Reliability Design
IWG Site Reliability Design
RR Site Reliability Design
Branch
Branch
Branch
Branch
Primary path
Backup path
Notes: Active-active hub site networking based on service network segments:
  If branch sites' access to DCs can be distinguished based on service network segments, active-active hub sites can be implemented based on the service network segments. Each of the hub sites functions as the active hub site for one service or standby hub site for another different service.
Active-active hub site networking based on spoke sites:
  If an enterprise's WAN spans a large physical distance and the enterprise's two DCs are far away from each other, active-active hub sites based on spoke sites are recommended. Each spoke site connects to both hub sites deployed in the DCs and preferentially accesses the nearer hub site for a better DC service access experience. The nearer hub site is the primary one, while the farther hub site is the backup one.

## Slide 109: RR Site Reliability Design: RR Redundancy
RR site
One CPE can be connected to two RR sites (four RRs) at most. The following figures from left to right show the RR site deployment modes in three scenarios, where reliability is enhanced in ascending order.
MPLS
Internet
One RR site, two RRs at such site
Two RR sites, one RR at each site
Two RR sites, two RRs at each site
RR site
MPLS
Internet
RR site
MPLS
Internet
RR site
RR site
Enhanced reliability in ascending order
CPE
CPE
CPE
CPE
CPE
CPE
Branch
Branch
Branch
Branch
Branch
Branch
Hub Site Reliability Design
IWG Site Reliability Design
RR Site Reliability Design

## Slide 110: RR Site Reliability Design: RR Link Redundancy
The edge site needs to be dual-uplinked to the RR site.
Low reliability: If one RR is faulty, some branch sites will lose connection with the RR site, causing service interruptions.
Multiple links are deployed on the RR side. This ensures reliable connections between CPEs and RRs.
Multiple links are deployed at the branch site. This ensures reliable connections between CPEs and RRs.
MPLS
Internet
Single link
Multi-link (topology 1)
Multi-link (topology 2)
RR site
MPLS
Internet
RR site
MPLS
Internet
RR site
CPE
CPE
CPE
CPE
CPE
CPE
Branch
Branch
Branch
Branch
Branch
Branch
Hub Site Reliability Design
IWG Site Reliability Design
RR Site Reliability Design

## Slide 111: IWG Reliability Design
Branch sites are specified with active and standby IWGs to establish IWG tunnels. On the active and standby IWGs, BGP routing policies are automatically orchestrated to control the preference of BGP routes originated from the legacy network.
The preference of BGP routes on the active IWG is higher than that of BGP routes on the standby IWG.
Internet
MPLS
CPE
CPE
Active IWG
Standby IWG
ASBR-PE
ASBR-PE
PE
CE
Legacy network
SD-WAN network
Branch
Branch
Branch
Hub Site Reliability Design
IWG Site Reliability Design
RR Site Reliability Design
MPLS

## Slide 112
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution
  Reliability and Security Design Overview
  Site Reliability Design
  Controller Reliability Design
  Security Design

## Slide 113: Controller Reliability Design Overview
The controller iMaster NCE-WAN is the core component of Huawei SD-WAN Solution. All services in Huawei SD-WAN Solution are orchestrated through the controller. Therefore, controller reliability directly affects network services.
Controller reliability design generally covers:
  Controller deployment reliability design
  Controller networking reliability design
Primary DC
Internet/MPLS
iMaster NCE-WAN cluster (active)
Backup DC
iMaster NCE-WAN cluster (standby)
Egress device
Egress device
Controller deployment reliability design
Controller networking reliability design

## Slide 114: Controller Deployment Design in a Site
Controller Deployment Reliability Design
Controller Networking Reliability Design
The controller is deployed in distributed cluster architecture to provide high reliability and load balancing capabilities. When a node in the cluster is faulty, other nodes take over services, without affecting services.
Northbound load balancing: External requests are distributed to all nodes in the cluster instead of being centrally processed on just one node. Doing so fully utilizes cluster capabilities and improves reliability.
Southbound load balancing: Controller nodes are dynamically assigned to network devices based on the loads of each controller node.
Cluster | Function Description
Service processing cluster | Provides service processing capabilities, such as CPE management, overlay network configuration delivery, and traffic policy configuration.
Data processing cluster | Provides functions such as CPE performance data storage and data aggregation.
Nginx cluster | Serves as a high-performance HTTP proxy server that forwards concurrent connection requests and implements L4-L7 load balancing for northbound traffic.
LVS | Works as a load balancing component and implements L1-L4 load balancing for southbound and northbound traffic.
Controller deployment in distributed cluster architecture
Nginx cluster
Service processing cluster
Data processing cluster
Linux Virtual Server (LVS)
Physical server
Virtual machine

## Slide 115: Controller DR Deployment Design
The geo-redundant disaster recovery (DR) system consists of two sets of iMaster NCE-WAN, which are deployed at two geo-redundant sites.
Primary site
Backup site
Controller cluster
Controller cluster
Heartbeat link
Data replication link
Geo-redundant DR ensures backup between two controller clusters. The number of nodes in the active cluster must be the same as that in the standby cluster.
The active and standby controller clusters are both running. However, only the active cluster can provide services, while the standby cluster does not provide services. Data in the active cluster is synchronized to the standby cluster in real time to ensure data consistency.
The same domain name solution is used for northbound and southbound interfaces of the active and standby controller clusters. Tenants and devices access the active controller cluster through this unified domain name. After active/standby switchover, this domain name is mapped to the new active controller cluster.
Active/standby switchover is performed manually and can be completed within 10 minutes. In the case of component-level faults in the controller cluster, services are still guaranteed through reliability technologies, including clustering and fault tolerance.
Geo-redundant DR network requirements: latency ≤ 20 ms; bandwidth ≥ 125 Mbit/s
Controller Deployment Reliability Design
Controller Networking Reliability Design

## Slide 116: Reliability Design for Single-Controller Networking
To ensure the reliability of SD-WAN management channels, dual gateways and dual links generally need to be deployed for highly reliable communication between CPEs/RRs and the controller.
Hybrid networking (public and private network)
The controller is deployed inside the HQ DC, and uses public IP addresses to provide services for CPEs.
1:1 static NAT is deployed on the public network egress device at HQ.
NAT-related public IP addresses need to be advertised into the private line network.
Communication between CPEs and the controller through the public network or private line must traverse the NAT device on the public network.
Internet
CPE
CPE
CPE
NAT GW
Single-network-type networking
The controller is deployed inside the HQ DC.
The private line network needs to send the network segment where the controller resides to VPN networks.
On the public network, 1:1 static NAT must be deployed on the public network egress device. Static NAT uses the same public IP address.
CPE
CPE
CPE
Branch
Branch
Private line
HQ DC
HQ DC
Private line/Public network
Private line/Public network
Controller Deployment Reliability Design
Controller Networking Reliability Design

## Slide 117: Reliability Design for Active and Standby Controller Networking
In active and standby controller scenarios, communication between CPEs and the active and standby controllers is regulated by controlling route priorities.
Single-network-type networking
CPE
CPE
CPE
EBGP
EBGP
High priority
Low priority
Use the same southbound and northbound IP addresses.
Heartbeat tunnel
Active controller
Standby controller
Branch
Private line/Internet
Primary DC
Backup DC
On a pure private line network, the southbound and northbound IP addresses of the active and standby controllers need to be advertised to the private line network through EBGP peers. Additionally, routing policies are used to ensure the route destined for the active controller is preferentially selected.
On a pure public network, 1:1 static NAT needs to be deployed for southbound and northbound IP addresses, and the NAT configurations on the two egress gateways must be the same. Routes related to NAT addresses are advertised to the public network through EBGP, and routing policies are used to ensure the NAT-related route destined for the primary DC is preferentially selected.
Controller Deployment Reliability Design
Controller Networking Reliability Design
Notes: The active controller is deployed in the primary DC, and the standby controller in the backup DC. A heartbeat tunnel is established between the active and standby controllers to synchronize data and verify the controller status.
The active and standby controllers use the same southbound and northbound IP addresses. In public network scenarios, the same NAT address must also be configured.

## Slide 118
Development Trends and Challenges Facing Enterprise WAN Interconnection
Overview of Huawei SD-WAN Solution
Networking Design for Huawei SD-WAN Solution
Service Design for Huawei SD-WAN Solution
Reliability and Security Design for Huawei SD-WAN Solution
  Reliability and Security Design Overview
  Site Reliability Design
  Controller Reliability Design
  Security Design

## Slide 119: Security Design Overview
Security design for Huawei SD-WAN Solution generally covers:
  System security: The security requirements of the SD-WAN Solution must be met. In this way, the entire system can run securely and stably.
  Service security: The security requirements of services carried by the SD-WAN Solution must be met. Appropriate security protection measures are flexibly selected as required, thereby ensuring secure and reliable running of user services.
RR
CPE
CPE
Branch site
HQ/DC site
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE or GRE over IPsec (data channel)
Data channel security
Service traffic security
1
1
1
1
2
CPE security hardening
1
Control channel security
Management channel security
Controller security hardening

## Slide 120: System Security Design: Inter-Component Communication Security
The communication channels between components of Huawei SD-WAN Solution are classified into three types: management channels, control channels, and data channels. CPEs/RRs communicate with the controller through management channels, CPEs communicate with RRs through control channels, and CPEs communicate with each other through data channels.
The components of Huawei SD-WAN Solution use secure communication protocols to establish management, control, and data channels, thereby ensuring inter-component communication data security.
RR
CPE
CPE
Branch site
HQ/DC site
MPLS
NETCONF Over SSH
(management channel)
BGP over IPsec
(control channel)
GRE or GRE over IPsec (data channel)
Using IPsec to secure control channels
Using SSH to secure management channels
System Security Design
Service Security Design
  Security mechanisms for management channels and control channels are enabled by default. You do not need to configure them.
  Security mechanisms for data channels need to be designed flexibly as required.
Internet
Using IPsec to secure the forwarding plane

## Slide 121: System Security Design: Data Channel Security
Data channels are overlay tunnels established between CPEs. IPsec is used on such tunnels to ensure data confidentiality and integrity during transmission.
  IPsec must be deployed when data channels are established over the Internet.
  IPsec can be deployed as required when data tunnels are established over MPLS or private networks.
CPE
CPE
Branch site
HQ/DC site
MPLS
Internet
GRE tunnel
GRE tunnel
IPsec tunnel
System Security Design
Service Security Design

## Slide 122: System Security Design: Administrator Authentication and Authorization
The system supports local and remote authentication for administrators. Strict identity authentication ensures that only authorized administrators can log in to the system.
When a tenant administrator logs in to iMaster NCE-WAN, two-factor authentication (account/password + SMS verification code) is supported. The tenant administrator can be authenticated in either of the following modes:
  Local authentication: When a tenant administrator logs in to iMaster NCE-WAN, iMaster NCE-WAN authenticates the tenant administrator.
  LDAP server authentication: iMaster NCE-WAN connects to an LDAP server (such as a general-purpose LDAP server or Windows AD server). When a tenant administrator logs in to iMaster NCE-WAN, the LDAP server authenticates the tenant administrator.
When a device administrator logs in to a CPE through the CLI, the device administrator can be authenticated in either of the following modes:
  Local authentication: The tenant administrator can set passwords for device administrators on iMaster NCE-WAN, which then delivers the passwords to CPEs. When a device administrator logs in to a CPE, the CPE authenticates the device administrator.
  TACACS authentication: A CPE connects to a TACACS server through the underlay network. When a device administrator logs in to the CPE, the TACACS server authenticates the device administrator.
System Security Design
Service Security Design

## Slide 123: System Security Design: CPE Security
A CPE must have a secure system architecture and support multiple security protection measures for defending against various security threats.
A CPE must have multiple security protection capabilities on the control plane, management plane, and forwarding plane, including but not limited to the following:
  Physical security: A CPE must be able to disable the service ports, serial ports, and services that are not in use, thereby preventing attacks.
  Data security: A CPE must be able to encrypt sensitive information, such as service data, user names, and passwords, to prevent sensitive information leakage. A CPE must also control data access permissions to prevent unauthorized access to data.
  Authentication: A CPE must provide system permission control and account permission management functions to implement strict identity authentication and permission control on login behaviors. It also must support security mechanisms such as account/password protection, password complexity check, and anti-brute force cracking of passwords.
  Attack defense: A CPE must be able to defend against various network attacks, such as IP flood attacks, ICMP flood attacks, malformed packet attacks, and fragment attacks.
  Security audit: A CPE must have a comprehensive log system to log all configuration operations and abnormal status during system running for future audit.
System Security Design
Service Security Design

## Slide 124: Service Security Design: Internet Access Security
Huawei SD-WAN Solution uses the built-in security capabilities of CPEs — including ACL filtering, firewall, IPS, and URL filtering — to ensure service security, thereby flexibly meeting service security requirements in different scenarios.
Internet access traffic from the branch site and HQ site directly goes to the Internet through their respective local CPE.
Enable the firewall function on the CPEs at the branch site and HQ site to isolate internal and external networks.
MPLS
Internet
Internet access traffic from all branch sites is diverted to the HQ site and then goes to the Internet.
Enable the firewall function on the CPE at the HQ site to isolate internal and external networks.
Local Internet access
Centralized Internet access
Overlay traffic
Underlay traffic
CPE
CPE
CPE
CPE
Underlay traffic
MPLS
Internet
Branch
HQ
Branch
HQ
System Security Design
Service Security Design

## Slide 125: Service Security Design: VAS Advanced Security
In the centralized Internet access scenario, when a site accesses the Internet through a WAN-side outbound interface, a physical firewall can be deployed in off-path mode to provide VAS-based advanced security protection functions.
VAS advanced security
A physical firewall is deployed in off-path mode. It provides advanced security protection functions for centralized Internet access traffic from the site.
After VASs are deployed, centralized Internet access traffic is diverted to the physical firewall on the LAN side of the HQ CPE. After being processed by the firewall, centralized Internet access traffic then goes to the Internet through the underlay network.
CPE
CPE
Physical firewall deployed in off-path mode
CPE
Firewall
Internet
Branch
Branch
HQ
MPLS
System Security Design
Service Security Design

## Slide 126: Service Security Design: Third-Party Cloud Security
Huawei SD-WAN Solution can connect to third-party cloud security gateways (Zscaler and Forcepoint). In this way, enterprises' public cloud access traffic and SaaS traffic are sent to such gateways. Third party cloud security gateways perform security check for the traffic and provide access control, threat prevention, and data protection functions, implementing security protection.
Internet
Application scenario
CPE
CPE
SaaS cloud applications
Third-party cloud security gateway
iMaster NCE-WAN
To improve network reliability, the third-party cloud security gateway generally provides two access points to establish tunnels with the CPE, and the CPE uses GRE tunnels to connect to such access points.
  Single-gateway scenario
  One CPE establishes two GRE tunnels (active and standby) with the two access points of the third-party cloud security gateway.
  Dual-gateway scenario
  Two CPEs establish four GRE tunnels (active and standby) with the two access points of the third-party cloud security gateway.
Branch
Branch
System Security Design
Service Security Design

## Slide 127
Reliability and security design for Huawei SD-WAN Solution covers site reliability design, controller reliability design, and security design.
  Site reliability design: hub site reliability design, RR site reliability design, and IWG site reliability design.
  Controller reliability design: controller deployment reliability design and controller networking reliability design.
  Security design: system security design and service security design.

## Slide 128
(Multiple-answer question) Which of the following overlay network topology types are supported by Huawei SD-WAN Solution? ( )
  Hub-spoke
  Full-mesh
  Partial-mesh
  Hierarchical networking
(True or false) The intelligent traffic steering function can dynamically adjust data forwarding links based on link quality. ( )
  True
  False
Notes: ABCD
A

## Slide 129
Huawei SD-WAN Solution efficiently addresses the challenges facing today's WANs.
Huawei SD-WAN Solution provides abundant functions, including ZTP, flexible networking, intelligent traffic steering, and service security.
Design for Huawei SD-WAN Solution mainly covers three parts:
  Networking design: site design, tunnel design, and VPN design
  Service design: application service design and network service design
  Reliability and security design: site reliability design, controller reliability design, and security design