## Slide 1
Datacom
V1.0
He Junjian/WX580230
2020.03.06
Shi Miaomiao/swx791350
Update

## Slide 2: Data Center Network Architecture and Key Technology Application Overview

## Slide 3
Data centers (DCs) have been playing an important role since the information age. They have strong or weak connections with enterprises of various scales in all industries including Internet, finance, and education.
With the development and transformation of IT technologies, such as virtualization, cloud computing, container, and artificial intelligence (AI) technologies, DCs, as the basis for carrying enterprise services, have evolved from traditional DCs to cloud DCs.
This course describes the data center network (DCN) technology and DC solution.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the definitions of DC and DCN
  Describe the development phases of the DCN technology
  Describe key IT technologies of DCs
  Illustrate key network technologies of DCs

## Slide 5
DC and DCN Overview
Terms and Key Technologies of DCs
CloudFabric Solution and Related Technologies

## Slide 6: What Is a DC?
A DC is a complex set of facilities. It consists of the computer system and related devices (such as communications and storage devices), as well as redundant data communication connections, environmental control devices, monitoring devices, and various security devices.
A DC uses a layered architecture. Generally, L1 refers to the DC infrastructure, and L2 refers to the ICT devices in the DC.
Data center equipment room
Power distribution facilities
Cabinets + cabling system
Cooling facilities
DCN
Server
SAN
Campus
Internet
Storage
DCI
DC L1 view (infrastructure)
DC L2 view (ICT devices)
Management and
O&M center
Notes: Generally, a DC can be divided into the following layers:
  L0: civil engineering and equipment room building.
  L1: infrastructure, including equipment room decoration, power supply, cooling, and fire fighting.
  L2: IT infrastructure, including servers, storage devices, networks, and virtualization software.
  L3: application platform.
  L4: various services.
The concepts, topology, and architecture of DCs in this course are based on L2 and above.

## Slide 7: What Does a DC Have?
DC devices are classified into computing devices, storage devices, and network devices, excluding DC infrastructure.
Computing device
Server
Network device
Router
Switch
Firewall
Storage device
Storage array
Load balancer (LB)
IDS/IPS
FusionServer Pro intelligent server
TaiShan server
Atlas AI computing platform
OceanStor Dorado all-flash storage
OceanStor V5 hybrid flash storage
FusionStorage cloud storage
Cloud storage
Notes: This course uses Huawei devices as an example.

## Slide 8: Typical DC Networking
Typical DC networking consists of the DCN, storage area network (SAN), and servers.
SAN (storage array)
Storage network (FC)
Server (compute node)
DCN (IP)
Distributed storage
Server (storage node)
Notes: A DCN provides interconnection between computing units in a DC and interconnection between computing units in a DC and an external egress.
A SAN consists of storage arrays and Fibre Channel (FC) switches and is used to provide block storage. A storage network that uses the FC protocol is called an FC SAN, and a storage network that uses the IP protocol is called an IP SAN.
Distributed storage: The deployment mode of distributed storage is different from that of storage arrays. It stores data on multiple independent servers (storage nodes), which is also used for cloud storage.
Server (compute node): a server that provides computing services.

## Slide 9: DCN
A DCN provides interconnection in a DC and interconnection between a DC and an external egress.
A DCN consists of a series of network devices and is divided into different zones based on service functions.
Test environment zone
Production environment zone
Spine
Leaf
Spine
Leaf
Server
Server
Core
Server
Campus network access zone
WAN access zone
Internet access zone
Notes: Zone division for a DCN varies depending on industries and enterprises. For example, a financial DC is divided into production zone 1, production zone 2, test zone 1, test zone 2, big data zone, and operation management zone.
In this example:
  Internet access zone: is used for Internet user traffic access.
  Campus network access area: is used for enterprise campus user traffic access.
  WAN access area: connects to the WAN built by the enterprise.
  Production environment zone: connects to the production environment network.
  Test environment zone: connects to the test environment network.

## Slide 10: DCN Architecture Evolution
access
access
Access
Access
Aggregation
Aggregation
Core
Core
VRRP+STP
Stacking/M-LAG
TRILL
(Transition)
Access
Access
Aggregation
Aggregation
Core
Core
VRRP
STP
Stack
Stack
M-LAG
VXLAN
Leaf
Leaf
Spine
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
DCN 1.0: STP+VRRP
DCN 2.0: Stack/M-LAG
DCN 3.0: Spine-Leaf + VXLAN
VXLAN
Implements basic reliability
Uses VRRP master/backup gateways
STP blocks interfaces to prevent loops, resulting in low link usage
Supports inter-device link bundling for server access
Supports full load balancing among links
Limited scale
East-west Layer 3 traffic is not optimal
Supports full load balancing among links
Full spine-leaf architecture, supporting four or more spine nodes
Optimal path for east-west Layer 3 traffic
Notes: Transparent Interconnection of Lots of Links (TRILL) is a large Layer 2 technology. However, TRILL is seldom used because it is difficult to deploy.

## Slide 11: DCN 1.0: STP+VRRP
At the early stage of DCN development, no independent DCN solution is available. In this case, the typical STP+VRRP solution is used. The key points of the networking are as follows:
  Aggregation switches and access switches form a Layer 2 network, and STP is used to eliminate Layer 2 loops.
  Gateways are deployed on the aggregation switches, and VRRP is used to provide redundancy.
Core switch
Aggregation switch
Access switch
VRRP
STP
Notes: This solution solves the basic reliability problems of Layer 2 and Layer 3 switching. However, with the increase of the DC scale and service bandwidth, the following problems become increasingly prominent:
  The network throughput is low and cannot meet the increasing traffic requirements:
    The STP blocking mechanism causes low network link usage.
    The VRRP single-active gateway mechanism fails to fully unleash the device forwarding performance.
    Layer 2 traffic is forwarded along a non-shortest path. The root bridge easily becomes a bandwidth bottleneck and causes a long forwarding delay.
  The STP network scale is limited, and the convergence performance is poor.
  There are a large number of managed nodes, and the logical topology and maintenance are complex.

## Slide 12: DCN 2.0: Stacking/M-LAG
DCN 2.0 uses the stacking and M-LAG technologies to solve the STP+VRRP network problems in the DCN 1.0 phase. Both stacking and M-LAG are network virtualization technologies that implement many-to-one virtualization of devices and support inter-device link bundling. The key points of the networking are as follows:
  Aggregation layer: Devices form an M-LAG or are stacked, which function as the Layer 3 gateways. The aggregation layer and access layer are interconnected through inter-device link bundling.
  Access layer: Devices form an M-LAG or are stacked to meet the requirement that server NICs are dual-homed to two physical devices in NIC binding mode.
Core switch
Aggregation switch
Access switch
Stacking/M-LAG
Stacking/M-LAG
Notes: Regardless of whether the stacking or M-LAG technology is used, DCN 2.0 has the following characteristics:
  Traffic forwarded at Layer 2 and Layer 3 is load balanced, making full use of all links.
  Inter-device link aggregation is deployed to support protection against physical node faults.
  Compared with STP, the Layer 2 forwarding path is shorter and the delay is shorter.
  A larger Layer 2 network can be constructed.

## Slide 13: DCN 3.0: Spine-Leaf + VXLAN
DCN 3.0 uses the spine-leaf architecture and combines VXLAN and Ethernet VPN (EVPN) technologies.
VXLAN uses MAC-in-UDP packets to implement data plane encapsulation and construct IP-based overlay virtual local area networks (VLANs). Spine and leaf nodes are fully meshed.
Spine
Leaf
VXLAN+EVPN
Data plane
Overlay control plane
Overlay network (logical network)
Underlay network (physical network)
Notes: Compared with DCN 2.0, DCN 3.0 greatly improves the scalability and flexibility of service networks. DCN 3.0 has the following advantages:
  10GE NICs are mainly used on servers, and 10GE access and 40GE interconnection are used on the network.
  Network-wide resource sharing and access resource pooling in a data center are supported.
  VXLAN and EVPN technologies are used to improve link utilization.
  The spine-leaf architecture has strong horizontal scalability.
  Layer 3 ECMP networking is formed through full mesh connections to implement a non-blocking, highly reliable, high-performance, and low-latency network.
  The M-LAG technology can be used to support load balancing of Layer 3 gateways.
  The EVPN distributed gateway function is used to achieve optimal Layer 3 traffic paths.
  Outer packets are encapsulated using the common IP protocol, which facilitates network extension and reuse of assets and tools.
DCN 3.0 is recommended for DCN planning and design.

## Slide 14
DC and DCN Overview
Terms and Key Technologies of DCs
  Common Terms of DCs
  Key Services of DCs
CloudFabric Solution and Related Technologies

## Slide 15: Integrated Cabling
Integrated cabling in a DC involves three concepts: Top of Rack (TOR), End of Row (EOR), and Middle of Row (MOR).
TOR switch
Server
Server
Server
Aggregation switch
(modular)
Server
Server
Server
Server
Aggregation switch
(modular)
EOR switch
EOR switch
EOR switch
A row of cabinets
A row of cabinets
Aggregation switch
(modular)
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf
Notes: A common standard cabinet in a DC is 42 U, and the height of each U is 4.445 cm.
TOR switches are deployed on the top of a cabinet. Servers in the cabinet are connected to the TOR switches through optical fibers or network cables. The TOR switches are connected to the upper-layer aggregation switches. This distributed access mode is applicable to the scenario where there are a large number of access devices or the density of devices in a single cabinet is high. This mode reduces the number of cables between server cabinets and network cabinets, simplifying connection management. However, access switches are distributed in multiple cabinets, which is inconvenient for centralized maintenance and management of switches. This mode is common in cloud DCs.
EOR switches are deployed in one or two cabinets at the end of each row of cabinets. All servers in the row are connected to the EOR switches through horizontal cabling. This mode is common in traditional DCs. In this mode, a large number of cables are aggregated from multiple server cabinets to the network cabinet, which is difficult to manage. However, switches can be managed and maintained in a centralized way.
MOR switches are deployed in one or two cabinets in the middle of each row of cabinets. In this mode, the cabling from the server cabinet to the network cabinet is simpler than that in the EOR mode. In addition, switches are managed in a centralized manner, which is a compromise between the TOR and EOR modes.

## Slide 16: Equipment Room Modules
Take a financial DC as an example. Each floor of a building is divided into multiple equipment room modules.
Equipment room modules can be classified into the network module, storage module, open module, and test module by function. Each module has a different power supply density.
As shown in the figure, each floor is divided into three areas by power supply density: high-density area, medium-density area, and low-density area.
Network module: is responsible for network access and is the core of the WAN and LAN. The power consumption varies depending on the device type.
Storage module: stores storage devices in a centralized manner.
Open module: stores servers in a centralized manner.
Test module: stores test devices in a centralized manner.
Open
Network
Network
Open
Open
Open
Low density
High density
Medium density
Open
Extranet
Test
Open
Open
Open
Storage
Storage
Open
Open
Storage
Storage
Open
Open
Open
Open
Network
Network
Open
Network
Network
Open
Open
Open
Branch
Branch
Test
Open
Open
Open
Storage
Storage
Open
Open
Storage
Storage
Test
Test
Test
Test
Open
Open
Floor-X
Floor-Y
Floor-Z
Floor-W
Building-1
Building-2
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf
Notes: Network module: is responsible for network access and is the core of the WAN and LAN. It connects to carriers' networks and connects to branches across the country. Internally, it functions as the LAN core of the DC. The power consumption varies depending on the device type. For example, large core network devices consume high power, and LBs, firewalls, switches, and routes consumer low power.
Storage module: stores storage devices, including NAS and SAN storage devices, tape libraries, and virtual tape libraries.
Open server module: stores standard servers in a centralized manner. The servers include PC servers, blade servers, and midrange servers. Servers feature high standardization and high density.
Test module: stores test devices in a centralized manner. The test module is flexible and has lower security requirements than the production module. It can be adjusted based on the test requirements at any time. The management requirements are not high.
In the DC of a financial institution, several special types of equipment room modules can be planned for some special purposes.
Internet module: is mainly responsible for connecting to Internet applications such as e-banking, website, and e-commerce applications. It usually needs to be connected to the Internet, and is vulnerable to an attack. Therefore, the security requirements of this module are high.
Extranet module: connects to third-party companies, third-party organizations, and partner companies that have service relationships. There are a large number of interconnection private lines.
Host module: is used to deploy a host system. The device type and deployment mode of a host system are different from those of common IT devices. Therefore, a dedicated host module can be planned.
Visit modules and hosting modules can also be planned.

## Slide 17
Notes: Power supply density of equipment room modules:
Based on the power supply density, equipment room modules are classified into low-density modules (0.4–0.9 kW/m²), medium-density modules (0.9–2.5 kW/m²), and high-density modules (> 2.5 kW/m²).
  Low-density modules can be used to deploy network devices. They can be used to deploy a single cabinet for large-scale network devices (6 kW) and meet the requirements for low average power consumption of network modules.
  Medium-density modules can well meet the deployment requirements of conventional PC servers and midrange computers. A 42 U cabinet can be used to deploy 12 PC servers of 2 U (5–7 kW) or 8 PC servers of 4 U (6–7 kW) to make full use of power resources.
  High-density modules are suitable for blade servers. Three blade servers can be deployed in a 42 U cabinet. The power consumption is up to 14.3 kW, fully utilizing power resources. If PC servers are deployed in a high-density module, the maximum power utilization can reach only about 50%.
Suggestion: The area of each equipment room module is about 400 to 500 square meters. The designed area of a medium-density module is 1–2 kW/m². The number of such modules accounts for more than 70%. The number of low-density and high-density modules does not exceed 30%.

## Slide 18: PoD
To facilitate resource pooling and management in a DC, a DC can be divided into one or more physical partitions. Each physical partition is called a Point of Delivery (PoD). It is a modular entity that integrates network, storage, and computing.
PoDs can be defined based on actual service requirements:
  For a large DC, the entire equipment room can be defined as a PoD.
  For a medium DC, two or more rows of cabinets can be defined as a PoD.
  For a small DC, one or more cabinets can be defined as a PoD.
DC (Example)
PoD 1
PoD 2
Spine
Spine
Leaf
Leaf
Leaf
Spine
Spine
Leaf
Leaf
Leaf
PoD 3
Spine
Spine
Leaf
Leaf
Leaf
PoD 4
Spine
Spine
Leaf
Leaf
Leaf
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf
Notes: The PoD definition varies depending on the enterprise. For example, in the DC of a large enterprise, a PoD may be considered smaller than an equipment room. In another enterprise, a PoD consists of 48 TOR switches and four spine switches.

## Slide 19: DC Switch
DC switches generally refer to hardware switches. Its development goes through the following three phases: FE/GE access and GE uplink; GE/10GE access and 10GE/40GE uplink; 10GE/40GE access and 100GE uplink.
Phase 3: High-density 10GE/40GE access and 100GE uplink
Phase 2: High-density GE/10GE access and 10GE/40GE uplink
Phase 1: High-density FE/GE access and GE uplink
About 2000 to 2006
About 2006 to 2012
About 2012 to 2020
DC servers mainly use GE/10GE access. DC switches provide mainly GE interfaces and a few 10GE interfaces to meet the requirements of a small or medium DCN that consists of GE servers.
DC servers mainly use FE/GE access. Most DC switches mainly provide 100 Mbit/s or 1000 Mbit/s interfaces, which can meet the requirements of a DCN consisting of a small number of servers.
DC servers mainly use 10GE/40GE access. Therefore, core switches in the DC must provide high-density 10GE/40GE interfaces to meet server access requirements.
Core
Core
10GE access
40GE access
100GE access
Core
Core
100 Mbit/s access
FE access
GE access
Core
Core
GE access
GE access
10 GE access
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf
GE
10/40GE
100GE

## Slide 20: DC Switches for the AI Era
Huawei CloudEngine 16800 series switches (CE16800 for short) are DC switches built for the AI era.
  Ultra-large capacity: The CE16800 provides 734 Tbit/s switching capacity, scalable to 3096 Tbit/s. It supports 400GE smooth evolution to meet the demand for surging digital traffic in the future.
  Intelligent engine: The iLossless algorithm is used to learn and train network-wide traffic in real time, implementing network adaptation and self-optimization. Zero packet loss, E2E μs-level latency, and high throughput are achieved.
  Intelligent O&M: The CE16800 provides telemetry-based data collection in milliseconds, building a data basis for the intelligent O&M platform. The edge AI processing capability is supported to implement local fault inference.
CloudEngine 16804
CloudEngine 16816
CloudEngine 16808
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf

## Slide 21: Basic Concepts of the Spine-Leaf Architecture
Server leaf
Service leaf
Border leaf
Fabric
Spine
Concept | Description
Spine | Core node on a VXLAN fabric, which provides high-speed IP forwarding and connects to leaf nodes using high-speed interfaces.
Leaf | Access node on a VXLAN fabric, which connects various network devices to the VXLAN network.
Fabric | Basic physical network topology of a DC, comprised of a group of spine and leaf nodes.
Service leaf | Functional node that connects to L4-L7 value-added service (VAS) devices, such as firewall and LBs, to the VXLAN fabric.
Server leaf | Functional node that connects virtual and physical servers to the VXLAN fabric.
Border leaf | Functional node that connects routers or transmission devices outside a DC to the VXLAN fabric of the DC.
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf

## Slide 22: Advantages of the Spine-Leaf Architecture
Spine-leaf is a new network architecture for DCs. It consists of spine nodes and leaf nodes. A spine node is a backbone node that provides high-speed IP forwarding. A leaf node provides network access.
Leaf and spine nodes are fully meshed at Layer 3 and use ECMP to improve network availability.
The spine-leaf architecture provides high scalability.
Leaf
Leaf
Spine
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
Leaf
Spine
Spine
Leaf
Leaf
Leaf
Spine
Spine
Spine
Spine-leaf architecture
Multi-node expansion
Multi-level expansion
Integrated Cabling
Equipment Room Modules
PoD
DC Switch
Spine-Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Leaf
Notes: Characteristics of the spine-leaf architecture:
  Each leaf node (low level) is fully meshed to all spine nodes (high level).
  Nodes at the same level are not connected to each other.
  In a typical application scenario, the spine-leaf architecture functions as a logical modular switch. A leaf node functions as an LPU of the modular switch and is responsible for external traffic access. A spine node functions as the SFU of the modular switch and is responsible for traffic forwarding between leaf nodes.
The spine-leaf architecture provides high scalability:
  The number of spine nodes can be expanded to 4 or more. The maximum number of spine nodes depends on the number of uplink interfaces on leaf nodes.
  A two-level spine-leaf architecture can be expanded to a three-level spine-leaf architecture to implement high-speed data exchange between more leaf nodes.

## Slide 23
DC and DCN Overview
Terms and Key Technologies of DCs
  Common Terms of DCs
  Key Technologies of DCs
CloudFabric Solution and Related Technologies

## Slide 24: Load Balancing
Load balancing is a technology used for load distribution in a computer cluster. It uses a proxy device to receive external requests, and then distributes the requests to multiple internal servers. This proxy device is called an LB.
Layer 3 load balancing is based on IP addresses. Similarly, Layer 4 load balancing and Layer 7 load balancing are based on the IP address + port number and application layer protocol (such as HTTP), respectively.
Load balancing classification
Load balancing is classified into the following types based on technologies:
  Layer 3 load balancing, for example, router
  Layer 4 load balancing, such as LVS and HAProxy
  Layer 7 load balancing, such as Nginx and HAProxy
Load balancing is classified into the following types based on the deployment mode:
  Software load balancing
  Hardware load balancing
192.168.1.10
192.168.1.11
192.168.1.12
Virtual IP:
192.168.1.100
External request
Load balancing algorithm
Example of Layer 3 load balancing
Round robin
Least connections
Hash
Random weight
...
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG
LB
Server 1
Server 2
Server 3
Notes: The access IP address provided by the LB is called the virtual IP address in this example and is called the floating IP address (FIP) in OpenStack.
The load balancing algorithm determines the health servers to be selected. The common algorithms are as follows:
  Round robin: The LB distributes each request sequentially around the server list.
  Least connections: The LB preferentially selects the server with the least connections.
  Hash: The LB calculates a hash value based on the source IP address of a request and determines the server to which the request is distributed based on the hash value.
  Random: The LB randomly distributes traffic based the weight.

## Slide 25: Application of Load Balancing in a DC
Load balancing applications in DCs include Server Load Balancing (SLB) and Global Server Load Balancing (GSLB). The former implements load balancing among servers in a DC, and the latter implements load balancing among DCs.
The user accesses www.huawei.com and applies to the DNS server for address resolution.
The DNS server forwards the query request to the GSLB for resolution.
The GSLB selects the optimal result (service virtual IP address provided by the SLB) and sends the result to the DNS server.
The DNS server returns the result to the user.
The user accesses the virtual IP address provided by the SLB.
The SLB forwards the request to the specified server.
SLB (active)
DC A
Server cluster
GSLB
1
DNS server
2
3
4
DC B
2
5
6
GSLB
SLB (standby)
User
Server cluster
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG
Notes: GSLB is used when an enterprise has multiple DCs in different locations. Users can access the nearest DC based on their locations. There are multiple GSLB solutions. This example describes the most common DNS-based GSLB solution used in DCs.
In the GSLB solution, the domain name service provider adds a GSLB with the intelligent DNS resolution function to the Name Server (NS) record of a domain name. Then the GSLB resolves the domain name. If GSLBs are deployed in multiple locations, all of them should be added to the NS record to ensure high availability. The GSLB performs health check on backend servers and public IP addresses of other DCs. Health check results are synchronized between GSLBs in different DCs using proprietary protocols. The GSLB selects the optimal address based on the global load balancing policy and sends the address to the DNS server. The DNS server then sends the optimal address to the user.
The SLB in the DC distributes requests to application servers based on the information contained in the requests. In addition, the SLB ensures that the system selects the optimal server for processing based on the predefined policy. This improves the availability and scalability of applications to some extent.

## Slide 26: M-LAG
M-LAG is a technology that implements inter-device link aggregation. It provides device-level link redundancy. M-LAG implements load balancing as well as backup protection.
In a DC, two TOR switches negotiate to form an M-LAG in active/standby mode to connect to other devices (servers or firewalls).
Active/standby negotiation
M-LAG
TOR
TOR
Layer 2 traffic forwarding
Dual-active detection (DAD)
Server
An M-LAG is presented as one device to a server.
The server considers the connected M-LAG to be one device.
Eth-Trunk
Logical perspective
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 27: Application of M-LAG in a DC
Currently, a DCN uses the spine-leaf architecture. To meet high reliability requirements, M-LAG is recommended for server or firewall access.
Firewall
Spine
Leaf
Egress
Server
Server
M-LAG
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG
Notes: In this example, the spine node, border leaf node, and service leaf node are combined.

## Slide 28: VXLAN
VXLAN is a point-to-point Layer 2 tunneling technology that can build a Layer 2 virtual network over a physical network with reachable routes. The underlay routing network on which the VXLAN depends is not limited by the network structure and provides scalability.
A VXLAN packet contains a VXLAN Network Identifier (VNI) field, which is similar to a VLAN ID and is used to differentiate VXLANs. Generally, there is only one VXLAN tunnel between two devices. Similar to a trunk link, a VXLAN tunnel is used to carry traffic corresponding to all VNIs allowed between the devices.
IP network
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
VXLAN tunnel
NVE
NVE
VNI 5000
VNI 6000
VNI 7000
192.168.10.10-VNI5000
192.168.10.20-VNI5000
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 29: VXLAN Packet Format
Outer
Ethernet header
Outer
IP header
UDP header
VXLAN
header
Inner
Ethernet header
Inner
IP header
Payload
Original data frame
VXLAN encapsulation
VXLAN flags
(00001000)
Reserved field
VNI
Reserved field
8 bits
24 bits
24 bits
8 bits
Source UDP port
(Hash value)
Destination UDP port
(4789)
Length
Checksum
Source IP address: IP address of the source VTEP of a VXLAN tunnel
Destination IP address: IP address of the destination VTEP of a VXLAN tunnel
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG
Notes: The preceding figure shows the standard VXLAN packet format. The packet format of Huawei CloudEngine S series switches is different from the standard VXLAN packet format. The reserved fields in the VXLAN packet format are user-defined.

## Slide 30: Basic Concepts of VXLAN: NVE
Network Virtualization Edge (NVE):
  An NVE is a network entity that implements network virtualization functions. A hardware or software switch can work as an NVE.
  NVEs run VXLAN and construct a Layer 2 virtual network over a Layer 3 network. SW1 and SW2 in the figure are NVEs.
SW1 (NVE)
SW2 (NVE)
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
IP network
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 31: Basic Concepts of VXLAN: VTEP
VXLAN tunnel endpoint (VTEP):
  A VTEP is located on an NVE and performs VXLAN encapsulation and decapsulation.
  In the outer IP header of VXLAN packets, the source IP address is the IP address of the source VTEP, and the destination IP address is the IP address of the destination VTEP.
SW1
SW2
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
IP header
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
IP header
Payload
Ethernet header
Source IP address: 1.1.1.1
Destination IP address: 2.2.2.2
Original data frame
Original data frame
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG
Notes: A VXLAN tunnel is defined by a pair of VTEPs.
The source VTEP encapsulates packets and sends the encapsulated packets to the destination VTEP through the VXLAN tunnel. After receiving the encapsulated packets, the destination VTEP decapsulates the packets.
Generally, the IP address of a loopback interface on a device is used as the VTEP address.

## Slide 32: Basic Concepts of VXLAN: VNI and BD
VNI:
  VNIs are similar to VLAN IDs and are used to differentiate VXLANs. VMs in different VXLANs cannot communicate with each other at Layer 2.
  A tenant can have one or more VNIs. The VNI length is 24 bits, and a maximum of 16M tenants are supported.
BD 20
VNI2000
BD 20
VNI2000
SW1
SW2
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
IP header
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
IP header
Payload
Ethernet header
VNI: 2000
Original data frame
Bridge domain (BD):
  VLANs are used to divide broadcast domains on a traditional network. Similarly, BDs are used to divide broadcast domains on a VXLAN network. A BD identifies a large Layer 2 broadcast domain on a VXLAN network.
  VNIs are mapped to BDs in 1:1 mode. Terminals in the same BD can communicate with each other at Layer 2.
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 33: Basic VXLAN Concepts: Layer 2 and Layer 3 VXLAN Gateways
Edge1
Layer 2 gateway
Edge2
Layer 2 gateway
Border
PC1
192.168.1.1/24
PC2
192.168.1.2/24
Layer 2 gateway: allows traffic to enter a VXLAN network or is used for intra-subnet communication between terminals on the same VXLAN network.
Edge1
Layer 2 gateway
Edge2
Layer 2 gateway
Border
Layer 3 gateway
PC1
192.168.1.1/24
PC2
192.168.2.2/24
Layer 3 gateway: enables inter-subnet communication between terminals on a VXLAN network and allows terminals to access external networks (non-VXLAN networks).
VXLAN tunnel
VXLAN tunnel
VXLAN tunnel
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 34: Basic Concepts of VXLAN: VBDIF Interface
VLANIF interfaces are used for communication between broadcast domains on a traditional network. Similarly, VBDIF interfaces are used for communication between BDs on a VXLAN network.
A VBDIF interface is a Layer 3 logical interface created for a BD on a Layer 3 VXLAN gateway.
VBDIF interfaces allow users on different network segments to communicate with each other through VXLAN networks, implements communication between VXLAN and non-VXLAN networks, and connects a Layer 2 network to a Layer 3 network.
VBDIF 10
192.168.1.254
VBDIF 20
192.168.2.254
SW1
Layer 2 gateway
SW2
Layer 2 gateway
SW3
Layer 3 gateway
BD 10 (VNI 1000)
BD 20 (VNI 2000)
PC1
192.168.1.1/24
PC2
192.168.2.2/24
VXLAN tunnel
VXLAN tunnel
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 35: Basic VXLAN Concepts: Distributed and Centralized Gateways
Layer 3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
Layer 2 gateway
Layer 2 gateway
PC2
192.168.2.1/24
A Layer 3 gateway is deployed on a device. All inter-subnet traffic is forwarded through the Layer 3 gateway, implementing centralized traffic management.
Advantage: Inter-subnet traffic is managed in a centralized manner, simplifying gateway deployment and management.
Disadvantage: The forwarding path is not optimal. The ARP entry specification is a bottleneck. The centralized gateway needs to maintain ARP entries of a large number of terminals connected to the network through VXLAN.
VTEPs function as both Layer 2 and Layer 3 gateways. Non-gateway nodes are unaware of VXLAN tunnels and only forward VXLAN packets.
Advantage: VTEPs only need to learn ARP entries of terminals connected to them. Therefore, the number of ARP entries supported is no longer a bottleneck on distributed VXLAN gateways, and the network scalability is improved.
Disadvantage: The deployment, configuration, and implementation of distributed gateways are complex, and the deployment workload is heavy.
Centralized gateway
Distributed gateway
Layer 2/3 gateway
Layer 2/3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
PC2
192.168.2.1/24
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 36: VXLAN Tunnel Establishment Modes
A VXLAN tunnel is identified by a pair of VTEP IP addresses. Packets are encapsulated on a VTEP and then transmitted in the VXLAN tunnel via routing. A VXLAN tunnel can be established successfully as long as the VTEPs at both ends of the tunnel have reachable routes to each other's IP address at Layer 3.
VXLAN tunnels are classified into the following types based on the VXLAN tunnel creation mode:
  Static tunnel: The local and remote VNIs, VTEP IP addresses, and ingress replication list (head-end peer-list) are configured manually.
  Dynamic tunnel: VXLAN tunnels are dynamically established using BGP EVPN. The local and remote VTEPs establish a BGP EVPN peer relationship and then exchange BGP EVPN routes to learn the VNIs and VTEP IP addresses from each other.
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 37: Application of VXLAN in a Cloud DC
In a cloud DC, a large number of services are deployed on VMs, which can be live migrated in a server cluster. When a VM is migrated to a server connected to another leaf node, the IP address and MAC address of the VM remain unchanged. In this way, service access is not interrupted.
Spine-leaf + VXLAN is the best practice in this scenario.
OSPF
Open vSwitch
VM
VM
VM'
Open vSwitch
VM
VM
VM
Open vSwitch
VM
VM
VM
Leaf
Spine
VM migration
VXLAN tunnel
Service access
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 38: EVPN
EVPN is initially defined in RFC 7432. The MPLS-based EVPN meets the requirements for high bandwidth and complex QoS.
The virtualization technology is introduced to the cloud DC. A host can carry multiple VMs that belong to different tenants. This poses new requirements on the network, and the Network Virtualization Overlay (NVO) solution is used to solve this problem.
Huawei NVO solution uses BGP EVPN as the control plane and VXLAN tunnels as the data forwarding plane.
Control plane
EVPN MP-BGP
Data plane
Label Switching(MPLS)
IP/GRE tunnel
Control plane
EVPN MP-BGP
Data plane
VXLAN
Huawei NVO solution
MPLS-based EVPN
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 39: Telemetry
Telemetry is also called network telemetry, which is a technology that remotely collects data from physical or virtual devices at a high speed.
Compared with SNMP, telemetry has a subsecond-level collection interval. Devices periodically report information in push mode, providing real-time and high-speed data collection.
Traditional SNMP
First request
First response
Second request
Second response
Telemetry
T < 1s
Subscription and query at an interval of 1s
First response
Second response
Nth response
T > 5 minutes
"Subscription and push"
"Pull"
Load Balancing
VXLAN
EVPN
Telemetry
M-LAG

## Slide 40
DC and DCN Overview
Terms and Key Technologies of DCs
CloudFabric Solution and Related Technologies

## Slide 41: CloudFabric Solution Architecture
Application
layer
Control layer
Forwarding layer
Computing management platform
VMM
Intelligent and lossless DCN
Fabric
vSwitch
VAS pool
Network controller
iMaster NCE-Fabric
VAS controller
Multi-DC controller
MDC
WAN controller
Server pool
Multi-DC fabric
Core
WAN
Fabric gateway
NGFW/
vNGFW
Fabric gateway
DC 1
DC 2
...
Cloud OS
Cloud platform
Container platform
FabricInsight
HiSec Insight
Spine
Leaf
Third-party VAS
Third–party firewall
SecoManager
Notes: Application layer
  Cloud OS
    OpenStack-based cloud platform (open-source OpenStack or Huawei FusionSphere): collaboratively manages computing, storage, and network resources.
    Container provisioning platform: creates and provisions containers.
  Analyzer: iMaster NCE-FabricInsight (FabricInsight for short) is used to analyze the network and application health status of DCNs. HiSec Insight, an advanced threat analysis system, can effectively collect massive basic network data, such as traffic on the network and network status and security logs of various devices. Through real-time and offline big data analysis, HiSec Insight can effectively detect potential threats on the network based on machine learning technologies, expert reputation, and intelligence drive, implementing network-wide security situational awareness.
Control layer
  Computing management platform: The Virtual Machine Management (VMM) implements virtualization and resource management at the computing layer.
  Network controller: iMaster NCE-Fabric is used to centrally manage and control cloud DCNs. It provides automatic mapping from applications to physical networks, resource pool deployment, and visualized O&M, helping customers dynamically schedule service-centric network services.

## Slide 42
Notes:   VAS controller: The SecoManager implements centralized security policy management and control for firewalls, monitors events in real time, comprehensively analyzes security events such as attacks, and provides statistical reports in different formats. These benefits help customers understand the network security status at any time.
  Multi-DC controller (MDC) and WAN controller (DCI link optimization)
Forwarding layer
  Network device
    Physical switches use CloudEngine (CE for short) series. They are high-performance cloud switches designed for next-generation DCs and support extensive DC and campus service features.
    The virtual switch uses Huawei CloudEngine 1800V (CE1800V for short). The CE1800V is an intelligent software switch designed for virtualization environments of enterprises and industry DCs.
  VAS device
    Huawei next-generation firewall (NGFW) or virtual NGFW (vNGFW) provides NAT, VPN, virtualization, and multiple security features for DCs.
    The load balancer (LB) flexibly load balances services for DCs.
    Third-party VAS devices can be deployed in DCs, and traffic can be diverted to them.

## Slide 43: Huawei CloudFabric Solution Scenarios
Scenario 2: Network Virtualization - Computing
Scenario 3: Cloud-network integration
Third-party computing virtualization management platform
Container platform
Scenario 4: Container network
iMaster
NCE-Fabric
The cloud platform provides a unified interface for managing computing, storage, and network resources.
The cloud platform delivers network services through iMaster NCE-Fabric.
The container platform provides a unified interface for managing computing and network resources.
The container platform delivers network services through iMaster NCE-Fabric.
The network administrator uses iMaster NCE-Fabric to configure the network.
After detecting that a VM goes online, the network automatically configures a logical port for connecting to the VM.
Cloud platform
iMaster
NCE-Fabric
iMaster
NCE-Fabric
Scenario 1: Network Virtualization - Hosting
No computing platform or cloud platform is available. The network administrator uses iMaster NCE-Fabric to provision network services.
iMaster
NCE-Fabric

## Slide 44: Huawei CloudFabric Solution: Network Virtualization - Hosting Scenario
In this scenario, no computing virtualization platform is connected, and network administrators directly deliver network resources and services.
Network Virtualization - Hosting has the following characteristics:
  Service automation: iMaster NCE-Fabric automatically delivers network configurations and provides multi-path detection, single-path detection, network connectivity detection, and pre-orchestrated emergency plans to implement fast fault locating and isolation.
  Self-service: iMaster NCE-Fabric provides service operation portals and open APIs. Users can develop service portals and provide self-service capabilities for tenants to quickly deploy and adjust services.
  Large Layer 2 network: The VXLAN overlay technology is used to build a large Layer 2 network, improving resource utilization.
Control
layer
Forwarding layer
Computing management platform
VMM
Fabric
vSwitch
VAS pool
Network controller
iMaster NCE-Fabric
VAS controller
SecoManager
Server pool
NGFW/
vNGFW
FabricInsight
HiSec Insight
Spine
Leaf
Hosting
Computing
Cloud-Network Integration
Container Network Association
Third-party VAS

## Slide 45: Virtualization: Basic Concepts
Virtualization is a technology with which you can virtualize a computer into multiple virtual machines (VMs). The VMs can run different operating systems, so that they run independently without affecting each other, thereby significantly improving the computer utilization.
The core component of service virtualization is the virtualization software layer (Hypervisor). It allows multiple VMs to run on the same server.
Physical server
Hardware
Host machine
VM monitor
Hypervisor
VM
Guest machine
OS
Guest OS
Application
Guest OS: VM OS
Guest machine: VM
Hypervisor: virtualization software layer, also called VM monitor
Host OS: OS running on a physical machine
Host machine: physical machine
Hardware
Host machine
OS
Host OS
Application
Common virtualization technologies in the industry include:
Open-source technologies: Xen and KVM
Closed-source technologies: Microsoft Hyper-V, VMware ESXi, and Huawei FusionSphere
Physical server
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: Multiple virtualization technologies including computing, storage, and network virtualization are required to implement virtualization:
  Computing virtualization: includes CPU, memory, and I/O virtualization. CPU virtualization technologies include Intel VT-x and AMD-V. Memory virtualization technologies include shadow page table and extended page table (EPT). I/O virtualization technologies include QEMU simulation, Virtio, and SR-IOV.
  Storage virtualization: For example, Huawei FusionCompute implements storage virtualization using the high-performance virtual cluster file system VIMS.
  Network virtualization: is implemented through virtual switches. For example, Huawei FusionCompute implements network virtualization using distributed virtual switches (DVSs).

## Slide 46: Virtualization: Virtualization Management Platform
When there are multiple virtualized servers, a platform is needed to centrally manage and control them, that is, virtualization management platform.
A virtualization management platform manages virtual resources, such as VMs, virtual switches (vSwitches), and cluster file systems, and provides GUIs for performing operations on these resources, such as creating VMs and vSwitches and adding data stores.
Mainstream virtualization platforms in the industry include Huawei VRM, VMware vCenter, and Microsoft System Center.
(VRM/vCenter/System Center)
Virtualization management platform (physical or virtual machine)
LAN
Administrator
VM
VM
VM
vSwitch
VM
VM
VM
vSwitch
Server
Server
VM
VM
VM
Server
Compute cluster management
VM management
Virtual network management
Data storage management
...
vSwitch
Hosting
Computing
Cloud-Network Integration
Container Network Association

## Slide 47: Virtual Network: vSwitch
vSwitch is a software switch deployed on a server. It is mainly used to implement communication between virtual interfaces on a server.
Common vSwitches in the industry include the open-source Open vSwitch, Huawei CE1800V, and VMware vSphere Standard Switch.
Server
NIC 1
vSwitch 1
VM 0
VM 1
NIC 2
VM 2
TOR
vSwitch 2
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: Open vSwitch (OVS) is an open-source project of Apache 2.0. It is a virtual switch running on a virtualization platform (such as KVM and Xen) and is the mainstream virtual switch in the industry. Strictly speaking, OVS is a DVS.
vSwitches provide various functions. For example, OVS provides Layer 2 switching for dynamically changed endpoints to control access policies, isolate networks, and monitor traffic on virtual networks.

## Slide 48: Virtual Network: DVS
DVS provides virtual network functions across hosts to meet VM migration requirements. VM migration requires that the network status (such as the VLAN, IP address, and network policy) remain unchanged after the migration. Common vSwitches cannot meet this requirement.
In this example, after VM 2 is migrated to VM 2', its network status remains unchanged.
Port group
Uplink
DVS provides two types of virtual interfaces:
Port group: is used to bind VM NICs and add different VLAN tags to VM traffic.
Uplink: is used to select a physical network port to be bound to guide traffic forwarding.
Server 1
Server 2
DVS 2
DVS 1
VM 1
VM 2
VM 2'
VM 3
TOR switch
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: DVS is the distributed virtual switch on the Huawei virtualization platform VRM.
In vCenter, vSphere Distributed Switch (VDS) is used.
Huawei CloudFabric Solution supports interconnection with mainstream virtualization platforms.

## Slide 49: Huawei CloudFabric Solution: Network Virtualization - Computing Scenario
In this scenario, a computing virtualization platform is connected and no cloud platform is connected. iMaster NCE-Fabric and the computing management platform deliver services.
Network Virtualization - Computing has the following characteristics:
  Service automation: Network devices are managed by the controller and are interconnected with the VMM to implement automatic network service deployment. This shortens the deployment period of traditional networks to minutes.
  Elastic resource pooling: VXLAN overlay network virtualization and SFC technologies are used to virtualize network forwarding resources and service resources into pools. This improves the flexibility and scalability of the network framework and allows the framework to evolve.
  Refined O&M: The application, logical, and physical networks are visible, the service quality is visible and controllable, and the network status is visible. The solution provides multiple fault location and O&M methods, such as multi-path detection, single-path detection, network connectivity detection, and pre-orchestrated emergency plan. It implements fast fault location and isolation based on iMaster NCE-FabricInsight.
Control layer
Forwarding layer
Computing management platform
VMM
Fabric
vSwitch
VAS pool
Network controller
iMaster NCE-Fabric
VAS controller
SecoManager
Server pool
NGFW/
vNGFW
FabricInsight
HiSec Insight
Spine
Leaf
Third-party VAS
Hosting
Computing
Cloud-Network Integration
Container Network Association

## Slide 50: OpenStack Overview
OpenStack is an open-source cloud operating system that controls large pools of computing, storage, and network resources throughout a DC. After OpenStack is deployed, users can manage resources through the web UI, CLI, or APIs.
OpenStack is not a cloud computing platform, but a key component of cloud computing. OpenStack is designed for resource management and can be used to manage computing, storage, and network resource pools of heterogeneous vendors.
Hardware and DC infrastructure
Cloud OSS
Cloud console
Cloud BSS
Cloud services
Cloud platform
Resource pool
OpenStack
...
Resource pool
Resource pool
Cloud computing architecture
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: FusionSphere OpenStack is Huawei's commercial release with a built-in Huawei KVM virtualization engine.

## Slide 51: OpenStack Overview: Core Projects
OpenStack consists of multiple projects. These projects are independent of each other and implement different functions.
Core projects related to resource management on OpenStack:
  Nova: manages compute resources.
  Cinder: manages block storage resources.
  Neutron: manages network resources.
The cloud platform connects to the cloud management platform. Cloud management functions include tenant-oriented operation, cloud service provisioning, accounting, and multi-cloud monitoring.
OpenStack
Nova (computing)
Cinder (block storage)
Neutron (network)
Compute resource pool
Server
Server
Server
Storage resource pool
Server
Disk array
Network resource pool
Switch
Firewall
Other
SDN controller
Virtualization management platform
Cloud management platform
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: In the HUAWEI CLOUD Stack (HCS) architecture, ManageOne functions as the cloud management platform, which provides refined operation, intelligent O&M, and centralized management.
FusionSphere OpenStack is Huawei's commercial release with a built-in Huawei KVM virtualization engine.
Nova: is a core component of OpenStack. It provides virtual compute resources for OpenStack and manages the lifecycle of VMs, including creating, modifying, and deleting VMs.
Cinder (block storage): is an indispensable component in the virtual infrastructure and is the basis for storing VM image files and data used by VMs.
Neutron: is a core component of OpenStack and provides network services for it. Neutron enables OpenStack to flexibly divide physical networks and provide an independent network environment for each tenant in multi-tenancy scenarios.
In the Huawei CloudFabric Solution, Neutron interconnects with the SDN controller to manage hardware network resources.

## Slide 52: Neutron's Core Network Models
Neutron provides network services for OpenStack and has three core network models: network, subnet, and port.
Network: indicates a Layer 2 network. It describes basic network information, such as the name and creation time.
Subnet: indicates a network segment, for example, 192.168.10.0/24. A subnet is associated with a network.
Port: indicates a virtual port. A MAC address and an IP address are defined on the port. The IP address is obtained from the subnet.
Port
Subnet
Port
Port
Subnet
Port
Network
Subnet
Port
1:N
1:N
Hosting
Computing
Cloud-Network Integration
Container Network Association

## Slide 53: Huawei CloudFabric Solution: Cloud-Network Integration Scenario
In this scenario, the cloud platform provides a unified computing and network management interface. iMaster NCE-Fabric interconnects with the cloud platform.
Cloud-network integration has the following characteristics:
  Service automation: Network devices are managed by the controller and are interconnected with the cloud platform and VMM to implement automatic network service deployment. This shortens the deployment period of traditional networks to minutes.
  Elastic resource pooling: VXLAN overlay network virtualization and SFC technologies are used to virtualize network forwarding resources and service resources into pools. This improves the flexibility and scalability of the network framework and allows the framework to evolve.
  Refined O&M: The application, logical, and physical networks are visible, the service quality is visible and controllable, and the network status is visible. The solution provides multiple fault location and O&M methods, such as multi-path detection, single-path detection, network connectivity detection, and pre-orchestrated emergency plan. It implements fast fault location and isolation based on iMaster NCE-FabricInsight.
Application
layer
Control layer
Forwarding layer
Computing management platform
VMM
Fabric
vSwitch
VAS pool
Network controller
iMaster NCE-Fabric
VAS controller
SecoManager
Server pool
NGFW/
vNGFW
Cloud OS
FabricInsight
HiSec Insight
Spine
Leaf
OpenStack
FusionSphere
Third–party firewall
Third-party VAS
Hosting
Computing
Cloud-Network Integration
Container Network Association

## Slide 54: Container Overview
A container is a virtual instance. The kernel of an operating system can contain multiple isolated user spaces. Compared with VMs, containers provide more lightweight and process-level isolated spaces.
An advantage of containers is that applications and their running environments can be packaged into containers. This allows applications to be quickly "transported", greatly simplifying the "development -> test -> deployment -> O&M" process.
You only need to develop standard transport methods, and do not need to pay attention to the contents in containers.
Hosting
Computing
Cloud-Network Integration
Container Network Association
Container
filesystem
running job
Notes: On Linux, the kernel space is distinguished from the user space. The Linux OS and drivers run in the kernel space, and applications run in the user space.
A container is a runtime instance of an image.
Container image
  An application and its dependencies (including all files and directories of the complete OS) can be packaged into an image.
  The image contains all dependencies required for application running. You only need to run the image in the isolated sandbox without any modification or configuration.
  Images focus on packaging applications and their runtime environments in a unified format. This ensures high consistency between the local environment and the cloud environment.

## Slide 55: Comparison Between Containers and VMs
Compared with VMs, containers share the kernel of an operating system, and therefore are less independent, and only process-level isolation is provided.
The startup speed, running performance, and server resource usage of containers are higher than those of VMs.
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Bins/Libs
Bins/Libs
Bins/Libs
Web
DB
App
Server
Host OS
Bins/Libs
Bins/Libs
Bins/Libs
Web
DB
App
Container engine
VM
Container
Hosting
Computing
Cloud-Network Integration
Container Network Association

## Slide 56: Container Orchestration: Kubernetes
Container orchestration is used to manage a series of operations for defining, creating, and configuring a container. Technically, large-scale applications of containers need to be centrally managed and scheduled by the container orchestration engine. Commercially, users are willing to pay for the tools with platform capabilities, because users' services or applications need to be deployed on a platform.
Kubernetes is an open-source project initiated by Google. It aims to manage containers across hosts and provide basic deployment, maintenance, and application scaling. A Kubernetes cluster consists of the master node (master) and compute nodes (node).
  The master node provides the cluster's control plane and makes global decisions about the cluster, such as scheduling. Generally, user containers do not run on the master node.
  There are many compute nodes in a cluster, which are used to run containerized applications. The master node installs kubelet on each compute node as the agent for managing the node.
Node
Master
Node
Fabric
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: Kubernetes is an open-source container scheduling platform across host clusters. It can manage various underlying containers. It is similar to OpenStack, which manages a large number of virtual nodes at the bottom layer to form a large cluster to provide cloud services. Kubernetes provides a container-centric architecture by managing the underlying container nodes and automating deployment, scaling, and operations of application containers.
In terms of container technology development, the major orchestration platforms include Docker's Swarm, Apache's Mesos (initially developed by AMPLab of the University of California, Berkeley), and Google's Kubernetes. Kubernetes (K8S) has become the standard of container management platforms.

## Slide 57: Challenges to the Container Network
Large-scale container deployment poses new challenges to SDN networks, including the control plane and the forwarding plane.
Challenges to the control plane of the container network
Challenges to the forwarding plane of the container network
Scalability: Containers can be quickly started or stopped, which brings configuration changes of a large number of access points. Therefore, the container network must have good scalability to meet current and future requirements.
Automation: Containers occupy only a few resources and frequently and rapidly go online and offline. Therefore, the solution needs to support large-scale provisioning of cluster container networks. A single open-source Kubernetes cluster supports a maximum of 5,000 compute nodes and 150,000 PoDs. DCs should provide higher performance in management scale and forwarding capability. The container network must support high concurrency and quick provisioning so that containers can be started in seconds. Otherwise, containers may be started before the network is connected.
Service orchestration and O&M: The container network requires flexible access control, and inter-fabric interconnection requires orchestration by the SDN controller.
Security: Containers running on the same host share the same kernel. As a result, the isolation between containers is much lower than that between VMs provided by a hypervisor. This is a limitation of container technology and brings security risks.
A Kubernetes cluster has a large amount of east-west traffic. Typical scenarios involve intra-host and inter-host communication across PoDs. This imposes high requirements on the forwarding performance of vSwitches on servers.
A Kubernetes service is an abstraction layer that defines a logical set of PoDs at the backend. Therefore, Kubernetes compute nodes must implement high-performance service proxy and load balancing.
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: A container network can be deployed independently or associated with a physical network.

## Slide 58: Huawei CloudFabric Solution: Association Between the Container Network and the Physical Network
In this scenario, iMaster NCE-Fabric and the container orchestration platform deliver services.
Association between the container network and the physical network has the following characteristics:
  Service automation: The containers on the container network can be quickly started and the network has good scalability, meeting future requirements.
  Refined O&M: The application, logical, and physical networks are visible, the service quality is visible and controllable, and the network status is visible. The solution provides multiple fault location and O&M methods, such as multi-path detection, single-path detection, network connectivity detection, and pre-orchestrated emergency plan. It implements fast fault location and isolation based on iMaster NCE-FabricInsight.
Application
layer
Control
layer
Forwarding layer
Computing management platform
VMM
Fabric
vSwitch
VAS pool
Third-party
firewall
Network controller
iMaster NCE-Fabric
VAS controller
SecoManager
Third-party VAS
Server pool
NGFW/
vNGFW
Kubernetes master
FabricInsight
HiSec Insight
Spine
Leaf
LB ctrl
K8S node
Hosting
Computing
Cloud-Network Integration
Container Network Association
Notes: The LB ctrl plug-in is deployed on the Kubernetes master node to listen to the service and ingress object events of the API server and deliver the L4-L7 service orchestration configuration to LBs.

## Slide 59: iMaster NCE-FabricInsight Intelligent O&M Solution
Based on Huawei-developed big data analytics platform, iMaster NCE-FabricInsight (FabricInsight for short) receives data from network devices in telemetry mode and uses intelligent algorithms to analyze network data.
The overall architecture of FabricInsight consists of three parts: network devices, FabricInsight collector, and FabricInsight analyzer. In standard clustering deployment of FabricInsight, the analyzer and collector are combined. That is, no independent collector server needs to be deployed. FabricInsight uses the microservice architecture. Each service is deployed in multi-instance mode, which features high reliability and scalability. The system management capacity can be expanded by adding instance nodes.
FabricInsight
Fabric
Applications
Security policy application
APM application
Data visualization application
APIs
Network telemetry
Big data analytics platform
Spark
Druid
Kafka
HDFS
Fabric state database
Flow state database
AI engine
Machine learning algorithm library
Machine learning framework
Intelligent analysis system
Notes: Network devices
  Network devices include Huawei CloudEngine switches and NetEngine routers. For details about the models and supported specifications, see the specification list of the corresponding version.
  These devices use telemetry to report performance metrics such as interface traffic based on Google Remote Procedure Call (gRPC). Devices are connected to FabricInsight as gRPC clients. Users can run commands to configure the telemetry sampling function on the devices. The devices then proactively establish a gRPC connection with the target collector and send data to the collector. The current version supports the following sampling metrics: CPU and memory usage of devices and boards; number of sent and received bytes, number of discarded sent and received packets, and number of sent and received error packets of interfaces; number of congested bytes of queues; packet loss behavior data. For details about metrics and device models, see the product specification list.
FabricInsight collector
  The FabricInsight collector receives data reported by network devices in telemetry mode, including performance metric data reported through gRPC. The collector parses the metrics, combines and compresses the metric data, and reports the data to the analyzer.
FabricInsight analyzer
  The FabricInsight analyzer receives performance metrics from switches. In addition, the FabricInsight analyzer establishes dynamic baselines for some performance metrics based on the AI algorithm, detects exceptions, and displays the analysis result on the GUI.

## Slide 60: "1-3-5" Troubleshooting: AI + Knowledge-based Inference
Collection
Analysis
Decision
Holographic data of DCs
Service flow data,
Telemetry data, etc.
Root cause analysis
Knowledge-based inference engine
Intelligent analysis engine
Manual recovery
Huawei 30+ years'
O&M experience
Continuous learning and training
based on real site faults
Model application
Risk prediction
Anomaly detection
Intent-based troubleshooting in a closed-loop manner
Data cleansing
BGP
OSPF
IS-IS
……
BFD
STP
AI-powered anomaly identification
Network object modeling
iMaster NCE-FabricInsight
iMaster NCE-Fabric
Knowledge point 1
Knowledge point 2
Knowledge point 3
Knowledge point 4
Notes: "1-3-5" troubleshooting: Faults can be detected within 1 minute, located within 3 minutes, and rectified within 5 minutes.

## Slide 61
(Short-answer question) What is a DC?
(Single-answer question) Which of the following protocols is used as the control plane in the Huawei CloudFabric Solution? ( )
  VLAN
  VXLAN
  EVPN
  VRRP
Notes: A DC is a complex set of facilities including buildings. It not only includes the computer system and related devices (such as communications and storage devices), but also includes redundant data communication connections, environmental control devices, monitoring devices, and various security devices.
C

## Slide 62
DCN has evolved from DCN 1.0 and DCN 2.0 to DCN 3.0. Currently, the spine-leaf architecture is typically used together with VXLAN and EVPN.
DCs carry many mission-critical IT services, including virtualization, cloud computing, distributed storage, and AI applications. Knowing these services helps you better understand DCN technologies.
Key DCN technologies include load balancing, M-LAG, VXLAN, EVPN, telemetry, and intelligent O&M.
This course provides an overview of the preceding contents to help you get a preliminary understanding of DCs.