## Slide 1
Datacom
V1.0
Wu Yue/WWX291773
2021.5.12
Lu Yueyue/LWX445705
New

## Slide 2: Enterprise Bearer WAN Design

## Slide 3
The enterprise bearer WAN is also called the enterprise backbone WAN, which is used for interconnection between enterprise branches, between enterprise branches and clouds, and between clouds.
In the past, the enterprise bearer WAN only needs to forward traffic. However, as growing enterprise services depend increasingly on the network, service SLA assurance requirements are imposed on the network.
To meet service requirements, the enterprise bearer WAN has employed various new technologies, which complicates the O&M and design of the bearer WAN.
This course describes the technologies and network design roadmap of the bearer WAN based on Huawei's CloudWAN solution.
Notes: This course is based on Huawei's CloudWAN solution.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the challenges faced by the enterprise bearer WAN.
  Describe the basic functions of Huawei's CloudWAN solution.
  Describe the basic design roadmap of the enterprise bearer WAN.
  Describe the tunnel and VPN design roadmap of the enterprise bearer WAN.
  Describe the SLA and reliability design roadmap of the enterprise bearer WAN.
  Describe the optimization and O&M design roadmap of the enterprise bearer WAN.

## Slide 5
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 6: Enterprise Bearer WAN Overview
Bearer WANs can be classified into IP bearer networks and transmission bearer networks by network layer. For most enterprises, transmission bearer networks cannot be built by themselves (optical fiber layout requires qualification certificates). Therefore, they usually lease transmission lines from carriers. An enterprise can build its own IP bearer network over the transmission bearer network.
The IP bearer network built by an enterprise is called the enterprise bearer WAN, which is also called the enterprise backbone network or enterprise core network.
The enterprise bearer WAN carries the enterprise's internal cross-region interconnection services, such as synchronization services between data centers and voice services between enterprise branches and the HQ.
Transmission bearer network
Branch site
Branch site
Data center
HQ
IP bearer network
Notes: The bearer WAN mentioned in this course mainly refers to the IP bearer WAN.

## Slide 7: Enterprise Bearer WAN Architecture
While the bearer WANs of different enterprises vary greatly in scale and actual topology, their architecture can be generally divided into the access, aggregation, and core layers.
Branch site
Branch site
Data center
HQ
Access layer:
provides access for enterprise sites in different regions or different types of services.
Aggregation layer:
Aggregates traffic by service type or geographical location and then transmits aggregated traffic to the core backbone network.
Access layer
Aggregation layer
Core layer
Core layer:
serves as the top-layer interconnection area to provide high-speed mutual access between services.

## Slide 8: Development Trend of the Enterprise Bearer WAN
The emergence of new technologies such as cloud computing and big data promotes the development of enterprise services and poses new requirements on enterprise bearer WANs.
  Multi-network convergence
  Flexible multi-service bearer
  High reliability
  Easy O&M
Production bearer network
Office bearer network
Branch site
Branch site
Data center 1
HQ
Data center 2
Easy O&M
NMS/Controller
High reliability
Flexible multi-service bearer
Converged bearer network
Multi-network convergence
Notes: Multi-network convergence:
  The bearer network uses one physical network to carry production, office, and other services. Powerful BGP routing policies are used to control traffic on the bearer network. Traffic diversion policies are deployed based on service attributes so that different types of services, such as production and office services, can run on different paths based on the customized policies.
Flexible multi-service bearer:
  As multiple services are migrated to the cloud and multiple networks are converged, issues such as low network resource utilization and unbalanced traffic distribution become more prominent. The segment routing technology can be used to flexibly plan paths to carry traffic, improving network utilization.
High reliability:
  Reliability is classified into network reliability and service reliability.
  Network reliability is ensured from aspects such as network architecture and network stability.
  Service reliability is mainly ensured by optimizing network bandwidth, delay, and packet loss rate based on service requirements.

## Slide 9
Notes: Easy O&M:
  Topologies, events, configurations, service provisioning, and link quality are managed in a unified manner.
  The import of traffic into tunnels, tunnel bandwidth, paths, and node traffic are dynamically controlled.
  Application data flows are visible, analyzable, and predictable.

## Slide 10: Challenges Faced by Enterprise Bearer WANs
The development trend of the enterprise bearer WAN brings many challenges.
  Multi-network convergence
    Challenge: It is difficult to isolate multiple services.
  Flexible multi-service bearer
    Challenge: Network resource planning is not precise enough, and traffic path planning and deployment are difficult.
  High reliability
    Challenge: Fast convergence cannot be implemented in all scenarios, and service SLA cannot be effectively guaranteed.
  Easy O&M
    Challenge: Precise traffic path optimization and visualized O&M cannot be provided.
Branch site
Data center 1
HQ
Data center 2
NMS/Controller
Difficult multi-service isolation
Flawed path planning
Path optimization not accurate enough
Fast network convergence not possible in some scenarios
Visualized traffic O&M not possible
Difficult traffic path deployment
Type 1 service forwarding path
Backup type 1 service forwarding path
Type 2 service forwarding path
Type 3 service forwarding path
Notes: Multi-service isolation:
  Due to the convergence of multiple networks, the originally physically isolated production and office networks are now carried on the same network. The service isolation requirements of some enterprises can be met using the VPN technology. However, for other enterprises, services need to be isolated using hard pipes.
Network resource and traffic path planning:
  To make full use of network resources (mainly bandwidth), network traffic needs to be planned. Traditional traffic engineering (mainly MPLS-TE) has many disadvantages, such as complex configuration and flawed path computation mechanism. Therefore, it cannot effectively solve the problem in multi-service bearing.
Fast network convergence and service SLA assurance:
  Traditional networks usually use FRR to shorten the convergence time. However, FRR based on the LFA or RLFA algorithm has restrictions in application scenarios and may fail to meet the high reliability of some networks.

## Slide 11
Notes: Traffic path optimization and visualized O&M:
  Traditional enterprise WANs mainly use the NQA technology to measure network quality. However, the NQA technology cannot precisely reflect the actual network situation. As a result, traffic paths cannot be effectively optimized.
  Traditional network management software cannot perform end-to-end traffic monitoring based on services, and therefore cannot implement visualized O&M for traffic.

## Slide 12: Solutions to Challenges Faced by the Enterprise Bearer WAN
To address challenges faced by the enterprise Bearer WAN, Huawei provides the CloudWAN solution.
  Difficult multi-service isolation
    Network slicing technology is deployed to carry different services over different slices.
  Difficult traffic path planning and deployment
    Based on SR, the controller plans paths globally and automatically deploys paths.
  Lack of fast network convergence and service SLA assurance
    TI-LFA is used for backup path computation, and TI-LFA works with FRR and HSB technologies for fast network convergence.
  Difficult traffic path optimization and lack of visualized O&M
    TWAMP and iFIT are used to precisely detect network quality, facilitating accurate traffic optimization.
High-bandwidth slice
Low-delay slice
Default slice
SR-based path planning
Network slicing for service isolation
Voice service
Cloud service
Internet access service
TI-LFA-based backup path computation
TWAMP/iFIT
TWAMP or iFIT for network performance detection

## Slide 13
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 14: Huawei CloudWAN Solution Overview
E2E SRv6
Backbone/DCI
Metro
Metro
B2C
B2B
B2H
Enterprise private line
Vertical industries
CloudVR
Online gaming
4K/8K video
Internet
Analyzer
Manager
Controller
NETCONF/YANG
Telemetry
Simplified architecture, intelligent connection, intelligent O&M
Solution highlights
A unified platform is provided for all scenarios, including broadband, private line, data center egress, IGW, and BNG service scenarios.
2. New protocol: SLA assurance and committed delay
4. New O&M: AI-powered intelligent O&M, visualizing service quality
SRv6 shortens the TTM and ensures committed delay.
iMaster NCE-IP + iFIT, hop-by-hop packet loss detection
TI-LFA, enabling E2E switching within 50 ms
Zero preemption between FlexE-based slices, ensuring bandwidth
Network slicing granularity (1 Gbit/s at least)
3. New pipe: FlexE-based hard slicing, ensuring bandwidth
Common services
VIP services
1. New platform: NetEngine series routers with large capacity and full-service support
Solution Overview
Application Scenarios
Main Functions
Notes: TI-LFA: Topology-Independent Loop-free Alternate
BNG: broadband network gateway
TTM: time to market

## Slide 15: Huawei iMaster NCE-IP Architecture
Manager & Controller
NBIs
Network devices
Apps
Basic apps
Value-added apps
Mobile bearer apps
RESTful
SNMP
XML
CORBA
FTP
Analyzer
Service management
MPLS optimization
PCEP
SBIs
NETCONF
Telnet
SNMP
BGP-LS
FTP
NE management
IP optimization
BGP-LS
Slice management
Centralized path computation
Route flooding
Third-party device adaptation
Southbound programming framework
Traffic forecast
Big data engine
Simulation analysis
Traffic analysis
Fault diagnosis
Anomaly detection
SLA monitoring
Telemetry
ATN
NE
CX
Unified portal
Solution Overview
Application Scenarios
Main Functions
Notes: Based on the cloud platform, iMaster NCE-IP provides three logical modules (Manager, Controller, and Analyzer) and various scenario-specific applications to achieve flexible modular deployment based on customer requirements.

## Slide 16: CloudWAN Product Overview
Internet
Cl
Cloud
Access
Metro
Backbone
ATN series mobile bearer routers
NE series metro routers
NE and CX series cloud backbone routers
Solution Overview
Application Scenarios
Main Functions
Notes: Huawei has all-scenario SRv6 product capabilities and can provide access, metro, and backbone network routers for carriers and enterprises.

## Slide 17: Main Functions of Huawei's CloudWAN Solution
Huawei's CloudWAN solution mainly provides the following functions:
  Automatic planning and deployment of forwarding paths
  Real-time network performance monitoring and intelligent traffic optimization
  Network slicing for isolated traffic forwarding
  Visualized O&M for quick fault locating
Solution Overview
Application Scenarios
Main Functions
Branch site
HQ
IP bearer network
Southbound channels
Automatic path planning
Automatic path deployment
Visualized O&M
Primary path
Backup path
Low-delay slice
Default slice
Network slice

## Slide 18: Path Planning and Deployment Overview
Traditional traffic engineering (MPLS TE) encounters problems such as inaccurate path computation and difficult forwarding path deployment during path planning and deployment.
To solve the problems of traditional traffic engineering, Huawei's CloudWAN solution uses the SDN controller and SR to optimize path computation and simplify forwarding path deployment.
SR is used to plan and deploy forwarding paths as follows:
  Devices use BGP-LS to report network topology information to the controller, which then generates forwarding paths based on requirements.
  The controller uses PCEP or BGP SR-Policy to deliver computed paths to devices.
  Target traffic travels along delivered paths.
Solution Overview
Application Scenarios
Main Functions
RR
PE1
PE2
P1
PE4
PE3
BGP-LS
BGP SR-Policy/PCEP
Network administrator
2
Inputs requirements.
Automatically plans paths.
3
Reports network topology information.
1
Deploys forwarding paths.
4
Notes: BGP-LS is a new method of collecting network topology information, which makes topology information collection simpler and more efficient. Using BGP-LS to report topology information has the following advantages:
  Requirements on the computing capability of the upper-layer controller are lowered, and there is no requirement on the IGP capability of the controller.
  BGP summarizes the topology information of each process or AS and directly sends the complete topology information to the controller, facilitating path selection and calculation.
  All topology information on the network is sent to the controller through BGP, unifying the protocols for sending topology information.
BGP SR-Policy delivers data forwarding path information to the headend through the BGP route. The headend then directs traffic to a specific SR Policy. Segment lists in SR Policies are used to guide traffic forwarding. A segment list is calculated based on a series of optimization objectives and constraints, such as delay, affinity, and SRLG.
SR Policy is the mainstream SR implementation mode.

## Slide 19: Network Performance Monitoring and Optimization
As networks carry increasingly more enterprise services, they need to meet increasingly higher requirements. As such, a fast, flexible IP network performance measurement tool is required to monitor network performance in a timely manner.
Huawei's CloudWAN solution uses TWAMP and iFIT to precisely and quickly measure historical and real-time network performance.
Based on real-time network performance, the controller can optimize the network through PCEP or BGP SR-Policy.
Solution Overview
Application Scenarios
Main Functions
RR
PE1
PE2
P1
PE4
PE3
BGP SR-Policy/PCEP
The controller optimizes forwarding paths based on network performance.
The controller delivers optimized forwarding paths.
SNMP/FTP/Telemetry
TWAMP/iFIT
Severe packet loss occurs on links.
TWAMP or iFIT is used to measure network quality.
1
2
Devices report network performance data to the controller.
3
4
5
Notes: TWAMP is a standard protocol and can be deployed on IP, MPLS, and L3VPN networks. TWAMP is easy to obtain and deploy and does not require clock synchronization.
iFIT measures the packet loss rate and delay of service packets transmitted on an IP network to determine network performance. It is easy to deploy and provides an accurate assessment of network performance.

## Slide 20: Network Slicing Overview
Slice resource reservation technologies, such as FlexE, channelized sub-interface, and QoS queuing, can be used to direct services to respective service slices. These slices are isolated from each other and do not affect each other, providing different SLA levels.
Slicing is an SLA assurance method in essence. It effectively integrates the network capabilities required by users to form a logical network called "slice".
Solution Overview
Application Scenarios
Main Functions
DP
SQ
GQ
VI
MAC
PHY
TM
PIC
CS7
BE
SQ
GQ
VI
TM
PIC
Channelized sub-interface
DP
MAC
PHY
CS7
BE
SQ
GQ
VI
CS7
BE
Channelized sub-interface
…
TM
PIC
…
SQ
DP
FlexE client
FlexE shim
PHY
CS7
BE
FlexE client
SQ
DP
CS7
BE
MAC
QoS
Channelized sub-interface
FlexE
Notes: Channelized sub-interfaces provide a mechanism to isolate different types of services. Different types of service traffic can be forwarded to different VLAN channelized sub-interfaces that use different dot1q encapsulation modes. Each channelized sub-interface can implement independent HQoS scheduling to isolate different types of services.
FlexE is an Ethernet-based bearer technology for multi-rate sub-interfaces on multiple PHY links. FlexE supports bundling, channelization, and sub-rating.
SQ: subscriber queue
GQ: group queue
VI: virtual interface
DP: data plane
TM: traffic manager
PIC: physical interface card

## Slide 21: O&M Overview
A second-level traffic burst is detected.
The peak traffic refers to the highest rate of traffic measured over a 15-minute period at a sampling interval of 5 seconds.
Solution Overview
Application Scenarios
Main Functions
Network top N, enabling quick identification of network bottlenecks
Regional traffic/quality map, enabling quick identification of hotspot areas
Performance topology, clearly showing quality deterioration
Second-level peak traffic, actually reflecting bandwidth bottlenecks

## Slide 22: Financial CloudWAN Scenario
With the deployment of distributed cloud data centers, the cloud backbone network is elastically expanded by adding core and aggregation nodes to implement interconnection between these data centers. In addition, technologies such as SDN and SRv6 are introduced to implement functions such as intelligent network management and traffic optimization.
  Fast service provisioning, centralized path computation, intelligent path selection
  Intelligent network visualization, enabling real-time awareness of service status
  Evolution to the distributed multi-city multi-center architecture
  Capability openness (the controller provides open southbound and northbound interfaces)
Solution Overview
Application Scenarios
Main Functions
Tier-1 branch
Data center A
Data center C
Data center B
DC-PE
DC-P
WAN-P
RR
WAN-P
WAN-P
DC-P
DC-PE
DC-PE
DC-P
RR
BR-PE
BR-PE
City A
City B
Backbone network
City C
iMaster NCE-IP
Tier-1 branch

## Slide 23
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 24: Basic Design Overview for the Enterprise Bearer WAN
Basic design for the enterprise bearer WAN includes physical network design, IP address planning, and routing design.
PE
PE
PE
PE
PE
PE
P
P
P
Bearer network
IS-IS
BGP
Physical network design
Route Design
IP address planning
1.1.1.1/32
1::1/128
RR

## Slide 25: Physical Network Design for the Enterprise Bearer WAN
1. Physical network design
Access layer design
BGP routing design
2. IP address planning
IGP routing design
Aggregation layer design
IPv4 address planning
IPv6 address planning
Core layer design
3. Routing design
SRv6 locator planning

## Slide 26: Core Layer Design
The core layer, as the backbone of the entire network, aggregates and forwards various service traffic. When selecting core nodes, consider the following factors:
  Service volume: Consider the current service volume and expected service growth.
  Physical location: Ensure that core nodes are secure, easy to obtain, and easy to maintain, as they are the key infrastructure of the bearer network.
  Number of nodes: The core layer usually adopts the full-mesh + dual-plane architecture to ensure stability.
Core Layer Design
Access Layer Design
Aggregation Layer Design
Core layer
City A
City C
City B
New site
Notes: The service volume involves two aspects. The first is the service flow direction, that is, where the services concentrate. The second is the service volume size. The two aspects are complementary to each other. Generally, a greater concentration indicates a larger service volume. The core nodes must be nodes where services concentrate and the service volume is large.
Core nodes in the same city are interconnected through WDM, and core nodes in different cities are interconnected through inter-provincial or inter-metro carrier private lines. The number of core nodes must be comprehensively considered and cannot be too large.

## Slide 27: Aggregation Layer Design
Aggregation layer design must take into account the service types and scale on each aggregation node. In the initial phase of bearer network planning and construction, the aggregation layer can be planned based on existing enterprise services. The following three aggregation modes are available:
  Data center aggregation (DC-PE): aggregates traffic from service units that provide services for the HQ in an enterprise. Such service units include data centers and service centers.
  Metro aggregation (MAN-PE): aggregates the metro services of intra-city institutions and affiliated institutions.
  Branch aggregation (BR-PE): aggregates the services of branches, provincial metro institutions, and affiliated institutions.
Model 1: Data center/Service center aggregation
Model 2: Municipal metro aggregation
Model 3: Regional branch aggregation
Core layer
Aggregation layer
Access layer
Core layer
Data center aggregation
Data center
Service center
…
Core layer
Aggregation layer
Access layer
Core layer
BR aggregation
Regional subsidiary
Affiliated institution
…
Core layer
Aggregation layer
Access layer
Core layer
MAN aggregation
Intra-city institution
Affiliated institution
…
Core Layer Design
Access Layer Design
Aggregation Layer Design

## Slide 28: Access Layer Design Factors
When designing the access layer, you need to consider factors such as the bandwidth required by access services, required private lines, and private line prices. Moreover, you need to consider access reliability and traffic load balancing. For example:
  You can use single-homed networking at the access layer to form dual planes working in active/standby mode. This helps improve network reliability.
  On the active and standby planes, you can load-balance WAN traffic through service planning or routing policies.
Access layer
Aggregation layer
Access layer
Aggregation layer
Core Layer Design
Access Layer Design
Aggregation Layer Design

## Slide 29: Bearer Network Private Line Selection
Only a few enterprises have the capability to build their own transmission private lines. Most enterprises need to purchase transmission private lines from carriers and build their own bearer networks over these transmission private lines.
Currently, the transmission private lines provided by carriers are mainly MSTP and OTN private lines:
  MSTP private lines or MPLS VPNs can be used to transmit services from branches to the access layer of the bearer network.
  MSTP private lines can be used between the access and aggregation layers of the bearer network.
  If the aggregation layer and core layer are in different equipment rooms, MSTP/OTN private lines can be used between them.
  MSTP/OTN private lines can be used between core-layer devices. DWDM private lines can also be used between core-layer devices if bare fibers are available.
PE
PE
P
P
MSTP
Bare fiber
OTN

## Slide 30: IP Address Planning Roadmap for the Enterprise Bearer WAN
1. Physical network design
Access layer design
BGP routing design
2. IP address planning
IGP routing design
Aggregation layer design
IPv4 address planning
IPv6 address planning
Core layer design
3. Routing design
SRv6 locator planning

## Slide 31: IP Address Planning Overview
With the development of services, increasingly more networks are deployed as IPv4/IPv6 dual-stack networks. Dual-stack address planning is essential to dual-stack networks.
IP address planning is generally classified into the following:
  IPv4 address planning
  IPv6 address planning
  SRv6 locator planning
PE
PE
PE
PE
P
P
P
PE
PE
Bearer network
1.1.1.1/32
100.0.0.0/24
100::/64
2000::/64
1::1/32
Locator: FC00::1
IPv4 address planning
IPv6 address planning
SRv6 locator planning
10.0.0.0/30

## Slide 32: IPv4 Address Design Rules
For the convenience of service inheritance and network management, the backbone network retains interconnection IPv4 addresses. IPv4 address allocation must comply with the existing IPv4 address allocation specifications of the customer.
IPv4 address design rules
Uniqueness
  Hosts on the backbone network must use unique IP addresses. Try to allocate a different address to each host even if they support VPN address overlapping.
Contiguity
  Routes with contiguous addresses can be easily summarized on a hierarchical network, reducing the routing table size and accelerating route calculation.
Scalability
  Addresses need to be reserved at each layer to ensure contiguity of addresses when the network is expanded.
Meaningfulness
  A well-planned IP address denotes the device to which the IP address belongs.
IPv4 address allocation range on the bearer WAN
Controller address
Interconnection address of a backbone network device
Loopback address of a backbone network device
PE/CE interconnection address
PE
PE
PE
PE
P
P
CE
CE
CE
CE
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 33: Loopback Address Design Rules
The loopback address of each router plays an important role in the normal running of the entire network. Therefore, a unified, dedicated address space must be used for the allocation and management of loopback addresses on each router.
Loopback address design rules and application scenarios
Use 32-bit masks for loopback addresses.
  Allocate loopback addresses based on physical locations and reserve sufficient address space.
  Allocate loopback addresses for the same geographical location by plane. If there are two planes, allocate IP addresses to planes 1 and 2 in sequence.
PE
P
CE
CE
PE
Used for communication between the device and controller.
Used to establish BGP peer relationships between devices.
Used to establish LDP peer relationships between devices.
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 34: IPv4 Address Planning Suggestions
It is recommended that the bearer WAN use a dedicated subnet. The allocated addresses include the management addresses and internal interconnection addresses of devices and access addresses of the bearer network. The following table describes the address allocation plan:
  Internal interconnection addresses: Use a 30-bit mask for IP addresses used for internal interconnection between devices on the bearer network.
  Access addresses: The access-layer device interfaces on the bearer network need to connect to the original network. Therefore, it is recommended that the IP addresses of these interfaces be allocated based on the original planning. For example, use a 29-bit mask for these IP addresses.
  Address allocation sequence: Allocate interconnection addresses in ascending order and loopback addresses in descending order.
  Interconnection between devices of the same layer: Assign an odd address to the device with a smaller number and an even address to the device with a larger number.
  Interconnection between devices at different layers: Assign an odd address to the device close to the network core and an even address to the device far away from the network core.
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 35: Typical IPv4 Address Planning
IPv4 addresses can be planned based on planning suggestions or the customer's planning rules.
PE1
PE2
P1
P2
CE2
CE1
PE3
PE4
P3
P4
CE3
CE4
Bearer network
128.1.1.0/30
.2
.1
128.1.1.4/30
.5
.6
128.1.1.8/30
.10
.9
128.1.1.12/30
.13
.14
128.1.1.16/30
128.1.1.20/30
128.1.1.24/30
128.1.1.28/30
128.1.1.32/30
128.1.1.36/30
.17
.18
.21
.22
.25
.26
.29
.30
.33
.34
.37
.38
192.168.1.0/29
192.168.1.8/29
192.168.1.16/29
192.168.1.24/29
.7
.1
.15
.9
.17
.23
.25
.31
L0: 128.0.0.251/32
L0: 128.0.0.253/32
L0: 128.0.0.254/32
L0: 128.0.0.252/32
L0: 128.0.0.247/32
L0: 128.0.0.250/32
L0: 128.0.0.249/32
L0: 128.0.0.248/32
Loopback IP addresses allocated in descending order
Odd IP address for the device near the core layer
Even IP address for the device far away from the core layer
Odd IP address for the device with a smaller number (intra-layer interconnection)
Even IP address for the device with a larger number (intra-layer interconnection)
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 36: IPv6 Address Planning Requirements and Rules
Uniformity
Uniqueness
Hierarchy
Security
Contiguity
Scalability
Number of required addresses
Address types for filtering/ACL
Routing domains on the network and where route summarization is performed
Requirements
Planning
PE
P
CE
CE
PE
2000:EAB8:2203:5505::1/127
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning
Notes: Uniformity: All IP addresses on the entire network are planned in a unified manner, including service addresses, platform addresses, and network addresses.
Uniqueness: Each address is unique throughout the entire network.
Hierarchy: The massive IPv6 address space poses higher requirements on the route summarization capability. The primary task of IPv6 address planning is to reduce network address fragments, enhance the route summarization capability, and improve the network routing efficiency.
Security: Services with shared attributes have the same security requirements. Mutual access between services needs to be controlled. Services with shared attributes are allocated with addresses in the same address space, which facilitates security design and policy management.
Contiguity: IPv6 addresses in an IPv6 address segment must be contiguous to prevent address wastes.
Scalability: IP addresses must be planned and allocated based on network development requirements to reserve space for future capacity expansion. The addition of a small number of subnets does not require large-scale architecture or policy adjustment.

## Slide 37: Structured IPv6 Address Planning
Structured planning: The massive IPv6 address space poses higher requirements on the route summarization capability. Hierarchical IPv6 address allocation is recommended, which helps reduce the sizes of routing tables through route summarization. In addition, the subnet field of an IPv6 address can be divided into several independent fields to make the address more readable. (If possible, it is recommended that the subnet field be divided by 4 bits.) The following is a planning example:
N bits
64 bits
(64 – N) bits
Network Type
Allocatable Address Block
Host Address
Fixed Prefix
4 bits
(64 – 4 – N) bits
  Fixed Prefix: indicates the fixed prefix applied for.
  Network Type: indicates the type of a network. For example, 0 indicates a backbone network, 1 indicates a data center, and 2 to F are reserved.
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 38: IPv6 Address Planning Suggestions
The user-defined part of an IPv6 address needs to be planned based on its summarization characteristics. Fields that are easy to summarize, such as the address space and area, should be placed in the left-most part. Excessive layering results in strong coupling between services and address planning, which hinders subsequent service development and reduces address space utilization. Therefore, you need to determine the number of fields based on site requirements.
N bits
64 bits
(64 – N) bits
Attribute ID
Network Type
Host Address
Fixed Prefix
4 bits
(64 – 16 – N) bits
Address Type
Area
Allocatable Address Block
  Fixed Prefix: indicates a fixed-length prefix applied for by an enterprise from an address allocation organization.
  Subnet:
  Attribute ID: is used to distinguish address types. It is used for level-1 address classification.
  Network Type: identifies the type of a network.
  Address Type: identifies the type of an address on the network.
  Area ID: identifies an area on the network.
  Allocatable Address Block: is reserved for future address allocation.
  Interface Address: indicates the last 64 bits of an IP address. It is equivalent to the host ID in an IPv4 address.
4 bits
4 bits
4 bits
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 39: Typical IPv6 Address Planning
IPv6 addresses can be planned based on planning suggestions or the customer's planning rules.
PE1
PE2
P1
P2
CE2
CE1
PE3
PE4
P3
P4
CE3
CE4
Bearer network
2001::1:1:103:100:0/127
IPv6 interconnection address: 2001 : : 1 : 1 : 101 : 100 : 0/127
Address use
Area
Interconnection device
Interconnection link
Fixed prefix
IPv6 loopback address: 2001 : : 1 : 100 : 0 : 0/128
Area
Device
Fixed prefix
Bearer network
2001::1:1:204:300:0/127
2001::1:1:102:200:0/127
2001::1:1:304:400:0/127
2001::1:2:103:100:0/127
2001::1:2:204:300:0/127
2001::1:2:304:400:0/127
2001::1:2:102:200:0/127
2001::1:102:303:100:0/127
2001::1:102:404:200:0/127
L0: 2001::1:100:0:0/128
L0: 2001::1:300:0:0/128
L0: 2001::1:200:0:0/128
L0: 2001::1:400:0:0/128
L0: 2001::2:300:0:0/128
L0: 2001::2:400:0:0/128
L0: 2001::2:100:0:0/128
L0: 2001::2:200:0:0/128
.0
.1
.1
.0
.1
.0
.0
.1
.0
.1
.0
.1
.0
.1
.0
.1
.1
.0
.1
.0
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 40: SRv6 SID Overview
An SRv6 SID usually consists of three fields: Locator, Function, and Arguments. The SRv6 SID is expressed in the Locator:Function:Arguments format. Note that the total length (Locator + Function + Arguments) is less than or equal to 128 bits. If the total length is less than 128 bits, the reserved bits are padded with 0s.
If the Arguments field does not exist, the format is Locator:Function. The Locator field occupies the most significant bits of an IPv6 address, and the Function field occupies the remaining part of the IPv6 address.
Locator
Function
Arguments
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)
128 bits
128 bits
128 bits
SRv6 segment: IPv6 address format
|--Locator--|--Dynamic Opcode--|--Static Opcode--|--Args--|
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning
Notes: The locator is an IPv6 network segment. All IPv6 addresses in this network segment can be allocated as SRv6 SIDs. After a locator is configured for a node, the system generates a locator route. The node can be located based on the locator route. In addition, all SIDs advertised by the node can reach the node through the locator route.
The Function field is also called opcode, which can be dynamically allocated using an IGP or statically configured using the opcode command. When configuring a locator, you can use the static static-length parameter to specify the length of the static segment, which determines the number of static opcodes that can be configured in the locator. When an IGP dynamically allocates opcodes, it applies for opcodes outside of the static segment range to ensure that SRv6 SIDs do not conflict.
The Args field is determined by the args args-length parameter. The Args field is optional in SRv6 SIDs and is determined by the command configuration.

## Slide 41: SRv6 Locator Overview
The Locator field identifies the location of a network node, and is used for other nodes to route and forward packets to this identified node so as to implement network instruction addressing.
A locator has two important characteristics: routable and aggregatable. After a locator value is configured for a node, the system generates a locator route and propagates the route throughout the SR domain using an IGP. A device advertising a locator route can be located by other devices on the same network based on the received locator route information, and all the SRv6 SIDs advertised by the device can be reached over the route.
It is recommended that the same mask be used for the locators of all NEs on the entire network. After the mask is set, locators can be allocated in ascending order for the core, aggregation, and access layers in sequence.
Locator
Function
Arguments
128 bit
IPv6 prefix
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 42: SRv6 Locator Planning Suggestions
SRv6 locator addresses are allocated from the IPv6 host address field. Using hierarchical address allocation and reserving some address spaces are recommended for future expansion. An example is provided as follows:
  Site ID: uniquely identifies a site.
  Node ID: uniquely identifies a device at a site.
  Function: indicates the Function field in an SRv6 SID.
  Dynamic/Static: indicates whether a SID is a dynamic or static SID. 0 indicates a static SID (it is recommended that the End, End.X, and OAM-related SIDs be statically allocated). 1 indicates a dynamic SID (if many VPNs exist or VPNs change frequently, it is recommended that service SIDs, such as End.DT SIDs, be dynamically allocated).
  End&End.X, etc: indicates the type of a SID. 0x000[1–F] indicates an End SID, and 0X1[peer site ID]X indicates an End.X SID.
  Args: indicates the parameter field in an SRv6 SID.
N bits
64 bits
(64 – N) bits
Subnet
Site ID
Reserved
Function
Args
Fixed prefix
8 bits
28 bits
12 bits
Node ID
8 bits
15 bits
1 bit
8 bits
Dynamic/Static
End.DT
End&End.X, etc.
12 bits
32 bits
For compatibility with future SID compression, keep this part within 32 bits. It is recommended that this part contain 32 bits.
88 bits
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning
Notes: End.DT SIDs can be classified into End.DT4 SIDs and End.DT6 SIDs.
  An End.DT4 SID (PE endpoint SID) identifies an IPv4 VPN instance on a network.
  An End.DT6 SID (PE endpoint SID) identifies an IPv6 VPN instance on a network.
In SRv6, End.OP SIDs are used to implement operation, administration and maintenance (OAM).
  End.OP SIDs are mainly used in ping/tracert scenarios.

## Slide 43: Typical SRv6 Locator Planning
In SRv6 Locator Planning, it is recommended that the locator length not exceed 88 bits. Moreover, try to statically configure SRv6 SIDs, so that SRv6 SIDs remain unchanged after devices go online again. This facilitates management.
SRv6 Locator: 2001 : : 2 : 2 : 1 : 0 : 0 88 Static 27 args 12
Address use
Area
Device number
Locator length
Fixed prefix
Static opcode length
Args length
PE1
PE2
P1
P2
CE2
CE1
PE3
PE4
P3
P4
CE3
CE4
Bearer network
Locator: 2001::2:1:1:0:0 88 static 27 args 12
Locator: 2001::2:1:4:0:0 88 static 27 args 12
Locator: 2001::2:2:3:0:0 88 static 27 args 12
Locator: 2001::2:2:2:0:0 88 static 27 args 12
Bearer network
IPv4 Address Planning
SRv6 Locator Planning
IPv6 Address Planning

## Slide 44: Routing Design Roadmap for the Enterprise Bearer WAN
1. Physical network design
Access layer design
BGP routing design
2. IP address planning
IGP routing design
Aggregation layer design
IPv4 address planning
IPv6 address planning
Core layer design
3. Routing design
SRv6 locator planning

## Slide 45: Routing Design Overview
Routing protocols are generally classified into IGP and BGP. These two types of protocols have different functions and therefore are designed for different purposes.
Routing design can be classified into the following types:
  IGP routing design
  BGP routing design
PE
PE
PE
P/RR
P/RR
CE
CE
CE
CE
PE
Bearer network
IS-IS
IS-IS
BGP
BGP
BGP routing design
IGP routing design

## Slide 46: IGP Overview
On a bearer WAN, an IGP functions as a basic support protocol to collect and flood Layer 3 topology information on the entire network, and works with protocols such as TWAMP and iFIT to collect network status information, such as link delay.
Generally, OSPF or IS-IS can be used on the backbone network for route reachability. However, the application scenarios of the two protocols are different to some extent.
 | IS-IS | OSPF | Remarks
Network scale | Large | Small | Some devices support a maximum of 4K IS-IS routes and a maximum of 2K OSPF routes in a single area (with a single level).
IPv6 support | TLV-based packets are used, and no extra protocol needs to be independently deployed. | OSPFv3 needs to be independently deployed. | When OSPF supports both IPv4 and IPv6, OSPFv2 and OSPFv3 neighbor relationships need to be configured separately. The exchange of large numbers of protocol packets consumes a lot of resources.
SRv6 support | Related standards or drafts are available. | Related standards or drafts are available. | The standardization process of OSPF lags behind that of IS-IS in terms of SRv6 support. Not all vendors support SRv6-oriented OSPF extensions.
SR-MPLS support | Supported. The related functions are complete. | Supported. The related functions are basically complete. | 
IGP Route Planning
BGP Route Planning

## Slide 47: IGP Route Planning
Compared with OSPF, IS-IS supports SR-MPLS/SRv6 in a more comprehensive and scalable manner. Considering network expansion brought by enterprise service growth, large enterprise bearer networks generally start to use IS-IS. Therefore, it is recommended that IS-IS be preferentially used as the IGP for bearer networks.
IGP Route Planning
BGP Route Planning
IS-IS: One IS-IS process is configured on the entire network, and an IS-IS level-2 area is configured in E2E mode.
PE
PE
PE
P/RR
P/RR
CE
CE
CE
CE
PE
Bearer network
IS-IS
L2
IS-IS
L2
Notes: It is recommended that some IGP parameters be set as follows:
  IGP process ID: It is recommended that the IS-IS or OSPF process ID of a device on the backbone network be the same as the BGP AS number.
  IS-IS NET: The recommended format is aa.bbbb.cccc.dddd.00. The loopback0 address of the device is used for NET derivation. For example, if the loopback0 address is 21.231.232.1, then the derived NET is 21.0231.0232.0001.00.
  OSPF router ID: The global router ID is used. Generally, the router ID is the same as the loopback0 address.
  Interface type: To speed up convergence, all interfaces are of the P2P type.
  Route advertisement: IGP is mainly used to ensure the reachability of internal addresses on the WAN. Therefore, IGP advertises only interconnection interface addresses and device management addresses.

## Slide 48: IGP Metric Planning
The bearer network transmits different types of service traffic. When deploying an IGP on the bearer network, properly plan route metric to maximize bandwidth utilization, improve service quality, and ensure service reliability.
IGP metric design rules:
  Ensure that the metric of access-layer links is lower than that of aggregation-layer links.
  Ensure that the metric of aggregation-layer links is lower than that of core-layer links.
  Ensure that the metric of links between data centers is lower than that of WAN links between branches and data centers.
  Ensure that inter-plane traffic between data centers preferentially traverses across planes through core nodes.
  If a standalone RR is deployed, ensure that the metric of the link between the RR and core P is set to the maximum value (the RR only reflects routing information and does not forward data).
IGP Route Planning
BGP Route Planning

## Slide 49: IGP Metric Planning Suggestions
CE
CE
PE
PE
P
P
P
P
PE
PE
CE
CE
RR
RR
RR
P
P
PE
PE
CE
CE
Data center A
Bearer network
IGP: IS-IS/OSPF
10
20
10
10
200
200
1000
1000
1000
1000
10000
10000
10000
10000
10000
10000
10
10
10
20
IGP Route Planning
BGP Route Planning
Data center B
Enterprise branch

## Slide 50: Overall BGP Planning
After an enterprise bearer WAN is used to carry services that were used to be carried by multiple networks, it needs to use BGP/MPLS IP VPN to isolate these services.
Generally, IBGP runs on the bearer network, and EBGP runs between the bearer network and other ASs (such as data centers and enterprise branches). PEs use BGP policies to control the transmission of VPN routes between ASs, achieving complex access control.
If a controller is deployed on the bearer WAN, BGP-LS must be deployed between the controller and RR.
IGP Route Planning
BGP Route Planning
Data center
Bearer network
Data center
Enterprise branch
Enterprise branch
EBGP
EBGP
EBGP
EBGP
MP-IBGP
BGP-LS
CE
PE
CE
PE
CE
PE
CE
PE
RR
MP-IBGP
Notes: In BGP peer relationship establishment, IBGP peer relationships are established using Loopback0 addresses, and EBGP peer relationships are established using interface addresses.
AS: The bearer WAN can be classified as an independent AS.
IBGP: PEs use loopback addresses to establish IBGP peer relationships with all RRs and use MP-IBGP to exchange VPN routes.
EBGP: PEs use interface IP addresses to establish EBGP peer relationships with CEs. In inter-AS VPN route exchange scenarios, Option A is generally used.
BGP-LS: The controller establishes BGP-LS peer relationships with all RRs to collect logical topology information on the backbone network.
Deploy independent RRs and establish IBGP peer relationships for RRs on the backbone network.
In addition to EBGP, IGPs such as OSPF, IS-IS, and RIP can also be used between PEs and CEs on the bearer network. Static routes can also be used to meet the requirements of flexible access in various scenarios.

## Slide 51: BGP AS Planning
An enterprise network usually uses a private AS number ranging from 64512 to 65534 during BGP deployment.
It is recommended that one AS be deployed as the high-speed forwarding core of the entire bearer network, independent ASs be deployed for data centers and enterprise branches in different regions, and EBGP peer relationships be established between these ASs and the bearer network AS.
IGP Route Planning
BGP Route Planning
Data center
Bearer network
Data center
Enterprise branch
Enterprise branch
EBGP
EBGP
EBGP
EBGP
MP-IBGP
CE
PE
CE
PE
CE
PE
CE
PE
RR
MP-IBGP
AS 65000
AS 65001
AS 65002
AS 65003
AS 65004

## Slide 52: BGP Route Control Planning
To ensure network reliability, dual planes working in active/standby mode are generally deployed on the bearer network.
Route control is required to ensure that the active plane carries traffic in normal cases, and the standby plane takes over traffic when the active plane fails.
  Generally, community attributes are added to routes between CEs and PEs, and the MED values of specific routes are changed based on community attributes.
  Generally, PEs and RRs change the MED values of specific routes based on community attributes.
  Changing the MED values of specific routes ensures that traffic is sent from the local PE on the active plane to the remote PE on the active plane in normal cases.
CE1
PE1
CE2
PE2
CE4
PE4
CE3
PE3
RR
Configure the PE to add a community attribute to routes received from the CE.
Data center
Bearer network
Enterprise branch
Configure bidirectional route import between CEs.
Plane A (active)
Plane B (standby)
Configure PEs to change the MED value of routes received from the RR to ensure that traffic is forwarded on the same plane.
Configure the active-plane PE to increase the MED value of a route by 10 before advertising the route to the CE.
Configure the standby-plane PE to increase the MED value of a route by 20 before advertising the route to the CE.
IGP Route Planning
BGP Route Planning
Notes: PE3 changes the MED value to 100 for the route whose next hop is PE1 (a PE on the same plane) and changes the MED value to 200 for the route whose next hop is PE2 (a PE on a different plane).
PE4 changes the MED value to 100 for the route whose next hop is PE2 (a PE on the same plane) and changes the MED value to 200 for the route whose next hop is PE1 (a PE on a different plane).
If PE1 and PE2 on the left learn the same VPN route and advertise the route to PE3 and PE4 on the right through the RR, PE3 and PE4 preferentially select the VPN route on the same plane as them. After the route is advertised to the CE, traffic from the CE preferentially travels along the route advertised by PE3 (because the MED value of the route advertised by PE3 is only increased by 10).

## Slide 53: Design for BGP Routing Loop Prevention and Sub-optimal Route Prevention
Generally, data center networks and branch networks do not run BGP. Their IGPs need to import routes learned by EBGP.
When an IGP imports EBGP routes, it needs to add a tag to the routes, so that the IBGP peer can filter out imported BGP routes based on tags when importing local IGP routes to BGP.
CE1
PE1
CE2
PE2
Data center/
Enterprise branch
Bearer network
Plane A (active)
Plane B (standby)
IGP adds a tag to imported BGP routes.
BGP filters out tagged routes when importing IGP routes.
IGP Route Planning
BGP Route Planning

## Slide 54
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 55: Tunnel and VPN Design Overview for the Enterprise Bearer WAN
Enterprises usually use VPN to isolate services and SR to establish tunnels for traffic optimization and path planning.
VPN traffic is carried over tunnels to isolate enterprise services while ensuring service quality.
IP bearer network
Primary tunnel
Backup tunnel
Branch site
HQ
Tunnel
VPN design
Tunnel design

## Slide 56: Tunnel Design Roadmap for the Enterprise Bearer WAN
1. Tunnel design
Basic tunnel concepts
2. VPN design
SR-MPLS tunnel planning
VPN classification
VPN type selection
SRv6 tunnel planning

## Slide 57: Tunneling Technology Overview
The tunneling technology uses one protocol to encapsulate the packets of another protocol, and the carrier protocol itself can be encapsulated or carried by other protocols.
For example, BGP/MPLS IP VPN commonly used on enterprise networks uses MPLS LDP or MPLS TE tunnels to carry VPN services.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
MPLS LDP tunnel
MPLS TE tunnel
VPN1
Site A
VPN2
Site A
VPN1
Site B
VPN2
Site B
MPLS LDP or MPLS TE is used to establish MPLS tunnels.

## Slide 58: Issues with MPLS LDP and RSVP-TE
MPLS LDP
RSVP-TE
R1
R2
R4
R3
IGP
LDP itself does not have the path computation capability and requires an IGP for path computation.
Both the IGP and LDP need to be deployed for the control plane, and devices need to exchange a large number of packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
If LDP-IGP synchronization is not achieved, data forwarding may fail.
RSVP-TE is complex to configure and does not support load balancing.
To implement TE, devices need to exchange a large number of RSVP packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
RSVP-TE uses a distributed architecture, so that each device only knows its own state and needs to exchange signaling packets with other devices.
LDP
LDP
LDP
LDP
IGP
IGP
IGP
R1
R2
R4
R3
RSVP response
RSVP response
RSVP request
RSVP request
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: MPLS is a tunneling technology that guides data forwarding in essence and has complete tunnel creation, management, and maintenance mechanisms. The preceding mechanisms are driven by network operation and management requirements, not by applications.

## Slide 59: Solution Provided by SR
Service-defined network
Simplifying protocols and extending existing protocols
  The extended IGP/BGP supports label distribution. Therefore, LDP is not required on the network, achieving protocol simplification. In addition, devices require only software upgrades instead of hardware replacement, protecting investments on the live network.
  The source routing mechanism is introduced. The forwarding policy is instantiated into a segment list on the ingress to control the forwarding path of service traffic.
Enabling networks to be defined by services
  After an application raises requirements (e.g. delay, bandwidth, and packet loss rate), the controller collects information (e.g. network topology, bandwidth usage, and delay) and computes an explicit path according to the requirements.
R2
R4
R3
Controller
IGP/BGP
R1
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design

## Slide 60: SR-MPLS Classification
SR-MPLS BE
An extended IGP has the label distribution capability. An LSDB can be formed based on the SRGB, prefix SID, link state, and other information distributed through the IGP, and the SPF algorithm can be used to compute the shortest forwarding paths based on labels. Therefore, LDP is no longer required on the network.
Because only the IGP/BGP is used, the network does not have traffic blackholes and does not need to maintain LDP peer relationships.
R1
R2
R4
R3
Extended IGP
Extended IGP
Extended IGP
Extended IGP
LSDB
LSDB
LSDB
LSDB
The IGP is used to distribute labels, and LDP is not required.
SR-MPLS Policy
Extended BGP/IGP sends the LSDB that carries label information to the controller, which then globally computes paths. There is no need to use RSVP-TE packets to apply for paths or maintain path status.
Node SIDs and adjacency SIDs are used to implement load balancing and strict explicit paths.
Path computation and service delivery are performed by the controller, simplifying configuration.
R1
R2
R4
R3
BGP LS
Extended IGP
Extended IGP
Extended IGP
LSDB
LSDB
LSDB
LSDB
Controller
Extended IGP
RSVP-TE is no longer needed, simplifying the configuration.
Moreover, load balancing and strict explicit paths are supported.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design

## Slide 61: SR-MPLS-based VPN Traffic Transmission
VPN1
Site B
VPN1
Site A
PE1
P2
P1
CE1
PE2
SR Domain
1036
1024
Data
1031
1024
Data
Data
Data
CE2
1036
1024
Data
VPN1
Site B
VPN1
Site A
PE1
P2
P1
CE1
PE2
SR Domain
16001
16002
1024
Data
Data
Data
CE2
16002
1024
Data
16001
16002
1024
Data
SR-MPLS BE-based VPN traffic transmission
SR-MPLS Policy-based VPN traffic transmission
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: The process of forwarding VPN traffic based on SR-MPLS BE is similar to the process of forwarding BGP/MPLS IP VPN traffic based on LDP.
  After PE1 receives a VPN packet from CE1, PE1 searches the routing table and pushes two layers of labels into the packet. The outer label is a public network label, and the inner label is a private network label.
  PE1 then sends the packet to P1, which swaps the outer label of the packet based on the SR-MPLS BE tunnel entry and sends the packet to P2. The process on P2 is similar to that on P1.
  Upon receipt of the packet, PE2 sends the packet to a specific VPN site based on the inner label (PHP is not considered in this case).
When an SR-MPLS Policy is used to carry VPN traffic, the forwarding path must be pre-computed and delivered to the ingress (PE1) as a segment list.
  After receiving a VPN packet from CE1, PE1 searches the corresponding table and pushes the related segment list into the packet.
  PE1 then sends the packet to P1, which determines the forwarding path based on the outer label, pops out the outer label, and sends the packet to P2.
  After receiving the packet, P2 determines the forwarding path based on the outer label, pops out the outer label, and sends the packet to PE2.
  PE2 sends the packet to the specified VPN site according to the inner label.

## Slide 62: SRv6 Overview
SRv6, or Segment Routing IPv6, is designed to forward IPv6 data packets on a network based on the source routing paradigm.
SRv6 forwarding is no longer based on MPLS, simplifying the forwarding plane. SRv6 implements hop-by-hop forwarding by adding a Segment Routing header (SRH) into IPv6 packets, encapsulating an explicit IPv6 address stack into the SRH, and continuously updating destination addresses on transit nodes.
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type=4 |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List[0] (128-bit IPv6 address) |  |  |  | 
Segment List[1] (128-bit IPv6 address) |  |  |  | 
Segment List[2] (128-bit IPv6 address) |  |  |  | 
Optional TLV objects (variable) |  |  |  | 
IPv6 Payload |  |  |  | 
Standard IPv6 header
IPv6 extension header (SRH)
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design

## Slide 63: SRv6-based VPN Traffic Transmission
VPN1
Site B
2001:: 64
VPN1
Site A
PE1
P2
P1
CE1
PE2
IPv6 Domain
FC01::1
2001::1
Data
CE2
VPN1
Site B
2001:: 64
VPN1
Site A
PE1
P2
P1
CE1
PE2
IPv6 Domain
CE2
SRv6 BE-based VPN traffic transmission
SRv6 Policy-based VPN traffic transmission
FC01::1
2001::1
Data
FC01::1
2001::1
Data
2001::1
Data
2001::1
Data
2001::1
Data
2001::1
Data
FC02::1
2001::1
Data
FC03::1
2001::1
Data
(SL=3)
FC10::1
FC03::1
FC02::1
(SL=2)
FC10::1
FC03::1
FC02::1
FC10::1
2001::1
Data
(SL=1)
FC10::1
FC03::1
FC02::1
FC02::1
FC03::1
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: When SRv6 BE is used to carry VPN traffic, data packets carry two layers of IPv6 headers. The outer IPv6 header address is used to identify the VPN to which the data belongs, and the inner IPv6 header identifies the actual destination address of the data.
  The outer IPv6 address is generated by the locator of PE2 and advertised to PE1 through BGP. PE2 advertises the locator to other devices in the form of a route.
  After PE1 receives a packet destined for the destination network segment (2001:: 64), PE1 encapsulates the packet with an outer IPv6 header and forwards the packet based on the routing table.
  Ps (P1 and P2) forward the packet based on the outer IPv6 header.
  After receiving the packet, PE2 matches the packet with the corresponding VPN instance based on the outer IPv6 header and forwards the packet based on the routing table.
When SRv6 Policy is used to carry VPN traffic, data packets carry two layers of IPv6 headers. The outer IPv6 header address is replaced by each hop based on the SRH information, and the inner IPv6 header identifies the actual destination address of the data.
  Upon receipt of a packet destined for 2001:: 64, PE1 adds an outer IPv6 header (including the SRH) to the packet and sends the packet to the next hop based on the header.

## Slide 64
Notes:   After receiving the packet, P1 replaces the outer IPv6 header based on the SRH information and forwards the packet. P2 processes the packet in a similar way.
  After receiving the packet, PE2 determines the VPN to which the packet belongs based on the outer IPv6 header and forwards the packet based on the routing table.

## Slide 65: SR-MPLS Tunnel Design Principles
Tunnels are intended to better serve services and focus on optimization requirements under the prerequisite that VPN bearer requirements are met. Comply with the following principles to achieve a balance among aspects such as service path visualization, service protection, network maintainability, and network scalability:
  Service path visualization: Associate service traffic with tunnels to achieve some degree of path visualization.
  Maintainability: Keep the total number of tunnels at an appropriate level to reduce live network maintenance pressure and shorten the optimization time.
  Ease of optimization: Ensure that the traffic on each tunnel is not too heavy. Otherwise, bandwidth optimization will be difficult.
  Reliability: Ensure that main services are under protection, and key services can be quickly converged.
  Scalability: Consider possible network expansion in the future.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: SR-MPLS BE tunnels are similar to LDP tunnels. Tunnel establishment depends on IGP design. Therefore, after IGP design is complete, SR-MPLS BE design is complete.
This section mainly focuses on SR-MPLS Policy design.

## Slide 66: SR-MPLS Policy Deployment Design
Generally, an enterprise bearer network belongs to an independent AS. Therefore, E2E SR-MPLS Policies can be deployed.
An E2E tunnel can be deployed between the ingress (PE) where service traffic enters the bearer network and the egress (PE) where service traffic leaves the backbone network.
VPN1
Site B
VPN1
Site A
PE1
P2
P1
CE1
PE2
SR domain
CE2
E2E SR-MPLS Policy
L2 VPN
L3 VPN
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: End-to-end deployment has the following characteristics:
  Strong path control can be implemented through the planning of end-to-end paths (especially explicit paths).
  Path visualization is relatively good.
  If the network is large (for example, a network with multiple data centers and dozens of branches) and has 5,000 to 10,000 TE tunnels, the maintenance workload is heavy.
  The scalability is fair. If a new data center or branch is added, a large number of end-to-end tunnels need to be added.

## Slide 67: SR-MPLS Policy Path Planning
SR-MPLS Policy paths can be planned based on factors such as bandwidth, delay, and path disjoint.
  When planning paths based on bandwidth, you need to set the maximum available bandwidth of each interface in advance.
  If path planning is based on delay, TWAMP or iFIT must be deployed in advance to detect real-time network delay.
If SR-MPLS Policy paths are planned through the controller or static configuration, the following two modes are available (CP stands for candidate path):
  Single-CP multi-segment path
  Multi-CP single-segment path
SR-MPLS Policy
Candidate path 1
(preference: 200)
Candidate path 2
(preference: 100)
Segment list 1
(weight: 10)
Segment list 1
(weight: 10)
<Headend, color, endpoint>
Single-CP multi-segment path
SR-MPLS Policy
Candidate path 1
(preference: 200)
Segment list 1
(weight: 20)
Segment List 2
(weight: 10)
<Headend, color, endpoint>
Multi-CP single-segment path
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: If iFIT is used to measure the network delay, 1588v2 must be enabled on the entire network. Therefore, there are restrictions on application scenarios.
TWAMP requires only NTP in network delay measurement.
For a tunnel planned based on bandwidth, the actual traffic volume of the tunnel cannot be limited on devices after the tunnel is delivered. The traffic volume of a tunnel needs to be limited on the ingress, and the QoS or network slicing technology needs to be used.

## Slide 68: SR-MPLS Policy Traffic Diversion Mode Design
SR-MPLS Policies need to steer service traffic into tunnels for forwarding. This process is called traffic diversion. Currently, SR-MPLS Policies support the following traffic diversion modes:
  Color-based traffic diversion: In this mode, the headend steers traffic into an SR-MPLS Policy through route recursion implemented based on the color value and destination address in the route.
  DSCP-based traffic diversion: In this mode, the headend searches for a matching SR-MPLS Policy group based on specific endpoint information and then finds the corresponding SR-MPLS Policy based on the DSCP value of packets.
Color-based traffic diversion
DSCP-based traffic diversion
FTP service
HTTP service
FTP service
HTTP service
Bearer network
Bearer network
DSCP-based traffic diversion can better ensure service quality.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: In color-based traffic diversion, different tunnels (including primary and backup tunnels) can only be selected based on endpoints. If different service traffic (such as HTTP and FTP traffic) is destined for the same address, color-based traffic diversion diverts the traffic to the same tunnel. As a result, the quality of some services deteriorates.
In DSCP-based traffic diversion, different tunnels can be selected based on endpoint + DSCP information. If different service traffic (such as HTTP and FTP traffic) is destined for the same address, DSCP-based traffic diversion will steer different services into different tunnels based on the configuration, thereby ensuring the service quality.

## Slide 69: Best-Effort Forwarding Design for SR-MPLS Tunnels
VPN services can be carried over either SR-MPLS Policies or SR-MPLS BE tunnels.
An SR-MPLS Policy can contain multiple candidate paths with the preference attribute. The valid candidate path with the highest preference functions as the primary path of the SR-MPLS Policy, and the valid candidate path with the second highest preference functions as the HSB path.
If all SR-MPLS Policies fail, VPN services can be carried over SR-MPLS BE tunnels.
It is recommended that both SR-MPLS Policies and SR-MPLS BE tunnels be deployed. SR-MPLS Policies are preferentially used, and SR-MPLS BE tunnels serve as their backup.
SR-MPLS Policy
Candidate path 1
(preference: 200)
Candidate path 2
(preference: 100)
Segment list 1
(weight: 20)
Segment List 2
(weight: 10)
Segment list 1
(weight: 10)
<Headend, color, endpoint>
SR-MPLS BE
Tunnel Selection
Primary tunnel
Best-effort tunnel
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Notes: An SR-MPLS Policy can have multiple candidate paths, such as CP1 and CP2. Each path is uniquely identified by a 3-tuple <protocol, origin, discriminator>.
CP1 is the activated path because it is valid and has a higher priority. The two SID lists (also called segment lists) of CP1 are delivered to the forwarder, and traffic is balanced between the two tunnel paths based on weight. For example, traffic along the SID list <SID11, SID12> is balanced based on W1/(W1+W2). In the current mainstream implementation, a candidate path has only one segment list.
If a controller is used to generate SR-MPLS Policies, only primary and backup tunnels can be established, and load balancing cannot be implemented for the primary tunnel.

## Slide 70: SRv6 Tunnel Design
SRv6 BE forwards traffic based on the optimal path selected by the routing protocol and applies to services that have low path SLA requirements. Services with high path SLA requirements need to be forwarded in SRv6 Policy mode where the controller is used to compute paths based on constraints to ensure service SLA.
The deployment and traffic import mode design for SRv6 Policies is similar to that for SR-MPLS Policies.
  It is recommended that E2E SRv6 tunnels be deployed on enterprise bearer networks to facilitate monitoring and O&M.
  Traffic can be steered into SRv6 tunnels based on either the color or DSCP attribute, and DSCP-based traffic diversion can better ensure service quality.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
Color-based traffic diversion
DSCP-based traffic diversion
FTP service
HTTP service
FTP service
HTTP service
DSCP-based traffic diversion can better ensure service quality.
Bearer network
Bearer network
Notes: Similar to LDP tunnels, SRv6 BE tunnels are calculated based on IGP/BGP optimal paths. Unlike label-featured MPLS, SRv6 BE uses the shortest path first (SPF) algorithm to calculate forwarding paths based on SRv6 SIDs in an IGP domain. SRv6 BE requires only one segment to identify a forwarding path and the carried services. Traffic forwarding along paths depends on cost planning. Traffic is forwarded based on the least-cost route.
This section describes SRv6 TE Policy design.

## Slide 71: SRv6 Policy Path Planning
SRv6 Policy paths can be planned based on factors such as bandwidth, delay, and path disjoint.
  When planning paths based on bandwidth, you need to set the maximum available bandwidth of each interface in advance.
  If path planning is based on delay, TWAMP or iFIT must be deployed in advance to detect real-time network delay.
If SRv6 Policy paths are planned through the controller or static configuration, the following two modes are available:
  Single-CP multi-segment path
  Multi-CP single-segment path
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
SRv6 Policy
Candidate path 1
(preference: 200)
Candidate path 2
(preference: 100)
Segment list 1
(weight: 10)
Segment list 1
(weight: 10)
<Headend, color, endpoint>
Single-CP multi-segment path
SRv6 Policy
Candidate path 1
(preference: 200)
Segment list 1
(weight: 20)
Segment List 2
(weight: 10)
<Headend, color, endpoint>
Multi-CP single-segment path
Notes: If iFIT is used to measure the network delay, 1588v2 must be enabled on the entire network. Therefore, there are restrictions on application scenarios.
TWAMP requires only NTP in network delay measurement.
For a tunnel planned based on bandwidth, the actual traffic volume of the tunnel cannot be limited on devices after the tunnel is delivered. The traffic volume of a tunnel needs to be limited on the ingress, and the QoS or network slicing technology needs to be used.

## Slide 72: Best-Effort Forwarding Design for SRv6 Tunnels
Similar to SR-MPLS, SRv6 can use either SRv6 BE tunnels or SRv6 Policies to carry VPN services.
SRv6 BE tunnels are generally used as best-effort tunnels. If all SRv6 Policies fail, SRv6 BE tunnels are used to carry services.
It is recommended that SRv6 BE tunnels and SRv6 Policies both be deployed. SRv6 Policies are preferentially used, and SRv6 BE tunnels serve as their backup.
Basic Tunnel Concepts
SR-MPLS Tunnel Design
SRv6 Tunnel Design
SRv6 Policy
Candidate path 1
(preference: 200)
Candidate path 2
(preference: 100)
Segment list 1
(weight: 20)
Segment list 2
(weight: 10)
Segment list 1
(weight: 10)
<Headend, color, endpoint>
SRv6 BE
Tunnel Selection
Primary tunnel
Best-effort tunnel

## Slide 73: VPN Design Roadmap for the Enterprise Bearer WAN
1. Tunnel design
Basic tunnel concepts
2. VPN design
SR-MPLS tunnel planning
VPN classification
VPN route transmission
SRv6 tunnel planning

## Slide 74: VPN Classification
Different enterprises have different requirements for VPN division. Most enterprises use one VPN for major services (including production and office services), one VPN for non-major services, one VPN for external services, and one VPN for Internet services.
PE
PE
PE
PE
PE
PE
P
P
P
Bearer network
IS-IS
BGP
RR
VPN access point
VPN Classification
VPN Route Transmission

## Slide 75: IPv4 VPN Type Selection
When SR-MPLS is used to carry IPv4 L3VPN traffic, the BGP VPNv4 or BGP EVPN address family can be used to transmit VPN routes.
When SRv6 is used to carry IPv4 L3VPN traffic, it is recommended that the BGP EVPN address family be used to transmit VPN routes, so that IPv6 and Layer 2 services can be carried in the same manner.
The L3VPN capabilities and implementation processes of VPNv4 and EVPN address families are basically the same.
 | VPNv4 | EVPNv4 | Remarks
Forwarding plane | MPLS/SRv6 | MPLS/SRv6 | 
VPN route learning | BGP | BGP | The BGP route formats are different.
Whether RR-based route reflection is supported | Supported | Supported | 
Failover | Supported | Supported | VPN FRR, IP FRR, TE-HSB (MPLS), CBTS, TI-LFA (SRv6), Mirror-SID
VPN Classification
VPN Route Transmission

## Slide 76: IPv6 VPN Type Selection
When SR-MPLS is used to carry IPv6 L3VPN traffic, the MP-VPNv6 or BGP EVPN address family can be used to transmit VPN routes.
When SRv6 is used to transmit IPv6 services, it is recommended that the BGP EVPN address family be used to transmit VPN routes.
 | VPNv6 | EVPNv6 | Remarks
Forwarding plane | MPLS/SRv6 | MPLS/SRv6 | 
VPN route learning | BGP | BGP | The BGP route formats are different.
Whether RR-based route reflection is supported | Supported | Supported | 
Failover | Supported | Supported | VPN FRR, IP FRR, TE-HSB, CBTS, TI-FLA, Mirror-SID
VPN Classification
VPN Route Transmission

## Slide 77
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 78: SLA and Reliability Design Overview for the Enterprise Bearer WAN
Low-delay slice
Default slice
The enterprise bearer WAN uses reliability and SLA technologies to effectively ensure the quality of carried services. Therefore, reliability and SLA design are very important.
IP bearer network
Primary tunnel
Backup tunnel
Branch site
HQ
Reliability design
SLA design

## Slide 79: SLA Design Roadmap for the Enterprise Bearer WAN
2. Reliability design
Controller reliability design
1. SLA design
Device reliability design
QoS design
Slice design
Network reliability design

## Slide 80: SLA Technology Overview
In Huawei's CloudWAN solution, iMaster NCE-IP can compute paths based on bandwidth requirements and deliver forwarding paths (SR Policies) to network devices.
Although the controller can compute paths based on bandwidth requirements, the delivered path information does not contain any traffic rate limiting policy. As a result, the traffic rate on the forwarding path (SR Policy) may exceed the planned bandwidth.
To ensure that the traffic rate does not exceed the planned bandwidth, SLA technologies need to be deployed on the network to limit traffic bandwidth.
SLA technologies mainly include QoS and network slicing.
RR
PE1
PE3
BGP SR-Policy/PCEP
Network administrator
Deploys a tunnel with a bandwidth of 1 Gbit/s.
Plans paths based on bandwidth requirements.
SR Policy
2 Gbit/s traffic
SLA technology
1 Gbit/s traffic
Uses the SLA technology to ensure that the traffic rate does not exceed the planned bandwidth.

## Slide 81: QoS Planning Principles
The enterprise bearer network needs to provide differentiated service quality assurance for different services. QoS planning ensures that various services are properly forwarded on the bearer network. QoS planning mainly complies with the following four principles:
  Reasonableness: Resources must be allocated appropriately based on the importance of services.
  Consistency: QoS planning involves various behaviors (such as service classification, marking, scheduling, and rate limiting), which must be consistent on the entire network.
  Scalability: Current QoS policies must take into account future service expansion.
  Maintainability: Because services change rapidly in real-world situations, QoS policies may be frequently adjusted during routine maintenance. Ensure that QoS policies can be easily adjusted and maintained.
QoS Design
Slice Design

## Slide 82: QoS Design Suggestions
When the network is normal, a different link can be planned for each service of an enterprise to ensure that these services do not affect each other. However, when a link is faulty, the affected services are switched to other links, and bandwidth competition may occur. QoS policies need to be deployed for key services in a unified manner.
If there are more than eight types of enterprise services, they need to be properly classified and combined. The following is an example of common enterprise service planning.
QoS Design
Slice Design
Priority | Service | Scheduling Mode | Weight | Traffic Shaping | Drop Method
CS6/CS7 | Protocol packet | PQ | NA | NA | Tail drop
EF | Production service | PQ | NA | NA | Tail drop
AF4 | VoIP, video conference | PQ | NA | Configure rate limiting to prevent bandwidth starvation of low-priority services. | Tail drop
AF3 | Video surveillance | WFQ | Determined based on live network conditions. | NA | WRED
AF2 | Office service | WFQ | Determined based on live network conditions. | NA | WRED
AF1 | OA service | LPQ | NA | NA | Tail drop
BE | Other workloads | LPQ | NA | NA | Tail drop

## Slide 83: QoS Deployment Design
QoS planning requires that QoS features be properly deployed at different locations on the network. The following figure shows the deployment of different features on the network:
QoS Design
Slice Design
PE
PE
PE
P/RR
P/RR
CE
CE
CE
CE
PE
Bearer network
1. If the CE cannot classify or mark services, the services can be marked on the PE ingress.
3. Congestion avoidance and congestion management must be deployed in the outbound direction of all devices on the bearer network.
2. Desired flows must be specified on the PE ingress, and rate limiting must be configured on the PE ingress.

## Slide 84: Network Slicing Overview
Network slicing can be used to allocate dedicated network resources on a network to carry high-value service traffic.
Network slicing and SR tunnels apply to different network layers. Network slicing reserves resources on the Layer 1.5 or Layer 2 network and can be used together with SR tunnels.
Network slicing is generally implemented based on channelized sub-interfaces or FlexE.
QoS Design
Slice Design
Channelized sub-interface
Channelized sub-interface: Queue resources are isolated. Hierarchical scheduling is used to implement flexible and refined management of interface resources, provide bandwidth guarantee, and work with the controller to provide E2E resource reservation.
FlexE
FlexE: Queue and interface resources are isolated. Every resource is divided by TDM timeslot. This meets the requirements for exclusive resource use and resource isolation and provides flexible and refined management of interface resources.
SQ
GQ
VI
TM
PIC
Channelized sub-interface
DP
MAC
PHY
CS7
BE
SQ
GQ
VI
CS7
BE
Channelized sub-interface
…
TM
PIC
…
SQ
DP
FlexE client
FlexE shim
PHY
CS7
BE
FlexE client
SQ
DP
CS7
BE
MAC

## Slide 85: Network Slicing Design
Currently, existing devices mainly implement network slicing based on bandwidth.
A slice with the corresponding bandwidth is created based on actual service requirements. An SR tunnel is then bound to the slice for bearing.
QoS Design
Slice Design
Default slice
Primary tunnel
Backup tunnel
Service slice
Primary tunnel
Backup tunnel
SR BE tunnels or SR Policies can be deployed in the default slice.
SR Policies are deployed in the service slice. BFD is deployed to detect tunnel status, implementing HSB protection and VPN FRR within slices.
iMaster NCE-IP computes tunnels over slices based on affinity attributes.
iMaster NCE-IP optimizes traffic within slices.

## Slide 86: Network Slicing Application Scenarios
FlexE-based network slicing and channelized sub-interface-based network slicing have different application scenarios.
  It is recommended that FlexE be used to reserve resources for 50GE and higher-speed interfaces and channelized sub-interfaces be used to reserve resources for lower-speed interfaces.
  Only channelized sub-interface-based network slicing can be deployed across MSTP devices.
  FlexE- or channelized sub-interface-based network slicing can be deployed across OTN devices as required.
QoS Design
Slice Design
Transmission bearer network
IP bearer network
MSTP network
Channelized sub-interface-based network slicing deployment
Transmission bearer network
IP bearer network
OTN
FlexE- or channelized sub-interface-based network slicing deployment

## Slide 87: Typical Network Slicing Planning
Services can be placed into different slices based on application types. Moreover, different slicing technologies can be used based on transmission lines (MSTP or OTN).
QoS Design
Slice Design
Transmission bearer network
IP bearer network
MSTP network
Internal communication service slice (bandwidth: 5 Gbit/s)
External communication service slice (bandwidth: 5 Gbit/s)
Internet service slice (bandwidth: 1 Gbit/s)
New service slice (bandwidth: 1 Gbit/s)
Production service
Office service
Tested Service
Gold service
Silver service
Bronze service
App service
Internet access service
New service
Network slice
Because the transmission network uses MSTP, only channelized sub-interface-based network slicing can be used as the slicing technology.

## Slide 88: Enterprise Bearer WAN Reliability Design
2. Reliability design
Controller reliability design
1. SLA design
Device reliability design
QoS design
Slice design
Network reliability design

## Slide 89: Controller Local Reliability Design
iMaster NCE-IP has two high reliability modes:
  Active/standby protection mode: Only the services on the active node are in the running status. If a service process on the active node encounters a fault, the controller automatically starts the service process on the standby node to provide services.
  Cluster protection mode: When running properly, all cluster nodes are in the all-active state. If one node is faulty, other nodes share the load of the faulty node and continue to provide services evenly.
Network Reliability Design
Device Reliability Design
Controller Reliability Design
VM1
Management plane
OS/DB
…
VMn
Network analysis
OS/DB
VM2
Network management
OS/DB
VM3
Network control
OS/DB
Protection Layer | Component | Remarks
Application layer | Manager | Protection mechanism: application active/standby protection Performance indicators: RPO: 0s; RTO: ≤ 5 minutes
 | Controller | Protection mechanism: application active/standby protection Performance indicators: RPO: 0s; RTO: ≤ 60s
 | Analyzer | Protection mechanism: application active/standby protection Performance indicators: RPO: 0s; RTO: ≤ 5 minutes
Database | Database | Protection mechanism: database active/standby protection Performance indicators: RPO: 60s; RTO: ≤ 60s
Virtualization layer | FusionCompute | N/A
Server | TaiShan/RH/E9000 server | Management module: 1+1 backup; power supply: 1+1 backup Network port: 1+1 backup; hard disk: RAID1/RAID10
Notes: RPO: recovery point objective
RTO: recovery time objective

## Slide 90: Controller Reliability Design: Geographic Redundancy
Two controllers with consistent hardware configuration, service schemes, and other configurations are respectively deployed at the active and standby sites. Data in each database at the active site is synchronized to the standby site in real time based on the corresponding synchronization policy. If the active site fails, the arbitration service automatically starts the standby site for controller service continuity. You can also manually start the standby site in this case.
Network delay: < 50 ms; packet loss rate < 1%
Active site
DRMgr
Database
File
Data
DR
Service 1
Service 2
Service n
.
.
.
Services
Automatic/manual switchover
RTO ≤ 15 minutes
RPO ≤ 60s
(A third site)
Arbitration
Status detection and automatic switchover
Asynchronous replication RPO ≤ 60s (service data of Manager and Controller)
* You are advised to use redundant private lines for replication. Ensure that the switching time is less than 1s.
Database
DRMgr
DR
Standby site
Data
Service 1
Service 2
Service n
.
.
.
Services
File
NCE database
Linux
VM
Hypervisor
Replication management
Monitoring management
Switchover management
DRMgr
Heartbeat
Replication link
Network Reliability Design
Device Reliability Design
Controller Reliability Design
Notes: During the operation of the DR system, NCE monitors the association status of the primary and secondary sites over the heartbeat link and synchronizes data over the replication link. If the heartbeat or replication link between the primary and secondary sites is abnormal, the controller reports an alarm. The fault can be either manually rectified or automatically processed by the arbitration service.
The DRMgr service is developed by Huawei. Customers do not need to purchase third-party HA management software.

## Slide 91: Control Network Reliability Design for the Controller
GR needs to be deployed on both iMaster NCE-IP and devices, so that policy entries on forwarders can be retained for a longer time if the controller is faulty, maintained, or upgraded, or an active/standby controller switchover occurs.
PE
PE
PE
P/RR
P/RR
CE
CE
CE
CE
PE
Bearer network
Active site
Standby site
Heartbeat
GR
GR
Network Reliability Design
Device Reliability Design
Controller Reliability Design
Notes: Currently, the active/standby switchover of iMaster NCE-IP can be completed within 10 minutes. Therefore, the GR time cannot be less than 20 minutes.
GR: graceful restart

## Slide 92: Device Reliability Design
High device reliability is essential to the effective running of the network and needs to be guaranteed through the hardware, software, and protection mechanisms.
Device reliability deployment:
  1+1 active/standby protection for main control boards (NSR is recommended for smooth active/standby switchovers)
  Load balancing among multiple microengines for interface boards
  Maximum backup for power supplies
  Redundancy protection for other key components (such as fan modules)
1+1 active/standby protection for main control boards
Maximum backup for power supplies
Network Reliability Design
Device Reliability Design
Controller Reliability Design
Notes: NSR: non-stop routing

## Slide 93: Network Reliability Solution Overview
Multiple reliability technologies can be deployed on the bearer network to implement E2E reliability protection.
Network reliability technologies include:
  BFD/SBFD: is mainly used to check network connectivity.
  IP FRR: is mainly used to provide link and node protection for transit networks and can work with the LFA/RLFA/TI-LFA algorithm.
  Anycast FRR: is mainly used to provide protection for specific nodes, including transit and egress nodes.
  HSB: is mainly used to provide E2E tunnel protection.
  Mirror SID: is mainly used to provide protection for egress nodes.
  Microloop avoidance: is mainly used to prevent temporary loops caused by inconsistent route convergence time on the entire network.
Network Reliability Design
Device Reliability Design
Controller Reliability Design

## Slide 94: Source Network Reliability Design
The source network mainly includes source CEs, source PEs, and links between source CEs and source PEs. The source network may encounter the following faults:
  Source CE fault
  Link fault between a source CE and a source PE
  Source PE fault
These three types of faults can be quickly detected through BFD, and IP FRR (mainly based on the LFA/RLFA algorithm) can be used to compute backup links, so that services can be quickly switched to the protection paths.
PE
PE
PE
P
P
CE
CE
CE
CE
PE
Bearer network
Source network
1
2
3
Protection path
P
P
Original path
Network Reliability Design
Device Reliability Design
Controller Reliability Design

## Slide 95: Transit Network Reliability Design
The transit network mainly includes Ps, links between Ps and source PEs, and links between Ps.
The transit network may encounter the following faults:
  P fault
  Link fault between a P and a PE or between Ps
The following method can be used to protect the network against these two types of faults:
PE
PE
PE
P
P
CE
CE
CE
CE
PE
Bearer network
Transit network
P
P
1
2
  Deploy BFD to quickly detect network link faults.
  Use IP FRR (mainly based on the TI-LFA algorithm) to compute backup paths.
  If the transit network cannot meet service requirements due to a fault, use the tunnel HSB technology to switch traffic to the backup path.
Original path
Node/link protection path
Backup tunnel path
Network Reliability Design
Device Reliability Design
Controller Reliability Design
Notes: The transit network may fail to meet service requirements due to insufficient bandwidth or long delay. To detect the network bandwidth or delay, network quality detection technologies such as TWAMP or iFIT need to be deployed.

## Slide 96: Destination Network Reliability Design
The destination network mainly includes destination PEs, destination CEs, links between destination PEs and Ps, and links between destination PEs and destination CEs.
The destination network may encounter the following faults:
  Destination PE fault
  Link fault between a destination PE and a P
  Destination CE fault
  Link fault between a destination PE and a destination CE
The following method can be used to protect the network against the type 1 and type 2 faults:
  Deploy BFD to quickly detect network link faults.
  Use mirror SID or anycast FRR to switch traffic to the standby destination PE.
The following method can be used to protect the network against the type 3 and type 4 faults:
  Deploy BFD to quickly detect network link faults.
  Compute backup paths through IP FRR (mainly based on the LFA/RLFA algorithm).
PE
PE
PE
P
P
CE
CE
CE
CE
PE
Bearer network
Destination network
P
P
1
2
3
4
Original path
Node/link protection path
Network Reliability Design
Device Reliability Design
Controller Reliability Design

## Slide 97
Current Situation and Challenges of the Enterprise Bearer WAN
Huawei CloudWAN Solution Overview
Basic Design for the Enterprise Bearer WAN
Tunnel and VPN Design for the Enterprise Bearer WAN
SLA and Reliability Design for the Enterprise Bearer WAN
Optimization and O&M Design for the Enterprise Bearer WAN

## Slide 98: Optimization and O&M Design Overview for the Enterprise Bearer WAN
Network operation becomes the new focus after the initial stage of network construction is complete. Network optimization and O&M are essential to smooth network operation.
To better support subsequent network optimization and O&M, network optimization and O&M design must be performed in advance.
PE
PE
PE
PE
P
P
P
Bearer network
RR
Network optimization design
0:00
8:00
24:00
Maintenance window
Normal running
O&M design

## Slide 99: Optimization Design Roadmap for the Enterprise Bearer WAN
2. O&M design
User management
1. Network optimization design
Maintenance window
Network performance monitoring design
Network traffic optimization design
Application optimization design

## Slide 100: Network Performance Monitoring Overview
Network performance monitoring can be implemented in multiple ways, one of the most common being SNMP. However, as services impose increasingly more requirements on networks, new technologies are required to quickly obtain network performance indicators.
Network performance monitoring technologies commonly used on live networks include:
  SNMP: During performance monitoring, SNMP obtains network performance information in a query-reply manner. When frequently obtaining information, SNMP imposes heavy pressure on the device.
  Telemetry: Telemetry mainly obtains network performance information in a subscription-reporting manner. When frequently obtaining information, telemetry does not impose much pressure on the device.
  NQA: NQA is mainly used to detect network quality. NQA uses simulated traffic to test the network environment. Therefore, the test result is not so accurate.
  TWAMP: TWAMP is mainly used to detect network quality. Compared with NQA, TWAMP has a unified detection model and packet format, and is easy to deploy.
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 101: Application Scenarios of Network Performance Monitoring
In Huawei's CloudWAN solution, SNMP is used to collect common device performance information, telemetry is used to collect information that needs to be measured within seconds, and TWAMP is used to collect link quality-related performance data (including packet loss, delay, and jitter).
PE
PE
PE
PE
P
P
P
Bearer network
RR
SNMP
Telemetry
Used to measure network performance (including SR Policy performance) within seconds
Used to detect common device performance
TWAMP
TWAMP
Used to detect network link quality
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 102: Network Performance Monitoring Design
The major performance indicators for WAN services include:
  Link bandwidth usage (measured through telemetry)
  Link delay (measured through TWAMP)
  Tunnel bandwidth usage (measured through telemetry)
  Tunnel packet loss rate (measured through telemetry)
PE
PE
PE
PE
P
P
P
Bearer network
RR
TWAMP
TWAMP
TWAMP is used to measure link delay.
SR Policy
Telemetry
Telemetry is used to measure the link bandwidth usage, tunnel bandwidth usage, and tunnel packet loss rate.
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 103: Network Traffic Optimization Overview
MPLS TE uses the Constrained Shortest Path First (CSPF) algorithm to compute paths. This distributed computation and management mode, however, cannot manage network bandwidth resources in a coordinated manner.
Huawei's CloudWAN solution uses BGP-LS (SRv6 Policy) or BGP-LS + SR-MPLS Policy (PCEP) to obtain tunnel status and adjusts tunnel paths based on the network status.
RR
PE1
PE2
P1
PE4
PE3
BGP SR-Policy/PCEP
The controller optimizes forwarding paths based on network performance.
The controller delivers optimized forwarding paths.
SNMP/FTP/Telemetry
TWAMP
Severe packet loss occurs on links.
TWAMP or iFIT is used to measure network quality.
1
2
Devices report network performance data to the controller.
3
4
5
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 104: Network Traffic Optimization Design
Network optimization design focuses on two aspects: what to optimize and how to optimize.
What to optimize
  Simply put, optimization is to optimize service paths (LSPs). An LSP is a logical path equivalent to a tunnel, and a link is a physical path. One link can carry multiple tunnels, and one tunnel (LSP) corresponds to one service. Therefore, service paths can be changed based on either links or tunnels.
    Link optimization: When one or more links are selected for optimization, all LSPs carried by the selected links are involved in path computation.
    Tunnel optimization: When one or more tunnels are selected for optimization, the LSPs corresponding to the selected tunnels are involved in path computation.
How to optimize
  Optimization can be performed either automatically or manually:
    In an automatic optimization scenario, traffic is automatically analyzed, and the optimization is automatically performed at scheduled times.
    In a manual optimization scenario, traffic is manually optimized on demand based on network conditions.
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 105: Automatic Tunnel Optimization Design
If the network scale is too large for manual tunnel quality assurance, automatic optimization can be used to automatically analyze tunnel quality and optimize tunnel paths. This helps reduce manual maintenance costs and improve network optimization efficiency.
Automatic tunnel optimization applies to the following scenarios:
  Scheduled optimization
  Automatic optimization upon bandwidth threshold crossing
  Maintenance window-triggered optimization
The optimization trigger mode can be Traffic, Delay, or Delay + Traffic:
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design
Notes: Automatic optimization:
  Scheduled optimization: You can set the interval for automatically optimizing network paths to 5 minutes or longer to ensure that the current service paths are optimal.
  Automatic optimization upon bandwidth threshold crossing: You can set the link threshold. Then, when the bandwidth usage of a link exceeds the threshold, the system automatically adds tunnels over the link to the path computation queue and performs optimization when the optimization period arrives.
  Maintenance window-triggered optimization: You can maintain a node or link. During the maintenance, the node or link is unavailable. After the maintenance starts or ends, the controller automatically recomputes the paths of tunnels that pass through the node or link.
  The automatic optimization interval is an integer multiple of 5 minutes, for example, 10 minutes or 15 minutes.
Optimization policy:
  Traffic-based optimization: In this mode, the link threshold must be set. If the bandwidth usage of links exceeds the threshold, the controller determines whether to perform local or global optimization based on the number of threshold-crossing links.

## Slide 106
Notes:   Delay-based optimization: In this mode, the controller traverses and compares the configured delay of all tunnels with the accumulated delay collected from forwarders, and performs local optimization on all the tunnels whose accumulated delay exceeds the configured delay.
  Delay+traffic-based optimization: If either of the preceding trigger conditions is met, traffic optimization is performed.

## Slide 107: Manual Tunnel Optimization Design
In manual optimization, the operator analyzes the network status and then adjusts the network manually. Manual optimization can be performed on demand at any time.
Manual optimization is typically performed in the following scenarios:
  If the current traffic paths do not meet requirements, you can modify link constraints and then manually trigger optimization to change traffic paths.
  After configuring a service, you can manually perform network re-optimization to ensure that all tunnel paths are optimal.
  When the link quality deteriorates (or the bandwidth usage is high but does not reach the automatic optimization threshold) or the bandwidth usage of links is uneven (some links have high bandwidth usage while others are idle), you can manually perform local/global optimization.
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 108: Application Optimization Overview
On a network where VPN is deployed and application-based differentiated SLA path assurance is required, applications can be classified into different types and identified based on differentiated services code point (DSCP) values. The DSCP value corresponds to the color of a tunnel. Application traffic can be steered into the corresponding tunnel based on the DSCP value.
PE
PE
PE
PE
P
P
P
RR
CE
CE
Service 1 DSCP EF
Service 2 DSCP AF41
SR Policy
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 109: Application Optimization Design
A different DSCP value must be assigned to each application prior to application optimization. Generally, DSCP values are assigned to applications on the CE side.
To enable different types of applications to be carried over different tunnels, the SR Policy group+DSCP mode is generally used.
PE
PE
PE
PE
P
P
P
RR
CE
CE
Service 1 DSCP EF
Service 2 DSCP AF41
VPN instance
SR Policy group 1
SR Policy group 2
Applications from the same VPN are differentiated by DSCP value.
DSCP values are assigned to applications on the CE side.
The traffic of different applications is steered into different SR Policies based on DSCP values.
SR Policy
Network Traffic Optimization Design
Network Performance Monitoring Design
Application Optimization Design

## Slide 110: Optimization Design Roadmap for the Enterprise Bearer WAN
2. O&M design
User management
1. Network optimization design
Maintenance window
Network Performance Monitoring Design
Network Traffic Optimization Design
Application Optimization Design

## Slide 111: User Type Overview
Operations that can be performed by a user on the cloud WAN vary according to the user type. iMaster NCE-IP provides the following default user roles:
  Administrators: Users attached to this role have permission to perform operations except managing users, querying security logs, querying personal security logs, and viewing online users.
  SMManagers: Users attached to this role have permission to manage users, query security logs, and view online users.
  Operators: Users attached to this role have permission to perform non-security-related operations.
  Monitors: Users attached to this role have permission to view non-security-related functions, but do not have permission to perform the corresponding operations.
Maintenance Window
User Management
System administrator (admin)
Administrators
Operators
Monitors
SMManagers

## Slide 112: User Monitoring Overview
By monitoring user sessions, the security administrator can learn information such as online users in the user system, IP addresses used by these users to access the system, access time, and roles of these users. When detecting that a user is attempting to perform unauthorized operations, the security administrator can send an instant message to the user or forcibly deregister the user.
  A user session refers to the connection between a user and the system. A session starts when a user logs in and ends when the user deregisters or logs out. A user can generate multiple sessions.
  The maximum number of online sessions allowed for a user is specified by the Max. online sessions parameter.
  The function of monitoring user sessions does not involve users' personal information.
Maintenance Window
User Management

## Slide 113: Maintenance Window Overview
When cutting over or maintaining devices and links, you can configure maintenance policies for them. The Network Path Navigation app allows you to configure maintenance policies for NEs and links.
After the maintenance starts, the system generates new service tunnel paths that bypass the maintained devices and links. After the maintenance is complete, the system triggers path computation for traffic optimization.
During the maintenance window, you can set the maintenance time and maintain the target devices. During the maintenance, the traffic does not pass through the maintained devices.
Peak hours
Maintenance window
Peak hours
Target device for maintenance
Target device under maintenance
Traffic bypasses the maintained device.
After the maintenance is complete, traffic recovers.
Maintenance Window
User Management

## Slide 114
(Multiple-answer question) Which of the following tunnels can be used to carry IPv6 services? ( )
  SR-MPLS BE tunnel
  SRv6 BE tunnel
  SR-MPLS Policy
  SRv6 Policy
Notes: ABCD

## Slide 115
When designing the enterprise bearer WAN, you need to design the infrastructure network first, including the physical network, IPv4/IPv6 addresses, and IGP/BGP.
Tunnels, including SR-MPLS BE tunnels, SR-MPLS Policies, SRv6 BE tunnels, and SRv6 Policies, can be established on the infrastructure network. During tunnel design, pay attention to the tunnel path planning, traffic diversion, and best-effort forwarding mode.
After a tunnel is established, it can carry VPN services. VPN planning must be based on enterprise service types and requirements.
Reliability and SLA assurance are also very important for services. QoS and network slicing design helps ensure service SLA, and high reliability design for controllers, devices, and networks helps ensure service reliability.
A network needs optimization and maintenance after it is constructed. Optimization design needs to cover both performance monitoring and traffic optimization. The maintenance scope needs to be divided based on user roles, and the network needs to be maintained at a proper time.