## Slide 1
Wang Changli/wwx408647
2020.04.17

## Slide 2: Introduction to Network Programming and Automation

## Slide 3
Networks are evolving to be more open, more flexible, and simpler. Huawei's vision is to help customers build intent-driven networks (IDNs).
Network openness and programmability are prerequisites of intent-driven networks.

## Slide 4
Upon completion of this course, you will be able to describe:
  Background of network programming and automation.
  Network openness levels.
  Open capabilities of Huawei iMaster NCE.
  Positioning and capabilities of network automation engineers.

## Slide 5
Network Programming and Automation
Network Automation Engineers
Course Overview

## Slide 6: Background: Complex Networks
From the first day when the computer network is generated, the network is complex and difficult to manage, which is reflected in the following aspects:
  There are various network devices such as routers, switches, firewalls, and intrusion detection system (IDS).
  Devices from different or even the same vendors are managed in different ways.
  Complex devices result in complex network management.
Diverse network devices
1
Different device management modes
2
Complex network management
3
Router
Switch
Firewall
Device from another vendor
Multiple network management systems
CLI
SNMP
Web
IPFIX
Notes: Different network devices communicate with each other through routing protocols.
There are different device management modes, such as SNMP, CLI, IPFIX, and Web UI.

## Slide 7: Background: Network Architecture Transformation
APP
Orchestration application layer
Controller layer
Device layer
NBI
SBI
Data forwarding
Service orchestration
Service collaboration
Software defined networking (SDN) brings about network architecture transformation. It introduces a network controller to implement centralized control from a global perspective, achieving objectives such as fast service deployment, traffic optimization, and network service openness.
Notes: Orchestration application layer: implements various upper-layer applications of user intents. Typical orchestration applications include OSS and OpenStack. The OSS is responsible for service collaboration on the entire network. The OpenStack is used for network, computing, and storage service collaboration in a data center. There are other orchestration-layer applications. For example, a user wants to deploy a security application. The security application does not care about the device deployment location but invokes a controller NBI, for example, Block (Source IP, DestIP). Then the controller delivers an instruction to network devices. This instruction varies according to the southbound protocol.
Controller layer: The entity at the controller layer is the SDN controller, which is the core of the SDN network architecture. The control layer is the brain of the SDN system. Its core function is to implement network service orchestration.
Device layer: The network devices receive instructions from the controller and forward the instructions.
NBIs: NBIs are used by the controller to interconnect with the orchestration application layer. The main NBIs are RESTful interfaces.
SBIs: SBIs are protocols used for interaction between the controller and devices, including NETCONF, SNMP, OpenFlow, and OVSDB.

## Slide 8: Basic Network Automation
Network automation means that tools are used to implement automatic network deployment, operation, and maintenance, gradually reducing the dependency on human resources.
There are many open-source tools that implement network automation in the industry, such as Ansible, SaltStack, Puppet, and Chef. These tools connect to devices through SSH to implement batch operation and management, achieving basic network automation.
Python
Chef
Ansible
NMS tool
Automation scripts
SaltStack
Shell
Network automation keywords
Notes: Network automation tools implement basic network automation. That is, tools connect to devices through SSH to implement batch operation and management.

## Slide 9: Development of Network Automation
In basic network automation, networks are managed on the CLI. The pain point is that network devices return unstructured data (text display), which is inconvenient for computers to process. The basic requirement of network automation development is that devices provide structured data, which can greatly promote the development of network automation. Devices provide NETCONF/RESTCONF interfaces to provide data in XML or JSON format.
Structured data: easy to understand for machines
{ "Interfaces":
{ "GigabitEthernet0/0/0":
{ "InUti": "10", "OutUti": "20", "inErrors": "0", "outErrors": "0" },
"GigabitEthernet0/0/1":
{"InUti": "20", "OutUti": "30", "inErrors": "0", "outErrors":"0"}
}
}
Unstructured data: easy to understand for humans
Interface InUti OutUti inErrors outErrors
GigabitEthernet0/0/0 10% 20% 0 0
GigabitEthernet0/0/1 20% 30% 0 0
...
Network devices
CLI/SSH, SNMP
NETCONF, RESTCONF
Discussion: What are the benefits of open APIs?
Notes: Unstructured data can be easily understood by humans, but it is difficult for machines to understand and difficult for automatic data collection.
NETCONF/RESTCONF has many advantages not limited to providing structured data. For details, see NETCONF Principles and Practices.

## Slide 10: Network Openness and Programmability
Network openness and programmability is to use programming methods to implement automated networks on the premise of open networks.
In the early stage of SDN commercial use and in the future, traditional networks and SDN networks will coexist on a large scale. Network openness is implemented at two levels: device openness and SDN platform openness.
RESTful API
CLI/SSH, SNMP, NETCONF, RESTCONF, Telemetry, OPS, ...
Device-based openness and programmability
SDN-based openness and programmability

## Slide 11: Huawei iMaster NCE, Open and Programmable
iMaster NCE (NCE for short) is an innovative network cloud engine of Huawei. The overall open programming capabilities of NCE include automation, analytics, and intent engines. The goal is to build a full-lifecycle open programmable architecture to meet customer requirements for openness and programmability. NCE service openness and programmability are designed to help customers implement service automation.
Intent
Automation
Analytics
Intent engine
Automation engine
Analytics engine
Design
Conversion
Verification
Sensing
Analysis
Decision making
Management unit
Control unit
Open and programmable NCE services
Notes: iMaster NCE is not only a controller, but also provides analysis and network management functions.

## Slide 12
Network Programming and Automation
Network Automation Engineers
Course Overview

## Slide 13: Overview and Objectives
Generally, network engineers focus on network protocol principles, configuration, and management of network devices. System engineers focus on operating system principles, configuration, and management of system services. Development engineers focus on programming languages, algorithms, and other related development capabilities.
Network automation engineers for network programming and automation must be all-rounders who master skills of these positions to some extent. This part introduces capability requirements on network automation engineers and how to implement network programming and automation.

## Slide 14: Network Automation Engineers
Network engineers:
  Network engineers are professionals who master network technologies, have professional skills, competence, and project management experience in the network engineering field. They are able to fully communicate with customers or other project stakeholders onsite. In addition, they can develop implementation solutions and project plans (recognized by project stakeholders) based on customer requirements and environment factors, fully mobilize resources of all parties to ensure timely and high-quality project implementation, and provide training for stakeholders and deliver engineering documents after the project is implemented.
Network automation engineers:
  They are professionals who have network skills, competence, and project management experience in the network automation field. They aim to meet the requirements of automatic deployment, development, and O&M of enterprise networks.

## Slide 15: Comprehensive Competence Model
Compared with the comprehensive competence model of network engineers, network automation engineers have the same basic competence and professional skills, but have different skill requirements in terms of expertise.
Comprehensive competence model for network engineers
Expertise
Technical knowledge
Product knowledge
Engineering knowledge
Industrial knowledge
Process specification
Basic qualification
Learning ability
Information search
Service consciousness
Values
Business etiquette
Professional skills
Communication competence
Problem solving
Presentation capability
Service management
Team collaboration
In addition to basic network technologies, network automation engineers need to master development-related technology, product, and engineering knowledge.

## Slide 16: Expertise
The expertise of network automation engineers must be all-rounders who master skills of network engineers, system engineers, and development engineers to some extent, including but not limited to the following capabilities:
Operating system (OS)
Network technology
Open network architecture
Programming language
Source code management
A good command of at least one programming language
Source code control to help developers manage and store code
A good command of the data structure and resource structure of open networks
A good command of basic network protocol principles and network engineering technologies
Understanding the basic principles and mechanism of the OS
Other professional knowledge
Other related professional knowledge, such as database knowledge
Notes: Network automation developers may need to have more professional knowledge, such as database, algorithm, cryptography, software development lifecycle management, development framework, big data, cloud computing, and artificial intelligence (AI), depending on the specific work content and scenario.

## Slide 17: Learning Objectives
Others
Programming language
This course focuses on the following capabilities of network automation engineers:
Python and integrated development environment (IDE)
OS
Network technology
Open network architecture
Source code management
Git
XML/JSON, Huawei NCE northbound RESTful API, and Huawei NCE service openness and programmability
Principles and code implementation of network technologies such as NETCONF, YANG, Telemetry, SNMP, and SSH
N/A
HTTP/TLS, northbound invocation tools

## Slide 18
Network Programming and Automation
Network Automation Engineers
Course Overview

## Slide 19: Introduction to Course Modules
This course consists of four modules: programming basics, device openness and programmability, NCE northbound openness, and NCE service openness and programmability.
Programming basics
Device openness and programmability
NCE northbound openness
NCE service openness and programmability
Basic programming knowledge, including:
Python basics
Python advanced knowledge
Source code management
Network programming and automation course module based on device openness capabilities and Python practices:
SSH
SNMP
NETCONF/RESTCONF
Telemetry
Huawei device OPS
Network automation course module based on the northbound openness capability of Huawei NCE, including:
REST and RESTful
HTTP/HTTPS
RESTful invocation tools
Scenario-based invocation practice (campus network and DCN)
Course module based on the NCE service open programming function, including:
Jinjia2
Compilation of an NE driver package
Compilation of a service driver package
Scenario-based service provisioning practices and NBI invoking
Notes: An open programmability system (OPS) is an open platform that provides representational state transfer (RESTful) application programming interfaces (APIs) to achieve programmability, allowing third-party applications to run on the platform.

## Slide 20: Python Overview
Python is a fully open-source high-level programming language. It was created by Guido van Rossum.
All coding practices in this course are based on Python.
Advantages of Python:
Python has elegant syntax, dynamic typing, and interpretative nature. Python allows learners to focus on program logic instead of learning syntax details.
Python supports both process-oriented and object-oriented programming.
Python has rich third-party libraries.
Python can invoke code written in other languages, therefore it is known as "glue language".
Disadvantages of Python:
Low running speed. Python is an interpreted language that can run without compilation. The code is translated line by line into machine code that the CPU can understand, which is time-consuming.
In addition to language advantages, Python has abundant third-party libraries. Therefore, Python can be used in many fields, such as AI, data science, apps, and automatic O&M scripts.

## Slide 21: Python Learning Map
Syntax basics
Data types and operators
Control flow
Functions
Python standard library
Python basics
I/O operation
Exception processing
Object-oriented programming
Regular expression
Python advanced knowledge
Decorators
Iterator and generator
Multitasking
Python environment setup
Others
Python can be used in many fields. To facilitate Python learning and use in the network engineering field, this course divides Python into basics and advanced learning. Python basics enable you to basically implement network programming and automation.

## Slide 22: Device Openness and Programmability
Device openness and programmability aim to provide engineers with guidance on how to implement network automation through programming based on device openness capabilities.
The following figure shows the open capabilities of Huawei network devices. This course module focuses on how to use Python modules.
#!/usr/bin/env python
...
Python code
Network devices
CLI/SSH
SNMP
NETCONF
RESTCONF
Telemetry
MIB
YANG
Open Programmability System
FTP
paramiko
pysnmp
ncclient
requests
grpc
Uploading .py files
Notes: Part 1 of this course module describes how to use Python modules, including paramiko, pysnmp, ncclient, requests, and grpc, to communicate with devices.
Part 2 focuses on the OPS. The OPS refers to open programmability provided by Huawei devices. You can upload Python code to a device, and the device runs the code to implement specified functions.

## Slide 23: NCE Northbound Openness
The openness and programmability of the controller provide engineers with guidance on how to implement network automation through programming based on the open capabilities of the SDN controller.
Huawei iMaster NCE includes controllers and provides northbound RESTful APIs. This course module focuses on how to use tools to invoke NCE NBIs.
RESTful API
CloudFabric
SD-WAN
CloudCampus
NCE-IP
Network devices

## Slide 24: Huawei NCE Service Openness and Programmability
NCE service openness and programmability is a subsystem of NCE. It provides E2E programing capabilities including the openness of NE-layer functions and the openness of network service functions.
Engineers compile an NE driver package (specific NE driver, SND) and a service driver package (specific service plugin, SSP) to implement the following functions:
  Multi-vendor device management
  User-defined network services
  Web-based service management
  Automatic exposure of northbound RESTful APIs
SSP
SND
Open programmability framework of Huawei NCE
SSP
SND
NCE automatically generates NETCONF packets and sends the packets to a device, or configure a device in CLI/SSH mode.
YANG
Service callback logic
NE profile 1
NE profile 2
NE YANG 2
Jinjia2
Python
YANG
YANG
NE YANG 1
RESTful API
Web UI
Notes: An SND abstracts device capabilities based on a device YANG model. A user can generate an SND based on device YANG files and a few Python code. After the SND is uploaded to NCE, device management and service provisioning can be implemented. SND types include NETCONF SNDs, CLI SNDs, and customized SNDs.
  NETCONF SND: provides the capability of converting YANG files into NETCONF files.
  CLI SND: provides the conversion capability from YANG to CLI.
  Customized SND: provides the capability of converting YANG to other protocols such as RESTCONF.
An SSP allows user to customize network services (apps), for example, quickly provision L3VPN services. These types of services or application involve multiple devices and protocols and are presented as an SSD. To compile an SSD, an engineer needs to compile service YANG files, Python scripts (service callback logic) for service mapping, and Jinjia2 template. The basic principles are as follows (from north to south):
  A service model automatically generates northbound interfaces or UIs, which are invoked by an external system to initiate a service request.

## Slide 25
Notes:   The service request is processed by the service logic compiled by the user. The processing includes two parts: Python code processing and Jinjia template processing.
    Python code processing implements service logic irrelevant to vendors.
    Template processing implements the logic related to vendors. A template is the data delivered to a device model. Different vendors use different templates. In this way, a user-defined service model is converted into a device model.
  The SND converts the device model into protocol packets and delivers the packets to the device. For example, the SND delivers the packets to a device through NETCONF.

## Slide 26
(Multiple) Which modules are included in this course? ( )
Programming basics
Device openness and programmability
NCE northbound openness
NCE openness and programmability
What are the differences between network automation engineers and network engineers?
Notes: ABCD
Network automation engineers: They are professionals who have network skills, competence, and project management experience in the network automation field. They aim to meet the requirements of automatic deployment, development, and O&M of enterprise networks. For details, see P14 to P16.

## Slide 27
Network programing and automation is to use programming methods to implement automated networks on the premise of open networks. Network openness is implemented at two levels: device openness and SDN platform openness.
Network automation engineers must be all-rounders who master skills of network engineers, system engineers, and development engineers to some extent to support enterprise network automation.
This course consists of four modules: programming basics, device openness and programmability, NCE northbound openness, and NCE service openness and programmability. Next, let's learn network programmability.