## Slide 1
2020.06.12
2020.06.12
2020.06.12
Wei Jiongjian/wwx935519
2020.06.12
Wan Changli/wx408647
2020.06.12

## Slide 2: SNMP Fundamentals and Practices

## Slide 3
As a network expands in scale, network management becomes complex and inefficient because various types and models of devices from different vendors coexist on the network. To simplify network management, the Simple Network Management Protocol (SNMP) is developed to standardize network management interfaces and protocols and uniformly manage all devices on the network.
To cope with diversified and changing O&M requirements, network administrators need to have certain programming capabilities to improve O&M efficiency. PySNMP implements SNMP functions and is a powerful tool for network administrators to improve O&M capabilities.
This course describes basic functions, fundamentals, and basic configurations of SNMP. It also describes PySNMP and its practices.

## Slide 4
Upon completion of this course, you will be able to:
  Describe basic SNMP concepts.
  Describe basic SNMP functions.
  Understand SNMP fundamentals.
  Perform basic SNMP configurations.
  Use PySNMP to perform SNMP operations.

## Slide 5
Overview of SNMP
SNMP Fundamentals
Basic SNMP Configurations
Introduction to PySNMP

## Slide 6: Overview of SNMP (1/3)
When various types and models of devices from different vendors coexist on a network, separate network management is complex and inefficient.
Network administrator
Separate management
Vendor A
Switch
Vendor A
Firewall
Vendor A
AC
Vendor A
Router
Vendor B
Router
Vendor C
Switch
Vendor D
Switch
As the network scale expands, unified network management is imperative.
Notes: Different vendors use their proprietary protocols to manage their own devices, resulting in complex and inefficient network management.

## Slide 7: Overview of SNMP (2/3)
The Internet Engineering Task Force (IETF) defines SNMP to implement unified management of devices.
Network administrator
Unified management
Vendor A
Switch
Vendor A
Firewall
Vendor A
AC
Vendor A
Router
Vendor B
Router
Vendor C
Switch
Vendor D
Switch
SNMP
A network administrator can uniformly manage all SNMP-capable network devices.

## Slide 8: Overview of SNMP (3/3)
SNMP has three versions: SNMPv1, SNMPv2c, and SNMPv3.
It is the initial version of SNMP and easy to implement at a low cost.
It cannot read a large amount of data and has low security.
It applies to secure networks or small-scale networks that have only a few devices and do not require high security, such as campus networks and small-scale enterprise networks.
SNMPv1
It extends functions based on SNMPv1, and provides the GetBulk and Inform operations.
It does not enhance security.
It applies to large-scale networks that have a large number of devices and do not require high security or secure networks that have heavy service traffic and may encounter traffic congestion.
SNMPv2c
It enhances security, and provides identity authentication and encryption.
It uses a new system architecture, and features strong adaptability, simple management, and good expansibility.
It applies to diversified networks especially those having high security requirements and allowing only authorized administrators to manage network devices.
SNMPv3
1990
1996
1998
Notes: SNMPv2c
  GetBulk operation: is performed by a network management system (NMS) to query information about managed devices in batches.
  Inform operation: is performed by a managed device to notify the NMS of a fault or event on the device and requires an acknowledgement from the NMS.
SNMPv3
  Strong adaptability: It adapts to both simple and complex networks.
  Simple management: It consists of multiple independent sub-systems and applications. When a fault occurs in an SNMP system, it is easy to locate the sub-system where the fault is originated according to the fault type.
  Good expansibility: Modules can be added to expand an SNMP system. For example, a module can be added to the security sub-system to run a new security protocol.

## Slide 9
Overview of SNMP
SNMP Fundamentals
Basic SNMP Configurations
Introduction to PySNMP

## Slide 10: SNMP Management Model
Basic SNMP concepts:
  Network management system (NMS): a system that uses SNMP to manage network devices
  Agent: a process running on a managed device that interacts with the NMS
  Management information base (MIB): a database containing the variables (information that can be queried and set by the agent) maintained by a managed device
  Managed object: an object to be managed on a network device, for example, a hardware component (such as an interface card) or a set of parameters configured for a piece of hardware or software
  Device: a device managed by the NMS
NMS
Agent
MIB
Managed
object
Device
SNMP

## Slide 11: MIB
  A MIB is a database containing the variables (information that can be queried and set by the agent) maintained by a managed device. It defines the attributes of managed objects, including:
  Object identifier (OID)
  Status
  Access permission
  Data type
A MIB uses a data structure containing all objects that may be managed on the network. Because the data structure is similar to a tree structure, a MIB is also called an object naming tree.
Objects on the Internet
Notes: A MIB is independent of a specific network management protocol. Device vendors can integrate SNMP agent software into their products (for example, routers), but they must ensure that this software complies with relevant standards after new MIBs are defined. Users can use the same network management software to manage routers containing MIBs of different versions. However, the network management software cannot manage a router that does not support the MIB function.
MIBs fall into public and private ones.
  Public MIBs are defined by RFCs and used for structure design of public protocols and standardization of interfaces. Most device vendors need to provide SNMP interfaces according to the specifications defined in RFCs.
  Private MIBs are the necessary supplement of public MIBs. Some enterprises develop proprietary protocols or special functions, they can design private MIBs to improve the management functions of SNMP interfaces. In addition, private MIBs enable third-party NMS software to manage devices that use proprietary protocols or have special functions. For example, OIDs of Huawei MIB objects start with 1.3.6.1.4.1.2011.

## Slide 12: Common MIB Objects
Objects used for query or modification
Object used for trap notification
OID | Object Name | Syntax | Maximum Access | Description
1.3.6.1.2.1.2.1 | ifNumber | Integer | read-only | Number of network interfaces in the system (regardless of the interface status).
1.3.6.1.4.1.2011.5.25.41.1.2.1.1.3 | hwIpAdEntNetMask | IpAddress | read-create | Subnet mask of an IP address.
OID | Object Name | Bound Variable | Description
1.3.6.1.6.3.1.1.5.3 | linkDown | ifIndex ifAdminStatus ifOperStatus ifDesc | It is detected that the ifOperStatus object has changed to the Down state from another state (not notPresent) which is represented by the value of ifOperStatus.
Notes: The maximum access of a MIB object specifies the operations that an NMS can perform on the MIB object. The options include:
  not-accessible: No operation can be performed.
  read-only: Read information.
  read-write: Read information and modify configurations.
  read-create: Read information, and modify, create, and delete configurations.
When generating a trap, a device reports the type of the current trap together with some variables. For example, when sending a linkDown trap, a device also sends variables such as the index and current configuration status of the involved interface.
  ifIndex: indicates the interface index.
  ifAdminStatus: indicates the interface management status, that is, whether the interface is shut down. The options include undo shutdown and shutdown.
  ifOperStasuts: indicates the interface operational status, that is, the link layer protocol status of the interface. The options include Up and Down.
  ifDesc: indicates the interface description.

## Slide 13: Basic SNMP Operations
An NMS uses SNMPv3 to send query and set operation instructions to managed devices, receive operation responses, and listen on trap information sent by managed devices.
Function | SNMPv3 Operation | Description
Query | Get | Obtains one or more variables from an SNMP agent.
 | GetNext | Obtains the next variable from an SNMP agent in lexicographical order.
 | GetBulk | Queries information from an SNMP agent in batches.
Set | Set | Requests an SNMP agent to set one or more variables.
Trap | Trap | An SNMP agent sends traps to notify the NMS of events generated by the managed device.
 | Inform | Provides similar functions to the trap operation. The difference is that the inform operation requires an acknowledgement from the NMS. Therefore, informs occupy more system resources than traps.
Response | Response | A response message is sent by an SNMP agent in response to the Get or Set operation or by an NMS in response to an inform.
Notes: This document describes SNMPv3 operations.

## Slide 14: Security Enhancement
SNMP faces security threats when performing basic operations such as Get and Set. SNMPv3 is more secure than SNMPv1 and SNMPv2c.
  Basic concepts:
    Group: a collection of users with a specific security level. The security levels include:
      Level 1: authPriv (authentication and encryption)
      Level 2: authNoPriv (authentication and no encryption)
      Level 3: noAuthNoPriv (no authentication and no encryption)
    View: a set of MIB objects that are accessible to users
  SNMPv3 enhances security with the following models:
    User-based security model (USM):
      Identity authentication: When receiving a message, an agent (or NMS) determines whether the message is from an authorized NMS (or agent) and whether the message has been modified during transmission.
      Data encryption: The NMS and agent use a symmetric key system, and use the same key to encrypt and decrypt data.
    View-based access control model (VACM): controls access of user groups based on views.
Notes: SNMPv1 and SNMPv2c provide user authentication based on community names, which has the following security risks:
  Most network product vendors deliver their devices with the default SNMP read-only community name being Public and the default read-write community name being Private. In most cases, network management personnel do not modify the default settings.
  SNMP community names are transmitted in plain text on the network, which may cause information leakage.

## Slide 15: SNMP Operation: Get
Get operation: obtains one or more variables from the SNMP agent of a managed device. The following shows how an NMS obtains the IP address of a specified interface on a managed device through the Get operation.
NMS
UDP port 162
Managed device
UDP port 161
Get
IP address
of GE0/0/1?
Encryption module
Get
Abstract
Encrypted
information
Response
10.0.1.1/24
Response
10.0.1.1/24
Response
Abstract
Encrypted
information
Get
IP address
of GE0/0/1?
Authentication module
Encryption module
Authentication module
Notes: The listening UDP port of a managed device is 161, so Get, GetNext, GetBulk, and Set packets are destined for port 161.
The listening UDP port of the NMS is 162, so Trap and Inform packets are destined for port 162.
The authentication and encryption modules provide the same identification and encryption functions as the USM in SNMPv3 to encrypt the sent SNMP packets and authenticate received the SNMP packets respectively.

## Slide 16: SNMP Operation: GetNext
GetNext: obtains the next variable from an SNMP agent in lexicographical order. The following shows how an NMS obtains the IP address of the next interface on a managed device through the GetNext operation.
GetNext
IP address
of GE0/0/2?
GetNext
GetNext
IP address
of GE0/0/2?
Response
Response
10.0.2.1/24
Response
10.0.2.1/24
NMS
UDP port 162
Managed device
UDP port 161
Abstract
Encrypted
information
Abstract
Encrypted
information
Encryption module
Authentication module
Encryption module
Authentication module

## Slide 17: SNMP Interaction: GetBulk
GetBulk: queries information from an SNMP agent in batches. The following shows how an NMS queries IP addresses of all interfaces on a managed device through the GetBulk operation.
GetBulk
IP addresses of
all interfaces?
GetBulk
Response
GetBulk
IP addresses of
all interfaces?
Response
IP addresses of
GE0/0/1, GE0/0/2…?
Response
GE0/0/1 IP: …
GE0/0/2 IP: …
NMS
UDP port 162
Managed device
UDP port 161
Abstract
Encrypted
information
Abstract
Encrypted
information
Encryption module
Authentication module
Encryption module
Authentication module

## Slide 18: SNMP Interaction: Set
Set: sets one or more variables through an SNMP agent. The following figure shows how an NMS sets an IP address for a specified interface on a managed device through the Set operation.
Set
Set the IP address of
GE0/0/3 to 10.0.3.1/24
Set
Response
Response
Success
Set
Set the IP address of
GE0/0/3 to 10.0.3.1/24
Response
Success
NMS
UDP port 162
Managed device
UDP port 161
Abstract
Encrypted
information
Abstract
Encrypted
information
Encryption module
Authentication module
Encryption module
Authentication module

## Slide 19: SNMP Interaction: Trap
Trap: The SNMP agent of a managed device sends traps to notify an NMS of certain events generated by the managed device. The following shows how the SNMP agent of a managed device sends a trap to notify an NMS of high CPU usage of the device.
Trap
Trap
High CPU usage
Trap
High CPU usage
NMS
UDP port 162
Managed device
UDP port 161
Abstract
Encrypted
information
Encryption module
Authentication module
Encryption module
Authentication module

## Slide 20: SNMP Interaction: Inform
Inform: provides similar functions to the trap operation. The difference is that the inform operation requires an acknowledgement from the NMS. The following shows how the SNMP agent of a managed device sends an inform to notify an NMS of high CPU usage of the device.
Inform
High CPU usage
Inform
Inform
High CPU usage
Response
Message received
Response
Response
Message received
NMS
UDP port 162
Managed device
UDP port 161
Abstract
Encrypted
information
Abstract
Encrypted
information
Encryption module
Authentication module
Encryption module
Authentication module

## Slide 21
Overview of SNMP
SNMP Fundamentals
Basic SNMP Configurations
Introduction to PySNMP

## Slide 22: Basic SNMP Configurations (1/3)
[Huawei] snmp-agent
Enable the SNMP agent function.
[Huawei] snmp-agent sys-info version [v1 | v2c | v3]
Configure the SNMP version.
[Huawei] snmp-agent group v3 group-name { authentication | noauth | privacy } [ read-view view-name | write-view view-name | notify-view view-name ]
Create or update a MIB view.
The SNMP version used on the device must be the same as that on the NMS.
4. Create an SNMP group by mapping SNMP users to SNMP views.
[Huawei] snmp-agent mib-view view-name { exclude | include } subtree-name [mask mask]
This command is used to create an SNMPv3 group, specify the authentication and encryption modes, and configure one or more of the following views: read-only view, read-write view, and notification view. It is a mandatory command on networks that require high security.

## Slide 23: Basic SNMP Configurations (2/3)
Configure the authentication mode and key for an SNMPv3 user.
[Huawei] snmp-agent usm-user v3 user-name authentication-mode { md5 | sha | sha2-256 }
[Huawei] snmp-agent usm-user v3 user-name privacy-mode { aes128 | des56 }
Configure the encryption mode and key for an SNMPv3 user.
[Huawei] snmp-agent usm-user v3 user-name group group-name
Add a user to an SNMP group.
[Huawei] snmp-agent target-host trap-paramsname paramsname v3 securityname securityname { authentication | noauthnopriv | privacy }
Set parameters for the device to send traps.

## Slide 24: Basic SNMP Configurations (3/3)
Enable all trap functions.
[Huawei] snmp-agent trap enable
[Huawei] snmp-agent trap source interface-type interface-number
Configure the source interface from which traps are to be sent.
This command only enables the device to send traps. It must be used together with the snmp-agent target-host command, which specifies the host to which traps are to be sent.
[Huawei] snmp-agent target-host trap-hostname hostname address ipv4-address trap-paramsname paramsname
Configure the target host of traps.
An IP address must have been configured for this source interface.

## Slide 25: SNMPv3 Configuration Example (on a Managed Device)
NMS
Managed device
192.168.1.10
GE0/0/1
Configurations on R1:
[R1]snmp-agent
[R1]snmp-agent sys-info version v3
[R1]snmp-agent group v3 test privacy
[R1]snmp-agent usm-user v3 R1 test authentication-mode md5 HCIP-Datacom123 privacy-mode aes128 HCIP-Datacom123
[R1]snmp-agent target-host trap-paramsname param v3 securityname sec privacy
[R1]snmp-agent target-host trap-hostname nms address 192.168.1.10 trap-paramsname param
[R1]snmp-agent trap source GigabitEthernet 0/0/1
[R1]snmp-agent trap enable
Info: All switches of SNMP trap/notification will be open. Continue? [Y/N]:y
R1
Enable SNMP on R1 and set the SNMP version to v3.
Create the SNMPv3 group test, and set both the encryption and authentication modes to privacy.
Create the SNMPv3 user R1, and set both the authentication and encryption keys to HCIP-Datacom123.
Create the trap sending parameter list param and set the user security name to sec.
Set the IP address of the target host for receiving traps to 192.168.1.10.
Enable the trap function and specify GE0/0/1 as the source interface from which traps are to be sent.

## Slide 26
Overview of SNMP
SNMP Fundamentals
Basic SNMP Configurations
Introduction to PySNMP

## Slide 27: Introduction to PySNMP
PySNMP is a third-party module of Python and implements all functions of SNMPv1, SNMPv2c, and SNMPv3. The latest version of PySNMP is v4.4.12. Users can use Python to implement all SNMP operations by using PySNMP.
PySNMP provides easy-to-use high-level APIs to simplify the coding process and improve the coding efficiency.

## Slide 28: High-Level API Architecture of PySNMP
The following shows the composition of PySNMP high-level APIs. Basic SNMPv3 operations involve the SnmpEngine, UsmUserData, UdpTransportTarget, ContextData, ObjectIdentity, and ObjectType classes, as well as the getCmd, setCmd, nextCmd, bulkCmd and sendNotification methods. This document describes only the getCmd method. The other methods are used similarly.
nextCmd
setCmd
sendNotification
getCmd
bulkCmd
PySNMP
Classes related to high-level APIs
Methods related to high-level APIs
UdpTransportTarget
UsmUserData
SnmpEngine
ContextData
ObjectIdentity
ObjectType

## Slide 29: PySNMP Encoding Process
Import high-level APIs.
Create the SNMP engine.
Create information about managed devices.
Create user information.
Create an SNMP context.
Invoke basic SNMP operation methods.
from pysnmp.hlapi import *
SnmpEngine class
Engine = SnmpEngine()
UsmUserData class
userData = UsmUserData(userName='testuser', authKey=<AUTHKEY>, privKey=<PRIVKEY>)
Create MIB objects.
UdpTransportTarget class
target = UdpTransportTarget((host, port))
ContextData class
context = ContextData()
ObjectType class
obj1 = ObjectType(ObjectIdentity(*args, **kwargs))
getCmd method
g = getCmd(Engine, userData, target, context, obj1)
Input parameters
Notes: The SnmpEngine, UsmUserData, UdpTransportTarget, ContextData, and ObjectType class instances of PySNMP high-level APIs are used as input parameters of PySNMP methods such as getCmd.
The ObjectType class is initialized using the ObjectIdentity class instance.

## Slide 30: SnmpEngine Class
SnmpEngine class: is a central, umbrella object in PySNMP. In PySNMP, all SNMP operations involve the SnmpEngine class instance.
Using this class:
engine = SnmpEngine()

## Slide 31: UsmUserData Class
UsmUserData class: provides SNMPv3 USM configuration for SNMPv3 systems. This class can be used to create SNMPv3 users and the corresponding authentication and encryption algorithms.
Using this class:
userData= UsmUserData(
‘admin’, # User name
        authKey = ‘Admin@123’, # Authentication key
        privKey = ‘Huawei@123’, # Encryption key
        authProtocol = usmHMACSHAAuthProtocol, # Authentication algorithm
        privProtocol = usmAesCfb128Protocol # Encryption algorithm
        )
Notes: For options of the authentication and encryption algorithms, visit http://snmplabs.com/pysnmp/docs/api-reference.html?highlight=usmuserdata#pysnmp.hlapi.UsmUserData.

## Slide 32: UdpTransportTarget Class
UdpTransportTarget class: specifies the IP address and port number of a managed device.
Using this class:
target = UdpTransportTarget((“192.168.56.101”, 161)) # (host, port) indicates the IP address and port number of a managed device.

## Slide 33: ContextData Class
ContextData class: specifies SNMP context.
Using this class:
context = ContextData() # If no parameter is specified when the ContextData class instance is initialized, the context object is empty.

## Slide 34: ObjectIdentity Class
ObjectIdentity class: represents the OID of a MIB object.
Using this class:
oid1 = ObjectIdentity('SNMPv2-MIB',' sysName', 0) # sysName object instance
oid2 = ObjectIdentity('1.3.6.1.2.1.1.5.0') # Use the OID string of the sysName object to initialize the ObjectIdentity class.

## Slide 35: ObjectType Class
ObjectType class: represents a MIB object, which is initialized using the ObjectIdentity object.
Using this class:
obj1 = ObjectType(ObjectIdentity('SNMPv2-MIB',' sysName', 0)) # Instantiate the ObjectType object of sysName.

## Slide 36: Method getCmd
getCmd method: implements the SNMP Get operation. The returned value is a generator.
Method declaration: getCmd(snmpEngine, authData, transportTarget, contextData, *varBinds)
Using this method:
Parameter | Description
snmpEngine | SnmpEngine class instance
authData | UsmUserData class instance
transportTarget | UdpTransportTarget class instance
contextData | ContextData class instance
*varBinds | ObjectType class instance
g = getCmd(snmpEngine, authData, transportTarget, contextData, *varBinds) # g is a generator.
# When the Python next method is used, a Get operation is generated. The obtained result is saved in varBinds. The other three returned values indicate error information.
errorIndication, errorStatus, errorIndex, varBinds =next(g)

## Slide 37: PySNMP Practice (1/4)
You can use the PySNMP classes and methods to perform the SNMP Get operation. The following case describes how to use Python to write code for the SNMP Get operation.
Case description: A managed device is connected to an NMS and has SNMP enabled. PySNMP is used on the NMS to compile a Python script to obtain the sysName of the managed device. The following figure shows the networking.
GE1/0/0
192.168.56.1
192.168.56.100
Managed device
NMS
PySNMP script

## Slide 38: PySNMP Practice (2/4)
The managed device delivers the following configurations to enable the SNMP service:
snmp-agent usm-user v3 admin group dc-admin # Create an SNMP user admin.
snmp-agent usm-user v3 admin authentication-mode sha # Set the authentication algorithm to HMAC-SHA-96. Huawei@123 # Set the authentication password.
Huawei@123
Set the snmp-agent usm-user v3 admin privacy-mode aes128 # Set the encryption algorithm to AES-128.
Huawei@123 # Set the encryption password.
Huawei@123
snmp-agent trap source ME0/0/0 # Specify the source interface for sending traps.
snmp-agent mib-view included nt iso # Create a MIB view.
snmp-agent mib-view included rd iso
snmp-agent mib-view included wt iso
snmp-agent mib-view included iso-view iso
snmp-agent group v3 dc-admin privacy read-view rd write-view wt notify-view nt # Create a user group.

## Slide 39: PySNMP Practice (3/4)
Compile a Python script:
from pysnmp.hlapi import * # Import high-level APIs of PySNMP.
userData = UsmUserData( # SNMP user information
'admin',
'Huawei@123',
'Huawei@123',
authProtocol=usmHMACSHAAuthProtocol,
privProtocol=usmAesCfb128Protocol)
g = getCmd(
SnmpEngine(),
userData,
UdpTransportTarget(("192.168.56.100", 161)),
ContextData(),
ObjectType(ObjectIdentity('SNMPv2-MIB','sysName',0))
)
errorIndication, errorStatus, errorIndex, varBinds =next(g) # Send a Get request to obtain the sysName value.
for i in varBinds:
print(i) # Print the sysName value.
Notes: Code explanation:
  Use the "from…import" statement to import high-level APIs of PySNMP.
  Create the UsmUserData class instance — userData, and set the user name, authentication algorithm, encryption algorithm, authentication key, and encryption key.
  Invoke the getCmd method and initialize the SnmpEngine, UdpTransportTarget, ContextData, and ObjectType class instances when they are input as parameters. Compared to initializing the class instances before the getCmd is invoked, this simplifies the coding process.
  Use the "errorIndication, errorStatus, errorIndex, varBinds =next(g)" statement to perform the next operation on the generator g obtained using the getCmd method. The obtained information about MIB objects is saved in varBinds.
  Finally, use loop statements to print information about all MIB objects in varBinds. In this example, only one MIB object is available in varBinds.

## Slide 40: PySNMP Practice (4/4)
Run the Python script on the NMS to implement the Get operation. The result is as follows:
Summary: The values of other MIB objects on the managed device can also be obtained using the Python script that is used to implement a Get operation. The scripts for implementing the Set, GetNext, GetBulk, Trap, and Inform operations by using PySNMP are similar to this Python script.
SNMPv2-MIB::sysName.0 = CE1
Notes: For the values of MIB objects on a managed device, refer to the product documentation of the managed device.

## Slide 41
(Multiple) Compared with SNMPv1 and SNMPv2c, what are the improvements of SNMPv3 in terms of security? ( )
  Identity authentication
  Encryption
  View-based access control
  Authentication based on community names
Notes: ABC

## Slide 42
SNMPv3 is more secure than SNMPv1 and SNMPv2c.
PySNMP can implement SNMP functions, helping engineers improve O&M efficiency.

## Slide 43
For more information about the SNMPv3 framework, see RFC 3411.
For more information about the USM for SNMPv3, see RFC 5590.
For more information about the VACM for SNMPv3, see RFC 3415.
PySNMP projects: https://github.com/etingof/pysnmp
PySNMP documentation: http://snmplabs.com/pysnmp/