## Slide 1
Wan Changli/wx408647
2020.12.29
Liu Bin/00483614

## Slide 2: NETCONF YANG Principles and Practices

## Slide 3
For device configuration management, engineers are more accustomed to using the CLI to interact with devices. This mode is simple, direct, and easy to understand. However, in the network automation field, the CLI mode has problems such as low efficiency and difficult command understanding.
To simplify device configuration and management, Internet Engineering Task Force (IETF) has set up work groups and released NETCONF, YANG, and RESTCONF standards.

## Slide 4
On completion of this course, you will be able to:
  Describe the problems and challenges of traditional network configuration management.
  Describe the basic principles of NETCONF, YANG, and RESTCONF.
  Describe the differences and relationships between NETCONF, YANG, and RESTCONF.
  Understand the working principles of NETCONF and RESTCONF.

## Slide 5
Network Management Technology Background
NETCONF Protocol
Modeling Language of YANG
RESTCONF Protocol

## Slide 6: Introduction to Device Data
Configuration data
Status data
SNMP
NETCONF
RESTCONF
Telemetry
CLI
Data is the carrier of information. Information that can be obtained from a running device is classified into configuration data and status data.
  Configuration data is writable. It can change the system status, for example, from the initial state to the current state.
  Status data is read-only non-configuration data in a system, for example, status information and statistics information.
There are multiple methods to modify device data, either based on command lines or based on specific protocols. The CLI and SNMP are the most typical methods for obtaining device data.

## Slide 7: Configuring a Network Device
Console
Telnet/SSH
SNMP set operation
CLI
SNMP
NETCONF
RESTCONF
NETCONF/RESTCONF
You can configure and manage a device in multiple ways. You can use the console cable to directly connect to the device or use SSH to remotely log in to the device, and then use the CLI to configure the device. You can also use the NMS server to set parameters in the MIB node of the device through SNMP set.
With the increase of network scale and complexity, the preceding two methods cannot satisfy the configuration management requirements. To resolve this problem, NETCONF based on Extensible Markup Language (XML) is introduced.
Notes: SNMP is based on UDP and is stateless, unordered, and unreliable for configuration management.
SNMP can be configured for only one object, not for one service. During the concurrent configuration of multiple objects, if some objects are successfully configured but some objects fail to be configured, unknown impacts will be caused on the network.
The SNMP interface is difficult to understand.

## Slide 8: Typical Configuration Management Methods
Based on the UDP protocol, it is stateless, unordered, and unreliable.
Configuration can be performed on objects only one by one, but does not orient to a service. During the concurrent configuration of multiple objects, if some objects are successfully configured but some objects fail to be configured, unknown impacts may be caused on the network.
SNMP manages only a single device and does not support network-level configuration or multi-device configuration collaboration.
The binary interface is difficult to understand.
It is insecure.
Advantage
Disadvantage
CLI
SNMP
Vendors have different definitions. Carriers need to learn and develop adaptation scripts for each vendor.
Configuration scripts are unstructured, unpredictable, and easy to change, which makes parsing complex. CLI scripts are difficult to maintain, and automatic parsing is difficult to implement.
It uses a text interface, which is easy to understand.
Based on Telnet/SSH, it is easy to use.
It uses an interface between machines. The data model file (MIB) is available.
It is mainly used for network monitoring.
No matter how configuration automation technologies develop, the CLI is still used in essence.
SNMP is not suitable for configuration management.

## Slide 9: Requirements for Network Management
04
05
Ease of use
At the 2002 IAB Network Management Workshop, 14 essential requirements for network management were raised.
01
Proper internal configuration sequence, minimizing the impact caused by configuration changes
06
Supports configuration backup and restoration.
07
Clear distinction between configuration data and status data
02
Separate obtaining of configuration data and status data and support for data comparison between devices
03
Network-level service configuration capability
Support for network-level configuration transactions
Support for configuration verification, including network-level configuration verification
08
Text-based configuration
10
Standard data models and unified data formats
09
Role-based access control and minimum authorization
11
Support for consistency check of access control lists across devices
12
Support for data-oriented or task-oriented access control
14
Support for multiple configuration sets and distinguishing between the distribution of configurations and the activation of a certain configuration
13
Notes: For details, see RFC 3535.
Different IETF work groups and drafts gradually meet 14 requirements.

## Slide 10: Gradual Implementation of Meeting Conclusions by the IETF Work Group
2008
2014
2010
2016
2006
2011
RFC4741, 4742
NETCONF 1.0, not restricting the model language
RFC6020
YANG 1.0, defining the method of combining with NETCONF
RFC6241, 6242
NETCONF 1.1, determining the combination with YANG
RFC7223, 7224, 7277, 7317, 7407
Four standard YANG models: Interface, IP, System Management, SNMP Config
RFC5277
NETCONF Event Notification
RFC7950
YANG 1.1
RFC3535
IAB Network Management Workshop
2002
2012
RFC6536
NETCONF access control
2017
RFC8040
RESTCONF 1.0
2009
RFC5717
Partial Lock
RFC6022
NETCONF Monitoring
RFC6243
With-defaults
RFC6470
Base Notification
RFC7895
YANG Library
RFC7951
JSON encoding of YANG modeling data
Notes: The IETF gradually implements the conclusions of the IAB meeting. Different work groups gradually improve the 14 requirements.
NETCONF 1.0 has no requirements on the model language. The combination between NETCONF 1.1 and YANG is determined.

## Slide 11: Process for an Engineer to Configure Devices
Device Description
[Router] interface interface GE 1/0/0
[Router-GE1/0/1] mtu 1500
CLI
The command line is an interactive language between humans and devices. Engineers query the product documentation and configure a device using the CLI.
Command lines are nested to implement device configuration.
SSH/Console
Attributes
Interfaces
Interface name
MTU
Router
...
System name
...

## Slide 12: Process for NETCONF to Configure Devices
Device Description
YANG File
NETCONF
A YANG file describes device data in another way.
The YANG model uses the module-container-leaf structure to describe devices. For example, the YANG model defines field types and specifications for router interfaces and attributes.
Attributes
Interfaces
Interface name
MTU
Router
...
System name
...
module HuaweiRouter {
container interface {
leaf name {
type string;
}
leaf mtu {
type uint16;
}
}
container properties {
leaf sysname {
type string;
}
leaf ...
}
}
The NETCONF client converts the YANG file into NETCONF messages to configure a device.
Notes: This example is not a real example. The YANG model does not take the entire device as one YANG file. Instead, the YANG model splits it into multiple YANG files by function.

## Slide 13
Network Management Technology Background
NETCONF Protocol
Modeling Language of YANG
RESTCONF Protocol

## Slide 14: NETCONF Overview
NETCONF Server
Device
Device 1
Device 2
Device 3
Management platform
NETCONF Client
NETCONF
NETCONF provides a network device management mechanism. You can use NETCONF to add, modify, or delete configurations of network devices, and obtain configurations and status of network devices.
NETCONF has three objects:
    NETCONF client
    NETCONF server
    NETCONF message

## Slide 15: NETCONF Protocol Framework
NETCONF
Content layer
Operations layer
Messages layer
Secure transport layer
Config&Status
Data
Notification
Data
<edit-config>
<get-config>
>.etc
<
rpc
>
<rpc-reply>
<notification>
SSH
BEEP
SOAP
TLS
NETCONF is partitioned into four layers, as described in the following table.
Secure transport layer: provides a communication path for interaction between the client and server. Currently, Huawei uses SSH as the transport protocol of NETCONF.
Messages layer: provides a simple RPC request and response mechanism independent of the transport protocol layer. The NETCONF client uses an <rpc> element to encapsulate RPC request information and sends the information to the NETCONF server. Upon receipt, the NETCONF server uses an <rpc-reply> element to encapsulate RPC response information and returns the information to the NETCONF client.
Operations layer: defines a group of basic operations as RPC invoking methods. These operations constitute basic NETCONF capabilities.
Content layer: describes configuration data involved in network management. The configuration data depends on vendors' devices. Currently, mainstream data models include the Schema model and YANG model.

## Slide 16: Complete NETCONF Packet
This figure shows a complete NETCONF packet.
Based on the SSH secure transmission, a packet contains information at the messages layer, operations layer, and content layer.
NETCONF packets are encoded in XML format.
<?xml version="1.0" encoding="UTF-8"?>
<rpc message-id=“101” xmlns=“urn:ietf:params:xml:ns:netconf:base:1.0”>
<edit-config>
<target>
<running/>
</target>
<default-operation>merge</default-operation>
<error-option>rollback-on-error</error-option>
<config xmlns:xc="urn:ietf:params:xml:ns:netconf:base:1.0">
<isiscomm xmlns=“http://www.Huawei.com/netconf/vrp/Huawei-isiscomm”>
<isSites>
<isSite xc:operation=“merge”>
<instanceld>100</instanceld>
<description>ISIS</description>
<vpnName>_public_</vpnName>
</isSite>
</isSite>
</isiscomm>
</config>
</edit-config>
</rpc>
Message
Operations
Content

## Slide 17: XML Encoding
XML is the encoding format of NETCONF. NETCONF uses text files to represent complex hierarchical data.
<?xml version="1.0" encoding="UTF-8"?>
<note>
<to>Learners</to>
<from>Huawei</from>
<heading>Reminder</heading>
<body>Don't forget Reading!</body>
</note>
The header of an XML encoding file is as follows:
<?xml version="1.0" encoding="UTF-8"?>
In the preceding format:
  <?: indicates the start of an instruction.
  xml: identifies an XML file.
  version: indicates the XML version. "1.0" indicates that the XML1.0 standard version is used.
  encoding: indicates the character set encoding format. Only UTF-8 encoding is supported.
  ?>: indicates the end of an instruction.
The XML document forms a tree structure, unfolding from the root.
The <note><to><from><heading><body> tag is private. The XML language does not have predefined tags, allowing users to customize tags and document structures.
Content is nested in the tag format. The slash (/) indicates the end of the current tag.

## Slide 18: Transport Layer and Messages Layer
The RPC framework is independent of the transport layer, and is used to indicate NETCONF requests and responses.
Transport layer
Messages layer
Operations layer
Content layer
<rpc>
NETCONF Client
NETCONF Server
SSH
<rpc-reply>
<rpc>: encapsulates NETCONF requests from the client to the server. The header defines the message-id identification sequence.
<rpc-reply>: response message sent by the user server to the <rpc>. The values of message-id in the headers are the same.
  <rpc-error> is sent in <rpc-reply>. One <rpc-reply> element can contain multiple <rpc-error> elements.
  If <ok> is sent in <rpc-reply>, no error or data is returned.
NETCONF uses SSH to implement secure transmission and uses Remote Procedure Calls (RPCs) to implement communication between the client and server.
Notes: For details, see RFC 6241.

## Slide 19: Basic Operations of NETCONF
NETCONF defines a series of operations:
Operation | Scenario Type | Function Description
<get-config> | Querying data | Queries configuration data.
<get> |  | Queries the current configuration and status data of the device.
<edit-config> | Editing data | Creates, modifies, or deletes configuration data.
<copy-config> | Backup/Recovery | Exports configuration data, or replaces one set of configuration data with another set of configuration data.
<delete-config> |  | Deletes the configuration data set and clears the startup configuration.
<lock> | Locking/Unlocking | Locks and exclusively occupies the permission to modify the configuration data set.
<unlock> |  | Unlocks the configuration data set and cancels the exclusive permission to modify the configuration data set.
<commit> | Transaction | Commits configuration data in the <candidate> data set to the current running configuration data.
<cancel-commit> |  | Cancels the trial run of configuration committing.
<discard-changes> |  | Discards the uncommitted configuration data in <candidate>.
<validate> |  | Checks whether the syntax and semantics of the specified configuration data are correct.
<close-session> | Session | Normally ends the NETCONF session.
<kill-session> |  | Forcibly terminates other NETCONF sessions. You must have the administrator rights to perform this operation.
Transport layer
Messages layer
Operations layer
Content layer

## Slide 20: Operation Objects of NETCONF
Operation objects have three configuration databases. You can flexibly read and edit the candidate, running, and startup configuration databases to deliver, verify, and roll back the overall configuration.
Running configuration database
<running>
Startup configuration database
<startup>
Candidate configuration database
<candidate>
<edit-config>
<copy-config>
<commit>
<copy-config>
Router/
Switch
<lock> / <unlock>
<delete-config>
<discard-changes>
File
<url>
Restart/Recovery
<copy-config>
<validate>
Transport layer
Messages layer
Operations layer
Content layer

## Slide 21: Example: Delivering VLAN Configurations
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="801">
<edit-config>
<target>
<running/>
</target>
<default-operation>merge</default-operation>
<error-option>rollback-on-error</error-option>
<config xmlns:xc="urn:ietf:params:xml:ns:netconf:base:1.0">
<vlan xmlns="http://www.huawei.com/netconf/vrp/huawei-vlan">
<vlans>
<vlan>
<vlanId>10</vlanId>
<protocolVlans>
<protocolVlan xc:operation="merge">
<protocolIndex>0</protocolIndex>
</protocolVlan>
</protocolVlans>
</vlan>
</vlans>
...
</rpc>
RPC request: Create a common VLAN with the VLAN ID of 10.
In this example, the edit-config operation can load data to the running configuration database <running/>.
Deliver the information for creating VLAN 10.
The operation is merge. Other operations are as follows:
  merge
  create
  delete
  remove
Transport layer
Messages layer
Operations layer
Content layer
Notes: <config> may contain the optional attribute <operation>, which is used to specify an operation type for a configuration item. If the <operation> attribute is not carried, the <merge> operation is performed by default. The <operation> attribute values are as follows:
  merge: In the database, modify the existing data or create data that does not exist. This is the default operation.
  create: Add configuration data to the configuration database only when the configuration data to be created does not exist in the configuration database. If the configuration data exists, <rpc-error> is returned, in which the <error-tag> value is data-exists.
  delete: Delete a specified configuration data record from the configuration database. If the data record exists, the data record is deleted. If the data record does not exist, <rpc-error> is returned, in which the <error-tag> value is data-missing.
  remove: Delete a specified configuration data record from the configuration database. If the data exists, the data is deleted. If the data does not exist, a success message is returned.

## Slide 22: Content Layer of NETCONF
The NETCONF content layer configures data for devices. Configuration data requires a modeling language, which depends on the implementation of each vendor. NETCONF 1.0 has no requirements on the model language. NETCONF 1.1 clearly defines the combination with YANG and starts to standardize the NETCONF content format.
Currently, Huawei devices support the following content layers:
  Huawei-YANG
  NETCONF Schema
  IETF-YANG
  OpenConfig-YANG
NETCONF has two modeling languages: Schema and YANG.
Schema is a set of defined rules for describing XML documents. A schema file defines all the management objects on a managed device, the constraints and hierarchical relationships between these management objects, and the read and write permissions of these management objects.
YANG is a data modeling language developed to design NETCONF-oriented configuration data, status data models, RPC models, and notification mechanisms.
Transport layer
Messages layer
Operations layer
Content layer
Notes: Schema is a language that Huawei extends private syntax based on the W3C XML standard. Before the NETCONF standard is bound to the YANG model, VRPV8 has implemented Schema.
Huawei-YANG has the most abundant content.

## Slide 23: Example: Delivering VLAN Configurations (HUAWEI-YANG)
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="801">
<edit-config>
<target>
<running/>
</target>
<default-operation>merge</default-operation>
<error-option>rollback-on-error</error-option>
<config xmlns:xc="urn:ietf:params:xml:ns:netconf:base:1.0">
<vlan xmlns="http://www.huawei.com/netconf/vrp/huawei-vlan">
<vlans>
<vlan>
<vlanId>10</vlanId>
<protocolVlans>
<protocolVlan xc:operation="merge">
<protocolIndex>0</protocolIndex>
</protocolVlan>
</protocolVlans>
</vlan>
</vlans>
...
</rpc>
RPC request: Create a common VLAN with the VLAN ID of 10.
In this example, the edit-config operation can load data to the running configuration database <running/>.
<config></config>: content layer information.
The namespace of the content layer is http://www.huawei.com/netconf/vrp/huawei-vlan.
The content layer structure is as follows: <vlans> contains <vlan>, including <vlanId> and <protocalVlans>.
Transport layer
Messages layer
Operations layer
Content layer
Notes: For details, see the NETCONF YANG API Reference released at the official website.

## Slide 24: Example: Delivering VLAN Configurations (Schema)
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="801">
<edit-config>
<target>
<running/>
</target>
<default-operation>merge</default-operation>
<error-option>rollback-on-error</error-option>
<config>
<vlan xmlns="http://www.huawei.com/netconf/vrp" content-version="1.0" format-version="1.0">
<vlans>
<vlan operation="merge">
<vlanId>10</vlanId>
<vlanType>common</vlanType>
</vlan>
</vlans>
</vlan>
</config>
</edit-config>
</rpc>
RPC request: Create a common VLAN with the VLAN ID of 10.
This example also describes how to create VLAN 10, but the content is in the Schema mode.
HUAWEI-YANG is recommended, because it has more comprehensive support features.
Transport layer
Messages layer
Operations layer
Content layer

## Slide 25: NETCONF Configuration
Enter the NETCONF view.
Run the netconf command in the system view to enter the NETCONF view.
Configure the port number for NETCONF services.
Enable NETCONF services on port 830 of the SSH server.
Enable NETCONF.
Enable the NETCONF services of the SSH server on TCP port 22.
Either snetconf server enable or protocol inbound ssh port 830 command can be used to enable NETCONF. If both commands are executed, the client can use port 22 or 830 to establish a NETCONF connection with the server.
NETCONF uses SSH as the transport protocol. Therefore, you must configure SSH before using NETCONF.
[Huawei] netconf
[Huawei-netconf] protocol inbound ssh port 830
[Huawei] snetconf server enable

## Slide 26
Network Management Technology Background
NETCONF Protocol
Modeling Language of YANG
RESTCONF Protocol

## Slide 27: Origin of YANG
Although the NETCONF protocol is standardized, data content is not standardized. How can we describe a piece of data?
Data
NETCONF session
RPC message
Data
model
Data structure
Data integrity constraint
Data operation
Three factors
Intuitive simulation of the real world
Easy to understand
Easy to be implemented by computers
Requirements
To describe the data model,
a language is required.
A data model is an abstraction and expression of data features.
√
√
×

## Slide 28: YANG Language Overview
Yet Another Next Generation (YANG) is a data modeling language.
The YANG model defines the hierarchical structure of data and can be used for NETCONF-based operations. Modeling objects include configuration, status data, remote procedure calls, and notifications. This allows a complete description of all data exchanged between a NETCONF client and server. YANG has the following features:
  Hierarchical tree-like structure modeling.
  Data models are presented as modules and sub-modules.
  It can be converted to the YANG Independent Notation (YIN) model based on the XML syntax without any loss.
  Defines built-in data types and extensible types.
The YANG model is presented as a .yang file.
Notes: YANG originates from NETCONF but is not only used for NETCONF. Although the YANG modeling language is unified, YANG files are not unified.
YANG files can be classified into three types: vendor-specific YANG files, IETF-defined YANG files, and OpenConfig YANG files.
The Config&Status Data, Notification Data, and bottom-layer RPC messages in NETCONF can be modeled using the YANG model. YANG model files can be converted into XML/JSON files using a tool and then encapsulated into NETCONF/RESTCONF messages.
For details, see RFC 7950.

## Slide 29: Introduction to YANG Files – Module
module example-system {
yang-version 1.1;
namespace "urn:example:system";
prefix "sys";
organization "Example Inc.";
contact "joe@example.com";
description
"The module for entities implementing the Example system.";
revision 2007-06-09 {
description "Initial revision.";
}
container system {
leaf host-name {...}
container login{...}
}
container X {...}
}
A YANG file can be defined as a module or submodule. Modules and submodules can reference other modules' model files to use the data types and structures defined by other modules.
Each module contains multiple declarations, including:
  YANG version, which is 1.0 or 1.1.
  YANG namespace, which is IETF YANG or Openconfig YANG.
  Organization information
  Contact
  File description
  Change history
Notes: For details, see RFC 7950.

## Slide 30: Introduction to YANG Files – Leaf Node
leaf host-name {
type string;
description
"Hostname for this system.";
}
<host-name>my.example.com</host-name>
YANG model
XML encoding
A leaf node is used to define a variable of a simple specified type and is declared using the leaf keyword.
A leaf node has sub-declarations and values but no sub-nodes. In this example, host-name contains two sub-declarations: type and description.
type indicates the value type. In this example, the value is string.
description indicates the description.
Notes: For more information, see RFC 7950.

## Slide 31: Introduction to YANG Files – Leaf List
leaf-list domain-search {
type string;
description
"List of domain names to search.";
}
<domain-search>high.example.com</domain-search>
<domain-search>low.example.com</domain-search>
<domain-search>everywhere.example.com</domain-search>
YANG model
XML encoding
Leaf List is used to define an array variable and is declared using the leaf-list keyword.
In this example, domain-search has two sub-declarations: type and description.
type indicates the value type. In this example, the value is string.
description indicates the description.

## Slide 32: Introduction to YANG Files – List Node
list user {
key "name";
leaf name {
type string;
}
leaf full-name {
type string;
}
leaf class {
type string;
}
}
<user>
<name>glocks</name>
<full-name>Goldie Locks</full-name>
<class>intruder</class>
</user>
<user>
<name>snowey</name>
<full-name>Snow White</full-name>
<class>free-loader</class>
</user>
<user>
<name>rzell</name>
<full-name>Rapun Zell</full-name>
<class>tower</class>
</user>
YANG model
XML encoding
A list node is used to define a higher-level data node. Each list node is uniquely identified by a key and can contain multiple leaf nodes.

## Slide 33: Introduction to YANG Files – Container Node
<system>
<login>
<message>Good morning</message>
</login>
</system>
YANG model
XML encoding
Container nodes are used to define data sets in a larger scope. Each container node has only different sub-nodes, but does not have any value. These sub-nodes can be container, leaf, leaf-list, or list nodes.
container system {
container login {
leaf message {
type string;
description
"Message given at start of login session.";
}
list user {
key "name";
leaf name {
type string;
}
leaf full-name {
type string;
}
leaf class {
type string;
}
}
}

## Slide 34: Introduction to YANG Files – Grouping
grouping target {
leaf address {
type inet:ip-address;
description "Target IP address.";
}
leaf port {
type inet:port-number;
description "Target port number.";
}
}
container peer {
container destination {
uses target;
}
}
Grouping is used to define nodes that can be reused. Generally, grouping is used together with uses. In this example, target defines leaf address and port. If use target is specified in the container peer, the leaf model is reused.

## Slide 35: Introduction to YANG Files – Configuration Data and Status Data
list interface {
key "name";
config true;
leaf name {
type string;
}
leaf speed {
type enumeration {
enum 10m;
enum 100m;
enum auto;
}
}
leaf observed-speed {
type uint32;
config false;
}
}
YANG files can declare data types. The config declaration is used to distinguish configuration data from status data.
config true indicates configuration data.
config false indicates status data.
Notes: For details, see RFC 7950.

## Slide 36: Introduction to YANG Files – Data Type
The YANG model supports built-in default data types and extended data types. The typedef declaration is used to define extended data types.
typedef percent {
type uint8 {
range "0 .. 100";
}
}
leaf completed {
type percent;
}
Name | Description
binary | Any binary data
bits | A set of bits or flags
boolean | “true” or “flase”
decimal64 | 64-bit single decimal number
empty | A leaf that does not have any value
enumeration | One of an enumerated to an abstract identity
instance-identifier | A reference to an abstract identity
int8 | 8-bits signed integer
int16 | 16-bit signed integer
int32 | 32-bit signed integer
int64 | 64-bit signed integer
leafref | A reference to a leaf instance
string | A character string
uint8 | 8-bit unsigned integer
uint16 | 16-bit unsigned integer
uint32 | 32-bit unsigned integer
uint64 | 64-bit unsigned integer
union | Choice of member types

## Slide 37: FAQ: How Do I Load a YANG Model?
NETCONF
Device
Huawei YANG
IETF YANG
OpenConfig YANG
NETCONF Schema
YANG
YANG file translation
Management platform/SDN controller
A YANG file is loaded on the NETCONF client (such as the NMS or SDN controller). A tool is used to convert YANG files into NETCONF messages and deliver the messages to devices.
table1
table2
tableN…

## Slide 38
Network Management Technology Background
NETCONF Protocol
Modeling Language of YANG
RESTCONF Protocol

## Slide 39: Origin of RESTCONF
Doctoral thesis of Roy Thomas Fielding in 2000
REST:
Client-server
interaction framework
Resource: data.
Unique URI
Representation mode
State transfer: HTTP operation
REST: Representational State Transfer
The state of a resource is transferred in a representation mode on the network.
In 2017, IETF released RFC 8040.
REST + Configuration
"Architectural Styles and the Design of Network-based Software Architectures"
Internet Engineering Task Force (IETF)
Request for Comments: 8040
Category: Standards Track
ISSN: 2070-1721
RESTCONF Protocol
Abstract
This documents describes an HTTP-based protocol that provides a programmatic interface for accessing data defined in YANG, using the datastore concepts defined in the Network Configurastion Protocol (NETCONF).
A, Bierman
YumaWorks
M. Bjorklund
Tail-f Systems
K.Watsen
Juniper.Networks
January 2017

## Slide 40: RESTCONF Overview
YANG
DataStore
Device
NETCONF
Management platform
SDN controller
NETCONF Client
Web APP
RESTCONF
RESTCONF allows web applications to access configuration data, status data, and event notifications of network devices in a modular and scalable manner. It has the following features:
  RESTCONF uses HTTP methods to perform operations (CRUD) on data defined by YANG.
  YANG files can be shared by NETCONF and RESTCONF.
  The data encoding format can be XML or JSON.
Compared with NETCONF, RESTCONF uses different operation methods and data encoding formats.
Notes: NETCONF and RESTCONF can coexist.
CRUD: Create, Remove, Update, Delete.

## Slide 41: Comparison Between RESTCONF and NETCONF
Data (XML)
Content layer
GET, POST
PUT, PATCH, DELETE
Operations layer
Messages layer
Transport layer
Data (XML/JSON)
<get>, <get-config>
<edit-config>, etc.
<rpc>, <rpc-reply>
SSH over TCP
RESTCONF | NETCONF Operation
GET | <get-config>, <get>
POST | <edit-config> (nc:operation="create")
 | invoke an RPC operation
PUT | <edit-config> (nc:operation="create/replace")
 | <copy-config> (PUT on datastore)
PATCH | <edit-config> (nc:operation depends on PATCH content)
DELETE | <edit-config> (nc:operation="delete")
NETCONF
RESTCONF
HTTP
TLS over TCP
NETCONF operates multiple configuration libraries of a device. The transaction mechanism and rollback mechanism are available.
RESTCONF uses HTTP operations, which are stateless, have no transaction mechanism, and does not support rollback.

## Slide 42: Typical RESTCONF Interaction
YANG
DataStore
A complete RESTCONF interaction includes a request and a response.
In this example, the client uses the OPTIONS method to obtain the operations supported by the device.
The device response supports the following operations: POST, DELETE, GET, HEAD, PATCH, and OPTIONS.
OPTIONS /restconf/data/huawei-aaa:aaa/domains/domain HTTP/1.1
HTTP/1.1 200 OK
Accept-Patch: application/yang-data+xml, application/yang-data+json
Allow: POST, DELETE, GET, HEAD, PATCH, OPTIONS
Content-Length:0
RESTCONF request
RESTCONF response
Web App
Notes: NETCONF and RESTCONF can coexist.

## Slide 43: RESTCONF Request Packet
RESTCONF request
RESTCONF response
YANG
DataStore
RESTCONF request
Web App
Method
URI
HTTP/Version
Header 1 : value
Header 2 : value
...
(Optional) request body
Description | 
Method | HTTP method, performed on the resource identified by the request URI.
URI | Uniform Resource Identifier.
HTTP/Version | HTTP version.
Header : value | Header of a request packet, which has specific field requirements. The format is header field and value.
Request body | (Optional) Request body. Some methods do not carry body information.
Notes: A request header may contain multiple fields, such as Accept, Authorization, Host, and From. For details, see RFC 2916.

## Slide 44: RESTCONF Request Example
POST /restconf/data/huawei-aaa:aaa/domains HTTP/1.1
Host: 192.168.56.100
Content-Type: application/yang-data+xml
<domain xmlns="http://www.huawei.com/netconf/vrp/huawei-aaa">
<domainName>abc</domainName>
<accessLimit>10</accessLimit>
</domain>
Request body
Header
HTTP method URI HTTP/Version
The IP address of the RESTCONF request object is 192.168.56.100. Change the value of domainName to abc and the value of accessLimit to 10.
RESTCONF request
RESTCONF response

## Slide 45: RESTCONF Response Packet
YANG
DataStore
RESTCONF response
Web App
HTTP/Version
Status Code
Message
Header 1 : value
Header 2 : value
...
(Optional) response body
Description | 
HTTP/Version | HTTP method, performed on the resource identified by the request URI.
Status code | HTTP status code.
Message | HTTP status message.
Header : value | Header of a response packet, which has specific field requirements. The format is header field and value.
Response body | (Optional) Response body. Some methods do not carry body information.
RESTCONF request
RESTCONF response
Notes: Header information contains details about Response Header and Entity Header. For details, see sections 6.2 and 7.1 in RFC 2916.

## Slide 46: HTTP Status Code
An HTTP status code is a three-digit number indicating the status of a response from the server. It is used to return the operation result to the client.
Status Code |  | Description | 
1XX | (Informational) The request is received. | 100 Continue | If the request is received, go to the next step.
2XX | (Successful) The request is successful. | 200 OK | Success. The response body is available.
 |  | 201 Created | A resource is successfully created, and the URI of the newly created resource exists in the location field.
 |  | 204 No Content | Success. The response body is unavailable.
3XX | (Redirection) Further operations need to be performed. | 301 Moved Permanently | A new URI is allocated to the target resource, and all future resources will be associated with the new URI.
4XX | (Client Error) Request error. | 400 Bad Request | The request body is incorrect and carries error information.
 |  | 401 Unauthorized | Authorization failed. For example, the certificate does not match.
 |  | 403 Forbidden | Access denied. The possible cause is that the user attempts to perform operations beyond the permission or the login user name or password is incorrect.
 |  | 404 Not Found | The requested resource cannot be found.
5XX | (Server Error) Server error. | 500 Internal Server Error | The request cannot be executed due to an internal server error. The user needs to resend the request later.
 |  | 501 Not Implemented | The function has not been implemented.
RESTCONF request
RESTCONF response
Notes: For details, see 6 Response Status Code in RFC 7231.

## Slide 47: RESTCONF Response Example
HTTP/1.1 201 Created
Content-Type:application/yang-data+xml
Content-Length:0
Header
HTTP/Version Status code HTTP status message
RESTCONF response packet
If status code 201 is returned, the resource is successfully created.
Content-Type and Content-Length in the header describe body information. The body data type is XML, and the content length is 0.
RESTCONF request
RESTCONF response

## Slide 48
Which protocol is used at the transport layer of Huawei NETCONF?
What is the relationship between NETCONF, RESTCONF, and YANG?
Notes: Huawei uses SSH as the transport layer protocol. Before enabling the NETCONF function on a device, you need to create an SSH user as the NETCONF user for login.
YANG is a modeling language used to describe the content layer of NETCONF and RESTCONF. The difference between NETCONF and RESTCONF is as follows: RESTCONF constructs the transport layer, messages layer, and operations layer based on HTTP, while NETCONF has defined the operations layer and uses SSH as the transport layer and RPC as the messages layer.

## Slide 49
NETCONF provides a network device management mechanism. You can use NETCONF to add, modify, or delete configurations of network devices, and obtain configurations and status of network devices.
The YANG model defines the hierarchical structure of data and can be used for NETCONF-based operations.
RESTCONF uses HTTP methods to perform operations (CRUD) on data defined by YANG.

## Slide 50
For details about NETCONF, see RFC 6241.
For details about YANG, see RFC 7950.
For details about RESTCONF, see RFC 8040.

## Slide 51
https://e.huawei.com/cn/talent/#/home