## Slide 2: Telemetry Fundamentals and Practices

## Slide 3
Telemetry is a network device monitoring technology that periodically samples statistics and status data on network devices. This course describes the technical background, concepts, framework, and technical fundamentals of telemetry, as well as the configuration procedure of static telemetry subscription.

## Slide 4
On completion of this course, you will be able to:
  Describe the background of the telemetry technology.
  Describe the telemetry concepts and framework.
  Distinguish static and dynamic telemetry subscriptions.
  Describe the concepts and functions of gRPC.
  Configure telemetry data sampling.

## Slide 5
Introduction to Telemetry
  Technical Background
  Overview
Telemetry Technical Fundamentals
Telemetry Configuration and Practice

## Slide 6: Technical Background: Introduction to Network Device Monitoring
Monitoring center
Equipment room A
Equipment room B
Equipment room C
Device monitoring data can be obtained through SNMP, CLI, Syslog, NetStream, and sFlow.
NetSteam and sFlow deal with network traffic monitoring and are mainly applicable to data-plane data.
SNMP is the most popular protocol for device monitoring.
An O&M platform mainly provides unified monitoring and performance management for network devices. It monitors device data on the data, control, and management planes.
Management-plane data | CPU speed, device temperature, and fan speed
Control-plane data | BGP peer, MPLS neighbor, and routing information
Data-plane data | Incoming and outgoing interface traffic

## Slide 7: Technical Background: Bottlenecks of Traditional Data Sampling Technologies (1/2)
The red wavy line represents a normal interface bandwidth change trend. Traffic exceptions cannot be detected through periodic SNMP-based data collection.
Long sampling period
Bandwidth (Mbit/s)
Time
SNMP sampling point
SNMP sampling point
5 min
The Nyquist Sampling Theorem states that a signal must be sampled at more than twice the highest frequency component of the signal to ensure that no information will be lost. Data loss may occur if the data is sampled through SNMP every 5 minutes.

## Slide 8: Technical Background: Bottlenecks of Traditional Data Sampling Technologies (2/2)
Low collection efficiency
Poor data model compatibility
Traditional data collection uses the pull mode.
SNMP data is based on MIBs which are defined by vendors separately.
Traditional SNMP-based data collection uses the pull mode, in which one request and one response are involved in each interaction. To collect sampled data, the network management system (NMS) needs to send a query request to the device. After parsing the request, the device sends the sampled data to the NMS. Each vendor customizes its Management Information Base (MIB), resulting in poor compatibility.
Notes: MIB is a standard for network management data.

## Slide 9: Summary: Traditional Network O&M Faces Many Challenges
The large sampling interval results in low network visibility.
SNMP-based O&M systems are inefficient.
Real-time end-to-end monitoring, like IT O&M, cannot be achieved, and complete historical data cannot be retained.
Network problems caused by a large number of microbursts cannot be detected.
Problems in traditional network O&M
SNMP
Pulling model
sFlow
NetStream
Data collection
Data analysis
Sampling model
Error correction
On a traditional network, data is sampled in pull mode at an interval of 5 to 15 minutes on average. Data sampling in pull mode at a shorter interval will result in network breakdown.
Notes: A microburst refers to a situation in which a large amount of burst data is received within a very short time (milliseconds), so that the burst data rate is tens or hundreds times higher than the average rate or even exceeds the port bandwidth. The NMS or network performance monitoring software calculates the real-time network bandwidth at an interval of seconds to minutes. At such an interval, the network traffic seems to be stable. However, packet loss may have occurred due to microbursts.

## Slide 10: Summary: Traditional Data Collection Mechanisms Cannot Cope with Massive Data
Network data source
Data consumer
SNMP
Syslog
CLI
Pull mode for full polling, poor performance, not timely
Text mode, without model definition, poor scalability.
Text mode, without model definition, poor scalability.
SNMP
server
Syslog
server
Shell client
scripts
A mechanism that supports ultra-large-scale networks and O&M of massive data is required. This mechanism must feature real-time data collection, high performance, and easy scalability.
Telemetry
Notes: SNMP queries are performed in a question-answer manner. If 1000 interactions are performed within 1 minute, SNMP parses 1000 query request packets. Telemetry avoids repeated queries. This is because subscription needs to be performed only once and then devices can continuously push data to the NMS.

## Slide 11
Introduction to Telemetry
  Technical Background
  Overview
Telemetry Technical Fundamentals
Telemetry Configuration and Practice

## Slide 12: Telemetry Overview
Telemetry, also called network telemetry, is a technology that remotely collects data from physical or virtual devices at a high speed. Devices periodically send interface traffic statistics, CPU usage, and memory usage to collectors in push mode. Compared with the traditional pull mode (question-answer interaction), the push mode provides faster and real-time data collection.
Analyzer
Device
Controller
Collector
Telemetry-based data push
Notes: There is also a view in the industry that SNMP is considered as a traditional telemetry technology, and telemetry is currently referred to as streaming telemetry or model-driven telemetry.
Telemetry packs the data to be sent, improving transmission efficiency.

## Slide 13: Telemetry Technical Features
Improves devices' data collection capabilities.
Supports the subscription mechanism.
Constructs standard data models.
Analyzer
Device
Controller
Collector
The traditional NMS is decoupled into a collector and a controller. In addition, communication protocols and management applications are decoupled.
Open APIs are available to third-party data analysis and processing companies, providing stronger data storage and processing capabilities.
Telemetry works in push mode. YANG models define the telemetry data structure, and data sampling can be performed at an interval of sub-seconds.

## Slide 14: Telemetry Advantages
Telemetry
A
B
C
Refined monitoring
The collected data is of high precision and various types, which can fully reflect the network status.
Fast fault locating
Users want faults to be quickly located in seconds or even sub-seconds on a complex network.
Proactive data reporting
For telemetry, subscription needs to be performed only once. Then devices can continuously report data, reducing the pressure on devices to process query requests.
Telemetry obtains abundant monitoring data in push mode in a timely manner. The data helps quickly locate network faults. In addition, telemetry provides a uniform data stream format, which simplifies data collection and analysis to solve problems in traditional network O&M.

## Slide 15: Telemetry Network Model
The telemetry network model is defined in two ways:
  In a broad sense, telemetry is a self-closed-loop system consisting of network devices, a collector, an analyzer, and a controller.
  In a narrow sense, telemetry is the function of sending sampled device data to a collector.
Analyzer
Controller
Collector
Device 1
Device 2
Telemetry in a broad sense
Telemetry in a narrow sense
Using telemetry, a collector can collect a large amount of device data and send the data to an analyzer for comprehensive analysis. The analyzer sends the results to a controller, which then adjusts device configurations accordingly, enabling the analyzer to determine whether the device status after adjustment meets expectations in real time.
Collection
Data sending and analysis
Response
Configuration adjustment

## Slide 16: Telemetry Application Scenario: WAN
CDN settings
Data collection
Data analysis
Cost adjustment
Routing policy
Node addition or deletion
Link capacity expansion
AS 1
AS 2
AS 3
Internet
Fixed broadband network
Content supervision
IGW
Mobile data network
Domestic interconnected peers
Interface data of routers is reported in real time to help you gain insight into the traffic direction.

## Slide 17: Telemetry Application Scenario: Campus Network
Data collection
Data analysis
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
WAN
NMS O&M zone/Analyzer
Data center
Measurement Object | Metric
AP | CPU usage, memory usage, and number of online clients
Radio | Number of online users, channel usage, noise, traffic, backpressure queue, interference rate, and power
User | RSSI, negotiated rate, packet loss rate, and latency
Device/Board | CPU and memory usages
Port | Numbers of sent and received broadcast, multicast, and unicast packets, numbers of discarded received and sent packets, and numbers of received and sent error packets
On a campus network, telemetry can be used to monitor and report device status and wired and wireless data to the analyzer at the same time, implementing intelligent O&M.

## Slide 18: Telemetry Application Scenario: Data Center
Data collection
Data analysis
Upon the receipt of data sent through telemetry, the analyzer calculates the forwarding path, forwarding latency, and link latency of packets. In addition, it analyzes the application interaction relationship and associates applications with network paths. The analyzer can collect statistics, analyze data, and display analysis results, implementing intelligent O&M.
Spine
Leaf
Core switch
Server
Production environment zone
Test environment zone
WAN
Campus network
Internet
NMS O&M zone/Analyzer
Measurement Object | Metric
Device | CPU and memory usages
Board | CPU, memory, FIB entry, and MAC entry usages
Chip | TCAM usage
Port | Number of received/sent packets, number of bytes, number of lost packets, number of error packets, and numbers of broadcast, multicast, and unicast packets
Queue | Buffer size
Optical module | Receive/Transmit optical power, current, voltage, and temperature
Packet loss behavior | Detection of packet loss due to congestions
Telemetry/ERSPAN
Notes: The collector in the data center collects device performance data through telemetry and collects device flow mirroring data through ERSPAN.

## Slide 19
Introduction to Telemetry
Telemetry Technical Fundamentals
Telemetry Configuration and Practice

## Slide 20: Telemetry Framework
Data collection
Data subscription
Data push
Data generation
Data source
UDP
NP
Data analysis
The framework of telemetry in a narrow sense consists of four modules: data source, data generation, data subscription, and data push.
Notes: For details about the framework, see the corresponding RFC draft at https://tools.ietf.org/html/draft-song-ntf-02.
Google Remote Procedure Call (gRPC) is an open-source remote procedure call (RPC) system developed by Google.
User Datagram Protocol (UDP) provides a method for an application to send encapsulated IP packets without establishing a connection.
Protocol buffers (Protobuf) is a mechanism for serializing structured data.

## Slide 21: Telemetry Protocol Stack
YANG models
SSH
XML
NETCONF
API
App 1
HTTP
JSON
GPB
RESTCONF
gRPC
App 3
App 2
VRP (central processing module)
CPU/NP
SSH
NETCONF
HTTP
JSON
GPB
RESTCONF
gRPC
XML
YANG models
MIB
MIB
SNMP
SNMP
UDP
UDP
BER
BER
Data model layer
Data encoding layer
Communication layer
Transport layer
Network device
Telemetry data user end
The telemetry protocol stack is divided into the transport layer, communication layer, data encoding layer, and data model layer.
Notes: A YANG model is similar to a menu for a fast-food restaurant. If a customer wants to eat a hamburger or fried chicken, the customer writes an A4 paper purchase list with one hamburger and two fried chickens according to the menu, folds the list into a stamp-sized note, puts it in the GPB envelope, and gives the envelope to the messenger gRPC at the door. The gRPC then rides on an HTTP/2 electric motorcycle and goes to the fast food restaurant. The messenger gRPC gives the GPB envelope to the restaurant boss, and the restaurant manager opens the envelope to check whether the items that the customer orders are on the restaurant menu.

## Slide 22: Telemetry Data Source
Data Push
Data Generation
Data Subscription
Data Source
YANG models
SSH
XML
NETCONF
HTTP
JSON
GPB
RESTCONF
gRPC
VRP (central processing module)
CPU/NP
MIB
SNMP
UDP
BER
Data collection
Data subscription
Data push
Data generation
Data source
UDP
NP
Data analysis
Data source position in the protocol stack
The telemetry data source defines the data that can be obtained. Telemetry uses various types of YANG models to define data sources available to devices, such as Huawei-YANG, IETF-YANG, and OpenConfig-YANG.

## Slide 23: YANG Model and Sampling Path
The preceding information forms a sampling path:
Top node in the YANG model
Top container in the YANG model
Level-2 container in the YANG model
Node to be sampled
huawei-debug:debug/cpu-infos/cpu-info
Data Push
Data Generation
Data Subscription
Data Source
Notes: For more information about the YANG model, visit https://datatracker.ietf.org/doc/rfc7895/.

## Slide 24: Telemetry Data Subscription
Data collection
Data subscription
Data push
Data generation
Data source
UDP
NP
Data analysis
Huawei provides two subscription modes for telemetry: static and dynamic.
In static telemetry subscription, a device functions as a client and a collector functions as the server. The device proactively initiates a connection to the collector to collect and send data. This mode is applicable to long-term inspection.
In dynamic telemetry subscription, a collector functions as a client and initiates a connection to a device functioning as a server to collect data. This mode is applicable to short-term monitoring.
Collector
Device
Static configuration
The device proactively sends data
(dial-out).
CLI/NMS
Collector
Device
Static subscription
Dynamic subscription
Dynamic subscription (dial-in)
Telemetry data subscription defines the data receive end and transmit end, as well as their interactions.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 25: Static Telemetry Subscription
Static Telemetry Subscription
  The NMS delivers static subscription configurations to the device, including the sampling path, sampling interval, destination to which the sampled data is reported, and data. The configurations can be delivered in the following modes:
    Through the CLI
    Through the NETCONF model openconfig-telemetry.yang
  The device starts to sample data, establishes a connection with the collector, and pushes the sampled data to the collector in the following modes:
    Through gRPC using the RPC method dataPublish
    Through UDP
Time 1, data 1
Time 2, data 2
Time 3, data 3
Time n, data n
T = λ
ΣT = ∞
Collector
Router
CLI/NMS
...
The NMS subscribes to sampled data, and the router continuously sends data at an interval of λ seconds.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 26: Static Telemetry Subscription
Configure the collector. | system-view Telemetry destination-group ipv4-address IP address, port number, protocol, and encryption mode for the collector
Configure the data to be sampled. | system-view telemetry sensor-group sensor-path Sensor sampling path
Create a subscription. | system-view telemetry subscription sensor-group Associate the sampling sensor group, and configure a sampling period, redundancy suppression, and a heartbeat interval.
Verify the configuration. | display telemetry sensor display telemetry destination display telemetry subscription display telemetry sensor-path
Data Push
Data Generation
Data Subscription
Data Source
Time 1, data 1
Time 2, data 2
Time 3, data 3
Time n, data n
T = λ
ΣT = ∞
Collector
Router
CLI/NMS
...
The NMS subscribes to sampled data, and the router continuously sends data at an interval of λ seconds.

## Slide 27: Customized Event Reporting
When a parameter exceeds the threshold, the NMS starts to subscribe to some data.
Condition = True
Whether the CPU usage exceeds 40%
Configure a customized event in the static subscription. | system-view telemetry sensor-group Sensor-path //Configures a customized event. Example: sensor-path huawei-devm:devm/cpuInfos/cpuInfo condition express op-field systemCpuUsage op-type gt op-value 40
After a specific parameter exceeds the threshold, static subscription is triggered.
Time 1, data 1
Time 2, data 2
Time n, data n
...
Collector
Router
CLI/NMS
Data Push
Data Generation
Data Subscription
Data Source

## Slide 28: Dynamic Telemetry Subscription Using gRPC
Dynamic Telemetry Subscription
  The collector initiates a gRPC connection request to the router.
  The collector initiates a dynamic subscription request to the router.
    RPC method: Subscribe
    Specify the sampling path and sampling interval.
  The router starts to sample data, sends the sampled data (as the response to the dynamic subscription request) to the collector.
Configure the device so that its data can be subscribed.
Time 1, data 1
Time 2, data 2
Time n, data n
...
Subscribes to a device parameter temporarily. The sampling interval is λ seconds.
T = λ
Tears down the connection.
ΣT = λn
Collector
Router
CLI/NMS
Data Push
Data Generation
Data Subscription
Data Source
Notes: gRPC is a RPC system developed by Google.

## Slide 29: Dynamic Telemetry Subscription Using gRPC
Time 1, data 1
Time 2, data 2
Time n, data n
...
T = λ
ΣT = λn
Parameter-specific data collection and on-demand data push
Configure the collector. | system-view grpc grpc server // Enters the gRPC server view. source-ip // Specifies a source IP address to be listened on. server-port // Specifies the number of a port to be listened on. service enable // Enables the gRPC service. (Optional) acl (Optional) idle-timeout (Optional) ssl-policy (Optional) ssl-verify peer commit
Verify the configuration. | display telemetry dynamic-subscription
Collector
Router
CLI/NMS
Data Push
Data Generation
Data Subscription
Data Source
Configure the device so that its data can be subscribed.
Subscribes to a device parameter temporarily. The sampling interval is λ seconds.
Tears down the connection.

## Slide 30: gRPC
TCP
TLS
HTTP2
gRPC
Data model
Focus on services
gRPC encapsulation
gRPC, developed by Google, is a language-neutral, platform-neutral, and open-source remote procedure call (RPC) system. It can be used to perform secondary development for both communication parties (NMS and devices). This development focuses on services and shortens interconnection development periods.
gRPC supports the following languages: C++, Node.js, Python, Ruby, Objective-C, PHP, C#, Java, and Go.
gRPC is based on HTTP/2, which is better than HTTP/1 in performance. HTTP/2 features include bidirectional streaming, flow control, header compression, and multiplexing request of a single connection.
Data Push
Data Generation
Data Subscription
Data Source
Notes: For more information about gRPC, visit https://doc.oschina.net/grpc?t=58009.

## Slide 31: gRPC Protocol Stack
TCP
TLS
HTTP2
gRPC
Data model
Focus on services
gRPC encapsulation
The gRPC protocol stack consists of the following layers:
  TCP layer: This layer provides connection-oriented and reliable data links.
  Transport Layer Security (TLS) layer: This layer ensures secure communication between devices and collectors using the TLS protocol, which is optional.
  HTTP/2 application layer: gRPC is based on the HTTP/2 protocol. To be specific, gRPC uses HTTP/2 features such as bidirectional streams, flow control, and multiplexing.
  gRPC layer: This layer defines the protocol interaction format for RPCs. Public RPC methods are defined in common .proto files, for example, huawei-grpc-dialout.proto.
  Data model layer: This layer carries encoded service data. The data can be encoded in Google Protocol Buffers (GPB), XML, and JSON.
Data Push
Data Generation
Data Subscription
Data Source
Notes: For more information about gRPC, visit https://doc.oschina.net/grpc?t=58009.

## Slide 32: gRPC Service Methods
gRPC defines four service methods (distinguished by streams).
  Unary RPCs: The client sends a single request to the server and gets a single response back.
    Example: rpc Cancel(CancelArgs) returns(CancelReply) {};
  Server streaming RPCs: The client sends a request to the server, and the server continuously sends a stream back.
    Example: rpc Subscribe(SubsArgs) returns(stream SubsReply) {};
  Client streaming RPCs: The client continuously sends a stream to the server and waits for a response from the server.
    Example: rpc LotsOfGreetings(stream HelloRequest) returns (HelloResponse) {};
  Bidirectional streaming RPCs: Both the client and server send a stream.
    Example: rpc dataPublish(stream serviceArgs) returns(stream serviceArgs) {};
Data Push
Data Generation
Data Subscription
Data Source
Notes: For more information about gRPC, visit https://doc.oschina.net/grpc?t=58009.

## Slide 33: Telemetry Data Generation
Data collection
Data subscription
Data push
Data generation
Data source
UDP
NP
Data analysis
YANG models
SSH
XML
NETCONF
HTTP
JSON
GPB
RESTCONF
gRPC
VRP central processing module
CPU/NP
MIB
SNMP
UDP
BER
XML
JSON
RESTCONF
VRP central processing module
CPU/NP
MIB
BER
GBP position in the protocol stack
With telemetry, data is encoded using GPB, which provides a mechanism for serializing structured data flexibly, efficiently, and automatically. Similar to XML and JSON, GPB is a binary encoding mode with better performance.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 34: GPB Encoding
Before GPB Encoding | huawei-telemetry.proto | After GPB Decoding
{ 1:"HUAWEI" 2:"s4" 3:"huawei-ifm:ifm/interfaces/interface" 4:46 5:1515727243419 6:1515727243514 7{ 1[{ 1: 1515727243419 2 { 5{ 1[{ 5:1 16:2 25:"Eth-Trunk1" }] } } }] } } | syntax = "proto3"; package telemetry; message Telemetry { string node_id_str = 1; string subscription_id_str = 2; string sensor_path = 3; string proto_path = 13; uint64 collection_id = 4; uint64 collection_start_time = 5; uint64 msg_timestamp = 6; TelemetryGPBTable data_gpb = 7; uint64 collection_end_time = 8; uint32 current_period = 9; string except_desc = 10; string product_name = 11; Encoding encoding =12; string data_str = 14; } | { "node_id_str":"HUAWEI", "subscription_id_str":"s4", "sensor_path":"huawei-ifm:ifm/interfaces/interface", "collection_id":46, "collection_start_time":"2018/1/12 11:20:43.419", "msg_timestamp":"2018/1/12 11:20:43.514", "data_gpb":{ "row":[{ "timestamp":"2018/1/12 11:20:43.419", "content":{ "interfaces":{ "interface":[{ "ifAdminStatus":1, "ifIndex":2, "ifName":"Eth-Trunk1" }] } } }] }
GPB uses a .proto file to describe the message format and uses digits to replace flag names (keyword names).
Data Push
Data Generation
Data Subscription
Data Source
Notes: GPB transmits data in binary mode with a small number of bytes for each transmission, and therefore stands out from other encoding methods, such as XML and JSON, in terms of transmission efficiency. Data collection efficiency is a key concern of Telemetry.
For more information, see https://developers.google.com/protocol-buffers/.

## Slide 35: Telemetry Data Push
Data collection
Data subscription
Data push
Data generation
Data source
UDP
NP
Data analysis
Telemetry data can be pushed in gRPC or UDP mode.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 36: gRPC-based Telemetry Data Push
Subscription A (over the gRPC tunnel)
Subscription B (over the gRPC tunnel)
Subscription C (over the gRPC tunnel)
Subscription B, subscription C
Subscription C
Reply C
Reply B
Reply A (over the gRPC tunnel)
Reply C
C
C
NP
Reply B (over the gRPC tunnel)
Reply C (over the gRPC tunnel)
LPU's packet forwarding engine
LPU's CPU
MPU's CPU
Collector
gRPC is connection-oriented. A gRPC connection is set up only between the collector and the MPU's CPU.
Data Push
Data Generation
Data Subscription
Data Source
Notes: The collector functions as the gRPC client, and the device functions as the gRPC server.
The collector constructs data in GPB or JSON format based on the subscribed event, compiles a .proto file through Protocol Buffers, establishes a gRPC channel with the device, and sends a request message to the device using gRPC.
After receiving the request, the device parses the .proto file using Protocol Buffers to restore the data for processing.
After data sorting is complete, the device re-compiles the data using Protocol Buffers and sends a response to the collector using gRPC.
The collector receives the response message. So far, the gRPC interaction ends.

## Slide 37: UDP-based Telemetry Data Push
Subscription A (over the UDP tunnel)
Subscription B (over the UDP tunnel)
Subscription C (over the UDP tunnel)
Subscription B, subscription C
Subscription C
Reply C
Reply A (over the UDP tunnel)
C
C
NP
Reply B (over the UDP tunnel)
Reply C (over the UDP tunnel)
LPU's packet forwarding engine
LPU's CPU
MPU's CPU
Collector
Compared with gRPC, data push based on UDP is optimized. In addition to the UDP tunnel with the MPU's CPU, the collector establishes a UDP tunnel with the LPU's CPU. This reduces the pressure on the MPU's CPU and improves efficiency.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 38: Format of Pushed Data (Based on gRPC)
Hierarchy |  | Description
TCP layer |  | Underlying communication protocol, which is based on TCP connections.
TLS layer |  | This layer is optional. It is based on the TLS 1.2–encrypted channel and bidirectional certificate authentication.
HTTP/2 layer |  | gRPC is based on HTTP/2, which is better than HTTP/1 in performance. HTTP/2 features include bidirectional streaming, flow control, header compression, and multiplexing request of a single connection.
gRPC layer |  | Defines the protocol interaction format for RPCs.
Data model layer | RPC layer | The device proactively initiates an RPC request to the collector, which is defined in the huawei-grpc-dialout.proto file. A collector proactively initiates an RPC request for dynamic subscription to a device, which is defined in the huawei-grpc-dialin.proto file.
 | Telemetry layer | This is defined in the huawei-telemetry.proto file.
 | Service data layer | Service data at this layer needs to be encoded by the .proto file of the corresponding service, and the NMS needs to decode the data using the .proto file of the corresponding service as well. For example, if the sampling path is huawei-debug:debug/cpu-infos/cpu-info, the huawei-debug.proto file needs to be used for data encoding and decoding.
The gRPC encapsulation layer is provided by the gRPC open-source software. The following figure shows the protocol stack for pushing data based on gRPC.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 39: Format of Pushed Data (Based on UDP)
Hierarchy |  | Description
UDP layer |  | Underlying communication protocol, which is connectionless based on UDP.
DTLS layer |  | This layer is optional. It is based on the TLS 1.2–encrypted channel and bidirectional certificate authentication.
Message header layer |  | This layer describes the message header format of pushed telemetry data. The IETF definition is available at https://datatracker.ietf.org/doc/draft-ietf-netconf-udp-pub-channel/01/?include_text=1 The draft has six versions ranging from 00 to 05. Currently, telemetry is implemented based on the 01 version, as shown in the following figure.
Notification message layer | Telemetry layer | This is defined in the huawei-telemetry.proto file.
 | Service data layer | Service data at this layer needs to be encoded by the .proto file of the corresponding service, and the NMS needs to decode the data using the .proto file of the corresponding service as well. For example, if the sampling path is huawei-debug:debug/cpu-infos/cpu-info, the huawei-debug.proto file needs to be used for data encoding and decoding.
The format of the data pushed based on UDP is as follows.
Data Push
Data Generation
Data Subscription
Data Source

## Slide 40
Introduction to Telemetry
Telemetry Technical Fundamentals
Telemetry Configuration and Practice

## Slide 41: Case: Configuring Static Telemetry Subscription
Description:
A company has deployed a CE12800 switch with the management IP address 192.168.56.100. To better collect device performance data, it is required that the device push CPU information to the collector in static telemetry subscription mode.
GE1/0/0
192.168.56.1
192.168.56.100
Network device
Collector
(Local PC in this example)

## Slide 42: Configuration Roadmap
Device configuration:
  Enter the telemetry view.
  Configure a destination collector for receiving sampled data.
  Configure data sampling.
  Configure static telemetry subscription.
Collector configuration:
  Prepare and compile .proto files.
  Compile Python code: Import modules, create a gRPC server, obtain telemetry data, and decode telemetry data.
GE1/0/0
192.168.56.1
192.168.56.100
Network device
Collector
(Local PC in this example)
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 43: Configuring a Destination Collector
Enter the telemetry view.
<CE1> system-view immediately
[CE1] telemetry
[CE1-telemetry]
Configure a destination collector for receiving sampled data.
Create a destination group where a destination collector belongs. In this example, create a destination group named Dest1 and set the IP address and port number of the destination collector to 192.168.56.1 and 20000, respectively.
[CE1-telemetry] destination-group Dest1
[CE1-telemetry-destination-group-Dest1] ipv4-address 192.168.56.1 port 20000 protocol grpc no-tls
GE1/0/0
192.168.56.1
192.168.56.100
Network device
Collector
(Local PC in this example)
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 44: Configuring Data Sampling and Static Subscription
Configure data sampling.
When configuring static subscription to collect sampled data, create a sampling sensor group and specify a sampling path. In this example, create a sampling group named Sensor1 and configure a sampling path of CPU information.
[CE1-telemetry] sensor-group Sensor1
[CE1-telemetry-sensor-group-Sensor1] sensor-path huawei-devm:devm/cpuInfos/cpuInfo
Configure static subscription.
Create a subscription by associating the destination group and the sampling sensor group. In this example, the destination group Dest1 is associated with the sampling sensor group Sensor1, and the sampling interval is set to 1000 ms. After the configuration is complete, the device continuously pushes data to the destination collector.
[CE1-telemetry]subscription Sub1
[CE1-telemetry-subscription-Sub1]destination-group Dest1
[CE1-telemetry-subscription-Sub1]sensor-group Sensor1 sample-interval 1000
GE1/0/0
192.168.56.1
192.168.56.100
Network device
Collector
(Local PC in this example)
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 45: Compiling .proto Files for the Collector (1/3)
Compile .proto files.
After the device pushes the sampled data to the collector using telemetry, the collector must connect to the device to obtain the sampled data. gRPC and GPB knowledge and development experience are required for interconnection.
The .proto files corresponding to the device are released. The collector needs to perform secondary development based on these .proto files to connect to the device. You can download the Huawei device .proto files from the Huawei official website.
  Common .proto file:
    huawei-grpc-dialin.proto: The collector functions as the client to send an RPC request to the device to subscribe to sampled data for dynamic telemetry subscription.
    huawei-grpc-dialout.proto: The device functions as the client to initiate an RPC request to the collector to push data for static telemetry subscription.
    huawei-telemetry.proto: After sampling service data, the device uses the telemetry header to encapsulate the data, facilitating interconnection with the collector.
  Service .proto files:
    huawei-xxx.proto: After sampling service data, the device encodes the sampled data in GPB method using this file, and the NMS decodes data using this file as well. Example: huawei-mac.proto and huawei-mpls.proto
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 46: Compiling .proto Files for the Collector (2/3)
Compile .proto files to obtain the method invoked by the server. You can create a Python script, for example, run_codegen.py, and compile .proto files with the following codes:
from grpc_tools import protoc
protoc.main(
(
'',
'-I./protos',
'--python_out=.',
'--grpc_python_out=.',
‘./protos/huawei-grpc-dialout.proto’, #dialout file path
)
)
protoc.main(
(
'',
'-I./protos',
'--python_out=.',
'--grpc_python_out=.',
'./protos/huawei-devm.proto', # devm file path
)
)
protoc.main(
(
'',
'-I./protos',
'--python_out=.',
'--grpc_python_out=.',
‘./protos/huawei-telemetry.proto’, # telemetry file path
)
)
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.
Notes: After the files are compiled successfully, multiple Python files are generated in the current folder.

## Slide 47: Compiling .proto Files for the Collector (3/3)
Run the run_codegen.py script file to obtain related files generated in the current directory after .proto files are compiled in Python.
.py files generated after .proto files are compiled
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 48: Compiling Python Code (1/2)
Compile Python code to obtain device information.
_ONE_DAY_IN_SECONDS = 60 * 60 * 24
def serve():
server = grpc.server(futures.ThreadPoolExecutor(max_workers=10))
huawei_grpc_dialout_pb2_grpc.add_gRPCDataserviceServicer_to_server(Telemetry_CPU_Info(), server)
server.add_insecure_port('192.168.56.1:20000')
server.start()
try:
while True:
time.sleep(_ONE_DAY_IN_SECONDS)
except KeyboardInterrupt:
server.stop(0)
from concurrent import futures
import time
import importlib
import grpc
import huawei_grpc_dialout_pb2_grpc
import huawei_telemetry_pb2
Import modules.
--
Create a gRPC server object.
--
--
Register the data listening service.
--
Set the socket listening port.
--
Start the gRPC server.
Infinite loop listening
--
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.
Notes: The gRPC module is installed by running the pip install grpc command.
The huawei_grpc_dialout_pb2_grpc and huawei_telemetry_pb2 modules are generated after the .proto files are compiled.

## Slide 49: Compiling Python Code (2/2)
class Telemetry_CPU_Info(huawei_grpc_dialout_pb2_grpc.gRPCDataserviceServicer):
if __name__ == '__main__':
serve()
def __init__(self):
return
def dataPublish(self, request_iterator, context):
for i in request_iterator:
print ('############ start ############\n')
telemetry_data = huawei_telemetry_pb2.Telemetry.FromString(i.data)
print (telemetry_data)
for row_data in telemetry_data.data_gpb.row:
print ('-----------------')
print ('The proto path is :'+telemetry_data.proto_path)
print ('-----------------')
module_name = telemetry_data.proto_path.split('.')[0]
root_class = telemetry_data.proto_path.split('.')[1]
decode_module = importlib.import_module( module_name+'_pb2')
print (decode_module)
decode_func = getattr(decode_module,root_class).FromString
print ('----------- content is -----------\n')
print (decode_func(row_data.content))
print ('----------- done -----------------')
--
Create a class to inherit the Servicer method.
--
Inherit the dataPublish method.
Dynamically load a module for obtaining data through telemetry.
--
Dynamically load a module for obtaining data through telemetry.
--
Decode and print data.
--
--
Define the initialization method.

## Slide 50: Verifying the Configuration
Verify the configuration.
Run the following script to check whether the CPU information is successfully obtained.
----------- content is -----------
cpuInfos {
cpuInfo {
entIndex: 16842753
interval: 8
ovloadThreshold: 90
position: "1"
systemCpuUsage: 6
unovloadThreshold: 75
}
}
----------- done -----------------
Configure a destination collector.
Configure static subscription.
Configure data sampling.
Compile .proto files.
Compile Python code.
Verify the configuration.

## Slide 51
(Multiple) Which of the following methods can be used to push data using telemetry? ( )
  TCP
  UDP
  gRPC
What are telemetry data subscription modes?
Notes: BC
Static subscription and dynamic subscription

## Slide 52
  Telemetry remotely collects data from physical or virtual devices at a high speed.
  In a narrow sense, the telemetry framework consists of four modules: data source, data generation, data subscription, and data push.
  The data source uses YANG models to define devices. Data is generated using the GPB encoding method. Data subscription can be implemented in static or dynamic mode. Sampled data can be pushed based on gRPC or UDP.
  Python scripts can be run to subscribe to sampled device data through telemetry.

## Slide 53
Protobuf official website
  https://developers.google.com/protocol-buffers/
  gRPC official website
  https://www.grpc.io/