## Slide 1
Wan Changli/wwx408647
2020.5.25

## Slide 2: SDN Overview

## Slide 3
The open ecosystem of the computing industry brings booming development of multiple fields. The network industry is seeking transformation and development, where Software Defined Networking (SDN) is a concept that attracts great attention.
This course aims to help engineers understand SDN concepts and learn Huawei SDN solutions.

## Slide 4
On completion of this course, you will be able to:
  Describe the development of SDN.
  Describe Huawei SDN solutions.

## Slide 5
SDN Overview
Introduction to Huawei iMaster NCE

## Slide 6: SDN Origin
OpenFlow switches
SDN was developed by the Clean Slate Program at Stanford University as an innovative new network architecture. The core of SDN is to separate the control plane from the data plane of network devices to implement centralized control of the network control plane and provide good support for network application innovation.
SDN has three characteristics in initial phase: forwarding-control separation, centralized control, and open programmable interfaces.
OpenFlow controller
SDN application
OpenFlow
Control plane
Forwarding plane
Forwarding plane
Control plane
OpenFlow switches have only the data plane.
The OpenFlow controller provides control plane functions.
OpenFlow interconnection
Notes: OpenFlow was defined in the initial phase of SDN. With technology development, many other southbound interface (SBI) protocols are defined between the controller and network devices.

## Slide 7: Essential Requirements of SDN
The essence of SDN is to make networks more open, flexible, and simple. It builds a core brain for a network and implements fast service deployment, traffic optimization, or network service openness through centralized control in the global view.
Highlights:
  Provides centralized management, simplifying network management and O&M.
  Shields technical differences, simplifying network configuration and reducing O&M costs.
  Offers automatic optimization, improving network utilization.
  Deploys services rapidly, shortening the service provisioning time.
  Builds an open network, supporting open and programmable third-party applications.
SDN transforms the network architecture.
Notes: SDN is a broader concept, not limited to OpenFlow. Separation between the control and data planes is a method rather than the essence of SDN.

## Slide 8: SDN Architecture
APP
Application layer
Control layer
Infrastructure layer
NBI
SBI
Data forwarding
Service orchestration
Service collaboration
An SDN architecture consists of the application layer, control layer, and infrastructure layer. To communicate between these layers, SDN uses open interfaces where the northbound interfaces (NBIs) communicate between the infrastructure and control layers and the southbound interfaces (SBIs) communicates between the application and the control layers. OpenFlow is an SBI protocol.
Notes: Application layer: provides various upper-layer applications for service intents, such as OSS and OpenStack. The OSS is responsible for service orchestration of the entire network, and OpenStack is used for service orchestration of network, compute, and storage resources in a DC. There are also other applications at this layer. For example, a user deploys a security app. This app invokes NBIs of the controller, such as Block (Source IP，DestIP), regardless of the device locations. Then the controller delivers different instructions to network devices based on different southbound protocols.
Control layer: The SDN controller is deployed at this layer and is the core of the SDN network architecture. The control layer is the brain of the SDN system and implements network service orchestration.
Infrastructure layer: A network device receives instructions from the controller and performs data forwarding.
NBI: NBIs, mainly RESTful APIs, are used by the controller to interconnect with the application layer.
SBI: SBIs are used by the controller to interact with devices through protocols such as NETCONF, SNMP, OpenFlow, and OVSDB.

## Slide 9: Huawei SDN Network Architecture
Network
application
Forwarding device
Switch
CPE
AP
Router
Security gateway
VNF
NBI plane
RESTful
MTOSI/CORBA
Kafka/SFTP
Cloud platform
EMS
Orchestration
App
PCEP
interface
NETCONF
interface
OpenFlow
interface
BGP-LS
interface
OVSDB
interface
SNMP
interface
BGP
interface
JSON-RPC
interface
Telemetry
SBI
NBI
Huawei SDN network architecture supports various SBIs and NBIs, including OpenFlow, OVSDB, NETCONF, PCEP, RESTful, SNMP, BGP, JSON-RPC, and RESTCONF interfaces.
SNMP
RESTCONF
Notes: Cloud platform: resource management platform in a cloud DC. The cloud platform manages network, compute, and storage resources. OpenStack is the most mainstream open-source cloud platform.
The Element Management System (EMS) manages one or more telecommunication network elements (NEs) of a specific type.
Container-based orchestration: The container-based orchestration tool can also provide the network service orchestration function. Kubernetes is a mainstream tool.
MTOSI or CORBA is used to interconnect with the BSS or OSS. Kafka or SFTP can be used to connect to a big data platform.

## Slide 10: Huawei SDN Solution - Integrating Management, Control, and Analysis to Build an Intent-Driven Network
Self-service
portal
Mobile
app
Third-party app
Cloud platform
WAN/DCI
Campus
Branch
CPE
CPE
DC fabric
DC fabric
CPE
CPE
SD-WAN
AP
AP
WAN/DCI
Application layer
Network
management and control layer
Network layer
Campus
Branch
…
Controller
Manager
Analyzer

## Slide 11
SDN overview
Introduction to Huawei iMaster NCE
  iMaster NCE-Campus
  iMaster NCE-Fabric

## Slide 12: Introduction to iMaster NCE
3
4
2
SDN-based automatic service configuration and deployment
AI-based intelligent analysis, prediction, and troubleshooting
Automated + Intelligent
Manager + Controller + Analyzer
Planning + Construction + Maintenance + Optimization
Unified data base
Centralized detection, location and troubleshooting
Full lifecycle management
Simulation verification and monitoring optimization
Manager
Controller
Analyzer
=
Autonomous Driving
Network System
Network
Huawei iMaster NCE is an industry intelligent network automation platform that integrates management, control, analysis, and AI capabilities.
Notes: iMaster NCE effectively connects physical networks with business intents and implements centralized management, control, and analysis of global networks. It enables resource cloudification, full lifecycle automation, and data analytics-driven intelligent closed-loop management according to business and service intents and provides open network APIs for rapid integration with IT systems.
Huawei iMaster NCE can be used in the enterprise data center network (DCN), enterprise campus, and enterprise branch interconnection (SD-WAN) scenarios to make enterprise networks simpler, smarter, open, and secure, accelerating enterprise service transformation and innovation.

## Slide 13: iMaster NCE Application
Data center
iMaster NCE-Fabric *
Enterprise campus
iMaster NCE-Campus *
SD-WAN
iMaster NCE-WAN
WAN transmission
iMaster NCE-T
IP WAN
iMaster NCE-IP
* Introduced in this document

## Slide 14
SDN overview
Introduction to Huawei iMaster NCE
  iMaster NCE-Campus
  iMaster NCE-Fabric

## Slide 15: Introduction to a Campus
District/County core
District/County core
Government building
Smart street lamp
School
Hospital
Community
Industrial park
Safe city
Operations center
Municipal core
Data center (active)
Data center (standby)
Enterprise
Shopping mall and supermarket
Notes: Campuses are everywhere, including factories, government buildings and facilities, shopping malls, office buildings, school campuses, and parks. According to statistics, 90% of urban residents work and live in campuses, 80% of gross domestic product (GDP) is created in campuses, and each person stays in campuses for 18 hours every day.
Campus networks, as the infrastructure for campuses to connect to the digital world, are an indispensable part of campus construction and play an increasingly important role in daily working, R&D, production, and operation management.
Campus networks vary according to the size and industry characteristics. From the industry perspective, typical industry campus networks include education campus networks, government campus networks, commercial campus networks, office campus networks, and manufacturing campus networks.

## Slide 16: What Is a Campus Network?
A campus network generally refers to the internal network of an enterprise or organization, which is connected to the wide area network (WAN) and data center networks.
A campus network is built to ensure that key enterprise services are running more efficiently.
Based on the scale, campus networks can be classified into large-, medium-, and small-scale campus networks.
Some enterprises have branches dispersed in different areas. Each branch network can be considered as a single campus network.
Notes: Large- and medium-sized campus network: is a network where more than 2000 terminals are present.
  The network usually covers multiple buildings. Multiple aggregation layers are used to centralize networks of multiple buildings to the core layer.
  The access layer needs to provide high-density wired interfaces and a large number of access points (APs). In addition, the access layer needs to provide differentiated access control based on terminal types.
  To ensure service continuity, the campus network needs to support advanced capabilities such as the virtual network, free mobility, and security visibility.
  A campus network is typically equipped with a data center, which provides service computing and storage capabilities for the campus network.
  Typical examples: large-scale enterprise office networks, campus networks for higher education institutions, networks for large-scale government agencies, and airport networks.
Small- and medium-sized campus network: is a network where no more than 2000 terminals are present.
  Network layers are simple.
  Due to the limitations of traditional network management technologies, the branches are often managed separately.
  Typical examples: campus networks for primary/secondary schools, networks for small-scale government agencies, networks for small-scale supermarkets, and networks for micro stores.

## Slide 17: Campus Network Classification (1/3)
Scale
Large-sized campus network
Differ in the number of end users or NEs
Medium-sized campus network
Small-sized campus network
Number of end users > 2000
Number of NEs > 100
Number of end users: 200 to 2000
Number of NEs: 25 to 100
Number of terminal users < 200
Number of NEs < 25
Networks of different scales have different requirements and pain points.
Service object
Close campus network
Differ in service objects on the network
Open campus network
User: internal personnel only
Security requirements: network access control and external threat defense
Users: both internal and external personnel, such as the general public
Security requirements: access control, identity identification, behavior control, and threat defense
A campus network usually has both close and open subnets.

## Slide 18: Campus Network Classification (2/3)
Service
Single-service campus network
Differ in services
Multi-service campus network
Single service
Simple network architecture
Carries a large number of services and the network scale is large. Different services need to be isolated and guaranteed.
Has a complex and virtualized network architecture.
Access mode
Wired
campus
Differ in service objects on campus networks
Wireless
campus
Each device connected to the network must be connected to the preset network interface using cables.
The hierarchical architecture with clear logic facilitates troubleshooting.
A wireless campus network is built based on the 802.11 protocol (Wi-Fi), and is also called WLAN.
AP deployment and installation affect signal coverage. Interference and conflicts may occur and need to be optimized periodically.
Faults are difficult to locate.
Currently, most campus networks are hybrid networks of the wired and wireless networks.
How complex the network architecture is depends on the services running on the campus network.

## Slide 19: Campus Network Classification (3/3)
To meet the requirements of different industries, the campus network architecture is designed based on the characteristics of the industry that the campus network serves. In this case, a campus network solution dedicated for a specific industry is launched.
Enterprise Campus Network
Education Campus Network
Government Campus Network
Business Campus Network
Refers to an Ethernet-based enterprise office network.
Focuses on network reliability and advancement, to continuously improve employees' office experience and ensure the efficiency and quality of operation and production.
Classification: campus networks for primary/secondary schools and for higher education institutions.
Campus networks for higher education institutions are complex, since they may require teaching research networks, student networks, and operational dormitory networks.
High requirements on manageability, security, and advancement.
Refers to the internal network of government agencies.
Has high security requirements. Generally, the intranet and extranet are isolated to ensure the absolute security of confidential information.
Applicable to shopping malls, supermarkets, hotels, and parks.
Used to serve consumers and also contains subnets for internal office work.
Provides Internet access services and builds a business intelligence system to improve user experience, reduce O&M costs, improve business efficiency, and realize value transfer.

## Slide 20: Typical Logical ARCH of a Campus Network
Service application platform
LBS applications
IoT applications
Big data applications
Security applications
EMS
Security platform
Device monitoring Configuration management Fault management ...
Security monitoring
Policy control
Threat detection
Campus data network
Terminal
It is built based on Ethernet or WLAN technologies, and has various network devices deployed.
It carries multiple services, such as office, IoT, and video conferencing.
Wired and wireless terminals from both internal and external networks may access the campus network.
Terminal admission and security management need to be considered.
The next-generation EMS achieves automation, intelligence, and capability openness based on the traditional NMS and can interact with the security platform.
The security platform can identify and defend against advanced persistent threats, display the network-wide security situation, and interwork with network devices to isolate and block threat flows after detecting threats.
Service applications can be developed based on the EMS to build a service application platform for the campus network.

## Slide 21: Typical Physical ARCH of a Campus Network
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
NMS O&M zone
DataCenter
Core layer: This layer is the backbone area of a campus network, which is the data switching core. It connects the various parts of the campus network, such as the data center, aggregation layer, and campus egress.
Aggregation layer: This layer is a middle layer of a campus network, and is responsible for data aggregation or switching. Some basic network functions, such as routing, QoS, and security, are also provided at this layer.
Access layer: As the edge of a campus network, this layer connects end users to the campus network.
Egress zone: This zone is the edge between the campus internal network and the external network. Through this zone, internal users can access the public network and external users (including customers, partners, branches, and remote users) can access the internal network.
Data center area: This area has servers and application systems deployed to provide data and application services for internal and external users of the enterprise.
Demilitarized zone (DMZ): This zone has public servers deployed to provide access services to external guests (non-employees). The access permission to this area is strictly controlled.

## Slide 22: Huawei CloudCampus Solution
Fast network deployment, improving deployment efficiency by 600%
Device plug-and-play: simplified device deployment, scenario-based navigation, and template-based configuration
Simplified network deployment: network resource pooling, multi-purpose network, and automatic service provisioning
Fast service provisioning, improving user experience by 100%
Free mobility: GUI-based policy configuration, allowing users to access the network anytime and anywhere with unchanged roaming permission and user experience
Intelligent terminal identification: anti-spoofing for terminal access, with an intelligent terminal identification accuracy of over 95%
Intelligent HQoS: application-based scheduling and shaping, and refined bandwidth management, ensuring service experience of key users.
Fast intelligent O&M, improving network performance by over 50%
Real-time experience visualization: telemetry-based network experience visualization at each moment, for each user, and in each area
Precise fault analysis: proactively identifying 85% of typical network issues and providing suggestions, and comparing and analyzing real-time data to predict faults
Intelligent network optimization: predictive optimization of wireless networks based on historical data, improving network-wide performance by over 50% (certified by Tolly).
Analyzer
Manager
Controller
Design
Deploy
Policy
One-stop management platform
NETCONF/YANG
WAN/
Internet
Medium- and large-sized campuses
Small- and medium-sized campus
Campus interconnection
VN for office services
VN for R&D services
VN for office services
VN for R&D services
Security group 1
Security group 2
Security group 3
Security group 4
Security group 5
Access control policy
Bandwidth
Priority

## Slide 23: Cover All Campus Network Scenarios
Multi-branch campus
Multi-service campus
Simple-service campus
 | Simple-Service Campus | Multi-Service Campus | Multi-Branch Campus
Network structure | Network covering a single campus, which is mainly used for Internet access | Complex network covering multiple areas and carrying various services | Wired and wireless networks for Internet access are available in the headquarters and branches. VPNs are built between the headquarters and branches for interconnection.
General requirements | Management of various network devices and user authentication | Management of various network devices, user authentication, and service isolation | Management of various network devices (such as APs, switches, firewalls, and ARs), user authentication, and VPN management
Typical scenario | Multi-branch campuses and small-sized enterprises, such as hotels and primary/secondary schools | Education institutions, government agencies, and large-scale enterprises | Large-scale enterprises and financial branches
Internet
Hotels
Large-scale enterprises
Primary/secondary schools
Stores
Education institutions and large-scale enterprises
VN 1
VN 2
VN 3
Internet
MPLS

## Slide 24: Full Lifecycle Services
Planning (Day 0)
Construction (Day 1 to 2)
O&M (Day N)
Optimization (Day N)
Wired network design
WLAN design
Hardware installation
Routine device maintenance
Controller system maintenance
Experience visualization
Network monitoring
Network optimization
WLAN Planner
Manual planning
Manual installation
Exception detection
Fault demarcation
The services marked in blue are the full-lifecycle network services provided by iMaster NCE.
Site design
Network resource design
Physical network deployment
VN deployment
Service policy provisioning
Hardware installation
Physical network deployment
VN deployment
Service policy provisioning
Notes: Full Lifecycle: Planning, Construction, O&M, and Optimization

## Slide 25: Three CloudCampus Deployment Scenarios
Operations entity
Customers
MSPs and carriers
Huawei
On-Premise
MSP-owned Cloud
Scenario definition
Target customer
Huawei Public Cloud
Customers purchase and own software, such as the controller and analyzer, which can be deployed in their data centers or on the public cloud IaaS platform.
MSP-operated: MSPs purchase software, such as controller and analyzer, for operational purposes. The software can be deployed in their data centers or on the public cloud IaaS platform.
Huawei operated: Customers do not need to purchase the controller or analyzer software. Instead, customers just purchase the Huawei's cloud-managed network service.
Customers in industries such as government, education, large enterprise, retail, and financial services
MSPs and carriers
Customers in industries such as government, education, large enterprise, retail, and financial services
Intent-Driven CloudCampus Network

## Slide 26: Device Plug-and-Play
Registration center
DHCP server
Pre-configuration
Obtaining registration information through the DHCP server
Automatic device registration and login
Automatic configuration delivery
Deployment Through Barcode Scanning
DHCP-based Deployment
Deployment Through the Registration Center
1
2
3
4
1
1
2
2
3
3
4
4
5
Pre-configuration
Deployment by scanning barcodes
Automatic device registration and login
Automatic configuration delivery
Pre-configuration
Information synchronization
Obtaining registration information through the registration query center
Automatic device registration and login
Automatic configuration delivery
Notes: The device plug-and-play feature is applicable to multiple deployment modes, including deployment through barcode scanning, DHCP-based deployment, and deployment through the registration center.
Registration center: is one of the main components of the Huawei CloudCampus Solution for query of the device management mode and the home cloud management platform. According to the query result, a device determines whether to change to the cloud-based management mode and which cloud management platform it must register with. For example, all the APs that support cloud-based management will have the Huawei device registration query center's URL (register.naas.huawei.com) and port number (10020) pre-configured.

## Slide 27: One Network for Multiple Purposes
Internet
Border
AP
Host 1
Sales staff
Host 2
R&D employee
Host 3
IoT device
Host 4
Guest
Office network
R&D network
IoT
By leveraging the virtualization technology, multiple VNs are created on a physical campus network, each deployed with a unique service, such as office, R&D, and IoT.
iMaster NCE manages network-wide devices in a centralized manner. Administrators can configure networks on the iMaster NCE web UI.
iMaster NCE translates service configuration intents of an administrator into configuration commands and delivers them to devices through NETCONF to implement network autonomous driving.

## Slide 28: Free Mobility
Campus network
Free mobility: Enables users to have consistent network rights and security policies regardless of their locations and IP addresses.
Sales user
security group
R&D user
security group
Server resource
security group
User A
User B
User C
Access authentication
Access authentication
Access authentication
Configure security groups. A security group is a group of users for which the same security policy is used.
Define security group-based permission control policies and user experience policies and deliver the policies to network devices.
A security group is authorized to a user after the user passes access authentication.
1
2
3
After user traffic enters a network, network devices enforce policies based on the source and destination security groups of the traffic.
4
Security group configuration and policy delivery
Rights policy
Experience policy
Notes: Free Mobility: Policy Management Based on Security Groups

## Slide 29: Wired and Wireless Convergence
The switch integrates the AC function, eliminating wireless traffic forwarding bottlenecks and reducing fault nodes. Wired and wireless devices are centrally managed.
Unified management and converged forwarding of wired and wireless services
Converged management for wired and wireless users and gateway convergence
Converged authentication points for wired and wireless access
Unified wired and wireless policy enforcement
Wired and Wireless Convergence (Integrated AC)
This mode poses a wireless traffic bottleneck and increases faulty nodes.
Wired and wireless management is independent.
Wired and wireless authentication points are separated.
An AC card is installed on a switch to provide AC functions.
Hardware-level convergence only
WLAN with a Standalone AC
WLAN with an AC Card
Wired and wireless authentication points are separately deployed, policy control is decentralized, and traffic forwarding is separated, resulting in difficulties in fault troubleshooting and network management.
Standalone AC
AC card
Integrated AC

## Slide 30: Intelligent Terminal Identification
Built-in
terminal fingerprint library
Huawei supports identification of 1000+ office or IoT terminals.
>>
Requirements and Challenges
It is difficult to locate access spoofing.
An enterprise
100+ authentication
faults reported per day
50+ types of smart terminals
A university
Terminal information is collected by colleges:
MAC address collection is difficult and error-prone.
By terminal type
Automatic authorization
Camera
Is automatically added to the video surveillance group.
Is configured as a VIP.
By terminal type
Automatic authentication
Printer
Automatic MAC address authentication, without entering any MAC address
By terminal type
Spoofing detection
Recognized as an IP phone first and then as a PC
A terminal spoofing alarm is reported.
>>
Notes: Intelligent Terminal Identification, Ensuring Secure Access

## Slide 31: AI-Powered Intelligent O&M
As-Is: device-centric network management
To-Be: user experience-centric AI-powered intelligent O&M
Device-centric O&M method: User experience cannot be detected.
Fault-triggered responses: Potential faults cannot be identified.
Rely on professional engineers to locate faults onsite
SNMP
Network data collection within minutes
Topology management
Performance management
Alarm management
Configuration management
NMS
Experience visualization: telemetry-based data collection within seconds, visualized experience of each user and each application in real time
Potential fault identification and root cause location within minutes
Identify potential faults based on dynamic baselines and big data correlation analysis.
Accurately locate root causes of faults through KPI association analysis and protocol tracing.
Predictive network optimization: AI is used to intelligently analyze the AP load trend and implement predictive optimization on the wireless network.
The efficiency is improved by using algorithms. With scenario-based continuous learning and expert experience, intelligent O&M frees O&M personnel from complex alarms and noises, making O&M more automated and intelligent.
Traditional NMS
Telemetry
Network data collection within seconds
Visualized experience management
User journey playback
Potential fault identification
Root cause identification
Predictive network optimization
Intelligent network analyzer

## Slide 32
SDN Overview
Introduction to Huawei iMaster NCE
  iMaster NCE-Campus
  iMaster NCE-Fabric

## Slide 33: Introduction to a Data Center
A data center is an entire suit of facilities, including buildings. It includes the computer system and the devices related to the computer system (for example, communication and storage devices), as well as redundant data communication connections, environmental control devices, monitoring devices, and various safety devices.
A data center uses a layered architecture. In most cases, L1 refers to the data center’s infrastructure, and Layer 2 refers to the data center's ICT equipment.
Data center equipment room
Power distribution facilities
Cabinets + cabling system
Cooling facilities
Management and O&M center
Layer 1 (infrastructure)
Layer 2 (ICT equipment)
DCN
Server
SAN
Campus
Internet
Storage
DCI
Notes: The concepts, topology, and architecture of a data center in this course are based on layer 2 or above.

## Slide 34: Devices in a Data Center
Devices in a data center are classified into computing, storage, and network devices (excluding data center infrastructure).
Computing device
Server
1
Network device
Router
Switch
Firewall
3
Storage device
Storage array
2
Load balancer
IDS/IPS
FusionServer server
TaiShan server
Atlas AI computing platform
OceanStor Dorado all-flash storage
OceanStor V5 hybrid-flash storage
FusionStorage cloud storage
Cloud storage device
Notes: Huawei devices are used as an example here.

## Slide 35: Typical Data Center Networking
SAN (storage array)
Storage network (FC)
Server (compute node)
DCN (IP)
Distributed storage
Server (storage node)
A typical data center networking consists of a data center network (DCN), a storage area network (SAN), and servers.
Notes: DCN: enables communication between computing instances in a DC and between computing units and external egresses.
SAN: consists of storage arrays and Fiber Channel (FC) switches to provide block storage. The storage network that uses the FC protocol is called FC SAN, and the storage network that uses the IP protocol is called IP SAN.
Distributed storage: The deployment mode of distributed storage is different from that of storage array. Data is stored on multiple independent servers (storage nodes). It is also used as cloud storage.
Server (compute node): provides computing services.

## Slide 36: DCN
DCN: enables communication between units in a data center and between units and external egresses.
A data center network consists of various network devices and is divided into different areas based on services.
Test environment zone
Production environment zone
Spine
Leaf
Spine
Leaf
Server
Server
Core
Server
Campus network access zone
WAN access zone
Internet access zone
Notes: Data center networks can be flexibly divided into different zones based on enterprise or industry requirements. For example, a financial data center network can be divided into production zone 1, production zone 2, test zone 1, test zone 2, big data zone, operation management zone, and other zones.
In this example, the data center data network is divided in to the following zones:
  Internet access zone: transmits Internet access traffic from users.
  Campus network access zone: transmits traffic from users on enterprise campus networks.
  WAN access zone: connects to the enterprise-built WAN. Data centers and campuses in other cities may reside on the other side of this zone.
  Production environment zone: connects to the production environment.
  Test environment area: connects to the test environment.

## Slide 37: Huawei CloudFabric Solution
VM
VM
VM
VM
VM
VM
VM
VM
VM
Service Intent/Strategy
Simplification elements
Telemetry + ERSPAN
NETCONF + SNMP
Analyzer
Manager
Controller
+AI
iMaster NCE-Fabric provides full-lifecycle services covering planning, construction, O&M, and optimization.
Integrated planning and construction
The planning tool interworks with iMaster NCE-Fabric to implement integrated planning and construction.
Zero Touch Provisioning (ZTP)
Simplified deployment
Service intent self-understanding and conversion
Network change simulation and evaluation, eliminating human errors
Intelligent O&M
Rapid fault detection and location based on knowledge graph and expert experiences
Fast fault rectification based on expert experiences and simulation analysis
Real-time optimization
Local traffic inference and online model training and optimization based on AI Fabric
User behavior prediction and resource optimization suggestions

## Slide 38: Open Architecture, Building a DCN Ecosystem
Third-party computing management platform
OpenStack
Kubernetes
Third-party apps
Service provisioning
Resource reporting
Firewall
Load balancer
Switch
Resource synchronization
Virtual awareness
Configuration delivery
Status reporting
Router
Computing resource
RESTful
OpenFlow/OVSDB/NETCONF/BGP EVPN
Northbound ecosystem
Provides standard Neutron/GBP RESTful APIs to enable abstraction of fabric configuration.
Interconnects with standard OpenStack and Kubernetes.
Eastbound and westbound ecosystem
Supports interconnection with third-party computing management platforms and works with compute resources to implement on-demand VM on-boarding and elastic scaling.
Southbound ecosystem
Provides standard APIs for service provisioning and device configuration.
Provides southbound plug-ins, through which third-party devices can interoperate with Huawei devices.

## Slide 39: Simplified ZTP Deployment
Network administrator
Spine
Leaf
1
ZTP process:
  The network administrator starts the ZTP task on the iMaster NCE-Fabric GUI.
  A device automatically obtains an IP address to access iMaster NCE-Fabric.
  iMaster NCE-Fabric determines the device role (spine or leaf node), delivers configurations such as the management IP address, SNMP configuration, and NETCONF configuration to the device, and manages it through the management IP address.
  iMaster NCE-Fabric globally delivers interconnection configurations as well as OSPF or BGP configurations.
  The device goes online successfully, and the administrator checks network-wide information on iMaster NCE-Fabric.
2
3
4
5
Note: The DC uses the spine-leaf architecture.
VXLAN

## Slide 40: Network Intent Self-Understanding and Fast Service Provisioning
Intent conversion
Simulation verification
Network design
iMaster NCE-Fabric
Network configuration
Work order
Intent model
Built-in model:
ACL deployment
Network provisioning
2 to 3 days
10 minutes
1 to 2 days
Network design
Configuration delivery
Service verification
10 minutes
Huawei iMaster NCE-Fabric supports automatic and fast deployment of virtualization, cloud computing, and container networks.
Verification result analysis
Notes: iMaster NCE-Fabric can connect to customer IT systems to match an intent model for customer intents and deliver configurations to devices through NETCONF to implement fast service deployment.
iMaster NCE-Fabric can interconnect with the mainstream cloud platform OpenStack, virtualization platform vCenter and System Center, and the container orchestration platform Kubernetes.

## Slide 41: Network Change Simulation and Change Risk Prediction
Live-network configuration
Live-network topology
Live-network resource
Data collection/upload
Modeling and computing
Verification result
Network modeling
Formal verification algorithm
Establish physical, logical, and application network models.
Use the formal verification method to solve the problem.
Check whether resources on the live network are sufficient and whether the network is connected.
Analyze and display the impact of changes on original services.
Configuration to be changed
Resource sufficiency
Access connectivity
Impact on original services

## Slide 42: AI-powered Intelligent O&M for DCNs
Collection
Analysis
Decision
DC holographic data
Service flow data /Telemetry data
Root cause analysis
Knowledge inference engine
Intelligent analysis engine
Manual rectification
Recommended emergency plans:
Interface isolation
Configuration rollback
Capacity expansion recommendation
Huawei 30+ years of O&M
Expert experience
Continuous learning and training
based on real site faults
Knowledge
Model application
Risk prediction
Exception detection
Intent-based loop closing
Data cleaning
BGP
flapping
OSPF
flapping
ISIS
flapping
Interface flapping
BFD
flapping
Router ID conflict
AI-based exception identification
Network object modeling
Knowledge
Knowledge
Knowledge
Notes: iMaster NCE-FabricInsight provides AI-powered intelligent O&M capabilities for data centers.

## Slide 43
(Multiple) Which of the following deployment scenarios are supported by CloudCampus? ( )
A. On-premise scenario
B. Huawei public cloud scenario
C. MSP-built cloud scenario
D. Campus scenario
(Single) Which of the following is the latest product in Huawei CloudFabric Solution? ( )
A. iMaster NCE-Campus
B. iMaster NCE-Fabric
C. Agile Controller-DCN
Notes: 1. ABC
2. B

## Slide 44
SDN innovates the network architecture. It uses a controller to build a more open, flexible, and simplified network.
Huawei IDN solution covers various network scenarios, including enterprise campus networks, data center networks, SD-WAN, enterprise WAN IP networks, and enterprise transport networks.
This course introduces the CloudCampus and CloudFabric solutions. For more information about Huawei IDN solutions, see HCIP-Datacom certification materials in each domain.

## Slide 45
For more information about Huawei IDN solutions, see:
https://e.huawei.com/en/products/network-management-and-analysis-software.
For more information about Huawei solution certifications, see HCIP-Datacom courses of each domain.

## Slide 46
Huawei Talent: https://e.huawei.com/en/talent/#/home