## Slide 1
Chen Can/cwx934766
2020.6.17
Chen Can/cwx934766
2020.6.19

## Slide 2: RESTful Principles and Practices

## Slide 3
In the network communications field, network openness is an inevitable trend of industry development. In a fully connected, intelligent world, opening more interfaces means quick connections with other networks. Network openness not only transforms networks, but also further segments the industry chain, bringing new opportunities for industry development. Nowadays, REST is selected and preferred by a growing number of companies, and likewise, RESTful application programming interfaces (APIs) are growing in popularity across the entire network.
This course describes the concepts and functions of REST and RESTful, working principles of HTTP, and typical practices in invoking RESTful APIs.

## Slide 4
Upon completion of this course, you will be able to:
  Have full knowledge of the background, concepts, and highlights of REST.
  Understand the relationship between REST, RESTful, and RESTCONF.
  Master the HTTP packet format and field descriptions.
  Understand the relationship between HTTP, HTTPS, and HTTP/2.
  Grasp basic capabilities for invoking RESTful APIs.

## Slide 5
REST and RESTful
  Background of REST
  Overview of REST
Working Principle of HTTP
Practices in Invoking RESTful APIs

## Slide 6: Basic Concepts of Southbound and Northbound
Southbound and northbound are relative concepts. Generally, the interfaces provided by an upper-layer system for a lower-layer system are called southbound APIs, and the interfaces provided by a lower-layer system for an upper-layer system are called northbound APIs.
APIs provide the interaction function to implement data transmission.
Southbound API
Controller
Northbound API
MTOSI/CORBA/SNMP/REST
OSS
Notes: The operation support system (OSS) is a necessary support platform for telecom services.
MTOSI: Multi-Technology Operations System Interface
Common Object Request Broker Architecture (CORBA) is a standard object-oriented application program system specification formulated by Object Management Group (OMG).

## Slide 7: Development of Northbound APIs
There are many northbound API standards, for example, MTOSI and CORBA. Vendors' controllers need to open northbound APIs compliant with specific standards to easily interconnect with carriers' integrated network management platform.
Devices may use diverse northbound APIs such as SNMP, CORBA, and REST. Nowadays, these APIs are gradually unified into the REST style.
Controller
MTOSI/CORBA/SNMP
OSS
Controller
REST
OSS

## Slide 8: API Evolution: Unified URI Naming Conventions
REST standardizes universal resource identifier (URI) naming conventions. Resource-oriented URI names are easy to understand.
  A URI identifies the location of a resource.
With REST: URIs are independent and methods are clear.
Without REST: URIs were randomly named.
URIs with naming conventions of REST:
Reserving a meeting room: /meetingroom/B25R, with the calling method being POST
Canceling a reserved meeting room: /meetingroom/B25R, with the calling method being DELETE
Querying the meeting room status: /meetingroom/B25R, with the calling method being GET
URIs without constraints on naming conventions:
Reserving a meeting room: /reserve/meetingroom/B25R
Canceling a reserved meeting room: /cancel/meetingroom/B25R
Querying the meeting room status: /meetingroom/B25R?method=query

## Slide 9: API Evolution: Stateless Design
REST uses a stateless design to enhance system scalability.
  Stateful: The server needs to save and maintain the state information of previous requests. Each subsequent state depends on the previous state.
  Stateless: The server sends back the same response for invocation of the same request, function, or method, without depending on other requests. The server does not need to maintain state information, facilitating expansion. At least one URI is available to locate a resource.
With REST: stateless
Without REST: both stateful and stateless used
In the REST architecture, the required result can be obtained with only one request. For example, the salary can be queried using the following URIs:
Salary of Tom: http://oa.company.com/salary/tom
Salary of Jerry: http://oa.company.com/salary/jerry
Log in to the OA system
Access the personal center
Access the salary query page
View the salary
A client can obtain the required information only after multiple requests. The figure on the right shows an example of logging in to the office automation (OA) system to view the salary. The process is complex, affecting user experience.
The required information cannot be directly located using only one URI.
Notes: Stateful request: A server generally needs to save and maintain the status information of previous requests. Each request can use information about the previous requests by default.
Stateless request: The processing result on the server must be based on the information carried in the same request.

## Slide 10: API Evolution: Separation Between Frontend and Backend (1)
REST provides good cross-platform compatibility and separates the frontend from the backend.
  The frontend mainly involves the pages that can be viewed by users.
  The backend mainly involves the logical functions related to data processing.
With REST: separation between the frontend and backend
Without REST: tight coupling between the frontend and backend
Controller
(Servlet)
Model
(Java Beans)
View
(JSP)
Client
Request
Response
Client
Server MVC
Data
Data
Rendering
API
Server
Request
Request
Response
Response
PC
Android
iOS
Notes: An API is a set of predefined functions or methods for connecting different components of a software system. It is a set of routines that can be accessed by applications and developers based on software or hardware without having to access the source code or understand the details of the internal working mechanism. For example, if a computer needs to invoke information in a mobile phone, we simply need to connect the computer and the mobile phone by using a data cable. In this example, the interfaces on the computer and mobile phone at both ends of the data cable.

## Slide 11: Interface Evolution: Separation Between Frontend and Backend (2)
In early web projects, rendering is generally performed on the server. A client directly obtains and interacts with the rendered view on the server.
Controller
(Sevlet)
Model
(Java Beans)
View
(JSP)
Client
Request
Response
Client
Server MVC
Data
Data
Rendering
Advantage: The entire page is sent back with only one request, featuring a high loading speed.
Disadvantage: Components are closely associated with each other. If a view is modified on the frontend, the logical modules of the backend must be modified accordingly.
Notes: Rendering refers to the process of transforming views such as HTML into visual images that can be seen by human eyes.
For web applications of early days, a view is a graphical user interface (GUI) composed of HTML elements. For today's web applications, the GUI incorporates new elements such as Adobe Flash, XHTML, XML/XSL, and WML.
The Model-View-Controller (MVC) is a pattern for creating web applications and consists of three parts: controller, model, and view.
  The controller is responsible for processing user interaction in an application. Generally, the controller reads data from the view, controls user input, and sends data to the model.
  The model is responsible for processing the data logic of an application. Generally, the model stores and reads data from the database.
  The view is responsible for processing data display. Generally, a view is created based on model data.

## Slide 12: API Evolution: Separation Between Frontend and Backend (3)
REST develops rapidly with the emergence of the mobile Internet. The server cannot render a GUI for each type of terminal. Therefore, rendering on the server cannot meet the requirements of mobile Internet. To maintain compatibility with various types of terminals, REST emerges and becomes pervasive.
With REST, the server only processes data, and the client is responsible for GUI rendering. In this way, the frontend and backend are separated.
REST-compliant RESTful APIs provide a unified communication method for various types of terminals, which is beyond the reach of traditional APIs.
API
Server
Request
Request
Response
Response
PC
Android
iOS
Notes: An API is a set of predefined functions or methods for connecting different components of a software system. It is a set of routines that can be accessed by applications and developers based on software or hardware without having to access the source code or understand the details of the internal working mechanism.
Separation between the frontend and backend has become an industry standard for the Internet projects in the industry. It lays a solid foundation for the large-scale distributed architecture, elastic computing architecture, microservice architecture, and multi-terminal services (such as browsers, vehicle-mounted terminals, Android, and iOS). The key to separation between the frontend and backend is that the frontend page invokes the RESTful API of the backend for data interaction.

## Slide 13
REST and RESTful
  Background of REST
  Overview of REST
Working Principle of HTTP
Practices in Invoking RESTful APIs

## Slide 14: Overview of REST
Representational State Transfer (REST) was proposed by Roy Thomas Fielding, HTTP's leading designer, in his doctoral dissertation in 2000. In short, REST is a design style.
REST
Resource
State transfer
Presentation
  REST uses the client-server interaction framework and involves the following concepts:
  Resource
  Presentation
  State transfer
Notes: Abstract of Roy's doctoral dissertation Architectural Styles and the Design of Network-based Software Architectures: This dissertation explores a junction on the frontiers of two research disciplines in computer science: software and networking. Software research has long been concerned with the categorization of software designs and the development of design methodologies, but has rarely been able to objectively evaluate the impact of various design choices on system behavior. Networking research, in contrast, is focused on the details of generic communication behavior between systems and improving the performance of particular communication techniques, often ignoring the fact that changing the interaction style of an application can have more impact on performance than the communication protocols used for that interaction. My work is motivated by the desire to understand and evaluate the architectural design of network-based application software through principled use of architectural constraints, thereby obtaining the functional, performance, and social properties desired of an architecture.

## Slide 15: REST Concepts — Resource
A resource is an information entity. All things on the network can be abstracted as resources. Each resource has a URI. For example, ports, network elements (NEs), boards, and equipment rooms are resources.
Resources and operations are the core of REST. The URI is used to locate resources, and HTTP actions (GET, POST, PUT, and DELETE) are used to describe operations.
GET/POST/PUT/DELETE
API
Presentation layer: Format for presenting resources
State transfer: HTTP actions for create, read, update, delete (CRUD) operations
Resource: URI for locating resources
Notes: REST is short for Representational State Transfer, in which the main entity — resource — is not presented.

## Slide 16: REST Concepts — Presentation Layer
Representation is the way a resource is presented.
For example, a text can be presented in TXT, HTML, XML, JSON, or even binary format; an image can be presented in JPG, PNG, or other formats.
GET/POST/PUT/DELETE
API
Presentation layer: Format for presenting resources
State transfer: HTTP actions for CRUD operations
Resource: URI for locating resources
Notes: A URI represents only a resource entity but not its presentation.

## Slide 17: REST Concepts — State Transfer
Accessing a URI represents an interaction between the client and the server. In this process, data and status changes are involved.
Hypertext Transfer Protocol (HTTP) is a stateless protocol. This means that all states are stored on the server side, not on the client side. Therefore, the client performs operations on the server by using a certain method, so that a state transfer occurs on the server. Such a state transfer depends on the presentation layer, so it is called "Representational State Transfer".
The method used by the client is HTTP.
Presentation layer: Format for presenting resources
State transfer: HTTP actions for CRUD operations
Resource: URI for locating resources
GET/POST/PUT/DELETE
API

## Slide 18: RESTful and RESTCONF
RESTful APIs comply with the REST design style. There are no mandatory requirements on RESTful APIs, and therefore RESTful APIs can be defined freely.
RESTCONF APIs also comply with the REST design style. Unlike RESTful APIs, RESTCONF APIs must comply with RFC 8040 defined by Internet Engineering Task Force (IETF). RFC 8040 defines RESTCONF APIs and their specifications. RESTCONF APIs are based on HTTP and are used to access data defined in Yet Another Next Generation (YANG). RESTCONF allows web applications to access configuration data, status data, and event notifications of network devices in a modular and scalable manner.
REST + Configuration
REST style
RFC 8040
RESTCONF
Notes: YANG defines the storage content and configuration of data.

## Slide 19: Defining RESTful APIs
URI
Request method
Message header
Message body
Status code
All the preceding fields are contained in HTTP packets. Therefore, REST makes full use or heavily relies on HTTP.
HTTP response
HTTP request
What is the content defined when we define RESTful APIs?
Notes: Relationship between the URI and URL The URL is a subset of the URI. The former must be an absolute path, while the latter can be an absolute path or a relative path. For example, http://127.0.01:8080/AppName/rest/product/1 is a URL, and AppName/rest/product/1 is a URI.

## Slide 20
REST and RESTful
Working Principle of HTTP
  Overview of HTTP
  HTTP/1.1
  HTTPS and HTTP/2
Practices in Invoking RESTful APIs
Notes: As mentioned earlier, REST makes full use or heavily relies on HTTP. Next, we will move on to HTTP.

## Slide 21: Development of HTTP
1991
1996
2000
2009
1999
2013
2015
Future
HTTP/0.9
Only the GET method is supported.
The request header is not supported.
HTTP was proposed by Tim Berners-Lee in 1990. After the WWW Alliance was established, the IETF working group further optimized and released the HTTP protocol. Over the evolution from HTTP/0.9 to HTTP/3, HTTP offers increasingly high performance.
HTTP/1.0
Basic functions available, supporting rich text, request headers, and status codes
HTTP/1.1
Mainstream standard, supporting connection reuse and block-based transmission
HTTPS
TLS/SSL used
Encryption-enabled HTTP
SPDY
Predecessor of HTTP/2, which optimizes the performance of HTTP
QUIC
Predecessor of HTTP/3, which uses UDP to implement TCP + TLS + HTTP/2
HTTP/2
Second-generation protocol, supporting multiplexing, header compression, and priority
HTTP/3
HTTP-over-QUIC, which is being formulated
Notes: SPeeDY (SPDY) is a TCP-based application-layer protocol developed by Google. Its objective is to optimize the performance of HTTP and shorten the loading time of web pages and improve security by using technologies such as compression, multiplexing, and priority. The core idea of SPDY is to minimize the number of TCP connections. SPDY is an enhancement to HTTP, instead of a protocol for replacing HTTP.
Quick UDP Internet Connection (QUIC) is a UDP-based low-delay Internet transport layer protocol developed by Google. In November 2016, the IETF convened the first meeting of the QUIC working group, which attracted wide attention from the industry. This means that QUIC starts its standardization process and will become a next-generation transport layer protocol.

## Slide 22: Overview of HTTP
Hypertext Transfer Protocol (HTTP) is an application layer protocol for distributed, collaborative, and hypermedia information systems. HTTP has been used by the World Wide Web since its inception.
It uses TCP/IP to transmit data and uses TCP port 80 by default. Websites starting with http:// are standard HTTP services.
Notes: The data transmitted using HTTP can be HTML, images, texts, and so on.

## Slide 23: Working Principle of HTTP
HTTP is based on the client/server (C/S) architecture. The HTTP request and response process is as follows:
  A client establishes a TCP connection with the server.
  The client sends an HTTP request, which consists of a request line, request header, empty line, and request data.
  The server receives the request and sends back an HTTP response, which consists of a status line, response header, empty line, and response body.
  The TCP connection is released.
  The client parses the status line, response header, and response body in sequence and displays the response packet. If the body contains HTML data, the client formats the data based on the HTML syntax and displays the data.
HTTP response
HTTP request
Client
Server
Notes: An HTTP client is usually a browser. A web server can be an Apache server or an Internet Information Services (IIS) server.
When a TCP connection is released, if the value of the Connection field in the packet header is close, the server proactively closes the TCP connection, and the client passively closes and releases the TCP connection. If the value of Connection is keepalive, the connection lasts for a period of time and can continue to receive requests.

## Slide 24: Features of HTTP
HTTP has the following features:
  Connectionless: Only one request is processed for each connection. After processing the client's request, the server disconnects from the client.
  Media independent: Any type of data can be sent by HTTP as long as both the client and the server know how to handle the data content. It is required for the client as well as the server to specify the content type using appropriate MIME-type.
  Stateless: The server and client are aware of each other only during a current request. Afterwards, both of them forget about each other. This facilitates quick processing of a large number of transactions and enhances the protocol scalability.
Client
Server
Connectionless
Media independent
Stateless
HTTP request
HTTP response
Notes: The browser differentiates the displayed content such as HTML, XML, GIF, and flash based on MIME-type.
Advantages of the connectionless feature: This mode saves the transmission time and improves the concurrent performance. No persistent connection is established. Instead, one response is made to each request. However, if a connection is repeatedly established and torn down, the efficiency is affected. In HTTP/1.1, a TCP connection is maintained between the browser and the server for a period of time and will not be disconnected immediately after a request ends.
Stateless means that, if the processing of subsequent packets requires the previously exchanged information, the information must be retransmitted. Although HTTP/1.1 is a stateless protocol, cookies are introduced to implement the function of maintaining status information.
A cookie is a text file stored on a client. This file is associated with a specific web page and saves the information about the web page accessed by the client.

## Slide 25
REST and RESTful
Working Principle of HTTP
  Overview of HTTP
  HTTP/1.1
  HTTPS and HTTP/2
Practices in Invoking RESTful APIs
Notes: HTTP/1.1 has been widely used since it was proposed in 1999 and has become a mainstream standard for more than 20 years. In the following part, we will introduce HTTP packets, which are based on HTTP/1.1.

## Slide 26: Client Request Message
An HTTP request message sent by a client consists of a request line, request header, empty line, and request data. The following figure shows the format of a request message.
Request method
Protocol version
Data
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Request header
Request Data
Request line
Empty line
URI
Space
...
Linefeed
Request header
Request Data
Request line
Empty line

## Slide 27: Client Request Message - Request Line
A request line consists of the request method field, URI field, and HTTP version field.
  Request method: HTTP request method, for example, GET and POST. An HTTP client (for example, a browser) must specify the request type when sending a request to the server.
  URI: A URI identifies the resource involved in a request.
  Protocol version: The protocol version allows the sender to indicate the format of a message and its capacity for understanding further HTTP communication.
Request Line
Request Header
Request Data
Request method
URI
Protocol version
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
  Example of a request line: GET http://www.w3.org/pub/WWW/TheProject.html HTTP/1.1

## Slide 28: HTTP Request Method
HTTP requests can use multiple request methods. HTTP 1.0 defines three request methods: GET, POST, and HEAD. HTTP 1.1 provides six new request methods: OPTIONS, PUT, PATCH, DELETE, TRACE, and CONNECT.
Method | Function
GET | Requests the specified page information. The server returns the specific data.
POST | Submits data, for example, a form.
HEAD | Similar to the GET method. However, the response does not contain any specific data. HEAD is used to obtain the header.
PUT | Updates and modifies data.
DELETE | Deletes a specified page.
CONNECT | Implements HTTP proxy.
OPTIONS | Allows the client to check the server performance.
TRACE | Echoes back the request received by the server. This is used for testing or diagnosis.
PATCH | Partially updates known resources.
Request Line
Request Header
Request Data

## Slide 29: Client Request Message - Request Header
The request header allows the client to send additional information about the request to the server. These fields act as request modifiers whose semantics are equivalent to the parameters invoked in the programming language method.
Request method
URI
Protocol version
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Example of a request header:
Accept: text/html
Accept-Encoding: gzip, deflate, br
Connection: keep-alive
Request Line
Request Header
Request Data

## Slide 30: Request Header Fields
Request Header Field | Description
Accept | Media types which are acceptable for the response.
Accept-Encoding | Data encoding format that can be used by the client for decoding, for example, gzip.
Accept-Language | Natural languages that are preferred as a response to the request. This field is mandatory if the server can provide more than one language.
Authorization | Authorization information, which is usually contained in the response to the WWW-Authenticate header sent by the server.
Content-Type | Media type of the data. The default value is text/plain.
Content-Length | Length of the request message body.
Host | Name of the host to be accessed by the client.
Referer | Resource from which the client accesses the server. This field contains a URI, indicating that the client accesses the requested page from the page represented by the URI.
User-Agent | Information about the user who sends the request and the client type.
Cookie | Used by the client to save the data returned by the server. Generally, the user identity information is saved.
Connection | Whether to disconnect the connection after the request is processed.
Request Line
Request Header
Request Data
Notes: In HTTP 1.0, each connection involves only one request and response and is closed after the request is processed. HTTP 1.0 does not have the Host field. In HTTP 1.1, multiple requests and responses can be transmitted in the same connection, and multiple requests can be processed concurrently.
WWW-Authenticate is a simple and effective user identity authentication technology in the early stage.
The browser differentiates the displayed content such as HTML, XML, GIF, and flash based on MIME-type.
For more information, refer to RFC HTTP 1.1 at https://www.ietf.org/rfc/rfc2616.html.

## Slide 31: Client Request Message — Request Data
Empty line: The server is notified of the end of a request header through an empty line.
Request data: If the GET method is used, the request data is empty. If the POST method is used, the request data is the data to be submitted.
Request method
URI
Protocol version
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Example of request data:
user=admin&password=123456
Request Line
Request Header
Request Data

## Slide 32: Server Response Message
An HTTP response consists of four parts: status line, response header, empty line, and response body.
Protocol version
Status code
Reason phrase
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Response header
Response body
Status line
Empty line

## Slide 33: Server Response Message — Status Line
The first line of the response message is the status line, which consists of the protocol version, status code, and reason phrase, separated by a space character.
  Protocol version: The protocol version allows the sender to indicate the format of a message and its capacity for understanding further HTTP communication.
  Status code: a three-digit result code, which is used to return the operation result to the client.
  Reason phrase: a short text description of the status code, which facilitates understanding.
Status line
Response header
Response body
Protocol version
Status code
Reason phrase
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Example of a status line: HTTP1.1 200 OK

## Slide 34: Status Code
An HTTP status code is a three-digit number indicating the status of a response from the server. It is used to return the operation result to the client.
Status Code |  | Description | 
1XX | (Informational) The request is received. | 100 Continue | If the request is received, go to the next step.
2XX | (Successful) The request is successful. | 200 OK | Success. The response body is available.
 |  | 201 Created | Resource created successfully.
 |  | 204 No Content | Success. No response body is available.
3XX | (Redirection) Further operations need to be performed. | 301 Moved Permanently | A new URI is allocated to the target resource, and all future resources will be associated with the new URI.
4XX | (Client Error) Request error. | 400 Bad Request | The request body is incorrect and carries error information.
 |  | 401 Unauthorized | Authorization failed. For example, the certificate does not match.
 |  | 403 Forbidden | Access denied. The possible cause is that the user attempts to perform operations beyond the permission or the login user name or password is incorrect.
 |  | 404 Not Found | The requested resource cannot be found.
5XX | (Server Error) Server error. | 500 Internal Server Error | The request cannot be executed due to an internal server error. The user needs to resend the request later.
 |  | 501 Not Implemented | The function has not been implemented.
Status line
Response header
Response body

## Slide 35: Server Response Message — Response Header
A response header allows the server to transfer additional information about the response. These header fields provide information about the server and the resource identified by the URI.
Protocol version
Status code
Reason phrase
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Example of a response header: Server: JSP3/2.0.14
Status line
Response header
Response body
Notes: The response header describes the basic information about the server and data. The server uses the response header to notify the client of how to process the data that it replies to.

## Slide 36: Common Fields in the Response Header
Response Header Field | Description
Allow | Request methods, for example, GET and POST, supported by the server.
Content-Encoding | Encoding method of a document. The content type specified by Content-Type can be obtained only after decoding.
Content-Length | Content length. This field is required only when the client uses a persistent HTTP connection.
Content-Type | Media type of the data. The default value is text/plain.
Date | Current Greenwich Mean Time (GMT) time.
Location | Location from which the client obtains resources. This field is used together with status code 302 to specify a new URI as the recipient.
Server | Type of a server.
Set-Cookie | Cookie associated with the page.
Transfer-Encoding | Data transfer format.
WWW-Authenticate | Type of authorization information that the client should provide in the Authorization header. This field is mandatory in a response that contains the 401 (Unauthorized) status line.
Status line
Response header
Response body
Notes: The HTTP response header is often combined with the status code. For example, the status code 302 (indicating that the location has changed) is usually used together with the Location header, and the status code 401 (Unauthorized) must be used together with a WWW-Authenticate header. The response header can be used to set the cookie, specify the date, instruct the client to refresh the page at the specified interval, and so on.

## Slide 37: Server Response Message — Response Body
Empty line: It is used to inform the server of the end of the response header.
Response body: message body of the response. If data of the pure data type is requested by the client, pure data is returned. If an HTML page is requested, the HTML code is returned.
Protocol version
Status code
Reason phrase
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Status line
Response header
Response body

## Slide 38: Client Request Message — Example
POST http://www.w3.org/pub/WWW/TheProject.html HTTP/1.1
Accept: text/html
Accept-Encoding: gzip, deflate, br
Accept-Language: zh-CN,zh;q=0.9
Content-Type: text/html;charset=utf-8
Connection: keep-alive
user=admin&password=123456
Request method
URI
Protocol version
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
Request header
Request data
Request line
Empty line
A client sends a request containing the user name and password to the server for login authentication.

## Slide 39: Server Response Message — Example
Response header
Response body
Status line
Empty line
HTTP/1.1 200 OK
Date: Thu, 28 May 2020 07:49:08 GMT
Content-Encoding: gzip, deflate, br
Accept-Language: zh-CN,zh;q=0.9
Content-Type: text/html
Connection: keep-alive
Login succeeded
Protocol version
Status code
Reason phrase
Data
Space
Space
Carriage return
Linefeed
Header field name:Value
Carriage return
Linefeed
...
Header field name:Value
Carriage return
Linefeed
Carriage return
Linefeed
The server sends a response to the client, indicating that the authentication is successful.

## Slide 40
REST and RESTful
Working Principle of HTTP
  Overview of HTTP
  HTTP/1.1
  HTTPS and HTTP/2
Practices in Invoking RESTful APIs

## Slide 41: Overview of HTTPS
Based on HTTP, Hypertext Transfer Protocol over Secure Sockets Layer (HTTPS) uses SSL/TLS for encryption, enhancing security.
HTTP vs. HTTPS
Client
Server
Server
Client
IP
TCP
HTTP
IP
TCP
TLS
HTTP
Identity authentication
Information encryption
Integrity check
Plaintext
Ciphertext
Notes: HTTP transmits information in plaintext, which may pose risks of information interception, tampering, and hijacking. Transport Layer Security (TLS) provides identity authentication, information encryption, and integrity check functions, and therefore can prevent such problems.

## Slide 42: Overview of SSL/TLS
Secure Sockets Layer (SSL) and Transport Layer Security (TLS) are security protocols that ensure security and data integrity for network communication.
TLS is the successor of SSL. SSL and TLS encrypt data transmitted on network connections between the transport layer and application layer without affecting the TCP and HTTP protocols. Therefore, if HTTPS is used, it does not require much modification on HTTP pages.
Data integrity: HTTPS uses SSL/TLS to encrypt and transmit all HTTP packets. All information is encrypted and cannot be intercepted or tampered with by third parties.
Data verification: Communication data is verified. If data is tampered with, the communication parties can immediately detect the tampering.
Trusted data source: Identity certificates are used to prevent identity spoofing.
Features of HTTPS communication using SSL/TLS
Risks of HTTP communication without using SSL/TLS
Eavesdropping: HTTP transmits information in plaintext, and third parties can obtain communication data.
Tampering: Third parties can tamper with the communication content.
Pretending: Third parties can pretend others to participate in communications.
Notes: For more information, refer to the RFC document at https://www.ietf.org/rfc/rfc5246.html.

## Slide 43: Overview of HTTP/2
HTTP/2 is the second major version of the HTTP protocol. It was initially named HTTP 2.0 and is based on the SPeeDY (SPDY) protocol.
HTTP/2 greatly improves web performance without changing HTTP semantics, methods, status codes, URIs, and header fields.
HTTP/1.1
Latency: 57 ms
Load time: 7.84s
30%
HTTP/2
Latency: 38 ms
Load time: 3.6s
80%
Notes: SPDY is a TCP-based application-layer protocol developed by Google. SPDY aims to optimize the performance of HTTP and shorten the loading time of web pages and improve security by using technologies such as compression, multiplexing, and priority. The core idea of SPDY is to minimize the number of TCP connections. SPDY is an enhancement to HTTP, instead of a protocol for replacing HTTP.

## Slide 44: Core of HTTP/2 — Binary Transmission
The core of performance enhancement in HTTP/2 is binary transmission.
In HTTP/1, data is transmitted in text mode, which has some defects. This is because various scenarios need to be considered to achieve robustness, due to the diversity of text formats. On the contrary, the binary format involves only 0s and 1s, featuring significant convenience and robustness.
Session layer
Transport layer
Network layer
POST http://www.w3.org HTTP/1.1
Accept: text/html
Content-Type: text/html;charset=utf-8
Connection: keep-alive
user=admin&password=123456
Header
HTTP/1.1
HTTP/2
Frame
Application layer (HTTP)
Notes: Enhancements to HTTP/2:
Header compression: The HPACK algorithm is used to compress headers to reduce the header size and improve performance.
Multiplexing: A request message can be divided into frames, which are sent in sequence and are reassembled at the other end. In HTTP/1.1, when a client sends multiple requests through a TCP connection, the server can only respond to the requests in sequence. Subsequent requests may be blocked.
Resource pushing: In addition to responding to client requests, the server can push additional resources to clients.
Priority: HTTP/2 defines complex priority rules. A browser can request multiple resources at a time and specify priorities to help the server determine how to process these resources, avoiding resource competition.

## Slide 45
REST and RESTful
Working Principle of HTTP
Practices in Invoking RESTful APIs

## Slide 46: Case: Invoking RESTful APIs to Obtain Tokens
Description:
Huawei iMaster NCE is a network automation and intelligence platform that integrates management, control, analysis, and artificial intelligence (AI) functions. In the SDN network architecture, iMaster NCE centrally manages network devices. You can implement intent-driven networks based on open northbound APIs of iMaster NCE.
This case describes an example of how to use the Python Requests module to log in to iMaster NCE and invoke service interfaces.
Client (CloudIDE)
Send back an HTTP response containing a token.
Send an HTTP POST request to obtain a token.
Server (iMaster NCE)
Notes: In this case, two objects are involved in the networking: CloudIDE and iMaster NCE.
CloudIDE is a cloud-based development environment provided by HUAWEI CLOUD. The local environment can also be used to write code.
A sandbox environment is available to iMaster NCE in the datacom developer community.
A token is a character string used for authentication on APIs.
For details, see HCIP-Datacom-Northbound Openness Lab Guide.

## Slide 47: Case: Invoking RESTful APIs to Obtain Tokens
Configuration roadmap:
Prepare the environment, including the IDE and sandbox environment.
Compile the code for invoking Python RESTful APIs.
Verify the configuration.
Client (CloudIDE)
Send back an HTTP response containing a token.
Send an HTTP POST request to obtain a token.
Server (iMaster NCE)

## Slide 48: Procedure: Create a Code Repository
Access the CodeHub console and create a project and a code repository on the cloud.
Notes: For more operations, see the CodeHub guide at https://support.huaweicloud.com/codehub/index.html.

## Slide 49: Procedure: Fork the Complete Code
Fork the complete code to the repository. In this example, the complete code has been uploaded to DevCloud on HUAWEI CLOUD. You can use Huawei CloudIDE to download the code to the local host. (Alternatively, you can perform online programming.)
Notes: Code in DevCloud on HUAWEI CLOUD: https://devcloud.cn-north-4.huaweicloud.com/codehub/project/68494a8ad06b4eea9a1c3f18be115161/codehub/620653/home

## Slide 50: Procedure: Start the CloudIDE
Click CloudIDE to open the code.
Check the code in CloudIDE.

## Slide 51: Procedure: Reserve a Sandbox Environment
Reserve a sandbox environment.
The developer community provides the sandbox experience. The intent-driven campus network sandbox environment is used as an example.
You can experience the sandbox environment in three ways: Quick Try, Demo Commissioning, and API Commissioning. Here, Quick Try in CloudIDE is used as an example.
Notes: Website for reserving a sandbox environment: https://devzone.huawei.com/openecosystem/experienceView/campus.html

## Slide 52: Step: Check Sandbox Information
Check sandbox information.
Tenant account: account for logging in to iMaster NCE.
North Account: account used by a location application to interact with iMaster NCE.
Northbound IP:Port: URL for logging in to iMaster NCE. You can click Try Now to log in to iMaster NCE.
Password: password for logging in to the sandbox environment.

## Slide 53: Procedure: Install the Requests Module
Install the Requests module.
The Python Requests module is required in this experiment. Create and run the setup.py script in CloudIDE to install the Requests module. Alternatively, run pip3 install requests on the CloudIDE Python CLI to install the Requests module.
import os
os.system("pip3 install requests")
Notes: To run the code, right-click setup.py and choose Run Python File in Terminal from the shortcut menu.

## Slide 54: Procedure: Compile a Python Script
Compile a Python script.
import requests
nbi_name = "campus02@north.com"
nbi_pwd = "5aAZ4lh44@"
host = "139.9.213.72"
port = "18002"
POST_TOKEN_URL = "/controller/v2/tokens"
post_token_url = "https://" + host + ":" + port + POST_TOKEN_URL
headers_post = {'Content-Type': 'application/json', 'Accept': 'application/json'}
r = requests.post(post_token_url, headers=headers_post, json={"userName": nbi_name, "password": nbi_pwd}, verify=False)
token_id = r.json()['data']['token_id']
print("1.[Get Token Id]")
print("[post_token_url]:"+post_token_url)
print("[token_id]:"+token_id)
Configure the northbound user information and northbound address.
--
Define the URI of an interface.
--
Configure the URL.
--
Configure the request header.
--
Initiate a request, whose body is in JSON format.
--
Parse the returned data to obtain the token.

## Slide 55: Procedure: Verify the Configuration
1.[Get Token Id]
[Post_token_url]: https://139.9.213.72:18002/controller/v2/tokens
[Token_id]: x-rs5jvy7z47vsum042r2qc9vtaq44o9hgqohf3uca7z9clio5vvvz86al3s5dvs0aphpck5defw45uqpi3xdgddmn482kgajutf7vlfs649rw6k5c6r6l0a5i1g4b5j9c
The token (specified by token_id) is obtained by invoking the RESTful API.

## Slide 56
(Single) Which of the following HTTP request methods does not need to contain request data in an HTTP request? ( )
  POST
  GET
  PUT
  DELETE
  What is the relationship between REST and RESTful?
Notes: B
RESTful APIs comply with the REST design style.

## Slide 57
REST is an architectural or design style rather than a standard. It provides only design principles and constraints.
REST makes full use of HTTP. The core of REST is to perform operations (such as GET, POST, PUT, and DELETE) on resources in multiple forms.
By invoking RESTful APIs, users can write Python scripts to implement automation as required.

## Slide 58
REST dissertation
  https://www.ics.uci.edu/~fielding/pubs/dissertation/rest_arch_style.htm
RFC HTTP/1.1
  https://www.ietf.org/rfc/rfc2616.html
  RFC HTTP/2
  https://www.ietf.org/rfc/rfc7540.html
  RFC HTTPS
  https://www.ietf.org/rfc/rfc2818.html