## Slide 1
V300R019C10
V1R1
Lu Binghao 00396298
2019.12.06
New
iMaster NCE-Fabric

## Slide 2: iMaster NCE-Fabric Open API Introduction

## Slide 3
iMaster NCE-Fabric is a next-generation SDN controller for enterprise DC markets and is a core component of Huawei CloudFabric Solution.
iMaster NCE-Fabric can centrally manage cloud data center networks and provide automatic mapping from the application network to the physical network, resource pooling, and visualized O&M, helping customers build service-centric dynamic network service scheduling capabilities.
iMaster NCE-Fabric provides standard RESTful API openness capabilities, which can be used for:
  Seamless interconnection with customers' service systems, enabling customers to flexibly deploy and schedule network resources based on their service development.
  Cooperation with partners to develop innovative apps, continuously creating value for enterprise customers.

## Slide 4
Upon completion of this course, you will be able to:
  Understand the basic functions of iMaster NCE-Fabric.
  Understand constraints and specifications of iMaster NCE-Fabric open APIs.
  Understand the main open APIs and typical application scenarios of iMaster NCE-Fabric.
  Complete the example of invoking Neutron APIs for intra-VPC communication.

## Slide 5
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 6: iMaster NCE-Fabric Overview
  Automatic
  Application-based automatic network configuration and graphical configuration, implementing minute-level service provisioning
  Zero touch configuration
  VM-level physical path visualization
  Reliable
  Industry's top management capability, achieving geo-redundancy with clusters
  Data consistency check, ensuring a highly reliable network running
  Refined O&M
  Security resource pool management
  Dynamic and flexible scheduling and orchestration of service resources
  RBAC-based system security protection
  Open
  Interconnection with the standard OpenStack/Huawei FusionSphere and Kubernetes/Huawei FusionStage
  Association with third-party computing management platforms
  Interconnection with third-party app systems such as the customer's service system
  iMaster NCE-Fabric
  Abstracts network resources and services in the northbound and adapts to various devices and networks in the southbound
Network control layer
Fabric/
Network service layer
Service presentation/
orchestration layer
Server layer
vSwitch
VAS
Physical server
VM
VM
VM
vSwitch
VM-Web
VM-App
LB
Firewall
VXLAN
CE switch
Automatic
Deployment
Open
Architecture
Refined
O&M
OpenFlow/OVSDB/NETCONF
RESTful
Third-party app
FusionSphere
OpenStack
Third-party cloud platform
Kubernetes
FusionStage
Third-party computing management platform
Underlay
Overlay
Service orchestration

## Slide 7: iMaster NCE-Fabric Key Features
Service provisioning in multiple scenarios
Cloud-network integration
Network virtualization – computing
Network virtualization – hosting
Container network
Multi-fabric network
management
Network overlay
Hybrid overlay
Multicast overlay
IPv6 overlay
Multi-DC pooling management
Remote management of DCs using a single controller cluster
DC management using active and standby controller clusters
Independent deployment of multiple sets of controller clusters
Comprehensive refined O&M
Network-wide resource visualization
Three-level topology visibility
Service path visibility
Loop detection
One-click emergency
Flexible multi-service orchestration
Service Function Chain (SFC)
Microsegmentation

## Slide 8: iMaster NCE-Fabric Open Architecture
Third-party computing management platform
OpenStack
Kubernetes
Third-party app
Service provisioning
Resource reporting
Firewall
LB
Switch
Resource synchronization
Virtual awareness
Configuration delivery
Status reporting
Router
Compute resource
RESTful
OpenFlow/OVSDB/NETCONF/BGP EVPN
Northbound ecosystem
Provides the standard Neutron/RESTful APIs for VPC orchestration to enable abstraction of fabric configuration.
Provides interoperability with OpenStack and Kubernetes.
Eastbound and westbound ecosystem
Provides compatibility with third-party computing management platforms and associates with computing resources to implement on-demand VM go-online and elastic scaling.
Southbound ecosystem
Provides standard device configuration APIs for service provisioning.
Interconnects with Huawei devices through plug-ins. Third parties can develop plug-ins for interconnection with iMaster NCE-Fabric.

## Slide 9
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 10: URL Format
URL: http(s)://IP:port/controller/product/version/interface type/{module name}
The value of each field in the URL (product, version, interface type, and module name) is case-sensitive.
Parameter | Description
http(s) | HTTP and HTTPS are supported, and HTTPS is recommended.
IP | Controller IP address
port | Port number. For example, in https://189.200.44.100:18002, 18002 is the port number.
controller | Fixed value
Product | Product name: dc
Version | API version: v2 and v3
Interface type | API type name: neutronapi, logicnetwork, multicast, and so on.
Module name | Service module of an API type, for example, network and subnet under the Neutron API.

## Slide 11: HTTP Request Mode/Header Parameters
HTTP request mode:
  GET: Obtain detailed information about specified resources. You can choose an Internet media type as needed (for example, XML and JSON). This document uses JSON.
  PUT: Update a specified element.
  POST: Treat URI as a resource group and create an element in it.
  DELETE: Delete a specified element.
Parameter format: application/json;charset=UTF-8
HTTP header: The following three parameters must be added to the header before APIs (except the authentication interface) are invoked.
  Content-Type: format of the data received by the entity header. Value: application/json
  Accept: type of data received by the request header. Value: application/json
  X-ACCESS-TOKEN: variable name of the token in the HTTP header. Value: token ID obtained through the authentication API.

## Slide 12: Service_name of the Neutron API
The northbound Neutron API of iMaster NCE-Fabric contains the service_name field. This field is a string containing 1 to 255 bytes. This field specifies the name of a cloud platform and helps iMaster NCE-Fabric identify the cloud platform from which services are delivered.
The service_name field is mandatory for the creation operation of all modules through the Neutron API.
  L2-L3: subnet, network, port, router, router interface
  L4-L7: all services
The following uses network as an example.
  {
  "service_name": "openstack11",
  "network":
  {
  "shared": "false",
  "name": "liudongtest",
  "admin_state_up": "true",
  "tenant_id": "6fbe9263116a4b68818cf1edce16bc4"
  }
  }

## Slide 13: Response Value
The status code 201 is returned if the POST operation succeeded.
The status code 204 is returned if the DELETE operation succeeded.
The status code 200 is returned if the GET operation succeeded.
The status code 200 is returned if the PUT operation succeeded.
The status code 208 is returned if the object ID already exists but the content differs during creation. The status code 201 is returned if the object content duplicates.
The status code 400 is returned if the object ID does not exist during updating.
The status code 404 is returned if the object ID does not exist during query.
The status code 204 is returned if the object ID does not exist during deletion.
The URL format is context_path/path. The status code 404 is returned if context_path or path does not exist.
Special Response Values
Normal Response Values

## Slide 14: Authentication API (1)
As the first API invoked by a third-party application system, the authentication API returns a token ID. Before invoking any other API, the third-party application system must set X-ACCESS-TOKEN in the HTTP header to a token ID. Otherwise, the system will display "403: Authentication failed." when another API is invoked. The token is effective in a certain time period, and needs to be acquired again from the authentication API when the validity period expires.
URL: https://{ip}:{port}/controller/v2/tokens
Method: POST
Request body
Parameter | Type | Mandatory | Description
userName | string | Yes | Name of a northbound API user. The northbound API user is added to iMaster NCE-Fabric using the admin account.
password | string | Yes | Password of a northbound API user. The northbound API user is added to iMaster NCE-Fabric using the admin account.

## Slide 15: Authentication API (2)
Response body
data structure
Parameter | Type | Mandatory | Description
errcode | string | Yes | Returned error code. The value 0 indicates a success. For others, see description of errmsg.
errmsg | string | Yes | Information contained in the returned error message.
data | data | Yes | Returned token information.
Parameter | Type | Mandatory | Description
expiredDate | date | Yes | Expiration time of the token. Format: 2016-01-13 19:52:40.
token_id | string | Yes | Token ID.

## Slide 16
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 17: Overview of iMaster NCE-Fabric Open API
Physical network
Public resource
Underlay configuration
Planning and Design
Service Provisioning (Key Point)
Maintenance and Monitoring
Neutron
VPC
Multicast VPC
SFC
Tenant
O&M

## Slide 18: Typical Basic Networking
SubnetA
SubnetA
SubnetA
SubnetA
SubnetB
SubnetB

## Slide 19
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 20: Mapping Between Neutron Service Modules
Firewall policy
Firewall rule
VPN
IKE policy
IPsec policy
Router
Security group
Firewall
Floating IP address
L2BR
SNAT
1:n
Project
Port
Static route
Subnet
QoS
Network
Security group rule
IPsec site connection
1:n
1:n
1:n
1:n
1:n
1:n
1:n
1:n
1:n
1:1
n:1
1:1
1:n
1:n
1:1
1:1
1:1
Notes: When iMaster NCE-Fabric is interconnected with a cloud platform, the cloud platform invokes northbound APIs to provision services. Project, router, firewall, and security group in the figure are all network models of the cloud platform.
Neutron APIs are encapsulated based on the OpenStack Neutron model and match the network service models in the industry. Neutron APIs are recommended if you are familiar with the OpenStack Neutron models.
Projects are created on the cloud platform without invoking the RESTful interface.
For details about OpenStack principles, see the OpenStack Foundation at https://www.openstack.org/ or learn Huawei HCIP-Cloud Computing-OpenStack at https://e.huawei.com/cn/talent/.

## Slide 21: Mapping Between Neutron Service Modules and RESTful APIs (1)
Service Module | Description | Access Path
Router | vRouters are used for interconnection between subnets and accessing external networks. | https://{ip}:{port}/controller/dc/v2/neutronapi/routers
Static route | A static route is manually configured by the administrator because it cannot automatically adapt to network topology changes. | https://{ip}:{port}/controller/dc/v2/neutronapi/routers/{router_id}/add_routes
Network | An isolated Layer 2 network domain. Hosts on one network are visible at Layer 2. A user can have multiple networks. Subnets and ports must be associated with networks which are the basis. VXLAN and VLAN are supported. | https://{ip}:{port}/controller/dc/v2/neutronapi/networks
Subnet | A subnet indicates a network segment. Each subnet has a CIDR value and is associated with a network. The IP address can be selected from the CIDR or a specified pool. A subnet may have a gateway, a group of DNSs, and host routes. Subnets are invisible at Layer 2 and communicate with each other through Layer 3 routing on a Layer 3 gateway (router). A network supports only one subnet. | https://{ip}:{port}/controller/dc/v2/neutronapi/subnets
Port | A port belongs to a network and indicates an access point which is used to connect to VMs or routers. The NICs of VMs are connected to the port and the VMs access the network using the port. If an IP address is bound to the port, the port belongs to a subnet. | https://{ip}:{port}/controller/dc/v2/neutronapi/ports
QoS | Quality of service. When a network is overloaded or congested, QoS ensures that important services can be processed in a timely manner and the network can run efficiently. Currently, QoS supports only rate limiting. | https://{ip}:{port}/controller/dc/v2/neutronapi/qoss
Security group | Trusted VMs communicate with each other through security groups on OpenStack. VMs in the same security group use the same security policies. A security group works on a VM port and is a port-level vFW. It filters incoming and outgoing port traffic. | https://{ip}:{port}/controller/dc/v2/neutronapi/security-groups
Security group rule | A policy for implementing traffic filtering. One security group can have multiple security group rules. | https://{ip}:{port}/controller/dc/v2/neutronapi/security-group-rules

## Slide 22: Mapping Between Neutron Service Modules and RESTful APIs (2)
Service Module | Description | Access Path
Firewall | A firewall contains a series of components deployed among multiple networks or security zones, and monitors, restricts, and modifies data flows passing through it to ensure network security. | https://{ip}:{port}/controller/dc/v2/neutronapi/fw/firewalls
Firewall policy | In the Neutron system, a firewall policy contains a group of rules arranged in a specific sequence. | https://{ip}:{port}/controller/dc/v2/neutronapi/fw/firewall_policies
Firewall rule | Firewall rules are used to determine whether to allow traffic to pass through. | https://{ip}:{port}/controller/dc/v2/neutronapi/fw/firewall_rules
Floating IP address | Floating IP addresses can be dynamically allocated to VMs and translated during communication between internal and external networks. | https://{ip}:{port}/controller/dc/v2/neutronapi/floatingips
IPsec site connection | Connection objects define the routing mode, key mode, authentication mode, and even the parameters and service subnets of the connected sites. IPsec tunnels are set up between gateways to provide a secure connection between LANs. | https://{ip}:{port}/controller/dc/v2/neutronapi/vpn/ipsec-site-connections
VPN | A virtual private network (VPN) is built on a public network for encrypted communication. The VPN gateway enables remote access through data encryption and address translation. | https://{ip}:{port}/controller/dc/v2/neutronapi/vpn/vpnservices
IKE policy | An IKE policy defines parameters for IKE negotiation used during the first phase. | https://{ip}:{port}/controller/dc/v2/neutronapi/vpn/ikepolicies
IPsec policy | An IPsec policy defines ESP negotiation parameters used during the second phase. | https://{ip}:{port}/controller/dc/v2/neutronapi/vpn/ipsecpolicies
Internal router interface | An internal router interface is connected to a router. This interface functions as the gateway of a subnet. | https://{ip}:{port}/controller/dc/v2/neutronapi/routerinterface/{router_id}/add_router_interface
SNAT | Source network address translation (SNAT) is used to translate the source address of an IP data packet to another address. | https://{ip}:{port}/controller/dc/v2/neutronapi/snat
L2BR | Layer 2 Bridge (L2BR) implements Layer 2 communication between VXLAN VMs and VLAN physical servers. | https://{ip}:{port}/controller/dc/v2/neutronapi/l2brs

## Slide 23: Configuration Process
Only the tenant network is created by invoking the API. Other steps can be performed on the cloud platform.
The process of creating a tenant network varies according to users’ service requirements.
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting
Start
Is an external network connected?
Create a project
Create a tenant network
End
Communication between an intranet and the Internet
Communication between an intranet and a private network
Communication between VMs across VPCs
Communication between VMs within a VPC
VM traffic limiting based on security groups
No
Yes
Create an external network

## Slide 24: Traffic Limiting of VMs Using Security Groups
Start
End
Create a network and its subnet
Create a security group
Create a security group rule
Create a port
1
2
3
Network management interface and subnet management interface
Configuration Process
Reference Interface and Description
Security group management interface
(Optional) Security group rule management interface
Mandatory
Optional
1
2
3
4
4
Port management interface, which is associated with a security group. Instances in the same security group can access each other on an intranet.
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting

## Slide 25: Intra-VPC Communication on an Intranet
Start
End
Create a router
Create a network and its subnet
Create a router interface and associate it with the subnet
Create a security group and configure a rule
Create an instance to connect VMs to the network
1
2
3
Router management interface
Configuration Process
Reference Interface and Description
Network management interface and subnet management interface
Router management interface
4
5
(Optional) Security group management interface
Port management interface, which is associated with a security group. Instances in the same security group can access each other on an intranet.
1
2
3
4
5
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting
Mandatory
Optional
Notes: A virtual private cloud (VPC) contains logical NEs abstracted from a physical network. These logical Nes are orchestrated based on service requirements to form a virtual network. Different VPCs are logically isolated but share the same physical network. In this way, physical network resources can be shared after being pooled.

## Slide 26: Inter-VPC Communication on an Intranet
1
2
3
Configuration Process
Reference Interface and Description
4
1
2
3
Router management interface
Network management interface and subnet management interface
Router management interface
4
5
(Optional) Security group management interface
Port management interface, which is associated with a security group. Instances in the same security group can access each other on an intranet.
6
7
(Optional) Firewall management interface
Static route management interface
Start
End
Create a router
Create a network and its subnet
Create a router interface and associate it with the subnet
Create a security group and configure a rule
Create an instance to connect VMs to the network
Create a firewall, select a firewall policy, and associate the firewall with a route
Configure the route between the corresponding firewalls of the two VPCs (vRouters)
5
6
7
Mandatory
Optional
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting

## Slide 27: Communication Between an Intranet and the Internet
1
2
3
Configuration Process
Reference Interface and Description
4
1
2
3
Router management interface
Network management interface and subnet management interface
Router management interface
4
5
(Optional) Security group management interface
Port management interface, which is associated with a security group. Instances in the same security group can access each other on an intranet.
6
7
SNAT interface
Firewall management interface
Start
End
Create a router
Create a network and its subnet
Create a router interface and associate it with the subnet
Create a security group and configure a rule
Create an instance to connect VMs to the network
Set the gateway and select an external network (Configure SNAT for intranet-to-Internet access)
Create a firewall, select a firewall policy,
and associate the firewall with a route
Bind floating IP addresses for Internet-to-intranet access
5
6
7
8
8
Floating IP address interface
Mandatory
Optional
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting

## Slide 28: Communication Between an Intranet and an External Private Network Through IPsec VPN
Start
End
Create a router
Create a network and its subnet
Create a router interface and associate it with the subnet
Create a security group and configure a rule
Create an instance to connect VMs to the network
Configure a gateway and select an external network
Create a firewall, select a firewall policy,
and associate the firewall with a route
Create a VPN
1
2
3
Configuration Process
Reference Interface and Description
4
1
2
3
Router management interface
Network management interface and subnet management interface
Router management interface
4
5
(Optional) Security group management interface
Port management interface, which is associated with a security group. Instances in the same security group can access each other on an intranet.
6
7
Distributed router management interface
Firewall management interface
8
(Optional) IPsec VPNaaS interface. This step is required only when VPN access is involved.
5
6
7
8
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process
VM Traffic Limiting
Mandatory
Optional

## Slide 29
Neutron APIs are encapsulated based on the OpenStack Neutron model and match network service models in the industry. Neutron APIs are recommended if you are familiar with the OpenStack Neutron model.
After receiving the request for calling Neutron APIs, iMaster NCE-Fabric invokes the corresponding VPC APIs based on the mapping between the Neutron service model and iMaster NCE-Fabric service model.
Learn the mapping between Neutron service modules and RESTful APIs.
Use Neutron APIs to orchestrate VPCs to implement the following typical service scenarios:
  Traffic limiting of VMs using security groups
  Intra-VPC communication on an intranet
  Inter-VPC communication on an intranet
  Communication between an intranet and the Internet
  Communication between an intranet and an external private network through IPsec VPN
Notes: For more API information, see "Secondary Development" in the iMaster NCE-Fabric Product Documentation.

## Slide 30
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 31: Mapping Between Main Service Modules of a VPC
1:n
Logical network
Logical router
Logical VAS
External network
connection
Logical port
Static route
Logical subnet
End port
Logical switch
1:n
1:1
1:n
1:n
1:n
1:n
1:n
1:n
The northbound open APIs for VPC services are encapsulated based on the iMaster NCE-Fabric service models. The content of the APIs is the same as that of the APIs invoked when performing operations on the iMaster NCE-Fabric GUI. Third parties can use the APIs based on the site requirements.
1:n
1:n
Subnet connected to an external network

## Slide 32: Mapping Between VPC Service Modules and the RESTful APIs
Service Module | Description | Access Path
Logical network | A logical network (VPC) provides isolated VMs and network environments to meet the network isolation requirements of different departments. Each VPC can provide independent vFWs, elastic IP addresses, security groups, super VLANs, IPsec VPNs, and NAT gateways. (Some functions can be provided by vFWs.) | https://{ip}:{port}/controller/dc/v3/logicnetwork/networks
Logical router | A logical router implements interworking between subnets and access to external networks. | https://{ip}:{port}/controller/dc/v3/logicnetwork/routers
Static route | A static route is manually configured by the administrator because it cannot automatically adapt to network topology changes. | https://{ip}:{port}/controller/dc/v3/logicnetwork/routers/router/{id}/route-sets
Logical switch | An isolated Layer 2 network domain. Hosts on one network are visible at Layer 2. A user can have multiple logical switches. Logical subnets and logical ports must be associated with logical switches. | https://{ip}:{port}/controller/dc/v3/logicnetwork/switchs
Logical subnet | A logical subnet indicates a network segment. Each subnet must have a CIDR and be associated with a network. Subnets are invisible at Layer 2 and communicate with each other through Layer 3 routes by passing through a Layer 3 gateway. One logical switch supports only one logical subnet. | https://{ip}:{port}/controller/dc/v3/logicnetwork/subnets
Logical port | A logical port belongs to a logical switch and is classified into User Network Interface (UNI) or Network to Network Interface (NNI). UNIs are used to connect user VMs/BMs to a VXLAN network. NNIs are used to connect VXLAN networks. | https://{ip}:{port}/controller/dc/v3/logicnetwork/ports
End port | An end port indicates a VM or BM on the user side and is associated with a logical port to access a VXLAN network. | https://{ip}:{port}/controller/dc/v3/logicnetwork/endports
Logical VAS | A unified abstracted logical unit of L4-L7 VASs, such as a firewall and an LB. Logical VASs need to be associated with logical routers and logical networks. | https://{ip}:{port}/controller/dc/v3/servicenetwork/vass
External network connection | A VPC can be associated with multiple external networks, which can be configured as a public external network and multiple private external networks. Different external networks connect to different service egresses. | https://{ip}:{port}/controller/dc/v3/servicenetwork/external-connects
Subnet connected to an external network | Specifies a logical subnet used to connect to an external network, that is, CIDR. | https://{ip}:{port}/controller/dc/v3/servicenetwork/external-connects/external-connect/{id}/action/add-cidrs

## Slide 33: Neutron/iMaster NCE-Fabric Service Models and Physical Model Mapping
Router
Network/Subnet
Port
Logical port
Logical router
Logical switch
External gateway
Logical VAS
End port
Border leaf
VRF
(DVR)
VRF
(DVR)
Leaf
Spine
VRF
(DVR)
BD
vsys1
Ext VRF
BD
Neutron service models
iMaster NCE-Fabric service models
Physical network models
VM/BM
VTEP
VM/BM
VTEP
Leaf
VTEP
BDIF
BDIF
Ext vsys
Firewall
External network
PE
Firewall
Notes: Border leaf (BL): A border leaf node is connected to an egress device.

## Slide 34: Intra-subnet Communication in a VPC
Start
End
Create a logical switch
Create a logical port
Create an end port
1
2
3
1
2
3
Logical switch management interface, which is used to create a large Layer 2 BD on a VXLAN.
Configuration Process
Reference Interface and Description
Logical port management interface. Multiple Layer 2 sub-interfaces can be created based on service scenarios.
End port management interface. End ports correspond to VMs/BMs. Multiple end ports can be created based on service scenarios and associated with their logical ports.
Communication with a Private Network
Communication with Internet
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process

## Slide 35: Inter-subnet Communication in a VPC
1
2
3
Logical network management interface used to create a VPC.
Configuration Process
Reference Interface and Description
Logical router management interface used to create a VRF.
Logical switch management interface and logical subnet management interface. Multiple logical switches and subnets can be created and logical ports can be created on logical switches.
1
2
3
Start
End
Create a logical network
Create a logical router
Create a logical switch
and a logical subnet
Create a logical port
Create an end port
4
5
4
5
Logical port management interface.
End port management interface.
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process

## Slide 36: Inter-VPC Communication on an Intranet
1
2
3
1
2
3
Logical network management interface. Create two VPCs or two VRFs under a VPC based on service requirements. VPC communication and intra-VPC VRF mutual access are supported.
Configuration Process
Reference Interface and Description
Logical router management interface used to create a VRF.
Logical switch management interface and logical subnet management interface.
4
4
5
Logical port management interface.
End port management interface.
Start
End
Create a logical network
Create a logical router
Creating a logical switch
and a logical subnet
Create a logical port
Create an end port
Create a logical firewall
Create a VPC communication instance
5
6
7
6
7
(Optional) Logical VAS management interface. Select Firewall, associate the logical VAS with the logical router, and create a logical firewall instance.
VPC communication instance management interface. You need to associate the VPC communication instance with the source and destination logical routers. You can also associate it with the source and destination logical firewalls.
Mandatory
Optional
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process

## Slide 37: Communication Between an Intranet and the Internet
1
2
3
Logical network management interface used to create a VPC.
Configuration Process
Reference Interface and Description
Logical router management interface used to create a VRF.
Logical switch management interface and logical subnet management interface.
4
5
Logical port management interface.
End port management interface.
6
7
(Optional) Logical VAS management interface. Select Firewall, associate the logical VAS with the logical network and the logical router, and create a logical firewall instance.
External network connection management interface and subnet interface. The external network connection is associated with the logical router, logical firewall, and Layer 3 shared egress gateway. SNAT is enabled when an intranet accesses the Internet.
Create an end port
Create a firewall
Create an external network connection and a subnet
Start
End
Create a logical network
Create a logical router
Create a logical switch
and a logical subnet
Create a logical port
1
2
3
4
5
6
7
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process

## Slide 38: Communication Between an Intranet and an External Private Network
1
2
3
Logical network management interface used to create a VPC.
Configuration Process
Reference Interface and Description
Logical router management interface used to create a VRF.
Logical switch management interface and logical subnet management interface.
4
5
Logical port management interface.
End port management interface.
6
Logical routing interface management interface, which is associated with the logical router and Layer shared egress gateway.
End
Create an end port
Create a logical routing interface
1
2
3
4
5
6
Start
Create a logical network
Create a logical router
Creating a logical switch
and a logical subnet
Create a logical port
Communication with Internet
Communication with a Private Network
Intra-VPC Communication
Inter-VPC Communication
Overall Configuration Process

## Slide 39
APIs for VPC services are encapsulated based on the iMaster NCE-Fabric service models. The content of the APIs is the same as that of the APIs invoked when performing operations on the iMaster NCE-Fabric GUI. Third parties can use the APIs based on the site requirements.
Learn mapping between Neutron service models, iMaster NCE-Fabric logical models, and physical models.
Learn mapping Between VPC Service Modules and the RESTful APIs.
Use VPC APIs for orchestration to implement the following service scenarios:
  Intra-subnet Communication in a VPC
  Inter-subnet Communication in a VPC
  Inter-VPC Communication on an Intranet
  Communication Between an Intranet and the Internet
  Communication Between an Intranet and an External Private Network

## Slide 40
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 41: Mapping Between Service Modules of a Multicast VPC (IPv4)
Logical router
Logical switch
MSDP
Layer 3 multicast service on a logical router
Multicast replication address of BUM packets
1:n
1:1
1:1
Use the Neutron API or VPC API to create a VPC instance, and then use a multicast VPC API to create a multicast overlay service.
The following scenarios are supported: both the multicast source and requester are inside a DC, the multicast source is inside a DC and the requester is outside the DC, the requester is inside a DC and the multicast source is outside the DC.
Layer 3 multicast service on a VBDIF
1:1
Multicast access
control list
1:n
1:n
Multicast service on a logical port
1:1
Logical port
1:n
1:n
1:n
VPC service module
Multicast service module

## Slide 42: Mapping Between VPC Service Modules and RESTful APIs
Service Module | Description | Access Path
Layer 3 multicast service on a logical router | The multicast capability is enabled on a logical router. The MVPN, internal RP, multicast group replication address, and SSM mapping are also configured. | https://{ip}:{port}/controller/dc/v3/multicast/logicrouter
Layer 3 multicast service on a logical port | PIM and IGMP protocols and policies are configured based on VBDIFs of logical switches, VBDIFs of external networks, and logical routing interfaces. | https://{ip}:{port}/controller/dc/v3/multicast/logicinterface
MSDP | MSDP is used by a border leaf node in a DC to establish an MSDP peer relationship with an external RP/CRP to synchronize SA information. | https://{ip}:{port}/controller/dc/v3/multicast/msdp
Multicast replication address of BUM packets | Multicast replication addresses of BUM packets are configured based on logical switches. Multicast replication reduces bandwidth usage between any two VTEPs based on ingress replication, optimizing traffic forwarding. | https://{ip}:{port}/controller/dc/v3/multicast/bum
Multicast service on a logical port | A multicast group filtering policy is configured based on logical ports. | https://{ip}:{port}/controller/dc/v3/multicast/logicport
Multicast ACL | An ACL is configured to control PIM-SM and IGMP policies. | https://{ip}:{port}/controller/dc/v3/multicast/template/acl

## Slide 43: Multicast VPC Service Scenario
1
2
3
Configuration Process
Reference Interface and Description
4
1
2
3
Use the Neutron API or VPC API to create a VPC and the corresponding network object instances. (Optional) Create an external network, and enable the multicast capability for the tenant and VPC to which the external network belongs.
(Optional) Multicast ACL management interface.
Layer 3 multicast service management interface of a logical router, which is associated with a logical router and configured with a multicast replication address and an internal RP address.
4
5
Layer 3 multicast service management interface of a logical port, which is associated with a logical switch and an external network.
(Optional) Multicast service management interface of a logical port, which is used to set a multicast group filtering policy.
6
7
Management interface for a BUM multicast replication address, which is associated with a logical switch. Either this interface or the interface created in step 4 can be selected.
(Optional) MSDP management interface, which is used by the border leaf node to establish an MSDP peer relationship with the external RP/CRP.
Start
End
Create a logical network
Create a multicast
ACL
Create a Layer 3 multicast service on a logical router
Create a Layer 3 multicast service on a logical port
Create a multicast service on the logical port
Create a BUM multicast replication address
Create MSDP
5
6
7
Mandatory
Optional

## Slide 44
Layer 3 IPv4 multicast is supported in the distributed gateway scenario.
The following scenarios are supported: both the multicast source and requester are inside a DC, the multicast source is inside a DC and the requester is outside the DC, the requester is inside a DC and the multicast source is outside the DC.
The mapping between multicast VPC service modules and RESTful APIs is listed.
In the scenario where a multicast VPC is used to orchestrate multicast services, the Neutron API or VPC API needs to be used to create a VPC and the corresponding network object instances. The multicast capability needs to be enabled for the tenant and VPC of the network object instances.

## Slide 45
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 46: Mapping Between Main Service Modules in an SFC
Use the Neutron API or VPC API to create a VPC instance, and then use the SFC API to create an SFC service.
Destination EPG
SFC policy
1:1
SFC application instance
SFC profile
1:1
1:1
Source EPG
1:1
Notes: Service Function Chain (SFC)

## Slide 47: Mapping Between SFC Modules and RESTful APIs
Service Module | Description | Access Path
SFC profile | An SFC profile defines the service functions (SFs) through which packets pass between the SFC ingress (source EPG) and SFC egress (destination EPG) and their sequences. In addition, the SFC profile can be reused. | https://{ip}:{port}/controller/dc/v3/sfco/sfcs
SFC policy | A policy is used to ensure that only the EPG traffic that meets the requirements enters an SFC. The policy template can be reused for creating a policy. | https://{ip}:{port}/controller/dc/v3/sfco/contracts
EPG | An End Point Group (EPG) is a group of devices with the same characteristics. When creating an SFC, you can configure EPGs to determine the start point and end point for the SFC. | https://{ip}:{port}/controller/dc/v3/sfco/epgs
SFC application instance | An SFC application instance is defined based on the service access path. An SFC consists of the source EPG, SFs, and destination EPG. The source EPG is the ingress of an SFC, while the destination EPG is the egress. The service data to be processed enters the service function path (SFP) from the source EPG, and the processing result is obtained from the destination EPG. | https://{ip}:{port}/controller/dc/v3/sfco/scapps

## Slide 48: SFC Scenario
1
2
3
Configuration Process
Reference Interface and Description
4
1
2
3
Use the Neutron API or VPC API to create a VPC and the corresponding network object instances.
SFC profile management interfaces.
(Optional) SFC policy management interfaces.
4
5
EPG management interfaces.
SFC application instance management interface, which is associated with an SFC profile, source EPG, and destination EPG.
Start
End
Create a logical network instance
Create an SFC profile
Create an SFC policy template
Create a source EPG and a destination EPG
Create an SFC application instance
Mandatory
Optional
5

## Slide 49
Microsegmentations and SFCs use the same service model. The API orchestration logic used for creating a microsegmentation is the same as that used for creating an SFC.
Learn the mapping between SFC service modules and RESTful APIs.
In the scenario where an SFC API is used to orchestrate an SFC and a microsegmentation, you need to use a Neutron API or VPC API to create a VPC and the corresponding network object instances.

## Slide 50
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
  Northbound Open Neutron APIs
  Northbound Open APIs for VPC Services
  Northbound Open APIs for Multicast VPC Services
  Northbound Open APIs for SFCs
  Other Open APIs
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 51: Mapping Between Other Service Modules and RESTful APIs
Interface Type | Service Module | Description | Access Path
Underlay configuration | M-LAG | Configure the trunk module, status, and trunk member interfaces. | https://{ip}:{port}/sdn/acdcn/v3/underlay/ethTrunk-configure/......
 | Batch configuration | Deliver configurations to multiple devices in batches. | https://{ip}:{port} /controller/dc/v3/underlay/commands/execute
 | ZTP | Automatically deploy underlay functions. | https://{ip}:{port}/sdn/acdcn/v3/underlay/ztp/......
Physical network | Physical topology | Query the device list, host link list, host list, device link list, port list, resource pool topology, and DCN network topology. | https://{ip}:{port}/acdcn/v3/topoapi/dcntopo/......
 | Fabric resource pool | Manage fabric resource pools. | https://{ip}:{port}/controller/dc/v3/physicalnetwork/fabricresource/……
Public resource | External gateway | An external gateway is used for communication between VMs/BMs in a DC and the external network. | https://{ip}:{port}/controller/dc/v3/publicservice/external-gateways
Tenant | Tenant | Network administrators need to create a tenant and allocate network resources to the tenant so that the tenant can log in to the system using the associated account to view the network resource usage and adjust the existing services. | https://{ip}:{port}/controller/dc/v3/tenants
O&M | Connectivity test | MAC ping is used to check whether the ARP detection system is normal. IP ping is used to check the network reachability between a VM, BM, container, or device and the destination IP address is normal. | https://{ip}:{port}/controller/dc/v3/oam/ping
 | Path detection | Single-path detection: Check the actual physical path of a specific service flow between VMs, BMs, or devices. Multi-path detection: Check actual physical paths between two NVE devices. | https://{ip}:{port}/controller/dc/v3/oam/trace/......
 | Emergency plan | Atomic template: An atomic template supports operations on only one type of objects. Integration template: An integration template can be integrated with a maximum of 10 atomic templates of different types which are executed in sequence. | https://{ip}:{port}/controller/dc/v3/oam/emergency-plan/......

## Slide 52
iMaster NCE-Fabric Overview
General Restrictions and Specifications of iMaster NCE-Fabric Open APIs
iMaster NCE-Fabric Open APIs and Application Scenarios
Example of Invoking Neutron APIs for Intra-VPC Communication

## Slide 53: Example
In this example, the Neutron API of iMaster NCE-Fabric is invoked to implement access between intranets of a router.
iMaster NCE-Fabric
Tenant
Port
Port
Network/Subnet
Port
1:N
Network/Subnet
Network/Subnet
Router
Router
1:N

## Slide 54: Creating a Router
https://ip:18002/controller/dc/v2/neutronapi/routers
Url
Method
post
RequestBody
{
"router": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"admin_state_up": "true",
"name": "router_yao",
"id": "f9943c4c-a1c9-58b4-1fac-110000000004",
"status": "ACTIVE"
},
"service_name": "FusionSphere"
}
Cloud platform name
Virtual router ID, which is specified and delivered by the cloud platform
Tenant ID, which is specified and delivered by the cloud platform

## Slide 55: Creating Intranet 1
https://ip:18002/controller/dc/v2/neutronapi/networks
Url
Method
post
RequestBody
{
"service_name": "FusionSphere",
"network": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"shared": "false",
"provider:physical_network": "physnet1",
"provider:segmentation_id": 2009,
"provider:network_type": “vlan" ,
"router:external": "false",
"admin_state_up": "true",
"name": "net_yao",
"id": "f9943c4c-a1c9-58b4-1fac-110000000009",
"status": "ACTIVE"
}
}
Network ID, which is specified and delivered by the cloud platform.
Whether the network is an external network. In this scenario, the value must be false.

## Slide 56: Creating a Subnet for Intranet 1
https://ip:18002/controller/dc/v2/neutronapi/subnets
Url
Method
post
RequestBody
{
"subnet": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"enable_dhcp": "false",
"allocation_pools": [
{
"start": "172.172.1.2",
"end": "172.172.1.254"
}
],
"network_id": "f9943c4c-a1c9-58b4-1fac-110000000009",
"ip_version": 4,
"name": "sub_yao",
"cidr": "172.172.1.0/24",
"gateway_ip": "172.172.1.1",
"id": "f9943c4c-a1c9-58b4-1fac-110000000010"
},
"service_name": "FusionSphere"
}
Network ID. The value is the ID of intranet 1.
Subnet ID, which is specified and delivered by the cloud platform.
Available IP address pool of the subnet

## Slide 57: Creating a Port for Intranet 1
https://ip:18002/controller/dc/v2/neutronapi/ports
Url
Method
post
RequestBody
{
"port": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"mac_address": "fa:16:3e:9e:ff:55",
"id": "f9943c4c-a1c9-58b4-1fac-110000000011",
"device_id": "f9943c4c-a1c9-58b4-1fac-110000000004",
"device_owner": "network:router_interface",
"network_id": "f9943c4c-a1c9-58b4-1fac-110000000009",
"fixed_ips": [
{
"subnet_id": "f9943c4c-a1c9-58b4-1fac-110000000010",
"ip_address": " 172.172.1.1 "
}
],
"name": ""
},
"service_name": "FusionSphere"
}
Network ID. The value is the ID of intranet 1.
Port ID, which is specified and delivered by the cloud platform.
Subnet ID. The value is the subnet ID of intranet 1.
ID of the logical router. The value must be the same as that created previously.

## Slide 58: Creating Intranet 2
https://ip:18002/controller/dc/v2/neutronapi/networks
Url
Method
post
RequestBody
{
"service_name": "FusionSphere",
"network": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"shared": "false",
"provider:physical_network": "physnet1",
"provider:segmentation_id": 2010,
"provider:network_type": “vlan" ,
"router:external": "false",
"admin_state_up": "true",
"name": "net_yao",
"id": "f9943c4c-a1c9-58b4-1fac-110000000012",
"status": "ACTIVE"
}
}
Network ID, which is specified and delivered by the cloud platform.
Whether the network is an external network. In this scenario, the value must be false.

## Slide 59: Creating a Subnet for Intranet 2
https://ip:18002/controller/dc/v2/neutronapi/subnets
Url
Method
post
RequestBody
{
"subnet": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"enable_dhcp": "false",
"allocation_pools": [
{
"start": "172.172.2.2",
"end": "172.172.2.254"
}
],
"network_id": "f9943c4c-a1c9-58b4-1fac-110000000011",
"ip_version": 4,
"name": "sub_yao",
"cidr": "172.172.2.0/24",
"gateway_ip": "172.172.2.1",
"id": "f9943c4c-a1c9-58b4-1fac-110000000012"
},
"service_name": "FusionSphere"
}
Network ID. The value is the ID of intranet 2.
Subnet ID, which is specified and delivered by the cloud platform.
Available IP address pool of the subnet

## Slide 60: Creating a Port for Intranet 2
https://ip:18002/controller/dc/v2/neutronapi/ports
Url
Method
post
RequestBody
{
"port": {
"tenant_id": "f9943c4c-a1c9-58b4-1fac-110000000005",
"mac_address": "fa:16:3e:9e:ff:55",
"id": "f9943c4c-a1c9-58b4-1fac-110000000013",
"device_id": "f9943c4c-a1c9-58b4-1fac-110000000004",
"device_owner": "network:router_interface",
"network_id": "f9943c4c-a1c9-58b4-1fac-110000000011",
"fixed_ips": [
{
"subnet_id": "f9943c4c-a1c9-58b4-1fac-110000000012",
“ip_address”: “172.172.2.1"
}
],
"name": ""
},
"service_name": "FusionSphere"
}
Network ID. The value is the ID of intranet 2.
Subnet ID. The value is the subnet ID of intranet 2.
Port ID, which is specified and delivered by the cloud platform.
ID of the logical router. The value must be the same as that created previously.

## Slide 61
This example demonstrates how to invoke the Neutron API to implement inter-network segment access within a VPC.
Before demonstrating this example, ensure that the fabric network and tenant have been created.
When designing the API invoking process in actual projects, you can refer to the configuration process and specific API specifications in the typical service scenarios listed in Part 3.

## Slide 62
How do I configure microsegmentation using the SFC API?
Notes:   Microsegmentations and SFCs use the same service model. The API orchestration logic used for creating a microsegmentation is the same as that used for creating an SFC. In the scenario where an SFC API is used to orchestrate an SFC and a microsegmentation, you need to use a Neutron API or VPC API to create a VPC and the corresponding network object instances, such as a logical router, logical switch, and logical port.

## Slide 63
Huawei enterprise service website - Data Center Network Solution
  https://e.huawei.com/en/solutions/business-needs/enterprise-network/data-center-network
Section "Secondary Development" in the iMaster NCE-Fabric Product Documentation
  https://support.huawei.com/enterprise/en/network-management-and-analysis-software/imaster-nce-fabric-pid-250938411/doc