## Slide 1
Wangchangli/wx408647
2020.5.28
You Yanyan/00334121
New/Update
You Yanyan/00334121
2020.3.28
Ji Lei/00348665
New/Update

## Slide 2: NCE Service Openness and Programmability

## Slide 3
As digital network transformation moves forward, new services and technologies are burgeoning, and network requirements become more complex. Traditional closed networks cannot meet the requirements for rapid service innovation. It is an inevitable trend to improve network openness using existing assets. More agile planning of new services and network service orchestration based on customized customer intents are core capabilities.
NCE service openness and programmability are based on the open architecture driven by the YANG model. Huawei enables openness and programmability at the NE and network layers in the form of Specific NE Driver (SND) and Specific Service Plugin (SSP) packages, implementing quick interconnection between new devices and fast rollout of new network services.
This course introduces the background of service openness and programmability and Huawei's practices.

## Slide 4
On completion of this course, you will be able to:
  Describe the basic concepts of Huawei NCE service openness and programmability.
  Describe the open and programmable architecture and working principles of NCE services.
  Describe the application scenarios of NCE service openness and programmability.
  Use the iMaster NCE open programmability system (OPS) to interconnect new devices and roll out new services.

## Slide 5
Background
Introduction to NCE Service Openness and Programmability
Key Capabilities
Related Concepts
Practice Cases

## Slide 6: Network O&M Adjustment in the 5G/Cloud Era
Driven by service innovation
Driven by network transformation
Driven by customization requirements
Notes: First, let's take carriers as an example. Globally, most carriers face the problems of revenue decrease and OPEX increase. Moreover, as OTT providers continue to preempt market shares, more and more carriers take OTT providers as their competitors. These factors drive carriers to transform their networks. In this case, carriers are faced with the following problems: how to implement multi-network convergence, multi-vendor collaboration, and fast and efficient management of converged networks.
In the 5G era, everyone predicts that 5G will lead to new businesses and services. However, carriers raise requirements for the rollout of new services, and device vendors implement the requirements. The rollout period is half a year or several years. It takes only a few months for OTT providers to launch new services, which makes it impossible for carriers and OTT providers to compete equally. There are many reasons for slow service rollout. One of the reasons is that there is a gap between carriers and vendors. That is, carriers do not understand devices, and vendors do not understand carrier services. It is an urgent issue to eliminate the impact of this gap and enable carriers and vendors to play their roles in the fields they are familiar with and quickly provision new services.
Finally, the products provided by vendors are universal, that is, they are applicable to most operators. Carriers want systems to match their service requirements and enterprise cultures. Therefore, they have customization requirements. For example, a carrier writes the customization capability into its bidding document or customizes enterprise specifications. From the perspective of vendors, customization requirements of customers generate high costs. Therefore, the best solution is to provide the customization capability and let customers complete customization by themselves.

## Slide 7
Notes: For other enterprises, they also face the same problem in the cloud era. Cloudification is a trend. Infrastructures need to be managed by the cloud platform in a unified manner. In addition, frequent service changes in the cloud data center have high requirements on automation. These requirements require a more open network.

## Slide 8: Evolution from CLI to Full Automation
Traditional device adaptation mode
Centralized management is implemented, and network automation objects are changed from one-to-many to one-to-one.
Application programming interfaces (APIs) on the control plane are used to indirectly control network devices, laying a foundation for network automation.
A set of industry-standard models are built to describe managed devices, and network configurations are automated with the APIs generated based on these models.
Model-based APIs are used to quickly manage and detect networkwide devices and automatically deliver services.
Model-based APIs are used to perform self-programming and build a tool chain, realizing intent-driven networks.
The command line interface (CLI) script is generated based on the template mechanism. The device runs the CLI script through the network management protocol for device configurations.
The script scale is increasing, maintainability is continuously degraded, and the time required for new mapping is also increasing.
Model-based APIs make device adaptation easier.
Traditional network automation, unsuitable command lines
CX600
NE40E
Third-party device
Separation of control and forwarding planes, triggering network automation
SDN architecture
Network programmability, achieving full automation
Notes: On traditional networks, network automation refers to the process of generating command line scripts based on the template mechanism and enabling devices to run the received command line scripts through the network management protocol. It does not change the way it interacts with network devices. During device adaptation, network management engineers use Python or Perl to compile a specific function with a narrow application scope to implement a series of automatic operations, or use automation tools such as Ansible and Puppet to implement more complex automation tasks. Network management engineers need to adapt to network devices to be supported one by one, regardless of whether they write scripts or use automation tools. As the script scale becomes larger and larger, script maintainability decreases continuously, and the time required for adding a new version increases accordingly. With the advent of the Internet of Everything (IoE) era, the time to market (TTM) of new services has become a core indicator for enterprises to survive.
With the great success of the commercialization of cloud computing, the concept of software-defined networking (SDN, sometimes referred to as “software-driven network”), which was popular only in the academic circle, has begun to flourish. On an SDN network, the separation between the control and forwarding planes is highly recommended. In an ideal SDN network, a centralized controller becomes an indispensable basis. As the brain of the entire network, it collects information about the network topology, calculates an optimal path globally based on service requirements, and notifies devices along the path. When receiving a service packet, these devices forward the packet according to a path determined by the centralized controller.

## Slide 9
Notes: In this case, enterprises can directly control the forwarding plane of network devices through the application programming interface (API) exposed on the control plane, which paves the way for modern network automation.
On a modern network with forwarding-control decoupling, the separation of the forwarding and control planes and centralization of the control plane change the network automation object from "one-to-many" to "one-to-one". Network engineers no longer need to worry about device adaptation. With PCEP (RFC 5440), FORCES (RFC 5810), BGP-LS (RFC 7752), and NETCONF/YANG (RFC 6241/RFC 7950) contributed by the open source community, software vendors can build a set of industry-standard models to describe managed objects, and the APIs generated based on these models are called by automation scripts or network configuration applications.
The benefits of using model-based APIs are significant. Because each model is decoupled from protocols and encoding rules, one model can adapt to multiple protocols and encoding rules. This provides a solution to uniformly adapt to network devices that support different network management protocols. Thanks to a unified device adaptation solution, we have a new direction to do things that we could not do before.
  (1) Using model-based APIs, enterprises can quickly implement telemetry of devices on the entire network and automatically collect device-level and service-level network running data, helping network O&M engineers learn about the network running status promptly.
  (2) Model-based APIs can also help enterprises build a tool chain to implement user intent identification, automatic service provisioning, automatic network-wide telemetry, and automatic network adjustment and optimization based on data analysis, thereby implementing intent-driven networks.

## Slide 10: Huawei's NCE Service Openness and Programmability Practice
iMaster NCE (NCE for short) is an innovative network cloudification engine of Huawei. The overall openness and programmability of NCE include automation, analytics, and intent. The goal is to build an open programmable architecture throughout the lifecycle to satisfy customers' requirements for openness and programmability.
Huawei open programmability system (OPS), a closed-loop component of the automation engine, are crucial to the entire open programming system of iMaster NCE.
Overall Openness and Programmability of NCE (Open API)
Intent
Automation
Analytics
Intent engine
Automation engine
Analytics engine
Design
Conversion
Awareness
Analysis
Decision
Administration unit
Control unit
OPS
Verification
Notes: iMaster NCE is an innovative network cloudification engine developed by Huawei. Positioned as the brain of future cloud-based networks, NCE integrates functions such as network management, service control, and network analysis. It is the core enablement system for network resource pooling, network connection automation, and O&M automation. NCE aims to build an intent-driven network (IDN) that is first automated, then self-adapting, and finally autonomous.
The overall openness and programmability of NCE include automation, analytics, and intent. The goal is to build a full-lifecycle open and programmable architecture to satisfy customer needs. The OPS, as a part of the automation engine, are crucial for the entire open programming system of NCE to form a closed loop. Equivalent to the limbs of the human body, the OPS is an executor, which needs to be flexible to support the automatic closed-loop capability driven by the brain of an intent-driven network.

## Slide 11
Background
Introduction to NCE Service Openness and Programmability
Key Capabilities
Related Concepts
Practice Cases

## Slide 12: Introduction (1)
Similar to the operating system on a computer, NCE service openness and programmability are crucial to networks.
Know devices.
Understand device capabilities.
Manage device status and configurations.
Provide functions such as device grouping and device configuration synchronization.
Build new network services based on service requirements.
View NE-level configurations decomposed based on services.
Provide other functions such as rollback upon a transaction failure.
Device management
Device driver
Service management
NCE service openness and programmability
Hardware management
Program management
Operating system
Mouse
Keyboard
Other hardware
CX600
NE40E
Third-party device
Driver
Notes: The open architectures of different industries are similar. Similar to the operating system on a computer, NCE service openness and programmability are crucial to networks.
To connect the operating system to managed hardware, such as the mouse and keyboard, you need to install corresponding drivers. The drivers enable the operating system to recognize the hardware. NCE service openness and programmability have similar functions. The difference is that switches and routers are managed in the datacom industry. First, we need to understand and manage these switches and routers. That is, load device drivers first, and then add and understand the specific capabilities of the devices.
At the upper layer, the operating system implements hardware management, specifically, managing the status of the mouse and keyboard. NCE service openness and programmability implement device management, such as managing device status and configurations.
At the top layer, the operating system provides program management to manage various applications, such as Word and Excel. Note that the mouse and keyboard capabilities are required for using these programs. NCE service openness and programmability implement service management at the top layer, that is, building network service capabilities based on application scenarios. In addition, NCE provides capabilities such as rollback up on a transaction failure and automatic detection of device configuration changes to improve O&M.

## Slide 13: Introduction (2)
NCE service openness and programmability are implemented based on two key software packages: Specific NE Driver (SND) and Specific Service Plugin (SSP). By compiling and loading two driver packages, you can quickly interconnect new devices and build new services.
Know devices.
Understand device capabilities.
Manage device status and configurations.
Provide functions such as device grouping and device configuration synchronization.
Build new network services based on service requirements.
View NE-level configurations decomposed based on services.
Provide other functions such as rollback upon a transaction failure.
Device management
Device driver
Service management
iMaster NCE
Compile the SSP package.
Compile the SND package.
Load
Load
2
1
4
3
IDE
IDE
Notes: NCE service openness and programmability depend on two software packages: SND and SSP.
  Specific NE Driver (SND): provides a data model for the iMaster NCE OPS to interact with NEs.
  Specific Service Plugin (SSP): defines a data model for completing network service configuration.
Engineers compile SND packages and load them to iMaster NCE to quickly interconnect with new devices. Then, engineers compile SSP packages and load them to iMaster NCE to quickly construct new services.

## Slide 14: Architecture
NETCONF
STelnet
Project management
SSP
Service YANG model
Python
Mapping
Huawei SND...
3rd-party SND...
NE YANG model
NE YANG model
Transaction mechanism
Easymap
DataStore
Python
Framework
Web UI
RESTCONF
CLI
Provided by NCE
Provided by customers
Framework and mechanism
Open programming
Provided by Huawei
Open device and service programmability
Open device capabilities: Device capability openness is enabled by loading the YANG model of an NE.
Open service definition capabilities: Service capability openness is enabled by customizing and loading service YANG models and service logic.
Open northbound capabilities: The system automatically generates northbound RESTCONF interfaces based on the YANG model to quickly interconnect with northbound man-machine and machine-machine interfaces.
Application scenarios
3
3
2
1
Supports cross-vendor device management and quick interconnection with third-party devices.
Quickly constructs services and automatically generates northbound interfaces.
Supports NETCONF- and STelnet-based device interconnection in the southbound direction.
iMaster NCE
Notes: NE YANG model: YANG files generated by abstracting atomic capabilities (such as creating sub-interfaces) at the device layer. They are provided by device vendors.
Service YANG model: YANG files generated by abstracting service models can be used to generate northbound interfaces and configuration GUIs.
Easymap: a mapping logic algorithm that decomposes network-layer services into NE-layer services.

## Slide 15: Principles
NCE service openness and programmability consist of the design state and running state. The design state is used to design and develop service logic. The running state automatically generates service and device management GUIs and northbound interfaces based on the model defined in the design state. Users can configure devices and deliver services through the GUIs and northbound interfaces.
Service YANG model
NE YANG model
NE YANG model
Huawei Jinja2
3rd Jinja2
Huawei SND
3rd SND
Protocol Stack
NETCONF
STelnet
Mapping
Service management
Device management
API gateway
Automatic UI generation
CRUD
Dry run/Preview
Deliver configuration/Reset
NE management
Synchronization
Reconciliation
Comparison
CRUD
Dry run/Preview
Deliver configuration/Reset
Web UI
Service management
Device management
GET
POST
PUT
DELETE
NBI
User management
Transaction mechanism
Phase 2
Globalization
NCE portal
...
Common Foundation
Inconsistency discovery
Design state
Running state
Operated by users
Provided by Huawei or a third party
Base
Programmed by the user
Notes: The design state is used to establish the mapping between the service YANG model and NE YANG model. The system provides the mapping logic algorithm to decompose network-layer services into NE-layer services. Currently, the NCE service openness and programmability framework supports two layers of mapping logic: 1. Mapping from the service model to the device model, which is processed by the SSP package. 2. Mapping from the device model to protocol packets, which is processed by the SND package.
The running state uses the mappings established in the design state to manage devices and provision services. Specifically:
  Service management automatically generates a service management GUI based on the service YANG model to add, delete, modify, and query services.
  Device management automatically generates an NE management GUI based on the NE YANG model to add, delete, modify, and query NE resources, achieving functions such as difference comparison, data synchronization, and configuration reconciliation.
  API gateway automatically generates northbound RESTCONF interfaces based on the service and device YANG models and works with the mapping between the two models to add, delete, modify, and query services and NE resources.
The running state provides the dryRun function to help users preview the results of the current operation and the modification of related device configurations.
Jinja2 is a Python template engine. NCE service openness and programmability use Jinja2 to quickly complete the template-based processing of SSP packages.

## Slide 16: Development Process
SSP development
SND development
(On-demand)
New device driver development
Southbound template development
Mapping code
Debugging and verification
Enter the production environment.
Modification and adjustment
Service YANG definition
Incremental design
The customer provides and verifies the service package. (One month)
Provided by Huawei
Customer analysis
The customer analyzes requirements based on service scenarios.
The customer performs HLD and outputs the configurations to be delivered and the involved device types.
Develop the SND package based on the configurations to be delivered and the involved device types.
Develop the southbound Jinja2 template based on the driver package.
Define the service YANG model based on service scenarios.
Develop service code and logic code based on service scenarios.
Perform testing and verification in a lab environment.
After verification is completed, enter the production environment.
Requirement analysis
HLD
The overall development process is led by the customer, including requirement analysis and design, SND package development, SSP package development, and commissioning and verification.
Notes: The development process of NCE service openness and programmability is as follows:
  First, analyze requirements based on service scenarios and output the high level design (HLD). In this phase, analyze the configuration commands to be delivered and the involved device types, and then start the development of a Specific NE Driver (SND) package. The SND package is developed as required. If the SND package of a device exists and the SND package to be delivered is supported, you do not need to develop the SND package again.
  Then, develop a Specific Service Plugin (SSP) package. Step 1: Develop the southbound Jinja2 template. The southbound Jinja2 template can be considered as the tailoring of the open interfaces of the device. There are many open capabilities of devices. However, we only need to use some of them. Therefore, find and select the required ones. Step 2: Define the service YANG model and determine northbound input parameters. Step 3: Develop the service logic. This step is optional. If the service layer can directly map and use the southbound template, skip this step.
  Finally, perform commissioning and verification. After the commissioning and verification are completed, the use in the production environment is formally started. If there are incremental requirements, follow the incremental design process and perform incremental development with reference to the preceding steps.

## Slide 17
Background
Introduction to NCE Service Openness and Programmability
Key Capabilities
Related Concepts
Practice Cases

## Slide 18: Overview of Key Capabilities
Key Capabilities
Device capability openness
Service capability openness
Shielding of device differences for services
Multi-protocol interconnection
Batch configuration
Transaction mechanism
Service conflict detection
Security audit

## Slide 19: Device Capability Openness
Open atomic capabilities of devices. Driven by the device YANG model, the iMaster NCE OPS automatically generates northbound interfaces and configuration GUIs to quickly manage Huawei and third-party devices. It supports device data consistency comparison, configuration reconciliation, and configuration synchronization.
NCE service openness and programmability
Bearer mode during running
Quickly manage Huawei and third-party devices.
Open device configuration capabilities.
Device management
SND
YANG

## Slide 20: Service Capability Openness
Open service configuration mapping capabilities. Driven by the service YANG model, the iMaster NCE OPS automatically generates northbound and southbound interfaces to quickly build new services. The Easymap algorithm in the mechanism is used. Users only need to write the creation process. The update and deletion processes are calculated by the algorithm, thereby simplifying programming and reducing development difficulties.
NCE service openness and programmability
Bearer mode during running
SSP
Open service configuration mapping capabilities.
Automatically generate southbound and northbound interfaces based on the service YANG model.
Write only the mapping creation process. This simplifies programming and reduces development difficulties.
Easymap
YANG
Notes: Easymap: a mapping logic algorithm that decomposes network-layer services into NE-layer services. Currently, the NCE service openness and programmability framework supports two layers of mapping logic: 1. Mapping from the service model to the device model, which is processed by the SSP package. 2. Mapping from the device model to protocol packets, which is processed by the SND package.

## Slide 21: Multi-Protocol Interconnection
Support NETCONF- and STelnet-based device interconnection in the southbound direction. New devices can be interconnected using NETCONF, and existing devices can be interconnected using commands.
NCE service openness and programmability
NETCONF
CLI driver
YANG driver
STelnet
New devices can be interconnected using NETCONF.
Existing devices can be interconnected using commands.
Notes: The SND package of the CLI driver is also a YANG file.

## Slide 22: Shielding of Differences Between Underlying Devices at the Service Layer
Only specific services need to be focused on at the service layer. Devices of different vendors and using different protocols do not need to be interconnected separately. The OPS supports service interconnection between the devices of different vendors and using different protocols.
NCE service openness and programmability
Bearer mode during running
SSP
Support service interconnection between the devices of different vendors and using different protocols.
STelnet/NETCONF
YANG
Service
Easymap
YANG driver

## Slide 23: Batch Configuration
Provide batch configuration capabilities. Devices with the same configuration can be grouped. A template is preset in the system first, and then configurations are delivered in batches.
Templates are applied in batches by device group to improve efficiency.
NCE service openness and programmability
Task management
Support device grouping.
Preset templates, which are delivered in batches by device group.
Deliver asynchronous tasks in batches.
Easymap
Preset template

## Slide 24: Transaction Mechanism
Provide a transaction mechanism to ensure data consistency between the device and controller in both success and failure scenarios. The dryRun function enables the customer to check the correctness of configurations before delivery. The configurations can be repeatedly modified, and then the dryRun function is implemented until the configurations are correct. Then, the Commit operation can be started to commit the configurations to the device.
NCE service openness and programmability
dryRun
The transaction mechanism ensures data consistency between the device and controller.
Perform dryRun to check the correctness of configurations before delivery.
Perform the Commit operation to commit the configurations to the device. If the Commit operation fails, a rollback based on the transaction occurs automatically.
Database
Commit
Rollback

## Slide 25: Service Conflict Detection
Provide service conflict detection capabilities. The OPS supports source tracing of configured data sources. Configuration conflicts between different services can be detected before delivery. If the configurations of a device are modified by a third party, the device can automatically detect the modifications and re-deploy the configurations to restore the services interrupted by the modifications by the third party.
Implement in-depth difference discovery. The controller directly compares the NE-level data decomposed by services with device data to check data consistency.
Perform data source tracing and conflict detection.
Support service and device data consistency check.
Automatically detect device configuration modifications by a third party and restore services.
Configuration conflict
Configuration consistency check
SSP1
SSP2
In-depth difference discovery
diff

## Slide 26: Security Audit
Provide security audit capabilities. Historical configuration points can be recorded and rolled back, and service association configurations can be visualized.
NCE service openness and programmability
Record and roll back historical configuration points.
Support visualization of service association configurations.
Configuration data
Commit history
Commit 1
Commit 2
Commit 3
Rollback
Rollback
Rollback
diff

## Slide 27
Background
Introduction to NCE Service Openness and Programmability
Key Capabilities
Related Concepts
Practice Cases

## Slide 28: Function Package
Specific NE Driver (SND)
Specific Service Plugin (SSP)
A type of software package that provides a data model for interaction between the OPS and NEs.
The data model usually contains a .py file and a data model (YANG) of several features. Specifically:
The former is used to define information related to an NE, such as device type, vendor, and connection information.
The latter describes the data structure of NE-related features.
A type of software package that defines a data model for completing network-level service configurations.
The data model usually contains a Jinja2 template file, a Python mapping script, and a service YANG model. Specifically:
The Jinja2 template describes the data structure of services and uses the Jinja2 syntax to perform operations such as interpolation, condition judgment, and recursion.
The Python mapping script describes how to fill the data submitted by users into the template and map the data to the NE data structure.
The service YANG model describes service parameters and is constructed based on service input.

## Slide 29: Package Mapping Mechanism
Specific Service Plugin (SSP)
Specific NE Driver (SND)
NCE service openness and programmability framework
Service package
NE driver package
Automatically generate NETCONF packets or deliver CLI commands to devices through SSH.
YANG
Service callback logic
NE template 1
NE template 2
NE YANG 2
RESTful API
Web-UI
Jinja2
Python
YANG
YANG
NE YANG 1
Packet mapping supports two layers of mapping logic: During the mapping from the service model to the device model, the logic is processed by the SSP package. During the mapping from the device model to protocol packets, the logic is processed by the SND package.
NCE automatically generates northbound interfaces or configuration GUIs based on service models.
Users send configuration requests to the service logic compiled by users through the interface provided by the service model.
The service processing consists of two parts:
  Python code processing, which processes service logic. For example, allocate resources and read NE or service information.
  Jinja2 template processing, which processes vendor-related logic. A template is actually the data delivered to a device model. Devices from different vendors have different templates.
Notes: Currently, the NCE service openness and programmability framework supports two layers of mapping logic: 1. Mapping from the service model to the device model, which is processed by the SSP package. 2. Mapping from the device model to protocol packets, which is processed by the SND package.
For SND package processing, if the device is a NETCONF device, NCE service openness and programmability automatically convert the model data into NETCONF packets.

## Slide 30: NETCONF
NETCONF server
NETCONF client
Content layer
Operations layer
Messages layer
Secure transport layer
SSH, TLS, BEEP/TLS, SOAP/HTTP/TLS
<rpc>, <rpc-reply>
<notification>
<edit-config>...
Data configuration
Notification data
NETCONF is a protocol defined by the IETF for installing, maintaining, and deleting configuration data on NEs. All NETCONF operations are implemented using XML-encoded RPCs. NCE service openness and programmability use NETCONF to communicate with NEs.
Content layer: It needs to transmit configuration data and notification data.
Operations layer: It defines an XML-encoded operation set for implementing RPC operations.
Messages layer: It implements a simple framing mechanism based on the requirements of the transport protocol to encapsulate RPC messages or notification messages.
Secure transport layer: It provides a communication path between the client and server. The NETCONF message hierarchy mechanism is implemented by using the communication paths that meet related conditions.
NETCONF
Notes: For more information about NETCONF, see NETCONF/YANG Principles and Practices.

## Slide 31: YANG Model
YANG,
short for Yet Another Next Generation, is a standard-based and extensible data modeling language. It can be used to model the configuration and running status data of network devices, remote procedure calls, and server event notifications. YANG was originally designed to model network management data and provide a standardized content layer for the NETCONF model.
Module
A module is a collection of related definitions. Each module contains the module header, revision, and description statements.
In a module, you can use the include statement to import submodules or use the import statement to import other modules. You can also use the augment statement in a module to extend a specified module.
A module may include the following four main types of data nodes, including Leaf, Leaf-list, Container, and List nodes.
module hbng {
namespace http://www.huawei.com/hbng;
prefix hbng;
import ietf-inet-types {
prefix inet;
}
include foo-bar-types;
description "This module can configure and manage the HBNGs (Huawei NE40-X8)";
revision 2018-04-20 {
description "Initial revision";
}
augment "/app:applications" { ... }
}
Notes: In this example, the service YANG module hbng is customized.
description describes the functions of the hbng module.
revision is 2018-04-20, indicating the initial version of the hbng module.
import and include introduce two modules for subsequent node definition.
augment "/app:applications" { ... } indicates that the current module hbng is extended to the /app:applications directory of the app module.

## Slide 32: YANG – Data Nodes
Leaf & Leaf-list
A leaf node contains simple data, such as integers and character strings. It has only one value of a specific type and has no sub-nodes.
A leaf-list node defines a sequence of values of a specific type.
Container
A container is used to group nodes. It has only sub-nodes, but does not have any value. A sub-node can be a container, leaf, leaf-list, or list node.
List
A list node is a set of data nodes, which are identified by key. The unique parameter specifies the data nodes that must be unique. A sub-node can be a container, leaf, or leaf-list node.
container system {
container login {
leaf message {
type string;
description "Message given at start of login session.";
}
leaf-list prohibited-users {
type: string;
description: "List of users not allowed to log in.";
}
list user {
key "name";
unique "name";
leaf name {
type string;
}
leaf level {
type uint8;
}
}
}
}
Notes: In this example, a container node named system is created, including the login container sub-node for recording login information.
The container sub-node login contains the following:
  A leaf node named message, which records the login prompt information.
  A leaf-list node named prohibited-users, which records the blacklist of users who are not allowed to log in to the system.
  A list node named user. In the list node, the unique key is defined as name and its type is character string; level is defined as user level and its type is number.

## Slide 33: YANG – Data and Data Types
Config. & Status
YANG can model status data and configuration data based on the "config" statement. If a node is marked as "config false", its sub-layer is marked as status data. If a node is marked as "config true", its sub-layer is marked as configuration data.
In the example on the right, leaf nodes name and speed are configuration data, and leaf node observed-speed is status data.
list interface {
key "name";
config true;
leaf name {
type string;
}
leaf speed {
type enumeration {
enum 10m;
enum 100m;
enum auto;
}
}
leaf observed-speed {
type uint32;
config false;
}
}
Native and derived types
When defining a leaf or leaf-list node, you must specify the value type. The native data types supported by YANG are binary, bits, boolean, decimal64, empty, enumeration, identityref, int8/16/32/64, leafref, string, and uint8/16/32/64.
In addition, the typedef statement can be used to derive a new type from a base type. The base type can be either a native type or a derived type.
typedef percent {
type: uint8 {
range: "0 .. 100";
}
}
Notes: In this example, the list interface is defined. config true indicates that the list is configuration data, and config false in observed-speed indicates that this leaf is status data.
The leaf node name is a character string. The leaf node speed provides three options. type enumeration indicates that the enumerated values are 10m, 100m, and auto. The leaf node observed-speed is a positive integer of the uint32 type.

## Slide 34: YANG – Reuse & Selection
Reusable node group (grouping)
If a group of nodes can be reused in different modules or nodes, you can define this group of nodes as a reusable node group and use the uses keyword to reference modules or nodes.
grouping ip-port {
leaf ip {
type inet:ip-address;
description "ip address";
}
leaf port {
type inet:port-number;
description "port number";
}
}
container quadruple {
container source {
uses ip-port;
}
container destination {
uses ip-port;
}
}
Choices
YANG allows data models to use the choice and case statements to define a set of pattern nodes that cannot appear together.
container transfer-protocol {
choice name {
case a {
leaf udp {
type empty;
}
}
case b {
leaf tcp {
type empty;
}
}
}
}
Notes: In this example, a group node named ip-port is defined, including two leaf sub-nodes: ip and port.
The container quadruple contains the source and destination information containers, both of which use the IP address and port information. The group node ip-port is reused.
The container transfer-protocol is used to indicate the transmission protocol. The UDP and TCP protocols are provided. Either of them can be selected using the choice function. case a indicates that the UDP protocol is used, and case b indicates that the TCP protocol is used.

## Slide 35: YANG – Operations
RPCs & Actions
YANG allows the following operation definitions:
Operations at the top layer of the module are defined using RPC statements. An RPC node usually consists of an input node and an output node. The input and output nodes can contain container, list, leaf, and leaf-list nodes.
Operations in a container or list node are defined by action statements. Generally, an action node contains an input node and an output node.
The difference between RPC and action is that RPC does not directly operate data, but action is directly bound to the node in the data storage.
module server-farm {
yang-version: 1.1;
namespace: "urn:example:server-farm";
prefix: "sfarm";
import ietf-yang-types {
prefix: yang;
}
rpc reset-specified-servers {
input {
leaf-list servers {
type: "inet:ip-address";
}
}
}
list servers {
key: "name";
leaf name {
type: string;
}
leaf address {
type: inet;
}
leaf location {
type: string;
}
action reset {
input {
leaf reset-at {
type: yang:date-and-time;
}
}
output {
leaf complete-at {
type: yang:date-and-time;
}
}
}
Notes: In this example, an RPC interface named reset-specified-servers is defined for resetting services. input indicates that the input parameter is the IP address of the server to be restarted. If output is not defined, the HTTP status is used to determine the returned result.
The servers list node defines action reset to restart the corresponding service. Input defines the leaf node reset-at, which indicates that the input parameter is the restart time. Output defines the leaf node complete-at, which indicates that the returned result is the restart completion time.

## Slide 36: Template Language Jinja2
Template language Jinja2
Jinja2 is a modern, design-friendly Python template engine. NCE service openness and programmability use Jinja2 to quickly process service packets using templates.
Specifically, Jinja2 is a text file that contains tags, variables, and expressions. Tags in the file are used to control the internal logic of the template. Variables and expressions are replaced with corresponding values when the template is rendered.
<inventory-cfg xmlns="urn:huawei:yang:huawei-ac-nes">
<nes>
{% for dev in nesInterfacesCfg.nes %}
<ne>
<neid>{{dev.neName | to_ne_id}}</neid>
<ifm xmlns="urn:huawei:yang:huawei-ifm">
<interfaces>
{% for ifName in dev.ifNames %}
<interface xmlns:ns0="urn:ietf:params:xml:ns:netconf:base:1.0"ns0:operation="merge">
...
</interface>
{% endfor %}
</interfaces>
</ifm>
{% endfor %}
</ne>
</nes>
</inventory-cfg>
Notes: The Jinja2 template is only a text file, which can be based on any text format (HTML, XML, CSV, etc.). In this example, the XML format is used.
A template contains variables and expressions. The variables and expressions are converted to corresponding values when the template is used. It has the following common syntaxes:
  {% ... %} contains Control Structures. In this example, {% for dev in nesInterfacesCfg.nes %} indicates that the for loop starts, and {% endfor %} indicates that the loop ends.
  {{...}} contains an expression, which can be a constant, variable, mathematical formula, or logical statement.
  {# ... #} indicates the comment.
The variables in {{...}} can be modified using filters. Filters and variables are separated by vertical bars (|). For example, {{ 'abc' | capitalize }} indicates that the first letter is capitalized and the filtering result is Abc. In this example, {{dev.neName | to_ne_id}}: to_ne_id is a user-defined filter, indicating that the variable device name dev.neName is converted to the device ID.
For more information, see the Template Designer Document at https://jinja.palletsprojects.com/en/2.11.x/.

## Slide 37
Background
Introduction to NCE Service Openness and Programmability
Key Capabilities
Related Concepts
Practice Cases

## Slide 38: Case 1: Fast Interconnection with New Devices and Automatic Generation of NBIs
In the OPS, choose Project Management > Software Package Management and generate an SND template.
Download the generated SND template and import it to the local IDE tool.
Develop the SND package based on the device type.
Load the developed SND package to NCE.
Add a new device. Device information is the same as that in the imported SND package.
Automatically generate configuration GUIs and NBIs for new devices.
Generating the SND template
1
2
3
Developing the SND package
Loading the SND package
4
Delivering basic device configurations
Apply basic device configurations through the GUIs or NBIs.
OSS/Orchestrator
NE management
Huawei NE Driver
3rd NE Driver
Service management
GUI
HVPN Service
SRV6 Service
SND
NBI
iMaster NCE
NETCONF
STelnet
Device management
...
Device group
Software package management
Public key management
Protocol
System configuration
Project management
Service template
Protocol parameter
NE template
1
IDE
2
3
4
Implementation process
Notes: NCE uses the Specific NE Driver (SND) package to quickly interconnect and manage Huawei and third-party devices and open device configuration capabilities. To manage third-party devices, you need to obtain the YANG file of the device from the vendor's website. If third-party devices support only command lines and do not support NETCONF interconnection, Huawei can customize interconnection capabilities.
Key capabilities:
  1. Quickly manage Huawei and third-party devices.
  2. Open device configuration capabilities.
  3. Automatically generate the configuration GUIs and northbound interfaces of new devices.

## Slide 39: Case 2: Fast Building of New Services and Automatic Generation of NBIs
In the OPS, choose Project Management > Software Package Management and generate an SSP template.
Download the generated SSP template and import it to the local IDE tool.
Develop the SSP package based on the service scenario.
Log in to the OPS and load the developed SSP package.
Automatically generate configuration GUIs and NBIs for new services.
Generating the SSP template
1
2
3
Developing the SSP package
Loading the SSP package
Key capabilities
4
Delivering service configurations to devices
Deliver service configurations to devices through the GUIs or NBIs.
OSS/Orchestrator
NE management
Huawei NE Driver
3rd NE Driver
Service management
GUI
HVPN Service
SRV6 Service
SND
NBI
iMaster NCE
NETCONF
STelnet
Device management
...
Device group
Software package management
Public key management
Protocol
System configuration
Project management
Service template
Protocol parameter
NE template
1
IDE
2
3
4
Implementation process
Notes: In this example, the service openness capability is used. Similar to the device atomic capability openness, the system is developed based on the standard NETCONF protocol. The internal data model uses the YANG modeling language to automatically generate configuration GUIs and northbound interfaces based on the YANG model of services. In addition, the Easymap algorithm is provided for customers to write only the creation process, and the update and deletion are calculated by comparing algorithms. This simplifies customer programming.
The service layer shields differences between devices, supports interconnection with different device types, and delivers configurations through different protocols. The maintenance personnel or upper-layer system only needs to view corresponding services. They do not need to know the specific vendor and protocol of the device. This feature improves interconnection efficiency and reduces the pressure on maintenance personnel.
Key capabilities:
  1. Open service capabilities.
  2. Shield differences between underlying devices at the service layer.
  3. Automatically generate southbound and northbound interfaces based on the YANG model.

## Slide 40: Case 3: Batch Configuration Delivery
Implementation process
Choose NE Management > Device Management, add a device, and match the SND package based on the device NE type, software version, and vendor.
Synchronize device configurations to the OPS.
Managing devices
1
To apply one template to multiple devices, you can add these devices to the same device group.
Grouping devices on demand
2
3
Delivering configurations in batches
by device group
Some templates can be preset for common configurations (such as underlay), and device groups can be selected for batch delivery.
OSS/Orchestrator
NE management
Huawei NE Driver
3rd NE Driver
Service management
HVPN Service
SRV6 Service
SND
NBI
iMaster NCE
Device management
...
Device group
Software package management
Public key management
Protocol
System configuration
Project management
Service template
Protocol parameter
NE template
GUI
1
2
3
NETCONF
STelnet
Notes: Devices with the same configuration can be grouped. A preset template can be applied to the system for batch configuration delivery. Currently, more than 60 templates are preset in the enterprise DCN for users to apply.

## Slide 41: Case 4: Configuration Correctness Pre-check Using the dryRun Function
OSS/Orchestrator
NE management
Huawei NE Driver
3rd NE Driver
Service management
GUI
HVPN Service
SRV6 Service
SND
NBI
iMaster NCE
Device management
...
Device group
Software package management
Public key management
Protocol
System configuration
Project management
Service template
Protocol parameter
NE template
3
1
2
Key capabilities
Configure services on the Service Management page as required.
Create a service.
Select an existing service and modify the configuration parameters.
Select an existing service and delete it.
Configuring services
1
2
Checking before service configuration delivery
Perform dryRun and check whether the generated configurations are correct.
Perform the Commit operation to deliver configurations to the device.
View the delivered configurations through the associated data.
3
Delivering service configurations to devices
NETCONF
STelnet
Implementation process
Notes: Before service configurations are delivered, the OPS provides the dryRun function to check the correctness of delivered configurations in advance. If an error occurs, modify the dryRun function. After the configurations are correct, commit the configurations again. The system provides a transaction mechanism to ensure data consistency between the device and controller. If the data fails to be synchronized, the system automatically rolls back the data to ensure that no residual data exists. For a service that is successfully delivered, you can view the delivered configurations of the associated device. In addition, you can view the delivered configurations in historical records. You can roll back the configurations based on the rollback point.
Key capabilities:
  1. Use the dryRun function to check whether the delivered configurations are correct in advance.
  2. Provide a transaction mechanism to ensure data consistency between the device and controller. If a failure occurs, automatic rollback will be performed.
  3. Provide the visualized display of service association data and historical configurations.

## Slide 42: Case 5: Automatic Detection of Service Configuration Conflicts
Before delivering configurations, the OPS automatically checks whether the configurations delivered to devices conflict with each other. For example, if service 1 delivers the description configuration of VLAN 2 to device 1 and service 2 also delivers the description configuration of VLAN 2 to device 1, this system checks whether the two values are the same. If they are different, a message indicating that the configurations conflict will be displayed.
On the Service Management page, deliver configurations. The system automatically checks whether service configurations conflict.
Automatic detection of service configuration conflicts
1
1
OSS/Orchestrator
NE management
Huawei NE Driver
3rd NE Driver
Service management
HVPN Service
SRV6 Service
SND
NBI
iMaster NCE
Device management
...
Device group
Software package management
Public key management
Protocol
System configuration
Project management
Service template
Protocol parameter
NE template
GUI
NETCONF
STelnet
Implementation process

## Slide 43
This chapter describes the practice cases of Huawei NCE service openness and programmability, including compiling NE driver packages to interconnect with new devices, compiling service packages to build new services, delivering configurations in batches, using the dryRun function to check configuration correctness, and automatically detecting service configuration conflicts.
For details, see the HCIP-Datacom-NCE Service Openness and Programmability Lab Guide.

## Slide 44
What are the core function packages of Huawei iMaster NCE service openness and programmability?
(Multiple) Which of the following are included in a Specific Service Plugin (SSP) package? ( )
  Service YANG model
  Device YANG model
  Jinaji2 template
  Python mapping script
Notes: Specific NE Driver (SND) and Specific Service Plugin (SSP) packages.
ACD

## Slide 45
Network service openness and programmability pave the way for development of the network industry. Enabling the capabilities of network service openness and programmability is the cornerstone of building an open network ecosystem.
Huawei OPS is a practice offered by Huawei in this field. Users can compile SND and SSP packages to quickly interconnect new devices and construct new services.
To learn this chapter, you need to have a good understanding of Python, NETCONF, YANG, and Jinja2.

## Slide 46
Log in to the HUAWEI CLOUD developer community and click the Datacom Network Openness and Programmability tab to obtain related tools and documents.
https://developer.huaweicloud.com/resource/network.html#AOC
Key documents:
  Datacom Network Openness and Programmability Development Guide: This document describes the development process and methods of related driver packages, and provides guidance for developers to develop SND and SSP packages, load the packages to the system, and automatically generate configuration GUIs and NBIs.
  Datacom Network Openness and Programmability User Guide: This document describes operations related to the configuration GUIs and NBIs, and provides guidance for O&M personnel to deliver device and service configurations.

## Slide 47
For more information about Jinja2, visit the following website:
https://jinja.palletsprojects.com/en/2.11.x/